PART-A

GUJRAT DIVISION UJC

CHAPTER - 1

SALIENT FEATURES OF THE GUJRAT DIVISION UJC

  - LOCATION

Gujrat Division UJC is located on right side of Gujrat Bhimber Road near Aziz Bhatti Shaheed Hospital Gujrat.

1.2	GENERAL DESCRIPTION

Gujrat Division UJC is responsible for the maintenance of Bunds and Spurs constructed on the right side of Rivers Chenab and Munawar Tawi, hill torrents like Bhimber Nallah, Bhinder Nallah, Halsi Nallah and Dawara Nallah in Gujrat and Mandi Bahauddin Districts. Total length of Bunds and Spurs in Gujrat Division is 91.00 miles along right bank and 666.78 Miles of canals which exist in Gujrat/Mandi Bahauddin/Sargodha Districts. The purpose of these infrastructures is to save tens of thousands of inhabitants dwelling along River Chenab from ravages of the river which can wreak havocs to their lives and property during monsoon. A brief description of Rivers/Nallah which brings floods in District Gujrat/Mandi Bahauddin and detail of flood protection works constructed or being constructed to mitigate flood damages have been explained in this flood fighting plan. An index plan of Gujrat Division UJC showing all flood protection works constructed along different hill torrents and River Chenab and Munawar Tawi  is placed at page No. 18-A.

        - 1.3 	ADMINISTRATIVE SETUP

- Executive Engineer Gujrat Division UJC Gujrat

- Sub Divisional Officer Phalia, Sub Division UJC Phalia.

- Sub Divisional Officer Gujrat Sub Division UJC Gujrat.

- Sub Divisional Officer S & I, Sub Division UJC Gujrat.

- Sub Divisional Officer Sohawa, Sub Division UJC M.B. Din.

- Sub Divisional Officer Busal, Sub Division UJC M.B. Din.

- 19 No. Sub Engineers

Organization Chart is attached at page No. 2-A

XEN/GRT

CHAPTER – 2

FLOOD PROTECTION AND RIVER TRAINING WORKS

  - DESIGN PARAMETER OF TRAINING WORKS

BHIMBER NALLAH

Bhimber Nallah is a non-perennial hill torrent which originates from the hills of Jammu & Kashmir with a catchment of nearly 415 square miles. This Nallah outfalls in River Chenab from its right side just U/S of Khanki Headworks. The Nallah has very steep slope and thus brings flashy discharge which creates havoc in the plains of District Gujrat. A discharge to the tune of 78000 Cs. was observed during flood season of 1988. Average annual rain in the catchment area of this Nallah ranges from 26” to 38”. A number of important towns like Lalamusa, Rattowal Syedan and important communication infrastructure like GT Road, Railway Line and H.T transmission lines are endangered by the flash flood of this Nallah. For protection of these town etc. a flood bund namely “Lalamusa flood bund has been constructed along its right bank.

- LALAMUSA FLOOD BUND

Data of Lalamusa flood bund is as under:-

i)	Length RD 0-81270		=	16.25 miles

ii)	Location	=	Along right bank Bhimber Nallah from kharian-Jalalpur Jattan Defence road to G.T road bridge (Rehmania bridge) near Gujrat city District Gujrat.

iii)	Side slopes	=	3:1 on inner side = 2:1 outer side

iv)	Top width	=	20’

v)	Free board			=	5’ above HFL of 1992

A series of 33 No. stone sloping spur have been constructed on Lalamusa Flood Bund for its protection against erosion and to keep the active current sufficiently away from the main bund.

XEN/GRT

RD and length of stone sloping spurs are given as under:-

| Sr. No. | RD of spur | Length of spur | Nature of spur |
| --- | --- | --- | --- |
| 1. | 13300 | 125’ | Stone sloping spur |
| 2. | 13370 | 150’ | -do- |
| 3. | 14145 | 160’ | -do- |
| 4. | 14300 | 156’ | Stone sloping spur |
| 5. | 14450 | 130’ | -do- |
| 6. | 14600 | 120’ | -do- |
| 7. | 14820 | 75’ | -do- |
| 8. | 14950 | 75’ | -do- |
| 9. | 15115 | 150’ | -do- |
| 10. | 15270 | 150’ | -do- |
| 11. | 15570 | 75’ | -do- |
| 12. | 25970 | 77’ | -do- |
| 13. | 26070 | 100’ | -do- |
| 14. | 26350 | 90’ | -do- |
| 15. | 26470 | 87’ | -do- |
| 16. | 26720 | 87’ | -do- |
| 17. | 29060 | 125’ | -do- |
| 18. | 29170 | 120’ | -do- |
| 19. | 41070 | 110’ | -do- |
| 20. | 41170 | 100’ | -do- |
| 21. | 41295 | 90’ | -do- |
| 22. | 41420 | 100’ | -do- |
| 23. | 41570 | 115’ | -do- |
| 24. | 41670 | 100’ | -do- |
| 25. | 41870 | 100’ | -do- |
| 26. | 66120 | 75’ | -do- |
| 27. | 66270 | 80’ | -do- |
| 28. | 66520 | 75’ | -do- |
| 29. | 66655 | 75’ | -do- |
| 30. | 66980 | 100’ | -do- |
| 31. | 67155 | 120’ | -do- |
| 32. | 67320 | 120’ | -do- |
| 33. | 67735 | 115’ | -do- |

Vulnerable sites are protected with stone pitching supported with stone apron at the base. Detail of stone pitched sites is fabled as under:-

XEN/GRT

VULNERABLE SITES OF LALAMUSA FLOOD BUND

Chachian, Guliana, Aiko, Dahu, Kamla, Bhand, , Qazi Imam Shah, Syeda Goll, Gill, Kot Bella.chakha

1.	RD 9000-10000			=	1000

- BHIMBER RIGHT BUND

It has been constructed on right bank of Bhimber Nallah with bridge on G.T road and bridge on Gujrat-Sargodha road as its starting and terminating point respectively.

Salient features of Bhimber Right bund is as under:-

i)	Length RD 0-21550		=	4.31 miles

ii)	Location	=	along left bank of Bhimber Nallah from G.T road Rehmanianwala Bridge to Sargodha Gujrat Road.

iii)	Top width	=	20.0’

iv)	Side slopes	=	3:1 inner side   = 2:1 outer side

v)	Free Board	=	3.20’

Vulnerable villages

Dhool, Vanse, Changanwali, Melo, Qasibabad, Khokhar

- BHIMBER LEFT BUND

It has been constructed on left bank of Bhimber Nallah with bridge on G.T road and bridge on Gujrat-Sargodha road as its starting and terminating point respectively.

Salient features of Bhimber left bund is as under:-

i)	Length RD 0-19050		=	3.81 miles

ii)	Location	=	Along left bank of Bhimber Nallah from G.T. Road Rehmanianwala bridge to Sargodha Gujrat Road.

iii)	Top width	=	20.0’

iv)	Side slopes	=	3:1 inner side = 2:1 outer side

v)	Free Board	=	3.0’

Vulnerable villages

Sanawal, Sheikh Sukha.

XEN/GRT

2.	BHINDER NALLAH

Bhinder Nallah is a left side tributary of Bhimber Nallah. The confluence point of Bhimber and Bhinder Nallah is located near village Musa Kamala on the U/S side of old G.T Road Bridge. It was used to inundate Gujrat city and other villages like Musa kamala and Phullarwan etc. in the past. Musa kamala flood bund has been constructed along left bank of this Nallah to protect above said abadies and infrastructure from the flooding of this Nallah. This bund having a length of 15000 feet commences from the strip of Gujrat Air Port and terminates at G.T road bridge Salient features of this flood bund are given as under:-

MUSA KAMALA FLOOD BUND

Salient features of Musa kamala flood bund is as under:-

i)	Length RD 0-15000	=	3 miles

ii)	Location	=	Along left bank of Bhinder Nallah from village Kamala to Rehmanianwala bridge at G.T Road Gujrat.

iii)	Side slopes	=	3:1 inner side and 2:1 outer side

iv)	Top width	=	20’

v)	Free board	=	5’ above HFL of 1973

A battery of 17 spurs has been constructed for the safety of bund and to push the violent currents to remain away from it.

| Sr. No. | RD of spur | Length of spur | Nature of spur |
| --- | --- | --- | --- |
| 1. | 6965 | 3620 Lft | Earthen with stone pitching & apron at nose. |
| 2. | 7450 | 370 Lft. | -do- |
| 3. | 7925 | 180 Lft. | -do- |
| 4. | 8500 | 185 Lft. | -do- |
| 5. | 8975 | 185 Lft. | -do- |
| 6. | 9250 | 150 Lft. | Stone sloping spur |
| 7. | 9550 | 250 Lft. | -do- |
| 8. | 9700 | 150 Lft. | -do- |
| 9. | 10050 | 320 Lft. | Earthen with stone pitching & apron at nose. |
| 10. | 10250 | 200 Lft. | -do- |
| 11. | 10550 | 370 Lft. | -do- |
| 12. | 12325 | 180 Lft. | -do- |
| 13. | 12700 | 108 Lft. | -do- |
| 14. | 12915 | 170 Lft. | -do- |
| 15. | 13160 | 170 Lft. | -do- |
| 16. | 13510 | 200 Lft. | -do- |
| 17. | 13865 | 220 Lft. | -do- |

XEN/GRT

3.	HALSI NULLAH

Halsi Nullah is a hill torrent which originates from the hills in Azad Jammu and Kashmir and passes along eastern side of Gujrat City and outfalls in River Chenab near village Kathala Chenab U/S of Alexandra bridge. A flood bund namely “Gujrat Flood Bund RD 4000-33500” was constructed for protection of Gujrat City and adjoining abadies on right bank of Halsi Nullah. The existing bund has now been extended from RD 33500 to 55200. Work at RD 0 to 4000 could not be executed earlier due to a stay order issued by court in 1957. Besides, a left over work from RD 0-4000 & 33500-54200 was also been constructed/completed during the year 2004-5 and 2005-6. Salient features of Gujrat flood bund from RD 4-33500 are given as under and Salient features of Gujrat Flood bund from RD 0-4 and 33500-54200 are given on page No. 9:-

GUJRAT FLOOD BUND (EXISTING PORTION)

- Salient features of previously existing Gujrat Flood bund is as under:-

A Flood Bund namely “Gujrat Flood Bund” has been constructed along right bank of halsi Nalla.

i)	Length RD 4-33500	=	5.9 miles

ii)	Location		=	Along right bank of Halsi Nallah in the vicinity and suburbs of Gujrat City.

iii)	Side slopes		=	3:1 inner side

=	2:1 outer side

iv)	Top width		=	20’

v)	Free Board		=	5’ above HFL of 1973.

A battery of 47 No. stone spurs is constructed for safety of the bund against erosion. Detail of spurs is given below:-

| Sr. No | RD of spur | Length of spur | Nature of spur |
| --- | --- | --- | --- |
| 1. | 4350 | 52.50’ | Stone sloping spur |
| 2. | 4475 | 42.5’ | -do- |
| 3. | 4650 | 57.5’ | -do- |
| 4. | 11700 | 48.04’ | -do- |
| 5. | 11850 | 40.0’ | -do- |
| 6. | 12000 | 40.0’ | -do- |
| 7. | 12974 | 40.0’ | -do- |
| 8. | 14885 | 77.0’ | -do- |
| 9. | 15070 | 60.0’ | -do- |
| 10. | 15195 | 55.0’ | -do- |
| 11. | 15320 | 54.0’ | -do- |
|  |  |  | XEN/GRT |
| Sr. No | RD of spur | Length of spur | Nature of spur |
| 12. | 15495 | 55.0’ | -do- |
| 13. | 17232 | 55.0’ | -do- |
| 14. | 25150 | 35.0’ | -do- |
| 15. | 25250 | 35.0’ | -do- |
| 16. | 25380 | 35.0’ | -do- |
| 17. | 25480 | 40.0’ | -do- |
| 18. | 25620 | 30.0’ | -do- |
| 19. | 25720 | 35.0’ | -do- |
| 20. | 25850 | 25.0’ | -do- |
| 21. | 25950 | 30.0’ | -do- |
| 22. | 28000 | 40.0’ | -do- |
| 23. | 28335 | 40.0’ | -do- |
| 24. | 28420 | 85.0’ | -do- |
| 25. | 28640 | 40.0’ | -do- |
| 26. | 28790 | 45.0’ | -do- |
| 27. | 28940 | 50.0’ | -do- |
| 28. | 29060 | 60.0’ | -do- |
| 29. | 4950 | 30.0’ | Earthen with stone pitched nose. |
| 30. | 5500 | 50.0’ | -do- |
| 31. | 6000 | 60.0’ | -do- |
| 32. | 7800 | 75.0’ | -do- |
| 33. | 8000 | 40.0’ | -do- |
| 34. | 12100 | 40.0’ | -do- |
| 35. | 16500 | 120.0’ | -do- |
| 36. | 17100 | 75.0’ | -do- |
| 37. | 18800 | 40.0’ | -do- |
| 38. | 19200 | 100.0’ | -do- |
| 39. | 21500 | 1200.0’ | -do- |
| 40. | 25100 | 30.0’ | -do- |
| 41. | 27500 | 30.0’ | -do- |
| 42. | 27500 | 75.0’ | -do- |
| 43. | 29500 | 75.0’ | -do- |
| 44. | 29650 | 40.0’ | -do- |
| 45. | 29950 | 80.0’ | -do- |
| 46. | 16000 | 10.0’ | On Bhimber right flood bund |
| 47. | 15400 | 100.0’ | On Bhimber right flood bund |

B 	CONSTRUCTED/COMPLETED WORK DURING 2004-05, 2005-06

Newly constructed part of Gujrat flood bund includes earthen flood bund, earthen flood bund with right side inner slopes of Nallah and flood bund completely pitched, partially pitched left side inner slopes on Nallah and retaining walls where space for construction way of bund was not available due to presence of road, population etc.

XEN/GRT

Salient features of newly constructed Gujrat Flood Bund.

(a)      i)      	RD 0-4000			=	0.80 miles

ii)	Side slopes			=	3:1 & 2:1

iii)      Top width			=	20’

v)      	Free board			=	5.0 above H.F.L

(b)	i)      	RD 33500 –54200		=	4.27 miles

+length of tie bund 650’

ii)       Side slopes			=	2:1 & 1:1

iii) 	Top width 			=	20’

iv)	Free board			=	5’ above H.F.L

- Pitched portion

Left side			                                      Right side

Tie bund               =  350’

RD 37500-37750  =  250’		       RD 33500-40000  =  6500’

RD 38750-40500  =  1750’                   RD 40000-43000  = 3000’

RD 46750-48000  =  1250’                    RD 43000-47200  = 4200’

RD 47200-54200  = 7000’

Total	      =  3250’	                                           = 21050’

Total length of left and right side pitching = 3250’ + 21050’	 = 24300’

vi)       Retaining wall

RD 39000-41000 	=	2000’(Opposite village Gorali)

RD 46800-48500	=	1700’(Opposite village (kathala

Chenab)

Total		            =        3700’

ABSTRACT OF GUJRAT FLOOD BUND.

i)         	Total length      =  	RD 0-4000                        	= 0.80 Mile

RD 4000-33500                	= 5.90 –“-

=	RD 33500-54200               	= 4.14 –“-

Total  			=  10.84 Miles

VULNERABLE VILLAGES ALONG HALSI NALLAH

Gorali, Gorala, Kathala, Kalra, Malhowal, Ghazi Khan Kalwari, Gagian, Jamalpur, Mararpur.

4.         DAWARA NULLAH

Dawara Nullah a small hill torrents originates from foot hills in Azad Jammu & Kashmir and outfalls in River Chenab at its right side in Marala-Alexandra bridge reach of River Chenab. It is used to inundate village Khewa Hafiz, Hayat Garh and other adjoining several abadies near Jalal Pur Jattan. An embankment on right bank of Dawara Nullah was constructed during 1989-90 for protection of above mentioned villages. This embankment is named as Dawara Nullah Bund and has a length 4800’. Its salient features are as under: -

XEN/GRT

Salient features of Dawara Nalla Flood Bund constructed along                                right bank of Dawara Nalla is as under:-

i) 	Length		          =   	RD 0-4100 (0.82 miles)

ii)	Location                 	=  	Along right bund of River Chenab   from foot hills of Azad Jamu & Kashmir to village Khewa Hafiz.

iii)	Top Width	=   	20’

iv)        Side slopes	=	2:1 inner side

2:1 outer side

v)	Free board		=	5’

vi)	Pitched section	=	RD 0-250	     =	250’

RD 670-2170=1500’

Total   =1750’

Salient features of Flood Embankment on Rainy Nallah near Village Keeranwala East.

Length				=		0-5000 (1.0 Mile)

Location	=	Along left bank of Bhimber Nallah

Top width	=		15 ft.

Side slope	=		2:1 on both side

Free board	=		5’

Salient features of Guide wall spur near village Kot Ghulam on right bank of River Chenab

Length				=		973 ft.

Location	=	Along right bank of River Chenab near village Kot Ghulam

Top width	=		25 ft.

Side slope	=		2:1 on both side

Free board	=		5’

Top RL	=		770.00

Salient features of Inverted Hockey Stud No. 1 & 2 near village Behlolpur on Right Bank of River Chenab

Length of Hockey		=		520 ft.

Length of Gunda Bund No.1	=		833 ft.

Length of Gunda Bund No.2	=		442 ft.

Location	=	Along right bank of River   Chenab near village Behlolpur

XEN/GRT

Top width	=		25 ft.

Top R.L	=		805.00

Side slope	=		2:1 on both side

Free board	=		5’

- RIVER CHENAB

Chenab River originates from the hills of occupied Jammu and Kashmir and after entering in Pakistan, it is controlled at Marala Barrage in District Sialkot. Other important structures on this River D/S Marala Barrage are Alexandra Railway Bridge and G.T Road Bridges near Gujrat city.

Prior to 1983, this River used to flow along its left bank but it started to drift towards right side in the subsequent flood seasons. The trend of right wards drift kept on increasing and the situation became critical to such an extent that Irrigation and Power Department had to construct a No. of spurs along right bank of this River in the subject reach of about 25 miles length to check erosion/embayment along right bank and to arrest the chances of Alexandra Bridge from being by-passed by the river.

The area of responsibility of Gujrat Division on river Chenab is spread along its right bank starting from the D/S of Marala Head Works upto the escape of lower Jhelum canal. Covering these river reaches, namely, Marala-Alexandra bridge reach in district Gujrat, Alexandra bridge –Khanki barrage reach is in district Gujrat and Qadirabad Head Works to escape reach is in district M.B.Din.

Detail of works in the above mentioned river reaches is as under.

- Marala to Alexandra Bridge(River reach)

| Sr.No. | Name of spur | Location | Length of spur | Length of shank | Length of head | Top width | Side slope of shank |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Spur No. 1 U/S Alexandra Bridge. | Distt: Gujrat | 7753’ | 6423’ | 1330’ | 25’ | 2:1 |
| 2. | Spur NO.2 near Pandi village | -do- | 8805’ | 7475’ | 1330’ | 25’ | 2:1 |
| 3. | Mole head prong U/S side of spur No.2. | -do- | 450’ | -- | -- | 25’ | 2:1 |
| 4. | Slopping stud U/S spur No. 2 near village Patwan converted in Hockey spur. | -do- | 1630’ | 1060’ | 570’ | 25’ | 2:1 |

XEN/GRT

| Sr.No. | Name of spur | Location | Length of spur | Length of shank | Length of head | Top width | Side slope of shank |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 5. | J- Head Spur No. 3 near kotli village. | -do- | 3980’ | 2600’ | 1380’ | 25’ | 2:1 |
| 6. | J- Head Spur No. 4 near Dera Nasir. | -do- | 2657’ | 1300’ | 1357’ | 25’ | 2:1 |
| 7. | Slopping stud U/S spur No. 4 near village kot Ghulam. | -do- | 1056’ | -- | -- | 25’ | 2:1 |
| 8. | J- Head Spur No. 5 near Lambore village | -do- | 4235’ | 2905’ | 1330’ | 25’ | 2:1 |
| 9. | J- Head Spur No. 6 near kot Nikka village. | -do- | 3590’ | 2250’ | 1340’ | 25’ | 2:1 |
| 10. | J- Head Spur No. 7 near Dawara Nallah. | -do- | 3847’ | 2500’ | 1347’ | 25’ | 2:1 |
| 11. | Guide bank/spur No. 8 near Shahbazpur village. | -do- | 1925’ | 500’ | 1425’ | 25’ | 2:1 |
| 12. | Slopping stud U/S spur No. 8 near village Changanwali. | -do- | 2070’ | -- | -- | 25’ | 2:1 |
| 13. | Guide bank/spur No. 9 near Dera Hakim Ali. | -do- | 1820’ | 750’ | 1320’ | 25’ | 2:1 |
| 14. | Guide bank spur No. 10 near Sajawal village. | -do- | 1760’ | 500’ | 1260’ | 25’ | 2:1 |
| 15. | Guide bank/Spur No. 11 near Chopala village. | Distt: Gujrat | 1790’ | 400’ | 1390’ | 25’ | 2:1 |
| 16. | Restoring plug bund of river creek near Shampur khokhran in District Gujrat (FPSP). | -do- | 900’ | 1700’ including length of head | -- | 20’ | 2:1 |
| 17. | Protective measure against erosion of River Chenab to Sherines of Hazrat Ammoon and Hazrat Tanooh (Aleh Salam) near village Sheikh Chugani in District Gujrat. | -do- | 465’ | 1700’ including length of head | -- | 15’ | 1:2` |
| 18. | J-head spur near village Shampur. | -do- | 2394’ | 1644’ | 750’ | 25’ | 2:1 |
| 19. | Guide wall spur near village Nut Sharki. | -do- | 1013’ | 620’ | 293’ | 20’ | 2:1 |
| 20. | Construction of Inverted Hockey Stud No. 1&2 near village Behlolpur on right bank of River Chenab. | -do- | 520’ | 365’ | 155’ | 25’ | 2:1 |
|  |  |  |  |  | XEN/GRT |
| Sr.No. | Name of spur | Location | Length of spur | Length of shank | Length of head | Top width | Side slope of shank |
| i) | Gunda Bund No. 1 | -do- | 833’ | 833’ | -- | 25’ | 2:1 |
| ii) | Gunda Bund No. 2 | -do- | 442’ | 442’ | -- | 25’ | 2:1 |
| 21. | Construction of Guide Wall Spur near village Kot Ghulam on right bank of River Chenab. | -do- | 973’ | 633’ | 340’ | 25’ | 2:1 |
|  | Total length |  | 54908 |  |  |  |  |
|  |  |  | 10.98 Miles |  |  |  |  |

ALEXANDRA TO KHANKI HEADWORKS (River Reach)

| Sr.No. | Name of spur | Location | Length of spur | Length of shank | Length of head | Top width | Side slope of shank |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | J-head spur near village Samma Mohla. | Distt: Gujrat | 2887’ | 2187’ | 700’ | 25’ | 2:1 |
|  | Total |  | 2887’ |  |  |  |  |
|  |  |  | 0.58 Miles |  |  |  |  |

QADIRABAD BARRAGE TO OUTFALL LJC ESCAPE (RIVER REACH)

| Sr.No. | Name of spur | Location | Length of spur (in ft.) | Length of shank | Length of head | Top width (in ft.) | Side slope of shank |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Guide wall spur opposite village Kalashadian. | Distt: MBDin | 1170 | -- | -- | 30 | 2:1 |
| 2. | Guide wall spur village Farrukhpur. | Distt: MBDin | 2240 | -- | -- | 25 | 2:1 |
| 3. | Guide wall spur U/S Haveli Manik. | Distt: MBDin | 1400 | -- | -- | 25 | 2:1 |
| 4. | Guide wall spur village Noorpur. | Distt: MBDin | 1581 | -- | -- | 25 | 2:1 |
| 5. | J-head spur Chakori village. | Distt: MBDin | 2650 | -- | 855 | 25 | 2:1 |
| 6. | Guide wall spur village Bari & Randali. | Distt: MBDin | 1387 | -- | -- | 25 | 2:1 |
| 7. | Stone pitched guide wall and stud. | Distt: MBDin | 700 | -- | -- | 20 | 2:1 |
| 8. | Inverted Hockey Spur near village Bari. | Distt: MBDin | 2034 | -- | -- | 20 | 2:1 |
| 9 | Hockey Spur with stud near Village Bherowal. | Distt: MBDin |  |  |  |  | 2:1 |
| 10. | Hockey Spur near village Miana Hazara | Distt: MBDin | 684 | - | - | 25 | 2:1 |
|  | Total |  | 13846 |  |  |  |  |
|  |  |  | 2.77 Mile |  |  |  |  |

XEN/GRT

ABSTRACT

i)	Marala to Alexandra Bridge J-head spurs			=	23 No.

ii)	Guide wall spur at river munawar tawi			=	3 No.

iii)	Alexandra to Khanki Headworks J-head spurs		=	1 No.

iv)	Qadirabad Barrage to outfall LJC escape sloping

spurs/J-head hockey spur,Guide wall.			=	8 No.

v)	Misc. works							=	Nil

TOTAL		=	35 No.

TOTAL LENGTH	= 14.27 Miles

B.				DETAIL OF FLOOD BUNDS

- CHUKNAWALI FLOOD BUND

This bund is situated downstream Qadirabad Barrage for protection of 15-R disty and village abadies of Tehsil Phalia District Mandi Bahauddin. Its total length is 12.38 miles and is quite safe to combat high floods in River Chenab.

Salient features of Chuknawali flood bund are as under:-

i)	Length RD 111400-173360	=	12.38 Miles

ii)	Location	=	Along right bank of River Chenab Jaggo kalan to D/S UJC

iii)	Side slopes	=	3:1 inner & 2:1 outer side.

iv)	Top width	=	20’

v)	Free board	=	5’ above HFL of 1973

- HUMBER FLOOD BUND

This bund has been constructed to protect Phalia disty system & agriculture land of villages Thakar Kalan, Miana Thakar, Waryam, Bharowal, Humber, Basti Makhdum & Dhunny Kalan etc. from flood waters of River Chenab. Its total length is about 16.50 miles and is quite safe to face high floods in River Chenab. However, general maintenance in terms of removal of rain cuts/gharas and making up of deficient height/slopes will be done during the current financial year.

Salient features of Humber Flood Bund is as under:-

i)	Length RD 0-82500		=	16.50 Miles

ii)	Location	=	Along right bank of River Chenab near village Dhuni kalan to tail LJC escape.

XEN/GRT

iii)	Side slopes	=	3:1 on water side & 2:1 on Country side.

iv)	Top width	=	25’

v)	Free board	=	6’ above HFL of 1973

vi)	Pitched section	=	39000-40000=1000’

Total length of Chuknawali & Humber Flood bund.	=	28.88 Miles

- CONSTRUCTED/COMPLETED WORK DURING 2005-06,

2006-07.				__

Following works namely “Construction of spurs/studs on right bank of River Chenab to protect village abadies and agricultural lands of Qadirabad, Farrukhpur, Chakori, Noorpur, Bari and Randiali etc. were planned to be executed under ADP 2005-06 and work has been completed on 30.6.2007. The salient features of these components are as under:-

1)	Constructing Farrukhpur flood protection bund                         RD 0+000 to 33+500.

| 1. | Length of bund | 6.80 Mile |
| --- | --- | --- |
| 2. | Top width | 25 feet |
| 3. | Side slopes | Outer side 2:1/Inner side 3:1 |
| 4. | Kind of bund | Earthen |

2)         Constructing Guide Wall spur near Farrukhpur village

| 1. | Length of guide wall | 2240 feet |
| --- | --- | --- |
| 2. | Top width | 25 feet |
| 3. | Side slopes | 2:1 |
| 4. | Thickness of pitching | 2 feet |
| 5. | High flood level | 675.0 ft. |
| 6. | Top level of guide wall. | 680.0 ft. |
| 7. | Top level of apron | 659.50 ft. |
| 8. | Free board | 5.00 ft. |

3)	Constructing J-head spur near Chakori village.

| 1. | Length of shank | 2650 feet |
| --- | --- | --- |
| 2. | Length of head | 855 ft. |
| 3. | Top width | 25 feet |
| 4. | Side slopes | 2:1 |
| 5. | Thickness of pitching | 2 feet |
| 6. | High flood level | 671.50 ft. |
| 7. | Top level of spur. | 676.50 ft. |
| 8. | Top level of apron | 656.00 ft. |
| 9. | Free board | 5.00 ft. |

XEN/GRT

4.	Constructing Guide wall spur with sloping stud near Noorpur village.

| 1. | Length of guide wall | 1581 feet |
| --- | --- | --- |
| 2.. | Top width | 25 feet |
| 3. | Side slopes | 2:1 |
| 4. | Thickness of pitching | 2 feet |
| 5. | High flood level | 659.60 ft. |
| 6. | Top level of guide wall. | 659.60 ft. |
| 7. | Top level of apron | 654.50 ft. |

5.	Salient features of sloping stud.

| 1. | Length | Straight part = 100 feet Sloping part = 192 feet Total = 292 feet |
| --- | --- | --- |
| 2. | Top width | 15 feet |
| 3. | Side slopes | 1:1 |

6.	Constructing Guide wall spur with sloping stud U/S Haveli Manik.

| 1. | Length of guide wall | 1400 feet |
| --- | --- | --- |
| 2.. | Top width | 25 feet |
| 3. | Side slopes | 2:1 |
| 4. | Thickness of pitching | 2 feet |
| 5. | High flood level | 668.20 ft. |
| 6. | Top level of guide wall. | 668.20 ft. |
| 7. | Top level of apron | 653.70 ft. |

7.	Salient features of sloping stud.

| 1. | Length | Straight part = 100 feet Sloping part = 171 feet Total= 271 feet |
| --- | --- | --- |
| 2. | Top width | 15 feet |
| 3. | Side slopes | 1:1 |

8)	Construction of a guide wall spur with slopping stud to save the fertile agricultural land of village Bari & Randiali.

| 1. | Length of guide wall | 1387 ft. |
| --- | --- | --- |
| 2. | Top width | 25 ft. |
| 3. | Side slopes | 2:1 |
| 4. | Thickness of pitching | 2 ft. |
| 5. | High flood level | 669.60 ft. |
| 6. | Top level of guide wall. | 669.60 ft. |
| 7. | Top level of apron | 654.50 ft. |

XEN/GRT

9.	Salient features of sloping stud.

| 1. | Length | Straight part = 100 feet Sloping part = 192 feet Total = 292 feet |
| --- | --- | --- |
| 2. | Top width | 15 feet |
| 3. | Side slopes | 1:1 |

- Inverted Hockey spur near village Bari

| 1. | Length of Hockey | 1076 Feet |
| --- | --- | --- |
| 2. | Top width | 20 feet |
| 3. | Side slopes | 2:1 |
| 4. | Thickness of pitching | 2 ft. |
| 5. | Top level of apron | 677.0 ft. |

- Flood Embankment on Rainy Nallah near village Keeranwala East

| 1. | Length of embankment | 5000 ft. |
| --- | --- | --- |
| 2. | Top width | 15 ft. |
| 3. | Side slopes | 2:1 on both side |

iv)         RIVER MUNAWAR TAWI

Three Guide Bank Spurs, namely (a) Guide Bank Spur near village Lashkari Chak, (b) Guide Bank Spur near Village Barmala, (c) Guide Bank Spur near village Surkhpur have been constructed U/S Marala Head works on River Munawar Tawi to check the right wards drift of the river in order to save land, abadies and adjoining fertile agriculture lands. During unexpected freshets in River Munawar Tawi in 3/2003, an old creek got reactivated due to which D/S side of the shank of spur near Surkhpur and the nearby Surkhpur-Marala Road came under direct hit of the river. As an immediate remedy under attack part of the shank and the road were stone pitched while a model study was conducted to arrest the problem on permanent basis. This model study has recommended certain improvements in guide wall spurs near Surkhpur and Barmala as a permanent measure to protect the spurs, road and agricultural land. Irrigation department initiated a summary for seeking approval of the Chief Minister Punjab to execute work during the financial year under ADP 2004-2005, which were approved and the work has been completed.

XEN/GRT

3 NO. GUIDE BANK SPURS ON RIGHT BANK OF RIVER

MUNAWAR TAWI IN DISTRICT GUJRAT.

A salient feature is given as under:-

A)      Location    	=     Originate from Azad Jammu Kashmir                     to River Chenab

i)	Surkhpur 	=	Length = 1777’

Side slopes = 2:1 either Side

Top width=20ft.

ii)	Barmala	=	Length = 1666’	                                                                          Side slopes = 2:1 either Side

Top width=20ft.

iii)	Chak lashkri	=	Length = 1277’	                                                                          Side slopes = 2:1 either Side

Top width=20ft.

2.2	LOCATION MAP

Location Map is attached

XEN/GRT

CHAPTER – 3

BRIEF HISTORY OF PAST FLOOD EVENTS

Unexpected heavy rains in the first week of September, 1992 caused historic floods in the catchment area of Twin Rivers i.e. Jhelum and Chenab at the same occasion. The discharge in river Chenab at Marala Barrage 845090 Cs. was experienced on 10.9.1992 at 18.00 hours.  Similarly the flow in River Chenab at Qadirabad Barrage at 1800 hours of 9.9.1992 was only 41681 Cs. which started rising on 10.9.1992 morning and went upto 948530 Cs. on 11.9.1992. The flood water spread on the right side of River Chenab and river edge were badly damaged.

During subsequent flood seasons, the main river channel started drifting towards right side between Marala to Alexandra Bridge reach. As a result of this development, the entire river started flow along its right bank. Consequently, serious problems such as embayment, land erosion, bank sloughing and inundation of agricultural lands, basis infrastructures and villages were experienced. Due to this expanding erosive tendency of the river, a number of villages and thousands of acres of valuable agricultural land was lost to the river. This problem, therefore, required a suitable and effective preventive measure. To evolve an affective flood management plan for this area, model studies were carried out by the Irrigation Research Institute. 11 No. spurs were constructed along Right Bank of River Chenab from D/S Marala Headworks to Alexandra Ridge in District Gujrat.

During flood season of 1997, heavy rains started in Gujrat District on 26.8.1997. Incessant heavy rains continued for about 36 hours without any break. Situation took serious turn on 27-28/8/97 when heavy discharge in River Chenab (exceptionally high flood of 775525 Cs.) along with dangerous wind storm and heavy rain made the situation precarious. Floods in Nallahs also joined hands. Joint action blow was so serious that a time came when situation was out of the control of a man and it power. In fact, even it could be termed as a calamity or bolts from the blue. Following spurs/guide banks suffered heavy damages i.e J-head spur No. 2, 3,4,6,8, Guide bank spur No. 9 & Guide bank spur No. 10 were damaged. These damages were restored during financial year 1997 to 1999.

XEN/GRT

A high flood was received D/S Qadirabad Barrage on 7.8.2010 with  discharge of 319733 Cs. Resultantly a loop was developed in between guide wall spur on right bank of River Chenab opposite village Randiali and inverted hockey spur opposite village Bahri and J-Head Spur Chakori in District M.B.Din. The sites were inspected by the Executive Engineer, Gujrat Division UJC on 16.8.2010. The condition of structures was serious. The apron from RD 0-70 of the inverted hockey spur Bahri was completely launched and pitching slipped into the scour pit in different reaches. The shank of the spur has also washed away in a length of 70 feet. The apron and solid portion of J-Head spur Chakori was also badly damaged. The model study of these structures was made by the Irrigation Research Institute. In the light of design and proposals given by the Principal Research Officer (Hydraulics) the restoration work of Inverted Hockey Spur Bahri was carried out. Simultaneously J-Head Spur near village Chakori was also replenished re-constructed and restoration completed accordingly. The both works have been completed at site during the fiscal year of 2011-2012.

As regard, the following infrastructures were badly damaged during flood season 2010 which was repaired/restored.

Frukhpur Flood Bund

- Repairing & providing pitching in damage and vulnerable reaches of Farrukhpur flood bund.

Lala Musa Extension Flood Bund

- Protecting & restoring Lalamusa Extension Flood Bund from erosion of Bhimber Nallah by providing & laying pitching with apron.

Haveli Manik Guide Wall

- Restoration damaged and by-passed sloping stud U/S Haveli Manik Guide wall.

Bherwal Guide Wall

- Protecting/Restoring by passed solid stud D/S hockey spur near village Bherowal.

During subsequent flood season 2011 and 2012, the discharge received in River Chenab was 166383 Cs. and 170210 Cs. respectively. During this medium flood no damages were occurred fortunately.

During flood season 2013, a high flood was received with discharge of 369960 Cs. downstream Murala Barrage. This heavy discharge damaged various infrastructures which were existed on the right bank of River Chenab. The following works were taken up under Para 2.89 of PWD code.

XEN/GRT

| Sr. | Name of scheme |
| --- | --- |
| 1 | Construction of 3 No. Solid Stone Studs for protection of village Shahbazpur. |
| 2 | Protection of Farrukhpur flood bund on erosion side at RD 11-12 & 14-15. |
| 3 | Protecting & restoring of hockey stud/spur for protection of village Behlolpur from erosion of right side of River Chenab, |
| 4 | Protection abadies of village Bhutta Piran from erosion on Right Side of River Chenab. |

A work namely “Checking erosion on right bank of River Chenab to protect Bhekho out fall drain and agriculture land of Miana Hazara”.

The above scheme was approved by the Federal Flood Commission Islamabad and work completed during the Financial year 2012-13 to 2014-15.

| Sr. No. | Name of Work |
| --- | --- |
| 1. | Checking erosion on right bank of River Chenab to protect Bhekho out fall drain and agriculture land of Miana Hazara |

During that flood season a heavy flood was received in Bhimber Nallah which originates from the hills of Jammu and Kashmir and outfall in River Chenab upstream Khanki Head Works. The discharge of Bhimber Nallah raised up to 50596 Cfs which damaged the Lalamusa Flood Bund and Lalamusa Extension Flood Bund which had been constructed on the Right Bank for protection of Lalamusa City and allied abadies. The infrastructures damaged during peak flood and taken up under Para 2.89 of PWD code for restoration are as under:-

| Sr. | Name of scheme |
| --- | --- |
| 1 | Protecting & restoring Lalamusa Extension flood bund RD 7-8 from erosion of Bhimber Nallah by providing pitching with apron. |
| 2 | Restoring damaged between RD 17-18 of Lalamusa flood bund. |

During flood season 2014, a discharge of 856464 Cs. was received downstream Marala Barrage on 6.9.2014 which create a hue and cry situation in the surrounding abadies located on the Right Bank of River Chenab in District Gujrat. The hill torrents and nallahs also joined hands and enhanced the disturbance situation. The sudden increase in the discharge badly eroded the Right Bank of River Chenab as well as the infrastructures. It is also worth mentioning here that the heavy rains started in the first week of September 2014 in Gujrat District. The incessant heavy rains continued and the situation took serious turn hour to hour. Consequently an exceptional heavy flood played a

XEN/GRT

havoc role in the lives and livings of inhabitants of District Gujrat. Downstream Khanki Barrage the discharge of 947099 Cs. was received which created a hue and cry situation in the upstream locality and damaged a lot of agricultural and stock lives. The flood protection infrastructures and river training works between Marala Head Works to Khanki Head Works was also damaged.

Downstream Qadirabad Barrage 903504 Cs. Discharge passed which damaged the flood bunds, embankments; guide walls etc. existed on the right bank of River Chenab and falling in the jurisdiction of District Mandi Bahauddin. Consequently, the following infrastructures were damaged partially and to some extent.

| Sr. No. | Name of infrastructure/minor damaged |
| --- | --- |
| 1. | Restoration of J-Head Spur No. 2 between RD 3-4, 5-6 near village Pandi. |
| 2. | Restoration of J-Head Spur No.3 near Kotli village. |
| 3. | Restoration of J-Head Spur No. 4 near Dera Nasir. |
| 4. | Restoration of J-Head Spur Samma Mohla. |
| 5. | Restoration of J-Head Spur No. 8 near village Shahbazpur. |
| 6. | Restoration of J-Head Spur near village Shampur. |
| 7. | Restoration of Inverted Hockey Spur near village Behlolpur. |
| 8. | Restoration of damages/by pass sloping stud U/S Guide Wall Haveli Manik. |
| 9. | Restoration of cut between RD 23-24 of Farrukhpur Flood Bund. |
| 10. | Restoration of eroded bank between RD 3-4, 7-8, 10-11 and RD 21-22 of Farrukhpur Flood Bund. |
| 11. | Restoring cuts from RD 10-50100 tail of Qadirabad minor. |

The following works were taken up during the financial year 2014-15 and 2015-16.

INESCABLE WORKS

| Sr. No. | Name of infrastructure |
| --- | --- |
| 1. | Restoration of Guide wall spur No. 8 near village Shahbazpur |
| 2. | Restoration of eroded bank between RD 3-4, 7-8, 10-11, 11-12, 21-22 and closing cut between RD 23-24 Furkhpur Flood Bund. |

CRITICAL WORKS

| Sr. No. | Name of infrastructure |
| --- | --- |
| 1. | Restoration of J-head spur No. 2 near village Pandi on Right Side of River Chenab Damage during flood 2014. |
| 2. | Restoration damage pitching around the village and J-head spur near village Shampur on Right Side of River Chenab. |
|  |  | XEN/GRT |
| 3. | Restoration of inverted hockey spur near village Behlolpur on Right Side of River Chenab damage during flood 2014. |
| 4. | Protecting and restoring of inverted hockey spur for protection of village Behlolpur (By constructing 3 No. solid stone stud). |
| 5. | Restoration of Guide Bank spur near village Sukhpur on River Munawar Tawi. |
| 6. | Restoraiton damaged bypassed sloping stud U/S Guide wall Haveli Manik. |
| 7. | Restoration of J-head Spur No.3 near village Kot Patwan on Right side of River Chenab Damage During flood 2014. |
| 8. | Restoration of J-head Spur No. 4 near village Kalowal/Dera Nasir on Right Side of River Chenab Damage during flood 2014. |

OTHER WORK

| Sr. No. | Name of infrastructure |
| --- | --- |
| 1. | Construction of 5 No. solid stone stud for protection of village Chak Bazurg. |
| 2. | Construction of Solid stone stud to protect pitching of village Kokary. |
| 3. | Construction of 2 No. solid stone stud on dulli Nullah to protect village abadies of Malikpur Mirza. |

WORK EXECUTED UNDER PARA 2.89 OF PWD (2015-16)

| Sr. No. | Name of infrastructure |
| --- | --- |
| 1. | Checking erosive action of Chenab River near village Bhuta Maranran. |
| 2. | Restoration of existing Ganda bund and extension of Ganda bund near village Behlolpur, |

WORK EXECUTED UNDER PARA 2.89 OF PWD (2016-17)

| Sr. No. | Name of infrastructure |
| --- | --- |
| 1 | Checking erosive action of river Chenab U/S Stud No.1 near village Behlolpur. |
| 2 | Protecting Lala Musa extension bund between RD 6-7 by providing solid stone studs. |
| 3 | Restoration of damaged apron of spur No. 8 near village Shahbazpur damaged during flood 2016. |
| 4 | Checking erosive action of River Munwar Tawi at Guide bank spur near village Barmala. |
| 5 | Constructing solid stone studs on right bank of River Chenab to protect village Bhutta Marran |
|  | WORK EXECUTED UNDER PARA 2.89 OF PWD (2018-19 |
| 1 | Providing Protection to right bank of Nullah Bhimber in front of village Dadu Barsala. |
| CRITICALWORKS TAKEN UP DURING 2017-18 |
| 1 | Repairing pitching and launched apron of J-head Spur No. 5 on right bank of River Chenab. |
| 2 | Repairing of Ganda Bund No. 2 on right bank of River Chenab. |
| 3 | Restoration of Guide bank Spur at right bank of Munawar Tawi near village Surkhpur. |
| 4 | Restoration of Guide Wall Bahri Randiali. |
| 5 | Restoring of Solid Stone Stud near village Bahri.(Damages due to flood 2014 in River Chenab) |
| 6 | Restoration of Inverted Hockey spur RD 0+000 to 0+815 near village Bahri on right bank of river Chenab. |

XEN/GRT

CHAPTER – 4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS/BARRAGES AND OR OTHER CONTROL POINTS

  - FLOOD LIMITS OF MARALA HEAD WORKS

1.	Normal flood			=	0.0 – 1.0 lac Cs.

- Low flood			=	1.0 – 1.5 lac Cs.

3.	Medium flood			=	1.5 – 2.0 lac Cs.

4.	High flood			=	2.0 – 4.0 lac Cs.

5.	Very high flood		=	4.0 – 6.0 lac Cs.

6.	Exceptionally high flood	=	6.0 & above.

4.2	TIME LAGS OF FLOODS

- Distance 8 Km from Border to Murala time for flood water.= 2hours

AHKNOOR TO MURALA

- LOW Flood					=	9-10 hours.

- Medium Flood					=	8-9 hours.

- High Flood					=	7-8 hours.

- Very high Flood				=	5 hours.

- Exceptionally high Flood			=	4 hours.

Flood water above 1.00 lac

Marala to Alexandra bridge 	(42KM)	=	 5-6 hours.

Alexandra bridge to Khanki	(14KM)	= 	1.5-2 hours

Khanki to Qadirabad		(28KM)	= 	3-4 hours

  - HIGHEST FLOODS

1992		-		845090 Cs. Marala Barrage

1992		-		650000 Cs. Alexandra Bridge

1992		-		910000 Cs.  Khanki Headworks

1992		-		948530 Cs. Qadirabad Barrage

2014		-		856464 Cs. Marala Barrage

2014		-		780216 Cs. Alexandra Bridge

2014		-		947099 Cs.  Khanki Headworks

2014		-		903504 Cs. Qadirabad Barrage

XEN/GRT

4.4	PEAK DISCHARGES.

i)           YEARLY PEAK DISCHARGES OF RIVER CHENAB AT MARALA

| Year | Peak Flood | Year | Peak Flood | Year | Peak Flood |
| --- | --- | --- | --- | --- | --- |
| 1925 | 139596 | 1959 | 870795 | 1993 | 409490 |
| 1926 | 202765 | 1960 | 599303 | 1994 | 472570 |
| 1927 | 237718 | 1961 | 272003 | 1995 | 439970 |
| 1928 | 686000 | 1962 | 331362 | 1996 | 766860 |
| 1929 | 718000 | 1963 | 204158 | 1997 | 775525 |
| 1930 | 254000 | 1964 | 215863 | 1998 | 213705 |
| 1931 | 260238 | 1965 | 144677 | 1999 | 214765 |
| 1932 | 332326 | 1966 | 618338 | 2000 | 247610 |
| 1933 | 366000 | 1967 | 190386 | 2001 | 160950 |
| 1934 | 228000 | 1968 | 155262 | 2002 | 224780 |
| 1935 | 253000 | 1969 | 219302 | 2003 | 313024 |
| 1936 | 177500 | 1970 | 203733 | 2003 | 147318 |
| 1937 | 145759 | 1971 | 175143 | 2004 | 93150 |
| 1938 | 261700 | 1972 | 132915 | 2005 | 345479 |
| 1939 | 203000 | 1973 | 769550 | 2006 | 332956 |
| 1940 | 167100 | 1974 | 192630 | 2007 | 252409 |
| 1941 | 297000 | 1975 | 582600 | 2007 | 148627 |
| 1942 | 301500 | 1976 | 549400 | 2008 | 174977 |
| 1943 | 256900 | 1977 | 437125 | 2009 | 94168 |
| 1944 | 150500 | 1978 | 456394 | 2010 | 282418 |
| 1945 | 207650 | 1979 | 248111 | 2011 | 166383 |
| 1946 | 263540 | 1980 | 199981 | 2012 | 169914 |
| 1947 | 253720 | 1981 | 527462 | 2013 | 369960 |
| 1948 | 432000 | 1982 | 647098 | 2014 | 856464 |
| 1949 | 251956 | 1983 | 171579 | 2015 | 153408 |
| 1950 | 540761 | 1984 | 160042 | 2016 | 412065 |
| 1951 | 193847 | 1985 | 222595 | 2017 | 187470 |
| 1952 | 209570 | 1986 | 241800 | 2018 | 168278 |
| 1953 | 316898 | 1987 | 114140 | 2019 | 211296 |
| 1954 | 820090 | 1988 | 481365 | 2020 | 298884 |
| 1955 | 344090 | 1989 | 352115 |  |  |
| 1956 | 272200 | 1990 | 160020 |  |  |
| 1957 | 1100000 | 1991 | 40560 |  |  |
| 1958 | 478457 | 1992 | 845090 |  |  |

XEN/GRT

- YEARLY PEAK DISCHARGE OF RIVER CHENAB AT ALEXANDRA                         BRIDGE.

| Year | Peak Flood | Year | Peak Flood | Year | Peak Flood |
| --- | --- | --- | --- | --- | --- |
| 1932 | 269000 | 1966 | 439763 | 2000 | 120063 |
| 1933 | 242926 | 1967 | 162625 | 2001 | 143424 |
| 1934 | 144576 | 1968 | 110000 | 2002 | 229780 |
| 1935 | 256754 | 1969 | 160223 | 2003 | 311873 |
| 1936 | 152264 | 1970 | 149106 | 2004 | 64340 |
| 1937 | 99516 | 1971 | 179714 | 2005 | 283019 |
| 1938 | 255716 | 1972 | 171690 | 2006 | 359400 |
| 1939 | 166948 | 1973 | 640000 | 2007 | 298752 |
| 1940 | 124310 | 1974 | 116315 | 2007 | 192414 |
| 1941 | 164819 | 1975 | 448000 | 2008 | 101000 |
| 1942 | 203644 | 1976 | 500000 | 2010 | 286817 |
| 1943 | 233000 | 1977 | 340000 | 2011 | 169705 |
| 1944 | 160000 | 1978 | 126000 | 2012 | 170210 |
| 1945 | 174795 | 1979 | 103556 | 2013 | 405068 |
| 1946 | 214311 | 1980 | 116990 | 2014 | 780216 |
| 1947 | 310000 | 1981 | 206049 | 2015 | 134340 |
| 1948 | 404000 | 1982 | 279240 | 2016 | 257200 |
| 1949 | 212000 | 1983 | 185645 | 2017 | 155575 |
| 1950 | 243500 | 1983 | 185645 | 2018 | 139120 |
| 1951 | 138472 | 1985 | 201800 | 2019 | 186000 |
| 1952 | 114900 | 1986 | 309964 | 2020 | 274800 |
| 1953 | 246156 | 1987 | 133160 |  |  |
| 1954 | 812500 | 1988 | 842246 |  |  |
| 1955 | 812500 | 1989 | 433400 |  |  |
| 1956 | 213600 | 1990 | 309415 |  |  |
| 1957 | 1100000 | 1991 | -- |  |  |
| 1958 | 420000 | 1992 | 650000 |  |  |
| 1959 | 560000 | 1993 | 600000 |  |  |
| 1960 | 325000 | 1994 | 217000 |  |  |
| 1961 | 225000 | 1995 | 441000 |  |  |
| 1962 | 292345 | 1996 | 786000 |  |  |
| 1963 | 150846 | 1997 | 619000 |  |  |
| 1964 | 286271 | 1998 | 260000 |  |  |
| 1965 | 163964 | 1999 | 105113 |  |  |

XEN/GRT

iii)	YEARLY PEAK DISCHARGES OF RIVER CHENAB AT KHANKI.

| Year | Peak flood | Year | Peak flood | Year | Peak Flood |
| --- | --- | --- | --- | --- | --- |
| 1925 | 266809 | 1960 | 809524 | 1995 | 650000 |
| 1926 | 224640 | 1961 | 353994 | 1996 | 851000 |
| 1927 | 223796 | 1962 | 346279 | 1997 | 847000 |
| 1928 | 441497 | 1963 | 186435 | 1998 | 214954 |
| 1929 | 747000 | 1964 | 176590 | 1999 | 170815 |
| 1930 | 194376 | 1965 | 200618 | 2000 | 309253 |
| 1931 | 292098 | 1966 | 636670 | 2001 | 155648 |
| 1932 | 271769 | 1967 | 209767 | 2002 | 240389 |
| 1933 | 246163 | 1968 | 235397 | 2003 | 371888 |
| 1934 | 177813 | 1969 | 274357 | 2003 | 172593 |
| 1935 | 259730 | 1970 | 251954 | 2004 | 106934 |
| 1936 | 15946 | 1971 | 293293 | 2005 | 368078 |
| 1937 | 105835 | 1972 | 811723 | 2006 | 418740 |
| 1938 | 261685 | 1973 | 1000496 | 2007 | 300197 |
| 1939 | 175979 | 1974 | 189446 | 2008 | 202000 |
| 1940 | 128393 | 1975 | 666241 | 2009 | 74550 |
| 1941 | 168687 | 1976 | 615043 | 2010 | 327637 |
| 1942 | 210357 | 1977 | 472130 | 2011 | 131492 |
| 1943 | 238169 | 1978 | 433096 | 2012 | 186413 |
| 1944 | 164719 | 1979 | 246867 | 2013 | 410332 |
| 1945 | 180122 | 1980 | 194814 | 2014 | 947099 |
| 1946 | 149681 | 1981 | 563856 | 2015 | 163967 |
| 1947 | 236583 | 1982 | 243260 | 2016 | 418736 |
| 1948 | 438529 | 1983 | -- | 2017 | 184346 |
| 1949 | 224949 | 1984 | 134897 | 2018 | 182025 |
| 1950 | 986658 | 1985 | 148482 | 2019 | 181944 |
| 1951 | 217868 | 1986 | 341000 | 2020 | 286230 |
| 1952 | 264065 | 1987 | 109413 |  |  |
| 1953 | 315330 | 1988 | 844050 |  |  |
| 1954 | 806774 | 1989 | 512225 |  |  |
| 1955 | 230490 | 1990 | 270015 |  |  |
| 1956 | 340663 | 1991 | 314553 |  |  |
| 1957 | 1086460 | 1992 | 910000 |  |  |
| 1958 | 401682 | 1993 | 366680 |  |  |
| 1959 | 1021018 | 1994 | 509113 |  |  |

XEN/GRT

iv.     YEARLY PEAK DISCHARGES OF RIVER CHENAB AT

QADIRABAD

| Year | Peak discharge | Year | Peak discharge |
| --- | --- | --- | --- |
| 1968 | 221607 | 2004 | 90043 |
| 1969 | 360038 | 2005 | 379572 |
| 1970 | 240401 | 2006 | 443206 |
| 1971 | 312098 | 2007 | 311382 |
| 1972 | 249259 | 2008 | 194038 |
| 1973 | 854341 | 2009 | 55535 |
| 1974 | 198228 | 2010 | 319733 |
| 1975 | 669819 | 2011 | 164604 |
| 1976 | 628741 | 2012 | 180789 |
| 1977 | 482871 | 2013 | 403403 |
| 1978 | 428009 | 2014 | 903504 |
| 1979 | 240785 | 2015 | 175054 |
| 1980 | 178582 | 2016 | 416492 |
| 1981 | 575440 | 2017 | 164660 |
| 1982 | 245030 | 2018 | 172031 |
| 1983 | 303120 | 2019 | 159544 |
| 1984 | 108476 | 2020 | 258954 |
| 1985 | 321917 |  |  |
| 1986 | 318117 |  |  |
| 1987 | 342758 |  |  |
| 1988 | 892266 |  |  |
| 1989 | 497649 |  |  |
| 1990 | 290417 |  |  |
| 1991 | -- |  |  |
| 1992 | 948530 |  |  |
| 1993 | 434754 |  |  |
| 1994 | 425567 |  |  |
| 1995 | 644397 |  |  |
| 1996 | 853231 |  |  |
| 1997 | 873442 |  |  |
| 1998 | 259713 |  |  |
| 1999 | 630500 |  |  |
| 2000 | 291349 |  |  |
| 2001 | 136575 |  |  |
| 2002 | 226398 |  |  |
| 2003 | 367408 |  |  |
| 2003 | 159296 |  |  |

XEN/GRT

v.        YEARLY MAXIMUM GAUGES OF BHIMBER NULLAH   RECORDED                     AT RALWAY CROSSING  G.T.ROAD GUJRAT.

| Sr.No. | Year | Maximum | Approximate discharge |
| --- | --- | --- | --- |
| 1. | 1973 | 782.00 | 77898 |
| 2. | 1975 | 782.00 | 77898 |
| 3. | 1976 | 781.00 | 68367 |
| 4. | 1977 | 781.00 | 68367 |
| 5. | 1978 | 782.00 | 77898 |
| 6. | 1979 | 777.00 | 34709 |
| 7. | 1980 | 777.00 | 34706 |
| 8. | 1981 | 778.00 | 42402 |
| 9. | 1982 | 777.00 | 34709 |
| 10. | 1983 | 777.00 | 34706 |
| 11. | 1984 | 779.50 | 5130 |
| 12. | 1985 | 782.00 | 77898 |
| 13. | 1986 | 778.00 | 42404 |
| 14. | 1987 | 778.20 | 42600 |
| 15. | 1988 | 782.40 | 77938 |
| 16. | 1989 | 778.00 | 42402 |
| 17. | 1990 | 770.80 | 42009 |
| 18. | 1991 | 778.10 | 42407 |
| 19. | 1992 | 780.00 | 59256 |
| 20. | 1993 | 775.80 | 42282 |
| 21. | 1994 | 780.00 | 59256 |
| 22. | 1995 | 778.00 | 42402 |
| 23. | 1996 | 777.20 | 42358 |
| 24. | 1997 | 778.50 | 42538 |
| 25. | 1998 | 775.00 | 20951 |
| 26. | 1999 | 777.00 | 428347 |
| 27. | 2000 | 773.10 | 42135 |
| 28. | 2001 | 775.40 | 42260 |
| 29. | 2002 | 776.00 | 27541 |
| 30. | 2003 | 775.00 | 20951 |
| 31. | 2004 | 777.00 | 34706 |
| 32. | 2005 | 776.00 | 27542 |
| 33. | 2006 | 772.00 | 5300 |
| 34. | 2006 | 777.00 | 34706 |
| 35. | 2007 | 773.03 | 9737 |
| 36. | 2008 | 775.00 | 20951 |
| 37. | 2009 | 773.00 | 9737 |
| 38. | 2010 | 777.50 | 38991 |
| 39. | 2011 | 772.00 | 5300 |
| 40. | 2012 | 776.00 | 27541 |
| 41. | 2013 | 777.00 | 34706 |
| 42. | 2014 | 779.00 | 50596 |
| 43. | 2015 | 774.00 | 14991 |
| 44 | 2016 | 775.00 | 20951 |
| 45 | 2017 | 773.00 | 9737 |
| 46 | 2018 | 776.00 | 27541 |
| 47 | 2019 | 771.00 | 1874 |
| 48 | 2020 | 774.00 | 14991 |

XEN/GRT

Vi       YEARLY MAXIMUM GAUGES OF HALSI NALLAH RECORDED AT 	GUJRAT JALALPUR JATTAN BRIDGE CROSSING AT RD 18500 	GUJRAT FLOOD BUND.

| Year | Maximum gauge |
| --- | --- |
| 1973 | 12.00 |
| 1975 | 11.20 |
| 1976 | 11.60 |
| 1980 | 4.90 |
| 1981 | 10.00 |
| 1982 | 8.00 |
| 1983 | 2.00 |
| 1984 | 9.50 |
| 1985 | 10.50 |
| 1986 | 10.00 |
| 1987 | 9.00 |
| 1988 | 11.00 |
| 1989 | 10.40 |
| 1990 | 9.00 |
| 1991 | 10.00 |
| 1992 | 7.00 |
| 1993 | 8.00 |
| 1994 | 10.50 |
| 1995 | 10.80 |
| 1996 | 7.60 |
| 1997 | 10.00 |
| 1998 | 8.00 |
| 1999 | -- |
| 2000 | 4.20 |
| 2001 | 5.50 |
| 2002 | 5.40 |
| 2003 | 5.50 |
| 2004 | 4.00 |
| 2005 | -- |
| 2006 | 6.00 |
| 2007 | 4.00 |
| 2008 | 4.50 |
| 2009 | 3.00 |
| 2010 | 5.50 |
| 2011 | 4.00 |
| 2012 | 7.20 |
| 2013 | 6.00 |
| 2014 | 7.00 |
| 2015 | 5.00 |
| 2016 | 4.00 |
| 2017 | 7.00 |
| 2018 | 5.00 |
| 2019 | 3.00 |
| 2020 | -- |

XEN/GRT

CHAPTER - 5

FLOOD FIGHTING STRATEGY

In order to combat the flood, the following plan is to be put in operation for each River or Nallah and protective works on it.

BHIMBER NALLAH

- LALAMUSA FLOOD BUND

2 No. Gang huts are constructed at RD 14000 and 29000 in order to provide shelter to the seasonal establishment as well as to store flood fighting material. An emergency camp/store will be maintained at RD 40000 Lalamusa bund during flood season as this site is under direct hit of Nallah. List of flood fighting material for each control point is attached. Sub Engineer Gujrat Section and Sub Divisional Officer Gujrat Sub Division will be incharge of this bund to carry out all sorts of flood fighting operations.

- BHIMBER RIGHT FLOOD BUND

Flood fighting operation will be carried out by Sub Engineer Incharge i.e. Sub Engineer Gujrat Section, under the supervision of Sub Divisional Officer, Gujrat. Temporary camps/control points, will be set up at RD 7500 left side and at RD 17000 on right side, 2 temporary work charge gangs consisting of 1 Mate with eight beldars will be engaged in each shift for right & left bunds during flood season as no regular establishment exists. Necessary flood fighting material as per list attached will be kept at control points to meet with any emergency. In case of emergency, Sub Engineer Gujrat Section will inform District Flood Control Center and Deputy District Officer (Rev) Gujrat to seek all sort of assistance to control the situation at site. Sector Commander at Gujrat & Deputy District Officer (Rev) Gujrat will assist the department in case of any emergency. Executive Engineer, Gujrat Division UJC will supervise overall flood operations on Bhimber Flood Bunds in addition to other bunds of the Division.

BHINDER NULLAH

iii)        MUSAKAMALA FLOOD BUND

2 No. gang huts at RD 10000 and 14000 Musakamala bund have been constructed which will be equipped with necessary flood fighting material as per list attached to cope with any situation during emergency.

XEN/GRT

Sub Engineer Gujrat Section and Sub Divisional Officer Gujrat Sub Division are incharge of this bund. In case of any emergency, District Flood Control Center will be approached to seek assistance whenever necessary. An additional Sub Engineer within the Division will be deputed to assist the Sub Engineer Gujrat, during flood days.

In case of emergency, Gujrat Section becomes an important site, any other Sub Engineer from the Division will be given charge of this bund.

HALSI NULLAH

iv)	GUJRAT FLOOD BUND

2 No. gang huts at RD 10000 and RD 18500 Gujrat Bund have been constructed which will be equipped with necessary flood fighting material. Sub Engineer Leave Reserve and Sub Divisional Officer Gujrat Sub Division UJC shall be inchage of this bund.

In case of emergency, Sub Engineer Leave Reserve will inform District Flood Control Center to seek all possible assistance to control the situation to avoid any untoward accident.

Sector Commander at Gujrat city will be available to assist the department in case of any eventuality. Executive Engineer Gujrat Division UJC will supervise overall flood operations of Gujrat Flood Bund in addition to other bunds of Gujrat Division.

DAWARA NULLAH

V)         DAWARA NULLAH BUND

Sub Engineer leave reserve-II will be incharge of this bund in addition to Gujrat Flood Bund and will supervise flood fighting operations under the direction of Sub Divisional Officer, Gujrat Sub Division. In case of emergency, Sub Engineer Leave Reserve will inform District Flood Control Center to seek all possible assistance to control the situation to avoid any untoward accident.

RIVER CHENAB

Vi)      SPURS ON RIGHT BANK OF RIVER CHENAB IN

GUJRAT DISTRICT

During flood season distribution of duty shall be as under:-

| Sr. No. | Name of spur | Sub Divisional office |
| --- | --- | --- |
| 1. | Spur No. 1,2,3,4,5 | S&I Gujrat |
| 2. | Spur No. 6,7,8 | -do- |
| 3. | Spur No. 9,10,11 | -do- |
| 4. | 3 No. spurs on River Munawar Tawi | -do- |

XEN/GRT

In case of emergency on the request of Sub Divisional Officer,Survey & Investigation, the Executive Engineer Gujrat will order to deploy Sub Divisional Officer Sohawa and Busal along with their subordinate staff to assist/coordinate Sub Divisional Officer Survey & Investigation to cope with the emergency.  Every spur temporary camp sites will be equipped with flood fighting material to meet with any emergency. Sub Engineer and Sub Divisional Officer Incharge will be responsible to adopt protective measures during emergency to save the structures. Executive Engineer Gujrat Division UJC will be the overall incharge of flood fighting operation. During acute emergency, District Coordination Officer, Gujrat and District Police Officer, Gujrat will be approached to assist the department.

Vii)       CHUKNANWALI FLOOD BUND

Sub Engineer Kalupindi Section and Sub Divisional Officer Gujrat Sub Division are incharge of this flood bund. The flood does not touch this bund upto 5.0 lac cusecs discharge below Qadirabad Barrage. At a discharge of 6.50 lac cusecs below Qadirabad Barrage, Sub Engineer Kalupindi will shift to RD 147000 of Chuknanwali disty (15-R) for watching the bund. Between 6.5 to 8.0 lac cs. of discharge below Qadirabad Barrage sheet flow will touch the bund at RD 128-tail. However watching against sheet flow will be continued, when the discharge below Qadirabad Barrage is beyond 8.00 lac cs. Sub Divisional Officer Gujrat will also shift his camp to this bund and supervise watching operation.

In case of emergency, Sub Engineer Kalupindi will inform the Sector Commander Mano Chak and S.H.O Phalia who will inform all concerned through wireless about the situation and the help if needed will also be arranged by Sector Commander and Police authorities.

In case of simultaneous floods in Chenab & Bhimber Nullah, Sub Divisional Officer Busal will be incharge of Chuknanwali Flood Bund.

viii)		HUMBER PROTECTION BUND

Sub Engineer Bhikho and Sub Divisional Officer Phalia are incharge of this bund. Emergency flood fighting material as per list attached will also be available at huts, which have already been constructed for this purpose at vulnerable sites i.e. RD 20000,   RD 33000 and at RD 47000.

XEN/GRT

There is no likelihood of the flood water touching the bund upto 3.50 lac cs. discharge below Qadirabad Barrage. At 5.00 lac of discharge below Qadirabad Barrage, the flood water touches the bund in reach RD 10000 to RD 47000 and in this situation there is no likelihood of any attack on the bund. However when the discharge below Qadirabad exceeds 5.00 cusecs, the Sub Engineer Phalia will also shift his headquarter from Duggal Rest House to RD 55000 of Humber Protection Bund to watch the said bund from RD 40000 to 82500 and Sub Engineer Bhikho shall be incharge of reach RD 0-40000 with temporary headquarter at RD 33000. The gang huts on these points have already been constructed.

When the discharge below Qadirabad is more than 5.50 lac cusecs Sub Divisional Officer Phalia will also shift his camp to Humber flood bund and will be overall incharge of watching Humber Protection Bund. In case of acute emergency District Coordination, Mandi Bahauddin and District Police Officer, Mandi Bahauddin will be approached to assist the Department.

ix.	FARRUKHPUR FLOOD BUND

The said bund falls on the right edge of Budi Nallah having a length of 6.80 Miles. The condition of this bund at RD 13-17, 21-22 and 31-32 is very much critical. During the spilling of flood water from the River Chenab and entring in the Budi Nallah and running parallel in the toe of bund which may damage the Farrukhpur Flood Bund and adjoining abadies i.e. Qadirabad city, Alan, Thathi Shah Muhammad, Noshera, Farrukhpur, Melu and Watto and then enters again in the River Chenab opposite village Farrukhpur.

x.	KEERANWALA EAST FLOOD EMBANKMENT

The said flood bund falls on the right edge of Bhinder Nallah having a length of 1.01 mile. The condition of this embankment is satisfactory.

XEN/GRT

CHAPTER – 6

FLOOD DAMAGES RESTORATION WORKS

The following sites were damaged during flood season 2010 and work completed during 2010-11 which are as under:-

| Sr.# | Name of Scheme |
| --- | --- |
| 1. | Protecting & Restoring J-Head Spur Chakori |
| 2. | Protecting & Restoring and back extension of shank of the Inverted Hockey Spur and Providing sloping stud U/S of Inverted Hockey near Bari Village to eradicate the chance of by-pass of the River |

B)	The following sites were damaged during flood season 2013 and works have been taken up under para 2.89 of PWD Code.

| Sr. # | Name of scheme |
| --- | --- |
| 1 | Protecting & restoring Lalamusa Extension flood bund RD 7-8 from erosion of Bhimber Nallah by providing pitching with apron |
| 2 | Construction of 3 No. solid stone studs for protection of village Shahbazpur |
| 3 | Protecting abadies of village Bhutta Piran from erosion of right side of River Chenab. |
| 4 | Protection of Farrukhpur flood bund on erosion side at RD 11-12 & 14-15. |
| 5 | Protecting & restoring of hockey stud/spur for protection of village Behlolpur from erosion of right side of River Chenab. |
| 6 | Restoring damaged between RD 17-18 of Lalamusa flood bund |
| CRITICAL WORKS TAKEN UP DURING 2017-18 |
| 1 | Repairing pitching and launched apron of J-head Spur No. 5 on right bank of River Chenab. |
| 2 | Repairing of Ganda Bund No. 2 on right bank of River Chenab. |
| 3 | Restoration of Guide bank Spur at right bank of Munawar Tawi near village Surkhpur. |
| 4 | Restoration of Guide Wall Bahri Randiali. |
| 5 | Restoring of Solid Stone Stud near village Bahri.(Damages due to flood 2014 in River Chenab) |
| 6 | Restoration of Inverted Hockey spur RD 0+000 to 0+815 near village Bahri on right bank of river Chenab. |

XEN/GRT

CHAPTER – 7

FLOOD FIGHTING WATCHING ARRANGEMENT

7.1	PRE-FLOOD ARRANGEMENT

Necessary flood fighting material is available on stock. Structure wise status of Reserve Stock of stone is as under:-

| SR. NO. | NAME OF DIVISION /NAME OF INTERVENTION | SANCTIONED LIMIT OF RESERVE STOCK (Lac CFT) | STONE AVAILABLE AT SITE (LAC CFT) | BALANCE QUANTITY REQUIRED |
| --- | --- | --- | --- | --- |
| 1 | J-head spur No. 1 U/S Alexandra bridge. | 0.50 | 0.26 | 0.24 |
| 2 | J-head spur No. 2 near village Pandi. | 1.00 | 0.17 | 0.83 |
| 3 | J-head spur No. 3 near village Kotli. | 0.50 | 0.06 | 0.44 |
| 4 | J-head spur No. 4 near village Dera Hakim. | 0.50 | 0.07 | 0.43 |
| 5 | J-head spur No. 5 near village Lambor. | 0.50 | 0.45 | 0.05 |
| 6 | J-head spur No. near village Kot Nikka. | 0.50 | 0.11 | 0.39 |
| 7 | J-head spur No. 7 near village Dawara Nallah. | 0.50 | 0.16 | 0.34 |
| 8 | J-head spur No. 8 near village Shahbazpur. | 1.00 | 0.20 | 0.80 |
| 9 | Guide bank spur No. 9 near Dera Hakim. | 1.00 | 0.17 | 0.83 |
| 10 | Guide bank spur No. 10 near Sajawal. | 0.75 | 0.26 | 0.49 |
| 11 | Guide bank spur No. 11 near village Chopala. | 0.75 | 0.25 | 0.50 |
| 12 | Guide bank near village Barmala on River Tawi. | 0.50 | 0.08 | 0.42 |
| 13 | Guide bank near village Surkhpur on River Tawi. | 0.50 | 0 | 0.50 |
| 14 | Guide bank near village Lashkari Chak on River Tawi. | 0.50 | 0 | 0.50 |
| 15 | Lalamusa flood bund | 0.80 | 0.14 | 0.66 |
| 16 | Musakamala flood bund. | 0.50 | 0 | 0.50 |
| 17 | Bhimber left flood bund. | 0.50 | 0 | 0.50 |
| 18 | Bhimber right flood bund. | 0.50 | 0 | 0.50 |
| 19 | Humber flood bund. | 0.50 | 0 | 0.50 |
| 20 | Chuknawali flood bund. | 0.50 | 0 | 0.50 |
| 21 | Guide wall on kalashadian. | 1.00 | 0.84 | 0.16 |
| 22 | Guide wall/spur of Sheikh Choghani. | 0.35 | 0 | 0.35 |
| 23 | J-head spur D/S Alexandra bridge to check erosion near village Samma, Mohla, Qilladar and Sandar etc. on right bank of River Chenab Tehsil & District Gujrat. | 1.00 | 0 | 1.00 |

XEN/GRT

| S. NO. | NAME OF DIVISION /NAME OF INTERVENTION | SANCTIONED LIMIT OF RESERVE STOCK ( Lac CFT) | STONE AVAILABLE AT SITE (LAC CFT) | BALANCE QUANTITY REQUIRED |
| --- | --- | --- | --- | --- |
| 24 | J-head spur near village Shampur on right bank of River Chenab. | 1.00 | 0 | 1.00 |
| 25 | Restoration of Existing Ganda Bund and Extension of Ganda Bund near village Behlolpur. | 0.40 | 0.40 | 0 |
| 26 | Pitchng on inner slopes of Halsi Nallah from RD 46000-48000 & RD 33500-51500 to check sloughing bank erosion and spill of Halsi Nallah. | 2.00 | 0 | 2.00 |
| 27 | Sloping spur D/S spur No. 3 to check erosion on River Chenab near village Patwan. | 0.50 | 0 | 0.50 |
| 28 | Sloping stud D/S spur No. 4 near village Kot Ghulam. | 0.50 | 0 | 0.50 |
| 29 | Sloping stud U/S spur No. 8 near village Changanwali. | 0.50 | 0 | 0.50 |
| 30 | Guide wall spur near Bari and Randiali. | 1.00 | 0 | 1.00 |
| 31 | Guide wall spur near Farrukhpur village. | 1.00 | 0.03 | 0.97 |
| 32 | J-head spur near Chakori village. | 1.00 | 0.45 | 0.55 |
| 33 | Guide wall spur near Noorpur Village. | 1.00 | 0 | 1.00 |
| 34 | Guide wall spur U/S Haveli Manik. | 1.00 | 0 | 1.00 |
| 35 | Farrukhpur Flood Bund | 0.50 | 0 | 0.50 |
|  | Grand Total | 25.05 | 4.10 | 20.95 |

The balance quantity of stone will be procured after receipt of funds.

  - WATCHING ESTABLISHMENT

Following watching establishment will be engaged during the flood season for watching & general maintenance of flood works on monthly basis. However in case of very high flood or in real emergency the strength of watching establishment will be increased with the express permission of Executive Engineer Gujrat Division UJC. Day & night watching will be done in the months of July, August & September as the chances of flood are maximum during these months

| Sr. No. | Name of bund/protection works | For maintenance & watching in each shift during flood season |
| --- | --- | --- |
|  |  | Beldar | Mate | Gauge Reader | Chowkidar |
| 1. | Lalamusa bund. | 24 | 2 | 2 | 5 |
| 2. | Bhimber left bund. | 6 | 1 | -- | 1 |
| 3. | Bhimber right bund. | 6 | -- | 1 | 1 |
| 4. | Musakamala flood bund | 5 | -- | 1 | 1 |
| 5. | Gujrat flood bund. | 10 | 1 | 1 | 4 |
| 6. | Dawara Nallah. | 1 | -- | -- | -- |
| 7. | 11 No. spurs on right bank of River Chenab +3 No. Guide bank spurs. | 48 | 4 | -- | 13 |
| 8. | Chuknawali flood bund | 7+7=14 | 1 | 1 | 1 |
| 9. | Humber flood bund. | 21 | 1 | 1 | 3 |
| 10. | Guide wall spur Kala Shadian, Bari & Randiali.Hockey bari | 4+4+4=12 | -- | -- | 1+1+1=3 |
| 11. | Samma Mohla spur. | 8 | -- | 1 | 1 |
| 12. | 3 No. Guide wall spur on Munawar Tawi River. | 25 | 2 | -- | 4 |
| 13. | J-head spur near village Shampur. | 9 | -- | -- | 1 |
| 14. | J-head spur chakori | 10 | 1 | -- | 1 |
| 15. | Flood embankment keeranwala East | 1 | -- | -- | 1 |
| 16. | Farrukhpur flood bund | 15 | 3 | -- | 3 |

7.3	ARRANGEMENT AT SENSITIVE SITES

Necessary Flood Fighting Camps will be established at sensitive sites on 16th June 2021. The detail as under.

- BHIMBER NULLAH

i)       Lalamusa Bund		 =	          RD 14000,29000,40000

ii)      	Lalamusa Ist Extension)       =

iii)	Lalamusa 2nd Extension)       =           	RD 11500, 20000

iv)  	Bhimber left Bund		 =	           RD 7500

v)     Bhimber Right Bund            	 =           	RD 17000

2)       BHIMBER/BHINDER NULLAHS

i)	Musakamala Bund		=	RD 10000, 14000

3)	HALSI NULLAH

i)	Flood Bund		            =	RD 11000, 18500+

one camp near kuthala Chenab &one camp RD 13300

4)	RIVER CHENAB

- 17 No. spurs

On every spur necessary temporary camp sites shall be equipped with flood fighting material to meet with any emergency.

5)     CHUKNANWALI FLOOD BUND          	=	         RD 166000

- HUMBER FLOOD PROTECTION

BUND 				           =      RD 20000,33000,47000

XEN/GRT

  - WATCHING MATERIAL

| Sr. No. | Item | RequiredQuantity | Available | Balance required |
| --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |
| 4 | Ballies | 50 No. | -- | 50 No. |
| 5 | Service cable | 4 Coil | -- | 4 Coil |
| 6 | Wicks | 24 No. | -- | 24 No. |
| 7 | Sprit | 2 Bottles | -- | 2 Bottles |
| 8 | Match box | 1 Dozen | -- | 1 Dozen |
| 9 | Petrol | 500 Ltrs. | -- | 500 Ltrs. |
| 10 | M. Oil | 100 Ltrs. | -- | 100 Ltrs. |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |
| 12 | Spare chargeable cells AA size | 6 No. | -- | 6 No. |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |
| 14 | Cooking utensils 6 persons set | 1 No. | -- | 1 No. |
| 15 | Base set | 2 No. | -- | 2 No. |

WATCHING MATERIAL(TOTAL AVAILABLE

| Sr. No. | Item | Location | Total Quantity | Available Quantity | Balance Quantity |
| --- | --- | --- | --- | --- | --- |
| 1. | Lantern | Canal Colony Gujrat | 140 No. | 140 No. | -- |
| 2. | Chimneys for lanterns |  | 70 No. | 70 No. | -- |
| 3. | Torches with cells |  | 42 No. | 42 No. | -- |
| 4. | Axes |  | 70 No. | 70 No. | -- |
| 5. | Kassies with handles |  | 100 No. | 100 No. | -- |
| 6. | Baskets |  | 110 No. | 110 No. | -- |
| 7. | Handles for kassies |  | 140 No. | 140 No. | -- |
| 8. | Gas lamps |  | 28 No. | 28 No. | -- |
| 9. | G.I. wire |  | 1400 kg. | 1400 kg. | -- |
| 10 | Generator Set large |  | 1 No. | 1 No. | -- |
| 11 | Generator set small |  | 1 No. | 1 No. | -- |
| 12 | Service cable |  | 28 ft. | 28 ft. | -- |
| 13 | Wicks |  | 336 No. | 336 No. | -- |
| 14 | Sprit |  | 28 Bottles | 28 Bottles | -- |
| 15 | Match box |  | 14 dozen | 14 dozen | -- |
| 16 | Wooden mallet |  | 24 No. | 24 No. | -- |
| 17 | Search light |  | 10 No. | 10 No. | -- |
| 18 | Tents |  | 8 No. | 8 No. | -- |
| 19 | Wireless set Walky Talky VX-300 |  | 1 Set | 1 Set | -- |
| 20 | Spare chargeable cells AA size |  | 14 No. | 14 No. | -- |
| 21 | Gas lamp/Stove with 2 KG gas filled cylinder |  | 14 No. | 14 No. | -- |

XEN/GRT

| Sr. No. | Item | Quantity | Balance | Required |
| --- | --- | --- | --- | --- |
| 22 | Pedestal fan | 14 No. | 14 No. | -- |
| 23 | Cooking utensils 6 persons set | 14 No. | 14 No. | -- |
| 24 | Patha ban | 10 K.G | 10 K.G | -- |
| 25 | Shouldari | 7 No. | 7 No. | -- |
| 26 |  |  |  |  |
| 27 | Table with six Chairs | 2 Set | 2 Set | -- |
| 28 | Camping Chairs | 2 Dozen | 2 Dozen | -- |
| 29 | Charpai | 6 No. | 6 No. | -- |
| 30 | Pillow | 6 No. | 6 No. | -- |

7.5	ARRANGEMENT FOR SOUNDING & PROBING

There is no proper arrangements for sounding & probing in this Division.

7.6	LIGHTING ARRANGEMENT

During peak flood hours, flood fighting operations will be carried out  round the clock. In case of windstorm and rain, lantern and gas lamps fail to work, therefore, to overcome the problem, a reliable generator set with all accessories will be kept on each flood bund, which will facilitate successful operation. For this purpose, sufficient number of generators have already been arranged by this division.

7.7	RATION ARRANGEMENT

Relates to District Administration.

7.8	P.O.L ARRANGEMENT FOR VEHICLE

In case the petrol, oil and lubricants are in short supply on account of disruption of communication elsewhere in the country, the Executive Engineer Incharge will make timely arrangements for having adequate P.O.L reserve at convenient places i.e. petrol pumps at Gujrat, Lalamusa, Jalalpur Jattan, Phalia, Mandi Bahauddin and Qadirabad in consultation with and through an order by the concerned District Coordination Officer.

7.9	TRANSPORTATION

Presently 6 No. 4 X 4 vehicles are available in Gujrat Division UJC. Additional vehicles, if required, will be arranged from other departments.

1 No. jeep towed transport trolly is also available in the Division, which can transport ¼ ton material or manpower to the sites in case of emergency.

XEN/GRT

EARTH MOVING MACHINERY

Agriculture department Gujrat will made against 4 No. Dozers: for District Gujrat & one for District M.B.Din).  At the time of emergency for closing leakage or breaches on flood bunds/spurs.

7.10	LAW AND ORDER

Experience shows that whenever any flood emergency arises, inhabitants of the area try to cut the protection bund at upstream to divert the flood threat from their locality and a law order situation being arised.

In such a situation, it would be necessary for District Administration to provide:

a)        Adequate day & night patrolling to guard against any attempt to stealthily cutting a bund and:

b)      Adequate provision of police force for any open and defiant attempt of breaching the bund at any place.

In these situations, the District Coordination Officer and the District Police Officer of the respective Districts would be expected to promptly provide adequate police force accompanied with a Magistrate on being apprised of the situation by the officers of Irrigation.

7.11	MEDICAL ARRANGEMENT FOR LABOUR

Relates to District Administration.

7.12	LIAISON WITH OTHER DEPARTMENT

The District Coordination Officer & District Police Officer will be contacted in advance and a list of volunteers will be prepared with whom contact will be made during emergency. The list containing the names of volunteers and the village lumberdars made responsible by the Civil Authorities will also be maintained.

7.13	ROLE OF THE ARMY

Pak Army Representative has to inspect the flood infrastructure before flood season. The irrigation department will remove the deficiency pointed out by the army authority before coming flood season. Any emergent situation will be reported by the Irrigation Department to the Pak Army.

7.14   DUTY OF TELEPHONE ATTENDANT

Telephone Attendant will be available round the clock at Divisional Flood Emergency Camp.

XEN/GRT

7.15 WIRELESS ARRANGEMENTS

Speedy means of communications will be adopted through departmental Wireless sets, Canal Telegraph, Messengers & running the jeep drivers to keep a close liaison beginning from that of watchman to the Superintending Engineer. No important event should take more than one hour to be conveyed to the Executive Engineer and two hours to the Superintending Engineer. Mobile wireless sets have already been purchased and given to the Executive Engineer Gujrat (Code ‘AMJAD GUJRAT’) and all the four S.D.Os (Code of S.D.O Gujrat is ‘SADIQ GUJRAT’) & Sub engineers (Code is on their names) and also applied for wireless frequency. At present this office is using frequency of Police. Base sets have also been purchased out of which one has been installed at Canal Telegraph Office Gujrat and Phalia. During flood season, main camp will be established at Spur No. 8 (Right Bank of the River Chenab) for District Gujrat and at RD 40000 of Humber Flood bund for District Mandi Bahauddin as these points are centrally located and are, therefore, most suitable for exercising comprehensive check at all the vulnerable points. The concept of establishment of main camps have already been acceded to by the Army Monitors and District Administration of District Gujrat during flood season, 2000.

Similarly wireless communication has been established in Jhelum Division UJC. Good interaction is available through intercommunication network. The entire “CHAJ DOAB AREA” has been covered with this communication network.

Direct communication with the Flood Information Center Lahore is required to maintain for collection of necessary flood and rainfall data in upper catchments, so that timely intimation be conveyed to the concerned quarters. Similarly one Base station has been installed with the co-ordination of Executive Engineer Murala to receive current information on wireless.

XEN/GRT

CALLING CODE DATA OF IRRIGATION OFFICERS ON WIRELESS

| Sr. No. | Officer/official with designation | Calling Code | Police control/frequency |
| --- | --- | --- | --- |
| 1. | Chief Engineer, Sargodha | Farzand Sargodha | Sargodha |
| 2. | Superintending Engineer, UJC Jhelum | Amjad-1 Jhelum | Mohsin Control/162.975 |
| 3. | Executive Engineer, Gujrat | Amjad Gujrat | Azam Control/162.800 |
| 4. | Executive Engineer, Jhelum | Amjad Jhelum | Mohsin Control/162.975 |
| 5. | Executive Engineer, Murala | Amjad Murala | Nisar Sialkot/162.975 |
| 6. | Sub Divisional Officer, Gujrat | Sadiq Gujrat | Azam Control/162.800 |
| 7. | Sub Divisional Officer, Phalia | Sadiq Phalia | Salah-ud-Din/163.850 |
| 8. | Sub Divisional Officer, Sohawa | Sadiq Sohawa | Salah-ud-Din/163.850 |
| 9. | Sub Divisional Officer, Busal | Sadiq Busal | Salah-ud-Din/163.850 |
| 10. | Sub Engineer, Headquarter | Rashid Mehmood | Azam Control/162.800 |
| 11. | Sub Engineer, Spur 1-5 Leave Reserve-I & II | Muhammad Javed Iqbal/ Ijaz Ahmad UJC | -- |
| 12. | Sub Engineer, Munawar Tawi | Muhammad Javed Iqbal UJC | -- |
| 13. | Sub Engineer, Kalupindi | Mehmood ul Hasson Sherazi | -- |
| 14. | Sub Engineer, Bhikho | Muhammad Rizwan UJC | -- |
| 15. | Sub Engineer, Surkhpur | Muhammad Javed Iqbal UJC | -- |
| 16. | Sub Engineer, Sajjawal | Ijaz Ahmad UJC | -- |
| 17. | Sub Engineer, Shahbaz pur | Ijaz Ahmad UJC | -- |

XEN/GRT

FREQUENCY FOR THE POLICE CHANNELS

| Channel No.1 | 157.975 | Lahore |
| --- | --- | --- |
| Channel No.2 | 162.800 | Azam Control Gujrat |
| Channel No.3 | 162.850 | Zulfiqar, Gujranwala |
| Channel No.4 | 160.775 | Atta Control Chakwal |
| Channel No.5 | 162.900 | Shaheen, Murree |
| Channel No.6 | 162.925 | --- |
| Channel No.7 | 162.950 | -- |
| Channel No.8 | 162.975 | Mohsin, Jhelum |
| Channel No.9 | 160.025 | --- |
| Channel No.10 | 161.400 | Nisar,Sialkot |
| Channel No.11 | 163.850 | Salah-ud-Din, M.B.Din |
| Channel No.12 | 163.875 | Hassan, P.C Rawat |
| Channel No.13 | 163.900 | --- |
| Channel No.14 | 163.925 | --- |
| Channel No.15 | 163.950 | --- |
| Channel No.16 | 163.975 | Faisalabad |

XEN/GRT

CHAPTER – 8

DETAIL OF ENCROACHMENT

There is no encroachment on any flood protection work in Gujrat Division UJC. Some private properties have been constructed by the original owners on the flood banks particularly in Gujrat Sub Division. Department has not acquired the land, hence these constructions does not fall in the category of encroachments.

| Total Encroachment | Removal | Balance | Action to be Taken |
| --- | --- | --- | --- |
| --------------------------Nil-------------------------------- |

XEN/GRT

CHAPTER – 9

DUTY ROSTER/FLOOD FIGHTING PROGRAM

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the areas of District Gujrat & Mandi Bahauddin are in the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

In case of emergency, on the request of Sub Divisional Officers, Gujrat Sub Division and S&I Sub Division, the Executive Engineer Gujrat will order to deploy Sub Divisional Officer Sohawa and Busal along with their subordinate staff to assist/coordinate Sub Divisional Officer Gujrat to cope with the emergency.  Their duty roster will be as under:-

Sub Divisional Officer, Sohawa Canal Sub Division.

All Flood bunds around Gujrat city i.e. small spurs, mole head spurs along Bhimber Nullah, Halsi Nullah, Dawara Nullah etc. Sub Divisional Officer, Sohawa UJC will be mainly responsible for the protection of Gujrat city & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC. He will camp at Canal Colony Gujrat.

Sub Divisional Officer, Busal Canal Sub Division.

In case of simultaneous flood in Chenab and all the hill torrents,  Sub Divisional Officer, Busal along with his subordinate staff will be responsible for Chuknanwali Flood Bund of Gujrat Sub Division & Flood Bund along Chenab upto Qadirabad including Kala Shadian. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC & also camp at Shadiwal Canal Rest House with base station on Police frequency Gujrat.

XEN/GRT

Sub Divisional Officer, Phalia Canal Sub Division.

In case of emergency and high flood, he will be responsible for the watch and ward of Humber Flood Bund & Flood bunds along Right side of River Chenab falling in Phalia Sub Division. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Humber Flood bund at RD 40000 with base station on police frequency Mandi Bahauddin.

Sub Divisional Officer, Gujrat Canal Sub Division.

He will be responsible for monitoring the Lalamusa flood bund, Muskamala flood bund, Bhimber L/R flood bund, Chuknawali flood bund, J-head spur near village Samma Mohla, D/S Alexandra Bridge to Qadirabad river reach & guide wall spur near village kala Shadian. He will be mainly responsible for the protection of Gujrat city & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Musakamala flood bund with base station on Police frequency of Gujrat.

Sub Divisional Officer, Survey & Investigation Sub Division Gujrat

He will be responsible for all the spurs/structures on right bank of River Chenab D/S Marallah to Alexandra Bridge along with solid stone studs near village Changanwali etc. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at spur No. 8 with base station on Police frequency of Gujrat.

Sub Engineer, Chillianwala.

Sub Engineer, Challianwala will be attached at Headquarter Gujrat to attend the emergency if any.

XEN/GRT

Sub Engineer, Chhimon.

Sub Engineer, Chhimon  will be incharge of Gujrat Flood Bund, J-head spur No. 1 & 2 and watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Wasu.

Sub Engineer, Wasu will be incharge of Dawara Nallah Flood Bund, J-head spur No. 6&7 and watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Bhacher.

Sub Engineer, Bhacher will be attached at Headquarter Gujrat to attend the emergency if any .

Sub Engineer, Rukan

Sub Engineer, Rukan will be attached at Headquarter Gujrat to attend the emergency if any .

Sub Engineer, Busal.

Sub Engineer, Busal will be attached at Headquarter Gujrat to attend the emergency if any.

Sub Engineer, Dinga.

Sub Engineer, Dinga will be incharge of Humber Flood Bund and watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Phalia.

Sub Engineer, Phalia Section will be incharge of Guide wall spur Bherowal, Haveli Manik & Noorpur to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

XEN/GRT

Sub Engineer, Bhikho

Sub Engineer, Bhikho Section will be incharge of Farrukhpur Flood Bund, J-head spur Chakori and Guide wall to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Gujrat

Sub Engineer, Gujrat section will be incharge of Lalamusa Flood Bund, Lalamusa Extension flood bund & Musakamala Flood bund to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Kalupindi.

Sub Engineer, Kalupindi Section will be incharge of Chuknawali Flood Bund, Kala Shadian,. Bari & Randiali Guide walls to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Chuknawali

Sub Engineer, Chuknawali will be incharge of Bhimber left & right Flood Bund, J-head spur Samma Mohla to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Sajjawal

Sub Engineer, Sajjawal Section will be incharge of Guide wall No. 9, 10, 11 and 3 No. Guide walls on River Munawar Tawi to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Shahbazpur

Sub Engineer, Shahbazpur Section will be incharge of J-head spur & Guide walls No. 6,7 & 8 to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Leave Reserve-I

Sub Engineer, Leave Reserve-I will be attached at Headquarter Gujrat to attend the emergency if any.

Sub Engineer, Leave Reserve-II

Sub Engineer, Leave Reserve-II will be incharge of J-hear spur No. 3,4 &5 to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

XEN/GRT

CHAPTER – 10

EMERGENCY TELEPHONE NUMBERS

| Sr. # | Designation | Office | Residence |
| --- | --- | --- | --- |
| i) | IRRIGATION DEPARTMENT IRRIGATION & POWER SECRETARIAT LAHORE |
| 1. | Minister, Irrigation | 042-99212809-10 |  |
| 2. | Secretary, I&P Department Lahore | 042-99212117-18 | 042-35731116 |
| 3. | Addl. Secretary (Admn.) Lahore. | 042-99212119 | -- |
| 4. | Addl. Secretary (OP) Lahore. | 042-99212129 | 042-5224359 |
| 5. | Addl. Secretary (Technical) Lahore. | 042-99212123 | 042-6818219 |
| 6. | Deputy Secretary (Admn.) Lahore. | 042-99212126 | 042-570392 |
| 7. | Deputy Secretary (OP) Lahore. | 042-99212127 | 042-7848174 |
| 8. | Deputy Secretary (Development) Lahore. | 042-99212128 | 042-7586597 |
| 9. | Section Officer (Flood) Lahore. | 042-99212134 | 042-7581015 |
| ii) | SARGODHA IRRIGATION ZONE |
| 1. | Chief Engineer, Irrigation Sargodha | 048-9230445 | 048-9230451 |
| 2. | Executive Engineer (OP) Sargodha. | 048-9230446 | 048-729067 |
| 3. | Superintending Engineer, UJC Jhelum. | 0544-9270332 | 0544-9270332 |
| 4. | Telegraph Office UJC. | 0544-9270330 | -- |
| 5. | Executive Engineer, Jhelum Division UJC. | 0544-9270331 | 0544-9270331 |
| 6. | Executive Engineer, Gujrat Division UJC. | 053-9260398 Fax -9260396 | 053-9260398 |
| 7. | Sub Divisional Officer Gujrat. | 053-9260395 | 053-9260395 |
| 8. | Sub Divisional Officer Sohawa M.B.Din. | 0546-506562 | 0546-506562 |
| 9. | Sub Divisional Officer Busal M.B.Din. | 0546-506561 | 0546-506561 |
| 10. | Sub Divisional Officer Phalia. | 0546-596811 | 0546-596811 |
| 11. | Sub Divisional Officer S&I Gujrat | 053-9260397 | 053-9260397 |
| 12. | Telegraph office Gujrat (Flood Emergency Office) | 053-9260395 |  |

XEN/GRT

| iii) | HEADWORKS DIVISIONS |
| --- | --- |
| 1. | Executive Engineer, Murala. | 052-3502102 | -- |
| 2. | Executive Engineer, Khanki. | 055-6605255 | -- |
| 3. | Executive Engineer, Qadirabad. | 054-7550198 | 054-7424272 |
| iv) | DISTRICT ADMINISTRATION GUJRAT |
| 1. | District Administrator, Gujrat. | 053-9260071-72 | 053-511109 |
| 2. | District Coordination Officer, Gujrat. | 053-9260010 | 053-9260011 |
| 3. | District Police Officer, Gujrat. | 053/9260026-30-31 | 053-9260027 |
| 4. | E.D.O (Revenue), Gujrat. | 053-9260066 | 053-9230077 |
| 5. | District Officer (Revenue), Gujrat. | 053-9260061 | 053-9260062 |
| 6. | District Flood Control Officer, Gujrat. | 053-9260066 | -- |
| 7. | D.D.O (Revenue) Gujrat. | 053-9260063 | 053-9260064 |
| 8. | D.D.O (Revenue) Kharian. | 053-37532200 | -- |
| 9. | D.D.O (Revenue) Sarai-Alamgir. | 053-37651812 | 0544-614703 |
| 10. | S.D.P.O Sadar Gujrat. | 053-9260046 | -- |
| 11. | D.S.P Kharian. | 053-37511950 | -- |
| 12. | D.S.P Sara-i-Alamgir. | 053-37511950 | -- |
| v) | DISTRICT ADMINISTRATION MANDI BAHAUDDIN. |
| 1. | District Administrator, Mandi Bahauddin. | 0546-520900 | 0546-299009/ 599002 |
| 2. | District Coordination Officer, M.B.Din. | 0546-504220 | 0546-504200 |
| 3. | District Police Officer, M.B.Din. | 0546-502324 | -- |
| 4. | E.D.O (Revenue) M.B.Din. | 0546-501825 | 0546-506340 |
| 5. | D.D.O (Revenue) Phalia. | 0546-596460 | 0546-596690 |
| 6. | D.D.O (Revenue) M.B.Din. | 0546-506488 | 0546-505145 |
| 7. | D.D.O (Revenue) Malakwal. | 0546-591276 | 0546-591368 |

PAKISTAN BROAD CASTING CORPORATION

NEWS ORGANIZATION LAHORE

| Sr. No. | Designation | Office | Residence |
| --- | --- | --- | --- |
| 1. | Deputy Controller Incharge News Editor | 042-99200674 | 042-5862694 |
| 2. | Deputy Controller News | 042-99200681-4 | Ext. |
| 3. | Radio F.M 105 Gujrat. | 053-3520320 & 3520785 |  |
| 4. | Radio F.M 98 M.B.Din | 0546-509798 |  |

XEN/GRT

PAKISTAN TELEVISION CORPORATION LAHORE

| Sr. No. | Designation | Office | Residence |
| --- | --- | --- | --- |
| 1. | News Room | Direct= 042-99200617 042-99200618 | -- |
|  |  | Exchange= 042-99200651-59 | -- |
|  |  | Fax = 042-99200620 |  |

FLOOD CONTROL CENTER PUNJAB

| Sr. No. | Designation | Office | Residence |
| --- | --- | --- | --- |
| 1. | Flood warning Center, 46-Jail Road Lahore. | 042-7572091-93 | Fax 042-7572092 |
| 2. | Flood Cell, I&P Secretariat Lahore. | 042-99212134 | Fax 042-99212116 |
| 3. | Police Wireless Control, Jail Road Lahore. | 042-7572090 | -- |
| 4. | Flood Emergency Board of Rev. Punjab. | 042-99204408 | Fax-042-99204405 |
| 5. | National Flood Forecasting Bureau Lahore. | 042-7586479 | 042-7562874 |
| 6. | Senior Meteorologist | 042-7587625 7572092 | -- |
| 7. | Chief Engineer (D&F) Zone Lahore | 042/352913040 | 0300/8654409 |
|  | Fax | 042/35862081 |  |
| 8. | Director Flood (D&F) Zone Lahore | 042/99231614 | 0345/8451936 |
| 9. | Flood Cell I & PSecretariat Lahore | 042/99212134 |  |
| 10. | National flood forecasting Bureau Lahore | 042/99200208 | 042/7583747 |
| 11. | Senior Meteorologist | 042/99200144 |  |

MILITARY ENGINEERS TELEPHONE Nos.

| 1. | Headquarters Engineers, 30-Corps Gujranwala Cantonment. | 0432-269/2353 | -- |
| --- | --- | --- | --- |
| 2. | 24-Engineers Battalion, Sialkot Cantonment Sialkot. | 0432-571/5186 | -- |
| 3. | Headquarters Engineers 1-Corps, Kharian Cantonment. | 05771-095/2364 | -- |
| 4. | 15-Div. Sialkot | 0432-571/3223 & 3225 |  |
| 5. | 10-Brigade Sialkot | 0432-571/4202 |  |

XEN/GRT

CHAPTER – 11

STANDARD OPERATING PROCEDURE (SOP) FOR BREACHING SECTIONS

11.1	HISTORY OF THE BREACING SECTION

There is no breaching section on any flood protection work in Gujrat Division UJC.

  - LOCATION, DESIGN, QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATION

---------- NIL ----------

  - ARRANGEMENT OF EXPLOSIVES AND SECURITY OF EXPLOSIVE STORES.						__

---------- NIL ----------

  - LIST OF THE SECURITY STAFF ALONGWITH DETAIL OF THEIR TRAINING ETC.						__

---------- NIL ----------

  - DETAIL OF MECHANICAL MEANS AS A STANDBY ARRANGEMENTS IN CASE OF DETONATION FAILURE.	__

---------- NIL ----------

  - DUTY ROSTER IN CASE OF CRITICAL SITUATION.

---------- NIL ----------

  - BREACHING COMMITTEE WITH THEIR ACTION PLAN

---------- NIL ----------

  - LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN CASE OF BREACH.

---------- NIL ----------

  - ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENTS							__

---------- NIL ----------

XEN/GRT

  - DETAILS OF COORDINATION WITH CIVIL/ARMY AUTHORITIES

---------- NIL ----------

  - PARALLEL COMMUNICATION ARRANGEMENTS

---------- NIL ----------

  - INDEX PLAN                      Attached

Superintending Engineer					Executive Engineer

Upper Jhelum Canal Circle					Gujrat Division UJC

Jhelum								Gujrat

Chief Engineer

Irrigation Sargodha Zone

Sargodha

PART – B

CHAPTER – 12

VULNERABLE SITES ON FLOOD BUNDS/STRUCTURES

12.1	APPREHENDED BRACHES IN FLOOD BUNDS/STRUCTURES

For the following sites of flood bunds, there is apprehension of any mishap due to floods in River Chenab & Nallahs.

1.	Lalamusa flood bund along right bank of Bhimbr Nallah between RD             9000-10000(site 1).

2.	Bhimber Right flood bund along left bank of Bhimber Nallah between RD 3000-4000 & 9000-10000(site 2).

3.	Farrukhpur flood bund along left bank of Budi Nallah Drain RD 14000-17000, 21000-22000 & 31000-32000(site 3).

4.	Near village Bhelolpur on right bank of River Chenab (site 4)

5.	Near village Shahbazpur on right bank of River Chenab (site 5)

6.	Spur No. 2 on right bank of River Chenab.(site 6)

Deployment of Contractor Machinery at Vulnerable  Sites.

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley

It is further added that there is no vulnerable reach along Bhimber left bund, Gujrat flood bund, Musa Kamala flood bund, Chukananwali flood bund and Humber flood bund.

12.2	Operation of Breaching Sections.

No Breaching section exists under the jurisdiction of Gujrat Division UJC.

12.3	Breaches due to rising of flood water, deterioration of flood bunds etc.

No such occurrence

XEN/GRT

CHAPTER – 13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES SITE No. I

1.	Lalamusa flood bund along right bank of Bhimbr Nallah between RD   9000-10000.

13.1	Plan showing route of Flood Water coming out of the breach supported with levels.

Plan attached as Annex-A

13.2	Detail of villages abadies likely to be affected and this should also be shown on the plan.

Makan, Lala Musa, Mir Dad, Miana kot,

13.3	Strategy and action taken be explained in detail. This may include:

STRATEGY  OF LALAMUSA FLOOD BUND

The said bund falls on right edge of Bhimber Nallah having a length of 16.25 Miles. During the rainy season in the catchment area, the rain water received in the Bhimber Nallah with high velocity. If any damage occurs to Lalamusa Flood Bund, the flood water will inundate the villages as well as G.T Road and spread on the agricultural land and will damage the various corps i.e Rice, Fodder, Mize etc. In case of emergency, situation will be controlled through tree launching and dumping of stone along with Gunny Bags. Plan showing root of flood water coming out of the breach supported with level of vulnerable site of Lala Musa Flood Bund as mentioned at para No.12.1.

13.3.1 – Arrangements

The arrangements are as under:-

13.3.2 – Establishment of Flood Fighting Camps

i)	Lalamusa flood bund			=	RD 9000

XEN/GRT

WATCHING ESTABLISHMENT

| Sr. No. | Name of flood bunds | Camp RD | Beldar | Mate | Gauge Reader | Chowkidar |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Lalamusa flood bund. | 9000 | 5 | 1 | -- | 1 |

13.3.3 – Duties of Officers/Officials and their camp sites.

| CAMP No. | OFFICERS (Name,Designation& Mobile No.) | OFFICIALS (Name, Designation & Mobile No.) |
| --- | --- | --- |
| 01 | Ali Raza Sub Divisional Officer Gujrat (03092758455) | Rashid Mehmood , (Sub Engineer Gujrat Section (03238008001) |

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the areas of District Gujrat & Mandi Bahauddin are under the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

Sub Divisional Officer, Gujrat Canal Sub Division.

He will be responsible for monitoring the Lalamusa flood bund, Muskamala flood bund, Bhimber L/R flood bund, Chuknawali flood bund,  J-head spur near village Samma Mohla, D/S Alexandra bridge to Qadirabad river reach & gudie wall spur near village kala Shadian. He will be mainly responsible for the protection of Gujrat city & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Musakamala flood bund with base station on Police frequency of Gujrat.

Sub Engineer, Surkhpur

Sub Engineer, Surkhpur Section will be Incharge of Lalamusa Flood Bund to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

In case of emergency, the sister Division i.e Jhelum Division UJC Jhelum will help this Division.

13.3.4 – Departmental machinery available.

No Departmental machinery is available in this Division.

XEN/GRT

13.3.5 – Machinery available from Private Source

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley

13.3.6 – Flood Fighting Material required

The detail is prescribed at page No.60.

13.3.7- Flood Fighting Material available.

The detail is prescribed at page No. 60.

13.4	Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, Canals and drainage network.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

XEN/GRT

FLOOD FIGHTING MATERIAL REQUIRED / AVAILABLE

| Sr. No. | Item | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin | The balance Flood Fighting material will be purchased before flood season 2021 |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |  |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |  |
| 4 | Ballies | 50 No. | -- | 50 No. |  |
| 5 | Service cable | 1 Coil |  | 1 Coil |  |
| 6 | Wicks | 6 No |  | 6 No. |  |
| 7 | Sprit | 1 Bottles | -- | 1 Bottles |  |
| 8 | Mach boxes | 1 Packet | -- | 1 Packet |  |
| 9 | Petrol | 50 Ltrs. | -- | 50 Ltrs. |  |
| 10 | M. Oil | 10 Ltrs. | -- | 10 Ltrs. |  |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |  |
| 12 | Spare chargeable cells AA size | 2 No. |  | 2 No. |  |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |  |
| 14 | Lantern | 10 No. | 10 No. | -- | Available in Canal Colony Gujrat |
| 15 | Chimneys for lanterns | 7 No. | 7 No. | -- |  |
| 16 | Torches with cells | 6 No. | 6 No. | -- |  |
| 17 | Axes | 5No. | 5No. | -- |  |
| 18 | Kassies with handles | 10 No. | 10 No. | -- |  |
| 19 | Baskets | 15 No. | 15 No. | -- |  |
| 20 | Handles for kassies | 5 No. | 5 No. | -- |  |
| 21 | Gas lamps | 1 No. | 1 No. | -- |  |
| 22 | G.I. wire | 100 kg. | 100 kg. | -- |  |
| 23 | Generator set | 1 No. | 1 No. | -- |  |
| 24 | Service cable | 28 ft. | 28 ft. | -- |  |
| 25 | Wicks | 30 No. | 30 No. | -- |  |
| 26 | Sprit | 2 Bottles | 2 Bottles | -- |  |
| 27 | Match box | 1 dozen | 1 dozen | -- |  |
| 28 | Wooden mallet | 2 No. | 2 No. | -- |  |
| 29 | Search light | 1 No. | 1 No. | -- |  |
| 30 | Tents | 1 No. | 1 No. | -- |  |
| 31 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 32 | Spare chargeable cells AA size | 2 No. | 2 No. | -- |  |
| 33 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | 1 No. | -- |  |

XEN/GRT

CHAPTER – 13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES SITE No. 2

2.	Bhimber Right flood bund along left bank of Bhimber Nallah between RD 3000-4000 & 9000-10000.

13.1	Plan showing route of Flood Water coming out of the breach supported with levels.

Plan attached as Annex-B.

13.2	Detail of villages abadies likely to be affected and this should also be shown on the plan.

Vanis, Dhul Khurd, Changanwali, Mulo.

13.3	Strategy and action taken be explained in detail. This may include:

STRATEGY OF BHIMBER RIGHT FLOOD BUND

The said bund falls on right bank of Bhimder Nallah having a length of 4.31 Miles. If any damage occurs to this bund during the flood, adjoining village such as Dhool, Vanse, Changanwali, Melo, Qasibbad and khokhra will be affected and flood water will entere D/S of the Gujrat – Sargodha Road by crossing these villages and back fallen in river. In case of emergency situation will be controlled through tree launching, Gunny Bags and dumping of stone through departmental labour, work charge labour and by the motivation of public volunteers. Plan showing root of flood water coming out of the breach supported with level of vulnerable site of Bhimber right flood bund as mention at para No.12.2.

13.3.1 – Arrangements

The arrangements are as under:-

13.3.2 – Establishment of Flood Fighting Camps

i)	Bhimber right flood bund		=	RD 3000, RD 9000

WATCHING ESTABLISHMENT

| Sr. No. | Name of flood bunds | Camp RD | Beldar | Mate | Gauge Reader | Chowkidar |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Bhimber right flood bund. | 3000 | 5 | 1 | -- | 1 |
|  | Bhimber right flood bund. | 9000 | 5 | 1 | -- | 1 |
|  | Total |  | 10 | 2 | -- | 2 |

XEN/GRT

13.3.3 – Duties of Officers/Officials and their camp sites.

| Camp No. | Location | OFFICERS (Name,Designation & Mobile No.) | OFFICIALS (Name,Designation & Mobile No.) |
| --- | --- | --- | --- |
| 02 | Bhimber right flood bund RD 3000. | Ali Raza Sub Divisional Officer Gujrat (03092758455) | Rashid Mehmood , (Sub Engineer Gujrat Section (03238008001) |
|  | Bhimber right flood bund RD 9000. | Ali Raza Sub Divisional Officer Gujrat (03092758455) | Rashid Mehmood , (Sub Engineer Gujrat Section (03238008001) |

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the  areas of District Gujrat & Mandi Bahauddin are under the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

Sub Divisional Officer, Gujrat Canal Sub Division.

He will be responsible for monitoring the Lalamusa flood bund, Muskamala flood bund, Bhimber L/R flood bund, Chuknawali flood bund,  J-head spur near village Samma Mohla, D/S Alexandra bridge to Qadirabad river reach & gudie wall spur near village kala Shadian. He will be mainly responsible for the protection of Gujrat city & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Musakamala flood bund with base station on Police frequency of Gujrat.

Sub Engineer, Chakori

Sub Engineer, Chakori will be the Incharge of Bhimber right flood bund to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

13.3.4 – Departmental machinery available.

No departmental machinery is available in this Division.

13.3.5 – Machinery available from Private Source

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley

XEN/GRT

13.3.6 – Flood Fighting Material required

The detail is prescribed at page No.64.

13.3.7- Flood Fighting Material available.

The detail is prescribed at page No.64.

13.4 -- Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, Canals and drainage network.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

XEN/GRT

FLOOD FIGHTING MATERIAL REQUIRED / AVAILABLE

| Sr. No. | Item | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin | The balance Flood Fighting material will be purchased before flood season 2021 |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |  |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |  |
| 4 | Ballies | 50 No. | -- | 50 No. |  |
| 5 | Service cable | 1 Coil |  | 1 Coil |  |
| 6 | Wicks | 6 No |  | 6 No. |  |
| 7 | Sprit | 1 Bottles | -- | 1 Bottles |  |
| 8 | Mach boxes | 1 Packet | -- | 1 Packet |  |
| 9 | Petrol | 50 Ltrs. | -- | 50 Ltrs. |  |
| 10 | M. Oil | 10 Ltrs. | -- | 10 Ltrs. |  |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |  |
| 12 | Spare chargeable cells AA size | 2 No. |  | 2 No. |  |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |  |
| 14 | Lantern | 10 No. | 10 No. | -- | Available in Canal Colony Gujrat |
| 15 | Chimneys for lanterns | 7 No. | 7 No. | -- |  |
| 16 | Torches with cells | 6 No. | 6 No. | -- |  |
| 17 | Axes | 5No. | 5No. | -- |  |
| 18 | Kassies with handles | 10 No. | 10 No. | -- |  |
| 19 | Baskets | 15 No. | 15 No. | -- |  |
| 20 | Handles for kassies | 5 No. | 5 No. | -- |  |
| 21 | Gas lamps | 1 No. | 1 No. | -- |  |
| 22 | G.I. wire | 100 kg. | 100 kg. | -- |  |
| 23 | Generator set | 1 No. | 1 No. | -- |  |
| 24 | Service cable | 28 ft. | 28 ft. | -- |  |
| 25 | Wicks | 30 No. | 30 No. | -- |  |
| 26 | Sprit | 2 Bottles | 2 Bottles | -- |  |
| 27 | Match box | 1 dozen | 1 dozen | -- |  |
| 28 | Wooden mallet | 2 No. | 2 No. | -- |  |
| 29 | Search light | 1 No. | 1 No. | -- |  |
| 30 | Tents | 1 No. | 1 No. | -- |  |
| 31 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 32 | Spare chargeable cells AA size | 2 No. | 2 No. | -- |  |
| 33 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | 1 No. | -- |  |

XEN/GRT

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES SITE No.3

3.	Farrukhpur flood bund along left bank of Budhi Nallah Drain RD 14000-17000, 21000-22000 & 31000-32000.

13.1	Plan showing route of Flood Water coming out of the breach supported with levels.

Plan attached as Annex-C.

13.2	Detail of villages abadies likely to be affected and this should also be shown on the plan.

Village Farrukhpur, Village Noshara, Village Thatha Shah Muhammad, Village Mailu, Village Alan, Qadirabad, Channi.

13.3	Strategy and action taken be explained in detail. This may include:

STRATEGY OF FARRUKHPUR FLOOD BUND

The said bund falls on the right bank of Budi Nallah having a length of 6.80 Miles. The condition of this bund at RD 13-15, 31-32 and 21-28 is very much critical. During the flood water spills out from the River Chenab and enters the Budi Nallah and runs parallel in the toe of bund causing damage to Farrukhpur Flood Bund. If any damage occurs to this bund during the flood, water will enter the adjoining abadies i.e. Qadirabad city, Alan, Thathi Shah Muhammad, Noshera, Farrukhpur, Melu and Watto and then will enter again the River Chenab opposite village Farrukhpur. In case of emergency, situation will be controlled through tree launching, Gunny Bags and departmental labour, work charge labour and by the motivation of public volunteers. Plan showing root of flood water coming out of the breach supported with level of vulnerable site of Farrukhpur flood bund as mention at para No.12.3.

It is further added that there is no vulnerable reaches along Bhimber left bund, Gurat flood bund, Musa Kamala flood bund, Chukananwali flood bund and Humber flood bund.

XEN/GRT

13.3.1 – Arrangements

The arrangements are as under:-

13.3.2 – Establishment of Flood Fighting Camps

Farrukhpur flood bund		=	RD 14000, RD 21000 & 						   	RD 31000

WATCHING ESTABLISHMENT

| Sr. No. | Name of flood bunds | Camp RD | Beldar | Mate | Gauge Reader | Chowkidar |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Farrukhpur flood bund | 14000 | 5 | 1 | -- | 1 |
|  | Farrukhpur flood bund | 21000 | 5 | 1 | -- | 1 |
|  | Farrukhpur flood bund | 31000 | 5 | 1 | -- | 1 |
|  | Total |  | 15 | 3 | -- | 3 |

13.3.3 – Duties of Officers/Officials and their camp sites.

| CAMP No. | OFFICERS (Name,Designation& Mobile No.) | OFFICIALS (Name,Designation& Mobile No.) |
| --- | --- | --- |
| 03 | Allah Bakhish Sub Divisional Officer Phalia (0334-4913412) | Muhammad Akmal (Sub Engineer Bheikho Section 0300-7746292) |

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the  areas of District Gujrat & Mandi Bahauddin are under the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

Sub Divisional Officer, Phalia Canal Sub Division.

In case of emergency and high flood, he will be responsible for the watch and ward of Humber Flood Bund, Farrukhpur Flood bund and river training works along Right side of River Chenab falls in Phalia Sub Division. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Humber Flood bund at RD 40000 with base station on police frequency Mandi Bahauddin.

Sub Engineer, Kadher

Sub Engineer, kadher will be Incharge of Farrukhpur Flood bund to watch all activities and remain present round the clock with a gang of labour to look after flood infrastructures.

XEN/GRT

13.3.4 – Departmental machinery available.

No departmental machinery is available in this Division.

13.3.5 – Machinery available from Private Source

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley

13.3.6 – Flood Fighting Material required

The detail is prescribed at page No. 68.

13.3.7- Flood Fighting Material available.

The detail is prescribed at page No. 68.

13.4	Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, Canals and drainage network.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

XEN/GRT

FLOOD FIGHTING MATERIAL REQUIRED / AVAILABLE

| Sr. No. | Item | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin | The balance Flood Fighting material will be purchased before flood season 2021 |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |  |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |  |
| 4 | Ballies | 50 No. | -- | 50 No. |  |
| 5 | Service cable | 1 Coil |  | 1 Coil |  |
| 6 | Wicks | 6 No |  | 6 No. |  |
| 7 | Sprit | 1 Bottles | -- | 1 Bottles |  |
| 8 | Mach boxes | 1 Packet | -- | 1 Packet |  |
| 9 | Petrol | 50 Ltrs. | -- | 50 Ltrs. |  |
| 10 | M. Oil | 10 Ltrs. | -- | 10 Ltrs. |  |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |  |
| 12 | Spare chargeable cells AA size | 2 No. |  | 2 No. |  |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |  |
| 14 | Lantern | 10 No. | 10 No. | -- | Available in Canal Colony Duggal (Phalia) |
| 15 | Chimneys for lanterns | 7 No. | 7 No. | -- |  |
| 16 | Torches with cells | 6 No. | 6 No. | -- |  |
| 17 | Axes | 5No. | 5No. | -- |  |
| 18 | Kassies with handles | 10 No. | 10 No. | -- |  |
| 19 | Baskets | 15 No. | 15 No. | -- |  |
| 20 | Handles for kassies | 5 No. | 5 No. | -- |  |
| 21 | Gas lamps | 1 No. | 1 No. | -- |  |
| 22 | G.I. wire | 100 kg. | 100 kg. | -- |  |
| 23 | Generator set | 1 No. | 1 No. | -- |  |
| 24 | Service cable | 28 ft. | 28 ft. | -- |  |
| 25 | Wicks | 30 No. | 30 No. | -- |  |
| 26 | Sprit | 2 Bottles | 2 Bottles | -- |  |
| 27 | Match box | 1 dozen | 1 dozen | -- |  |
| 28 | Wooden mallet | 2 No. | 2 No. | -- |  |
| 29 | Search light | 1 No. | 1 No. | -- |  |
| 30 | Tents | 1 No. | 1 No. | -- |  |
| 31 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 32 | Spare chargeable cells AA size | 2 No. | 2 No. | -- |  |
| 33 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | 1 No. | -- |  |

XEN/GRT

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES SITE No.4

4.	Near village Bhelolpur on right bank of River Chenab

13.1	Plan showing route of Flood Water coming out of the breach supported with levels.

Plan attached as Annex-D.

13.2	Detail of villages abadies likely to be affected and this should also be shown on the plan.

Village Bhelolpur and deras.

13.3	Strategy and action taken be explained in detail. This may include:

STRATEGY OF INVERTED HOCKEY STUDS NEAR VILLAGE BHELOLPUR

The said studs fall on the right bank of River Chenab downstream Marala Barrage. The condition of these studs is very much critical. During the flood water spills out from the River Chenab and enters the village abadies of Bhelolpur and damaged the agricultural land. In case of emergency, situation will be controlled through tree launching, Gunny Bags and departmental labour, work charge labour and by the motivation of public volunteers. Plan showing root of flood water coming out of the breach supported with level of vulnerable site of Near village Bhelolpur on right bank of River Chenab as mention at para No.12.3.

13.3.1 – Arrangements

The arrangements are as under:-

13.3.2 – Establishment of Flood Fighting Camps

Inverted Hockey Studs =	Top of Stud

WATCHING ESTABLISHMENT

| Sr. No. | Name of flood Ifrastructures | Camp RD | Beldar | Mate | Gauge Reader | Chowkidar |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Inverted Hockey Studs | Top of stud | 5 | 1 | -- | 1 |
|  | Total |  | 5 | 1 | -- | 1 |

13.3.3 – Duties of Officers/Officials and their camp sites.

| CAMP No. | OFFICERS (Name, Designation& Mobile No.) | OFFICIALS (Name, Designation& Mobile No.) |
| --- | --- | --- |
| 01 | Faisal Nadeem Sub Divisional Officer S&I Sub Division UJC (0333-7483658) | Muhammad Javed Iqbal (Sub Engineer S&I (03027759148) |

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the  areas of District Gujrat & Mandi Bahauddin are under the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

Sub Divisional Officer, S&I Sub Division UJC.

In case of emergency and high flood, he will be responsible for the watch and ward of Halsi Nallah Dawara Nallah and river training works along Right side of River Chenab falls in S&I Sub Division UJC Gujrat. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Inverted Hockey Studs near Village Bhelolpur with base station on police frequency Gujrat.

Sub Engineer, S&I

Sub Engineer, s&i will be Incharge of Inverted Hockey Studs to watch all activities and remain present round the clock with a gang of labour to look after flood infrastructures.

13.3.4 – Departmental machinery available.

No departmental machinery is available in this Division.

13.3.5 – Machinery available from Private Source

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley						 XEN/GRT

13.3.6 – Flood Fighting Material required

The detail is prescribed at page No. 72.

13.3.7- Flood Fighting Material available.

The detail is prescribed at page No. 72.

13.4	Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, Canals and drainage network.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

XEN/GRT

FLOOD FIGHTING MATERIAL REQUIRED / AVAILABLE

| Sr. No. | Item | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin | The balance Flood Fighting material will be purchased before flood season 2021 |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |  |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |  |
| 4 | Ballies | 50 No. | -- | 50 No. |  |
| 5 | Service cable | 1 Coil |  | 1 Coil |  |
| 6 | Wicks | 6 No |  | 6 No. |  |
| 7 | Sprit | 1 Bottles | -- | 1 Bottles |  |
| 8 | Mach boxes | 1 Packet | -- | 1 Packet |  |
| 9 | Petrol | 50 Ltrs. | -- | 50 Ltrs. |  |
| 10 | M. Oil | 10 Ltrs. | -- | 10 Ltrs. |  |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |  |
| 12 | Spare chargeable cells AA size | 2 No. |  | 2 No. |  |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |  |
| 14 | Lantern | 10 No. | 10 No. | -- | Available in Canal Colony Gujrat |
| 15 | Chimneys for lanterns | 7 No. | 7 No. | -- |  |
| 16 | Torches with cells | 6 No. | 6 No. | -- |  |
| 17 | Axes | 5No. | 5No. | -- |  |
| 18 | Kassies with handles | 10 No. | 10 No. | -- |  |
| 19 | Baskets | 15 No. | 15 No. | -- |  |
| 20 | Handles for kassies | 5 No. | 5 No. | -- |  |
| 21 | Gas lamps | 1 No. | 1 No. | -- |  |
| 22 | G.I. wire | 100 kg. | 100 kg. | -- |  |
| 23 | Generator set | 1 No. | 1 No. | -- |  |
| 24 | Service cable | 28 ft. | 28 ft. | -- |  |
| 25 | Wicks | 30 No. | 30 No. | -- |  |
| 26 | Sprit | 2 Bottles | 2 Bottles | -- |  |
| 27 | Match box | 1 dozen | 1 dozen | -- |  |
| 28 | Wooden mallet | 2 No. | 2 No. | -- |  |
| 29 | Search light | 1 No. | 1 No. | -- |  |
| 30 | Tents | 1 No. | 1 No. | -- |  |
| 31 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 32 | Spare chargeable cells AA size | 2 No. | 2 No. | -- |  |
| 33 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | 1 No. | -- |  |

XEN/GRT

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES SITE No.5

5.	Near village Shahbazpur on right bank of River Chenab

13.1	Plan showing route of Flood Water coming out of the breach supported with levels.

Plan attached as Annex-E.

13.2	Detail of villages abadies likely to be affected and this should also be shown on the plan.

Village Shahbazpur, Changanwali and Daras.

13.3	Strategy and action taken be explained in detail. This may include:

Near village Shahbazpur on right bank of River Chenab

The Guide Bank Spur No. 8 near village Shahbazpur fall on the right bank of River Chenab downstream Marala Barrage. The condition of this Guide bank  is very much critical. During the flood water spills out from the River Chenab and enters the village abadies of Shahbazpur and damaged the agricultural land. In case of emergency, situation will be controlled through tree launching, Gunny Bags and departmental labour, work charge labour and by the motivation of public volunteers. Plan showing root of flood water coming out of the breach supported with level of vulnerable site of Near village Shahbazpur on right bank of River Chenab as mention at para No.12.3.

13.3.1 – Arrangements

The arrangements are as under:-

13.3.2 – Establishment of Flood Fighting Camps

iii)	Guide Bank Spur near village Shahbazpur    =   Top of Guide bank

WATCHING ESTABLISHMENT

| Sr. No. | Name of flood bunds | Camp RD | Beldar | Mate | Gauge Reader | Chowkidar |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Guide Bank Spur No. 8 near village Shahbazpur | Top of Spur | 5 | 1 | -- | 1 |
|  | Total |  | 5 | 1 | -- | 1 |

XEN/GRT

13.3.3 – Duties of Officers/Officials and their camp sites.

| CAMP No. | OFFICERS (Name, Designation& Mobile No.) | OFFICIALS (Name, Designation & Mobile No.) |
| --- | --- | --- |
| 01 | Faisal Nadeem Sub Divisional Officer S&I Sub Division UJC (0333-7483658) | Muhammad Javed Iqbal (Sub Engineer S&I (03027759148) |

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the  areas of District Gujrat & Mandi Bahauddin are under the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

Sub Divisional Officer, S&I Sub Division UJC.

In case of emergency and high flood, he will be responsible for the watch and ward of Halsi Nallah Dawara Nallah and river training works along Right side of River Chenab falls in S&I Sub Division UJC Gujrat. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at Humber Flood bund at RD 40000 with base station on police frequency Gujrat.

Sub Engineer, S&I

Sub Engineer, kadher will be Incharge of Farrukhpur Flood bund to watch all activities and remain present round the clock with a gang of labour to look after flood infrastructures.

13.3.4 – Departmental machinery available.

No departmental machinery is available in this Division.

13.3.5 – Machinery available from Private Source

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley 						XEN / GRT

13.3.6 – Flood Fighting Material required

The detail is prescribed at page No. 76.

13.3.7- Flood Fighting Material available.

The detail is prescribed at page No. 76.

13.4	Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, Canals and drainage network.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

XEN/GRT

FLOOD FIGHTING MATERIAL REQUIRED / AVAILABLE

| Sr. No. | Item | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin | The balance Flood Fighting material will be purchased before flood season 2021 |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |  |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |  |
| 4 | Ballies | 50 No. | -- | 50 No. |  |
| 5 | Service cable | 1 Coil |  | 1 Coil |  |
| 6 | Wicks | 6 No |  | 6 No. |  |
| 7 | Sprit | 1 Bottles | -- | 1 Bottles |  |
| 8 | Mach boxes | 1 Packet | -- | 1 Packet |  |
| 9 | Petrol | 50 Ltrs. | -- | 50 Ltrs. |  |
| 10 | M. Oil | 10 Ltrs. | -- | 10 Ltrs. |  |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |  |
| 12 | Spare chargeable cells AA size | 2 No. |  | 2 No. |  |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |  |
| 14 | Lantern | 10 No. | 10 No. | -- | Available in Canal Colony Gujrat |
| 15 | Chimneys for lanterns | 7 No. | 7 No. | -- |  |
| 16 | Torches with cells | 6 No. | 6 No. | -- |  |
| 17 | Axes | 5No. | 5No. | -- |  |
| 18 | Kassies with handles | 10 No. | 10 No. | -- |  |
| 19 | Baskets | 15 No. | 15 No. | -- |  |
| 20 | Handles for kassies | 5 No. | 5 No. | -- |  |
| 21 | Gas lamps | 1 No. | 1 No. | -- |  |
| 22 | G.I. wire | 100 kg. | 100 kg. | -- |  |
| 23 | Generator set | 1 No. | 1 No. | -- |  |
| 24 | Service cable | 28 ft. | 28 ft. | -- |  |
| 25 | Wicks | 30 No. | 30 No. | -- |  |
| 26 | Sprit | 2 Bottles | 2 Bottles | -- |  |
| 27 | Match box | 1 dozen | 1 dozen | -- |  |
| 28 | Wooden mallet | 2 No. | 2 No. | -- |  |
| 29 | Search light | 1 No. | 1 No. | -- |  |
| 30 | Tents | 1 No. | 1 No. | -- |  |
| 31 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 32 | Spare chargeable cells AA size | 2 No. | 2 No. | -- |  |
| 33 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | 1 No. | -- |  |

XEN/GRT

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES SITE No.6

6.	Spur No. 2 on right bank of River Chenab.

13.1	Plan showing route of Flood Water coming out of the breach supported with levels.

Plan attached as Annex-F

13.2	Detail of villages abadies likely to be affected and this should also be shown on the plan.

Village Pandi, Nutt sharqi etc.

13.3	Strategy and action taken be explained in detail. This may include:

STRATEGY OF SPUR NO. 2 ON RIGHT BANK OF RIVER CHENAB.

The J-Head Spur No. 2 near village Pandi fall on the right bank of River Chenab downstream Marala Barrage. The condition of this J-Head Spur is very much critical. During the flood water spills out from the River Chenab and enters the village abadies of Pandi, Nutt Sharqi and damaged the agricultural land. In case of emergency, situation will be controlled through tree launching, Gunny Bags and departmental labour, work charge labour and by the motivation of public volunteers. Plan showing root of flood water coming out of the breach supported with level of vulnerable site of Near village Shahbazpur on right bank of River Chenab as mention at para No.12.3.

13.3.1 – Arrangements

The arrangements are as under:-\

13.3.2 – Establishment of Flood Fighting Camps

iii)	Farrukhpur flood bund		=	RD 14000, RD 21000 & 						   	RD 31000

WATCHING ESTABLISHMENT

| Sr. No. | Name of flood bunds | Camp RD | Beldar | Mate | Gauge Reader | Chowkidar |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | J-Head Spur No. 2 near village Pandi. | Top of Spur | 5 | 1 | -- | 1 |

XEN/GRT

13.3.3 – Duties of Officers/Officials and their camp sites.

| CAMP No. | OFFICERS (Name,Designation& Mobile No.) | OFFICIALS (Name, Designation & Mobile No.) |
| --- | --- | --- |
| 01 | Faisal Nadeem Sub Divisional Officer S&I Sub Division UJC (0333-7483658) | Muhammad Javed Iqbal (Sub Engineer S&I (03027759148) |

Executive Engineer, Gujrat Canal Division UJC.

Executive Engineer will be overall incharge of flood activities in the jurisdiction of Gujrat Canal Division UJC. The flood protection works falling in the  areas of District Gujrat & Mandi Bahauddin are under the administrative control of Executive Engineer. He is responsible for maintenance and supervision of flood protection / watching arrangement during flood season.  He will also keep liaison with the civil / army authorities and Superintending Engineer UJC Circle Jhelum regarding the situation.

Sub Divisional Officer, S&I Sub Division UJC.

In case of emergency and high flood, he will be responsible for the watch and ward of Halsi Nallah Dawara Nallah and river training works along Right side of River Chenab falls in S&I Sub Division UJC Gujrat. He will be mainly responsible for the protection of flood infrastructure & coordination with the Army/District Civil Administration/Executive Engineer Gujrat Canal Division UJC and also camp at J-Head Spur near village Pandi with base station on police frequency Gujrat.

Sub Engineer, S&I

Sub Engineer, kadher will be Incharge of Farrukhpur Flood bund to watch all activities and remain present round the clock with a gang of labour to look after flood infrastructures.

13.3.4 – Departmental machinery available.

No departmental machinery is available in this Division.

13.3.5 – Machinery available from Private Source.

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley

XEN/GRT

13.3.6 – Flood Fighting Material required

The detail is prescribed at page No. 80.

13.3.7- Flood Fighting Material available.

The detail is prescribed at page No. 80.

13.4	Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, Canals and drainage network.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

XEN/GRT

FLOOD FIGHTING MATERIAL REQUIRED / AVAILABLE

| Sr. No. | Item | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | K. Oil | 1 Tin | -- | 1 Tin | The balance Flood Fighting material will be purchased before flood season 2021 |
| 2 | Chimneys for lanterns | 5 No. | -- | 5 No. |  |
| 3 | Gunny bags with suit & sewing needles | 50 No. | -- | 50 No. |  |
| 4 | Ballies | 50 No. | -- | 50 No. |  |
| 5 | Service cable | 1 Coil |  | 1 Coil |  |
| 6 | Wicks | 6 No |  | 6 No. |  |
| 7 | Sprit | 1 Bottles | -- | 1 Bottles |  |
| 8 | Mach boxes | 1 Packet | -- | 1 Packet |  |
| 9 | Petrol | 50 Ltrs. | -- | 50 Ltrs. |  |
| 10 | M. Oil | 10 Ltrs. | -- | 10 Ltrs. |  |
| 11 | Wireless set Walky Talky VX-300 | 1 No. | -- | 1 No. |  |
| 12 | Spare chargeable cells AA size | 2 No. |  | 2 No. |  |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | -- | 1 No. |  |
| 14 | Lantern | 10 No. | 10 No. | -- | Available in Canal Colony Gujrat |
| 15 | Chimneys for lanterns | 7 No. | 7 No. | -- |  |
| 16 | Torches with cells | 6 No. | 6 No. | -- |  |
| 17 | Axes | 5No. | 5No. | -- |  |
| 18 | Kassies with handles | 10 No. | 10 No. | -- |  |
| 19 | Baskets | 15 No. | 15 No. | -- |  |
| 20 | Handles for kassies | 5 No. | 5 No. | -- |  |
| 21 | Gas lamps | 1 No. | 1 No. | -- |  |
| 22 | G.I. wire | 100 kg. | 100 kg. | -- |  |
| 23 | Generator set | 1 No. | 1 No. | -- |  |
| 24 | Service cable | 28 ft. | 28 ft. | -- |  |
| 25 | Wicks | 30 No. | 30 No. | -- |  |
| 26 | Sprit | 2 Bottles | 2 Bottles | -- |  |
| 27 | Match box | 1 dozen | 1 dozen | -- |  |
| 28 | Wooden mallet | 2 No. | 2 No. | -- |  |
| 29 | Search light | 1 No. | 1 No. | -- |  |
| 30 | Tents | 1 No. | 1 No. | -- |  |
| 31 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 32 | Spare chargeable cells AA size | 2 No. | 2 No. | -- |  |
| 33 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. | 1 No. | -- |  |

XEN/GRT

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT/INUNDATED AREA ALONG RIVER & BUNDS OF THE BREACH SUPPORTED WITH LEVELS.

Plan showing route of flood water coming out of the breach are attached.

  - DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.                       i) RIVER CHENAB MARALA TO ALEXANDRA BRIDGE REACH (Annex –D)

| Sr. No. | Very high flood (depth 2’-3’) | Sr. No. | Exceptionally high flood (depth 3’-6’) |
| --- | --- | --- | --- |
| 1. | Changanwali | 1. | Umerwal |
| 2. | Jalowali | 2. | Noshera Miana |
| 3. | Nogran | 3. | Ali Sher |
| 4. | Sheikhpur | 4. | Khasa |
| 5. | Kot Nikka | 5. | Mehota |
| 6. | Chak Meero | 6. | Mehota Kalan |
| 7. | Chak Sada | 7. | Chak Pinar |
| 8. | Kaleki | 8. | Shahbazpur |
| 9. | Kalowal | 9. | Nabipur |
| 10. | Kotli Patwan | 10. | Chak Rehman |
| 11. | Patu | 11. | Nanokey |
| 12. | Nutt | 12. | Thatha Musa |
| 13. | Tara Grah | 13. | Kotli Shahani |
| 14. | Gorali | 14. | Jeowanjal |
| 15. | Gorala | 15. | Noorpur |
| 16. | Kathala | 16. | Mandiala |
| 17. | Chak Multan | 17. | Singanwala |
| 18. | Pindi Nutt | 18. | Miani Pindi |
| 19. | Nutt House | 19. | Mandiala |
| 20. | Saman | 20. | Nassuwali |
| 21. | Mohla | 21. | Chak Gilanwala |
| 22. | Goraya | 22. | Lambor |
| 23. | Tara Garh | 23. | Chak sada |
| 24. | Kot Ghulam | 24. | Ghazi Chak |
| 25. | Qiladar |  |  |
| 26. | Sindhar |  |  |
| 27. | Dherkey Kalan |  |  |

XEN/GRT

ii)       CHUKNANWALI FLOOD BUND ON RIVER CHENAB IN MANDI

BAHAUDDIN DISTRICT.

Plan showing villages abadies likely to be affected is attached at Annexure E.

| Sr. No. | Very high flood (depth 2’-3’) | Sr. No. | Exceptionally high flood (depth 3’-6’) |
| --- | --- | --- | --- |
| 1. | Randali | 1. | Sarang |
| 2. | Bhari | 2. | Dabola |
| 3. | Kala Shadian | 3. | Agroia |
| 4. | Khanpur | 4. | Bahu |
| 5. | Rakh Chani | 5. | Manga |
| 6. | Chani Mughlan | 6. | Sanawala |
| 7. | Chani Kalan | 7. | Alhan |
| 8. | Gidpur | 8. | Thathi Sadia |
| 9. | Jaggo | 9. | Thathi Meran |
| 10. | Jaggo Kalan | 10. | Thatha Khan Muhammad |

iii)     HUMBER FLOOD BUND ON RIVER CHENAB IN

MANDI BAHAUDDIN DISTRICT.

Plan showing villages abadies likely to be affected is attached at Annexure F.

| Sr. No. | Very high flood (depth 2’-3’) | Sr. No. | Exceptionally high flood (depth 3’6’) |
| --- | --- | --- | --- |
| 1. | Qadirabad | 1. | Kapoor Kot |
| 2. | Thathi Shah Muhammad | 2. | Korey Karam Shah |
| 3. | Noshera | 3. | Saida |
| 4. | Farkhpur Kohna | 4. | Bhikho |
| 5. | Burj | 5. | Dherm Kot |
| 6. | Burj Rathoran | 6. | Mehlu Kohna |
| 7. | Burj Ghanian | 7. | Matto |
| 8. | Burj Hassan | 8. | Bohoa Hassan |
| 9. | Burj Ummer | 9. | Devi Garh |
| 10. | Chak Chot | 10. | Burj Bakhat |
| 11. | Qilla Sardar Jawar Singh | 11. | Dhuni Khurd |
| 12. | Khaniawala | 12. | Dhuni Kalan |
| 13. | Teluwala | 13. | Khamb |
| 14. | Gaghianwala | 14. | Chakori |
| 15. | Fatuwala | 15. | Nurpur |

XEN/GRT

Sub Engineer, Chakori

Sub Engineer, Chakori will be the Incharge of Bhimber right flood bund to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

Sub Engineer, Surkhpur

Sub Engineer, Surkhpur Section will be Incharge of Lalamusa Flood Bund to watch all flood activities and remain present round the clock with a gang of labour to look after flood infrastructures.

In case of emergency the sister Division i.e Jhelum Division UJC Jhelum will help this Division.

13.3.4 	DEPARTMENTAL MACHINERY AVAILABLE

No departmental machinery is available in this Division.

13.3.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE.

Following machinery can be hired in case of emergency from private sources. List of machinery is under:-

- Dozer

- Excavator Machine

- Dumper

- Tractor with trolley

13.3.6	FLOOD FIGHTING MATERIAL REQUIRED FOR DIVISION

| Sr. No. | Item | Quantity |
| --- | --- | --- |
| 1 | K. Oil | 1 Tin |
| 2 | Chimneys for lanterns | 5 No. |
| 3 | Gunny bags with suit & sewing needles | 50 No. |
| 4 | Ballies | 50 No. |
| 5 | Service cable | 4 Coil |
| 6 | Wicks | 24 No. |
| 7 | Sprit | 2 Bottles |
| 8 | Match box | 1 Dozen |
| 9 | Petrol | 500 Ltrs. |
| 10 | M. Oil | 100 Ltrs. |
| 11 | Wireless set Walky Talky VX-300 | 1 No. |
| 12 | Spare chargeable cells AA size | 6 No. |
| 13 | Gas lamp/Stove with 2 KG gas filled cylinder | 1 No. |
| 14 | Cooking utensils 6 persons set | 1 No. |
| 15 | Base set | 2 No. |

XEN/GRT

13.3.7	FLOOD FIGHTING MATERIAL AVAILABLE IN HEADQUARTERS SUB DIVISION

| Sr. No. | Item | Required Quantity | Available Quantity | Balance Quantity | Location |
| --- | --- | --- | --- | --- | --- |
| 1. | Lantern | 140 No. | 140 No. | -- | Canal Colony Gujrat |
| 2. | Chimneys for lanterns | 70 No. | 70 No. | -- |  |
| 3. | Torches with cells | 42 No. | 42 No. | -- |  |
| 4. | Axes | 70 No. | 70 No. | -- |  |
| 5. | Kassies with handles | 100 No. | 100 No. | -- |  |
| 6. | Baskets | 110 No. | 110 No. | -- |  |
| 7. | Handles for kassies | 140 No. | 140 No. | -- |  |
| 8. | Gas lamps | 28 No. | 28 No. | -- |  |
| 9. | G.I. wire | 1400 kg. | 1400 kg. | -- |  |
| 10. | Generator Set Small | 1 No. | 1 No. | -- |  |
| 11 | Generator set Large | 1 No. | 1 No. | -- |  |
| 12 | Service cable | 28 ft. | 28 ft. | -- |  |
| 13 | Wicks | 336 No. | 336 No. | -- |  |
| 14 | Sprit | 28 Bottles | 28 Bottles | -- |  |
| 15 | Match box | 14 dozen | 14 dozen | -- |  |
| 16 | Wooden mallet | 24 No. | 24 No. | -- |  |
| 17 | Search light | 10 No. | 10 No. | -- |  |
| 18 | Tents | 8 No. | 8 No. | -- |  |
| 19 | Wireless set Walky Talky VX-300 | 1 Set | 1 Set | -- |  |
| 20 | Spare chargeable cells AA size | 14 No. | 14 No. | -- |  |
| 21 | Gas lamp/Stove with 2 KG gas filled cylinder | 14 No. | 14 No. | -- |  |
| 22 | Pedestal fan | 14 No. | 14 No. | -- |  |
| 23 | Cooking utensils 6 persons set | 14 No. | 14 No. | -- |  |
| 24 | Patha ban | 10 K.G | 10 K.G | -- |  |
| 25 | Shouldari | 7 No. | 7 No. | -- |  |
| 26 | Table with six Chairs | 2 Set | 2 Set | -- |  |
| 27 | Camping Chairs | 2 Dozen | 2 Dozen | -- |  |
| 28 | Charpai | 6 No. | 6 No. | -- |  |
| 29 | Pillow | 6 No. | 6 No. | -- |  |

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATION, ROAD NETWORK, OTHER BUILDINGS, CANALS AND DRAINAGE NETWORK.

There exist Electric line, Sui gas, telephone installation, road, building canals and drain in the area.

Superintending Engineer					Executive Engineer

Upper Jhelum Canal Circle					Gujrat Division UJC

Jhelum								Gujrat

Chief Engineer

Irrigation Sargodha Zone

Sargodha

(Chapter 14)

ACTION PLAN

14.1	Re-shuffling / Recouping plan of reserve stock stone Departmentally.

| Sr. No. | Name of Flood Infrastructures having reserve stock stone. | Available Quantity of Stone (Lac Cft) | Sites where stone can be used during Flood emergency |
| --- | --- | --- | --- |
| 1 | Ganda Bund near village Bhelolpur on right bank of River Chenab. | 0.40 | 1. J-head spur near village shampur on right bank of River Chenab. 2. Guide bank near village surkhpur on River Tawi. 3. Guide bank near village Lashkari Chak on River Tawi. |
| 2 | Guide wall on Kalashadian on right bank of River Chenab. | 0.84 | J-head spur D/S Alexandra Bridge near village samma, Mohla on right bank of River Chenab. |
| 3 | J-head spur No. 5 near village Lambor. J-head spur No. 6 near village Kot Nikha. J-head spur No. 7 near Dawara Nallah on right bank of River Chenab. | 1.23 | 1. J-head Spur No. 4 near village Dera Hakim. 2. J-head Spur No. 3 near village Kotli. 3. J-head Spur No. 2 near village pandi on right bank of River Chenab. |
| 4 | J-head spur No. 8 near village Shahbazpur on right bank of River Chenab. | 0.48 | 1. Guide bank spur No. 9 near Dera Hakim. 2. Guide bank spur No. 10 near Sajawal. 3. Guide bank spur No. 11 near village Chopala on right bank of River Chenab. |
| 5 | J-head spur near Chakori on right bank of River Chenab. | 0.45 | 1. Guide wall Spur near Noorpur village. 2. Guide wall Spur U/S Haveli Manik. 3. Farrukhpur Flood Bund on right bank of River Chenab. |

Reserve stock of stone will be reshuffled through Govt.Contractors

14.2	Detail of inlet . Outlet crossing along with closing methodology.

--------Nil------

14.3		Deployment Machinery (Medium to high flood)

Attached at Page 88-90

14.4		Deployment Machinery (High to very high flood)

Attached at Page 91-93

14.5	Deployment Machinery ( Very High to exceptionally high flood)

Attached at Page 94-96

14.6		Police Deployment plan

Attached at page 97

14.7	Details of synthetic bags with capacity of 500 kg and 1000 kg

| Synthetic Bags | Required | Available | Balance |
| --- | --- | --- | --- |
| 500 kg | 400 kg | Nil | 400 kg |
| 1000 kg | 500 kg | Nil | 500 kg |

14.8	Details of polythene sheet of black color to protect upstream slope against wave action and to control seepage through embankments

| Polythene Sheet | Required | Available |
| --- | --- | --- |
| Nil | Nil | Nil |

XEN/GRT

ACTION PLAN DURING FLOODS ON RIVER CHENAB

14.3	(DEPOLYMENT MACHINARY MEDIUM TO HIGH FLOOD)

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Bhimber Right Flood Bund | 4.310 | RD 3-4, 9-10 | RD 3-4 & 9-10 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 3 Tractor Trolleys | 0 | 6 Beldar | 0 |
| 2 | Bhimber Left Flood Bund | 3.810 | RD 3-4 | RD 3-4 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 3 Tractor Trolleys | 0 | 6 Beldar + 1 Mate | 0 |
| 3 | Lalamusa Flood Bund | 10.800 | RD 9-10 | RD 14, 29 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 4 Tractor Trolleys | 0 | 24 Beldar + 2 Mate | 0 |
| 4 | Lalamusa extension Flood Bund | 5.454 |  | RD 11 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 4 Tractor Trolleys | 0 | 12 Beldar + 1 Mate | 0 |
| 5 | J-Head Spur Samman Mohala | 0.580 |  | J-Head Spur Samma Mohla | Mehmood ul Hasson Sherazi(Sub Engineer 0300-7563303 | 1 | 0 | 5 Tractor Trolleys | 0 | 3 Beldar | 0 |
| 6 | J-Head Spur No.2 | 1.760 |  | J-Head Spur No.2 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 4 Dumpers | 0 | 3 Beldar | 0.67 |

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 7 | J-Head Spur No.3 | 0.800 |  | J-Head Spur No.3 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 3 Beldar | 0.06 |
| 8 | J-Head Spur No.4 | 0.530 |  | J-Head Spur No.4 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 4 Beldar | 0.17 |
| 9 | Guide Wall Spur No.8 | 0.380 |  | Guide Wall Spur No.8 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 4 Beldar | 0.48 |
| 10 | Guide Wall Spur No.9 | 0.410 |  | Guide Wall Spur No.9 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 4 Beldar | 0.17 |
| 11 | Guide Wall Spur No.11 | 0.360 |  | Guide Wall Spur No.11 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 3 Beldar | 0.25 |
| 12 | J-Head Spur Shampur | 0.480 |  | J-Head Spur Shampur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 4 Beldar | 0 |
| 13 | Inverted Hockey Spur Behlolpur | 0.081 |  | Inverted Hockey Spur Behlolpur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 4 Tractor Trolleys | 0 | 3 Beldar | 0 |

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 14 | Guide wall Spur Surkhpur | 0.355 |  | Guide bank Spur Surkhpur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 3 Tractor Trolleys | 0 | 3 Beldar | 0 |
| 15 | Humber flood bund | 16.500 |  | RD 31,47,72 | Muhammad Akmal, (Sub Engineer 0300 7746292) | 1 | 0 | 5 Tractor Trolleys | 0 | 10 Beldar + 1 Mate | 0 |
| 16 | Farrukhpur flood bund | 6.800 | RD 14-17, 21-22 & 31-32 | RD 14,21 & 31 | Muhammad Akmal, (Sub Engineer 0300 7746292) | 1 | 0 | 5 Tractor Trolleys | 0 | 10 Beldar + 1 Mate | 0 |
| TOTAL | 53.410 |  |  |  | 16 | 0 | 10 Dumper 57 Tractor Trolleys | 0 |  |  |

ACTION PLAN DURING FLOODS ON RIVER CHENAB

14.4		(DEPOLYMENT MACHINARY HIGH TO VERY HIGH FLOOD)

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Bhimber Right Flood Bund | 4.310 | RD 3-4, 9-10 | RD 3-4 & 9-10 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 3 Tractor Trolleys | 0 | 6 Beldar | 0 |
| 2 | Bhimber Left Flood Bund | 3.810 | RD 3-4 | RD 3-4 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 3 Tractor Trolleys | 0 | 6 Beldar + 1 Mate | 0 |
| 3 | Lalamusa Flood Bund | 10.800 | RD 9-10 | RD 14, 29 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 4 Tractor Trolleys | 0 | 24 Beldar + 2 Mate | 0 |
| 4 | Lalamusa extension Flood Bund | 5.454 |  | RD 11 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 4 Tractor Trolleys | 0 | 12 Beldar + 1 Mate | 0 |
| 5 | J-Head Spur Samman Mohala | 0.580 |  | J-Head Spur Samma Mohla | Mehmood ul Hasson Sherazi(Sub Engineer 0300-7563303 | 1 | 0 | 5 Tractor Trolleys | 0 | 3 Beldar | 0 |
| 6 | J-Head Spur No.2 | 1.760 |  | J-Head Spur No.2 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 4 Dumpers | 0 | 3 Beldar | 0.67 |

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 7 | J-Head Spur No.3 | 0.800 |  | J-Head Spur No.3 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 3 Beldar | 0.06 |
| 8 | J-Head Spur No.4 | 0.530 |  | J-Head Spur No.4 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 4 Beldar | 0.17 |
| 9 | Guide Wall Spur No.8 | 0.380 |  | Guide Wall Spur No.8 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 4 Beldar | 0.48 |
| 10 | Guide Wall Spur No.9 | 0.410 |  | Guide Wall Spur No.9 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 4 Beldar | 0.17 |
| 11 | Guide Wall Spur No.11 | 0.360 |  | Guide Wall Spur No.11 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 3 Beldar | 0.25 |
| 12 | J-Head Spur Shampur | 0.480 |  | J-Head Spur Shampur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 4 Beldar | 0 |
| 13 | Inverted Hockey Spur Behlolpur | 0.081 |  | Inverted Hockey Spur Behlolpur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 4 Tractor Trolleys | 0 | 3 Beldar | 0 |
| 14 | Guide wall Spur Surkhpur | 0.355 |  | Guide bank Spur Surkhpur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 3 Tractor Trolleys | 0 | 3 Beldar | 0 |

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 15 | Humber flood bund | 16.500 |  | RD 31,47,72 | Muhammad Akmal, (Sub Engineer 0300 7746292) | 1 | 0 | 5 Tractor Trolleys | 0 | 10 Beldar + 1 Mate | 0 |
| 16 | Farrukhpur flood bund | 6.800 | RD 14-17, 21-22 & 31-32 | RD 14,21 & 31 | Muhammad Akmal, (Sub Engineer 0300 7746292) | 1 | 0 | 5 Tractor Trolleys | 0 | 10 Beldar + 1 Mate | 0 |
| 17 | Gujrat Flood Bund | 16.840 |  | RD 33,50 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 7 Tractor Trolleys | 0 | 6 Beldar | 0 |
| 18 | Chuknawali Flood Bund | 12.390 |  | RD 111,147 | Mehmood –ul-Hasson Sherazi Sub Engineer (0300-9621742) | 1 | 0 | 5 Tractor Trolleys | 0 | 16 Beldar +2 Mate | 0 |
| TOTAL | 82.640 |  |  |  | 18 | 0 | 10 Dumper 69 Tractor Trolleys | 0 |  |  |

PLAN DURING FLOODS ON RIVER CHENAB

14.5	  (DEPOLYMENT MACHINARY HIGH TO EXCEPTIONALLY HIGH FLOOD)

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Bhimber Right Flood Bund | 4.310 | RD 3-4, 9-10 | RD 3-4 & 9-10 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 3 Tractor Trolleys | 0 | 6 Beldar | 0 |
| 2 | Bhimber Left Flood Bund | 3.810 | RD 3-4 | RD 3-4 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 3 Tractor Trolleys | 0 | 6 Beldar + 1 Mate | 0 |
| 3 | Lalamusa Flood Bund | 10.800 | RD 9-10 | RD 14, 29 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 4 Tractor Trolleys | 0 | 24 Beldar + 2 Mate | 0 |
| 4 | Lalamusa extension Flood Bund | 5.454 |  | RD 11 | Rashid Mehmood (Sub Engineer 03238008001) | 1 | 0 | 4 Tractor Trolleys | 0 | 12 Beldar + 1 Mate | 0 |
| 5 | J-Head Spur Samman Mohala | 0.580 |  | J-Head Spur Samma Mohla | Mehmood –ul-Hasson Sherazi ( Sub Engineer 0300-7563303 | 1 | 0 | 5 Tractor Trolleys | 0 | 3 Beldar | 0 |
| 6 | J-Head Spur No.2 | 1.760 |  | J-Head Spur No.2 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 4 Dumpers | 0 | 3 Beldar | 0.67 |

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 7 | J-Head Spur No.3 | 0.800 |  | J-Head Spur No.3 | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 3 Beldar | 0.06 |
| 8 | J-Head Spur No.4 | 0.530 |  | J-Head Spur No.4 | Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 4 Beldar | 0.17 |
| 9 | Guide Wall Spur No.8 | 0.380 |  | Guide Wall Spur No.8 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 4 Beldar | 0.48 |
| 10 | Guide Wall Spur No.9 | 0.410 |  | Guide Wall Spur No.9 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 4 Beldar | 0.17 |
| 11 | Guide Wall Spur No.11 | 0.360 |  | Guide Wall Spur No.11 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 3 Tractor Trolleys | 0 | 3 Beldar | 0.25 |
| 12 | J-Head Spur Shampur | 0.480 |  | J-Head Spur Shampur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 2 Dumpers 4 Tractor Trolleys | 0 | 4 Beldar | 0 |
| 13 | Inverted Hockey Spur Behlolpur | 0.081 |  | Inverted Hockey Spur Behlolpur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 4 Tractor Trolleys | 0 | 3 Beldar | 0 |
| 14 | Guide wall Spur Surkhpur | 0.355 |  | Guide bank Spur Surkhpur | Muhammad Javed Iqbal, (Sub Engineer 03027759148) | 1 | 0 | 3 Tractor Trolleys | 0 | 3 Beldar | 0 |

| Sr. No. | Name of structure | Length in mile | Vulnerable reach | Camp location | Site incharge by name & Cell No. | Machinery deployed | Availability of stone Lac cft |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Labour (Beldar+ Mate) |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 15 | Humber flood bund | 16.500 |  | RD 31,47,72 | Muhammad Akmal, (Sub Engineer 0300 7746292) | 1 | 0 | 5 Tractor Trolleys | 0 | 10 Beldar + 1 Mate | 0 |
| 16 | Farrukhpur flood bund | 6.800 | RD 14-17, 21-22 & 31-32 | RD 14,21 & 31 | Muhammad Akmal, (Sub Engineer 0300 7746292) | 1 | 0 | 5 Tractor Trolleys | 0 | 10 Beldar + 1 Mate | 0 |
| 17 | Gujrat Flood Bund | 16.840 |  | RD 33,50 | Ejaz Ahmad, (Sub Engineer 03328458465) | 1 | 0 | 7 Tractor Trolleys | 0 | 6 Beldar | 0 |
| 18 | Chuknawali Flood Bund | 12.390 |  | RD 111,147 | Mehmood –ul-Hasson Sherazi Sub Engineer (0300-9621742) | 1 | 0 | 5 Tractor Trolleys | 0 | 16 Beldar +2 Mate | 0 |
| TOTAL | 82.640 |  |  |  | 18 | 0 | 10 Dumper 69 Tractor Trolleys | 0 |  |  |

14.6 POLICE DEPLOYMENT PLAN

| S.No. | Vulnerable sites | Concerned Canal Division | Concerned Police station & Districe | Police persons to be deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector/ SI/ASI | Constable |  |
| 1 | Lalamusa flood bund along right bank of Bhimbr Nallah between RD 9000-10000 | Gujrat | Lalamusa ,Gujrat | Sub Inspector = 02 Nos. | 8 Nos |  |
| 2 | Bhimber Right flood bund along left bank of Bhimber Nallah between RD 3000-4000 & 9000-10000 | Gujrat | Rehmanian, Gujrat | Sub Inspector = 02 Nos. | 8 Nos |  |
| 3 | Farrukhpur flood bund along left bank of Budi Nallah Drain RD 14000-17000, 21000-22000 & 31000-32000 | Gujrat | Qadirabad Mandi Bahauddin | Sub Inspector = 03 Nos. | 12Nos |  |

(Chapter 15)

BACK UP DIVISIONS (IN CASE OF BREACH)

It is certified that no breaching section exists in the jurisdiction of this Division. The backup Division is Drainage Division Mandi Baha –ud-Din.

Executive Engineer

Gujrat Division UJC

Gujrat