FLOOD FIGHTING PLAN

OF

LAHORE DRAINAGE DIVISION LAHORE

FOR THE YEAR 2021

LAHORE IRRIGATION ZONE, LAHORE

LAHORE DRAINAGE CIRCLE,  LAHORE

LAHORE DRAINAGE DIVISION, LAHORE

IRRIGATION DEPARTMENT, LAHORE

INDEX PLAN

| Chapter No | Contents | Page No |
| --- | --- | --- |
|  | PART - A |  |
| 1 | Salient Features of the concerned Division |  |
|  | 1.1 | Location | 1 – 2 |
|  | 1.2 | General Description | 2 – 3 |
|  | 1.3 | Administrative Setup | 4 |
| 2 | Flood Protection and River Training Works |  |
|  | 2.1 | Design Parameters of Training Works | 5– 6 |
|  | 2.2 | Location Map | 7 |
| 3 | Brief History of Past Flood Events | 8 |
| 4 | Design Data, Historic peak flood data and previous five years flood data of Head Works / Barrages and or other control points |  |
|  | 4.1 | Flood Limits | 9 |
|  | 4.2 | Time Lags of Floods | 10 |
|  | 4.3 | Highest Floods | 10 |
|  | 4.4 | Peak Discharges | 11 |
| 5 | Flood Fighting Strategy | 12 – 13 |
| 6 | Flood Damages Restoration Works | 14 |
| 7 | Flood Fighting / Watching Arrangements |  |
|  | 7.1 | Pre-Flood Arrangement | 15 – 16 |
|  | 7.2 | Watching Establishment | 17 |
|  | 7.3 | Arrangement at Sensitive sites | 18 |
|  | 7.4 | Watching material | 18 – 21 |
| Chapter No | Contents | Page No |
|  | 7.5 | Arrangement for Sounding & Probing | 22 |
|  | 7.6 | Lighting Arrangement | 22 |
|  | 7.7 | Ration Arrangement | 22 |
|  | 7.8 | P.O.L Arrangement for Vehicles | 22 |
|  | 7.9 | Transportation | 22 |
|  | 7.10 | Law and order | 22 |
|  | 7.11 | Medical Arrangement for Labour | 23 |
|  | 7.12 | Liaison with other Departments | 23 |
|  | 7.13 | Role of the Army | 23 |
|  | 7.14 | Duties of Telephone Attendant | 23 |
|  | 7.15 | Wireless Arrangement | 23 |
| 8 | Detail of Encroachment | 24 – 32 |
| 9 | Duty Roster / Flood Fighting Program | 33 – 34 |
| 10 | Emergency Telephone Nos | 35 – 37 |
| 11 | Standard Operating Procedure (SOP) for Breaching Sections |  |
|  | 11.1 | History of the breaching section | 38 |
|  | 11.2 | Location, Design, Quantity and Variety of the explosive required for detonation. | 39 |
|  | 11.3 | Arrangement of explosives and security of explosive stores | 39 |
|  | 11.4 | List of security staff alongwith detail of their training etc | 39 |
|  | 11.5 | Detail of mechanical means as a standby arrangements in case of detonation failure | 40 |
|  | 11.6 | Duty Roster in case of critical situation | 40 |
|  | 11.7 | Breaching Committee with their action plan | 40 |
| Chapter No | Contents | Page No |
|  | 11.8 | List of the villages likely to be inundated in case of breach | 41 – 45 |
|  | 11.9 | Announcement and detail of evacuation arrangements | 45 |
|  | 11.10 | Details of coordination with Civil / Army Authorities | 45 |
|  | 11.11 | Parallel communication arrangements | 45 |
|  | 11.12 | Index Plan | 46 |
|  | PART - B |  |
| 12 | Vulnerable sites on Flood Bunds / Structures |  |
|  | 12.1 | Apprehended breaches in Flood Bunds / Structures | 47 |
|  | 12.2 Operation of Breaching Section | 47 |
|  | 12.3 Breaches Due To Rise Of Flood Water, Deterioration Of Flood Bunds. | 47 |
| 13 | Emergency Contingency Plan for vulnerable site listed above. Emergency Contingency Plan must include |  |
|  | SITE NO.1 R.D 9+000 to 15+000 SHAHDARA FLOOD PROTECTION BUND |  |
|  | 13.1 | Plan showing route of Flood Water coming out of the breach supported with levels. | 48 |
|  | 13.2 | Detail of villages / abadies likely to be affected and this should also be shown on the plan. | 48 |
|  | 13.3 | Strategy and action taken be explained in detail. | 49 |
|  |  | 13.3.1 | Arrangements | 49 |
|  |  | 13.3.2 | Establishment of Flood Fighting Camps | 49 |
|  |  | 13.3.3 | Duties of Officers / Officials and their camp sites | 50 |
|  |  | 13.3.4 | Departmental Machinery availability | 50 |
|  |  | 13.3.5 | Machinery available from Private Source | 50 |
|  |  | 13.3.6 | Flood Fighting Material required | 51 |
|  |  | 13.3.7 | Flood Fighting Material available | 52 |
| 13.4 | Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, canal and drainage network. | 53 |
| Chapter No | Contents | Page No |
|  | SITE NO.2 R.D 16+000 to 32+000 SHARKPUR FLOOD PROTECTION BUND |  |
|  | 13.1 | Plan showing route of Flood Water coming out of the breach supported with levels. | 54 |
|  | 13.2 | Detail of villages / abadies likely to be affected and this should also be shown on the plan. | 54 |
|  | 13.3 | Strategy and action taken be explained in detail. | 55 |
|  |  | 13.3.1 | Arrangements | 55 |
|  |  | 13.3.2 | Establishment of Flood Fighting Camps | 55 |
|  |  | 13.3.3 | Duties of Officers / Officials and their camp sites | 56 |
|  |  | 13.3.4 | Departmental Machinery availability | 56 |
|  |  | 13.3.5 | Machinery available from Private Source | 56 |
|  |  | 13.3.6 | Flood Fighting Material required | 57 |
|  |  | 13.3.7 | Flood Fighting Material available | 57 – 58 |
| 13.4 | Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, canal and drainage network. | 58 |
| 14 | Action Plan |  |
| 14.1 | Re-shuffling / recouping plan of reserve stock of stone departmentally | 59 |
| 14.2 | Detail of inlet and outlet crossing along with closing methodology. | 59 |
| 14.3 | Deployment of machinery (Medium to high flood) | 59 |
| 14.4 | Deployment of machinery (High to very high) | 60 |
| 14.5 | Deployment of machinery (High to exceptionally high flood) | 60 |
| 14.6 | Police deployment plan. | 61 |
| 14.7 | Detail of synthetic bags with capacity of 500 Kg and 1000 Kg. | 62 |
| 14.8 | Detail of Polythene sheets of black colour to protect upstream slope against wave action and to control seepage through embankment. | 62 |
| 15 | Back up divisions (In case of breach) | 63 |

PART – A

PART – B

FLOOD FIGHTING PLAN OF LAHORE DRAINAGE DIVISION, LAHORE

CHAPTER – 1

SALIENT FEATURES OF LAHORE DRAINAGE DIVISION

  - LOCATION

Lahore Drainage Division Lahore is situated at Canal Bank Mustafabad Lahore. River Ravi enters in Pakistan territory near Kot Nainan, Tehsil Shakargarh, and District Narowal. Many flood protection works on both sides of the river, such as Jalala Bund, Kotli Sanian bund, Hajipur Gujran Bund, Bheco Chak Bund Shahdara Bund, Mehmood Booti Bund, Lahore Protection Bund & Sharkpur Bund etc along with battery of spurs are located on Pakistan side. Right from Madhupur Head works to Ravi Syphon, the River is trained in Indian Territory by large number of River Training works by India.

On the Pakistan side in Narowal District, there are Jassar Bund, Highway Flood Protection Bund, and Raya Bund. Daily information regarding discharge in the River at Mahdupur Head works is received by the Flood Warning Center, Lahore and the Departmental functionaries are supposed to be vigilant to meet with any emergency from 15th June to 15th Oct. The jurisdiction of Lahore Drainage Division Lahore, on the left side is started from downstream Ravi Syphon to Head Balloki and on the right side it started from Shahdara Flood Protection Bund to Downstream Sharkpur Flood Protection Bund. On right side of River Ravi, there is Shahdara Flood Protection Bund RD.0-15+750 which starts from upstream of Shahdara Railway Bridge and connects Shahdara Disty Flood Protection Bund at RD.65+000. Similarly on left side of River Ravi, there is Mahmood Booti Bund RD.0-29+300 on the upstream of Shahdara Railway Bridge. The Mahmood Booti Bund has now come under the Ring Road and does not exist in its original shape and design. The Shahdara and Mahmood Booti Bunds are connected with series of River Training Works to train the river through Shahdara Railway Bridge and old G.T. Road Bridge.

On right side of River Ravi, down steam of Shahdara Railway Bridge there is Sharkpur Flood bund having length RD.0-32+060 and on the left side of the River Ravi, there is Lahore protection bund RD.0-26+000 and Tie Bund connected with series of river training works. It is again mentioned here that Ring Road and Motorway have been constructed over Lahore Protection bund & Tie Bund respectively and these both bunds now do not exist in their original shape and design.

1.2	GENERAL DESCRIPTION

Lahore Drainage Division was established during 1957-59. The main objectives of this Division are:-

- To look after the flood protection bunds along the River Ravi in District, Lahore and Sheikhupura.

- To maintain drains in Lahore and Kasur District.

There are four Sub Divisions under the control of this Division namely:-

- Flood Bund Sub Division

- Lahore Drainage Sub Division

- Kasur Drainage Sub Division

- River Survey Drainage Sub Division

Flood Bund Sub Division is entirely concerned with the flood protection works and to look after the flood Bunds. There are 5-No Flood Protection Bunds and 22 No spurs in Lahore and Sheikhupura District. However the J-head spur at Shahpur Kanjran and J-head spur at Chung are under control of Kasur Drainage Sub Division, Lahore.

- Shahdara Flood Protection Bund with 5 spurs.

- Mahmood Booti Bund with 2 spurs.

- Lahore Flood Protection Bund with 5 spurs.

- Lahore Tie Bund with 3 spurs.

- J-Head spur at Shahpur Kanjran.

- J-Head spur at Chung.

- J-Head spur at Qadirabad.

- Sharkpur Flood Protection Bund with 5 spurs.

The other 3 Sub Divisional Officers are responsible for the operation and maintenance of three drainage system:

- Hudiara Drainage System

- Pandoki Drainage System

- Raiwind Drainage System

Sub Divisional Officer Kasur Drainage Sub Division has the control of Raiwind Drainage System. Sub Divisional Officer Lahore Drainage Sub Division looks after the Hudiara Drainage System while the Sub Divisional Officer River Survey Drainage Sub Division is responsible for the Pandoki Drainage System.

Watching of the bunds and River Training works is done as per duty roster provided in the flood fighting plan of this Division (plan attached). All other details of flood fighting are given in the light of instructions issued by the Chief Engineer, Drainage & Flood Zone Lahore vide No.D&F/2012/859/25/76 dated.10-03-2012.

1.3 ADMINISTRATIVE SETUP

CHAPTER – 2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1	DESIGN PARAMETERS OF TRAINING WORKS

| S.# | Name of Bunds | Sub Division | Section | Length (in ft) | Top width (in feet) | Side Slopes | RD | H.F.L. (R.L) for the year 1988 326000 Cs | Free Board (in ft) | Top R.L. of bund / Spur |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | River Side | Country side |  |  |  |  |
|  | FLOOD BUND SUB DIVISION, LAHORE |  |  |  |  |  |  |  |  |  |  |
|  | Mahmood Booti Section |  |  |  |  |  |  |  |  |  |  |
| 1 | Mahmood Booti Bund RD.0-29000 (Lahore Ring Road) | F.B.S.D | M.B.B | 29000 | 40 | 3 ;1 | 2 ;1 | 0 | 694 | 6 | 700 |
| 2 | Hockey spur at RD.7000 M.B.Bund | F.B.S.D | M.B.B | 3700 | 25 | 3 ;1 | 2 ;1 |  | 694 | 6 | 700 |
| 3 | Slopping spur at RD.9000 M.B.Bund | F.B.S.D | M.B.B | 3650 | 15-18 | 3 ;1 | 3 ;1 |  | 694 |  | 695 |
|  | Shahdara Flood Protection Bund Section |  |  |  |  |  |  |  |  |  |  |
|  | Shahdara Flood Protection bund RD.15750 | F.B.S.D | S.F.P.B | 15750 | 25 | 3 ;1 | 2 ;1 | 15150 | 694 | 5 | 704.34 |
| 1 | T-Head spur No.1 at RD.2300 | F.B.S.D | S.F.P.B | 600 | 25 | 3 ;1 | 3 ;1 |  |  |  | 701 |
| 2 | T-Head spur No.2 at RD.4300 | F.B.S.D | S.F.P.B | 2000 | 25 | 3 ;1 | 3 ;1 |  |  |  | 702 |
| 3 | T-Head spur No.3 at RD.6300 | F.B.S.D | S.F.P.B | 1000 | 25 | 3 ;1 | 3 ;1 |  |  |  | 702.19 |
| 4 | T-Head spur No.4 at RD.7400 | F.B.S.D | S.F.P.B | 1200 | 25 | 3 ;1 | 3 ;1 |  |  |  | 703.48 |
| 5 | Hockey spur No.5 at RD.9500 | F.B.S.D | S.F.P.B | 3600 | 25 | 3 ;1 | 3 ;1 |  |  |  | 703.87 |
| 6 | Stone Stud No.1 along Hockey Spur. | F.B.S.D | S.F.P.B | 225 |  |  |  |  |  |  |  |
| 7 | Stone Stud No.2 along Hockey Spur. | F.B.S.D | S.F.P.B | 225 |  |  |  |  |  |  |  |
|  | Lahore Flood Protection Bund Section |  |  |  |  |  |  |  |  |  |  |
| 1 | Lahore Protection Bund RD.3000-26000 (Lahore Ring Road) | F.B.S.D | L.F.P.B | 23000 | 25 | 3 ;1 | 2 ;1 | 3000 | 693.7 | 3 | 696.4 |
| 2 | J-spur No.1 (Gowshala) at RD.3600 | F.B.S.D | L.F.P.B | 1490 | 25 | 3 ;1 | 3 ;1 |  |  | 6 | 697.46 |
| 3 | J-spur No.2 at RD.5700 | F.B.S.D | L.F.P.B | 3800 | 20 | 2 ;1 | 2 ;1 |  |  |  | 695.53 |
| 4 | J-spur No.3 at RD.9800 | F.B.S.D | L.F.P.B | 4295 | 20 | 2 ;1 | 2 ;1 |  |  |  | 694.77 |
| 5 | J-spur No.4 at RD.17800 | F.B.S.D | L.F.P.B | 3992 | 20 | 2 ;1 | 2 ;1 |  |  |  | 693.1 |
| 6 | T-Head spur No.5 at RD.19900 | F.B.S.D | L.F.P.B | 5775 | 20 | 2 ;1 | 2 ;1 |  |  |  | 691 |
|  | Tie Bund RD.0-20000 (Motorway) | F.B.S.D | L.F.P.B | 20000 | 25 | 3 ;1 | 2 ;1 | 500 |  |  | 694.78 |
| 1 | J-head spur No.1 at RD.6600 | F.B.S.D | L.F.P.B | 4363 | 25 | 3 ;1 | 3 ;1 |  |  |  | 694 |
| 2 | L-Bund / Spur at RD.10600 | F.B.S.D | L.F.P.B | 2000 | 25 | 3 ;1 | 3 ;1 |  |  |  | 692.48 |
| 3 | J-head spur No.2 at RD.20000 | F.B.S.D | L.F.P.B | 4562 | 25 | 3 ;1 | 3 ;1 |  |  |  | 689 |
| S.# | Name of Bunds | Sub Division | Section | Length (in ft) | Top width (in feet) | Side Slopes | RD | H.F.L. (R.L) for the year 1988 326000 Cs | Free Board (in ft) | Top R.L. of bund / Spur |
|  |  |  |  |  |  | River Side | Country side |  |  |  |  |
|  | Qadirabad Section |  |  |  |  |  |  |  |  |  |  |
| 1 | J-spur Qadirabad | F.B.S.D | Qadirabad | 5690 | 25 | 3 ;1 | 3 ;1 | 0 |  | - | 690 |
| 2 | Slopy spurs No.1 (Farkhabad) | F.B.S.D | Qadirabad | 135 | 10 | 2 ;1 | 2 ;1 |  |  | - | 688.5 |
| 3 | Slopy spurs No.2 (Farkhabad) | F.B.S.D | Qadirabad | 190 | 8 | 3 ;1 | 2 ;1 |  |  | - | 689 |
| 4 | Slopy spurs No.3 (Farkhabad) | F.B.S.D | Qadirabad | 135 | 10 | 2 ;1 | 2 ;1 |  |  | - | 690.83 |
|  | Sharkpur Flood Protection Bund Section |  |  |  |  |  |  |  |  |  |  |
| 1 | Sharkpur Flood Protection Bund RD.0-32060 | F.B.S.D | SKP.F.P | 32060 | 25 | 3 ;1 | 2 ;1 | 0 | 675.7 | 6 | 679.66 |
| 2 | J-spur No.1 at RD.5060 S.F.P.Bund | F.B.S.D | SKP.F.P | 4000 | 25 | 3 ;1 | 3 ;1 |  |  | 5 | 678.5 |
| 3 | J-spur No.2 at RD.11080 S.F.P.Bund | F.B.S.D | SKP.F.P | 4050 | 25 | 3 ;1 | 3 ;1 |  |  | 5 | 677.96 |
| 4 | Earthen spur No.3 at RD.16510 S.F.P.Bund | F.B.S.D | SKP.F.P | 4800 | 25 | 3 ;1 | 3 ;1 |  |  | 5 | 677 |
| 5 | T-head spur No.4 at RD.26860 S.F.P.Bund | F.B.S.D | SKP.F.P | 2230 | 25 | 3 ;1 | 3 ;1 |  |  | 5 | 674.3 |
| 6 | J-head spur No.5 at RD.30560 S.F.P.Bund | F.B.S.D | SKP.F.P | 1800 | 25 | 3 ;1 | 3 ;1 |  |  | 5 | 671.69 |
|  | Kasur Drainage Sub Division, Lahore |  |  |  |  |  |  |  |  |  |  |
| 1 | J-spur Shahpur Kanjran RD.0-7948 | Kasur | Niaz Baig | 7948 | 25 | 3 ;1 | 2 ;1 |  |  |  | 683 |
| 2 | J-head spur at Chung RD.0-5673 | Kasur | Niaz Baig | 5673 | 25 | 3 ;1 | 3 ;1 |  |  |  | 679.66 |
| 3 | Mole head spur | Kasur | Niaz Baig | 2244 | 25 | 3 ;1 | 3 ;1 |  |  |  |  |
|  | Total Length |  |  | 205182 |  |  |  |  |  |  |  |

NOTE:	As already discussed in the report Mahmood Booti Flood Protection Bund, Lahore Flood Protection Bund and Tie Bund have become under Ring Road and Motorway and do not exist in their original shape and design.

2.2	LOCATION MAP

On Next Page

CHAPTER – 3

BRIEF HISTORY OF PAST FLOOD EVENTS

There are three gauging stations upto Shahdara Railway Bridge when river Ravi enters into territory of Pakistan viz, Jassar, Ravi Syphon and Railway Bridge Shahdara. The first head works on this River in Pakistan is Balloki Head Works.

The gauge fixed at Shahdara Railway Bridge is recorded regularly during the flood season. In 1947, exceptional high flood of 225000 Cs was recorded at this site. In 1955  flood of 540000 Cs was experienced at Shahdara. In 1973, flood of 444299 Cs was noted at this site. During the flood of 1988, discharge of 326100 Cs. was experienced through Railway Bridge and the rest of about 249900 Cs through breaching section. The gauge observed at Shahdara Railway Bridge was R.L. 694.70 feet, when breaching section was operated during this flood. The Shahdara Flood Protection Bund breached at RD.13+ and 15+ when breaching section between RD.55+000 to 65+000 of Shahdara Distributary Bund was operated during this flood. The discharge of breached section at cut in the Shahdara Flood Protection Bund was estimated to be 1.0 Lac Cs. This discharge caused inundation of Shahdara Town and its suburbs. All the roads and other infrastructure came under water with varying depth from one foot to eight feet.

Massive destruction was caused by the flood of 1988 in Shahdara and allied abadies.

After 1988, the significant floods were experienced in 1993, 1995, 1996 & 1997 recorded as 91415, 171520, 182340 and 123080 Cs respectively. Since 1997, no real flood situation has been noted at Shahdara.

CHAPTER – 4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS / BARRAGES AND OR OTHER CONTROL POINTS

4.1	FLOOD  LIMITS (Cs)

| Location | LOW | MEDIUM | HIGH | VERY HIGH | EXCEPTIONAL HIGH |
| --- | --- | --- | --- | --- | --- |
| Jassar | 50000 To 75000 | 75000 To 100000 | 100000 To 150000 | 150000 To 200000 | 200000 and Above |
| Ravi Syphon | 40000 To 65000 | 65000 To 90000 | 90000 To 135000 | 135000 To 180000 | 180000 and Above |
| Shahdara | 40000 To 65000 | 65000 To 90000 | 90000 To 135000 | 135000 To 180000 | 180000 and Above |
| Balloki | 40000 To 65000 | 65000 To 90000 | 90000 To 135000 | 135000 To 180000 | 180000 and Above |

4.2	TIME LAGS OF FLOODS

| River | Site | Distance in Km | Time Lag in Hours |
| --- | --- | --- | --- |
|  | From | To |  |  |
| Ravi | Hajipur Gujran | Jassar | 94 | 12 |
|  | Jassar | Ravi Syphon | 73 | 18 |
|  | Ravi Syphon | Shahdara | 24 | 8 |
| Total Time Lag from Hajipur Gujran to Shahdara | 38 Hours |

4.3	HIGH FLOODS

| S.# | Highest Floods | Discharge at Shahdara Railway Bridge | Discharge Through Breaching Section | Total Discharge |
| --- | --- | --- | --- | --- |
| 1. | 1955 | 2,81,000 Cs | 2,59,000 Cs | 5,40,000 Cs |
| 2. | 1973 | 2,37,380 Cs | 2,06,919 Cs | 4,44,299 Cs |
| 3. | 1988 | 3,26,100 Cs | 2,49,900 Cs | 5,76,000 Cs |
| 4. | 1996 | 1,82,340 Cs | - | 1,82,340 Cs |

4.4	PEAK DISCHARGES

| YEAR | JASSAR | RAVI SYPHON | SHAHDARA |
| --- | --- | --- | --- |
|  | DATED | GAUGE | DISCHARGE | DATED | GAUGE | DISCHARGE | DATED | GAUGE | DISCHARGE |
| 1988 | 26-09-1988 | 791.00 | 121800 | 27-09-1988 | 715.70 | 325040 | 27-09-1988 | 694.70 | 576000 |
| 1989 | 31-07-1989 | 787.20 | 104818 | 01-08-1989 | 704.30 | 68702 | 01-08-1989 | 685.80 | 66985 |
| 1990 | 09-08-1990 | 782.00 | 46392 | 10-09-1990 | 703.30 | 59282 | 10-09-1990 | 684.80 | 52793 |
| 1991 | 11-08-1991 | 783.00 | 54975 | 12-08-1991 | 702.00 | 47582 | 12-08-1991 | 684.00 | 43163 |
| 1992 | 11-09-1992 | 789.60 | 148543 | 12-09-1992 | 704.50 | 80631 | 13-09-1992 | 684.80 | 62797 |
| 1993 | 11-07-1993 | 789.60 | 130740 | 13-07-1993 | 706.70 | 128188 | 14-07-1993 | 687.20 | 91415 |
| 1994 | 21-07-1994 | 791.70 | 173090 | 22-07-1994 | 706.20 | 101791 | 22-07-1994 | 685.90 | 54101 |
| 1995 | 05-09-1995 | 790.70 | 220800 | 06-09-1995 | 709.80 | 257000 | 07-09-1995 | 690.60 | 171520 |
| 1996 | 23-08-1996 | 788.80 | 151080 | 25-08-1996 | 708.40 | 196080 | 25-08-1996 | 689.40 | 182340 |
| 1997 | 26-08-1997 | 789.00 | 157600 | 30-08-1997 | 707.70 | 159200 | 30-08-1997 | 687.71 | 123080 |
| 1998 | 24-09-1998 | 783.80 | 35820 | 24-09-1998 | 703.80 | 56940 | 24-09-1998 | 684.50 | 58200 |
| 1999 | 20-08-1999 | 782.70 | 23620 | 21-08-1999 | 703.70 | 45200 | 11-08-1999 | 683.30 | 45000 |
| 2000 | 28-07-2000 | 783.70 | 34480 | 29-07-2000 | 704.10 | 39760 | 29-07-2000 | 683.20 | 51775 |
| 2001 | 15-08-2001 | 784.50 | 46100 | 15-08-2001 | 704.00 | 44100 | 16-08-2001 | 682.90 | 41000 |
| 2002 | 14-08-2002 | 785.80 | 69480 | 15-08-2002 | 703.80 | 42140 | 15-08-2002 | 682.50 | 37000 |
| 2003 | 04-08-2003 | 784.60 | 45135 | 05-08-2003 | 703.60 | 39963 | 05-08-2003 | 682.40 | 38763 |
| 2004 | 18-08-2004 | 782.70 | 30631 | 19-08-2004 | 703.70 | 37600 | 09-08-2004 | 681.80 | 32680 |
| 2005 | 08-07-2005 | 784.00 | 40200 | 08-07-2005 | 702.80 | 30720 | 09-07-2005 | 681.30 | 29130 |
| 2006 | 28-07-2006 | 783.50 | 36435 | 28-07-2006 | 702.20 | 26880 | 28-07-2006 | 680.50 | 23575 |
| 2007 | 30-06-2007 | 782.50 | 29272 | 30-06-2007 | 703.40 | 35200 | 01-07-2007 | 681.50 | 30550 |
| 2008 | 17-08-2008 | 783.50 | 36435 | 17-08-2008 | 703.00 | 32000 | 18-08-2008 | 681.70 | 31970 |
| 2009 | 29-07-2009 | 781.20 | 10080 | 30-07-2009 | 701.70 | 23920 | 30-07-2009 | 680.30 | 22205 |
| 2010 | 22-08-2010 | 782.50 | 13375 | 22-8-2010 | 702.40 | 41216 | 22-8-2010 | 679.50 | 41900 |
| 2011 | 14-08-2011 | 782.70 | 14070 | 14-08-2011 | 702.5 | 42320 | 14-08-2011 | 679.5 | 41900 |
| 2012 | 21-08-2012 | 782.80 | 26000 | 22-08-2012 | 702.3 | 40000 | 22-08-2012 | 679.3 | 39660 |
| 2013 | 16-08-2013 | 787.00 | 67700 | 18-08-2013 | 705.20 | 73551 | 18-08-2013 | 682.40 | 74880 |
| 2014 | 07-09-2014 | 787.00 | 67700 | 08-09-2014 | 705.70 | 93250 | 08-09-2014 | 682.70 | 91400 |
| 2015 | 16-08-2015 | 783.90 | 36070 | 18-07-2015 | 701.60 | 31000 | 19-07-2015 | 679.40 | 30000 |
| 2016 | 27-07-2016 | 782.00 | 25250 | 29-07-2016 | 701.50 | 45081 | 29-07-2016 | 678.70 | 44595 |
| 2017 | 02-08-2017 | 784.00 | 38004 | 02-08-2017 | 701.00 | 39853 | 20-07-2017 | 677.80 | 36258 |
| 2018 | 25-09-2018 | 786.20 | 66641 | 15-08-2018 | 700.70 | 37936 | 15-08-2018 | 677.90 | 37587 |
| 2019 | 18-08-2019 | 785.10 | 51000 | 19-08-2019 | 701.20 | 37885 | 16-08-2019 | 676.50 | 33228 |
| 2020 | 28-08-2020 | 783.10 | 30690 | 26-08-2020 | 100.70 | 34531 | 28-08-2020 | 676.60 | 34486 |

CHAPTER – 5

FLOOD FIGHTING STRATEGY

Sub Divisional Officers and their staff would remain present and vigilant in the area round the clock during flood period. The flood information would be communicated by wireless, mobile phone or sent through special messenger employed for this purpose. In case of any emergency, the Sub Divisional Officer concerned would report the matter to the Executive Engineer, Lahore Drainage Division, Superintending Engineer, Lahore Drainage Circle, Chief Engineer, Irrigation Lahore Zone, Director Regulation, Chief Engineer, Drainage & Flood and Secretary Irrigation and Power Department, Punjab Lahore.

- LOW FLOOD LEVEL STRATEGY:- (40000 Cs to 65000 Cs)

On receipt of any flood warning, Sub Divisional Officer Flood Bund and Kasur Sub Division will make necessary arrangements. Sub Divisional Officer, Flood Bund and Sub Divisional Officer Kasur alongwith their field staff will camp at spur No.1 at RD.2300 of Shahdara Flood Protection Bund and at Shahpur Kanjran spur respectively. It will be ensured that to cater for any emergency ample machinery will be available at camps of Shahdara Protection Bund and Sharkpur Flood Protection Bund during flood season. It will ensure protective measures for any emergency situation arises due to freshest from nullahs and unexpected rainfall ever in the catchment of River Ravi. Duty roster and detail of camps along Mahmood Booti Bund, Lahore Protection Bund, Shahdara Flood Protection Bund, Shahpur Kanjran, Chung Spur, and Sharakpur Flood Protection Bund is available in Chapter-9 Page-30 & 31.

- MEDIUM FLOOD LEVEL STRATEGY:- (65000 Cs to 90000 Cs)

In case of medium Flood, if any erosion on any structure Flood fighting start with the help of establishment and Flood fighting material.

- HEIGH FLOOD LEVEL STRATEGY:- (90000 Cs to 135000 Cs)

In case of High Flood, necessary arrangements for evacuation of affected people will be carried out by the Civil and Military authorities and the Engineering staff will remain busy in watching and protecting of the Flood Protection Works. The Lahore Division CBDC, Lahore will act as backup division once emergency is declared. All other Departments will have their own arrangements to provide help to the needy persons.

CHAPTER – 6

FLOOD DAMAGES / RESTORATION WORKS

OCCURRED DURING FLOOD 2020

-------------------------------NIL-----------------------------------

CHAPTER – 7

FLOOD FIGHTING / WATCHING ARRANGEMENT

7.1	PRE-FLOOD ARRANAGEMENT

- Camping sites along the flood bunds at critical points will be declared and camps will be established over there.

- Required flood fighting / watching material will be procured.

- Procurement of stone to maintain the minimum limit of reserve stock will be ensured.

- Information regarding earth moving machinery available in the local market will be gathered.

- Site visits along with field formation to identify the most critical points and to develop consensus for course of action if such points / reaches become dangerous.

- Arrangements will be made for the installation of base wireless station and mobile wireless sets in Government vehicles.

- Total length of protection bunds will be divided into different beats and assigned duties of watching of flood protection works through gangs comprising regular and work charge establishment.

- Special funds application based on estimated amounts of emergent works will be submitted.

STONE POSITION						Qty in Lac Cft

| S.# | Section / Site | Bund / Spur | Reserved stock limit as per yard stick | Exists at site as per stock register | Balance required Stone Qty |
| --- | --- | --- | --- | --- | --- |
| 1 | Shahdara |  |  |  |  |
|  | i) | T-Spur No.1 | 1.000 | 0.0475 | 0.9525 |
|  | ii) | T-Spur No.2 | 1.000 | 0.241 | 0.759 |
|  | iii) | T-Spur No.3 | 1.000 | 0.175 | 0.825 |
|  | iv) | T-Spur No.4 | 1.000 | 0.1455 | 0.8545 |
|  | v) | Hockey Spur No.5 | 1.000 | 0.5909 | 0.4091 |
|  | Total:- |  | 5.000 | 1.1999 | 3.8001 |
| 2 | Qadirabad |  |  |  |  |
|  | i) | J-Spur Qadirabad | 1.000 | 0.2065 | 0.7935 |
|  | Total:- |  | 1.000 | 0.2065 | 0.7935 |
| 3 | Sharkpur |  |  |  |  |
|  | i) | J-Spur No.1 | 1.000 | 0.699 | 0.301 |
|  | ii) | T-Spur No.2 | 1.000 | 0.731 | 0.269 |
|  | iii) | Earthen Spur No.3 | 0.000 | (-) 0.329 | 0 |
|  | iv) | T-Spur No.4 | 1.000 | 0.209 | 0.791 |
|  | v) | J-Spur No.5 | 1.000 | 0 | 1.000 |
|  | Total:- |  | 4.000 | 1.639 | 2.361 |
| 4 | Mehmood Booti |  |  |  |  |
|  | i) | Hockey Spur | 1.000 | 0.129 | 0.871 |
|  | ii) | Sloping Spur | 0.500 | 0 | 0.500 |
|  | Total:- |  | 1.500 | 0.129 | 1.371 |
| 5 | Lahore Protection Bund |  |  |  |  |
|  | i) | J-Spur No.1 | 1.000 | 0.0287 | 0.9713 |
|  | ii) | J-Spur No.2 | 1.000 | 0.004 | 0.996 |
|  | iii) | J-Spur No.3 | 0.000 | (-) 0.106 | 0.000 |
|  | iv) | J-Spur No.4 | 1.000 | 0.718 | 0.282 |
|  | v) | T-Spur No.5 | 1.000 | 0.006 | 0.994 |
|  | Total:- |  | 4.000 | 0.7567 | 3.2433 |
|  |  | Tie Bund |  |  |  |
|  | i) | J-Spur No.1 | 1.000 | 0.000 | 1.000 |
|  | ii) | L-Spur | 0.500 | 0.000 | 0.500 |
|  | iii) | J-Spur No.2 | 1.000 | 0.000 | 1.000 |
|  | Total:- |  | 2.500 | 0.000 | 2.500 |
| 6 | Niaz Baig |  |  |  |  |
|  | i) | Shahpur Kanjran | 1.000 | 0.219 | 0.781 |
|  | ii) | Mole & J-spur Chung | 1.000 | 0.645 | 0.355 |
|  | Total:- |  | 2.000 | 0.864 | 1.136 |
|  | G.Total:- |  | 20.000 | 4.795 | 15.205 |

* The Factual situation of existing stone is already reported vide Executive Engineer Lahore Drainage Division Lahore No, 127/17-A Dated 22-02-2018.

7.2	WATCHING ESTABLISHMENT

| S.# | Particulars | Period | Coolies | Mates | Vulnerable Points | Extra Collies for Vulnerable Points |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | No of beats | No of Collies per beat* | No of shifts | Total No of Collies | No of mates per beat | No of shift | Total No of mates |  |  |
|  |  |  |  |  |  |  |  |  |  |  | Coolies | Mates |
| 1 | Normal days of floods | 1st June To 15th October | 20 | 4 | 1 | 80 | 1 | 1 | 20 | 4 | 20 | 5 |
| 2 | Low Flood at Jassar 45000-75000 Cs | -do- | 20 | 8 | 2 | 320 | 1 | 2 | 40 | 4 | 60 | 5 |
| 3 | Medium flood at Jassar 75000-100000 | -do- | 20 | 8 | 3 | 480 | 1 | 2 | 120 | 8 | 120 | 10 |
| 4 | High Flood at Jassar 100000-150000 Cs | -do- | 20 | 10 | 3 | 600 | 2 | 3 | 120 | 8 | 120 | 10 |
| 5 | Very High Flood at Jassar 150000-200000 Cs | -do- | 20 | 15 | 3 | 900 | 2 | 3 | 120 | 10 | 150 | 15 |
| 6 | Exceptionally high flood at Jassar 200000 above | -do- | 20 | 20 | 3 | 1200 | 3 | 3 | 180 | 15 | 300 | 30 |
|  |  | *1 beat = 10 RDs = 10000 ft |  |  |  |  |  |  |  |  |
|  |  |  | ADDITIONAL ESTABLISHMENT |  |  |  |  |  |
|  |  |  | 1) Chowkidar day and night | (2No per beat) = 2x20 = 40 No |  |  |
|  |  |  | 2) Gauge reader 3 shift | (1 No per shift)= 3x4 = 12 No |  |  |
|  |  |  | 3) Telephone attendant |  | (1 No per shift)= 3x4 = 12 No |  |  |
|  | Justification: | Work charge establishment is needed in addition to regular establishment to combat the flood situation (shift duties). Therefore work charged watching establishment has been provided as per previous criteria. |  |

7.3	ARRANGEMENT AT SENSITIVE SITES

Shahdara Flood Bund is the sensitive site due to breaching section close to it. Flood watching / fighting camp is provided over there with all logistics.

7.4	WATCHING MATERIAL

Total Quantity required against available quantity of different flood fighting / watching material for all flood fighting camps including sensitive sites are as below:-

| S.# | Item | Unit | Total Quantity required | Quantity Available | Balance Quantity required | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Kassies / Belchas | No | 80 | 80 | - | Preparation of Estimate is under process and balance required material will be procured after due tendering process |
| 2 | handle of Kassies | No | 80 | 70 | 10 |  |
| 3 | Toot Baskets | No | 265 | 160 | 105 |  |
| 4 | Torches chargeable | No | 600 | - | 600 |  |
| 5 | Torches (3- cell) | No | 39 | 39 | - |  |
| 6 | Dry Cell | Dozen | 19 | 19 | - |  |
| 7 | Bulb for Torches | No | 6 | 6 | - |  |
| 8 | Axes | No | 10 | 8 | 2 |  |
| 9 | Handle for axe | No | 50 | 5 | 45 |  |
| 10 | Generator | No | 2 | 1 | 1 |  |
| 11 | Electric wire 3/29 s/c | Coil | 9 | 3 | 6 |  |
| 12 | Electric wire 7/29 s/c | Coil | 3 | 3 | - |  |
| 13 | Insulation tape | No | 18 | 0 | 18 |  |
| 14 | Bulb Holder | No | 85 | 85 | - |  |
| 15 | Shouldaries | No | 10 | 4 | 6 |  |
| 16 | Swiss cottage tent | No | 1 | 1 | - |  |
| 17 | Darries | No | 10 | 7 | 3 |  |
| 18 | Camp chair | No | 36 | 24 | 12 |  |
| 19 | camp Table | No | 5 | 4 | 1 |  |
| 20 | Buckets G.I | No | 80 | 50 | 30 |  |
| 21 | Suttly Seiba | Bundle | 5 | 1 | 4 |  |
| 22 | Life Jacket | No | 18 | 12 | 6 | Preparation of Estimate is under process and balance required material will be procured after due tendering process |
| 23 | Sounding Rod | No | 4 | 1 | 3 |  |
| 24 | Long rubber shoes | Pair | 22 | 22 | - |  |
| 25 | Emergency Lights | No | 14 | - | 14 |  |
| 26 | Nylon Bags | No | 7000 | 7000 | - |  |
| 27 | U-clamp 5/8” dia | No | 100 | 100 | - |  |
| 28 | U-clamp 1/2” dia | No | 60 | 50 | 10 |  |
| 29 | Water cooler | No | 8 | - | 8 |  |
| 30 | Hand Umbrella | No | 5 | - | 5 |  |
| 31 | Measuring tape 100’ | No | 5 | 5 | - |  |
| 32 | Manila rope | Rft | 200 | 200 | - |  |
| 33 | Steel wire rope 1/2” dia | Rft | 3000 | 200 | 2800 |  |
| 34 | Fiber glass boat | No | 2 | 1 | 1 |  |
| 35 | Bamboo 2 ½” dia 8-10 ft long with one end sharp | No | 1000 | 20 | 980 |  |
| 36 | Digital Camera | No | 3 | - | 3 |  |
| 37 | G.I.Wire Crates | No | 58 | 58 | - |  |
| 38 | Hammer Heavy | No | 5 | 3 | 2 |  |
| 39 | Wrench | No | 7 | 3 | 4 |  |
| 40 | Pliers | No | 6 | 3 | 3 |  |
| 41 | Umbrella 10’ | No | 1 | 0 | 1 |  |
| 42 | Gas lamp | No | 6 | 6 | - |  |
| 43 | Lantern | No | 50 | 50 | - |  |
| 44 | Energy Saver 45w | No | 100 | - | 100 |  |
| 45 | Jute bags | No | 2000 | 2000 | - |  |
| 46 | Electric Bulb 100 W | No | 100 | 70 | 30 |  |
| 47 | Electric Bulb 500 W | No | 50 | 40 | 10 |  |
| 48 | Electric Switch | No | 60 | 60 | - |  |
| 49 | Geo synthetic bags 500 kg | No | 5000 |  | 5000 |  |
| 50 | Geo Synthetic Bags 1000 kg | No | 5000 | - | 5000 |  |
| 51 | Geo Sheet | Rft | 15000 | - | 15000 |  |
| 52 | Pegs | No | 500 | - | 500 |  |
| 53 | Charpaye Iron | No | 25 | - | 25 |  |
| 54 | Search Light | No | 12 | - | 12 |  |
| 55 | Petrol chain saw | No | 6 | - | 6 |  |
| 56 | Digital video camera | No | 2 | - | 2 |  |
| 57 | Fiber Glass Boat with Petrol engine | No | 2 | - | 2 |  |

Flood Fighting Material required on Flood Bunds (except vulnerable sites)

| S.# | Item | Unit | Quantity required | Quantity Available | Balance Quantity required | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Kassies / Belchas | No | 20 | 20 | - | Preparation of Estimate is under process and balance required material will be procured after due tendering process |
| 2 | handle of Kassies | No | 60 | 50 | 10 |  |
| 3 | Toot Baskets | No | 130 | 25 | 105 |  |
| 4 | Torches chargeable | No | 600 | - | 600 |  |
| 5 | Torches (3- cell) | No | 14 | 14 | - |  |
| 6 | Dry Cell | Dozen | 11 | 11 | - |  |
| 7 | Bulb for Torches | No | 4 | 4 | - |  |
| 8 | Axes | No | 2 | - | 2 |  |
| 9 | Handle for axe | No | 45 | - | 45 |  |
| 10 | Generator | No | 1 | - | 1 |  |
| 11 | Electric wire 3/29 s/c | Coil | 7 | 1 | 6 |  |
| 12 | Electric wire 7/29 s/c | Coil | 3 | 3 | - |  |
| 13 | Insulation tape | No | 6 | - | 6 |  |
| 14 | Bulb Holder | No | 30 | 30 | - |  |
| 15 | Shouldaries | No | 8 | 2 | 6 |  |
| 16 | Swiss cottage tent | No | 1 | 1 | - |  |
| 17 | Darries | No | 3 | - | 3 |  |
| 18 | Camp chair | No | 24 | 12 | 12 |  |
| 19 | camp Table | No | 3 | 1 | 1 |  |
| 20 | Buckets G.I | No | 35 | 5 | 30 |  |
| 21 | Suttly Seiba | Bundle | 5 | 1 | 4 |  |
| 22 | Life Jacket | No | 6 | - | 6 |  |
| 23 | Sounding Rod | No | 3 | - | 3 |  |
| 24 | Long rubber shoes | Pair | 6 | 6 | - |  |
| 25 | Emergency Lights | No | 9 | - | 9 |  |
| 26 | Nylon Bags | No | 5000 | 5000 | - |  |
| 27 | U-clamp 5/8” dia | No | - | - | - |  |
| 28 | U-clamp 1/2” dia | No | 10 | - | 10 |  |
| 29 | Water cooler | No | 4 | - | 4 |  |
| 30 | Hand Umbrella | No | 4 | - | 4 |  |
| 31 | Measuring tape 100’ | No | 1 | 1 | - | Preparation of Estimate is under process and balance required material will be procured after due tendering process |
| 32 | Manila rope | Rft | 200 | 200 | - |  |
| 33 | Steel wire rope 1/2” dia | Rft | 2800 | - | 2800 |  |
| 34 | Fiber glass boat | No | 1 | - | 1 |  |
| 35 | Bamboo 2 ½” dia 8-10 ft long with one end sharp | No | 980 | - | 980 |  |
| 36 | Digital Camera | No | 2 | - | 2 |  |
| 37 | G.I.Wire Crates | No | 58 | 58 | - |  |
| 38 | Hammer Heavy | No | 5 | 3 | 2 |  |
| 39 | Wrench | No | 5 | 1 | 4 |  |
| 40 | Pliers | No | 4 | 3 | 1 |  |
| 41 | Umbrella 10’ | No | 1 | 0 | 1 |  |
| 42 | Gas lamp | No | - | - | - |  |
| 43 | Lantern | No | 45 | 45 | - |  |
| 44 | Energy Saver 45w | No | 100 | - | 100 |  |
| 45 | Jute bags | No | 2000 | 2000 | - |  |
| 46 | Electric Bulb 100 W | No | 100 | 70 | 30 |  |
| 47 | Electric Bulb 500 W | No | 50 | 40 | 10 |  |
| 48 | Electric Switch | No | 60 | 60 | - |  |
| 49 | Geo synthetic bags 500 kg | No | 5000 |  | 5000 |  |
| 50 | Geo Synthetic Bags 1000 kg | No | 5000 | - | 5000 |  |
| 51 | Geo Sheet | Rft | 15000 | - | 15000 |  |
| 52 | Pegs | No | 500 | - | 500 |  |
| 53 | Charpaye Iron | No | 25 | - | 25 |  |
| 54 | Search Light | No | 12 | - | 12 |  |
| 55 | Petrol chain saw | No | 6 | - | 6 |  |
| 56 | Digital video camera | No | 2 | - | 2 |  |
| 57 | Fiber Glass Boat with Petrol engine | No | 2 | - | 2 |  |

7.5	ARRANGEMENT FOR SOUNDING & PROBING

It is available at Shahdara Flood Watching Camp at RD.2300 of Shahdara Flood Protection Bund.

7.6	LIGHTING ARRANGEMENT

Two Nos of generators with the capacity of 2 KVA each, are available in case of non-availability or failure of electricity at Shahdara Flood Watching Camp at RD.2300.

7.7	RATION ARRANGEMENT

Ration would be made available at site as per Government policy.

7.8	POL ARRANGEMENT FOR VEHICLES

POL for vehicle will be made available from existing funds under the head of POL. In case of any shortage of funds in POL. The expenditure shall be met with embankment funds to cater for emergency.

7.9	TRANSPORTATION

All Government vehicles are in good running condition to perform flood duty.

7.10	LAW AND ORDER

It is the responsibility of local police. Close contact / liaison will be ensured with the civil administration.

7.11	MEDICAL ARRANGEMENT FOR LABOUR

First Aid / medicine boxes would be arranged at site by the Health Department along with other measures.

7.12	LIAISON WITH OTHER DEPARTMENTS

It would be ensured telephonically through official land line and private mobile numbers. The department liaison officer will be notified before the coming flood season.

7.13	ROLE OF THE ARMY

Besides arrangements of watching staff by Irrigation Department, additional volunteers will be requisitioned if needed from the army on special request. They will also take position for the rescue of the persons and live stock of flood affected areas on request of the Department.

7.14	DUTIES OF TELEPHONE ATTENDANT

He will record daily discharges at various control points and convey important information and messages etc 24 hours during flood season.

7.15	WIRELESS ARRANGEMENTS

Mobile wireless in Government vehicles would be installed during flood season. The requisition in this regard will be initiated.

CHAPTER – 8

DETAIL OF ENCROACHMENTS

There are encroachments inside the river along right as well as left side of River. On the left bank of the river Ravi, encroachments have developed inside the flood bunds all along the Mahmood Booti Bund and the Lahore Protection Bund. The workshops and small factories have developed along-with pacca houses within the river training works, which would create an alarming situation in case a medium flood passes downstream of Ravi Syphon. Other departments have provided facilities of electricity, telephone and sewerage to the inhabitants within the bunds area making things bad to worse. The list of Encroachment has already been circulated to Civil Administration to help the Department to remove these encroachments. The detail of encroachment including its type i.e. houses, shops and factories etc is attached herewith on next pages.

ENCROACHMENT ON BUNDS AND SPURS

| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| --- | --- | --- | --- |
| 1 | Nazir Ahmad, Haji Riaz and Sadiq Changhar etc | Spur No.4 at RD.2500 to 4000 | Illegal laying of sewer pipe in the toe of spur |
| 2 | Malik Asad. | T spur No.4 of Lahore Protection bund RD.4000 | illegal cutting of ramps / pitching |
| 3 | Unknow | T spur No.4 & 5 of Lahore Protection bund | illegal construction of Truck stand for goods |
| 4 | Unknow | T spur No.1 Mohammadia colony Gaoshala | illegal construction of Truck stand for goods |
| 5 | Nizami Motors | Spur No.1 at RD.1490 head Lahore Protection Bund | illegal construction of Truck stand for goods |
| 6 | Tanveer Tahir | Sharkpur Flood Protection Bund/T Spur No 4 R.D 26+860 | Illegal construction of Tubewel on head. |
| 7 | Contractor of Mineral Department. | Lahore Protection Bund between Spur No 4 & 5 | Illegal sand mining. |
| 8 | Contractor of Mineral Department. | Lahore Protection Bund between saggian and motorway bridges | Illegal construction of bunds for sand mining. |
| 9 | Malik Talib & Malik Alam | Spur No.5 Lahore Protection Bund R.D 5500 Head | Illegal water pump. |
| 10 | Malik Asad. | Spur No. 4 Lahore Protection Bund R.D 3400/L | Illegal construction |
| 11 | Malik Tahir. | Spur No 4Lahore Protection Bund R.D 3500/L | Illegal construction |
| 12 | Local Zamindars | Sharakpur Flood Protection Bund & its allied spurs. | Illegal cutting of ramps |
| 13 | Contractor of Mineral Department. | Shahdara Flood Protection Bund Spur No 4 . | Illegal cutting of ramps for sand carriage. |
| 14 | Malik Tahir & others. | Shahdara Flood Protection Bund Spur No 4 R.D 0-1 | Illegal cutting of ramps for sand carriage |
| 15 | Malik Tahir | Spur No 2 of shahdra Flood Protection Bund T-head | Illegal obstruction of Bund |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 16 | Malik Safdar | Spur No 5 of Lahore Protection Bund RD 4+000-4600 | Illegal laying of sewer |
| 17 | Malik Alam | Spur No 5 of Lahore Protection Bund RD 5+000 L/S | Excavation of earth/sand |
| 18 | Malik Alam | Spur No 5 of Lahore Protection Bund RD 5+000 R/S | Storage of sand |
| 19 | Abid Hussain | Spur No 5 of Lahore Protection Bund RD 5+000 L/S | Illegal installation of water pump & khurli |
| 20 | Haji Mustafa/Dr Shaheen | Spur No 5 of Lahore Protection Bund RD 2+000 R/S | Illegal Construction of Dera & house |
| 21 | Mohammad Arshad | Spur No 5 of Lahore Protection Bund RD 3+000 R/S | Illegal Construction of boundary wall |
| 22 | Haji Mohammad Ali | Spur No 5 of Lahore Protection Bund RD 5+000 R/S | Illegal Construction of wall & house |
| 23 | Ashfaq | Spur No 5 of Lahore Protection Bund RD 2+000 L/S | Illegal Construction of hotel |
| 24 | Unknown | Spur No 5 of Lahore Protection Bund RD 1+000 R/S | Illegal Construction of hotel |
| 25 | Asim Raza | Spur No 5 of Lahore Protection Bund RD 1+000 L/S | Illegal Construction of hotel |
| 26 | Rana Mohammad Iqbal | Spur No 5 of Lahore Protection Bund RD 4+500 | Illegal storage of Glass & garbage |
| 27 | Mohammad Nawaz | Spur No 5 of Lahore Protection Bund RD 3+500 L/S | Illegal storage of material |
| 28 | Mineral Department | Between Spur No 4 & 5 of Lahore Protection Bund RD 5+000 | Exeavation of earth/sand |
| 29 | Mehar Akhtar | Spur No 1 of Lahore Protection Bund RD 1+000 | Illegal Construction of boundary wall |
| 30 | Sufi Mohammad | Spur No 1 of Lahore Protection Bund RD 1+000 | Illegal Construction of hotel |
| 31 | Haji Mushtaq | Spur No 1 of Lahore Protection Bund RD 0+500 | Illegal Construction goods stand |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 32 | Muhammad jamil | Spur No 1 of Lahore Protection Bund RD 0+500 | Illegal Construction of boundary wall |
| 33 | Mian Abbas | Spur No 1 of Lahore Protection Bund RD 0+500 | Illegal Construction/Occupation of Govt land |
| 34 | Malik Farhat Abbas | Lahore Flood Protection Bund spur No.J-2 (Tie Bund) R.D 4+000 R/S | Illegal exeavation of earth from Govt Land |
| 35 | Unknown Persons | Spurs of Shahdara Flood Protection Bund | Illegal Making way for Tractor Trollies. |
| 36 | Shafat Ali, Ch: Karamat, Muhammad Munir, Muhammad Javwed and Others. | Shahdara Flood Protection Main Bund & spurs | Illegal Construction of Ramp by cutting Bund/Slops |
| 37 | Unknown Persons | Saggian Bridge River Ravi / R | Illegal Construction of Bund Near Sagian Bridge. |
| 38 | Muhammad Azhar | Lahore Flood Protection Bund Spur No.4 RD.1000/L | Illegal instalation of Sewarage Pipe top of Bund. |
| 39 | Muhammad Naeem | Lahore Flood Protection Bund Spur No.5 RD.2500/L | Illegal Construction of House. |
| 40 | Mohammad Ramzan S/O Kasam Gujjar | Lahore Flood Protection Bund Spur No.2 RD.3500/R, Spur No1 RD.1500/L | Obstruction on bund for catteles |
| 41 | Jamshad Iqbal | Lahore Flood Protection Bund Spur No.2 (Head Portion) | Damaged Pusta No.2 |
| 42 | Unknown Persons | Shahdara Flood Protection Bund spur No.5 RD.9500 | Illegal Cultivation of Govt. Land/cuts of slope/Bund. |
| 43 | Dad Muhammad Khan | Lahore Flood Protection Bund Spur No.5 RD.750/R | Illegal Occupation/Construction. |
| 44 | Jamshad Bao | Lahore Flood Protection Bund Spur No.2 RD.2800/R | Illegal Construction of Ramp on spur No.2. |
| 45 | Bodha Gujjar, Mushtaq Gujjar etc. | Lahore Flood Protection Bund Spur No.4 RD.2900-3000 | Illegal occupation of Govt: Land. |
| 46 | Mineral Department | Right Bank of River Ravi Downstream Saggian Bridge | Illegal obstruction of river bed |
| 47 | Unknown | Lahore Flood Protection Bund Spur No.5 RD.4500/L | Illegal Construction |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 48 | Unknown | Lahore Flood Protection Bund Spur No.5 RD.2500/R | Illegal Construction |
| 49 | Mohammad Majed,Abdul Rasheed | Shahdara Flood Protection Bund RD.4-5/L | Illegal Construction of Room |
| 50 | Mian Goga,wali Mohammad,abbas Khan Jaffar,Mohammad Maqbool,SyedIftikhar Shah, Allha Ditta,Mohammad Shari,Malik Zaheer,Mohammad Younis,Mohammad Zaka,lal Hussain,Malik Mohammad Akram,Mohammad Basheer(D/S of siggian bridge)Billa Khan,jaan Gul khan,Rehman khan,Fiaz,chand khan,Amanat khan,Ahmad shah khan,Dogar,Ghulam Rasool,Arif,Babar Bhatti,Haji Khizar,Malik Nawaz,Hakim Ali,Malik Sarwar,Sajjad(U/S of siggian Bridge) | Lahore Flood Protection Bund Downstream Saggian Bridge | Illegal Construction |
| 51 | Mian Goga,wali Mohammad,abbas Khan Jaffar,Mohammad Maqbool,SyedIftikhar Shah, Allha Ditta,Mohammad Shari,Malik Zaheer,Mohammad Younis,Mohammad Zaka,lal Hussain,Malik Mohammad Akram,Mohammad Basheer | Lahore Flood Protection Bund Downstream Saggian Bridge | Illegal Construction |
| 52 | Mohammad Akbar,Kala Mistry,Munshi khan,lal khan,Mohammad Rafique,Mohammad Hussain,Jaffar Hussain,Aziz khan,zafar khan,shan khan,Labha | Lahore Flood Protection Bund Spur No.5 R.D 0+000 To 3+000 | Illegal obstruction of Bund |
| 53 | Haji Nazir | Lahore Flood Protection Bund Spur No.1 R.D 1+000 R/S | Illegal Construction |
| 54 | Shoukat Ali | Lahore Flood Protection Bund Spur No.4 R.D 0+300 R/S | Illegal Construction |
| 55 | Mohammad Mushtaq | Lahore Flood Protection Bund Spur No.5 R.D 4+500 | Illegal Construction |
| 56 | Munir jutt,Mubarak jutt | Lahore Flood Protection Bund spur No.J-2 (Tie Bund)R.D 4+500 | Illegal occupation of Govt Quarter |
| 57 | Abdul Sattar khan | Lahore Flood Protection Bund spur No.J-2 (Tie Bund) R.D 4+500 | Illegal occupation of Govt Quarter |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 58 | Unknown | Lahore Flood Protection Bund Downstream Saggian Bridge | Illegal Bund |
| 59 | Billa,Arshad,Sharif,Mian jawed,Mairaj Din,Labha Gujjar ,noni, Kanwar Din Nadeem ,Afzal,Chiragh,Irfan,Saleem,Manaha,Bahadar ,Goga ,Muhamad Rafiqe,Bashir,Javed,Amanat Ali,Muhammad Asif,Haji muhammad Sharif,Muhammad Ramzan,Umar,Jajhi,Inyat ,Muhammad Younas,Muhammad Sadiq, Asghar Ali,Muhammad Aslim ,Malik Akbar,Mlik kala,Malik Liaqat Ali,Bagha,Mian Javed,Mian Iqbal,Mairge Din,Babar ,Amjad,Riasat,,Sohny,Amjad,Shahbaz,Goga,Malik Ramzan,Jajah Shah,Sadiq,Riaz,Bashir,Lal Din Dar,Muhammad Sharif,Muhammad Latif ,Liaqat Ali,.Ibrahim,Haji Sajid,Haji Qadir,Muhammad Rafiq,mUHAMMAD hANIF Haji yasseen,Mubarak Ali,Malik Asharaf,Abdulghafoor,Muhammad Rafiq,Haji Taj,Noor Muhammad, Malik Jamil,Muhammad Latif,Safdar Ali,Sher Muhammad,Malik Shakeel,CH Hayat,Niamat Ali, | Shahdara Flood Protection Bund RD.0-10000 | Illegal Construction/Occupation of Shahdara Flood Protection Bund |
| 60 | Billa,Arshad,Sharif,Mian jawed,Mairaj Din,Labha Gujjar ,noni, Kanwar Din Nadeem ,Afzal,Chiragh,Irfan,Saleem,Manaha,Bahadar ,Goga ,Muhamad Rafiqe,Bashir,Javed,Amanat Ali,Muhammad Asif,Haji muhammad Sharif,Muhammad Ramzan,Umar,Jajhi,Inyat ,Muhammad Younas,Muhammad Sadiq, Asghar Ali,Muhammad Aslim ,Malik Akbar,Mlik kala,Malik Liaqat Ali,Bagha,Mian Javed,Mian Iqbal,Mairge Din,Babar ,Amjad,Riasat,,Sohny,Amjad,Shahbaz,Goga,Malik Ramzan,Jajah Shah,Sadiq,Riaz,Bashir,Lal Din Dar,Muhammad Sharif,Muhammad Latif ,Liaqat Ali,.Ibrahim,Haji Sajid,Haji Qadir,Muhammad Rafiq,mUHAMMAD hANIF Haji yasseen,Mubarak Ali,Malik Asharaf,Abdulghafoor,Muhammad Rafiq,Haji Taj,Noor Muhammad, Malik Jamil,Muhammad Latif,Safdar Ali,Sher Muhammad,Malik Shakeel,CH Hayat,Niamat Ali, | Shahdara Flood Protection Bund RD.0-10000 | Illegal Construction/Occupation of Govt land |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 61 | Mohammad Shoukat, Mohammad Ashraf,haji Munir,kala gujjar,patthan taal wala,Mughal Sb,Mohammad Siddque,Sher Khan,Bhatti,Sh.Ahmad Din,Malik Brothers,Nadeem,pehlwan hotel wala, jaffar Khan,Allah Tawakal Building store, Moulvi Sardar,Rana Mohammad Iqbal,Malik Khadam. | Lahore Flood Protection Bund Spur No.5 RD 0+000 to 4+000 | Illegal Construction/Occupation of Govt land |
| 62 | Malik Akhtar,Mehar Sadiq,Nadeem,Malik Aslam,Iftikahr,Jabbar,Haji Mill wala,Nazir,Riasat,Bao Gujjar,Bao tali,Ch Khadam,Bao Ghaman,Haji Arshad,Dilshad Ghaman,Munir Shoping Baig,Abdullah,Abdullah,Aslam,Umer Hayat,Siddique,Basheer,Haji Billa Gujjar,Amin,Ashraf,Maqsood,Ashraf Gujjar,Shafaq,Ilyas Gujjar,Abbas Gujjar,Adress,Ch labbaha Bajwa,Haji Acid Fectory. | Mehmood Booti Bund RD.0-29300 R.D 0+000 -1+000 &2+000- 2+800 | Illegal construction on slopes of spur |
| 63 | Baba Anyat Ali | Lahore Flood Protection Bund spur No.J-2 (Tie Bund) R.D 4+500 | Illegal occupation of Govt Quarter |
| 64 | Mohammad Sharif | Shahdara Flood Protection Bund RD.11000-11500 | Illegal construction of wall |
| 65 | Mohammad Sharif | Shahdara Flood Protection Bund RD.11000-11500 | Illegal construction of wall |
| 66 | Mohammad Sharif | Shahdara Flood Protection Bund RD.11000-11500 | Illegal construction of wall |
| 67 | Malik Shoukat Ali | Lahore Flood Protection Bund Spur No.5 R.D 2+500 R/S | Illegal occupation of Govt Land |
| 68 | Mohammad Sharif | Shahdara Flood Protection Bund RD.11000-11500 | Illegal construction of wall for fectory |
| 69 | Mohammad Nazir Mehar | Lahore Flood Protection Bund Spur No.5 R.D 1+600 | Illegal occupation of Govt Land |
| 70 | Mr Jaffar Khan | Lahore Flood Protection Bund Spur No.5 R.D 2+100 | Illegal occupation of Govt Land |
| 71 | Nazir Ahmad | Lahore Flood Protection Bund Spur No.5 R.D 4+000 | Illegal occupation of Govt Land |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 72 | Asif Material store & Rana Mohammad Iqbal | Lahore Flood Protection Bund Spur No.5 R.D 3+000 | Illegal occupation of Govt Land |
| 73 | Abdul Aziz Khan | Lahore Flood Protection Bund Spur No.5 R.D 2+500 R/S | Illegal construction of wooden tall |
| 74 | Mohammad Ali Gujjar,Baba Munir Hussain,Haji Mohammad Anwar,Malik Mohanmmad Tufail,Sh Tariq,Mohammad Ashraf,Dr Zulfiqar,Wasa,Mohammad Farooq Gujjar,Mohammad Amin,Ch Khadam ali,Abdul khalid/Mohammad Arif,abbas Khan,Gujjar Khan,Nawaz Khan,Malik Waseem/Malik Sajjad,Malik Nawaz,Mohammad Aslam Sial,Tahira Firdous,Saeed Butt,Chacha Jawed,Mohammad Saeed Bhindhar,Mohammad Baseer,Mian Sajjad,Bao Saleem,Ruby Oil,Mian Raees,Munawar hasan,Meero Khan,Mohammd Nawaz,Haji Abdul Rauf,Malik Shezad,Haji Sher Afzal,Wasa,Malik Aman-ul-llah,Mehar Umer Saeed,Haji Ghulam Nabi,Mohammad Asghar Khan,Haji Ahmad Ali,Haji Mohammad Arshad,Khalid Mehmood,Mohammad Latif,Haji Mohammad Rafique,Mohammad Nawaz/Momin Khan,Malik Abbas,Bagha,Zafar Khan,Shamim Bashrat,Haji Mohammd Ayub,Zaheer Sb,Rana Basheer Ahmad,Grave Yard,Mehar Jagheer,Jammal,Mian Riaz/Abdul Rehman,Mian Tariq,Azam Gujjar,Masood Steel industry,Anyat Pipe industry,Mian Liaqat Pak Eastern Engineering,Ashfaq,Mumtaz Filling Station,Abdul Majeed,Mohammad Ghafoor/Mohammad Munzoor,Mohammad Shafique,Haji Mohammad Anees,Mohammad Ibrar,Mohammad Yousuf,Haji Habib,Mohammad Saleem,Fiaz Steel Fectory,Haji Ayub Shah,Sh Irfan,Haji Umer,Mian Naveed,Haji Mohammad Latif,Mohammad Khalid/Mohammad Sajjad,Mian Shehbaz/Mian Arif,Haji Morad,Sewrage Station,Muncipal Land,Inam Butt,Tubewell Wasa No 5,Mohammad Tufail,Muzafar Brothers,Waheed Bhatti,Tubewell wasa No 4,Mohammad Ayub,Tubewell wasa No 1,Iftikhar Ahmad,Mohammad Yaqoob,Mohammad Jahanghir,Mohammad Jamil,Mohammad Waheed,Mohammad Akram, | Mehmood Booti Bund RD.0-29+300 | Sr # 1-40 illegal Construction of house,dera,oil store,hotel,tubewell,shop,house,store pipe,godown fectory,markets,oil store,press fectory Sr # 14-74 Illegal construction of sewrege drain by wasa,house,oil store,brick depot,wooden store,pipe fectory,machinry godwen,nurcery,hotel,workshop,grave yard,steel fectory,plot foundation,Sr # 75-83 Illegal construction of fectories,steel industries,petrol pump,markets,pipe ,residential house,girder fectory,oil store,estate agency,Sr # 100-117 sewerage drain,umraha office,residential houses, |
| S.# | Name of Encroacher | Location Bund / Spur (Pushta) R.D | Nature Of Encroachment |
| 75 | Mohammad Basheer | Lahore Flood Protection Bund Spur No.5 | Illegal occupation of Govt Land |
| 76 | Mohammad Shoukat, Mohammad Ashraf,haji Munir,kala gujjar,patthan taal wala,Mughal Sb,Mohammad Siddque,Sher Khan,Bhatti,Sh.Ahmad Din,Malik Brothers,Nadeem,pehlwan hotel wala, jaffar Khan,Allah Tawakal Building store, Moulvi Sardar,Rana Mohammad Iqbal,Malik Khadam. | Lahore Flood Protection Bund Spur No.5 | Sr # 1-3 Hotel,workshop,wooden tall,Sr # 5-9 Building material wooden tall grocery store Sr # 10-22 Building material,Boring house,paan shop,weight machine and cattle fooder,building store,hotel,Plastic shop,Sr # 23-25 estate agency,stock of stone |
| 77 | Mohammad safdar | Lahore Flood Protection Bund Spur No.5 | Illegal construction of road for tractor trollies |
| 78 | Mohammad Jamsheed | Lahore Flood Protection Bund Spur No.5 R.D 4+000 | Illegal occupation of Govt Land |
| 79 | Gamma Gujjar,Hanif Gujjar,Bodha Gujjar | Lahore Flood Protection Bund Spur No.4 | Cattle form |
| 80 | Mohammad Shiukat,Mohammad Ashraf,Haji Munir,Kala Gujjar,Pathan Taal Wala Mughal,Mohammad Siddique,Sher Khan,Bhatti,Sh:Ahmed Din,Malik Brothers,Nadeem Pehlawan Hotel Wala,Jaffer Khan Allah tawaakal Building store,Molvi Sardar,Rana Mohammad Iqbal,Malik Khadam. | Lahore Flood Protection Bund Spur No.5 | Sr # 1-3 Hotel, workshop, wooden tall,Sr # 5-9 Building material wooden tall grocery store Sr # 10-22 Building material, Boring house, paan shop, weight machine and cattle fooder, building store, hotel, Plastic shop,Sr # 23-25 estate agency, stock of stone |
| 81 | Mohammad Bashir | Lahore Flood Protection Bund Spur No.5 | Illegal occupation of Govt Land |
| 82 | Mohammad Jamshed | Lahore Flood Protection Bund Spur No.5 R.D 4+000 R/S | Illegal Construction of wall By cutting spur slope 5' |
| 83 | Muhammad Abass | Lahore Flood Protection Bund Spur No.5 | Illegal Construction of wall in spur lands about 15’ wide. |

| S.# | Total Encroachment | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| 1 | 93 | 10 | 83 | Written to District Administration |

Critical Encroachments

| S.# | Total Encroachment | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| 1 | - | - | - | - |

CHAPTER – 9

DUTY ROSTER BATTLE STATIONS OF KEY PERSONNEL DURING HIGH FLOOD FLOW

| S.# | Designation | Camping Station | Duty |
| --- | --- | --- | --- |
| 1. | Executive Engineer, Lahore Drainage Division, Lahore. | At XEN Office Lahore Mustafabad Lahore Ph: No.042-99250327 | He will be the overall in charge of Lahore Drainage Division and will keep close contact with his staff and District Administration. He will also act as per flood situation keeping liaison with all concerned Departments related with flood activities. |
| 2. | Sub Divisional Officer, Flood Bund Sub Division, Lahore. | At Shahdara Hut No.1 RD.2300, of Shahdara Flood Protection Bund. | To monitor flood situation in River Ravi and keep watch on flood protection / River Training works of Shahdara, Mahmood Booti, Qadirabad and Lahore Protection section |
| 3. | Sub Divisional Officer, Kasur Drainage Sub Division, Lahore. | Shahpur Kanjran spur. | To monitor flood situation in River Ravi and keep watch on flood protection / River Training works in Niaz Baig section. |

DUTY ROSTER / FLOOD FIGHTING PROGRAMME

The section wise breakup of the bunds / spurs is given below:-

| Sr.# | Sub Engineer Section | Reach | Sub Division | Head quarter of Sub Engineer and location of stacking site of material. |
| --- | --- | --- | --- | --- |
| 1. | Mahmood Booti Section | Mahmood Booti Bund RD.0-29000 with spurs. | Flood Bund Sub Division, Lahore. | Remain Present in his Jurisdiction or where needed as defined by SDO. |
| 2. | Lahore Protection Bund Section | Lahore Protection Bund RD.0-23000 and spurs. Tie bund R.D 0-20000 and spurs. | -do- | Remain Present in his Jurisdiction or where needed as define by SDO |
| 3. | Shahdara Section | Shahdara Flood Protection Bund and spurs. | -do- | Camp at Hut No.1 RD.2300 Shahdara F.P.Bund. |
| 4. | Qadirabad Section | J-spur Qadirabad. 3 No sloppy spurs of Farkhabad & Diversion Bund at Qadirabad. | -do- | Remain Present in his Jurisdiction or where needed as define by SDO |
| 5. | Sharakpur Section | Sharakpur F.P. Bund and its spurs. | -do- | Camp at Sharakpur F.P.Bund RD.32060 |
| 6. | Niaz Baig Section | J-head spur at Shahpur Kanjran, Chung | Kasur Drainage Sub Division | Remain Present in his Jurisdiction or where needed as define by SDO |

CHAPTER – 10

EMERGENCY TELEPHONE NUMBERS

| S.# | Description of Department | Office Tel. No | Residence / Mobile Tel No. |
| --- | --- | --- | --- |
| 1 | Flood Control Cell (Irrigation Department) | 99212134 | - |
| 2 | Secretary Irrigation Department | 99212117-18 Fax No.9212116 | 99212116 |
| 3 | Flood Emergency center (Lahore Drainage Division) | 99250326 99250327 | - |
| 4 | Chief Engineer, Irrigation Lahore Zone, Lahore | 99212085-86 | 0301-8448709 |
| 5 | Superintending Engineer, Lahore Drainage Circle, Lahore | 99250306 | 0300-4441309 |
| 6 | Chief Engineer Drainage & Flood | 99230602 |  |
| 7 | Director Flood | 99231614 |  |
| 8 | Flood Forecasting Center 99205367-8 , 99205369-70, 99205157-8 | 99205371-72 | - |
| 9 | Canal Telegraph office Mustafa Abad | 99250318 | - |
| 10 | Executive Engineer, Rachna Drainage Division, Sheikhupura | 056-9200250 | 0333-4787659 |
| 11 | District Coordinator Officer (DCO) Sheikhupura | 056-9200151 | 99200153 |
| 12 | Brig 4-Core Munir Road Lahore Cantt: | 6699-3817 | - |
| 13 | D.C.O Lahore | 99211003-4 | 99200232 |
| 14 | Assistant Commissioner City Lahore | 99210608 | - |
| 15 | Executive Engineer, Lahore Drainage Division | 99250326-27 | 0302-3750100 |
| 16 | SDO/River Survey Drainage Sub Division, LHR | 99250326-27 | 0312-6524188 |
| 17 | SDO / Kasur Drainage Sub Division, Lahore | 99250326-27 | 0322-4642531 |
| 18 | SDO/Flood Bund Sub Division, Lahore | 99250326-27 | 0334-4123134 |
| 19 | SDO/Lahore Drainage Sub Division, Lahore | 99250326-27 | 0345-4920391 |
| 20 | Flood Cell committee room of I&P Secretariat, Lahore | 99212134 | - |
| 21 | Flood watching camp at Shahdara Flood Protection. | 042-36142233 | - |
| 22 | District Emergency Officer | 99231717, 1122 | - |
| 23 | Provincial Disaster Management Authority | 042-99203301 | - |
| 24 | Executive Engineer CBDC Division Lahore | 99250194 | 0323-4443607 |
| 25 | Executive Engineer Chakbandi Division Lahore | 99250312 | 0332-5543633 |

LIST OF OFFICERS / OFFICIALS OF LAHORE DRAINAGE DIVISION LAHORE

| S.# | Name of Officer / Official | Designation | Sub Division / Section | Mobile No. |
| --- | --- | --- | --- | --- |
|  | Ahmed Iqbal | Sub Divisional Officer | Flood Bund Sub Division Lahore | 0334-4123134 |
| 1 | Naveed Shehzad | Sub Engineer | Shahdara | 0307-4428758 |
| 2 | Abdul Ghaffar | Sub Engineer | Sharkpur | 0304-0596078 |
| 3 | Muhammad Akram Saleem | Sub Engineer | Mehmood Booti Bund | 0321-1130777 |
| 4 | Abdul Ghaffar | Sub Engineer | Lahore Protection Bund | 0304-0596078 |
| 5 | Hafiz Shakeel | Sub Engineer | Qadirabad | 0343-4646007 |
| 6 | Muhammad Ramzan | SDC | Flood Bund | 0307-4783695 |
|  | Maria Naeem | Sub Divisional Officer | River Survey Drainage Sub Division Lahore | 0312-6524188 |
| 1 | Vacant | Sub Engineer | Lilliani | - |
| 2 | Muhammad Bilal | Sub Engineer | Bhai Pheru | 0308-4822408 |
| 3 | Sheikh Iftikhar Ahmad | Sub Engineer | Mall | 0321-8658726 |
| 4 | Muhammad Umair Aslam | Sub Engineer | Ibrahimabad | 0305-7669904 |
| 5 | Muhammad Umair Aslam | Sub Engineer | Chathianwala | 0305-7669904 |
| 6 | Habib-Ur-Rehman | Sub Engineer | Rukhanwala | 0333-4849378 |
| 7 | Muhammad Zulqarnain | Sub Engineer | Jamman | 0333-4189240 |
| 8 | Muhammad Aslam |  | Sub Divisional Clerk | 0307-5211795 |
|  | Najam Waheed Qureshi | Sub Divisional Officer | Lahore Drainage Sub Division Lahore | 0345-4920391 |
| 1 | Muhammad Bilal | Sub Engineer | Ali Raza Abad | 0308-4822408 |
| 2 | Saleem Ashraf | Sub Engineer | Charrar | 0333-4974372 |
| 3 | Muhammad Rizwan | Sub Engineer | Khana | 0300-8532231 |
| 4 | Iftkhar saleem | Sub Engineer | Barki | 0333-4312908 |
| 5 | Muhammad Zeeshan | Sub Engineer | Bhasin | 0308-4308135 |
| 6 | Sajjad Ahmed |  | Sub Divisional Clerk | 0300-9648076 |
|  | Faisal Sardar | Sub Divisional Officer | Kasur Drainage Sub Division Lahore | 0322-4642531 |
| 1 | Azam Ali | Sub Engineer | Niaz Baig | 0322-7218487 |
| 2 | Shahid Sultan | Sub Engineer | Manga | 0300-4429808 |
| 3 | Muhammad Younis Amin | Sub Engineer | Raiwind-II | 0346-4427980 |
| 4 | Ahsan Jameel | Sub Engineer | Raiwind-I | 0333-7375014 |
| 5 | Javed Asif | Sub Engineer | Raiwind-III | 0322-8965134 |
| 6 | Tahir Hussain |  | Sub Divisional Clerk | 0333-4268193 |

CHAPTER – 11

STANDARD OPERATING PROCEDURE(SOP) FOR BREACHING SECTIONS

11.1	HISTORY OF THE BREACHING SECTION

There is an approved breaching section between RD.55+000 to 65+000 of Shahdara Distributory Flood Bund. The critical R.L. 698.00 for the operation of this breaching section will be monitored on the gauge fixed at RD.15+150 of Shahdara Flood Protection Bund. It is estimated that a discharge of about 1.0 Lac Cs. will pass through the breaching section, if operated. This breaching section was operated twice after 1947 i.e. during 1955 and 1988.

There is densely populated area just downstream side of the breaching section. The operation of breaching section has to be done very carefully with prior warning to the inhabitants of the area. Heavy building, infrastructure and life losses occurred when this breaching section was operated during 1988 flood as the area is thickly populated. The other option is to enhance the waterway under Shahdara Railway Bridge and Road Bridge (old) adjacent to the Railway Bridge, so that the situation for operation of the breaching section could be averted in future.

Location of breaching Section and strategy to activate Breaching Section.

| Location of approved breaching section | RD.55+000 to 65+000 (Shahdara Distributry flood protection Bund) |
| --- | --- |
| Location of critical gauge | Critical gauge is fixed at RD.15150 of Shahdara Flood Bund. |

11.2	LOCATION, DESIGN, QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATION.

Relates to Gujranwala Division, UCC as Breaching Section is under their control.

11.3	ARRANGEMENT OF EXPLOSIVES AND SECURITY OF EXPLOSIVE SORES

Relates to Gujranwala Division, UCC as Breaching Section is under their control.

11.4	LIST OF THE SECURITY STAFF ALONGWITH DETAIL OF THEIR TRAINING ETC

Relates to Gujranwala Division, UCC as Breaching Section is under their control.

11.5	DETAIL OF MECHANICAL MEANS AS A STANDBY ARRANAGMENTS IN CASE OF DETONATION FAILURE

Relates to Gujranwala Division, UCC as Breaching Section is under their control.

11.6	DUTY ROSTER IN CASE OF CRITICAL SITUATION

Relates to Gujranwala Division, UCC as Breaching Section is under their control.

11.7	BREACHING COMMITTEE WITH THEIR ACTION PLAN

If the water level in the river attains the critical level at critical gauge fixed at RD.15150 of Shahdara Flood Protection Bund and is in rising position, then the breaching section will be operated after the decision of the breaching operation committee comprising the following as per notification No.SO(Floods)VI-33/97 dated.15-07-2015.

- District Coordination Officer of the district in which the breaching section is located, who shall also be the convener of the Committee.

- District Coordination Officer of the District, likely to be effected by the operation of breaching section or his representative (in case the area affected falls outside the district in which the breaching section is located).

- Representative of the department owning the structure at which the breaching section is located (not less than the rank of Executive Engineer or equivalent).

- Representative from C&W Department not below the rank of an Executive Engineer,

- Executive Engineer concerned of the Irrigation Department.

- Representative from Pakistan Army not below the rank of a Lt. Colonol.

11.8	LIST OF THE VILLAGES & ABADIES LIKELY TO BE INUNDATED DURING VARIOUS FLOOD LIMITS

i)	Low Flood (40000 Cs – 65000 Cs) Almost no areas inundated.

ii)	AREAS LIKELY TO BE AFFECTED DURING LOW / MEDIUM FLOOD (65000 Cs – 90000 Cs)

A)	LAHORE PROTECTION BUND

1.	BETWEEN NEW ROAD  BRIDGE SHAHDARA AND J-SPUR NO.I

- Muhammadi Colony		ii)	Gow Shala

2.	BETWEEN J-SPUR NO.1 & J-SPUR NO.2

- Chiragh Park

3.	BETWEEN J-SPUR NO.2 & J-SPUR NO.3

i)	Ameen Park	ii)	Chaudhary Park	  iii)	New Shafiqabad

4.	BETWEEN SPUR NO.3 & SAGGIAN BRIDGE

i)	Ghulshan Riaz Colony		ii)	Mughal Park

5.	BETWEEN SAGGIAN BRIDGE & J-SPUR NO.4

i)	Akram Park			ii)	Sandha

6.	BETWEEN J-SPUR NO.4 & T-SPUR NO.5

- Tufail Colony

7.	BETWEEN T-SPUR NO.5 & MOTORWAY BRIDGE

i)	Fazal Colony	ii)	Shiblee Town

iii)	Ismail Colony	iv)	Yousuf Nagar

v)	Abu Bakar Siddique Colony		vi)	Shaheenabad

B)	TIE BUND

- BETWEEN MOTORWAY BRIDGE AND J-SPUR NO.1

i)	Talat Park	(ii)	Bhadroo Pind	(iii)	Malik Park

2.	BETWEEN L-BUND AND J-SPUR NO.2

I)	New Shadewal Village

C)	MEHMOOD BOOTI BUND

i) Karol (ii) Jabbo (iii) Bhama (iv) Khokhar Road (V) Jhuggian

D)	SOME OF THE OTHER VILLAGES ARE AS UNDER:

- Babakwal		ii)	Old Akbarabad	iii)	Saadpur Dossair

iv)	Toria Chotta		v)	Toria Bara		vi)	Bhyghanpura

vii)	Rajia Araian		viii)	Rahijian Phogan	ix)	Shahpur Kanjran

x)	Naul			xi)	Khanke Jhuggian	xii)	Babu Sabu

xiii)	Din Muhammad Farm				xiv)	Farid Colony

xv)	Mehrpur		xvi)	Rangilpur		xvii)	Nanu Dogar etc

II)	HIGH FLOOD, VERY HIGH FLOOD AND EXCEPTIONALLY HIGH FLOOD

The limit of high flood to exceptionally high flood ranges from 90000 Cs to 180000 Cs. The flood water touches the flood protection bunds at these limits and all the villages and abadies within the flood protection bunds are inundated.

LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN CASE OF SHAHDARA DISTY FLOOD BUND BREACH (INCLUDING INFRASTRUCTURE)

- Shahdara – Narowal Railway Line in front of breaching section upto       (4-K.M).

- Shahdara – Gujranwala Railway Line upto Kala Shah Kaku (10.54 KM)

- Shahdara – Gujranwala dual carriage way (G.T. Road) upto Kala Shah Kaku

- Shahdara – Sheikhupura Railway Line upto Missan Kalar Railway Station (9.65 K.M)

- Shahdara – Sheikhupura road upto over head bridge of Motorway (8 KM)

- Shahdara Distributory RD.65+000 to 100+000 (Upto Motorway)

- Shahdara – Sharakpur road upto Motorway

- Motorway from River Ravi to Kala Shah Kaku inter change and Bypass from G.T.Road to Motorway

- SHAHDARA / KALA KHATAI ROAD (BOTH SIDES)

- Industrial area between Shahdara Distributary and Kala Khatai Road (Haji Kot) including Flour Mills, dying / casting factories and foundries etc.

- Javed Park

- Barkat Town

- Jameel Park

- Garvi Mohallah

- Ali Park etc

- G.T.ROAD (SHAHDARA / GUJRANWALA) BOTH SIDES

- Scattered industry on both sides.

- Imamia Colony

- Feroze Wala

- Shah Khalid Town

- Shami Park

- Bashir Town

- Rana Town

- Khadija Town

- Ittehad Chemicals Colony Kala Shah Kaku etc

- KALA SHAH KAKU / MOTORWAY (L/S FACING LAHORE)

- Kallar

- Missin

- Dera Moulvian

- Green View Cooperative Housing Society

- Gulfishan Town

- Rangian Changian

- Kot Abdul Malik Villages and proposed toll plaza on Motorway etc

- SOME OF THE OTHER INFRASTRUCTURE / ABADIES ARE LISTED BELOW

- Nala Bhed

- Nala Lela

- Draghai Minor

- Taj Colony

- Vandala Deyai Shah

- Faisal Town

- Sharakpur Khurd

- Abul Khair

- Kot Abdul Malik

- Thatha Khuda yar

- Badoo

- Canal Rest House Shahdara

- Karol etc

11.9	ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENT

All announcements regarding evacuation will be made through District Administration by electronic media, radio, local Mosque and Loud speaker etc.

11.10 DETAIL OF COORDINATION WITH CIVIL / ARMY AUTHORITIES

If the water level in the river attains critical level i.e. 698.00 at gauge fixed at RD.15150 of Shahdara Flood Protection Bund and is in rising position then decision for operating breaching section will be obtained / taken by the committee as mentioned in Part-A, Section 11.7 (Page – 37)

11.11 PARALLEL COMMUNICATION ARRANGEMENTS

All communication will be made on wireless, special messengers and telephones mobile phones etc.

11.12 INDEX PLAN

On Next Page – 46

CHAPTER – 12

VULNERABLE SITES ON FLOOD BUNDS / STRUCTURES

No bund except the mentioned herein can breach even in exceptionally high flood.

12.1	APPREHENDED BREACHES IN FLOOD BUNDS

      - Shahdara Flood Protection Bund   R.D 9+000 to 15+000.

      - Sharkpur Flood Protection Bund   R.D 16+000 to 32+000.

12.2	OPERATION OF BREACHING SECTION

There is no Breaching Section in Lahore Drainage Division Lahore

12.3	BREACHES DUE TO RISE OF FLOOD WATER, DETERIORATION OF FLOOD BUNDS.

No high / exceptionally flood has been experienced after 1988 and the flood bunds of Lahore Drainage Division Lahore are safe and sound.

| S.# | Name of Structure | Location of Vulnerable site | Reference of Contingency Plan |
| --- | --- | --- | --- |
| 1 | Shahdara Flood Protection Bund | R.D 9+000 to 15+000 | As per contingency plan of Shahdara Breaching Section |
| 2 | Sharkpur Flood Protection Bund | R.D 16+000 to 32+000 | -do- |

CHAPTER – 13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE (SITES) LISTED ABOVE/ EMERGENCY CONTINGENCY PLAN

SITE NO.1 SHAHDARA FLOOD PROTECTION BUND R.D 9+000 to 15+000

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

Route of flood water is shown at page No.51-A. The flood water after breach between RD.9+000 to 15+000 will enter in Shahdara Town and after inundating the abadies of Shahdara Town including Jada, Power House, Jia Mousa, Begum Kot & Farkhabad etc will finally dispose back into River near Saggian Bridge.

13.2	DETAIL OF VILLAGES / ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN

| S.# | Shahdara Bund R.D 9+000 to 15+000 |
| --- | --- |
| H.F.L | 694.00 |
| 1 | Shahdrah Town |
| 2 | Jada |
| 3 | Their |
| 4 | Qazi Park |
| 5 | Power House |
| 6 | Paracha Colony |
| 7 | Juspat |
| 8 | Gulshanabad |
| 9 | Rasool Park |
| 10 | Jia Mousa |
| 11 | Begum Kot |
| 12 | Farkhabad |

13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

Sub Divisional Officers and their staff would remain present and vigilant in the area round the clock during flood period. The flood information would be communicated by wireless, mobile phone or sent through special messenger employed for this purpose. In case of any emergency, the Sub Divisional Officer concerned would report the matter to the Executive Engineer, Lahore Drainage Division, Superintending Engineer, Lahore Drainage Circle, Chief Engineer, Irrigation Lahore Zone, Director Regulation, Chief Engineer, Drainage & Flood and Secretary Irrigation and Power Department, Punjab Lahore.

On receipt of any flood warning, Sub Divisional Officer Flood Bund Sub Division will make necessary arrangements. Sub Divisional Officer, Flood Bund alongwith their field staff will camp at spur No.1 at RD.2300 of Shahdara Flood Protection Bund respectively.

In case of High Flood, necessary arrangements for evacuation of affected people will be carried out by the Civil and Military authorities, and the Engineering staff will remain busy in watching and protecting of the Flood Protection Works. The Lahore Division CBDC, Lahore will act as backup division once emergency is declared. All other Departments will have their own arrangements to provide help to the needy persons.

13.3.1	ARRANGEMENTS

As above 13.3

13.3.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

| S.# | Camping Site | Sub Engineer | Detail of Field Establishment |
| --- | --- | --- | --- |
|  |  |  | Mistry | Mate | Beldar | Total |
| 1 | Shahdara Flood Protection Bund | 1 | 1 | 1 | 18 | 20 |
|  | Total:- |  |  |  |  | 20 Nos |

13.3.3	DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP SITES

| S.# | Location | Officers (Name & Designation) & Mobile No | Officials (Name & Designation) & Mobile No |
| --- | --- | --- | --- |
| 1 | At XEN Office Mustafabad Lahore | Muhammad Riaz Executive Engineer, Lahore Drainage Division, Lahore. Phone No.0302-3750100 |  |
| 2. | At Shahdara Hut, at RD.2300, of Shahdara Flood Protection Bund. | Ahmed Iqbal Sub Divisional Officer, Flood Bund Sub Division, Phone No.0334-4123134 | Shahzad Naveed Sub Engineer Shahdara Section Phone No.0307-4428758 |
| 3. | J-head spur at Shahpur Kanjran | Faisal Sardar Sub Divisional Officer, Kasur Drainage Sub Division, Lahore Phone No.0322-4642531 | Azam Ali Sub Engineer Niaz Baig Section Phone No.0322-7218487 |

13.3.4	DEPARTMENTAL MACHINERY AVAILABLE

No machinery is available in this Division but during flood season excavator and tractor trollies will be hired through local contractor for flood season to be started at three number camps i.e. Shahdara Hut, Sharkpur Flood Protection Bund and Shahpur Kanjran spur to cater for any emergency situation.

13.3.5	MACHINERY AVAILABLE FROM PRIVATE SOURCE

The private machinery including Tractor trollies and excavators is available nearby at bund road. It may be arranged in emergent situation.

13.3.6	FLOOD FIGHTING MATERIAL REQUIRED SHAHDARA BUND

| S.# | Name of Items | Unit | Total Required Qty | Available Qty | Balanced Qty | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Kassies / Belchas | No | 30 | 30 | 0 | Preparation of Estimate is under process and balance required material will be procured after due tendering process |
| 2 | handle of Kassies | No | 20 | 20 | 0 |  |
| 3 | Toot Baskets | No | 100 | 100 | 0 |  |
| 4 | Torches (3- cell) | No | 15 | 15 | 0 |  |
| 5 | Dry Cell | Dozen | 4 | 4 | 0 |  |
| 6 | Bulb for Torches | No | 2 | 2 | 0 |  |
| 7 | Axes | No | 6 | 6 | 0 |  |
| 8 | Handle for axe | No | 4 | 4 | 0 |  |
| 9 | Generator | No | 1 | 1 | 0 |  |
| 10 | Electric wire 3/29 | Coil | 1 | 1 | 0 |  |
| 11 | Insulation tape | No | 8 | 0 | 8 |  |
| 12 | Electric bulb 100 (W) | No | 100 | 70 | 30 |  |
| 13 | Electric bulb 200 (W) | No | 50 | 40 | 10 |  |
| 14 | Bulb Holder | No | 50 | 50 | 0 |  |
| 15 | Electric Switch | No | 60 | 60 | 0 |  |
| 16 | Shouldaries | No | 1 | 1 | 0 |  |
| 17 | Swiss cottage tent | No | 1 | 1 | 0 |  |
| 18 | Darries | No | 5 | 5 | 0 |  |
| 19 | camp chair | No | 6 | 6 | 0 |  |
| 20 | camp Table | No | 1 | 1 | 0 |  |
| 21 | Buckets G.I | No | 45 | 45 | 0 |  |
| 23 | Life Jacket | No | 6 | 6 | 0 |  |
| 24 | Sounding Rod | No | 2 | 1 | 1 |  |
| 25 | Long rubber shoes | Pair | 10 | 10 | 0 |  |
| 26 | Emergency Lights | No | 3 | 0 | 3 |  |
| 27 | Gunny bags | No | 1000 | 1000 | 0 |  |
| 28 | Nylon Bags | No | 1000 | 1000 | 0 |  |
| 29 | U-clamp 5/8” dia | No | 100 | 100 | 0 |  |
| 30 | U-clamp 1/2” dia | No | 50 | 50 | 0 |  |
| 31 | Water cooler | No | 2 | 0 | 2 |  |
| 32 | Measuring tape 50’ | No | 6 | 3 | 3 |  |
| 33 | Steel wire rope 1/2” dia | Rft | 200 | 200 | 0 |  |
| 34 | Khaji Mats | No | 20 | 20 | 0 |  |
| 35 | Fiber glass boat | No | 1 | 1 | 0 |  |
| 36 | Bamboo 2 ½” dia 8-10 ft long | No | 20 | 10 | 10 |  |
| 37 | Energy Saver 45W | No | 12 | 0 | 12 |  |
| 38 | Digital Camera | No | 1 | 0 | 1 |  |

13.3.7	FLOOD FIGHTING MATERIAL AVAILABLE

| S.# | Name of Items | Unit | Shahdara Bund R.D 9+000 to 15+000 |
| --- | --- | --- | --- |
| 1 | Kassies / Belchas | No | 30 |
| 2 | handle of Kassies | No | 20 |
| 3 | Toot Baskets | No | 100 |
| 4 | Torches (3- cell) | No | 15 |
| 5 | Dry Cell | Dozen | 4 |
| 6 | Bulb for Torches | No | 2 |
| 7 | Axes | No | 6 |
| 8 | Handle for axe | No | 4 |
| 9 | Generator | No | 1 |
| 10 | Electric wire 3/29 | Coil | 1 |
| 11 | Insulation tape | No | 0 |
| 12 | Electric bulb 100 (W) | No | 70 |
| 13 | Electric bulb 500 (W) | No | 40 |
| 14 | Bulb Holder | No | 50 |
| 15 | Electric Switch | No | 60 |
| 16 | Shouldaries | No | 1 |
| 17 | Swiss cottage tent | No | 1 |
| 18 | Darries | No | 5 |
| 19 | camp chair | No | 6 |
| 20 | camp Table | No | 1 |
| 21 | Buckets G.I | No | 45 |
| 23 | Life Jacket | No | 6 |
| 24 | Sounding Rod | No | 1 |
| 25 | Long rubber shoes | Pair | 10 |
| 26 | Emergency Lights | No | 0 |
| 27 | Gunny bags | No | 1000 |
| 28 | Nylon Bags | No | 1000 |
| 29 | U-clamp 5/8” dia | No | 100 |
| 30 | U-clamp 1/2” dia | No | 50 |
| 31 | Water cooler | No | 0 |
| 32 | Measuring tape 50’ | No | 3 |
| 33 | Steel wire rope 1/2” dia | Rft | 200 |
| 34 | Khaji Mats | No | 20 |
| 35 | Fiber glass boat | No | 1 |
| 36 | Bamboo 2 ½” dia 8-10 ft long | No | 10 |
| 37 | Energy Saver 45W | No | 0 |
| 38 | Digital Camera | No | 0 |

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDINGS, CANALS AND DRAINAGE NETWORK

More or less all the infrastructure lies in the areas already identified to be inundated. Installations like WAPDA poles / cables, Sui Gas pipe lines, Railway Lines, Town roads and residential / commercial / Industrial buildings  etc exist in the area.

SITE NO.2 SHARKPUR FLOOD PROTECTION BUND R.D 16+000 to 32+000

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

Route of flood water is shown at page No.61 The flood water after breach will enter in Sharkpur Town and allied abadies including Sahajowal and Naul etc and finally dispose back into River beyond Deg Diversion Channel.

13.2	DETAIL OF VILLAGES / ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN

| S.# | Sharkpur Bund |
| --- | --- |
| H.F.L | 675.70 |
| 1 | Sharakpur Town |
| 2 | Sahajowal |
| 3 | Bhoe Wal |
| 4 | Bheni |
| 5 | Ghazi pur |
| 6 | Naul |
| 7 | Dhana |

13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

Sub Divisional Officers and their staff would remain present and vigilant in the area round the clock during flood period. The flood information would be communicated by wireless, mobile phone or sent through special messenger employed for this purpose. In case of any emergency, the Sub Divisional Officer concerned would report the matter to the Executive Engineer, Lahore Drainage Division, Superintending Engineer, Lahore Drainage Circle, Chief Engineer, Irrigation Lahore Zone, Director Regulation, Chief Engineer, Drainage & Flood and Secretary Irrigation and Power Department, Punjab Lahore.

On receipt of any flood warning, Sub Divisional Officer Flood Bund Sub Division will make necessary arrangements. Sub Divisional Officer, Flood Bund alongwith their field staff will camp at gauge reader hut at RD.32+060 of Sharkpur Flood Protection Bund.

In case of High Flood, necessary arrangements for evacuation of affected people will be carried out by the Civil and Military authorities, and the Engineering staff will remain busy in watching and protecting of the Flood Protection Works. The Lahore Division CBDC, Lahore will act as backup division once emergency is declared. All other Departments will have their own arrangements to provide help to the needy persons.

13.3.1	ARRANGEMENTS

As above 13.3

13.3.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

| S.# | Camping Site | Sub Engineer | Detail of Field Establishment |
| --- | --- | --- | --- |
|  |  |  | Mistry | Mate | Beldar | Total |
| 1 | Sharkpur Flood Protection Bund | 1 | 1 | 1 | 18 | 20 |
|  | Total:- |  |  |  |  | 20 Nos |

13.3.3	DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP SITES

| S.# | Officers | Officials | Camping Station | Duty |
| --- | --- | --- | --- | --- |
| 1 | Executive Engineer, Lahore Drainage Division, Lahore. |  | At XEN Office Mustafabad Lahore | He will be the overall in charge of Lahore Drainage Division and will keep close contact with his staff and District Administration. He will also act as per flood situation keeping liaison with all concerned Departments related with flood activities, |
| 2. | Sub Divisional Officer, Flood Bund Sub Division, Lahore. |  | At Shahdara Hut, at RD.2300, of Shahdara Flood Protection Bund. | To monitor flood situation in River Ravi and keep watch on flood protection / River Training works of Shahdara, Mahmood Booti, Qadirabad and Lahore Protection section |
| 3. |  | Sub Engineer Sharkpur Section | Camp at Gauge hut at RD.32+060 Sharkpur F.P. Bund. | To monitor flood situation in River Ravi and keep watch on flood protection / River Training works in Sharkpur Flood Protection Bund and its spurs. |

13.3.4	DEPARTMENTAL MACHINERY AVAILABLE

No machinery is available in this Division but during flood season excavator and tractor trollies will be hired through local contractor for flood season to be started at three number camps i.e. Shahdara Hut, Sharkpur Flood Protection Bund and Shahpur Kanjran spur to cater for any emergency situation.

13.3.5	MACHINERY AVAILABLE FROM PRIVATE SOURCE

The private machinery including Tractor trollies and excavators is available at bund road Lahore. It may be arranged in emergent situation.

13.3.6	FLOOD FIGHTING MATERIAL REQUIRED SHARKPUR BUND

| S.# | Name of Items | Unit | Total Required Qty | Available Qty | Balanced Qty | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Kassies | No | 30 | 30 | 0 | Preparation of Estimate is under process and balance required material will be procured after due tendering process |
| 2 | Toot Baskets | No | 35 | 35 | 0 |  |
| 3 | Torches (3- cell) | No | 10 | 10 | 0 |  |
| 4 | Dry Cell | Dozen | 4 | 4 | 0 |  |
| 5 | Axe | No | 4 | 4 | 0 |  |
| 6 | Generator | No | 1 | 1 | 0 |  |
| 7 | Electric wire 3/29 | Coil | 1 | 1 | 0 |  |
| 8 | Insulation tape | No | 4 | 0 | 4 |  |
| 9 | Bulb Holder | No | 5 | 5 | 0 |  |
| 10 | Shouldaries | No | 1 | 1 | 0 |  |
| 11 | Darries | No | 2 | 2 | 0 |  |
| 12 | Office chair | No | 6 | 6 | 0 |  |
| 13 | Office Table | No | 1 | 1 | 0 |  |
| 14 | Life Jacket | No | 6 | 6 | 0 |  |
| 15 | Long rubber shoes | Pair | 6 | 6 | 0 |  |
| 16 | Emergency Lights | No | 2 | 0 | 2 |  |
| 17 | Nylon Bags | No | 1000 | 1000 | 0 |  |
| 18 | Water cooler | No | 2 | 0 | 2 |  |
| 19 | Handle Umbrella | No | 1 | 0 | 1 |  |
| 20 | Measuring tape 100’ | No | 2 | 2 | 0 |  |
| 21 | Energy Saver 18 w | No | 10 | 0 | 10 |  |
| 22 | Wrench | No | 2 | 0 | 2 |  |
| 23 | Pliers | No | 2 | 0 | 2 |  |
| 24 | Gas Lamp | No | 6 | 6 | 0 |  |
| 25 | Lantern | No | 5 | 5 | 0 |  |

13.3.7	FLOOD FIGHTING MATERIAL AVAILABLE

| S.# | Name of Items | Unit | Material Available at Sharkpur Bund R.D 16+000 to 32+000 |
| --- | --- | --- | --- |
| 1 | Kassies | No | 30 |
| 2 | Toot Baskets | No | 35 |
| 3 | Torches (3- cell) | No | 10 |
| 4 | Dry Cell | Dozen | 4 |
| 5 | Axe | No | 4 |
| 6 | Generator | No | 1 |
| 7 | Electric wire 3/29 | Coil | 1 |
| 8 | Insulation tape | No | 0 |
| 9 | Bulb Holder | No | 5 |
| 10 | Shouldaries | No | 1 |
| 11 | Darries | No | 2 |
| 12 | Office chair | No | 6 |
| 13 | Office Table | No | 1 |
| 14 | Life Jacket | No | 6 |
| 15 | Long rubber shoes | Pair | 6 |
| 16 | Emergency Lights | No | 0 |
| 17 | Nylon Bags | No | 1000 |
| 18 | Water cooler | No | 0 |
| 19 | Handle Umbrella | No | 0 |
| 20 | Measuring tape 100’ | No | 2 |
| 21 | Energy Saver 18 w | No | 0 |
| 22 | Wrench | No | 0 |
| 23 | Pliers | No | 0 |
| 24 | Gas Lamp | No | 6 |
| 25 | Lantern | No | 5 |

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDINGS, CANALS AND DRAINAGE NETWORK

More or less all the infrastructure lies in the areas already identified to be inundated.

CHAPTER – 14

ACTION PLAN

14.1	RE-SHUFFLING / RECOUPING PLAN OF RESERVE STONE DEPARTMENTALLY

During any emergency stone will be reshuffled through Local Contractors.

14.2	DETAIL OF INLET / OUTLET CROSSING ALONG WITH CLOSING METHODOLOGY

There is no Inlet / Outlet crossing along with Flood Protection Bund.

14.3 	DEPLOYMENT MACHINERY (LOW TO HIGH FLOOD)

| Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site In-charge by name & Cell No. | Machinery Deployed |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Excavator | Dozer | Trolleys / Dumpers | Tractor with front blade | Labour (Beldar + Mate) | Availability of Stone Lac Cft |
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Shahdara Flood Protection Bund | 3.15 | 9+000 to 15+000 | Hut at RD.2300 Shahdara F.P.B | Sub Engineer Shahdara Section | 1 | -- | 2 |  | 20+2 | 0.537 |
| Sharkpur Flood Protection Bund | 6.41 | 16+000 to 32+000 | Hut at RD.32+060 Sharkpur F.P.B | Sub Engineer Sharkpur Section | 1 | - | 2 |  | 20+2 | 1.019 |
| Mehmood Booti Bund | 5.80 | - | RD.7000 Hockey Spur of | Sub Engineer M.B.B Section |  |  |  |  | 20+2 | 0.0161 |
| Lahore Protection Bund | 4.60 | - | T-head spur No.5 RD.19900 | Sub Engineer L.P.B Section |  |  |  |  | 20+2 | 0.7791 |
| Qadirabad Flood Protection Bund | 2.05 | - | Qadirabad spur | Sub Engineer Qadirabad Section |  |  |  |  | 20+1 | 0.1386 |
| J-Spur Shahpur Kanjran J-spur at Chung | 3.03 | - | J-head spur Shahpur Kanjran | Sub Engineer Niaz Baig Section | 1 | - | 2 |  | 20+1 | 1.055 |
| Total |  |  |  |  | 3 | -- | 6 |  | 120+10 | 3.54 |

14.4	DEPLOYMENT OF MACHINERY (HIGH TO VERY HIGH FLOOD)

| Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site In-charge by name & Cell No. | Machinery Deployed |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Excavator | Dozer | Trolleys / Dumpers | Tractor with front blade | Labour (Beldar + Mate) | Availability of Stone Lac Cft |
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Shahdara Flood Protection Bund | 3.15 | 9+000 to 15+000 | Hut at RD.2300 Shahdara F.P.B | Sub Engineer Shahdara Section | 1 | -- | 2 |  | 30+3 | 0.537 |
| Sharkpur Flood Protection Bund | 6.41 | 16+000 to 32+000 | Hut at RD.32+060 Sharkpur F.P.B | Sub Engineer Sharkpur Section | 1 | - | 2 |  | 30+3 | 1.019 |
| Mehmood Booti Bund | 5.80 | - | RD.7000 Hockey Spur of | Sub Engineer M.B.B Section |  |  |  |  | 30+3 | 0.0161 |
| Lahore Protection Bund | 4.60 | - | T-head spur No.5 RD.19900 | Sub Engineer L.P.B Section |  |  |  |  | 20+3 | 0.7791 |
| Qadirabad Flood Protection Bund | 2.05 | - | Qadirabad spur | Sub Engineer Qadirabad Section |  |  |  |  | 20+2 | 0.1386 |
| J-Spur Shahpur Kanjran J-spur at Chung | 3.03 | - | J-head spur Shahpur Kanjran | Sub Engineer Niaz Baig Section |  |  |  |  | 20+1 | 1.055 |
| Total |  |  |  |  | 2 | -- | 4 |  | 150+15 | 3.54 |

14.5	DEPLOYMENT OF MACHINERY (HIGH TO EXCEPTIONALLY HIGH FLOOD)

| Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site In-charge by name & Cell No. | Machinery Deployed |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Excavator | Dozer | Trolleys / Dumpers | Tractor with front blade | Labour (Beldar + Mate) | Availability of Stone Lac Cft |
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Shahdara Flood Protection Bund | 3.15 | 9+000 to 15+000 | Hut at RD.2300 Shahdara F.P.B | Sub Engineer Shahdara Section | 2 | -- | 4 |  | 50+5 | 0.537 |
| Sharkpur Flood Protection Bund | 6.41 | 16+000 to 32+000 | Hut at RD.32+060 Sharkpur F.P.B | Sub Engineer Sharkpur Section | 2 | - | 4 |  | 50+5 | 1.019 |
| Mehmood Booti Bund | 5.80 | - | RD.7000 Hockey Spur of | Sub Engineer M.B.B Section |  |  |  |  | 50+5 | 0.0161 |
| Lahore Protection Bund | 4.60 | - | T-head spur No.5 RD.19900 | Sub Engineer L.P.B Section |  |  |  |  | 50+5 | 0.7791 |
| Qadirabad Flood Protection Bund | 2.05 | - | Qadirabad spur | Sub Engineer Qadirabad Section |  |  |  |  | 50+5 | 0.1386 |
| J-Spur Shahpur Kanjran J-spur at Chung | 3.03 | - | J-head spur Shahpur Kanjran | Sub Engineer Niaz Baig Section |  |  |  |  | 50+5 | 1.055 |
| Total |  |  |  |  | 4 | -- | 8 |  | 150+15 | 3.54 |

LIST OF LOCAL CONTRACTORS

| Name of Govt. Contractor | Contact Number | Remarks |
| --- | --- | --- |
| M/S Muhammad Umar & Co | 0321-8527997 | Excavators and other machinery may be made available through these contractors. |
| M/S Malik Ashfaq & Co | 0300-8449133 |  |
| M/S Bashir Ahmed Enterprises | 0300-4651754 |  |

14.6 	POLICE DEPLOYMENT PLAN

Proforma – 1

| Sr. | Site of Breaching Section | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / Sub Inspector / A.S.I | Constable |  |
| 1 | - | - | - | - | - | - |

Proforma – 2

| Sr. | Vulnerable sites used for illegal cuts during floods | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / Sub Inspector / A.S.I | Constable |  |
| 1 | Shahdara Flood Protection Bund 9+000 to 15+000 | Lahore Drainage Division | Shadara Police Station District Lahore | ASI=1 | 2 | - |
| 2 | Sharkpur Flood Protection Bund 16+000 to 32+000 | Lahore Drainage Division | Sharkpur Police Station District Sheikhupura | ASI=1 | 2 | -- |

Proforma – 3

| Sr. | Name of Barrage | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / Sub Inspector / A.S.I | Constable |  |
| - | - | - | - | - | - | - |

14.7. DETAIL OF SYNTHETIC BAGS WITH CAPACITY OF 500 KG AND 1000 KG.

| Sr. # | Item | Required Qty No. | Available Qty No. |
| --- | --- | --- | --- |
| 1 | Synthetic Bags with capacity 500 KG | 5000 | 0 |
| 2 | Synthetic Bags with capacity 1000 KG | 5000 | 0 |

14.8	DETAIL OF POLYTHENE SHEETS OF BLACK COLOUR TO PROTECT UPSTREAM SLOPE AGAINST WAVE ACTION AND TO CONTROL SEEPAGE THROUGH EMBANKMENT.

| Sr. # | Item | Required Rft | Available Rft |
| --- | --- | --- | --- |
| 1 | Polythene sheets of black clolour for protecting upstream slopes from waves and control to seepage (Average 20 FT Width) | 0 | 0 |

CHAPTER – 15

BACKUP DIVISION (IN CASE OF BREACH)

In case of Emergency/Breach Lahore Division CBDC will act as sister Division of Lahore Drainage Division Lahore.

Executive Engineer,			Sub Divisional Officer,	Sub Divisional Officer,

Lahore Drainage Division,		Flood Bund Sub Division,	Kasur Drainage Sub Division,

Lahore.				Lahore.			Lahore.

FLOOD FIGHTING PLAN OF LAHORE DRAINAGE DIVISION LAHORE FOR THE YEAR 2021

PREPARED BY:				Executive Engineer,

Lahore Drainage Division,

Lahore.

Superintending Engineer,

Lahore Drainage Circle,

Lahore.

Chief Engineer,

Irrigation Lahore Zone,

Lahore.

# Text boxes

Executive Engineer

Lahore Drainage Division

Lahore

SDO

Flood Bund Sub Division

SDO

Kasur Drainage Sub Division

SDO

Lahore Drainage Sub Division

SDO

River Survey Drainage Sub Division

Sub Engineer

Shahdara Section

Sub Engineer

Sharkpur Section

Sub Engineer

Mehmood Booti Bund Section

Sub Engineer

Lahore Protection Bund Section

Sub Engineer

Qadirabad Section

Sub Engineer

Niaz Baig Section

Sub Engineer Manga Section

Sub Engineer

Raiwind-II Section

Sub Engineer

Raiwind-I Section

Sub Engineer

Raiwind-III Section

Sub Engineer Ali Raza Abad Section

Sub Engineer Charrar Section

Sub Engineer Khana Section

Sub Engineer Barki Section

Sub Engineer Bhasin Section

Sub Engineer Lulliani Section

Sub Engineer Bhai Pheru Section

Sub Engineer Mall Section

Sub Engineer Ibrahimabad Section

Sub Engineer Chathianwala Section

Sub Engineer Rukhanwala Section

Sub Engineer Jamman Section