# GOVERNMENT OF THE PUNJAB

# IRRIGATION DEPARTMENT

FLOOD FIGHTING PLAN FOR THE YEAR 2021.

18-HAZARI SUB DIVISION

FAISALABAD IRRIGATION ZONE, FAISALABAD

JHANG DIVISION LCC (W) JHANG

INDEX

FLOOD FIGHTING PLAN 2021

| Chapter | PART (A) | PAGE No. |
| --- | --- | --- |
| 1 | Salient Feature of Division | 1 |
| 1.1 | Location | 1 |
| 1.2 | General Description | 1 |
| 1.3 | Administrative Setup | 1 |
| 2 | Flood Protection and River Training Works | 2 |
| 2.1 | Design Parameter of River Training Works | 2 |
| 2.2 | Location Map | 3 |
| 3 | Brief History Of Past Flood Events | 4 |
| 4 | Design Data, Historic Peak Flood Data and Previous five years Flood Data of Headworks / Barrages and or other Control points | 5 |
| 4.1 | Flood Limits | 5 |
| 4.2 | Time Lags of Floods | 5 |
| 4.3 | Highest Floods | 6 |
| 4.4 | Peak Discharges | 6 |
| 5 | Flood Fighting Strategy | 7 |
| 6 | Flood Damages Restoration Works | 8 |
| 7 | Flood Fighting Watching Arrangement | 9 |
| 7.1 | Pre-Flood Arrangement | 9-11 |
| 7.2 | Watching Establishment | 12 |
| 7.3 | Arrangement at Sensitive sites | 12 |
| 7.4 | Watching Material | 13 |
| 7.5 | Arrangement for Sounding & Probing | 14 |
| 7.6 | Lighting Arrangement | 14 |
| 7.7 | Ration Arrangement | 14 |
| 7.8 | P.O.L Arrangement for Vehicle | 14 |
| 7.9 | Transportation | 14 |
| 7.10 | Law and Order | 14 |
| 7.11 | Medical Arrangement for Labour | 15 |
| 7.12 | Liaison with other Department | 15 |
| 7.13 | Role of the Army | 15 |
| 7.14 | Duties of Telephone Attendant | 15 |
| 7.15 | Wireless Arrangements | 15 |
| 8 | Detail of Encroachment | 16 |
| 9 | Duty Roaster / Flood Fighting Program | 17-18 |
| 10 | Emergency Telephone Nos | 19-20 |

| Chapter | PART (A) | PAGE No. |
| --- | --- | --- |
| 11 | Standard Operating Procedure (SOP) for Breaching Sections | 21 |
| 11.1 | History of the Breaching Section | 21 |
| 11.2 | Location, Quantity, Design and Variety of the Explosive Required for Detonation | 21 |
| 11.3 | Arrangements of Explosives and Security of Explosives Stores | 21 |
| 11.4 | List of Security Staff along with details of their trainings etc. | 21 |
| 11.5 | Details of machinery means as standby arrangements in case of detonation failure | 21 |
| 11.6 | Duty roaster in case of critical situation | 22 |
| 11.7 | Breaching committee with their action plan | 22 |
| 11.8 | List of villages likely to be inundated in case of breach | 22 |
| 11.9 | Announcement and details of evacuation arrangements | 22 |
| 11.10 | Details of coordination with civil/ army authorities | 23 |
| 11.11 | Parallel communication arrangements | 23 |
| 11.12 | Index plan | 24 |
| Chapter | Part – B |  |
| 12 | Vulnerable sites on flood Bund/ Structures | 25 |
| 12.1 | Apprehended Breaches in flood Bund/ structures | 25 |
| 12.2 | Operation of Breaching sections | 25 |
| 12.3 | Breaches due to rise of flood water, deterioration of flood bunds | 26 |
| 13 | Emergency contingency plan for vulnerable sites | 26 |
| 13.1 | Plan showing route of flood water coming out of the breach supported with levels | 26 |
| 13.2 | Details of villages, abadies likely to be affected and this should also be shown on plan | 26 |
| 13.3 | Strategy and action taken, explained in details. This may include: | 26 |
|  | 13.3.1Arrangements | 26 |
|  | 13.3.2 Establishment of flood fighting camps | 26 |
|  | 13.3.3 Duties of officers/ officials and their camp sites (Duty Roster) | 26 |
|  | 13.3.4 Departmental machinery available | 26 |
|  | 13.3.5 Machinery available from private sources | 27 |
|  | 13.3.6 Flood fighting material required | 28 |
|  | 13.3.7 Flood fighting material available | 29 |
| 13.4 | Detail of other infrastructure like electricity, sui gas, telephone installation, road network, other building, canal and drainage network. | 30 |
| 14 | Action Plan | 31 |
| 14.1 | Re-shuffling/ Recouping plan of reserve stone departmentally | 32 |
| 14.2 | Detail of inlet/ outlet crossing along with closing methodology | 32 |
| 14.3 | Deployment Machinery (Medium to high flood) | 33 |
| 14.4 | Deployment Machinery (High to very high flood) | 34 |
| 14.5 | Deployment Machinery (high to exceptionally high flood) | 35 |
| 14.6 | Police deployment plan | 36 |
| 14.7 | Details of synthetic bags with capacity of 500 kg and 1000kg | 36 |
| 14.8 | Details of polythene sheet of black colour to protect upstream slope against wave action and to control seepage through embankments | 36 |
| 15 | Back up divisions (In case of breach) | 37 |

SOP’s FOR FLOOD FIGHTING PLANS

PART-A

Chapter-1	Salient feature of the concerned Division

  - Location

  - General Description

  - Administrative setup

Chapter-2	Flood Protection and River Training Works

  - Design parameter of Training Works

  - Location Map

Chapter-3	Brief history of past flood events

Chapter-4	Design Data, Historic peak flood data and previous five years flood data of Head Works/Barrages and or other control points

  - Flood Limits

  - Time Lags of Floods

  - Highest Floods

  - Peak discharges

Chapter-5	Flood Fighting Strategy

Chapter-6	Flood Damages Restoration Works

Chapter-7	Flood Fighting Watching Arrangement

  - Pre-Flood Arrangement

  - Watching Establishment

  - Arrangement at Sensitive sites

  - Watching Material

  - Arrangement for Sounding & Probing

  - Lighting Arrangement

  - Ration Arrangement

  - P.O.L. Arrangement for Vehicle

  - Transportation

  - Law and order

  - Medical Arrangement for Labour

  - Liaison with other Department

  - Role of the Army

  - Duties of Telephone Attendant

  - Wireless Arrangements

Chapter-8	Detail of Encroachment

Chapter-9	Duty Roster/Flood Fighting Program

Chapter-10	Emergency Telephone Nos.

Chapter-11	Standard operating procedure(SOP) for Breaching Sections

  - History of the breaching section

  - Location, Design, Quantity and Variety of the explosive required for detonation.

  - Arrangement of explosives and security of explosive stores

  - List of the security staff alongwith detail of their training etc

  - Detail of mechanical means as a standby arrangements in case of detonation failure

  - Duty Roster in case of critical situation

  - Breaching Committee with their action plan

  - List of the villages likely to be inundated in case of breach

  - Announcement and detail of evacuation arrangements

  - Details of coordination with Civil/Army Authorities

  - Parallel communication arrangements

  - Index Plan

PART-B

Chapter-12		Vulnerable sites on Flood Bund/Structures:

  - Apprehended breaches in Flood Bunds/Structures.

  - Operation of breaching sections.

  - Breaches due to rising of flood water, deterioration of flood bunds etc.

Chaper-13		Emergency Contingency Plan for vulnerable site (sites)  				listed above.  Emergency Contingency Plan must include:-

  - Plan showing route of Flood Water coming out of the breach supported with levels.

  - Detail of villages abadies likely to be affected and this should also be shown on the plan.

  - Strategy and action taken be explained in detail. This may include:

    - Arrangements

    - Establishment of Flood Fighting Camps

    - Duties of Officers/Officials and their camp sites

    - Departmental Machinery available

13.3.5	 Machinery available from Private Source

    - Flood Fighting Material required

13.3.7  Flood Fighting Material available

  - Detail of other infrastructure like electric, Sui gas, Telephone installations, road network, other buildings, Canals and drainage network.

Chaper-14		Action Plan

| 14.1 | Re-shuffling/ Recouping plan of reserve stone departmentally |
| --- | --- |
| 14.2 | Detail of inlet/ outlet crossing along with closing methodology |
| 14.3 | Deployment Machinery (Medium to high flood) |
| 14.4 | Deployment Machinery (High to very high flood) |
| 14.5 | Deployment Machinery (high to exceptionally high flood) |
| 14.6 | Police deployment plan |
| 14.7 | Details of synthetic bags with capacity of 500 kg and 1000kg |
| 14.8 | Details of polythene sheet of black colour to protect upstream slope against wave action and to control seepage through embankments |

Note:-

Chaper-15		Back up divisions (In case of breach)

Last page of Part-A & Part-B be signed by the concerned Superintending Engineer and Chief Engineer in token of correctness of the Flood Fighting Plan.

PART----A

CHAPTER-1

SALIENT FEATURE OF THE 18HAZARI SUB DIVISION

1.1	LOCATION

18-Hazari Sub Division has been attached with Jhang Canal Division LCC(W), Jhang vide Secretary , Government of the Punjab Irrigation Department, Lahore vide No. SO(E-1) 9-6/2016 dated 11.07.2017.

It is located at a distance of about 35 Kilometers from Jhang Sadar. It falls in semi arid zone with desert on its right and Rechna Doab on its left.

1.2	GENERAL DESCRIPTION

Trimmu Barrage was constructed in 1938 –39 as a part of the Haveli Project. It is located just below the confluence point of the river Jhelum and Chenab. The main features of the barrage are as under:

## Rang Pur Canal

## Designed discharge		=2710/1800 Cusecs

## Operating discharge	=1800 Cusecs

Crest RL			= 483.50 Ft

Regulator			= 3 Nos bays with width of 24 feet each

( 3(24 = 72 Feet )

1.3	ADMINISTRATIVE SETUP

CHAPTER-2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1	DESIGN PARAMETER OF FLOOD WORKS

| Sr. No. | Name of Bund / Embankment | Free board | Reach (Ft.) | Top width (Ft.) | Side Slopes River / Country | Length |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | RANGPUR FLOOD BUND | 6 | RD 260 To RD 306 RD 306 To RD 318 | 20 25 | 1V:3H / 1V:2H | 58+000 (11.60 C.Mile) |
| 2 | DADAL FLOOD BUND | 6 | RD 0 To RD 11 RD 11 To RD 69629 | 20 25 | 1V:3H / 1V:1.5H 1V:3H / 1V:2H | 69+629 (13.93 C.Mile) |
|  | TOTAL LENGTH |  |  |  | 25.53 |

2.2	LOCATION MAP

CHAPTER-3

BRIEF HISTORY OF PAST FLOOD EVENTS

| YEAR | DISCHARGE | BREACHED REACHES |
| --- | --- | --- |
| 1959 | Through Barrage Through Breach Total | 718255 Cs 225000 Cs 943255 Cs | 6 Nos Breaches in Right Marginal Bund RD: 16-18 |
| 1973 | Through Barrage Through Breach Total | 666910 Cs 66000 Cs 732910 Cs | 4 Nos Breaches in Right Marginal Bund RD: 16-18 |
| 1992 | Through Barrage Through Breach Total | 683117 Cs 205000 Cs 888117 Cs | 6 Nos Breaches in Right Marginal Bund RD: 16-18 |
| 2014 | Through Barrage Through Breach Total | 626006 Cs 77000 Cs 703006 Cs | 6 Nos Breaches in Right Marginal Bund RD: 16-18 |

Events Flood 2014

| Sr. No. | Date of occurrence | Time | Nature of incidents | Place of incidents | Efforts made for controlling incidents | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 08-09-2014 | 5 :00 PM | Right pocket become non modular | Barrage |  |  |
| 2 | 09-09-2014 | 7 :20 PM | Leakage of dangerous nature | RD:44+360 LMB | By effective watching and exercising timely protective measure with the help of deployed machinery and flood fighting material, leakages, even of dangerous nature were controlled | Public property saved |
| 3 | 10-09-2014 | 1 :00 AM | Main Weir + Right Pocket Gates become free | Barrage |  |  |
| 4 | 10-09-2014 | 2:25 AM | Seepage of dangerous nature | RD:44+450 LMB |  |  |
| 5 | 10-09-2014 | 4:10 AM | Very serious leakage | RD:20+000 LMB |  |  |
| 6 | 10-09-2014 | 5:00 AM | All gates of barrage become free | Barrage |  |  |
| 7 | 10-09-2014 | 6:40 AM | Serious Seepage | RD:44+650 LMB |  |  |
| 8 | 10-09-2014 | 7:30 AM | Seepage of dangerous nature occurred | RD:44+500 LMB |  |  |
| 9 | 10-09-2014 | 8:15 AM | Seepage of dangerous nature was occurred | RD:25+940 LMB |  |  |
| 10 | 10-09-2014 | 10:30 PM | Seepage of dangerous nature was occurred | RD:44+450 LMB |  |  |

CHAPTER-4

DESIGN DATA , HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS / BARRAGES AND OR OTHER CONTROL POINTS

4.1	FLOOD LIMITS

Various flood limits of barrages as decided by flood commission on 17-04-1974 are tabulated as under

| River | Site | Design Capacity | Low Flood | Medium Flood | High Flood | Very High Flood | Exceptionally High Flood |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Lac Cusecs | Lac Cusecs | Lac Cusecs | Lac Cusecs | Lac Cusecs | Lac Cusecs |
| Jhelum | Kohala | 1.00 | 1.00 | 1.50 | 2.00 | 3.0 | 4.00 |
|  | Mangla | 10.00 | 0.75 | 1.10 | 1.50 | 2.25 | 3.00 |
|  | Rasool | 8.50 | 0.75 | 1.10 | 1.25 | 2.23 | 3.00 |
| Chenab | Marala | 11.00 | 1.00 | 1.50 | 2.00 | 4.00 | 6.00 |
|  | Khanki | 8.00 | 1.00 | 1.50 | 2.00 | 4.00 | 6.00 |
|  | Qadirabad | 9.00 | 1.00 | 1.50 | 2.00 | 4.00 | 6.00 |
|  | Trimmu | 6.45 | 1.50 | 2.00 | 3.00 | 4.50 | 6.00 |
| Ravi | Jassar | 2.75 | 0.50 | 0.75 | 1.00 | 1.50 | 2.00 |
|  | Shahdara | 2.50 | 0.40 | 0.65 | 0.90 | 1.35 | 1.80 |
|  | Balloki | 2.25 | 0.40 | 0.65 | 0.90 | 1.35 | 1.80 |
|  | Sidhanai | 1.75 | 0.30 | 0.45 | 0.60 | 0.90 | 1.20 |

4.2	TIME LAG OF FLOODS

The time lag of the peaks for river Jhelum and Chenab calculated by using the data of the past years is tabulated as under

| Sr. No. | Stage | River Chenab | River Jhelum |
| --- | --- | --- | --- |
|  |  | Marala to Khanki 39 Miles | Marala to Qadirabad 57 Miles | Qadirabad to Trimmu 163 Miles | Mangla to Rasool 43 Miles | Rasool to Trimmu 178 Miles |
|  |  | Hours | Hours | Hours | Hours | Hours |
| 1 | 0.5 to 1 lac Cusecs | 10 | 12 | 40 | 16-20 | 48 |
| 2 | Low Flood | 12 | 15 | 48 | 15 | 54 |
| 3 | Medium Flood | 14 | 16 | 60 | 12 | 60 |
| 4 | High Flood | 15 | 18 | 66-72 | 10 | 66-72 |
| 5 | Exceptionally High Flood | 15 | 18 | 78 | 8 | 72-78 |
| 6 | As approved by the federal Flood Commission for the months of July and August | 15 | 48 | 48 | 24 | 48 |

4.3	HIGHEST FLOODS

The history of highest floods is as under:-

| Year | Flood Level | Through Head Works | Through Breaches in embankments | Total |
| --- | --- | --- | --- | --- |
|  | U/S | D/S |  | Left Side | Right Side |  |
| 1959 | 492.1 | 489.5 | 718255 | - | 225000 | 943255 |
| 1960 | 490 | 488.5 | 605132 | - | - | 605132 |
| 1973 | 494.3 | 491.15 | 666910 | - | 66000 | 732910 |
| 1992 | 494.4 | 490.8 | 683117 | - | 205000 | 888117 |
| 1995 | 494.3 | 493.5 | 629561 | - | - | 629561 |
| 1997 | 494.5 | 491.95 | 677417 | - | - | 677417 |
| 2014 | 494.6 | 494.2 | 626003 | - | 77000 | 703006 |

4.4	PEAK DISCHARGES

The history of peak discharges is as under:-

| Year | Date | Discharge |
| --- | --- | --- |
| 2001 | 18.08.2001 | 72431 |
| 2002 | 17.08.2002 | 108627 |
| 2003 | 8.8.2003 | 122892 |
| 2004 | 21.08.2004 | 42756 |
| 2005 | 11.7.2005 | 162097 |
| 2006 | 7.9.2006 | 266270 |
| 2007 | 15.03.2007 | 173532 |
| 2008 | 7.8.2008 | 54234 |
| 2009 | 21.08.2009 | 46765 |
| 2010 | 11.8.2010 | 323026 |
| 2011 | 26.09.2011 | 127790 |
| 2012 | 7.8.2012 | 67694 |
| 2013 | 21.08.2013 | 267609 |
| 2014 | 10.9.2014 | 703006 |
| 2015 | 29.07.2015 | 150865 |
| 2016 | 10.08.2016 | 153339 |
| 2017 | 21.07.2017 | 92595 |
| 2018 | 16.08.2018 | 94680 |
| 2019 | 22.08.2019 | 105821 |
| 2020 | 01.09.2020 | 206077 |

CHAPTER-5

FLOOD FIGHTING STRATEGY

The following precautionary measures are adopted before flood season to face any alarming situation at Trimmu Barrage even then arrangements are necessary to avoid heavy damages and flood fighting strategy is adopted in such a way that flood water passes safely through Barrage, up to its limit.

In low flood, river water remains within the deep channel and do not cause any problem if regulation of gates is done as per rules. Watching establishment employed for this purpose will remain busy in removing jungle, filling gharas and porcupine holes          if any.

- Medium Flood

When river water enters into Medium Flood i.e 2 to 3 Lacs, it will start spreading on adjoining area and also touching the toe of bunds. Then it becomes necessary to be more vigilant. The watching of flood bunds will start to avoid any leakage from bunds. Sub Engineers will shift their camps to sites as per duty roaster. Hourly gauges and discharge will be conveyed to Civil Administration and flood warning centers to inform public accordingly.

ii) 	HIGH FLOOD

When river water enters into high flood range i.e 3 to 4.5 Lacs, Sub Divisional Officer Head Works will shift his camp at Trimmu Barrage to supervise staff working on L.M.B and D/S Spurs. In whole period regulation will be done in such a way that silt deposit in front of canals may be washed D/S of the river to minimize silt entry in to canals. Silt contents in water will be checked thrice a day and if it exceeds the permissible limit, canals will be closed accordingly. In Medium to high flood stage 02No. excavator, 04 No. Trolleys / Dumpers , 02 No. Tractor with front blade required.

iii) 	EXCEPTIONALLY HIGH FLOOD

Gauges of different sites especially gauge at RD: 15000 of L.M.B will be noted regularly and recorded. Executive Engineer will inform all agencies especially civil administration as well as Army about flood situation in rising position. In case of very high flood or exceptionally high flood, meeting will be held in field office with Army and Civil Administration to face the situation.

Two dozers will be kept ready at RD: 16000 to 18000 R.M.B for making cuts and closing breaches as and when required according to circumstances. When gauge RD: 15000 L.M.B touches level 500.00 and is found in rising position it will be the duty of Executive Engineer to request Army for operation of breach section for the safety of Barrage. When water subsides, the breaching sections will be closed (if operated) as soon as possible.

CHAPTER-6

FLOOD DAMAGES RESTORATION WORKS

There are no flood damage restoration works under execution in 18 Hazari Sub Division for the year 2020.

CHAPTER-7

FLOOD FIGHTING WATCHING ARRANGEMENTS

- UPTO DATE STATUS OF RESERVE STOCK OF STONE.

| Sanctioned Stock of Stone | Available Quantity | Defected Quantity | Remarks |
| --- | --- | --- | --- |
| - | - | - | - |

- UPTO DATE STATUS OF RESERVE STOCK OF STONE.

DETAIL STRUCTURE WISE

| Sr. No. | Name of Structure | Sanctioned Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| - | - | - | - | - | - |

7.1	PRE FLOOD ARRANGEMENTS

The watching establishment on marginal bunds is required to be employed as per following scale in accordance with the approval given by Superintending Engineer Haveli Canal Circle Multan vide his letter No. 6272-73/170-W dated  31-05-1974 (Duty Roaster attached). In addition to previous mentioned material, which will be placed at different hut sites, an additional material will be also be required in order to meet with extraordinary worst situation and to recoup the site situation.

As a guide the following scale is assumed to be sufficient. The Executive Engineer with the consultation of the Superintending Engineer, Haveli Canal Circle, Multan / Director Technical / DPD PMO Punjab Barrages, Lahore can increase the scale:

Flood Management Strategy For Flood Season 2021.

- Weak sites of flood bund / river training works have been attended / being attended.

- Data boards / gauges, RD Marks have been updated.

- Deficient reserve stock of stone has been recouped. 17.94 Lac cft reserve stock of stone is available to face any emergent situation during flood.

- Flood Fighting material is available to fight and pass the flood safely.

- Gates and gearing system of the Barrage have been checked and is functioning properly.

- Critical reaches of flood bunds are being attended to avoid any mishap.

- Breaching section has been restored.

- On receipt of flood warning, watching establishment will immediately be deployed on flood bunds as per flood fighting plan. Critical reaches of flood bund will be focused with much more care.

| Sr. No. | Item | Scale |
| --- | --- | --- |
| 1. | A xes | 2 No per mile |
| 2. | Kassies with handles | 1 for each beldar + 10% (for one shift only) |
| 3. | Hammer 2.5 lbs | 1 per mile |
| 4. | Hammer 10 lb | 2 per mile |
| 5. | Buckets (12 inch size) | 5 No. per mile |
| 6. | Sludge hammer 14 lbs | 1 per mile |
|  | Sand | Collection of 200 cft. Every mile for dangerous portions |
| 8. | Stacks (6-8 feet) long | 100 stacks per mile |
| 9. | Khajji mats 3’*4’ | 50 Nos per mile |
| 10. | Baskets | 1 toot/2 Pilchi baskets per beldar of shift twice a month |
| 11. | Sutli | 1 lb per 100 bags |
| 12. | Needles | 4 Nos per beldar huts |
| 13. | Kassi Handles | 50% of the no. of kassies as spare |
| 14. | Munj/Patha/Pees/ Taranger 3 cft capacity of stone. | 500 Nos for each structure. |
| 15 | Toot basket | 100 Nos each Sub Engineer |
| 16. | Torches – 3 cell | 1 for Executive Engineer, 1 for Sub Divisional Officer, 1 for Sub Engineer 1 one spare |
| 17. | Cells for Torches | 1 full and six spare sets |
| 18. | Fuel for lighting fire | To be collected by beldar establishment |
| 19. | Kerosine Oil | As per practice 1/3 bottle per lantern per night and one bottle per patromax per night (22 nights per month) |
| 20. | Match Boxes | 1 match box per month |
| 21 | Spirit | 1 bottle per patromax per month |
| 22. | Funnels | 2 No. per watching hut |
| 23. | Larmal 50 feet long | 50 per watching hut |
| 24. | Mallets wooden | 5 mallets per watching hut |
| 25. | Tranger wire | 1 roll of 14 BSW gauge at each bund |
| 26. | Gunny bags | 100 bags per mile |

Watching huts are almost available on all the embankments for the storage of the watching material and shelter for staff on or off duty. The watching material will be shifted into these huts at the start of the flood season.

Officer in-charge will issue the material as and when emergency arises. There is some material available from the last years received back after use in the flood only balance will be procured to meet the requirement of this year.

7.2	WATCHING ESTABLISHMENT

| Sr.# | Name of Bunds | Site | Flood Limit |
| --- | --- | --- | --- |
|  |  |  | Low | Medium | High | Very High | Exceptionally High |
|  |  |  | Man | Shift | Man | Shift | Man | Shift | Man | Shift | Man | Shift |
| 1 | Rangpur Flood Bund | RD 292+000 | - | - | 10 | 3 | 22 | 3 | 26 | 3 | 30 | 3 |
|  |  | RD 304+000 | - | - | 10 | 3 | 22 | 3 | 26 | 3 | 30 | 3 |
| 2 | Daddal Flood Bund | RD 28+000 | - | - | 10 | 3 | 22 | 3 | 26 | 3 | 30 | 3 |
|  |  | RD 64+000 | - | - | 10 | 3 | 22 | 3 | 26 | 3 | 30 | 3 |

7.3	ARRANGEMENT AT SENSITIVE SITES.

Relates to Trimmu Head Works

7.4	WATCHING MATERIAL

| Sr.No. | Description | unit | required quantity | Available quantity | Balance quantity | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No. | 2 | 2 | 0 |  |
| 2 | Baskets | No. | 38 | 30 | 8 |  |
| 3 | Buckets | No. | 6 | 6 | 0 |  |
| 4 | Burner and Lamps | No. | 1 | 1 | 0 |  |
| 5 | Cell for Torches | No. | 6 | 6 | 0 |  |
| 6 | Chimnies | No. | 5 | 5 | 0 |  |
| 7 | Chimnies of Gas | No. | 1 | 1 | 0 |  |
| 8 | Funnel (Ordinary) | No. | 2 | 2 | 0 |  |
| 9 | Funnel with W.G | No. | 1 | 1 | 0 |  |
| 10 | Gas Lamp | No. | 1 | 1 | 0 |  |
| 11 | Gunny Bags | No. | 160 | 160 | 0 |  |
| 12 | Hammer 2.5 lb | No. | 1 | 1 | 0 |  |
| 13 | Hammer 10 lb | No. | 2 | 2 | 0 |  |
| 14 | Kassi with handles | No. | 10 | 10 | 0 |  |
| 15 | Kerosene Oil | Ltr | 54 | 54 | 0 |  |
| 16 | Khajji Mate | No. | 60 | 60 | 0 |  |
| 17 | Lanterns | No. | 10 | 10 | 0 |  |
| 18 | Larmal 50 Ft | No. | 40 | 40 | 0 |  |
| 19 | Mallet wooden | No. | 4 | 4 | 0 |  |
| 20 | Match Box | No. | 17 | 0 | 17 |  |
| 21 | Mental | No. | 15 | 0 | 15 |  |
| 22 | Needles | No. | 1 | 1 | 0 |  |
| 23 | Needles for sewing bags | No. | 3 | 3 | 0 |  |
| 24 | Nozzles | No. | 1 | 1 | 0 |  |
| 25 | Oil Extractor | No. | 1 | 1 | 0 |  |
| 26 | Sledge Hammer 14 lb | No. | 1 | 1 | 0 |  |
| 27 | Spare handle for kassises | No. | 1 | 1 | 0 |  |
| 28 | Spirit | Bottles | 1 | 1 | 0 |  |
| 29 | Spirit Can | No. | 170 | 170 | 0 |  |
| 30 | Sticks (6-8) | No. | 1 | 1 | 0 |  |
| 31 | Sutli | Lb | 1 | 1 | 0 |  |
| 32 | Torch 3 Cell | No | 1 | 1 | 0 |  |
| 33 | Tranger Wire | CWT | 1 | 1 | 0 |  |
| 34 | Washers | No | 1 | 1 | 0 |  |
| 35 | Wicks | Yards | 8 | 8 | 0 |  |
| 36 | Petrol for generator | Liter | 0 | 0 | 0 |  |
| 37 | Diesel for Patrolling | Liter | 10 | 0 | 10 |  |
| 38 | Empty Drum | Each | 400 | 370 | 30 |  |
| 39 | Polythene Bag | Each | 0 | 0 | 0 |  |
| 40 | Bamboos | Each | 100 |  | 100 |  |

7.5	ARRANGEMENT FOR SOUNDING AND PROBING

The arrangement for sounding and probing will be taken up with the boat. An extra boat equipped with bathymetric arrangements is also available for drawing of sounding and probing by using software.

7.6	LIGHTING ARRANGEMENT

NIL

7.7	RATION ARRANGEMENT

Ration is provided by the Irrigation Department to the watching establishment deployed along flood bunds during flood days. However ration for displayed person from the flood area is provided by District Administration and NGOs.

7.8	P.O.L ARRANGEMENT FOR VEHICLE.

## Relates to Civil Administration District Muzafarghar & District Jhang

7.9	TRANSPORTATION

## Relates to Civil Administration District Muzafarghar & District Jhang

7.10	LAW AND ORDER

# (Attention: Deputy Commissioner & District Police Officer Jhang)

Police guard is already posted at head works Police department and the D.C Jhang will be requested to increase the strength so that the flood emergency measures are not interrupted. Police will be particularly requested to quell any effort made by the public to cut or breach any bund or embankment. In case miscreants try to cut any flood bund, the officer incharge will immediately call for the help of police. In case of any other type of law and order situation, the call for police will be made to deal with the situation, so that the flood emergency measure may go un-interrupted. The police will also be responsible for the protection of the installments at the barrage. Furthermore security guards are also hired for protection of Trimmu Barrage. The canal guards equipped with weapons are also available with the Sub Divisional Officers of Trimmu Barrage Division.

7.11	MEDICAL ARRANGEMENT FOR LABOUR

# (Attention: Chief Executive Officer Health, Jhang)

There is one Dispensary available at Trimmu Barrage to deal any emergency labour working at Rehabilitation Project of Trimmu Barrage. The Chief Executive Officer, Jhang will be requested to set up a medical facility at Trimmu Headworks having trained and experienced staff along with the sufficient medicine during the flood season. The staff will remain present for 24 hours to meet with the emergency during the extreme flood at Trimmu.

7.12	LIAISON WITH OTHER DEPARTMENT

# (Attention: Irrigation/Civil/Police department)

Sub Divisional Officer, will have close liaison with their counterparts of other departments and will call for any support they deem fit from them. Close contact will be maintained with civil authorities and police departments for all emergency measures. They will be constantly kept informed of the flood situation at 18Hazari Sub Division.

  - ROLE OF THE ARMY

-NIL-

7.14	DUTIES OF TELEPHONE ATTENDANT

| Sr.No. | Name of Officer / Official | Telephone # | Period | Time |
| --- | --- | --- | --- | --- |
|  |  |  |  | From | To |
| 1 | Mr. Qasim Ali Waris Sub Divisional Officer 18-Hazari Sub Division | 0323-4566538 | 24-hours | 24-hours |
| 2 | Mr. Aslam Pervaiz Sub Engineer Pir Abdul Rehman Section | 03247008563 | 24-hours | 24-hours |

The telephone attendant will present 24 hours turn wise. They will receive gauges from all related stations and pass on to concerned quarter for necessary action. An emergency Flood Control Center is established in Telegraph office of Trimmu Barrage Division during Flood days for the said purpose round the clock.

7.15	WIRELESS ARRANGEMENTS

There are two wireless sets working in Trimmu Barrage Division. One is working in Telegraph office Trimmu, and second with police is working at the Barrage. The wireless sets in vehicles will be provided by the DPO concerned before the  coming flood.

Chapter - 08

STATUS OF ENCROACHMENT OF 18-HAZARI SUB DIVISION

- DETAIL OF ENCROACHMENT

| Sr. No | Total Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| -NIL- |

- DETAIL OF CRITICAL ENCROACHMENT

| Sr. No | Total Critical Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| No critical encroachment |

Chapter - 09

DUTY ROSTER / FLOOD FIGHTING PROGRAM

## Phase I - (Pre Flood Period)

This phase covers the pre flood period starting from start of the flood season upto the time the flood water raises upto 1 foot above general Natural Surface Level (NSL) along the flood bunds.

##### WATCHING:  Flood watching establishment will be arranged according to flood scales / stages after consultation with the concerned authority and other essential need at site.

| Stage | Strength |
| --- | --- |
| Water level is 1 foot above NSL or below along the flood bund | 1 watchman per mile per shift in two shifts during 24 hours on Marginal and other flood bunds |
| Water level is more than1 foot above NSL along the flood bund | 1 watchman per mile per shift in three shifts during 24 hours on Marginal and other flood bunds |

During this phase the Sub Divisional officers of the bunds and respective Sub Engineers of the sections of the bunds will be the controlling officers under the overall supervision of the Executive Engineer, Trimmu Barrage Division, Trimmu.

Phase II – (Low Flood i.e. 1.5  to 2.0 Lac cusecs)

This phase starts when the discharge at the Trimmu Barrage is between 1.5 to 2 Lac cusecs. The details of the actions to be taken during this phase are as follows:

| Activity | Action |
| --- | --- |
| Shifting of watching & necessary flood material to watching huts | Respective Sub Engineers, SDO, XEN. |

| Stage | Strength |
| --- | --- |
| The discharge ranges between 1.5 to 2.0 lac cusecs | 2 persons per mile per shift in three shifts during 24 hours on Marginal and other flood bunds 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 foot above NSL. |

Supervisory Staff

The duty roster during this phase of the flood, officers/officials duties are tabulated below. The officials under the overall control of the sub-divisional officers concerned will perform the duties.

| Sr. No. | Location | Duty of Officer/Official |
| --- | --- | --- |
| 1 | Dadal Flood Bund (RD 0 – 25 ) Dadal Flood Bund (RD 25 – tail ) Embankment of 1L/3L (RD 5 – 15380) | Sub Engineer Pir Abdur Rehman Sub Engineer Lashari Sub Engineer Lashari |
| 2 | Rangpur Flood Bund ( RD 292) Rangpur Flood Bund ( RD 260 - 320) Rangpur Flood Bund ( RD 304 - 318) | Subdivisional Officer AtharaHazari Sub Engineer Rangpur Sub Engineer Diana |

Phase III – (Medium Flood i.e. 2.0  to 3.0 Lac cusecs)

This phase starts when the discharge at the Trimmu Barrage crosses the medium level and is upto high level flood i.e. between 2.0 to 3.0 Lac cusecs. The details of the actions to be taken during this phase are as follows:

| Stage | Strength |
| --- | --- |
| The discharge ranges between 2.0 to 3.0 lac cusecs | 4 persons per mile per shift in three shifts during 24 hours on Marginal and other flood bunds 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 foot above NSL. |

Supervisory Staff

The duty roster during this phase of the flood, officers/officials duties are tabulated below. The officials under the overall control of the concerned Sub Divisional officers will perform the duties.

| Sr. No. | Location | Duty of Officer/Official |
| --- | --- | --- |
| 1. | Dadal Flood Bund (RD 0 – tail ) Embankment of 1L/3L | Sub Engineer, Pir Abdur Rehman |
| 2. | Rangpur Flood Bund ( RD 292) Rangpur Flood Bund ( RD 260 - 320) Rangpur Flood Bund ( RD 304 – 318) | Sub divisional Officer AtharaHazari Sub Engineer Rangpur Sub Engineer Diana |

Phase IV – ( High Flood i.e. 3.0  to 4.5 Lac cusecs)

Relates to Trimmu Head Works

CHAPTER-10

EMERGENCY TELEPHONE NUMBERS

| Sr. No. | Departments | Office | Residence |
| --- | --- | --- | --- |
| 1 | Secretary I& Department Lahore | 042-99212117-18 | 042-35731116 |
| 2 | District Coordination Officer Jhang | 047-9200081 | 9200181 |
| 3 | District Officer (Revenue) | 047-9200107 | 9200299 |
| 4 | Deputy District Officer (Revenue) | 047-9200433 | 9200422 |
| 5 | D.D.O.(R) Jhang. | 047-9200433 | 9200422 |
| 7 | D.P.O Jhang | 047-9200444 | 9200445 |
| 8 | Add: D.P.O Jhang | 047-9200094 | 9200040 |
| 9 | S. D.P.O Sadar | 047-9200312 |  |
| 10 | Wireless Control | 047-9200066 |  |
| 11 | Army Flood Officer 72 Medium GRW | 2695064/5 |  |
| 12 | District & Session Judge | 047-9200092 | 9200096 |
| 13 | Executive Engineer Jhang Division L.C.C (W) Jhang | 047-9200300 | 03004021263 |
| 14 | Chief Engineer D & F Zone Lahore | 042-99230731 Fax:5862081 | 0300-4080364 |
| 15 | Telegraph Office Faisalabad | 041-9200774 |  |
| 16 | Flood Warning Centre Lahore | 042-7572091-93 | Fax: 7572092 |
| 17 | Flood Emergency Office Faisalabad | 041-9200270 |  |
| 18 | Chief Engineer Irrigation Faisalabad | 041-9200268 | 9200269 |
| 19 | Executive Engineer Khanki Division | 055-6266239 055-6605255 | 766239 |
| 20 | Executive Engineer Trimmu | 047-7647200 |  |
| 21 | Executive Engineer Q.B Link Division Farooqabad | 0563-874046 | 0563-876430 |
| 22 | Superintending Engineer Q.B Link Circle Farooqabad | 04945-874046 | 04945-2843 |
| 23 | Superintending Engineer, Lower Chenab Canal West Circle Faisalabad | 041-9200272 | 041-9200279 |
| 24 | Director Flood / Secretary, Flood Commission Punjab, Lahore | 042-99231614 | 0300-4777120 |
| 25 | Executive Engineer Qadirabad Barrage Division | 0547-550190 | 550198 |
| 26 | Tele Office Qadirabad Barrage Division | 0547-550490 |  |
| 27. | Sub Divisional Officer, 18-Hazari Sub |  | 0320411301 |

CHAPTER-11

STANDARD OPERATION PROCEDURE (SOP) FOR BREACHING SECTIONS

11.1	HISTORY OF THE BREACHING SECTION

There is no breaching section under the control of 18-Hazari Sub Division.

11.2	LOCATION, DESIGN, QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATION.

There is no breaching section under the control of 18-Hazari Sub Division.

11.3	ARRANGEMENT OF EXPLOSIVE & SECURITY OF EXPLOSIVE STORES

There is no breaching section under the control of 18-Hazari Sub Division.

CURRENT STATUS OF EXPLOSIVE / ACCESSORIES

There is no breaching section under the control of 18-Hazari Sub Division.

11.4	LIST OF SECURITY STAFF ALONG WITH DETAIL OF THEIR TRAINING ETC

There is no breaching section under the control of 18-Hazari Sub Division.

11.5	DETAIL OF  MECHANICAL MEANS AS A STANDBY ARRANGEMENTS IN CASE OF DETONATION FAILURE

The breaching section is activated with the help of the Army personal with explosive materials available at site. In case of the failure of this method, two No. Bulldozers and one No. excavator will be deployed to cause cuts in the Right Marginal Bund. For this purpose standby labour is also deployed. Furthermore  six bulldozers have been requested to be arranged by the Deputy Commissioner, Jhang.

In the event of the activation of the breaching section, the flood waters spread surround 18-Hazari Town and travels in 3 directions as enunciated below:-

1.  	Main current hits Rangpur Canal between RD: 21000-23000.

2. 	Another current flows in creek cuts through 1-R Disty between RD: 3000 and 4000 then hits to Rangpur Canal between RD: 44000-45000.

3.	3rd current flows in depression along sand dunes and 2-R Disty up to RD: 13000 and then hits to Rangpur Canal between RD: 74000-75000 being a natural depression.

11.6	DUTY ROSTER IN CASE OF CRITICAL SITUATION

Relates to Trimmu Head Works

11.7	BREACHING COMMITTEE WITH THEIR ACTION PLAN

Relates to Trimmu Head Works

11.8	LIST OF VILLAGES LIKELY TO BE INUNDATED IN CASE OF BREACH

The water escaping through the activated breaching section will flow along Right Bank of Rangpur Canal crossing Jhang-Muzaffar Garh Road at 30 KM from Jhang. The flood water traveling along Rangpur Canal crosses through cuts at Rangpur Canal at RD: 22000, 44000 and 80000 and remaining water spreads between Right Bank of Rangpur Canal and sand dunes up to a distance of about 100 K.M from Trimmu Barrage.

The area likely to be effected / inundated by the spills due to activation of the breaching section will be about 156500 acres. The villages / abadies and other infrastructures like road, canals etc inundated / damaged are detailed here under:-

| S# | Tehsil | Villages |
| --- | --- | --- |
| 1 | Tehsil Jhang | Dhoin Muhammad , Mansoor Sial , Diraj , Kot Khera, Mohal, Guniana, Wijhlana. Total Village = 7 Nos. |
| 2 | Tehsil 18-Hazari | Mari Shakir, Kot Shakir, Machiwal, Sajhran , Kot Maldave, Munday Syed, Dosa, Dabi, Umran Janubi, Kamra, Baila Chotra , Lateef Shah, Basti Sanga, Loaharan Wala, Kharal Sipra, Kotla Naik Ahmed, Kotli Baqir Shah, Gari Fateh Ullah, Sheroana, Loha Bhir, Johiya, Ahmed Abas, Bela Shar, Bolla Patwana. Rashid Pur , Jbanoana, Dhan Miani, Pahar Pur, Kot Murad, Rodo Sultan, Taror, Kot Rustum, Basti Nusrat , Dhoin Muhammad, Lashari, Malkana, Total Village = 36 |
| 3 | Tehsil Ahmed Pur Sial | Sultan Bahoo, Dull, Diraj, Pir Abdul Rehman , Saman. Sadan Naikokara Kotli, Mehmood Shah , Garh Maharaja , Chak 5/2-L, Tiba Gehli, Fateh Pur, Toba Jusa, Fateh Pur, Islam Pur Nashaib, Islam Pur faraz, Chak Norang Shah, Kot Mupal, Inayat Shah. Saiwa Sadhana. Total Village =23 |
| 4 | Tehsil Muzaffar Garh | Maqsoodpur , Dera Fazil ,Bahadaur, Amir Pur, Sargana, Kirari Ali Mardan , Kacha Nashaibi, Behram Pur ,Chbootra Mamil, Fatoo Fanaka, Dera Hayat, Bahli Shumali, Sadi Pur, Makoo Jamal Total Village = 13 |
|  | TOTAL VILLAGES | 79 Nos |

11.9	ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENTS

Relates to Trimmu Head Works

11.10	DETAIL OF COORDINATION WITH CIVIL / ARMY AUTHORITIES

Relates to Trimmu Head Works

11.11	PARALLEL COMMUNICATION ARRANGEMENT

In addition to installation of Wireless set at Trimmu Barrage some temporary connection will be required at left side of the Barrage as well as field office where all the Officers / Officials will meet together to chalk out further programs. One supervisor of T & T Department will remain available at site for proper control and operation of all this system.

11.12	INDEX PLAN

(Attached)

Sub Divisional Officer,					Executive Engineer,

18-Hazari  Sub Division 	 				Jhang Division LCC(W)

Garh More		.					Jhang.

Superintending Engineer,					Chief Engineer

Lower Chenab Canal(W)Circle,				Faisalabad Irrigation Zone,

Faisalabad.							Faisalabad

PART - B

CHAPTER-12

VULNERABLE SITES ON FLOOD BUND / STRUCTURES

12.1	APPREHENDED BREACHES IN FLOOD BUNDS / STRUCTURES

| Sr.No. | Name of Structure | Location of Vulnerable Site | Reference of contingency Plan |
| --- | --- | --- | --- |
| 1 | Rangpur Flood Bund | RD 303+000 to RD 318+000 |  |

12.2	OPERATION OF BREACHING SECTION

There is no breaching section under the control of 18-Hazari Sub Division.

12.3	BREACHES DUE TO RISING OF FLOOD WATER, DETERIORATION FLOOD BUNDS ETC.

There is no breaching section under the control of 18-Hazari Sub Division.

CHAPTER-13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE (SITES) LISTED ABOVE. EMERGENCY CONTINGENCY PLAN MUST INCLUDE

PLAN NO. 1

RD: 303+000 – 318+000 Rangpur Flood Bund

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

Plan Attached

13.2	DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.

- Rangpur Town.

- Kaudi Wal

- Kari Ali Mardan

- Bahrampur

- Chabootra Kamal

- Dera Habit

13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL. THIS MAY INCLUDE.

The employed labour, Flood Fighting Material and available machinery will be deployed on the breach for control of spilling water coming out from the breach. All efforts will be made to control the breach.

13.3.1	ARRANGEMENTS

The following arrangements will be made.

13.3.2 ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood fighting camp will be established at RD: 303+000 of Rangpur Flood Bund

13.3.3 DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP SITES

Sub Engineer Rangpur section will be incharge of the camp site. The following staff will be present at the camp site.

Sub Engineer			=	1 No.

Mate					=	4 No.

Beldar					=	36 Nos

13.3.4 DEPARTMENTAL MACHINERY AVAILABLE

Not available

13.3.5 MACHINERY AVAILABLE FROM PRIVATE SOURCE

The following machinery can be made available through private source i.e Government contractors.

- Excavator.

- Showal.

- Tractor with Trolleys

- Dozers

- Tractor with front blade.

The numbers of machinery will increase or decrease as per flood stage.

13.3.6 FLOOD FIGHTING MATERIAL REQUIRED

| Sr.No. | Description | unit | required quantity | Available quantity | Balance quantity | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No. | 2 | 2 | 0 |  |
| 2 | Baskets | No. | 38 | 30 | 8 |  |
| 3 | Buckets | No. | 6 | 6 | 0 |  |
| 4 | Burner and Lamps | No. | 1 | 1 | 0 |  |
| 5 | Cell for Torches | No. | 6 | 6 | 0 |  |
| 6 | Chimnies | No. | 5 | 5 | 0 |  |
| 7 | Chimnies of Gas | No. | 1 | 1 | 0 |  |
| 8 | Funnel (Ordinary) | No. | 2 | 2 | 0 |  |
| 9 | Funnel with W.G | No. | 1 | 1 | 0 |  |
| 10 | Gas Lamp | No. | 1 | 1 | 0 |  |
| 11 | Gunny Bags | No. | 160 | 160 | 0 |  |
| 12 | Hammer 2.5 lb | No. | 1 | 1 | 0 |  |
| 13 | Hammer 10 lb | No. | 2 | 2 | 0 |  |
| 14 | Kassi with handles | No. | 10 | 10 | 0 |  |
| 15 | Kerosene Oil | Ltr | 54 | 54 | 0 |  |
| 16 | Khajji Mate | No. | 60 | 60 | 0 |  |
| 17 | Lanterns | No. | 10 | 10 | 0 |  |
| 18 | Larmal 50 Ft | No. | 40 | 40 | 0 |  |
| 19 | Mallet wooden | No. | 4 | 4 | 0 |  |
| 20 | Match Box | No. | 17 | 0 | 17 |  |
| 21 | Mental | No. | 15 | 0 | 15 |  |
| 22 | Needles | No. | 1 | 1 | 0 |  |
| 23 | Needles for sewing bags | No. | 3 | 3 | 0 |  |
| 24 | Nozzles | No. | 1 | 1 | 0 |  |
| 25 | Oil Extractor | No. | 1 | 1 | 0 |  |
| 26 | Sledge Hammer 14 lb | No. | 1 | 1 | 0 |  |
| 27 | Spare handle for kassises | No. | 1 | 1 | 0 |  |
| 28 | Spirit | Bottles | 1 | 1 | 0 |  |
| 29 | Spirit Can | No. | 170 | 170 | 0 |  |
| 30 | Sticks (6-8) | No. | 1 | 1 | 0 |  |
| 31 | Sutli | Lb | 1 | 1 | 0 |  |
| 32 | Torch 3 Cell | No | 1 | 1 | 0 |  |
| 33 | Tranger Wire | CWT | 1 | 1 | 0 |  |
| 34 | Washers | No | 1 | 1 | 0 |  |
| 35 | Wicks | Yards | 8 | 8 | 0 |  |
| 36 | Petrol for generator | Liter | 0 | 0 | 0 |  |
| 37 | Diesel for Patrolling | Liter | 10 | 0 | 10 |  |
| 38 | Empty Drum | Each | 400 | 370 | 30 |  |
| 39 | Polythene Bag | Each | 0 | 0 | 0 |  |
| 40 | Bamboos | Each | 100 |  | 100 |  |

13.6.7 FLOOD FIGHTING MATERIAL AVAILABLE

| Sr.No. | Description | unit | required quantity | Available quantity | Balance quantity | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No. | 2 | 2 | 0 |  |
| 2 | Baskets | No. | 38 | 30 | 8 |  |
| 3 | Buckets | No. | 6 | 6 | 0 |  |
| 4 | Burner and Lamps | No. | 1 | 1 | 0 |  |
| 5 | Cell for Torches | No. | 6 | 6 | 0 |  |
| 6 | Chimnies | No. | 5 | 5 | 0 |  |
| 7 | Chimnies of Gas | No. | 1 | 1 | 0 |  |
| 8 | Funnel (Ordinary) | No. | 2 | 2 | 0 |  |
| 9 | Funnel with W.G | No. | 1 | 1 | 0 |  |
| 10 | Gas Lamp | No. | 1 | 1 | 0 |  |
| 11 | Gunny Bags | No. | 160 | 160 | 0 |  |
| 12 | Hammer 2.5 lb | No. | 1 | 1 | 0 |  |
| 13 | Hammer 10 lb | No. | 2 | 2 | 0 |  |
| 14 | Kassi with handles | No. | 10 | 10 | 0 |  |
| 15 | Kerosene Oil | Ltr | 54 | 54 | 0 |  |
| 16 | Khajji Mate | No. | 60 | 60 | 0 |  |
| 17 | Lanterns | No. | 10 | 10 | 0 |  |
| 18 | Larmal 50 Ft | No. | 40 | 40 | 0 |  |
| 19 | Mallet wooden | No. | 4 | 4 | 0 |  |
| 20 | Match Box | No. | 17 | 0 | 17 |  |
| 21 | Mental | No. | 15 | 0 | 15 |  |
| 22 | Needles | No. | 1 | 1 | 0 |  |
| 23 | Needles for sewing bags | No. | 3 | 3 | 0 |  |
| 24 | Nozzles | No. | 1 | 1 | 0 |  |
| 25 | Oil Extractor | No. | 1 | 1 | 0 |  |
| 26 | Sledge Hammer 14 lb | No. | 1 | 1 | 0 |  |
| 27 | Spare handle for kassises | No. | 1 | 1 | 0 |  |
| 28 | Spirit | Bottles | 1 | 1 | 0 |  |
| 29 | Spirit Can | No. | 170 | 170 | 0 |  |
| 30 | Sticks (6-8) | No. | 1 | 1 | 0 |  |
| 31 | Sutli | Lb | 1 | 1 | 0 |  |
| 32 | Torch 3 Cell | No | 1 | 1 | 0 |  |
| 33 | Tranger Wire | CWT | 1 | 1 | 0 |  |
| 34 | Washers | No | 1 | 1 | 0 |  |
| 35 | Wicks | Yards | 8 | 8 | 0 |  |
| 36 | Petrol for generator | Liter | 0 | 0 | 0 |  |
| 37 | Diesel for Patrolling | Liter | 10 | 0 | 10 |  |
| 38 | Empty Drum | Each | 400 | 370 | 30 |  |
| 39 | Polythene Bag | Each | 0 | 0 | 0 |  |
| 40 | Bamboos | Each | 100 |  | 100 |  |

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC SUI GAS TELEPHONE INSTALLATION, ROAD NETWORK, OTHER BUILDING, CANAL AND DRAINAGE NETWORK.

- PARCO Pipe Line

- Grid Station

- Telephone Exchange

- Rural Health Center

- Government Boys Degree College

- Vocational Institute.

- Government Schools

- Muzaffar Garh to Jhang Road.

- Rangpur to Chowk Sarwar Shaheed Road.

- 5-R Disty

- Rangpur Canal

Sub Divisional Officer,					Executive Engineer,

18-Hazari  Sub Division 	 				Jhang Division LCC(W)

Garh More		.					Jhang.

Superintending Engineer,					Chief Engineer

Lower Chenab Canal(W)Circle,				Faisalabad Irrigation Zone,

Faisalabad.							Faisalabad

.

CHAPTER NO. 14

ACTION PLAN

14.1	RE-SHUFFLING/ RECOUPING PLAN OF RESERVE STONE DEPARTMENTALLY

Relates to Head Works

14.2 -  DETAIL OF INLET / OUTLET CROSSING ALONG WITH CLOSING

METHODOLOGY

OUTLETS CROSSING THROUGH FLOOD BUNDS OF TRIMMU BARRAGE DIVISION, TRIMMU

| Sr.No. | Name of Flood Bund | Structures | Outlet RD | Location |
| --- | --- | --- | --- | --- |
| 1 | Daddal Flood Bund | - | 8510 | 3510 |
| 2 |  | - | 10486 | 5486 |
| 3 |  | - | 12468 | 7468 |
| 4 |  | - | 12488 | 7488 |
| 5 |  | - | 14440 | 9440 |
| 6 |  | - | 16456 | 11456 |
| 7 |  | - | 12000 | 12000 |
| 8 |  | - | 13000 | 13000 |
| 9 |  | - | 15500 | 15500 |
| 10 |  | - | 17600 | 17600 |
| 11 |  | - | 19200 | 19200 |
| 12 |  | - | 40500 | 40500 |
| 13 |  | - | 65900 | 65900 |
| 14 | Rangpur Flood Bund | - | 275500 | 275500 |
| 15 |  | - | 279500 | 279500 |

14.6 – POLICE DEPLOYMENT PLAN

Performa-1

| Sr. No. | Site of Breaching Section | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector /Sub Inspector / A.S.I | Constable |  |
| Relates to Civil Administration Department |

Performa-2

| Sr. No. | Vulnerable Sites used for illegal cuts during floods | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector /Sub Inspector / A.S.I | Constable |  |
| Relates to Civil Administration Department |

Performa-3

| Sr. No. | Name of Barrage | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector /Sub Inspector / A.S.I | Constable |  |
| Relates to Civil Administration Department |

14.7 – DETAILS OF SYNTHETIC BAGS WITH CAPACITY OF 500 KG & 1000 KG

| Sr. No | Name of Bund | Synthetic bags (500 Kg) | Synthetic bags (1000 Kg) | Quantity Required | Quantity Available | Balance Quantity required . |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| 1 | Dadal Flood Bund | 1000 | 500 | 1500 | - | 1,500 |
| 2 | Rangpur Bund | 500 | 250 | 750 | - | 750 |
|  | Total | 1500 | 750 | 2250 | - | 2250 |

14.8	Details of polythene sheet of black colour to protect upstream slope against wave action and to control seepage through embankments

| Sr. No | Name of Bund | Polyethene Sheets | Quantity Required | Quantity Available | Balance Quantity required . |
| --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 |
| 1 | Dadal Flood Bund | 40000Ft | 40000Ft | - | 40000Ft |
| 2 | Rangpur Bund | 43000Ft | 43000Ft | - | 43000Ft |
|  | Total | 83000 Ft | 83000 Ft | - | 83000 Ft |

CHAPTER NO. 15

BACK UP DIVISIONS (In case of Breach)

Jhang Division LCC(W), Jhang.

# Text boxes

PLAN NO.1

RD.303+000 TO 318+000 RANGPUR FLOOD BUND