GOVERNMENT OF SINDH

IRRIGATION DEPARTMENT

CONTINGENCY PLAN 2021

INSIDES

| S. No. | Description | Page No. |
| --- | --- | --- |
|  | Introduction | ( | 3 |
|  | Sindh Map | ( | 4 |
|  | River System & Flood Routing Model | ( | 5 |
|  | Bund Network | ( | 6 |
|  | Index Plan Showing Flood Protection Bunds | ( | 7 |
|  | River Discharge & Magnitude | ( | 8 |
|  | Flood Stages | ( | 9 |
|  | Yearly Maximum Recorded Discharge @ Sukkur Barrage | ( | 10 |
|  | Flood Frequency Analysis @ Gudu Barrage | ( | 11 |
|  | Identification Of All Vulnerable Points | ( | 12 |
|  | Gudu Barrage Region, Sukkur | ( | 12 |
|  | Left Bank Canal Area Water Board (SIDA) | ( | 12 |
|  | Ghotki Feeder Canal area Water Board | ( | 12 |
|  | Sukkur Barrage Left Bank Region, Sukkur | ( | 12 |
|  | Sukkur Barrage Right Bank Region, Larkana | ( | 13 |
|  | Kotri Barrage Region, Hyderabad | ( | 13 |
|  | Causes of Breaches | ( | 14 |
|  | Pre Abkalnai Arrangements | ( | 15 |
|  | During Abkalani Arrangements | ( | 17 |
|  | Important Telephone Numbers | ( | 20 |
|  | Coordination from other Departments | ( | 22 |

Introduction

Indus River is one of the world longest river. It begins in Tibet and flows into the Arabian Sea. The river system is fed mainly by snow and glaciers of the Himalayas and is one of the few rivers that exhibit a tidal bore. The flow is also determined by the seasons, being lower in winter and over flowing its banks in monsoon season, from July to September. Therefore the River Indus is the dominant source of surface water for the Indus Basin, the catchment of the river and its tributaries is 9,44,165 square kilometres (3,64,700 square miles) of which 5,61,010 square kilometres (2,16,700 square miles) lie within Pakistan. The basin can be divided into various regions based upon their physical and geographical features (Northern Mountains, Western Mountains, Potohar Plateau, Salt Range and Indus Plain). At Mithankot, the Indus receives the combined water of its five major left bank tributaries (Jhelum, Chenab, Ravi, Beas and Sutlej through Panjnad. Three barrages Gudu, Sukkur and Kotricontro the water in Sindh Province territory. The total length of Indus and Sindh is 537 miles (Gudu to Sukkur 108 miles, Sukkur to Kotri 286 miles and Kotri to Arabian Sea 143 miles)

The Sindh Province bounded to the west by Balochistan to the north by Punjab, the east by the Indian States of Gujrat and Rajasthan and to the south by the Arabian Sea. Sindh is the lower riparian of Indus Basin Irrigation System. The discharge of all the western and eastern rivers of Pakistan viz. Indus, Kabul, Jhelum, Chenab, Ravi and Sutlej accumulated at Mithan Kot and then entered in Sindh Province at Gudu Barrage. Thus Sindh Province is most vulnerable to river floods as accumulated flow from entire Indus Basin is to be conveyed to sea through the province. Moreover the river through Sindh runs on ridge, as much no quick relief is anticipated in case of breach.

Bund Network

In Sindh Province, the Indus River flows on a ridge and surrounding areas are generally lower than the river bed. Therefore, the water once leaving the Indus does not return. Escaped water thus causes greater damage to widespread areas and continues to stay there for a longer period even after the flood peaks are over.

In order to minimise such eventualities, double line of flood embankments have been constructed along almost both the banks from Gudu to few kilometres short of sea as shown in the table below. These embankments are often threatened due to active erosion bythe river flows and leakages in the embankments due to poor soils in some reaches.

Apart from this, the Flood Protective (FP) Bund was constructed to control flood flows from hill torrents in the command of right bank of Sukkur Barrage. It is 119.4 miles long, starting from the Manchar Lake in the south and Hamal Lake in the north, extending 53 miles upwards opposite Usta Muhammad towards east along Khirthar Canal named New FP Bund. This bund lies in two districts Dadu and Larkana, protecting the command area of Khirthar, Warah, Dadu and Rice Canal.

The inventory of bund in Sindh is as under: -

| S. No. | Name Of Region | 1st Line (In Mile) | 2nd Line (In Mile) |
| --- | --- | --- | --- |
| 1 | Gudu Barrage | 216 – 0 | 113 – 6 |
| 2 | Sukkur Barrage | 401 – 5 | 162 – 3 |
| 3 | Kotri Barrage | 257 – 6 | 54 – 4 |
| 4 | FP Bund | 119 | - |
| Total | 994 – 3 | 330 – 5 |
| Grand Total | 1324 – 8 |  |

River Discharge & Magnitude

The flow in the River Indus during the months of April and May varies between 30,000 cusecs to 2,00,000 cusecs. It swells as much as 7,00,000 to 12,00,000 cusecs in the months of July, August & September at Gudu Barrage, Sukkur Barrage and Kotri Barrage. It swells as much as 7,00,000 to 9,00,000 cusecs depending upon the intensity and duration of rains in the catchments areas:

Flood Stages

In order to define the degree of flood flows in the Indus the actual river discharges at Gudu, Sukkur and Kotri  Barrages categorised into various stages of flood as under: -

In Lac Cusecs

| River | Site of Gauge D/S | Design Capacity | Low Flood | Medium Flood | High Flood | Very High Flood | Super Flood |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Indus | Gudu | 12.00 | 2.00 | 3.50 | 5.00 | 7.00 | 9.00 |
|  | Sukkur | 9.00 | 2.00 | 3.50 | 5.00 | 7.00 | 9.00 |
|  | Kotri | 8.50 | 2.00 | 3.00 | 4.50 | 6.50 | 8.00 |

Yearly Maximum Recorded Discharge @ Sukkur Barrage

Flood Frequency Analysis @ Gudu Barrage

| Return Period (Year) | Flood (Cubic Feet) |
| --- | --- |
| 2 | 6,00,000 |
| 5 | 8,50,000 |
| 10 | 10,00,000 |
| 20 | 11,50,000 |
| 50 | 13,50,000 |

Identification of All Vulnerable Points

The dyke’s line is considered as strong as its weakest position. Thus every inch of the bund is to be properly guarded by patrolling yet certain points require special vigilance, which are identified and are given below along with arrangements made at these vulnerable points.

|  | Guddu Barrage Region Sukkur. |
| --- | --- |
| 1 | U/S LEFT MARGINAL BUND 7/2 TO 15/7. (V.P) |
| 2 | K.K.BUND 11/0. (V.P) |
| 3 | K.K LINK BUND 0/0 to 2/6. (V.P) |
| 4 | K.K FEEDER BUND R.D-79 TO R.D-84.5. (V.P) |
| 5 | OLD TORI BUND MILE 0/0 TO ¾. (M.V.P) |
| 6 | S.B.BUND MILE 0/0 TO 4/0. (V.P) |
|  | Sindh Irrigation and Drainage Authority (SIDA) |
| a. | Left Bank Canal Area Water Board, Badin |
| 7 | Ghalian Front Bund, mile 7/0 to 9/0,3/0 to 5/0, 10/5 (PUO) |
| 8 | Jamshoro Frond Bund, mile 1/0 to 2/3 (PUO) |
| 9 | Gidumal Front Bund mile 1/5 to 2/5 (PUO) |
| b. | Ghotki Feeder Canal Area Water Board (GFCAWB) |
| 10 | Qadirpur Shank Bund Mile 0/5 to 2/6. (V.P) |
| 11 | Qadirpur Loop Bund Mile 7/0 to 8/4. (V.P) |
| 12 | Qadirpur Bund Mile 10/4 to 11/4. (M.V.P) |
| 13 | Baiji Bund Mile 7/5 to 7/6. (V.P) |
| 14 | L M Bund mile 1/4 to 1/6 (V.P) |
|  | Sukkur Barrage Left Bank Region, Sukkur |
| 15 | Ulra Jagir 2/6-5/2 (M.V.P) |
| 16 | S. M Bund 4/0 -4/2 (Sagyoon) (PUO) |
| 17 | S.M Bund 12/4-12/7 (Bakhri) (M.V.P) |
| 18 | S.M Bund 37/4 (Bhorti) (M.V.P) |
| 19 | Right Guide Bank 0 to 3420 ft: |
| 20 | Left Guide Bank 0 to 3000 ft: U/S & 0 to 800 ft: D/S. |
| 21 | J-Spur of Dadu Moro Bridge 0 to 3280 ft: D/S (M.V.P) |
| 22 | S. M Bund 106/01 |
| 23 | Erosion point in front of Bhanoth Village 135/0-137/0 (M.V.P) |
|  | Sukkur Barrage Right Bank Region, Larkana |
| 24 | Ruk Spur, mile 0/5, 1/1, 1/6 & 2/3 (M.V.P) |
| 25 | Mori Loop Bund Mile 0/0 to 1/0 (M.V.P) |
| 26 | Akil Loop Bund Mile 0/0 to 0/7 (M.V.P) |
| 27 | Abad Mangli Extension Mile 0/0 to 1/5 (M.V.P) |
| 28 | L.S Bund 16/0 to 17/0 (M.V.P) |
| 29 | LS Bund mile 38/6 to 58/0 & 62/0 (V.P) |
| 30 | LS Bund, mile 74/0 to 77/2 (V.P) |
| 31 | LS Bund, mile 95/2to 99/7 (V.P) |
| 32 | LS Bund, mile 95/2 (V.P) |
| 33 | LS Bund, mile 99/7(V.P) |
| 34 | LS Bund, mile 100/0 (V.P) |
| 35 | Sehwan Protective Bund mile 0/0 (V.P) |
| 36 | Sann Veehdari Bund mile 11/6 (V.P) |
| 37 | Superior Bund RD 49 (PUO) |
| 38 | FP Bund RD 129 (PUO) |
| 39 | FP Bund RD 223, 246, 258, 282 and 325 (PUO) |
| 40 | FP Bund RD 169 to 183 (PUO) |
| 41 | FP Bund RD 346 to 353 (PUO) |
|  | Kotri Barrage Region, Hyderabad |
| 42 | H.P BUND MILE 4/6 (M.V.P) |
| 43 | HAJIPUR BUND MILE 3/7 (M.V.P) |
| 44 | M.S.BUND MILE 18/3 (V.P) |
| 45 | 1ST SURJANI BUND MILE 0/0 TO 1/5 (M.V.P) |
| 46 | M.S. BUND MILE 43/5 TO 44/0+200 (M.V.P) |
| 47 | KUKA LINK BUND MILE 0/0 TO 3/0 (V.P) |
| 48 | DOOLAH BRIDGE THATTA SAJAWAL ROAD BRIDGE. (M.V.P) |
| 49 | SONDA HILLAYA BUND MILE 1/3 TO 1/7. (V.P) |

Causes of Breaches

The most frequent cause of a breach is, however, the development of leak, presence of rat or snake holes in bund section, roots of small trees, treacherous soil, bank as kalar, hard clay or cracked soil in body of bund structure. In case of important or dangerous bunds, where such blowouts or leaks are found to occur frequently at high water, the areas subject to such underground leaks should have permanent “Ring Bunds” constructed around them. The history of irrigation in Sindh is bound up with that of the line of bunds along thaw Indus, without which the development of the country is impossible.

Pre Abkalani Arrangements

1.	Reconnaissance Survey

The reconnaissance survey is carried out along the Flood Protective (FP) Bund Line also inside the bund to observe the general conditions of the reverie area, river meanders and the erosion ordinate where the river meanders is following in the proximity of the bund line.

2.	Old Borrow Pits To Be Filled

According to the Bund Manual, the borrow bit near the toe of the bund line on either side of the body of the bund are strictly prohibited. Particularly the borrow pits line on the side of the bund be filled and it is also to be ensured that all the borrow pits are filled/levelled.

3.	Milestone Be Installed

Milestone, bearing the location and identification of the bund line are installed at site. However, missing milestones will be fixed/installed shortly.

4.	Gauge Pillars To Be Required & Painted

The gauges are to be installed at every mile along the bund line to record the flood levels at different flood stages and to show the depth of water against the respective bunds where it is located. The existing gauge pillars damaged during the last flood are repaired and repainted at some gauges, however the locations gauge pillars were collapsed or missing are to be reconstructed. (Work is in progress)

5.	Opening Up & Refilling Of Leaks Be Carried Out

The bunds where the leaks occurred during the last flood are located and identified at site. All the leaks are being opened and properly attended.

6.	All Masonry Works Be Inspected

The bund sluices lying along the front bund line are properly inspected and attended. Since all loop bunds are non-functional, hence all sluice are being/ seated properly in order to avoid any adverse cover as faced during flood 2010.

7.	Side Slopes Of All The Bunds Be Cleared

The most important feature of the Pre Abkalani Arrangement along the bund line is the clearance of jungle, weeds, grass and other unwanted material along entire slopes and the top of bund.

This Pre Abkalani Arrangement facilitates in exposure of the earthen body of the bund, where is becomes very easy to detect the leaks, rat holes and other activity of burrowing animals are exposed and during the flood season the occurrence of leaks is to be easily detected and timely controlled.

8.	All Abandoned Bunds Likely To Cause Pocketing Should Be Given Large &Effective Cuts

This activity is being fully implemented with help of Revenue/Police Department.

9.	Executive Engineer To Issue Certificate Duly Countersigned By The Superintending Engineer For The Good Condition Of The Bunds

Such certificate is issued.

10.	Streamlining Supply Chain

The intensity of flood can be coverage at the most a fortnight in advance. The period is too meagre for completion of procurement formalities. As such streamlining the supply chain for Abkalani material, machinery and equipment is inevitable. The process is supposed to be completed by 2nd week of June, without mention of quantity, which is specified on expectation of definite degree of receipt of flood. The procurement process stands initiated on basis of “right in time” supply management.

During Abkalani Arrangements

1.	Coordination With LEA &DCs

All the departments are in coordination with the Irrigation Department.

2.	Preparation Of Duty Roaster

All the staff employed along the bunds and the staff of the canal infrastructure is to be shifted and assigned the special task of performing the duties along bunds during Abkalani Season such duty roaster stand prepared by regional offices.

3.	Procurement Of Abkalani Material

In wake of the ensuing flood season the Abkalani material is to be procured up to 15th June and stocked at store Landhies along bund line.

4.	Construction Of Katcha Landhies

The construction of Katcha Landhies is to be started from 15th of June. In the month of June one Landhi per mile has been constructed. From 1st July at each furlong Landhies will be constructed.

5.	Patrolling Be Made Along The Bunds

Beside the regular establishment, work charge establishment/casual labour is to be engaged as the flood water touches the bund. During the month of June, two men per mile have been engaged and subsequently will be increased to 4 men per mile. During the month of July, August as per Bund Manual, 8 to 16 men per mile will be engage looking to magnitude of discharges, besides engagement of gauges to combat emergency.

6.	Equipment/Machinery Be Mobilised/Demobilised

The most prominent and important feature of the pre Abkalani arrangements is the arrangement of the equipment/machinery along the vulnerable/most vulnerable locations of the front bund line. The earth moving machinery like excavator, dozers and dumpers will be deployed along the important locations of the front bund line. One excavator, dozer, tractor trolley and Datsun Pickup at every 10 miles along the bund line will be deployed.

Deployment of machinery requisite from Agriculture Department and contractors stands streamlined.

7.	Arrangement Of Labour Be Made

All the Revenue Officers//Official and prominent Zamindars will be formally requested to provide the labour during flood season. Such activity will commence as soon as flood water approaches Gudu Barrage.

8.	Wetting/Soaking Of Bunds

Adequate arrangements for soaking and essential prerequisite of a safe bund for the consolidation or compaction of a bund depends on the soaking, which discloses faults, which can be made good or leaks, which can be filled before the main rise of river.

Irrigation Department Arrange Soaking Or Wetting Of Bunds By Two Methods

(a)	Wetting channels can be used for soaking both front and loop bunds.

(b)	Flooding of a compartment through a bund sluices in the front bund for wetting the loop or retired bunds.

The special arrangements of soaking are being arranged along front line bunds and those reaches of the loop bunds, which cannot be wetted by gravity channels by providing pumps for wetting.

9.	Jungle Clearance

The planting of trees is not allowable along bunds, because their roots tend to loosen the structure of the bund when shaken by wind storms and to encourage creep and the development of leaks, which because of the existence of the roots are difficult to close. When the organic matter dies and decays and crumbles, it leaves dangerous hollows, which cause settlement and lead to further trouble.

Irrigation Department removes the jungle from M&R Funds along the side slopes of all bunds up to widths respectively of 20 feet on land side and 10 feet on the river side. When clearing away jungle, care must be taken to have the roots thoroughly removed and the bund or ground should be properly made up lay growth, which should be encouraged for prevention of wave wash on river side.

The jungle clearance work stands started from 1st June.

10.	Bund Sluice

The bund sluice is constructing, where the bund line crosses a canal or water course, whereas loop bund. A bund sluice or sluices are required in the front bund to serve as controlled inlet and outlet of the flood water, especially for wetting of loop bunds. This should be kept in mind that the bund sluices are weak points in river bund embankment.

11.	Flood Warning Centres

In order to know the flood situations in the catchments areas, the Central Flood Warning Centre will be set up at Sindh Secretariat Building No. 2 (Tughlaq House), Karachi. This centre will be connected with the flood warning centres established at Gudu, Sukkur, Kotri and Flood Warning Centre, Lahore, where day and night staff will be available.

Based on discharge data received from Flood Warning Centre, Lahore, the Flood Warning Centre, Karachi will prepare the forecast in respect of probable river flows likely be expected at Gudu Barrage at least 7 days ahead. All the field staff as well as other concerned agencies will be informed accordingly.

| TELEPHINE DIRECTORY MONSOON AND FLOOD SEASON-2021 |
| --- |
| Name | Designation | Department | Telephone |
|  |  |  | Office | Residence | Mobil | E.mail / Fax |
| SINDH SECRETARIAT KARACHI |
| Mr. Saleem Raza | Secretary | Irrigation | 99211445 99211451 |  | 0300-260908 |  |
| Mr. Iqbal Ahmed Tenio | Section Officer Staff to Secretary. | Irrigation | 99211445 |  | 0300-3425219 |  |
| Mr. Massod Ahmeed Sehar | Special Secretay (Technical) | Irrigation | 99211446 |  | 0301-3816011 | 99211972 |
| Mr. Abdul Wahid Sathito | PS to Special Secretary (Technical) | Irrigation | 99211446 |  | 0323-2241680 | wahidsahito@gmail.com |
| Mr. Muhammad Ayoub Soomro. | Additional Secretary (Technical) | Irrigation | 99211448 |  | 0334-2628479 | 99211972 |
| Mr. Habib-ur-Rehman Ursani | Director Regulation | Irrigation | 99211505 |  | 0347-3898733 | 99211505 |
| Mr. Muhammad Shahbaz Akhtar | XEN, Regulation | Irrigation | 99211456 |  | 0333-3922723 |  |
| Mr. Shakeel Ahmed | XEN,DOC, Regulation Lahore | Irrigation | 042-35882285 |  | 0345-2308645 |  |
| GUDU BARRAGE REGIION SUKKUR |
| Mr. Ishaq Abbasi | Chief Engineer. | Irrigation | 071-9310181 | 071-9310183 | 0300-8089177 | 071-9310182 |
| Mr. Asadullah Shaikh | Superintending Engineer Begari Sindh Feeder Circle | Irrigation | 071-9310179 |  | 0300-3296019 |  |
| Mr. Ferozuddin Domki | XEN, Begari Division | Irrigation Jacobabad | 0722-652205 |  | 0300-3141331 |  |
| Haji Muhammad Ayaz Memon | Superintending Engineer Desert Pat FeederCircle | Irrigation Sukkur | 071-9310184 |  | 0300-3311441 |  |
| Mr. Shabbir Ahmed Bhutto | XEN Gudu Barrage Division | Irrigation Kashmore | 0722-576980 |  | 0333-2741567 |  |
| SUKKUR BARRAGE LEFT BANK REGION SUKKUR |
| Mr. Sardar Shah | Chief Engineer. | Irrigation | 071-9310187 | 071-9310190 | 0324-2212222 | 071-9310188 |
| Mr. Amjad Ali Bhatti | PS to Chief Engineer | Irrigation | 071-9310187 | 071-5613472 | 0300-3116409 |  |
| Mr. Javed Hakim Memon | Superintending Engineer Khaipur Irrigation Circle Sukkur | Irrigation | 071-9310195 | 071-9310180 | 0302-3344558 |  |
| MR. Syed Fayaz H.Shah | XEN Sukkur Barrage Division | Irrigation | 071-5612432 | 071-9310205 | 0300-8237686 | 071-5612974 |
| Mr. Muhammad Shoaib Samoo | Superintending Engineer Rohri Canal Circle | Irrigation Hyderabad | 022-9200278 |  | 0300-8372707 | 022-9200277 |
| SUKKUR BARRAGE RIGHT BANK REGION LARKANA |
| Mr. Nasir Ahmed Shaikh | Chief Engineer. | Irrigation | 074-4056907 |  | 0302-8282332 | 074-4753062 |
| Mr. Shujauddin Bhutto | PA to Chief Engineer | Irrigation | 074-4056907 |  | 0301-3481389 |  |
| Mr.Imran Shaikh | Superintending Engineer Saifullah Magsi Baranch Circle Larkana | Irrigation | 074-9410762 |  | 0333-2225521 | 074-9410762 |
| Mr. Imran Shaikh | Superintending Engineer Western Sindh Circle Larkana | Irrigation | 074-9410764 | 074-9410760 | 0333-2225521 | 074-9410764 |
| Mr. Iqbal Ahmed Palejo | Superintending Engineer Southern Sindh Circle Dadu | Irrigation | 025-9200071 | 025-9200070 | 0321-3219893 |  |
| KOTRI BARRAGE REGION HYDERABAD |
| Mr. Haji Khan Jamali | Chief Engineer Kotri | Irrigation | 022-9210334 022-9210335 |  | 3313207628 | 022-9210336 |
| Vacant | XEN Kotri Brrage | Irrigation Jamshoro | 022-3877403 |  |  |  |
| Mr. Suhail Hammed Baloch | Superintending Engineer Baghar Circle Hyderabad | Irrigation | 022-9210370 | 022-9210050 | 0300-8372573 | 022-9210396 |
| Mr. Fareed Ahmed Memon | Superintending Engineer Pinyari Circle Hyderabad | Irrigation | 022-9200165 | 022-9210078 | 0300-3049279 | 022-9200402 |
| SINDH IRRIGATION & DRAINAGE AUTHORITY (SIDA), HYDERABAD |
| Mr. Pritam Das | Managing Director SIDA Secretariate Hyderabad | Irrigation | 022-9210080 |  | 300-8373698 | 022-9210081 |
| Mr. Ghulam Mujtaba Damzah | Director Nara Canal Area Water Board Mirpurkhas | Irrigation | 0233-9290157 |  | 0342-3679880 | 0233-9290130 |
| Mr. Ghulam Ali Talpur | Director Left Bank Area Water Board Hyderabad | Irrigation | 022-9210399 022-7861259 |  | 0300-8377632 |  |
| Mr. Muhammad Ali Zardari | Director Ghotki Feeder Area Water Board Ghotki | Irrigation | 723684568 |  | 0303-3406450 | 0723-682093 |

Coordination From Other Departments

Revenue Department & District Arrangement

A very important role plays the Revenue Department along with District Management/Revenue Department helps the Irrigation Department with hand to hand. Revenue officers are requested to provide the cheer labour in case of acute emergency because the Revenue Department remains in close to touch with the people and their notables/tribal, chiefs.

PTCL

Irrigation Department has own wireless system and the important stations are connected with each other, but yet it is felt that it is not sufficient to cover whole of bund system. Hence the PTCL as and when needed is required to install special telephone connections.

All the vulnerable places of bunds require being equipped with landline phones.

Law & Order/Security For Supervisory Staff

Without law and order, no subordinate will be able to perform work during night/ odd hours but even in day time. The following agencies have to cooperate in this regard and provide protection to staff on bund.

- Police

- Police mobile

- Rangers

All the vulnerable places of bunds require protection to staff.

Forest Department

Forest Department is routinely asked to supply munasthunnies, panjarseto as far as possible as flood season is concerned. Irrigation Department requires the material at vulnerable points. In this regard Forest Department has been requested to arrange the following material in the following Sub Divisions.

Agriculture Department

In case of any emergency dozers will be requisite form Agriculture Department for deployment at vulnerable point as per flood situation. It may be made binding on the department concerned to make the dozer not only available at shortest possible notice but they may be requested to keep the dozers in working condition and available at workshop along with staff during all the days of the week i.e. working or closing days.

Role Of Army

Generally up to a very high flood, discharge i.e. 7 lac cusecs at Gudu Barrage, no assistance of armed forces will be required by the department, the help will be required, when flows in River Indus exceed by 7 lac cusecs or in some emergent situation arises at particular section of bund. Pre-warning signal of very high flood in Indus in Sindh can be available a week in advance of the actual arising of the flood at Gudu Barrage. In such case, vulnerable points will be looked after by army and administration for making arrangements as per situation.

WAPDA/HESCO

The WAPDA/HESCO has always been able to provide temporary emergency electric connections at special vulnerable points along bund lines at the time of high flood.

End Of Abkalani Be Announced & Relevant IRC Forum Be Submitted

Inshallah with the help of almighty Allah, the Abkalani season will end safely and the respective IRC Forum will be intimated.

******