CHAPTER: 1

SALIENT FEATURE OF THE MAILSI SYPHON DIVISION

  - LOCATION

Mailsi Syphon Division’s Headquarter is situated at Thingi RD.192+727 of Sidhnai Mailsi Bahawal Link at a distance of 11 Mile on Vehari – Multan Dehli Road. Mailsi Syphon Cum Barrage is located at RD.312 of Sidhnai Mailsi Bahawal Link on River Sutlej at distance 30 Miles Downstream Islam Headworks.

  - GENERAL DESCRIPTION.

Mailsi Syphon Division is under the control of Mailsi Canal Circle of Multan Irrigation Zone. The jurisdiction of this Division covers Sidhnai Mailsi Bahawal Link from RD.76+621 – 374+983 (Tail), and Mailsi Syphon-Cum-Barrage with its infrastructure. Sidhnai Mailsi Bahawal Link which was constructed under Indus Basin Project off takes from Sidhnai Barrage with A.F.S discharge of 13470 Cs Sidhnai Mailsi Bahawal Link passes through vast agricultural area of Kacha Khuh, Thingi, Mailsi and Khairpur Tamewali. About 22 Nos canal distributaries off-take from this Link which feed a vast land of 20 Million acres C.C.A of Pakpattan lower, Mailsi and Bahawal Canal system in Multan, Vehari, Lodhran, Bahawalpur and  Khanewal District which covers Western Bar Division and Bahawalpur Canal Circle of  Bahawalpur Zone.

Mailsi Syphon – Cum – Barrage which is a part of Sidhnai Mailsi Bahawal Link project was constructed across River Sutlej in the reach RD. 312+410 to 314+670 of Sidhnai Mailsi Bahawal Link. It is an important hydraulic structure which works as Syphon-Cum-Barrage. The total length of the Barrage is 1601 Ft having 24 gates. The designed discharge capacity is 429000 Cs. There are 2 No escape channel on S.M.B.Link at RD.151+180 and at RD.302+444 out of which escape at RD.302+444 is functional for emergencies.

  - ADMINISTRATIVE SETUP

ORGANIZATION CHART OF MAILSI SYPHON

Executive Engineer

CHAPTER: 2

FLOOD PROTECTION AND RIVER TRAINING WORKS.

2.1	DESIGNED PARA METER RIVER OF TRAINING WORKS.

BARRAGE

| 1 | Total Length of the Barrage | 1601 Ft |
| --- | --- | --- |
| 2 | Crest R.L. | 415.50 |
| 3 | Upstream Floor Level | 400.00 |
| 4 | Downstream Floor Level | 403.50 |
| 5 | Number of Gates | 24 No |
| 6 | Width of Gates | 60 Ft each |
| 7 | Designed H.F.L. Upstream | 434.80 |
| 8 | Flood level Downstream | 430.50 |

SYPHON

| 1 | Length of Barrel including sloping entrances & exists | 1881 Ft |
| --- | --- | --- |
| 2 | Floor R.L. of Barrels | 391.00 |
| 3 | Upstream bed R.L. of Barrel | 418.22 |
| 4 | Downstream bed R.L. in Link | 416.93 |
| 5 | No of Barrels | 5 No |
| 6 | i. Size of 4 No. Barrels | 13.50’ x 13.50’ |
|  | ii. Size of 1 No. New Barrel | 16.50’ x 13.50’ |
| 7 | Designed F.S.L in Link Upstream | 438.72 |
| 8 | Designed F.S.L in Link Downstream | 436.28 |

(i)		LEFT MARGINAL BUND

| This bund has been constructed on the Eastern Bank of River Sutlej and extends from village Namat Ali to Khairu Deh. It was restored in the year 1990, presently the condition of the bund is satisfactory and is out of danger. Weak reaches are strengthened as and when deemed necessary. The metaled road exists from RD.21-65282 (Tail) The following works has been executed & completed during Financial year 2018-19. 1.Strengthening and maintaining weak site RD.15+620 to RD.16+370 Left Marginal Bund of Mailsi Syphon Cum Barrage. 2. Maintaining Left Marginal Bund of Mailsi Syphon Cum Barrage From RD.10+500 to 11+000. |  |
| --- | --- |

LEFT MARGINAL BUND

| 1 | Length | 13.06 Miles |
| --- | --- | --- |
| 2 | Top Width | 25 feet |
| 3 | Side slope on both side | 3:1 |
| 4 | Free Board | 6 feet to 9.50 Feet |

(ii)		RIGHT MARGINAL  BUND

| This bund has been constructed on the Western Bank of River Sutlej and extends from village Namat Ali to Mouza Dhaloo. It was restored in the year 1990, presently the condition of the bund is satisfactory and is out of danger. Pacca metalled Road exist on R.M.B. from tail RD.51400 to Mailsi Syphon Cum Barrage. |  |
| --- | --- |

RIGHT  MARGINAL BUND

| 1 | Length | 10.29 Miles |
| --- | --- | --- |
| 2 | Top Width | 25 feet |
| 3 | Side slope on both side | 3:1 |
| 4 | Free Board | feet to 9.50 Feet |

(iii)    	MOLE HEAD SPUR

| An armored spur has been constructed at RD.4000 of RMB having length RD.0+000 to RD.5955 at right angle to plug the old river creak and to train the river properly towards the barrage by deflecting the flow of water from its old course. The spur from RD. (0 – 5955Nose) comes under wave action with the rise of water in this reach. It is the sensitive part of spur and is needed to keep under close watch during flood. Nose of the mole head spur is under direct river action and stone apron of mole head spur was launched during the flood 1998. The spur always remains under River action during flood and the deep creek of river flow in its toe. The Main river creek flows on the right with erosive velocities because the tendency of River has always been towards right, so the current flow is in the toe of the spur continuously. |  |
| --- | --- |

MOLE HEAD SPUR

| 1 | Length | 1.19 Miles |
| --- | --- | --- |
| 2 | Top Width | 25 feet |
| 3 | Side slope on both side | 3:1 |
| 4 | Free Board | 6.50 Feet HFL |

GUIDE BANKS

The flow of River just upstream & Downstream of the Barrage is guided towards the Barrage by guide banks on either side of the River

| S# | Description | Right U/S | Right D/S | Left U/S | Left D/S |
| --- | --- | --- | --- | --- | --- |
| 1 | Length | 3900 Ft | 850 Ft | 3900 Ft | 850 Ft |
| 2 | Top Width | 35 Ft | 35 Ft | 35 Ft | 35 Ft |
| 3 | Side slopes on both sides | 3:1 | 3:1 | 3:1 | 3:1 |
| 4 | Free Board | 6.50 Ft | 6.50 Ft | 6.50 Ft | 6.50 Ft |

CHAPTER: 3

BRIEF HISTORY OF PAST FLOOD EVENTS.

HIGH DISCHARGE FLOODS

Only 3 No high discharge floods were received in River Sutlej at Mailsi Syphon Cum Barrage. The detail is as under: -

| S# | Year | Discharge |
| --- | --- | --- |
| 1 | 1973 | 160535 Cs |
| 2 | 1988 | 217616 Cs |
| 3 | 1995 | 173527 Cs |

DAMAGES DUE TO HIGH FLOOD

I.		DURING FLOOD 1973

No major damage occurred to flood controlling structures i.e. Bunds / weir and its infrastructures. Only about 40 No villages in the area of Mailsi Syphon Cum Barrage inundated. Due to this high flood standing crops and houses of the village were damaged and no loss to human life was occurred.

II.		DURING FLOOD 1988

No major damage occurred to flood controlling structures i.e. Bunds / weir and its components.  Only about 54 No. villages in the area of Mailsi Syphon Cum Barrage on both sides inundated. Due to this high flood water, the standing crops and houses of the village were damaged and no loss to human life was occurred.

III.		DURING FLOOD 1995

No major damage occurred to flood controlling structure i.e. Bunds / weir and its infrastructures. Only about 54 No villages in the area of Mailsi Syphon Cum Barrage inundated. Due to this high flood, stranding crops and houses of the villages were damaged no loss to human life was occurred

CHAPTER: 4

DESIGNED DATA HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEAR FLOOD DATA OF HEAD WORKS / BARRAGES & OTHER CONTROL POINTS.

4.1	FLOOD LIMITS

At Mailsi Syphon Cum Barrage, the various flood stages of River Sutlej are as under: -

| Sr# | Discharge between | Flood Stage |
| --- | --- | --- |
|  | From | To |  |
| 1 | 50,000 Cs | 80,000 Cs | Low Flood |
| 2 | 80,000 Cs | 1,20,000 Cs | Medium Flood |
| 3 | 1,20,000 Cs | 1,75,000 Cs | High Flood |
| 4 | 1,75,000 Cs | 2,25,000 Cs | Very High Flood |

  - TIME LAG

Mailsi Syphon Cum Barrage is situated about 30 Miles downstream of Islam Headworks. Time lag for different stages of Flood are as under: -

| Stage of Flood | Time lag for Mailsi Syphon (Islam Headworks to Mailsi Syphon-Cum-Barrage) |
| --- | --- |
| Low flood | 16 Hours |
| Medium flood | 14 Hours |
| High flood | 12 Hours |

DISTANCE AND TIME LAGES BETWEEN ISLAM TO MAILSI SYPHON

| Description | Reach | Time LAGES IN DAYS | Distance |
| --- | --- | --- | --- |
|  |  | Nov: -April | May – June | July – Aug | Sep – Oct | Canal Miles |
| River Sutlej | Suleimanki – Islam | 4 | 3 | 2 | 3 | 121 |
|  | Islam – Mailsi Syphon | 1 | ¾ | ½ | ¾ | 30 |

4.3	HIGHIEST   FLOODS

Only 3 No high discharge floods were experience in River Sutlej is detail as under: -

| S# | Year | Discharge |
| --- | --- | --- |
| 1 | 1973 | 160535 |
| 2 | 1988 | 217616 |
| 3 | 1995 | 173527 |

4.4	PEAK DISCAHRGE OF MAILSI SYPHON CUM BARRAGE FROM 1974 TO 2022

| Sr. No | Year | Month | Discharge in Cs |
| --- | --- | --- | --- |
|  | 2022 | July | 10955 |
|  | 2021 | March | 2108 |
|  | 2020 | March | 7979 |
|  | 2019 | August | 40285 |
|  | 2018 | October | 8683 |
|  | 2017 | August | 13385 |
|  | 2016 | August | 12557 |
|  | 2015 | August | 39048 |
|  | 2014 | September | 15531 |
|  | 2013 | August | 62433 |
|  | 2012 | September | 11747 |
|  | 2011 | September | 48387 |
|  | 2010 | November | 29310 |
|  | 2009 | September | 9006 |
|  | 2008 | August | 24454 |
|  | 2007 | June | 10182 |
|  | 2006 | October | 7285 |
|  | 2005 | September | 26667 |
|  | 2004 | October | 13385 |
|  | 2003 | April | 591 |
|  | 2002 | June | 591 |
|  | 2001 | August | 3102 |
|  | 2000 | July | 13385 |
|  | 1999 | January | 32001 |
|  | 1998 | September | 65249 |
|  | 1997 | September | 39045 |
|  | 1996 | October | 45174 |
|  | 1995 | September | 173527 |
|  | 1994 | August | 90793 |
|  | 1993 | July | 87646 |
|  | 1992 | September | 108500 |
|  | 1991 | September | 14230 |
|  | 1990 | September | 121975 |
|  | 1989 | August | 10955 |
|  | 1988 | October | 217616 |
|  | 1987 | July | 12370 |
|  | 1986 | August | 17253 |
|  | 1985 | July | 26140 |
|  | 1984 | September | 25167 |
|  | 1983 | September | 36193 |
|  | 1982 | September | 14260 |
|  | 1981 | August | 31788 |
|  | 1980 | August | 37510 |
|  | 1979 | July | 8680 |
|  | 1978 | August | 134989 |
|  | 1977 | September | 33452 |
|  | 1976 | September | 105856 |
|  | 1975 | September | 42297 |
|  | 1974 | September | 8389 |

GRAPH SHOWING PEAK DISCAHRGE DOWN STREAM MAILSI SYPHON CUM BARRAGE FOR THE EYAR 1970 TO 2022

CHAPTER: 5

FLOOD FIGHTING STRATEGY

FLOOD FIGHTING STRATEGY

The following precautionary measures are adopted before flood season to face any alarming situation at Mailsi syphon cum Barrage even then arrangements are necessary to avoid heavy damages and flood fighting strategy is adopted in such a way that flood water passes safely through Mailsi syphon cum Barrage, up to its limit.

In low flood, river water remains within the deep channel and do not cause any problem if regulation of gates is done as per rules. Watching establishment employed for this purpose will remain busy in removing jungle, filling gharas and percupine holes

- MEDIUM FLOOD

When river water enters into Medium Flood range i.e 0.5 lac to 0.8 Lac cs, it will start spreading on adjoining area and also touches the toe of bunds. Then it becomes necessary to be more vigilant. The watching of flood bunds will start to avoid any leakage from bunds. Sub Engineers will shift their camps to sites as per duty roaster. Hourly gauges and discharge will be conveyed to Civil Administration and flood warning centers to inform public accordingly.

ii 	HIGH FLOOD

When river water enters into high flood range i.e 0.8 lacs to 1.75 Lacs cs Sub Divisional Officer Head Works will shift his camp at Mailsi Syphon Cum Barrage to supervise staff working on L.M.B/R.MB and D/S Spurs. In whole period regulation will be done in such a way that silt deposited in front of the gated may be washed D/S of the river to widen the waterway U/S.

iii 	VERY HIGH FLOOD

. 		When river water enters into very high flood range i.e 1.75 lac to 2.25 Lacs, Executive Engineer along with Sub Divisional Officer Head Works will shift his camp at Mailsi Syphon Cum  Barrage to supervise staff working on L.M.B, RMB and D/S Spurs and to check leakage if any. Critical gauge will be checked on hourly basis round the clock. If discharge is in continuously rising position, then breaching section is activated in consultation with Civil Administration and Pak Army.

iv 	EXCEPTIONALLY HIGH FLOOD

Gauges of different sites especially gauge at RD: 3000 to 6000 of L.M.B will be noted regularly and recorded. Executive Engineer will inform all agencies especially civil administration as well as Army about flood situation in rising position. In case of very high flood or exceptionally high flood, meeting will be held in field office with Army and Civil Administration to face the situation.

Two dozers will be kept ready at RD: 7500 to 9500 R.M.B for making cuts and closing breaches as and when required according to circumstances. When gauge RD: 15000 L.M.B touches level 500.00 and is found in rising position it will be the duty of Executive Engineer to request Army for operation of breach section for the safety of Barrage. When water subsides, the breaching sections will be closed (if operated) as soon as possible.

CHAPTER: 6

FLOOD DAMAGES RESTORATION WORKS.

| Flood Damages | Restoration Works |
| --- | --- |
| NIL | NIL |

CHAPTER: 7

FLOOD FIGHTING WATCHING ARRANGEMENT

7.1		PRE-FLOOD ARRANGMENT

Wireless Station at Mailsi Syphon Cum Barrage is available for communication which is connected with Flood Warning Centre At Lahore and Headworks on River Sutlej upstream of Mailsi Syphon Cum Barrage i.e. Islam Head Works and Suleimanki Headworks. Flood Warning are received through this communication. However, upon knowing flood forecasting, necessary pre-flood arrangements are ensured by the Executive Engineer, Mailsi Syphon, Thingi. The Flood Fighting Material is ensured at the shelter Huts / Temporary camps establishment by the Mailsi Syphon Division. All establishment of the Division is deputed on the Flood Embankment to ensure watching round the clock.

RESERVE STOCK OF STONE AT EVERY STRUCTURE

| S# | Name of Structure | Sanctioned Limit (Lac Cft) | Available Quantity (Lac Cft) | Required Quantity |
| --- | --- | --- | --- | --- |
| 1 | Right Guide Bund | 2.58984 | 2.58984 | ----- |
| 2 | Left Guide Bund | 2.59304 | 2.59304 | ---- |
| 3 | Left Marginal Bund | 0.04921 | 0.04921 | ---- |
| 4 | Mole Head Spur | 0.23641 | 0.23641 | ----- |
| Total | 5.4685 | 5.4685 Lac Cft |  |

7.2		WATCHING ESTABLISHMENT

| Site | Flood Limits |
| --- | --- |
|  | Low | Medium | High | Very High | Excep: High |
|  | Men | Shift | Men | Shift | Men | Shift | Men | Shift | Men | Shift |
| Right Marginal Bund(10.29 Mile) | 32 | 2 | 90 | 2 | 90 | 3 | 110 | 3 | 110 | 3 |
| Left Marginal Bund (13.06 Mile) | 42 | 2 | 114 | 2 | 135 | 3 | 180 | 3 | 180 | 3 |
| Mole Head Spur (1.19 Mile) | 4 | 2 | 10 | 2 | 12 | 3 | 18 | 3 | 18 | 3 |

On receipt of daily gauges from flood warning center and flood forecasting of metrological department a comprehensive plan is chalked out for flood management at Mailsi Syphon Cum Barrage.

Keeping in view the system of Bunds along river Sutlej to effectively handle any flood related situation, such flood Bunds areas are divided into various suitable sectors. Each sector is headed by Sub Engineer in-charge along with requisite manpower and other resources to fight flood as indicated.

The flood fighting area is divided into 4 to 6 sectors with respect to flood limits. The Executive Engineer Mailsi Syphon will be over all in-charge of Mailsi Syphon Cum Barrage and its infrastructures.

In order to effectively handle flood situation, this Division has prepared the sector wise plan to watch the Flood Embankment in this Division.

  - ARRANGEMENT AT SENSITIVE SITES.

During flood especially high flood stage, the Revenue Department will arrange Civil Labour and Sipah-Khidmat. The agriculture Department will supply the dozer as provided in the District Flood Plan to meet any emergency. 6 Nos Jeeps and 4 Nos Pickups will also have to be requisitioned for efficient watching and patrolling of the bunds. The District Coordination Officer Vehari & Bahawalpur will be specially requested to direct the District Machinery pool officer to arrange the same well in time.

| S# | Name of Site | Reach | Required Machinery |
| --- | --- | --- | --- |
|  |  |  | No of Dozer | No of Tractor | Other Machinery |
| 1 | Left Marginal Bund | RD.0-25 | 2 | 4 | - |
| 2 | Right Marginal Bund | RD.0-20 | 2 | 5 | - |
| 3 | Mole Head Spur | RD.0-Tail | 1 | 2 | - |

  - WATCHING MATERIAL

| S# | Name of Items | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | Torch Cells | 24 | 0 | 24 | This balance quantity of Flood Fighting Material will be procured before starting of flood season 2023. |
| 2 | Lanterns | 100 | 65 | 35 |  |
| 3 | Kerosene Oil | 30 Ltr | 0 | 30 |  |

  - ARRANGEMENT FOR SOUNDING & PROBING

Equipment’s including Sounding Rods, Leveling Instruments, Arrows etc are available to perform Sounding and Probing during the flood.

  - LIGHTING ARRANGEMENT

Necessary Lighting arrangements have also been improved as per security point of view, and electric poles with lights have also been fixed at various place Guide Bunds, Main Bridge of Syphon and one portable Generator is available with the department.

  - RATION ARRANGEMENT.

- There is no role of Irrigation Department in Ration arrangement.

- The ration will be provided by Civil authority to establishment and supervisory staff of Irrigation Department and refugees also.

  - P.O.L ARRANGEMENT FOR VEHICLE.

District Coordination Officer, Vehari will be requested to direct the petroleum dealers at Mailsi to reserve 300 Gallons of patrol and 500 Gallons of Diesel oil at each petrol pump for use at Mailsi Syphon cum barrage during flood emergency.

  - TRANSPORTATION.

There is no Truck in Mailsi Syphon Division. Two Trucks will have to be requisitioned through the District Coordination Officer, Vehari for working during               Phase-I & II.

  - LAW AND ORDER.

A few Constables headed by the Assistance Sub Inspector will be required to maintain law & order at the weir. District Coordination Officer / District Police Officer, Vehari will be requested to arrange the same when required.

  - MEDICAL ARRANGEMENT FOR LABOUR

There is no dispensary at Mailsi Syphon. Health Department will be requested to depute one Medical Officer with allied staff to perform duty during flood season. They will also be requested to arrange sufficient medicines.

  - LIAISON WITH OTHER DEPARTMENT

Executive Engineer, Mailsi Syphon Division and Sub Divisional Officer, Mailsi Syphon Sub Division will keep liaison with their counterparts of other Department. Higher authorities of other Department will be approached, if needed, through superintending Engineer, Mailsi Canal Circle, Multan and Chief Engineer, Irrigation Multan. Civil & Police authorities will be constantly kept informed about the flood situation.

  - ROLE OF THE ARMY

Regiment strength Role of Army (About 500 Jawans) will be requisitioned when discharge is likely to exceed 225,000 Cs.

  - DUTIES OF TELEPHONE ATTENDANT

The Telephone Attendant will be deputed for work during flood days to communicate the flood situation by Wireless and Telephone.

| S# | Name | Designation | Duty Hours | Remarks |
| --- | --- | --- | --- | --- |
| 1. | Allah Mair Khan | Telephone Attendant | 08.00 to 04.00 |  |
| 2 | Muhammad Mustafa | Telephone Attendant | 04.00 to 12.00 |  |
| 3 | Muhammad Sohail | Telephone Attendant | 12.00 to 08.00 |  |

  - WIRELESS ARRANGEMENTS

A Wireless set will be set up at Mailsi Syphon weir which will contact similar sets at Upper Barrage & will collect hourly flood warnings. Information thus obtained will be plotted to anticipate the flood discharge of Mailsi Syphon Barrage.

CHAPTER:8

DETAIL OF ENCROACHMENT

| No. of Encroachment | Removal | Balance | Action to be taken |
| --- | --- | --- | --- |
| NIL | NIL | NIL | NIL |

CHAPTER:9

DUTY ROSTER / FLOOD FIGHTING PROGRAM

WATCHING ESTABLISHMENT

AT MAILSI SYPHON CUM BARRAGE

PHASE-1

When Discharge will be 50,000 Cs to 80,000 Cs (Low Flood) the establishment deployed at vulnerable sites is as under: -

SECTOR No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO M/S 0302-7705684 | SBE Bund Section 0306-1416869 | RMB | RD.0-25 = 5 Mile | 3 Beldar per mile | 19 | 2 |
|  |  | Mole Head Spur | RD.0-5955 (T) = 1.19 Mile |  |  |  |

SECTOR No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO M/S 0302-7705684 | SBE Khanpur Section 0301-7406699 | RMB | RD.25 to Tail 51400 = 5.28 Mile | 3 Beldar per mile | 16 | 2 |

SECTOR No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Khairpur Section 0305-6509464 | LMB | RD. 0 to 30 = 6 Mile | 3 Beldar per mile | 18 | 2 |

SECTOR No.4

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Mechanical Section 0301-7401253 | LMB | RD.30 to Tail 65282 =7.0 5 Mile | 3 Beldar per mile | 21 | 2 |

PHASE-II

When Discharge will be 80,000 Cs to 175,000 Cs  ( Medium Flood) the establishment deployed at vulnerable sites is as under:-

SECTOR No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO M/S 0302-7705684 | SBE Bund Section 0306-1416869 | RMB | RD.0.25 = 5 Mile | 8 Beldar per mile | 50 | 5 |
|  |  | Mole Head Spur | RD.0-5955 (T) = 1.19 Mile |  |  |  |

SECTOR No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO M/S 0302-7705684 | SBE Khanpur Section 0301-7406699 | RMB | RD.25 to Tail 51400 = 5.28 Mile | 8 Beldar per mile | 42 | 4 |

SECTOR No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Khairpur Section 0305-6509464 | LMB | RD. 0 to 30 = 6 Mile | 8 Beldar per mile | 48 | 5 |

SECTOR No.4

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Mechanical Section 0301-7401253 | LMB | RD.30 to Tail 65282 =7.0 5 Mile | 8 Beldar per mile | 56 | 6 |

PHASE-III

When Discharge will be 175,000 Cs to 225,000 Cs  ( High Flood) the establishment deployed at vulnerable sites is as under:-

SECTOR No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO M/S 0302-7705684 | SBE Bund Section 0306-1416869 | RMB | RD.0-10 = 2 Mile | 10 Beldar per mile | 32 | 3 |
|  |  | Mole Head Spur | RD.0-5955 (T) = 1.19 Mile |  |  |  |

SECTOR No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO M/S 0302-7705684 | SBE Khanpur Section 0301-7406699 | RMB | RD. 10 to 30 = 2 Mile | 10 Beldar per mile | 20 | 2 |

SECTOR No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Mechanical Section 0301-7401253 | RMB | RD. 30 to 51400 = 4.28 Mile | 10 Beldar per mile | 43 | 4 |

SECTOR No.4

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Khairpur Section 0305-6509464 | LMB | RD. 0-20 = 4 Mile | 10 Beldar per mile | 40 | 4 |

SECTOR No.5

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Mechanical Section 0301-7401253 | LMB | RD. 20 to 40 = 4 Mile | 10 Beldar per mile | 40 | 4 |

SECTOR No.6

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| SDO Karampur 0300-8687588 | SBE Colony Section 0301-7946580 | LMB | RD. 40-65282 = 5.05 Mile | 10 Beldar per mile | 50 | 5 |

CHAPTER:10

EMERGENCY TELEPHONE NOS.

| S. # | DESIGNATION | OFFICE | RESIDENCE |
| --- | --- | --- | --- |
| 1 | Executive Engineer, Mailsi Syphon Division, Thingi District Vehari | 067-3788121 | 067-3788121 |
| 2 | Deputy Commissioner Vehari | 067-3362122 | 067-3362422 |
| 3 | District Police Officer Vehari | 067-3363244 | 067-3362953 |
| 4 | District Police Officer Bahawalpur | 062-9250360 | 062-9250361 |
| 5 | District Coordination Officer Bahawalpur | 062-9250492 | 062-9250063 |
| 6 | Assistant Commissioner Mailsi | 067-3410888 | 067-3410777 |
| 7 | Assistant Commissioner Khairpur Tamewali | 062-2261121 |  |
| 8 | Deputy Superintendent of Police Vehari | 067-3365058 | 067-3365003 |
| 9 | Deputy Superintendent of Police Mailsi | 067-3412006 | 067-3412005 |
| 10 | Superintending Engineer, Mailsi Canal Circle, Multan | 061-9200134 |  |
| 11 | Chief Engineer, Irrigation Zone Multan | 061-9200144 |  |
| 12 | Secretary Irrigation Department Lahore | 042-99212117-18 | 042-99203037 |
| 13 | Flood Emergency Officer / Executive Engineer (OP) Irrigation Multan | 061-9200019 |  |
| 14 | Executive Engineer, Islam Headworks Division Pallah | 067-3024490 |  |
| 15 | Executive Engineer, Highway Division, Vehari | 067-3362984 | 067-3362984 |
| 16 | Chief Engineer, Drainage + Flood Irrigation Department Lahore | 042-99230602 | 042-99239044 |
| 17 | Fax No. | 35862081 |  |
| 18 | Director Flood / Secretary Punjab Flood Commission Lahore | 99231614 |  |
| 19 | Sub Divisional Officer, Mailsi Syphon Sub Division Khairpur Tamewali | 0302-7705684 | 0302-7705684 |
| 20 | Flood Warning Centre 46-Jail Road, Lahore | 042-99205157 99205158 | Fax No. 042-97572092 |
| 21 | Military Office 31-Corp Bahawalpur | 062-8915632 |  |

Note:-	Urgent message can also be delivered through wireless set installed at Mailsi Syphon Cum Barrage.

CHAPTER:11

STANDARD OPERATING PROCEDURE (SOP) FOR BREACHING SECTIONS.

| 11.1 | History of the breaching section | Not Applicable |
| --- | --- | --- |
| 11.2 | Location, Design, Quantity and Variety of the explosive required for detonation | Not Applicable |
| 11.3 | Arrangement of explosive and security of explosive stores | Not Applicable |
| 11.4 | List of the security staff alongwith detail of their training etc | Not Applicable |
| 11.5 | Detail of mechanical means as a standby arrangements in case of detonation failure | Not Applicable |
| 11.6 | Duty Roaster in case of critical situation | Not Applicable |
| 11.7 | Breaching Committee with their action plan | Not Applicable |
| 11.8 | List of the village likely to be inundated in case of breach | Not Applicable |
| 11.9 | Announcement and detail of evacuation arrangements | Not Applicable |
| 11.10 | Detail of coordination with Civil/Army Authorities | Not Applicable |
| 11.11 | Parallel communication arrangements | Not Applicable |
| 11.12 | Index Plan | Not Related |

Executive Engineer,		Superintending Engineer,	      Chief Engineer,

Mailsi Syphon Division,	Mailsi Canal Circle,            	      Irrigation Zone Multan.

Thingi.				Multan

PART-B

CHAPTER:12

VULNERABLE SITES ON FLOOD BUND / STRUCTURES.

12.1	APPREHENDED BREACHES IN FLOOD BUNDS / STRUCTURES.

The vulnerable site on Flood Bunds are  enlisted as under:-

| Sr No. | Nam of Flood Bund | Reach | Remarks |
| --- | --- | --- | --- |
|  |  | From RD. | To RD. |  |
| 1 | Right Marginal Bund | 7500-9500 |  |
| 2 | Left Marginal Bund | 3000 - 6000 |  |

12.2	OPERATION OF BREACHING SECTIONS

There is no breaching Section exist in this Division

12.3	BREACHES DUE TO RISING OF FLOOD WATER, DETERIORATION OF FLOOD BUNDS ETC.

No such occurrence.

CHAPTER:13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE (SITES)

Site No. 1.   	Right Marginal Bund (RMB)

RD. (7500 -	9500)

13.2	DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.

The Villages / Abbadies likely to be affected due to apprehended breaches on RMB at RD. 75000-RD.95000.

R.M.B.

| S# | Name Village / Basti | No of House | Population |
| --- | --- | --- | --- |
| 1 | Mouza Namat Ali | 500 | 2000 |
| 2 | Mouza Murad Pur | 500 | 2200 |
| 3 | Basti Namat Ali | 30 | 150 |
| 4 | Mouza Remola | 250 | 1000 |
| 5 | Basti Mochi Pura | 300 | 1500 |
| 6 | Ara No.1 | 400 | 1500 |
| 7 | Basti Dabar | 450 | 1600 |
| 8 | Basti Ghous Pur | 450 | 1800 |
| 9 | Basti Kaman Wali | 700 | 3000 |
| 10 | Mouza Chatani | 2500 | 10000 |

The Villages / Abbadies likely to be affected due to apprehended breaches on LMB at RD.3-RD.6

  - STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL. THIS MAY INCLUDE

Though all precautionary measures are adopted before flood season to face any alarming situation at Mailsi Syphon Cum Barrage, even then arrangements are necessary to avoid heavy damages and flood fighting strategy is adopted in such a way that flood water passes safely through Mailsi Syphon Cum Barrage, up to its limit.

In low flood, watching establishment employed for this purpose will remain busy in removing jungle, filling gharas and porcupine holes if any.

When water increases beyond 50,000 cusecs, then it becomes necessary to be vigilant to avoid any mishap. Sub Engineers will shift their camps to sites as per duty roaster.

When river water enters into high flood range, Sub Divisional Officer  Mailsi Syphon  will shift his camp at Mailsi Syphon Cum Barrage  to supervise staff working on RMB, LMB and allied spurs and whole period regulation will be done wisely.

Gauges of different sites especially gauge at Mailsi Syphon Cum Barrage will be noted regularly and recorded. Executive Engineer will inform all agencies especially civil administration as well as Army about flood situation. In case of very high flood, meeting will be held in field office with Army and Civil Administration to face the situation.

In light of Standard Operation Procedure (SOPs) to minimize damage to public / private infrastructure, land and abadies, in case of emergency, the flood fighting activities have been divided in to three operational domains.

RESCUE

RELIEF

REHABILITATION ACTIVITES

During the emergency, each sector team shall remain present in its respective flood duty and coordinate with each other.

1 		RESCUE

The Rescue sector will watch precautionary measures, dissemination of flood alerts, evacuation call to the vicinity villages and forcible evacuation if required. Also work will be done with coordination and full cooperation of Pak Army.

2.		RELIEF

Relief sector will watch his responsibilities as provision of essential Articles such as food, medicine and shelter huts.

3.		REHABILITATION

Rehabilitation sector will watch the appraisal of damages, restorations of services like electricity, Telephone, Communication infrastructure etc, resettlement of displaced in temporary / permanent dwellings. Likewise, each team at flood relief camp shall be responsible for arrangements of food, bedding and other basic amenities required in flooded area.

13.3.1		ARRANGMENT

Watching establishments on vulnerable sites on RMB at RD.7500-RD.9500 and arrangement of tractors with front blade, excavators and other equipment’s for safety of flood bunds will be arranged to cope with the emergency.

13.3.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Establishment has been divided in different “Beats” for watching of flood bunds round the clock in different flood stage Detail is as under

RIGHT  MARGINAL BUND

Beat Number – 1		= RD. 0-15

Mole Head Spur		= RD. 0-5955

Beat Number – 2		= RD. 15-35

Beat Number – 3		= RD. 35-51400 Tail

1. LOW FLOOD (0.50 Lac  to 0.80 Lac Cusecs.

Beat  No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Khanpur Section 0305-650946 | RMB | RD.0-15 = 3 Mile | 3 Beldar per mile | 13 | 2 |
|  |  | Mole Head Spur | RD.0-5955 (T) = 1.19 Mile |  |  |  |

Beat  No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Khanpur Section 0305-6509464 | RMB | RD.15 to 35 = 4 Mile | 3 Beldar per mile | 12 | 2 |

Beat  No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Fawad SBE Khairpur Section 0301-4635383 | RMB | RD.35 to 51400 = 3.09 Mile | 3 Beldar per mile | 10 | 2 |

CAMPS OF WATCHING ESTABLISHMENT

RIGHT  MARGINAL BUND

Beat Number – 1		= RD. 0-15

Mole Head Spur		= RD. 0-5955

Beat Number – 2		= RD. 15-35

Beat Number – 3		= RD. 35-51400 Tail

2. MEDIUM  FLOOD ( 0.80 to 1,75,000 Lac Cusecs.

Beat  No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Khanpur Section 0305-6509464 | RMB | RD.0-15 = 3 Mile | 8 Beldar per mile | 32 | 4 |
|  |  | Mole Head Spur | RD.0-5955 (T) = 1.19 Mile |  |  |  |

Beat  No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Khanpur Section 0305-6509464 | RMB | RD.15 to 35 = 4 Mile | 8 Beldar per mile | 32 | 4 |

Beat  No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Ahmad SDO Karampur 0300-7301344 | Fawad SBE Khairpur Section 0301-4635383 | RMB | RD. 35-51400 = 3.09 Mile | 8 Beldar per mile | 24 | 3 |

CAMPS OF WATCHING ESTABLISHMENT

RIGHT  MARGINAL BUND

Beat Number – 1		= RD. 0-15

Mole Head Spur		= RD. 0-5955

Beat Number – 2		= RD. 15-35

Beat Number – 3		= RD. 35-51400 Tail

3.HIGH  FLOOD (  1,75,000 2,25,000 Lac Cusecs.

Beat  No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Khanpur Section 0305-6509464 | RMB | RD.0-15 = 3 Mile | 10 Beldar per mile | 40 | 4 |
|  |  | Mole Head Spur | RD.0-5955 (T) = 1.19 Mile |  |  |  |

Beat No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Khanpur Section 0305-6509464 | RMB | RD. 15- to 35 = 4 Mile | 10 Beldar per mile | 40 | 4 |

Beat  No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Ahmad SDO Karampur 0300-7301344 | Fawad SBE Khairpur Section 0301-4635383 | RMB | RD. 35 to 51400 = 3 Mile | 10 Beldar per mile | 30 | 3 |

[

    - DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP SITES

Duties of Officers / Officials & Their Camp at RD. 10 of RMB

SUB DIVISIONAL OFFICERS

The flood fighting camps will be arranged on RD.10 of Right Marginal Bund. Sub Divisional Officer Mailsi Syphon Sub Division will be the in charge. Sub Engineer Khanpur & Sub Engineer Bund will be the incahrge and will perform their duties with other establishment i.e. Beldars, mates etc.

| S# | Name OF SDO | Reach | Headquarter |
| --- | --- | --- | --- |
| 1 | Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | RD.0-20/R.M.B. | Mailsi Syphon Cum Barrage |

SUB ENGINEERS

| S# | Name OF sub Engineer | Reach | Headquarter |
| --- | --- | --- | --- |
| 1 | Ghulam Nabi SBE Khanpur Section 0305-6509464 | RD.0-20/R.M.B. | RD.10 of RMB |

MATE & BELDARS

| S# | Reach | Beldar | Mate |
| --- | --- | --- | --- |
| 1 | RD.0-20/R.M.B. | 20 | 2 |

    - DEPARTMENTAL MACHINERY AVAILABLE

Departmental machinery is not available. This will be brought on site from the Agriculture Department.

    - MACHINERY AVAILABLE FROM PRIVATE SOURCE

R.M.B.

1.	Excavator		= 4 No.

2.	Dumper		= 4 No.

3.	Tractor Trolly	= 8 N

    - FLOOD FIGHTING MATERIAL REQUIRED FOR MAILSI

SYPHON CUM BARARGE.

    - FLOOD FIGHTING MATERIAL AVAILABLE FOR

MAILSI SYPHON CUM BARARGE.

| Sr # | Item | Unit | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | G.I. Bucket | No | 75 | 75 | 0 |  |
| 2 | Kassi Handle | No | 20 | 20 | 0 |  |
| 3 | Khaji Mate | No | 1000 | 0 | 1000 |  |
| 4 | Basket | No | 1000 | 0 | 1000 |  |
| 5 | Torche cell | No | 24 | 0 | 24 |  |
| 6 | Lantern | No | 100 | 65 | 35 |  |
| 7 | Petromax lamp | No | 13 | 13 | 0 |  |
| 8 | Gunney bag | No | 6000 | 0 | 6000 |  |
| 9 | Faber glass boat | No | 1 | 1 | 0 |  |
| 10 | Kassi | No | 500 | 478 | 22 |  |
| 11 | Munjban | KG | 300 | 0 | 300 |  |
| 12 | Stone for emergency at LMB & RMB | Cft | 5.468 Cft Lac | 5.4685 Cft Lac | 0 |  |

This balance quantity of Flood Fighting Material will be procured before starting of flood season 2022.

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDINGS, CANALS & DRAINAGE NETWORK

R.M.B.

TELEPHONE.

There is no Land Line Telephone Service in this Area.

CANALS.

Sidhnai Mailsi Bahawal Link.

ROAD NETWORK

- Mailsi – Khairpur Tamewali Road.

2.	Hasilpur – Bahawalpur Road.

OTHER STRUCTURE / BUILDINGS

| Electric Pools 11 KVA |  |
| --- | --- |
| Government Girls Primary School | Ara No.2 |
| Government Boys Primary School | Ara No.2 |
| Government Boys Primary School | Basti Ghous Pur |
| Government Boys High School | Ara No.2 |
| Government Girls Middle School | Basti Chatani 2 No |
| Government Girls High School | Chatani |
| Government Boys Primary School | Basti Shina |
| Government Boys Primary School | Javaid More |

CHAPTER:13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE (SITES) LISTED ABOVE. EMERGENCY CONTIGENCY PLAN MUST INCLUDE.

Site No. 2.   	Left Marginal Bund ( LMB)

RD (3000 – 6000)

13.2	DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.

L.M.B.

| S# | Name Village / Basti | No of House | Population |
| --- | --- | --- | --- |
| 1 | Mouza Darod Ghan | 20 | 100 |
| 2 | Basti Nagana | 500 | 2200 |
| 3 | Javed Chaock | 30 | 150 |
| 4 | Korara Basti | 250 | 1000 |
| 5 | Chena Basti | 300 | 1500 |
| 6 | Bihnda Chadhr | 400 | 1500 |
| 7 | Basti Sindian | 450 | 1600 |
| 8 | Chak Faisalabad | 450 | 1800 |
| 9 | Joeyan Wala | 700 | 3000 |
| 10 | Budhan Wali Basti | 2500 | 10000 |

The Villages / Abbadies likely to be affected due to apprehended breaches on LMB.

  - STRATEGY AND ACTION TAKEN

Through all precautionary measures are adopted before flood season to face any alarming situation at Mailsi Syphon Cum Barrage, even then arrangements are necessary to avoid heavy damages and flood fighting strategy is adopted in such a way that flood water passes safely through Mailsi Syphon Cum Barrage, up to its limit.

In low flood, watching establishment employed for this purpose will remain busy in removing jungle, filling gharas and porcupine holes if any.

When water increases beyond Fifty thousand cusecs, then it becomes necessary to be vigilant and to avoid any mishap. Sub Engineers will shift their camps to sites as per duty roaster.

When river water enters into high flood range, Sub Divisional Officer  Mailsi Syphon  will shift his camp at Mailsi Syphon Cum Barrage  to supervise staff working on RMB, LMB and allied spurs and whole period regulation will be done wisely.

Gauges of different sites especially gauge at Mailsi Syphon Cum Barrage will be noted regularly and recorded. Executive Engineer will inform all agencies especially civil administration as well as Army about flood situation. In case of very high flood, meeting will be held in field office with Army and Civil Administration to face the situation.

In light of Standard Operation Procedure (SOPs) to minimize damage to public / private infrastructure, land and abadies, in case of emergency, the flood fighting activities have been divided in to three operational domains.

RESCUE

RELIEF

REHABILITATION ACTIVITES

During the emergency, each sector team shall remain present in its respective flood duty and coordinate with each other.

RESCUE

The Rescue sector will watch   precautionary measures, dissemination of flood alerts, evacuation call to the vicinity villages and forcible evacuation if required. Also work will be done with coordination and full cooperation of Pak Army.

2.		RELIEF

Relief sector will watch his responsibilities as provision of essential Articles such as food, medicine and shelter huts.

3.		REHABILITATION

Rehabilitation sector will watch the appraisal of damages, restorations of services like electricity, Telephone, Communication infrastructure etc, resettlement of displaced in temporary / permanent dwellings. Likewise, each team at flood relief camp shall be responsible for arrangements of food, bedding and other basic amenities required in flooded area.

13.3.1  ARRANGMENT

L.M.B.

Watching establishments on vulnerable sites on LMB at RD.3000-RD.6000 and arrangement of tractors with front blade, excavators and other equipment for safety of flood bunds will be arranged to cope with the emergency.

CAMPS OF WATCHING ESTABLISHMENT

Establishment has been divided in different “Beats” for watching of flood bunds round the clock in different flood stage Detail is as under

LEFT  MARGINAL BUND

Beat Number – 1		= RD. 0-20

Beat Number – 2		= RD. 20-40

Beat Number – 3		= RD.40-65282 Tail

1. LOW FLOOD (0.50 Lac  to 0.80 Lac Cusecs.

Beat  No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Mechanical Section 03056509464 | LMB | RD.0-20 = 4 Mile | 3 Beldar per mile | 12 | 2 |

Beat  No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Arshad Javaid SBE Thingi Section 0300-8111461 | LMB | RD. 20-40 = 4 Mile | 3 Beldar per mile | 12 | 2 |

Beat  No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Toseef Shah SBE Colony Section 0301-7401253 | LMB | RD.40-65282 = 5 Mile | 3 Beldar per mile | 15 | 2 |

13.3.2  	CAMPS OF WATCHING ESTABLISHMENT

LEFT  MARGINAL BUND

Beat Number – 1		= RD. 0-20

Beat Number – 2		= RD. 20-40

Beat Number – 3		= RD.40-65282 Tail

2.MEDIUM  FLOOD ( 0.80 to 1,75,000 Lac Cusecs.

Beat  No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulam Nabi SBE Mechanical Section 03056509464 | LMB | RD.0-20 = 4 Mile | 8 Beldar per mile | 32 | 4 |

Beat  No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Arshad Javaid SBE Thingi Section 0300-8111461 | LMB | RD. 20-40 = 4 Mile | 8 Beldar per mile | 32 | 4 |

Beat  No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Toseef Shah SBE Colony Section 0301-7401253 | LMB | RD.40-65282 = 5 Mile | 8 Beldar per mile | 40 | 4 |

CAMPS OF WATCHING ESTABLISHMENT

LEFT  MARGINAL BUND

Beat Number – 1		= RD. 0-20

Beat Number – 2		= RD. 20-40

Beat Number – 3		= RD.40-65282 Tail

3.HIGH  FLOOD (  1,75,000 2,25,000 Lac Cusecs.

Beat  No.1

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Ghulan Nabi SBE Mechanical Section 03056509464 | LMB | RD.0-20 = 4 Mile | 10 Beldar per mile | 40 | 4 |

Beat  No.2

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Arshad Javaid SBE Thingi Section 0300-8111461 | LMB | RD. 20-40 = 4 Mile | 10 Beldar per mile | 40 | 4 |

Beat  No.3

| Site incharge | Sector incharge | Name of Site | Reach | Unit Rate of Men | No of Beldars | No of Mate |
| --- | --- | --- | --- | --- | --- | --- |
| Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Toseef Shah SBE Colony Section 0301-7401253 | LMB | RD.40-65282 = 5 Mile | 10 Beldar per mile | 50 | 5 |

13.3.3 	DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP SITES

Duties of Officers / Officials & Their Camp at RD.7 of LMB

SUB DIVISIONAL OFFICERS

The flood fighting camps will be arranged on RD. 7 of Left Marginal Bund Sub Divisional Officer Mailsi Syphon Sub Division will be in charge Sub Engineer Khanpur & Sub Engineer Bund will be incahrge and will performance also  their duties with other establishment i.e. Beldars, Mates etc.

| S# | Name of SDO | Reach | Headquarter |
| --- | --- | --- | --- |
| 1 | Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | RD.0-13/L.M.B. | Mailsi Syphon Cum Barrage |

SUB ENGINEERS

| S# | Sub Engineer | Reach | Headquarter |
| --- | --- | --- | --- |
| 1 | Ghulam Nabi SBE Khanpur 0305-6509464 | RD. 0-13/ L.M.B. | RD. 7 of L.M.B |

MATE & BELDARS

| S# | Reach | Beldar | Mate |
| --- | --- | --- | --- |
| 1 | RD. 0-13/L.M.B. | 13 | 2 |

    - DEPARTMENTAL MACHINERY AVAILABLE

Departmental machinery is not available. This will be brought on site from the Agriculture Department.

    - MACHINERY AVAILABLE FROM PRIVATE SOURCE

L.M.B.

1.	Excavator		= 4 No.

2.	Dumper		= 4 No.

3.	Tractor Trolly	= 8 No

    - FLOOD FIGHTING MATERIAL REQUIRED FOR

MAILSI  SYPHON CUM BARARGE.

    - FLOOD FIGHTING MATERIAL AVAILABLE FOR

MAILSI  SYPHON CUM BARARGE.

| Sr # | Item | Unit | Required | Available | Balance | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | G.I. Bucket | No | 75 | 75 | 0 |  |
| 2 | Kassi Handle | No | 20 | 20 | 0 |  |
| 3 | Khaji Mate | No | 1000 | 0 | 1000 |  |
| 4 | Basket | No | 1000 | 0 | 1000 |  |
| 5 | Torche cell | No | 24 | 0 | 24 |  |
| 6 | Lantern | No | 100 | 65 | 35 |  |
| 7 | Petromax lamp | No | 13 | 13 | 0 |  |
| 8 | Gunney bag | No | 6000 | 0 | 6000 |  |
| 9 | Faber glass boat | No | 1 | 1 | 0 |  |
| 10 | Kassi | No | 500 | 478 | 22 |  |
| 11 | Munjban | Kg | 300 | 0 | 300 |  |
| 12 | Stone for emergency at LMB & RMB | Cft | 5.4685 Cft Lac | 5.4685 Cft Lac | 0 |  |

This balance quantity of Flood Fighting Material will be procured before starting of flood season 2022.

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDINGS, CANALS & DRAINAGE NETWORK

L.M.B.

TELEPHONE.

There is no Land Line Telephone Service in this Area.

CANALS.

Sidhnai Mailsi Bahawal Link.

ROAD NETWORK

- Mailsi – Khairpur Tamewali Road.

- Hasilpur – Bahawalpur Road.

OTHER BUILDINGS

| Electric Pools 11 KVA |  |
| --- | --- |
| Government Girls Primary School | Basti Chadar |
| Government Boys Primary School | Madina Chowk |
| Government Boys Primary School | Joya Wala |
| Government Boys High School | Madina Chowk |

Chapter :14

Action Plan

| 14.1 | Re-shuffling / recouping plan of reserve stone departmentally |
| --- | --- |

| S.No | Reserve Stock limit (Lac Cft) | Quality Available (Lac Cft) | Balance quantity required (Lac Cft) |
| --- | --- | --- | --- |
| 1 | 5.4685 | 5.4685 | --- |

Reserve Stock of Stone will be reshuffled through Govt contractor.

| 14.2 | Detail of inlet / outlet crossing along with closing methodology. |
| --- | --- |

LMB		Sluice 			RD.25279/L

Pipe of Tubewell		RD.27300 Culvert Jamalpur Minor

Sluice				RD.29569/L

Sluice				RD.32900

Sluice 			RD.46500

RMB		Sluice				RD.36415

Sluice				RD.39383

14.3		Deployment Machinery (Medium to high flood)

| S# | Name of Structure | Length in Mile | Vulnerable reach | Camp location | Site incharge Name & Cell No. | Sector incharge | Machinery deployed | Labour Beldar + Mate | Availability of Stone in lac Cft |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Excavator | Dozer | Trolly Dumper | Tractor with front blade |  |  |
| 1 | RMB | 10.28 | RD.7500-9500 | Mailsi Syphon | Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Sub Engineer Bund | 2 | 1 | 2 | - | 30 + 5 | - |
| 2 | Mole Head Spur | 1.19 | - |  |  | Sub Engineer Bund | 1 | - | - | 2 | 4 + 1 | 0.27 |
| 3 | LMB | 13.06 | RD.3000-6000 |  |  | Sub Engineer Mechanical | 2 | 1 | 2 | - | 39 + 6 | 0.04921 |
|  |  |  |  |  |  | Total:- | 5 | 2 | 4 | 2 | 85 |  |

‘Payment for Machinery and Work Charge Employees subject to verification by TPM/Consultant’’

| 14.4 | Deployment of Machinery (High to very high flood) |
| --- | --- |

| S# | Name of Structure | Length in Mile | Vulnerable reach | Camp location | Site incharge Name & Cell No. | Sector incharge | Machinery deployed | Labour Beldar + Mate | Availability of Stone in lac Cft |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Excavator | Dozer | Trolly Dumper | Tractor with front blade |  |  |
| 1 | RMB | 10.28 | RD.7500-9500 | Mailsi Syphon | Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Sub Engineer Bund | 4 | 2 | 4 | - | 100 + 10 | - |
| 2 | Mole Head Spur | 1.19 | - |  |  | Sub Engineer Bund | 2 | - | - | 4 | 12 + 2 | 0.27 |
| 3 | LMB | 13.06 | RD.3000-6000 |  |  | Sub Engineer Mechanical | 4 | 2 | 4 | - | 130 + 13 | 0.4921 |
|  |  |  |  |  |  | Total:- | 10 | 4 | 8 | 4 | 267 |  |

‘Payment for Machinery and Work Charge Employees subject to verification by TPM/Consultant’’

| 14.5 | Deployment of Machinery (High to exceptionally high flood) |
| --- | --- |

| S# | Name of Structure | Length in Mile | Vulnerable reach | Camp location | Site incharge Name & Cell No. | Sector incharge | Machinery deployed | Labour Beldar + Mate | Availability of Stone in lac Cft |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Excavator | Dozer | Trolly Dumper | Tractor with front blade |  |  |
| 1 | RMB | 10.28 | RD.7500-9500 | Mailsi Syphon | Muhammad Hanif Zahid SDO Mailsi Syphon 0302-7705684 | Sub Engineer Bund | 4 | 2 | 4 | - | 125 + 15 | - |
| 2 | Mole Head Spur | 1.19 | - |  |  | Sub Engineer Bund | 2 | - | - | 4 | 20 + 5 | 0.27 |
| 3 | LMB | 13.06 | RD.3000-6000 |  |  | Sub Engineer Mechanical | 4 | 2 | 4 | - | 150 + 15 | 0.4921 |
|  |  |  |  |  |  | Total:- | 10 | 4 | 8 | 4 | 330 |  |

‘Payment for Machinery and Work Charge Employees subject to verification by TPM/Consultant’’

| 14.6 | Police deployment plan. Flood duty roaster Police & Ranger |
| --- | --- |

| Sr | Name of Barrage | Concerned Canal Division | Concerned Police Station & District | Police personal to be deployed | Remarks (If any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / S.I / A.S.I | Constable |  |
| 1 | Mailsi Syphon | Mailsi Syphon Division | Mailsi Saddar & Vehari | 1 No Hawaldar | 3 No. Constable 2 No Wireless Operator |  |

| 14.7 | Detail of synthetic bags with capacity of 500 Kg to 1000 Kg |
| --- | --- |

Not required

| 14.8 | Detail of polythene sheets of black color to protected upstream slope, against wave action and to control seepage through embankments. |
| --- | --- |

Not required

Chapter: 15

BACK UP DIVISION (IN CASE OF BREACH)

In case of breach, Lower Western Bar Division will work as back up division.

Executive Engineer,		Superintending Engineer,	      Chief Engineer,

Mailsi Syphon Division,	Mailsi Canal Circle Multan,          Irrigation Zone Multan

Thingi.

# Text boxes

Sub Divisional Officer

Karampur  Sub Division

Sub Divisional Officer

Mailsi Syphon  Sub Division

Sub Engineer

Alipur Section

S.M.B. Link RD.76-145

Sub Engineer

Mailsi Syphon Section

S.M.B. Link RD.300-325

Sub Engineer

Colony Section

S.M.B. Link RD.145-170

Sub Engineer

Khairpur Section

S.M.B. Link RD.325-375(T)

Sub Engineer

Thingi Section

S.M.B. Link RD.170-240

Sub Engineer

Mechanical   Section

Sub Engineer

Khanpur Section

S.M.B. Link RD.240-300

Sub Engineer

Bund   Section

RMB 0-51

LMB 0-65

Sub Engineer

Mech Section