IRRIGATIpON  DEPARTMENT

POTOHAR IRRIGATION ZONE RAWALPINDI/ISLAMABAD

FLOOD FIGHTING PLAN 2023

PART A & B

SMALL DAM CIRCLE-II JHELUM

JHELUM CANAL DIVISION, JHELUM

INDEX

FLOOD FIGHTING PLAN 2021

| Chapter | PART (A) | PAGE No. |
| --- | --- | --- |
| 1 | Salient Feature of Division |  |
| 1.1 | Location | 1 |
| 1.2 | General Description | 1 |
| 1.3 | Administrative Setup | 2 |
| 2 | Flood Protection and River Training Works |  |
| 2.1 | Design Parameter of River Training Works | 3-6 |
| 2.2 | Location Map | 7 |
| 3 | Brief History Of Past Flood Events | 8 |
| 4 | Design Data, Historic Peak Flood Data and Previous five years Flood Data of Headworks / Barrages and or other Control points | 9 |
| 4.1 | Flood Limits | 10 |
| 4.2 | Time Lags of Floods | 10 |
| 4.3 | Highest Floods | 10 |
| 4.4 | Peak Discharges | 11 |
| 5 | Flood Fighting Strategy | 12 |
| 6 | Flood Damages Restoration Works | 14 |
| 7 | Flood Fighting Watching Arrangement | 15 |
| 7.1 | Pre-Flood Arrangement | 15 |
| 7.2 | Watching Establishment | 15 |
| 7.3 | Arrangement at Sensitive sites | 16 |
| 7.4 | Watching Material | 16 |
| 7.5 | Arrangement for Sounding & Probing | 17 |
| 7.6 | Lighting Arrangement | 17 |
| 7.7 | Ration Arrangement | 17 |
| 7.8 | P.O.L Arrangement for Vehicle | 17 |
| 7.9 | Transportation | 17 |
| 7.10 | Law and Order | 18 |
| 7.11 | Medical Arrangement for Labour | 18 |
| 7.12 | Liason with other Department | 18 |
| 7.13 | Role of the Army | 18 |
| 7.14 | Duties of Telephone Attendant | 19 |
| 7.15 | Wireless Arrangements | 19 |
| 8 | Detail of Encroachment | 21 |
| 9 | Duty Roaster / Flood Fighting Program | 22 |
| 10 | Emergency Telephone No’s | 24 |
| 11 | Standard Operating Procedure (SOP) for Breaching Sections | 26 |
| 11.1 | History of Breaching Section | 26 |
| 11.2 | Location, Quantity, Design and Variety of the Explosive Required for Detonation | 26 |
| 11.3 | Arrangements of Explosives and Security of Explosives Stores | 26 |
| 11.4 | List of Security Staff along with details of their trainings etc. | 26 |

| Chapter |  | PAGE No. |
| --- | --- | --- |
| 11.5 | Details of machinery means as standby arrangements in case of detonation failure | 26 |
| 11.6 | Duty roaster in case of critical situation | 26 |
| 11.7 | Breaching committee with their action plan | 26 |
| 11.8 | List of villages likely to be inundated in case of breach | 26 |
| 11.9 | Announcement and details of evacuation arrangements | 26 |
| 11.10 | Details of coordination with civil/ army authorities | 26 |
| 11.11 | Parallel communication arrangements | 26 |
| 11.12 | Index plan | 26 |
| Chapter | Part – B |  |
| 12 | Vulnerable sites on flood Bund/ Structures | 28 |
| 12.1 | Apprehended Breaches in flood Bund/ structures | 28 |
| 12.2 | Operation of Breaching sections | 28 |
| 12.3 | Breaches due to rise of flood water, deterioration of flood bunds | 28 |
| 13 | Emergency contingency plan for vulnerable sites | 29-42 |
| 13.1 | Plan showing route of flood water coming out of the expected breaching point supported with levels |  |
| 13.2 | Details of villages, abadies likely to be affected and this should also be shown on plan |  |
| 13.3 | Strategy and action taken, explained in details. This may include: |  |
|  | 13.3.1 Arrangements |  |
|  | 13.3.2 Establishment of flood fighting camps |  |
|  | 13.3.3 Duties of officers/ officials and their camp sites |  |
|  | 13.3.4 Departmental machinery available |  |
|  | 13.3.5 Machinery available from private sources |  |
|  | 13.3.6 Flood fighting material requited |  |
|  | 13.3.7 Flood fighting material available |  |
| 13.4 | Detail of other infrastructure like electricity, sui gas, telephone installation, road network, other building, canal and drainage network. |  |
| 14 | Action Plan | 43 |
| 14.1 | Re-shuffling/ Recouping plan of reserve stone departmentally | 43 |
| 14.2 | Detail of inlet/ outlet crossing along with closing methodology | 43 |
| 14.3 | Deployment Machinery (Medium to high flood) | 43 |
| 14.4 | Deployment Machinery (High to very high flood) | 45 |
| 14.5 | Deployment Machinery (Very high to exceptionally high flood) | 46 |
| 14.6 | Police deployment plan | 47 |
| 14.7 | Details of synthetic bags with capacity of 50 kg and 100 kg | 47 |
| 14.8 | Details of polythene sheet of black colour to protect upstream slope against wave action and to control seepage through embankments | 47 |
| 15 | Back up Divisions (In case of breach) | 48 |

PART-A

OFFICE OF THE

EXECUTIVE ENGINEER

JHELUM CANAL DIVISION JHELUM

IRRIGATION DEPARTMENT

Tel: 0544-9270331, Fax: 0544-9270311

Email: xen_jhelum@irrigation.punjab.gov.pk

To

The Director Flood,

Drainage & Flood Zone,

Govt. Engineering Academy Punjab,

Canal Bank Road,

Thokar Niaz Lahore.

No.		/5-W/Flood			dated		/2023

SUBJECT:-	FLOOD FIGHTING PLAN FOR THE YEAR 2023

Kindly find enclosed herewith a copy of Flood Fighting Plan 2023 pertaining to Jhelum Canal Division Jhelum for necessary vetting and return please.

DA/As above								Executive Engineer

Jhelum Canal Division

Jhelum

CC

- The Chief Engineer, Irrigation, Potohar Zone, Islamabad for information please.

- The Project Director, Small Dam Circle-II, Chakwal for information please.

OFFICE OF THE

EXECUTIVE ENGINEER

JHELUM DIVISION UJC JHELUM

IRRIGATION DEPARTMENT

Tel: 0544-9270331, Fax: 0544-9270311

email: xenjhelum_canal@yahoo.com

To

The Project Director,

Small Dam Circle-II,

JHELUM

No.XEN		/5-W/Flood		dated		/2023

SUBJECT:-	FLOOD FIGHTING PLAN FOR THE YEAR 2023.

Kindly find enclosed herewith the Flood Fighting Plan 2023 after vetting the Chief Engineer, D&F Zone vide letter D&F/2021/2102/25/76 dated   /04/2023 for onward transmission to  CE Irrigation, Potohar Zone, Islamabad may signature please.

DA/As above								Executive Engineer

Jhelum Canal Division

Jhelum

OFFICE OF THE

EXECUTIVE ENGINEER

JHELUM DIVISION UJC JHELUM

IRRIGATION DEPARTMENT

Tel: 0544-9270331, Fax: 0544-9270311

email: xenjhelum_canal@yahoo.com

To

The Chief Engineer,

Irrigation Sargodha Zone,

Sargodha

No.XEN(DB)		/5-W/Flood		dated		/2023

SUBJECT:-	FLOOD FIGHTING PLAN FOR THE YEAR 2023.

Kindly find enclosed herewith 2-copies of Flood Fighting Plan 2023  vetting by the CE D&F Zone vide letter No. D&F/2023/1142/25/46 dated   /04/2019 for submission may signature please.

DA/As above								Executive Engineer

Jhelum Division UJC

Jhelum

CC.

The Superintending Engineer, Upper Jhelum Canal Circle, Jhelum for information please.

CHAPTER-1

SALIENT FEATURES OF JHELUM DIVISION

1.1	LOCATION

Upper Jhelum Canal off takes from Mangla Dam at 33 ͦ 07’ 16” N Latitude & 73 ͦ 38’ 24” Longitude and passes through the Districts Mirpur, Bhimber, Gujrat and Mandi Bahauddin before it out falls in the River Chenab U/S Khanki Barrage at Latitude 32 ͦ  27’ 45” N and Longitude 74 ͦ 01’ 26” E.

1.2	GENERAL DESCRIPTION

Jhelum Division has been entrusted with the maintenance of Upper Jhelum Canal from RD 27+500 to 440+000 (134 KM).The length of Flood embankment in the jurisdiction is 52.763 KM. Jhelum Canal Division is affected by the Floods in River Jhelum, Nullah Kahan, Nullah Bunahan River Chenab and Bhimber Nullah.

- RIVER JHELUM

Jhelum River originates from occupied territories of Jammu and Kashmir and after traversing a long distance in the hilly areas of Gilgit and Azad Kashmir it enters into Mangla Dam Reservior.

Mangla Head works was constructed on River Jhelum in the year 1915 at a distance of about 23 miles in the Northern direction of Jhelum City. It remained in operation till the construction of Mangla Dam. River Jhelum flows parallel to the UJC in reach RD. 27+500 to 243+000 and poses a threat to the safety of Canal in the reach RD 27+500 to 41+000.

- KAHAN RIVER

It is a hill torrent. Maximum discharge of 1, 20,000 Cs was noticed during the flood of 1992. It outfalls into River Jhelum, D/S of Jhelum Cantonment near Village Naugran, after traversing a long distance in District Jhelum. As it is a hill torrent and carries flashy discharge due to very steep slope, it causes erosion to the Adjoining lands and abadies of District Jhelum.

XEN/JLM

- BHIMBER NULLAH

Bhimber Nullah is a tributary of River Chenab and flows along the left bank of Upper Jhelum Canal from RD. 414+000 to 425+000 before it outfalls into River Chenab, upstream of Khanki Headwork’s. This reach of the channel, where Nullah is in closed vicinity has been protected by properly designed stone pitching; however, the channel is kept under watch during flood season.

- NULLAH BUNAHAN

Nullah Bunahan is tributary of River Jhelum which originates from boundary of District Chakwal and falls in River Jhelum U/S Rasul Barrage. The Discharge of Nullah Bunahan is 75000 Cs which causes inundation of crop and abadies of Village Bhambar and water spreads over Jhelum-PD Khan Road as well. Now Bhamber Flood Bund has been constructed along left bank of Nullah Bunahan up to 7473 Ft to safeguard crops and Adjoining  village abadi.

XEN/JLM

  - ADMINISTATIVE SETUP

The Jhelum Canal Division Jhelum has now been attached with Small Dam Circle-II,Jhelum. The Head Quarter of Jhelum Division is at 46-A Sarwar Road Jhelum Cantt.

- Mangla Sub Division with Office of the SDO stationed at WAPDA Colony Mangla is responsible for maintaining Upper Jhelum Canal from RD. 27+500 to 150+000, flood bunds along River Jhelum from Mangla to G.T Road bridge and flood bunds on Nullah  Kahan and Nullah Bunhun Maintenance and safe ruing  .

- Khokhra Sub Division Office at Rasul is responsible to maintain Upper Jhelum Canal from RD. 150+000 to RD. 440+000 (tail) and flood bunds/ guide walls along River Jhelum from G.T Road Bridge to Rasul Head Works.

XEN/JLM

CHAPTER-2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1	  DESIGN PARAMETERS OF TRAINING WORKS

| S.No. | Name of Bund or Stud | Top width | Length | Side Slope | Remarks |
| --- | --- | --- | --- | --- | --- |
| i | RIVER JHELUM |  |  |  |  |
| 1. | C.D. Bund | 20 Ft | 2260 Ft | 3:1 inner & 2:1 outer | Bund is abandoned due to construction of Jhelum City Flood Bund River Side. |
| 2. | G.H. Bund | 20 Ft | 840 Ft | 3:1 inner & 2:1 outer | Bund is abandoned due to construction of Buildings on River Side. |
| 3. | Spur No.1 | 24 Ft | 1365 Ft | 2:1 inner & 2:1 outer | Spur from Sr. No. 3 to 8 Located in Jhelum City Due to Construction of Jhelum City Bund |
| 4. | Spur No.2 | 24 Ft | 790 Ft | 2:1 inner & 2:1 outer |  |
| 5. | Spur No.3 | 24 Ft | 725 Ft | 2:1 inner & 2:1 outer |  |
| 6. | Spur No. ’X’ | 20 Ft | 130 Ft | 2:1 on either side |  |
| 7. | Spur No. ’Y’ | 30 Ft | 165 Ft | 2:1 on either side |  |
| 8. | Spur No. ’Z’ | 20 Ft | 185 Ft | 2:1 on either side |  |
| 9. | Jhelum Cantt Protection Bund | 25 Ft | 2500 Ft | 2:1 on either side |  |
| 10. | Stud No. 1 near village Sheikhupur . | 15 Ft | 75 Ft | 2:1 on either side |  |
| 11. | Stud No. 2 near village Loharian | 15 Ft | 75 Ft | 2:1 on either side |  |
| 12 | Stud No. 3 near village Khatana. | 15 Ft | 75 Ft | 2:1 on either side |  |
| 13. | Stud No. 4, 5, 6, near village Dulyal (3 No.) | 15 Ft | 75 Ft | 2:1 on either side |  |
| 14. | Stud No. 7 near village Budhar | 15 Ft | 75 Ft | 2:1 on either side | Washed away during Flood 2014 Estimate has been submitted for Restoration which is under approval process |
| 15. | Stud No.8 near Pind Rajwal | 15 Ft | 75 Ft | 2:1 on either side |  |
| 16. | Stud No.9 near village Chak Balian | 15 Ft | 75 Ft | 2:1 on either side |  |
| 17. | Stud No.10 U/s village Bhoundnan Gakhran | 15 Ft | 75 Ft | 2:1 on either side |  |
| 18. | Stud No.11 near village Pindi Khaira | 15 Ft | 75 Ft | 2:1 on either side |  |
| 19. | Stud No.12near village Pindi More | 15 Ft | 75 Ft | 2:1 on either side | Washed away during Flood 2014 Estimate has been submitted for Restoration which is under approval process |
| 20. | Stud No.13,14, near village Chak Daulat | 15 Ft | 75 Ft | 2:1 on either side |  |
| 21 | Stud No.15,16, near village Chak Daulat | 15 Ft | 75 Ft | 2:1 on either side |  |

XEN/JLM

| S.No. | Name of Bund or Stud | Top width | Length | Side Slope |
| --- | --- | --- | --- | --- |
| 22. | Stud No.17 near village Masumpur | 15 Ft | 150+55 Ft | 2:1 on either side |
| 23. | Paharwal guide wall | 25 Ft | 2299 Ft | 2:1 on either side |
| 24. | Shah Madar guide wall | 25 Ft | 1847 Ft | 2:1 on either side |
| 25. | Khaderiala guide wall | 25 Ft | 2182 Ft | 2:1 on either side |
| 26. | New Paharwal Guide wall | 25 Ft | 1980 Ft | 2:1 on either side |
| 27. | Kharka Guide wall | 25 Ft | 1444 Ft | 2:1 on either side |
| 28. | Gurha Jattan Guide wall | 25 Ft | 2105 Ft | 2:1 on either side |
| 29. | Protection Bund near RD.33 UJC. | 25 Ft | 1500 Ft | 2:1 on either side |
| 30. | Jabbar Bund | 20 Ft | 4200 Ft | 3:1 on either side |
| 31. | Solid Stone Spur Pakhwal & Tawakal Pakhwal | 20 FT | 410 Ft | 1½:1 on either side |
| 32. | Jhelum City Bund | 25 Ft | 20000 Ft | 2:1 River side & 3:1 Country side |
| 33. | Saraland guide Bund | 25 Ft | 1800 Ft | 2:1 River side & 3:1 Country side |
| 34. | Spur No.1 | 15 Ft | 250 Ft | 2:1 on either side |
| 35. | Spur No.2 | 15 Ft | 330 Ft | 2:1 on either side |
| 36. | Spur No.3 | 15 Ft | 200 Ft | 2:1 on either side |
| 37. | Spur No.4 | 15 Ft | 350 Ft | 3:1 on either side |
| 38. | Spur No.5 | 15 Ft | 300 Ft | 2:1 on either side |
| 39. | Spur No.6 | 15 Ft | 700 Ft | 2:1 on either side |
| 40. | Gurha Ahmed Bund | 25 Ft | 7000 Ft | 2:1 on either side |
| 41. | Naugran Flood Bund | 20 Ft. | 27500 Ft | 2:1 on either side |
| 42. | UJC Protection Bund RD.293-299/L | 25 Ft | 6000 Ft | 1½:1 on either side |
| 43. | UJC Protection Bund RD.305-320/L | 25 Ft | 15000 Ft | 1½:1 on either side |
| 44. | UJC Protection Bund RD.418-438/L | 25 Ft | 20000 Ft | 1½:1 on either side |
| 45. | UJC Protection Bund RD.427-440/R | 25 Ft | 13000 Ft | 1.½:1 on either side |

XEN/JLM

| Sr. No. | Name of Bund or Stud | Top width | Length | Side Slopes (River Side / Country Side) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Nullah Bunahan |
| 1 | Bhamber Flood Bund on Nullah Bunahan | Village Bhambar | 7473 Ft | 2:1 on either side | 2:1 on either side |

BUNDS ALONG LEVEL CROSSINGS.

| 1. | BONG LEVEL CROSSING |
| --- | --- |
| i | U/S Right Bund | 20 Ft | 300 Ft | Pitched 1.5:1/2:1 |  |
| ii. | U/S Left Bund | 20Ft | 2500Ft | Pitched 1.5:1/2:1 |  |
| iii. | D/S Right Bund | 20 Ft | 150 Ft | Pitched 1.5:1/2:1 |  |
| iv | D/S Left Bund | 20 Ft | 2900 Ft | Pitched 1.5:1/2:1 |  |
| 2. | JATLI LEVEL CROSSING |
| i. | U/S Right Bund | 30Ft | 925 Ft | Pitched 1.5:1/2:1 |  |
| ii. | U/S Left Bund | 30 Ft | 4550 Ft | Pitched 1.5:1/2:1 |  |
| iii. | D/S Right Bund | 30 Ft | 1250 Ft | Pitched 1.5:1/2:1 |  |
| iv. | D/S Left Bund | 30 Ft | 1250 Ft | Pitched 1.5:1/2:1 |  |
| 3. | REHMANPUR LEVEL CROSSING |
| i. | U/S Right Bund | 30 Ft | 6000 Ft | Pitched 1.5:1/2:1 |  |
| ii. | U/S Left Bund | 30 Ft | 1000 Ft | Pitched 1.5:1/2:1 |  |
| iii. | D/S Right Bund | 30 Ft | 1000 Ft | Pitched 1.5:1/2: |  |
| iv. | D/S Left Bund | 30 Ft | 1000 Ft | Pitched 1.5:1/2: |  |
| JAGGU LEVEL CROSSING |
| i. | U/S Right Bund | 25 Ft | 4750 Ft | Pitched1.5:1/2:1 |  |
| ii. | U/S Left Bund | 25 Ft | 2705 Ft | Pitched 1.5:1/2:1 |  |
| iii. | D/S Right Bund | 20 Ft | 1000 Ft | Pitched 1.5:1/2:1 |  |
| iv. | D/S Left Bund | 25 Ft | 1000 Ft | Pitched 1.5:1/2:1 |  |
|  | TOTAL |  | 173062 Ft. |  |  |
|  | G.TOTAL |  | 52.763 KM |  |  |

XEN/JLM

2.2	LOCATION MAP

CHAPTER-3

BREIF HISTORY OF PAST FLOOD EVENTS

RIVER JHELUM.

Since construction of Mangla Dam, flood discharges in River Jhelum D/S Mangla are very low, however, in 1992, an exceptionally high flood of 10,50,000 Cs. was experienced in River Jhelum. The abadies along River Jhelum on both banks were affected. Jhelum City was inundated with a heavy loss to lives and properties. Vast lands of villages U/S Jhelum city on right bank were eroded. Consequently 17 No. Studs were constructed in 1994-95 for protection of these villages against erosion.

The tendency of River flow D/S G.T. Road Bridge was towards left Bank and eroded away the abadies and agricultural land of villages Chak Sikandar, Kharka, Gurha Jattan, Bhalwal Gharbi, Paharwal. 6 No. Guide walls were constructed to safeguard these villages.

KAHAN RIVER

Normally 60,000 to 70,000 Cs. discharge is experienced in River Kahan, but in 1992 about 1,20,000 Cs. was recorded. The velocities are very high due to steeper slope. Six No. spurs for protection of village Chak Almas, Kalwantpur, Shahmadpur, Bagh, Rajupindi and Chah Gunja were constructed during 1986-87 and 1989-90 to save these abadies against erosion. A flood embankment for protection of village Gurha Ahmed has been constructed in a length of 10000 ft. in the year 1994-95 and 2016-17 on L/side. Another flood embankment namely, “Naugran Flood Protection Bund” was constructed in the year 1929 by District Council Jhelum and has been rehabilitated under ADP up to length of 19500 Feet on Right side.

BHIMBER NULLAH

Bhimber Nullah is a tributary of river Chenab and directly hit the left Bank of UJC at RD 414-425

XEN/JLM

CHAPTER-4

# DESIGN DATA HISTORIC PEAK FLOOD DATA AND PREVIOUS  YEARS FLOOD DATA OF HEAD WORKS/ BARRAGES AND OR OTHER CONTROL POINTS.

4.1	FLOOD LIMITS

River Jhelum at Railway Bridge

| 1. Low flood. | 0.75 lac to 1.10 lac Cs. |
| --- | --- |
| 2. Medium Flood | 1.10 lac to 1.50 lac Cs. |
| 3. High Flood | 1.50 lac to 2.25 lac Cs. |
| 4. Very High Flood | 2.25 lac and above. |

4.2	TIME LAGS OF FLOODS

The flood water from Mangla to Railway Bridge Jhelum reaches in about 7 hours after traversing a distance of 20 miles whereas from Railway Bridge to Rasul Barrage  also takes about 7 hours.

4.3	HIGHEST FLOODS

| YEAR | Max. Discharge (in Cs.) |
| --- | --- |
| 1988 | 2,53,000 |
| 1992 | 10,50,000 |
| 1995 | 2,80,000 |
| 1997 | 4,64,000 |
| 2010 | 2,26,000 |
| 2014 | 4,80,000 |

XEN/JLM

4.4	PEAK  DISCHARGES JHELUM RIVER

| YEAR | Max. Discharge (in Cs.) | YEAR | Max. Discharge (in Cs.) |
| --- | --- | --- | --- |
| 1980 | 58,146 | 2015 | 129000 |
| 1981 | - | 2016 | 56700 |
| 1982 | - | 2017 | 55000 |
| 1983 | 88,445 | 2018 | 73792 |
| 1984 | 49,993 | 2019 | 105000 |
| 1985 | - | 2020 | 125000 |
| 1986 | 1,03,085 | 2021 | 43000 |
| 1987 | 1,35,000 | 2022 | 55000 |
| 1988 | 2,53,000 |  |  |
| 1989 | 1,53,174 |  |  |
| 1990 | 1,25,247 |  |  |
| 1991 | 1,04,692 |  |  |
| 1992 | 10,50,000 |  |  |
| 1993 | 1,00,000 |  |  |
| 1994 | 1,03,430 |  |  |
| 1995 | 2,80,000 |  |  |
| 1996 | 1,45,336 |  |  |
| 1997 | 4,64,000 |  |  |
| 1998 | 79,500 |  |  |
| 1999 | 45,000 |  |  |
| 2000 | 31,000 |  |  |
| 2001 | 30,000 |  |  |
| 2002 | 40,000 |  |  |
| 2003 | 78,000 |  |  |
| 2004 | 42,000 |  |  |
| 2005 | 92,000 |  |  |
| 2006 | 86,000 |  |  |
| 2007 | 41,000 |  |  |
| 2008 | 37,000 |  |  |
| 2009 | 72,000 |  |  |
| 2010 | 2,26,000 |  |  |
| 2011 | 1,20,000 |  |  |
| 2012 | 82,950 |  |  |
| 2013 | 41,000 |  |  |
| 2014 | 480,000 |  |  |

XEN/JLM

CHAPTER-5

FLOOD FIGHTING STRATEGY

In order to combat the flood, following plan( Low Flood and Medium Flood) is to be put in operation for each River or Nullah and protective works as discussed under: -

RIVER JHELUM

Due to construction of Mangla Dam there is very rare flood trouble in Jhelum River downstream Mangla. However, any flood warning will be tackled as under.

- Low Flood   (0.75 lac to 1.10 lac Cs.)

The Sub Engineer Mangla will remain present at Head quarter during the low floods. Sub Engineer Jhelum will remain present at Jhelum Spurs with watching establishment. Sub Engineer Rajar will remain present at Rajar and shall keep the guide wall along left bank of River Jhelum under watch.

- Medium Flood   (1.10 lac to 1.50 lac Cs.)

The Sub Engineer Mangla will remain present at Head quarter during the low and medium floods. Sub Engineer Jhelum will remain present at Jhelum Spurs with watching establishment. Sub Engineer Rajar will remain present at Rajar and shall keep the guide wall along left bank of River Jhelum under watch.

- HIGH FLOOD (1.50 lac to 2.25 lac Cs)

On receipt of high flood warning, Sub Divisional Officer, Mangla will be stationed at Mangla Head Works and Sub Engineer Bong will patrol right bank of UJC from RD. 27+500 to 41+000. He will be responsible to watch and report any unusual behavior of River Jhelum as far its tendency to move closer to UJC in reach RD. 27+000-41+000. Sub Engineer Jhelum with watching establishment, shall watch all the flood works around Jhelum City.

- VERY HIGH FLOOD (2.25 lac and above)

On receipt of high flood warning, downstream Mangla, the Sub Divisional Officer Mangla will keep Executive Engineer, Jhelum and Project Director Chakwal informed through telephone regarding the situation of Jhelum protection works. He will supervise flood works on River Jhelum. All the flood works will be kept under day & night watch with flood fighting material to meet any emergency. Sub Divisional Officer Khokhra will supervise day and night watching of guide bunds and will keep Executive Engineer Jhelum and Project Director Chakwal informed about the latest situation.

XEN/JLM

RIVER CHENAB

Flood warnings from Marala Headworks and Khanki Headworks will be transmitted through Telephone to flood information center, Jhelum as well as Sub Divisional Officer, Small Dams Sub Division No.1.

i).	Low /Medium Floods (1.50 to 2.0 Lac cs.)

Sub Engineer, Ali Raza will shift to Budhi Nullah Regulator and Sub Engineer Muhammad Arif Bajwa Small Dams, Sub Division Officer, Mian Masood No.1 to tail regulator of R.Q Link.

ii)	HIGH FLOOD (2.0 to 4.00 Lac Cs)

Sub Divisional Officer, Small Dams Sub Division No.II and will supervise watching operations of banks of Upper Jhelum Canal from RD 150 to Tail

iii)	Very High Flood (2.25 to 6.0 Lac Cs) And Budhi Nullah Discharge over 0.10 Lac Cs

District Coordination Officer and Superintendent of Police, Mandi Bahauddin will be approached to assist the Department in case of any emergency.

iv)	Exceptionally High Floods (6.0 Lac Cs and above)

Full mobilization of all resources shall be done. All the flood works will be kept under day and night watch.

Bhimber Nullah along Tail reach UJC, RD. 414+000 to 425+000.

Sub Engineer Shadiwal will remain present, watch and transmit gauges of Bhimber to all concerned round the clock during floods. Sub Divisional Officer Khokhra shall also supervise the operation.

XEN/JLM

CHAPTER-6

FLOOD DAMAGES RESTORATION WORKS

No major flood damages occurred during the flood 2022.

Sara-i-Alamgir Flood Bund

Repairing of damaged River side slopes of the Bund will be done before start of Flood Season 2023.

XEN/JLM

CHAPTER-7

FLOOD FIGHTING WATCHING ARRANGEMENT

7.1	PRE FLOOD ARRANGEMENT

The material as detail attached shall be stored at the following sites.

STATUS OF RESERVE STOCK

| Sr. No. | Name of Division | Reserve Stock Limit (As per Yard Stick) | Quantity available | Balance Required | Tentative Cost of Stone (Rs. In Million) | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| 1 | Jhelum | 5.20 | 1.01 | 4.19 |  | Procurement of reserve stock against minimum requirement has been tried by this Division but no success has so far been achieved. |

Detail is as under:-

| Sr. No. | Name of Structure | Reserve Stock (Lac Cft) | Remarks |
| --- | --- | --- | --- |
|  |  | Limit | Available | Required |  |
| 1. | Old Paharwal Guide Wall on Left Bank of River Jhelum | 1.00 | 0.20 | 0.80 | Will be procured Before Flood Season. |
| 2. | Kharka Guide Wall on Left Bank of River Jhelum | 1.00 | 0.00 | 1.00 |  |
| 3. | Gurha Jattan Guide Wall on Left Bank of River Jhelum | 1.00 | 0.00 | 1.00 |  |
| 4. | Malo Kas on Left Bank of River Jhelum. | 0.20 | 0.00 | 0.20 |  |
| 5. | New Paharwal Guide Wall on left Bank of River Jhelum. | 0.40 | 0.00 | 0.40 |  |
| 6. | Khaderiala Guide wall on Left Bank of River Jhelum. | 0.40 | 0.20 | 0.20 |  |
| 7. | Gurha Ahmed Bund on Kahan River. | 0.30 | 0.20 | 0.10 |  |
| 8. | Jhelum Cantt: Bund on Right Bank of River Jhelum. | 0.20 | 0.05 | 0.15 |  |
| 9. | Jhelum Protection works & studs on Right Bank of River Jhelum. | 0.50 | 0.36 | 0.14 |  |
| 10. | Spurs on Kahan River. | 0.20 | 0.00 | 0.20 |  |
|  | Total | 5.20 | 1.01 | 4.19 |  |

RIVER JHELUM

| 1. Regulation Hut at Bong Level Crossing. | For watching of Jabbar Bund and UJC RD. 27+500 to 41+000. |
| --- | --- |
| 2. Canal Colony Jhelum. | For watching of Protection works around Jhelum City |
| 3. Gurha Ahmed Bund. | For watching of Gurha Ahmed Bund. |

XEN/JLM

KAHAN RIVER

| 4. At studs No. 2 | For watching of 6 No. Studs on Kahan River. |
| --- | --- |
| 5. Rajar Rest House. | For watching/Flood fighting on Guide Bunds at Paharwal, Khaderiala and Shah Madar. |

BHIMBER NULLAH

| 1. Shadiwal Rest House | For watching of left bank of UJC from RD.414+000 to 425+000. |
| --- | --- |

7.2	WATCHING ESTABLISHMENT

Following watching establishment will be engaged during the flood season for watching and general maintenance of flood works on monthly basis. However, in case of very high flood or in real emergency, the strength of watching establishment will be increased with the express permission of Executive Engineer, Jhelum Canal Division.

| Item | Flood Status |
| --- | --- |
|  | Low | Medium | High | Very High | Exceptionally High |
|  | Men | Shift | Men | Shift | Men | Shift | Men | Shift | Men | Shift |
| Jabbar Bund. | 1 | - | 1 | 2 | 3 | - | 4 | - | 5 | 2 |
| UJC RD. 27500-41000. | 1 | - | 1 | 1 | 2 | 1 | 3 | 1 | 5 | 2 |
| Jhelum Protection Works (Studs & Bunds). | 10 | - | 30 | 2 | 40 | 2 | 45 | 2 | 50 | 3 |
| Guide bunds on left bank of River Jhelum. | 8 | - | 1 | - | 4 | 2 | 25 | 1 | 35 | 2 |
| Kahan River. (Gurha Ahmed Bund & Studs).+ Naugran Flood Bund | 3 | - | 16 | 1 | 1 | 1 | 22 | 1 | 30 | 2 |
| UJC RD. 414+000-425+000. | 1 | - | 4 | 1 | 2 | 1 | 6 | 1 | 10 | 1 |

Payment for Machinery & work charge Employment subject to verification by TPM/Consultants.

XEN/JLM

7.3	ARRANGEMENT AT SENSATIVE SITE

1.	Jabbar Bund.

2.	UJC RD. 27500-41000.

3.	Jhelum Protection Works (Studs & Bunds).

4.	Guide bunds on left bank of River Jhelum.

5.	Kahan River. (Gurha Ahmed Bund & Studs).+ Naugran Flood Bund

6.	UJC RD. 414+000-425+000.

7.4	WATCHING MATERIAL

| S.No. | ITEM | Required Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Torches Chargeable (Medium) | 10 No. | NIL | 10 No. | Balance required material will be managed / arranged before Flood Season 2023. |
| 2. | New Gunny Bags (4-6 Cft) with Sulti and sewing needles | 100 No. | NIL | 100 No. |  |
| 3. | Axes large | 5 No. | NIL | 5 No. |  |
| 4. | Kassies with Handles | 10 No. | NIL | 10 No. |  |
| 5. | Long Shoes | 6 No. | NIL | 6 No. |  |
| 6. | Rain Coat | 6 No | NIL | 6 NO |  |
| 7 | Umbrella | 6 No | NIL | 6 No |  |
| 8. | Jug Glass (1 Jug +6 Glass) | 1 Set. | NIL | 1 No. |  |
| 9. | Shouldari Medium | 1 No. | NIL | 1 No. |  |
| 10. | G.I.Wire | 100 Kg | NIL | 100 Kg |  |
| 11. | Generator set. | 1 No. | NIL | 1 No. |  |
| 12. | Service Cable | 4 Coils | NIL | 4 Coils |  |
| 13. | Search light (Large) | 2 No. | NIL | 2 No. |  |
| 14. | Wooden Mallet | 2 No. | NIL | 2 No. |  |
| 15. | Petrol | 500 Liter | NIL | 500 Liter |  |
| 16. | M. Oil | 10 Liter | NIL | 10 Liter |  |
| 17. | Pitching Stone | 50000 Cft. | NIL | 50000 Cft. |  |
| 18. | Water Cooler (Medium Size) | 2 No | NIL | 2 No. |  |
| 19. | First aid Box | 1 No. | NIL | 1 No. |  |

The Flood Fighting Material will be purchased before Flood Season 2023.

7.5	ARRANGEMENT FOR SOUNDING AND PROBING

Sub Divisional Officer concerned will be responsible for making necessary arrangement for observing soundings/ probing of structures in his jurisdiction with the help of Sub Engineers concerned.

7.6	LIGHTING ARRANGEMENT

During peak flood hours, flood fighting operations are carried out round the clock. Torches and rechargeable emergency lights will be arranged, which will facilitate the field formation for successful flood fighting operation. Regular field staff is required to be trained properly and thoroughly to carry out flood watching operations during odd hours. Material will be issued through proper indents.

XEN/JLM

7.7	RATION ARRANGEMENT

Necessary arrangements will be made for ration for the flood watching/ fighting establishment.

7.8	POL ARRANGEMENT FOR VEHICLE

In case the petrol, Oil and lubricants are in short supply on account of disruption for communication elsewhere in the country, the Executive Engineer Incharge will make timely arrangements for having adequate P.O.L reserve at conveniently places at one or more petrol pumps at Dina, Sarai Alamgir, Jhelum and Mandi Bahauddin in consultation with concerned District Coordination Officers/ Deputy District Revenue Officers.

7.9	TRANSPORTATION

Already allocated vehicles to the Division will be used during flood season. In case of exceptionally high flood in River Jhelum, District Coordination Officer, will be requested to supply additional vehicles for the Supervisory staff and for transportation of labour as well as flood fighting material to the sites of work. A Tractor along with Front & rear blade and trolley has allotted to Jhelum Division UJC for regulation of material etc. Sand Bag filling Machine are also available for any emergency situation on Flood protection works in Jhelum Canal Division.

7.10	LAW AND ORDER

Experience shows that whenever any flood emergency arises, inhabitants of the area try to cut the protection bund at upstream to divert the flood threat from their locality. In such a situation it would be necessary for District Administration to provide.

- Day and night patrolling to guard against any attempt to cut a bund or structure.

- Provision of Police Force for any open and defiant attempt of breaching the bund at any place.

In these situations, the District Coordination Officer and District Police Officer of the respective District would be expected to promptly provide adequate police force accompanied with a Magistrate on being apprised of the situation by Executive Engineer In-charge.

7.11	MEDICAL ARRANGEMENT FOR LABOUR

Medical arrangements will be made with the help of District Government / District Health Officer.

XEN/JLM

7.12	LIASON WITH OTHER DEPARTMENTS

The District Coordination Officer and District Police Officer will be contacted in advance and a list of volunteer will be prepared who can be contacted during emergency. The list containing the names of such volunteers and the village Lumbardars made responsible by the Civil Authorities will also be maintained.

7.13	ROLE OF ARMY

Role of Army Authorities during pre flood and in the flood season is very important. Army Authorities have visited all the flood protection works along with departmental inspection team. During flood and in emergency, Army is always available to assist the civil departments fully equipped with all kind of machinery and man power.

7.14	DUTIES OF TELEPHONE ATTENDANT

| Sr. # | Name of Official | Period | Time | Ph. # | Remarks |
| --- | --- | --- | --- | --- | --- |
|  |  |  | From | To |  |  |
| 1 | Hafiz Ghulam Murtaza Signaller | Flood Season | 6.00 | 14.00 | 0331-9606258 | Telegraph Office will be opened 24 Hours in Flood season. |
| 2 | Adeel Ali Naib Qasid | Flood Season | 6.00 | 14.00 | 0345-5699889 |  |
| 3 | Hafiz Waqar N.Qasid | Flood Season | 14.00 | 24.00 | 0314-7862100 |  |
| 4 | Asjad Mehmood Telephone Attendent | Flood Season | 14.00 | 24.00 | 0333-5845997 |  |

Flood Control Centre will be setup in Canal Colony Jhelum from Ist July 2023 to 15th October 2023, which will remain open round the clock and is well equipped with telephone, wireless sets, fax machines etc. to receive / pass important massages from all flood related quarters and will be responsible for supplying flood information to all concerned as well as public (Telephone numbers 0544-9270330).

7.15	WIRELESS ARRANGEMENT

Wireless Communication Network was established at Jhelum in 2015 with Base Station at following places.

XEN/JLM

S.No.	            Location of station		         	Calling Code

1.		Flood Control Center UJC Circle Jhelum 	Control Canal Tele Office Jhelum.

2.		Mangla Head Works. 		           		Zahid Control.

3.		Jatli Level Crossing 				Jatli

4.		Rajar Rest House.				Zahid –II

5.		Rasul Head Works.				Zahid–III

6.		Khokhra Sub Station at

Khokhra Headworks.  			Khokhra

The following Officers /Officials were provided with the Mobile wireless sets/ handy walky talky set.

SR.No.	   Officer/Official	Calling Code 		       Status

1. 	Executive Engineer Jhelum                  	Amjad JlM            2 Mobile Set+I walky talky

2.	Asst. Executive Engineer Mangla         	Sadiq  Mangla     1 Mobile Set+I walky talky

3.	Asst. Executive Engineer Khokhra		Sadiq Khokhra     	I walky talky

4.	Sub Engineer Headquarter Jhelum      	Sadiq Jhelum.		I walky talky

5.	Sub Engineer Mangla 		     	Sadiq Mangla		I walky talky

6.	Sub Engineer Rajar                                	Sadiq Rajar		I walky talky

However the same wireless Networks have now been abolished and communication will only be made through Mobile Phones / PTCL.

XEN/JLM

CHAPTER-8

DETAIL OF ENCROACHMENT

River Jhelum

- Normal

| Total No. Encroachment | No. of Encroachment removed during last Year | Balance Encroachment | Remarks |
| --- | --- | --- | --- |
| NIL | NIL | NIL | NIL |

- Critical Encroachment

| Total Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- |
| NIL | NIL | NIL | NIL |

XEN/JLM

| CHAPTER NO.9 DUTY ROSTER FLOOD FIGHTING PROGRAM. |
| --- |
| SITE | LENGTH | STAGE-I DISCHARGE | LABOUR REQUIRED | LABOUR FOR WATCHING BE DEPUTED (PER SHIFT) | STAGE-II DISCHARGE | LABOUR REQUIRED | LABOUR FOR WATCHING BE DEPUTED (PER SHIFT) | STAGE-III DISCHARGE | LABOUR REQUIRED | LABOUR FOR WATCHING BE DEPUTED (PER SHIFT) | STAGE-III DISCHARGE | LABOUR REQUIRED | LABOUR FOR WATCHING BE DEPUTED (PER SHIFT) | STAGE-III DISCHARGE | LABOUR REQUIRED | LABOUR FOR WATCHING BE DEPUTED (PER SHIFT) | Remarks |
|  |  |  |  | MATE | BELDAR |  |  | MATE | BELDAR |  |  | MATE | BELDAR |  |  | MATE | BELDAR |  |  | MATE | BELDAR |  |
| Jabba Band | - | 0.75 lac to 1.10 lac cs. | 2 | 1 | 1 | 1.10 lac to 1.50 lac cs. | 3 | 1 | 2 | 1.50 lac to 2.25 lac cs. | 3 | 1 | 2 | 2.25 lac to 6.00 lac cs. | 4 | 1 | 3 | 6.0 lac and above | 7 | 2 | 5 |  |
| UJC RD 27+500 to 41+000 | 13500 |  | 3 | 1 | 2 |  | 3 | 1 | 2 |  | 4 | 1 | 3 |  | 4 | 1 | 3 |  | 7 | 2 | 5 |  |
| JHELUM prptection Works (Stud & Bund) | - |  | 25 | 2 | 23 |  | 25 | 3 | 22 |  | 30 | 3 | 33 |  | 35 | 4 | 31 |  | 50 | 5 | 45 |  |
| Guide Bunds on Left Bank of River Jhelum | - |  | 11 | 1 | 10 |  | 15 | 1 | 14 |  | 4 | 1 | 3 |  | 25 | 2 | 23 |  | 35 | 3 | 32 |  |
| Kahan River (Gurah Ahmed Bund & Naugran Flood bund) | - |  | 6 | 1 | 5 |  | 12 | 1 | 11 |  | 2 | 1 | 1 |  | 22 | 2 | 20 |  | 30 | 3 | 27 |  |
| UJC RD 414+500 to 425+000 | 11000 |  | 2 | - | 2 |  | 4 | = | 3 |  | 2 |  | 2 |  | 6 | 1 | 5 |  | 10 | 1 | 9 |  |

XEN/JLM

CHAPTER-10

EMERGENCY TELEPHONE NUMBERS

| Sr. No. | Name | Designation | Office | Residence / Mobile |
| --- | --- | --- | --- | --- |
| 1 | Muhammad Mohsin Laghari | Minister Irrigation | 042-99212809-10 | 0300-8454445 |
| 2 | Shehryar Sultan | Secretary ,Irrigation Department | 042-99212117 042-99212118 | 042-3573116 |
| 3 | Khurram Amin | Additional Secretary (Tech) | 042-99212128 | 0301-8466321 |
| 4 | Zafar Ullah Doger | Additional Secretary (OP) | 042-99213612 | 0333-0565258 |
| 5 |  | Deputy Secretary (Admn) | 042-99212126 |  |
| 6 | Hamad Ali | Deputy Secretary (OP) | 042-99212127 | 0321-7613969 |
| 7 | Muhammad Usman | Deputy Secretary (Dev) | 042-99212129 | 0333-4136600 |
| 8 | Hamar Fasheen | Section Office Flood | 042-99212134 | 0306-6201450 |

POTHOHAR IRRIGATION ZONE

| 1. | Naeem Ashraf Ghummen | Chief Engineer, Potohar Zone Islamabad | 051-9255749 | 0321-4117766 |
| --- | --- | --- | --- | --- |
| 2. | Tabraiz Ahmed | Project Director-II Chakwal | 0544-9270332 | 0300-7624714 |
| 3. | Ali Haider | Executive Engineer (OP), Islamabad | 0333-8880654 | 0333-8880654 |
| 4. | Naveed Akber | Executive Engineer, Jhelum Canal Division, Jhelum | 0544-9270331 Fax-9270311 | 0301-6623908 |
| 5. | Riasat Ali Malik | Sub Divisional Officer, Mangla | 0321-7756211 | 0321-7756211 |
| 6. | Zia Ullah Sheikh | Sub Divisional Officer, Khokhra (Rasul) |  | 03127743303 |
| 7. | Muhammad Siddique | Flood Control Centre Irrigation Jhelum | 0544-9270330 | 0345-5699889 |

XEN/JLM

DISTRICT ADMINISTRATION GUJRAT

| 1. | District Administrator Gujrat | 053-9260071-72 | 053-511109 |
| --- | --- | --- | --- |
| 2. | District Coodination Office Gujrat | 053-9260010 | 053-9260011 |
| 3. | District Police Office Gujrat | 053-9260026-30-31 | 053-9260027 |
| 4. | E.D.O (Revenue),Gujrat | 053-9260026 | 053-9260077 |
| 5. | District Officer, (Revenue), Gujrat | 053-9260061 | 053-9260062 |
| 6. | District Flood Control Office Gujrat | 053-9260066 | ------- |
| 7. | D.D.O(Revenue),Gujrat | 053-9260063 | 053-9260064 |
| 8. | D.D.O(Revenue),Gujrat | 053-37532200 | ------- |
| 9. | D.D.O(Revenue),Gujrat | 053-37651812 | 053-614703 |
| 10. | S.D.P.O Sadar Gujrat | 053-9260042 | ------- |
| 11. | D.S.P Karina. | 053-37511950 | ------- |
| 12. | D.S.P Sara-i-Alamgir. | 053-37511950 | ------- |

DISTRICT ADMINISTRATION JHELUM

| 1. | Capt ® Samiullah Farooq | Deputy Commissioner Jhelum | 0544-9270081 | 0544-9270081 |
| --- | --- | --- | --- | --- |
| 2. | Nasir Mehmood Bajwa | District Police Office Jhelum | 0544-9270042 | 0544-9270042 |
| 3. |  | Assistant Deputy Commissioner (General) Jhelum | 0544-9270109 | 0544-9270109 |
| 4. | Muhammad Mubeen | Assistant Commissioner Jhelum | 0544-9070012 | 0544-9070012 |
| 5. | Hamdullah | Assistant Commissioner Dina | 0544-280255 | 0544-280255 |
| 6. | Anwar Ali | Assistant Commissioner Sohawa | 0544-221101 | 0544-221101 |

FLOOD CONTROL CENTRE PUNJAB, LAHORE

| 1. | Flood Warning Centre 46-Jail Road Lahore. | 042-99205157 |  |
| --- | --- | --- | --- |
| 2. | Flood Cell I & P Secretariat Lahore. | 042-99212134 | 042-9212116 |
| 3. | Police Wireless Control, Jail Road Lahore. | 042-99205156 | - |
| 4. | Flood Emergency Board of Revenue | 042-9204408-9 | 042-9204405 |
| 5. | National Flood Forecasting Bureau Lahore. | 042-99200139 |  |
| 6. | Senior Meteorologist. | 042-99200208 | 042-99200144 |
| 7. | Chief Engineer (D&F) Zone Lahore. | 042-35291304 | 042-5900049 |
| 8. | Director Flood D & F Zone Lahore | 042-99231614 0300-4777120 | 042-6653943 |
| 9. | Flood Cell I & P Secretariat Lahore. | 042-99212134 | - |

MILITARY ENGINEER’S TELEPHONE NUMBERS

| 1. | Headquarter Engineer 30-Corps Gujranwala Cantt. | 0553-269/2353 | 055-3830247 |
| --- | --- | --- | --- |
| 2. | 6-Engineer Battalion Sialkot Cantt. | 052-571/5186 | 052-42665118 |
| 3. | Headquarter Engineer 1-Corps Kharian Cantt | 053-59/2364 | 053-9240144 |

XEN/JLM

CHAPTER-11

STANDARD OPERATING PROCEDURE (SOP) FOR BREACHING SECTION.

11.1	HISTORY OF BREACHING SECTION

There is no breaching section in this Division.

11.2	LOCATION, DESIGN, QUALITY AND VARIETY OF THE 	EXPLOSIVE REQUIRED FOR DETONATION

Not applicable.

11.3	ARRANGEMENT OF EXPLOSIVE STORES

Not applicable.

11.4	LIST OF THE SECURITY STAFF ALONGWITH DETAIL OF THEIR 	TRAINING ETC.

Not applicable.

11.5	DETAIL OF MACHENICAL MEANS AS A STANDBY ARRANGEMENT IN CASE OF   DETONATION FAILURE.

Not applicable.

11.6	DUTY ROSTER IN CASE OF CRITICAL SITUATION

Please see Ch-9.

11.7	BREACHING COMMITTEE WITH THEIR ACTION PLAN

Not applicable.

11.8	LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN CASE 	OF 	BREACH

Not applicable.

11.9	ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENT

Not applicable.

11.10	DETAIL OF COORDINATION WITH CIVIL/ ARMY AUTHORITIES

Please see Ch-10.

11.11	PARALLEL COMMUNICATION ARRANGEMENTS

Not applicable.

11.12	INDEX PLAN.

Not applicable.

Project Director						             Executive Engineer

Small Dam Circle-II                          Chief Engineer	     	  	 Jhelum Canal Division

Jhelum		                          Irrigation Photohar Zone	       	 Jhelum

Islamabad

PART-B

CHAPTER-12

VULNERABLE SITES ON FLOOD BUNDS / STRUCTURES

  - APPREHENDED BREACHES IN FLOOD BUNDS / STRUCTURES

RIVER JHELUM

- Jhelum City

- Jhelum Cantonment Bund may breach at RD 1100+2500

RIVER KAHAN

- Naugran flood bund can breach between RD. 11+000 to 18+000.

- Gurha Ahmed Flood Bund on River Kahan can breach from RD.3+000- 3+500.

RIVER CHENAB

- Shadiwal Flood Bund can breach from RD.418+438/L

  - OPERATION OF BREACHING SECTIONS.

NIL

12.3   	BREACHES DUE TO RISE OF FLOOD WATER, DETERIORATION OF FLOOD BUNDS.

No Breaches.

XEN/JLM

CHAPTER-13

CONTINGENCY PLAN 2023

(COMING MONSOON SEASON)

# EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE NO.1: JHELUM CITY FLOOD BUND RD.18+000

# 13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

29-a.

# 13.2	DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.

Jhelum City.

# 13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL. THIS MAY INCLUDE:

Back flow through sewerage system will occur when discharge in River Jhelum increases upto 2 lac Cs. and may inundate Jhelum City. However 8 No. disposal gates have recently been constructed/ Installed beneath the Jhelum City Flood Bund. Back watering will be controlled through these installed Gates.

# 13.3.1	ARRANGEMENTS

# Necessary arrangements have been made to meet with the any emergency during Flood.

# 13.3.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood fighting camp will be established Near Railway Bridge.

# 13.3.3	DUTIES OF OFFICERS/ OFFICIALS AND THEIR CAMP SITES

| Camp No. | Location | Officer Name Designation Mobile # | Official Name Designnation Mobile # |
| --- | --- | --- | --- |
| 1 | Near Railway Bridge. | Malik Riasat Ali Sub Divisional Officer, Mangla 0321-7756211 | Nasir Mansha Sub Engineer H/Q Jhelum 03316869374 |

The Sub Divisional Officer, Mangla will shift his Head Quarter to Jhelum near Railway Bridge and will be responsible for flood fighting / restoration activities. The Sub Engineer Mangla and his establishment will assist the SDO Mangla in flood fighting activities. Mr. Nazir Ahmed Artificer will act as Store keeper.

XEN/JM

13.3.4		DEPARTMENTAL MACHINERY AVAILABLE

1 No tractor trolley is available with this Division.

13.3.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE

Private machinery including tractor trolleys, excavators and dumpers are available near village Thune and Simbly Bridge opposite RD. 153-155 UJC and will be hired as and when required.

# 13.3.6		FLOOD FIGHTING MATERIAL REQUIRED

| S.No. | ITEM | Required Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Torches Chargeable (Medium) | 10 No. | NIL | 10 No. | Balance required material will be managed/ arranged before Flood Season 2023. |
| 2. | New Gunny Bags (4-6 Cft) with Sulti and sewing needles | 100 No. | NIL | 100 No. |  |
| 3. | Axes large | 5 No. | NIL | 5 No. |  |
| 4. | Kassies with Handles | 10 No. | NIL | 10 No. |  |
| 5. | Long Shoes | 6 No. | NIL | 6 No. |  |
| 6. | Rain Coat | 6 No | NIL | 6 No |  |
| 7 | Umbrella | 6 No | NIL | 6 No |  |
| 8. | Jug Glass (1 Jug +6 Glass) | 1 Set. | NIL | 1 No. |  |
| 9. | Shouldari Medium | 1 No. | NIL | 1 No. |  |
| 10. | G.I.Wire | 100 Kg | NIL | 100 Kg |  |
| 11. | Generator set. | 1 No. | NIL | 1 No. |  |
| 12. | Service Cable | 4 Coils | NIL | 4 Coils |  |
| 13. | Search light (Large) | 2 No. | NIL | 2 No. |  |
| 14. | Wooden Mallet | 2 No. | NIL | 2 No. |  |
| 15. | Petrol | 500 Liter | NIL | 500 Liter |  |
| 16. | M. Oil | 10 Liter | NIL | 10 Liter |  |
| 17. | Pitching Stone | 50000 Cft. | NIL | 50000 Cft. |  |
| 18. | Water Cooler (Medium Size) | 2 No | NIL | 2 No. |  |
| 19. | First aid Box | 1 No. | NIL | 1 No. |  |

# 13.3.7		FLOOD FIGHTING MATERIAL AVAILABLE

Flood Fighting Material will be purchased before Flood season, 2023.

# 13.4	DETAIL OF OTHER INFRASTRUCTURES LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORKS, OTHER BUILDINGS, CANAL AND DRAINAGE WORKS.

Electric / Telephone lines installations are there across the River Jhelum besides important Government / public infrastructure in Jhelum City Area.

XEN/JM

- EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE NO.2: JHELUM CANTONMENT BUND RD 1+200

## 13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

31-a.

## 13.2		DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED.

Jhelum Cantt, Bagga, Saeela, Chottala, Khurrd and Sangoi.

## 13.3		STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

Water may spill over across the Jhelum Cantonment and adjoining villages Area when discharge exceeds limits of very high flood in River Jhelum (2.25 lac Cs.). Flood fighting will be done using all the available resources if and when required.

## 13.3.1		ARRANGEMENTS

# Necessary arrangements have been made to meet with the any emergency during Flood.

## 13.3.2		ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood fighting camp will be established at RD 3+500 of flood bund.

## 13.3.3		DUTIES OF OFFICERS/ OFFICIALS AND THEIR CAMP SITES

| Camp No. | Location | Officer Name | Official Name |
| --- | --- | --- | --- |
| 2 | Cantonment Bund RD 1+200. | Malik Riasat Ali Sub Divisional Officer, Mangla 0321-7756211 | Nasir Mansha Sub Engineer H/Q Jhelum 03316869374 |

The Sub Divisional Officer, Mangla will shift his Head Quarter to Jhelum Cantonment and will be responsible for flood fighting / restoration activities. The Sub Engineer Rahmanpur and his establishment will assist the SDO Mangla in flood fighting activities. Mr. Afzal Ahmed beldar will act as Store keeper.

## 13.3.4		DEPARTMENTAL MACHINERY AVAILABLE

1 No tractor trolley is available with this Division.

XEN/JM

## 13.3.5		MACHINERY AVAILABLE FROM  PRIVATE SOURCE

Private machinery including tractor trolleys, excavators and dumpers are available near village Thone and Thone Bridge opposite RD. 153-155 UJC and can be hired as and when required.

## 13.3.6		 FLOOD FIGHTING MATERIAL REQUIRED

| S.No. | ITEM | Required Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Torches Re-Chargeable (Medium) | 10 No. | NIL | 10 No. | Balance required material will be managed/ arranged before Flood Season 2023. |
| 2. | New Gunny Bags (4-6 Cft) with Sulti and sewing needles | 100 No. | NIL | 100 No. |  |
| 3. | Axes large | 5 No. | NIL | 5 No. |  |
| 4. | Kassies with Handles | 10 No. | NIL | 10 No. |  |
| 5 | Long Shoes | 6 No | NIL | 6 No |  |
| 6 | Rain Coat | 6 NO | NIL | 6 No |  |
| 7 | Umbrella | 6 No | Nill | 6 No |  |
| 8 | Jug Glass (1 Jug +6 Glass) | 1 Set. | NIL | 1 No. |  |
| 9 | Shouldari Medium | 1 No. | NIL | 1 No. |  |
| 10 | G.I.Wire | 100 Kg | NIL | 100 Kg |  |
| 11 | Generator set. | 1 No. | NIL | 1 No. |  |
| 12 | Service Cable | 4 Coils | NIL | 4 Coils |  |
| 13 | Search light Flood Light | 2 No. | NIL | 2 No. |  |
| 14. | Wooden Mallet | 2 No. | NIL | 2 No. |  |
| 15. | Petrol for Generator | 500 Liter | NIL | 500 Liter |  |
| 16. | M. Oil | 10 Liter | NIL | 10 Liter |  |
| 17. | Pitching Stone | 50000 Cft. | NIL | 50000 Cft. |  |
| 18. | Water Cooler | 2 No | NIL | 2 No. |  |
| 19. | First aid Box | 1 No. | NIL | 1 No. |  |

## 13.3.7		FLOOD FIGHTING MATERIAL AVAILABLE

Flood Fighting Material will be purchased/Arranged before flood season 2023.

## 13.4	DETAIL OF OTHER INFRASTRUCTURES LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORKS, OTHER BUILDINGS, CANAL AND DRAINAGE WORKS.

Electric / Telephone lines installations are there across the River Jhelum besides important infrastructure like Golf Club, Military dairy farm etc in Jhelum Cantonment Area.

XEN/JM

### EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE NO.3:

### RD 11+000 TO 13+000 NAUGRAN FLOOD BUND

### 13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

33-a.

### 13.2		DETAIL OF VILLAGE ABADIES LIKELY TO BE AFFECTED.

Village Naugran,  Kotla Faqir and CMH Jhelum

13.3		STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

Day & Night watching will be done through Field Establishment especially when discharge exceeds limits of high flood in River Kahan. Back Water effects from River Jhelum may cause threats to Village Abadi of Naugran & Kotla Faqir, thus, Flood fighting will be done using all the available resources if and when required.

### 13.3.1		ARRANGEMENTS

# Necessary arrangements have been made to meet with the any emergency during Flood.

### 13.3.2		ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood fighting camp will be established at RD 11+000 of flood bund.

### 13.3.3		DUTIES OF OFFICERS/ OFFICIALS AND THEIR CAMP SITES

| Camp No. | Location | Officer Name Designation Mobile # | Official Name Designation Mobile # |
| --- | --- | --- | --- |
| 3 | NAUGRAN FLOOD BUND. RD 11+000 to 13+000 | Malik Riasat Ali Sub Divisional Officer, Mangla 0321-7756211 | Nasir Mansha Sub Engineer H/Q Jhelum 03316869374 |

The Sub Divisional Officer, Mangla will shift his Head Quarter to Naugran Flood Bund and will be responsible for flood fighting/ restoration activities. Sub Engineer Jaggu, and his establishment will assist the SDO Mangla in flood fighting activities. Mr. Muhammad Amjad Mate will act as Store keeper.

13.3.4		DEPARTMENTAL MACHINERY AVAILABLE

1 No tractor trolley is available with this Division.

### 13.3.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE

XEN/JM

Private machinery including tractor trolleys, excavators and dumpers are available near village Thon and Simbly Bridge opposite RD. 153-155 UJC and can be hired as and when required.

### 13.3.6		FLOOD FIGHTING MATERIAL REQUIRED

| S.No. | ITEM | Required Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Torches Chargeable (Medium) | 10 No. | NIL | 10 No. | Balance required material will be managed/ arranged before Flood Season 2023. |
| 2. | New Gunny Bags (4-6 Cft) with Sulti and sewing needles | 100 No. | NIL | 100 No. |  |
| 3. | Axes large | 5 No. | NIL | 5 No. |  |
| 4. | Kassies with Handles | 10 No. | NIL | 10 No. |  |
| 5. | Long Shoes | 6 No. | NIL | 6 No. |  |
| 6. | Rain Coat | 6 No. | NIL | 6 No. |  |
| 7 | Umbrella | 6 No. | NIL | 6 No. |  |
| 8 | Jug Glass (1 Jug +6 Glass) | 1 Set. | NIL | 1 No. |  |
| 9 | Shouldari Medium | 1 No. | NIL | 1 No. |  |
| 10 | G.I.Wire | 100 Kg | NIL | 100 Kg |  |
| 11 | Generator set. | 1 No. | NIL | 1 No. |  |
| 12 | Service Cable | 4 Coils | NIL | 4 Coils |  |
| 13 | Search light (Large) | 2 No. | NIL | 2 No. |  |
| 14 | Wooden Mallet | 2 No. | NIL | 2 No. |  |
| 15 | Petrol | 500 Liter | NIL | 500 Liter |  |
| 16 | M. Oil | 10 Liter | NIL | 10 Liter |  |
| 17 | Pitching Stone | 50000 Cft. | NIL | 50000 Cft. |  |
| 18 | Water Cooler (Medium Size) | 2 No | NIL | 2 No. |  |
| 19 | First aid Box | 1 No. | NIL | 1 No. |  |

### 13.3.7		FLOOD FIGHTING MATERIAL AVAILABLE

Flood Fighting Material will be purchased before Flood Season, 2023.

### DETAIL OF OTHER INFRASTRUCTURES LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORKS, OTHER BUILDINGS, CANAL AND DRAINAGE WORKS.

Electric / Telephone lines installations are there besides important infrastructure like CMH and other Army installations.

XEN/JM

#### EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE NO.4: GURHA AHMED  FLOOD BUND RD 3+000 TO 3+500

#### 13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE  BREACH SUPPORTED WITH LEVELS.

35-a.

#### 13.2		DETAIL OF VILLAGE ABADIES LIKELY TO BE AFFECTED.

Village Gurha Ahmed

#### 13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

Day & Night watching will be done through Field Establishment especially when discharge exceeds limits of high flood in River Kahan. Back Water effects from River Jhelum may cause threats to Village Abadi of Gurha Ahmed, thus, Flood fighting will be done using all the available resources if and when required.

#### 13.3.1		ARRANGEMENTS

# Necessary arrangements have been made to meet with the any emergency during Flood.

#### 13.3.2		ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood fighting camp will be established at RD 3+500 of flood bund.

#### 13.3.3		DUTIES OF OFFICERS/ OFFICIALS AND THEIR CAMP SITES

| Camp No. | Location | Officer Name Designation Mobile # | Official Name Designation Mobile # |
| --- | --- | --- | --- |
| 4 | GURHA AHMED FLOOD BUND RD 3+000 TO 3+500 | Malik Riasat Ali Sub Divisional Officer, Mangla 0321-7756211 | Nasir Mansha Sub Engineer H/Q Jhelum 03316869374 |

The Sub Divisional Officer, Khokhra will shift his Head Quarter to Gurha Ahmed Flood Bund and will be responsible for flood fighting / restoration activities. Sub Engineer Pauranwala  and his establishment will assist the SDO Khokhra in flood fighting activities. Mr. Sufian Ahmad will act as Store keeper.

#### 13.3.4		DEPARTMENTAL MACHINERY AVAILABLE

1 No tractor trolley is available with this Division.

XEN/JM

#### 13.3.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE

Private machinery including tractor trolleys, excavators and dumpers are 	available near village Thon and Thon Bridge opposite RD. 153-155 UJC and can be hired as and when required.

#### 13.3.6		FLOOD FIGHTING MATERIAL REQUIRED

| S.No. | ITEM | Required Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Torches Chargeable (Medium) | 10 No. | NIL | 10 No. | Balance required material will be managed/ arranged before Flood Season |
| 2. | New Gunny Bags (4-6 Cft) with Sulti and sewing needles | 100 No. | NIL | 100 No. |  |
| 3. | Axes large | 5 No. | NIL | 5 No. |  |
| 4. | Kassies with Handles | 10 No. | NIL | 10 No. |  |
| 5. | Long Shoes | 6 No | NIL | 6 NO |  |
| 6. | Rain Coat | 6 No | NIL | 6 NO |  |
| 7 | Umbrella | 6 No | NIL | 6 NO |  |
| 8 | Jug Glass (1 Jug +6 Glass) | 1 Set. | NIL | 1 No. |  |
| 9 | Shouldari Medium | 1 No. | NIL | 1 No. |  |
| 10 | G.I.Wire | 100 Kg | NIL | 100 Kg |  |
| 11 | Generator set. | 1 No. | NIL | 1 No. |  |
| 12 | Service Cable | 4 Coils | NIL | 4 Coils |  |
| 13 | Search light (Large) | 2 No. | NIL | 2 No. |  |
| 14 | Wooden Mallet | 2 No. | NIL | 2 No. |  |
| 15 | Petrol | 500 Liter | NIL | 500 Liter |  |
| 16 | M. Oil | 10 Liter | NIL | 10 Liter |  |
| 17 | Pitching Stone | 50000 Cft. | NIL | 50000 Cft. |  |
| 18 | Water Cooler (Medium Size) | 2 No | NIL | 2 No. |  |
| 19 | First aid Box | 1 No. | NIL | 1 No. |  |

#### 13.3.7		 FLOOD FIGHTING MATERIAL AVAILABLE

Flood Fighting Material will be purchased before Flood Season, 2023.

#### 13.4	DETAIL OF OTHER INFRASTRUCTURES LIKE ELECTRIC, SUI   GAS,TELEPHONE INSTALLATIONS, ROAD NETWORKS, OTHER BUILDINGS, CANAL AND DRAINAGE WORKS.

Electric lines and Roads.

XEN/JM

##### EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE NO.5: SHADIWAL FLOOD BUND RD 31+000

##### 13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

36-a.

##### 13.2		DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED.

Village Qasim abad, Jassoki, Sadoki, Tarowal and Golaki.

##### 13.3		STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

Back flow through River Chenab and U/S Head Khanki due to heading of water exceeding River discharge 3 Lac Cs. And also it is effected by flash flooding in Nullah Bhimber joining Upper Jhelum Canal at RD 426.

##### 13.3.1		ARRANGEMENTS

# Necessary arrangements have been made to meet with the any emergency during Flood.

##### 13.3.2		ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood fighting camp will be established at RD 31000 of flood bund.

##### 13.3.3		DUTIES OF OFFICERS/ OFFICIALS AND THEIR CAMP SITES

| Camp No. | Location | Officer Name Designation Mobile # | Official Name Designation Mobile # |
| --- | --- | --- | --- |
| 5 | SHADIWAL FLOOD BUND RD 31+000 | Zia Ullah Sub Divisional Officer, Khokhra 0321-7743303 | Usman Ali Sub Engineer, Pauranwala 0300-7270475 |

The Sub Divisional Officer, Khokhra will shift his Head Quarter to Gurha Ahmed Bund and will be responsible for flood fighting / restoration activities. The Sub Engineer Pauranwala  and his establishment will assist the SDO Khokhra in flood fighting activities. Mr. Shafqat Ullah Gauge Reader will act as Store keeper.

##### 13.3.4		DEPARTMENTAL MACHINERY AVAILABLE

1 No tractor trolley is available with this Division.

XEN/JM

13.3.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE

Private machinery including tractor trolleys, excavators and dumpers are available near village Saroki Bridge opposite RD. 414385/L UJC and can be hired as and when required.

##### 13.3.6		FLOOD FIGHTING MATERIAL REQUIRED

| S.No. | ITEM | Required Quantity | Available Quantity | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Torches Chargeable (Medium) | 10 No. | NIL | 10 No. | Balance required material will be managed/ arranged before Flood Season 2023. |
| 2. | New Gunny Bags (4-6 Cft) with Sulti and sewing needles | 100 No. | NIL | 100 No. |  |
| 3. | Axes large | 5 No. | NIL | 5 No. |  |
| 4. | Kassies with Handles | 10 No. | NIL | 10 No. |  |
| 5. | Long Shoes | 6 No. | NIL | 6 No. |  |
| 6. | Rain Coat | 6 No. | NIL | 6 No. |  |
| 7 | Umbrella | 6 No. | NIL | 6 No. |  |
| 8 | Jug Glass (1 Jug +6 Glass) | 1 Set. | NIL | 1 No. |  |
| 9 | Shouldari Medium | 1 No. | NIL | 1 No. |  |
| 10 | G.I.Wire | 100 Kg | NIL | 100 Kg |  |
| 11 | Generator set. | 1 No. | NIL | 1 No. |  |
| 12 | Service Cable | 4 Coils | NIL | 4 Coils |  |
| 13 | Search light (Large) | 2 No. | NIL | 2 No. |  |
| 14 | Wooden Mallet | 2 No. | NIL | 2 No. |  |
| 15 | Petrol | 500 Liter | NIL | 500 Liter |  |
| 16 | M. Oil | 10 Liter | NIL | 10 Liter |  |
| 17 | Pitching Stone | 50000 Cft. | NIL | 50000 Cft. |  |
| 18 | Water Cooler (Medium Size) | 2 No | NIL | 2 No. |  |
| 19 | First aid Box | 1 No. | NIL | 1 No. |  |

##### 13.3.7		FLOOD FIGHTING MATERIAL AVAILABLE

Flood Fighting Material will be purchased before flood season, 2023.

##### 13.4	DETAIL OF OTHER INFRASTRUCTURES LIKE ELECTRIC, SUI GAS,    TELEPHONE INSTALLATIONS, ROAD NETWORKS, OTHER BUILDINGS, CANAL AND DRAINAGE WORKS.

Electric lines and Roads.

Executive Engineer 		        Chief Engineer 			Project Director		       Jhelum Canal Division	 Irrigation Potohar Zone	            Small Dam Cir	cle-II		     Jhelum				 Rawalpindi/Islamabad                              Jhelum

ACTION PLAN

14.1   RE-SHUFFLING/ RECOUPING PLAN OF RESERVE STONE DEPARTMENTALLY.

Reserve stock of stone will be reshuffled through Govt. contractor in case of emergency.

14.2  	DETAIL OF INLET/ OUTLET CROSSING ALONG WITH CLOSING METHODOLOGY

NIL

14.3  	DEPLOYMENT MACHINERY (MEDIUM TO HIGH FLOOD)

| Sr.# | Name of Structure | Length in Mile | Vulnerable reach | Camp Location | Site incharge by Name & Cell # | Machinery Deployed | Labour Deployed | Availability of Stone Lac Cft |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Beldar + Mate |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Paharwal Guide Wall | 0.46 | 0 | Guide Wall Spur | Muhammad Jabran, Sub Engineer, Cell # 03004574082 | 1 | 0 | 2 | 1 | 1 | 0.20 |
| 2 | Kharka Guide Wall Jhelum | 0.29 | 0 | Guide Wall | Muhammad Jabran, Sub Engineer, Cell # 03004574082 |  |  |  |  | 1 | 0 |
| 3 | Gurah Jattan Guide Wall | 0.42 | 0 | Guide Wall | Muhammad Jabran, Sub Engineer, Cell # 03004574082 |  |  |  |  | 1 | 0 |
| 4 | New Paharwal Guide Wall | 0.396 | 0 | New Paharwal Guide Wall | Muhammad Jabran, Sub Engineer, Cell # 03004574082 |  |  |  |  | 1 | 0 |
| 5 | Khadirala Guide Wall | 0.436 | 0 | Khadirala Guide Wall | Muhammad Jabran, Sub Engineer, Cell # 03004574082 |  |  |  |  | 1 | 0.20 |
| 6 | Shah Madar Guide Wall | 0.369 | 0 | Guide Wall | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 0 | 1 | 1 | 1 | 0 |
| 7 | City Flood Bund | 4 | 0 | Near Railway Bridge | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 0 | 2 | 1 | 4 | 0.005 |
| 8 | Sara-I-Alamgir Flood Bund | 0.36 | 0 | Near Railway Bridge | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 0 | 1 | 1 | 1 | 0.185 |
| 9 | Gurah Ahmed Flood bund | 1.4 | RD 3-4 | RD 3-4 | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 0 | 1 | 1 | 1 | 0.295 |
| 10 | Jhelum Cantt Flood bund | 0.5 | RD 12 | RD 12 | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 0 | 1 | 1 | 1 | 0.036 |
|  | Total | 8.631 |  |  |  | 6 | 0 | 8 | 6 | 13 | 0.623 |

Payment for Machinery & work charge Employment subject to verification by TPM/Consultants.

Executive Engineer

Jhelum Canal Division

Jhelum

14.4   DEPLOYMENT MACHINERY (HIGH TO VERY HIGH FLOOD)

| Sr.# | Name of Structure | Length in Mile | Vulnerable reach | Camp Location | Site incharge by Name & Cell # | Machinery Deployed | Labour Deployed | Availability of Stone Lac Cft |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Beldar + Mate |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Paharwal Guide Wall | 0.46 | 0 | Guide Wall Spur | Usman Ali, Sub Engineer, Cell # 03007270475 | 2 | 1 | 6 | 2 | 3 | 0.20 |
| 2 | Kharka Guide Wall Jhelum | 0.29 | 0 | Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 3 | 0 |
| 3 | Gurah Jattan Guide Wall | 0.42 | 0 | Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 3 | 0 |
| 4 | New Paharwal Guide Wall | 0.396 | 0 | New Paharwal Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 3 | 0 |
| 5 | Khadirala Guide Wall | 0.436 | 0 | Khadirala Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 3 | 0.20 |
| 6 | Shah Madar Guide Wall | 0.369 | 0 | Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 | 1 | - | 2 | 1 | 3 | 0 |
| 7 | Gurah Ahmed Flood bund | 1.4 | RD 3-4 | RD 3-4 | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | - | 2 | 1 | 3 | 0.005 |
| 8 | City Flood Bund | 4 | 0 | Near Railway Bridge | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 2 | 1 | 4 | 1 | 9 | 0.185 |
| 9 | Sara-I-Alamgir Flood Bund | 0.36 | 0 | Near Railway Bridge | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | - | 2 | 1 | 3 | 0.295 |
| 10 | Jhelum Cantt Flood bund | 0.5 | RD 12 | RD 12 | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 1 | 1 | 1 | 3 | 0.036 |
|  | Total | 8.631 |  |  |  | 8 | 3 | 17 | 7 | 36 | 0.623 |

Payment for Machinery & work charge Employment subject to verification by TPM/Consultants.

Executive Engineer

Jhelum  Canal Division

Jhelum

14.5   DEPLOYMENT MACHINERY (VERY HIGH TO EXCEPTIONALLY HIGH FLOOD)

| Sr.# | Name of Structure | Length in Mile | Vulnerable reach | Camp Location | Site incharge by Name & Cell # | Machinery Deployed | Labour Deployed | Availability of Stone Lac Cft |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Trolleys/ Dumpers | Tractor with front blade | Beldar + Mate |  |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Paharwal Guide Wall | 0.46 | 0 | Guide Wall Spur | Usman Ali, Sub Engineer, Cell # 03007270475 | 3 | 1 | 8 | 3 | 4 | 0.20 |
| 2 | Kharka Guide Wall Jhelum | 0.29 | 0 | Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 4 | 0 |
| 3 | Gurah Jattan Guide Wall | 0.42 | 0 | Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 4 | 0 |
| 4 | New Paharwal Guide Wall | 0.396 | 0 | New Paharwal Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 4 | 0 |
| 5 | Khadirala Guide Wall | 0.436 | 0 | Khadirala Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 |  |  |  |  | 4 | 0.20 |
| 6 | Shah Madar Guide Wall | 0.369 | 0 | Guide Wall | Usman Ali, Sub Engineer, Cell # 03007270475 | 1 | 1 | 3 | 1 | 4 | 0 |
| 7 | Gurah Ahmed Flood bund | 1.40 | RD 3-4 | RD 3-4 | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 2 | 1 | 4 | 1 | 4 | 0.005 |
| 8 | City Flood Bund | 4.00 | 0 | Near Railway Bridge | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 3 | 1 | 9 | 2 | 12 | 0.185 |
| 9 | Sara-I-Alamgir Flood Bund | 0.36 | 0 | Near Railway Bridge | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 1 | 2 | 1 | 4 | 0.295 |
| 10 | Jhelum Cantt Flood bund | 0.50 | RD 12 | RD 12 | Nasir Mansha, Sub Engineer, Cell # 03316869374 | 1 | 1 | 3 | 1 | 4 | 0.036 |
|  | Total | 8.631 |  |  |  | 11 | 6 | 29 | 9 | 48 | 0.623 |

Payment for Machinery & work charge Employment subject to verification by TPM/Consultants.

Executive Engineer

Jhelum Canal Division

Jhelum

14.6		DEPLOYMENT PLAN OF POLICE.

| Sr. # | River Reach/ Embankment | Tehsil | Concerned Police Station |
| --- | --- | --- | --- |
| 1 | River Chenab Mangla Dam to G.T Road bridge Right side | Jhelum, Dina | Mangla, Jhelum Civil Line, Jhelum City |
| 2 | River Jhelum , Mangla Dam to G.T Road bridge left side | Mirpur, Bhaimber, Sarai Alamgir | Mangla, Afzalpur, Sarai Alamgir |
| 3 | G.T Road bridge to Rasul H/W right side | Jhelum PD Khan | Jhelum Sadar, Chotala |
| 4 | G.T Road bridge to Rasul H/W left side | Sarai Alamgir, M.B Din | Sarai Alamgir,M.B Din Sadar |
| 5 | Kahan River | Jhelum , Dina | Jhelum Sadar, Dina |
| 6 | Bhnahan Nallah | Jhelum | Chotala |

14.7 DETAIL OF SYNTHIC BAGS WITH CAPACITY OF 50 KG AND 100 KG

| Sr. No. | Items | Required Qty | Available Qty | Remarks |
| --- | --- | --- | --- | --- |
| 1 | Synthetic bags (50 KG Capacity) | 500 No. | Nil |  |
| 2 | Synthetic bags (100 KG Capacity) | 300 No. | Nil |  |

14.8 DETAIL OF POLYTHENE SHEETS OF BLACK COLOR TO PROTECT    U/S SLOPS AGAINST WAVE ACTION AND TO CONTROL SEEPAGE   THROUGH EMBANKMENT.

| Sr. No. | Items | Required Qty. | Available Qty. | Remarks |
| --- | --- | --- | --- | --- |
| 1 | Black Polythene Sheet | 15,000 Sft | Nil | Material will be procured before Flood season 2023 |

Executive Engineer

Jhelum Canal Division

Jhelum

CHAPER-15

BACK UP DIVISIONS (IN CASE OF BREACH)

Jhelum Canal Division, Jhelum and Jhelum Small Dams Division, Jhelum will back-up in case of emergency / Breach.

Executive Engineer

Jhelum Canal Division

Jhelum