GOVERNMENT OF THE PUNJAB

IRRIGATION DEPARTMENT

FLOOD FIGHTING PLAN

FOR THE YEAR 2024

AHMADPUR CANAL DIVISION

Table of Contents

PART – A

CHAPTER-1

SALIENT FEATURE OF AHMADPUR CANAL DIVISION………………............2

1.1 	LOCATION……………………………………………………………………..............2

1.2	GENERAL DESCRIPTION…………...……………………………………………...2

1.3	ADMINISTRATIVE SETUP………………………………………………………….3

CHAPTER-2

FLOOD PROTECTION AND RIVER TRAINING WORKS……………….……….4

2.1	DESIGN PARAMETER OF TRAINING WORKS……………………………4

2.2	LOCATION MAP…………………………………..............................................5

CHAPTER-3

BRIEF HISTORY OF PAST FLOOD EVENTS…………………………....……………6

CHAPTER-4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEADWORKS / BARRAGES AND OR OTHER CONTROL POINTS…………………………………………………………………………………………..

4.1	FLOOD LIMITS………………………………………………………………............7

4.2	TIME LAGS OF FLOODS…........................................................................8

4.3	HIGHEST FLOODS…...................................................................................8

4.4	PEAK DISCHARGES……………………………………………………….............9

CHAPTER-5	FLOOD FIGHTING STRATEGY…………………………………….…….........10

CHAPTER-6	FLOOD DAMAGES RESTORATION WORKS……………………………13

CHAPTER-7	FLOOD FIGHTING WATCHING ARRANGEMENT…………………....14

7.1	PRE-FLOOD ARRANGEMENT……………………………………………......14

7.2	WATCHING ESTABLISHMENT……………………………………………14

7.3	ARRANGEMENT AT SENSITIVE SITES…………………………………14

7.4	WATCHING MATERIAL……………………………………………………….14

7.5	ARRANGEMENT FOR SOUNDING & PROBING………………….22

7.6	LIGHTING ARRANGEMENT……………………………………………….22

7.7	RATION ARRANGEMENT…………………………………………………..22

7.8	POL ARRANGEMENT FOR VEHICLE………………………………..….22

7.9	TRANSPORTATION…………………………………………………..….……22

7.10	LAW AND ORDER……………………………………………………………..22

7.11	MEDICAL ARRANGEMENT FOR LABOUR…………………………..23

7.12	LIAISON WITH OTHER DEPARTMENT……………………………….24

7.13	ROLE OF THE ARMY…………………………………………………………30

7.14	DUTIES OF TELEPHONE ATTENDANT……………………………….31

7.15	WIRELESS ARRANGEMENTS……………………………………………..31

CHAPTER-8

DETAIL OF ENCROACHMENT………………………………………….32

CHAPTER-9

DUTY ROSTER / FLOOD FIGHTING PROGRAM…………….….36

CHAPTER-10

EMERGENCY TELEPHONE NOS……………………………………….39

CHAPTER-11

STANDARD OPERATING PROCEDURE (SOP) FOR

BREACHING SECTIONS……………………………………….………….40

  - HISTORY OF THE BREACHING SECTION..……………………….40

  - LOCATION, DESIGN, QUANTITY AND VARIETY OF THE

EXPLOSIVE REQUIRED FOR DETONATION. ..……………….....40

  - ARRANGEMENT OF EXPLOSIVES AND SECURITY OF

EXPLOSIVE STORES. ..…………………………….…………….……….40

  - LIST OF THE SECURITY STAFF ALONG WITH DETAIL OF

THEIR TRAINING ETC. ………………………………………………..…….40

  - DETAIL OF MECHANICAL MEANS AS A STANDBY

ARRANGEMENTS IN CASE OF DETONATION FAILURE………40

  - DUTY ROSTER IN CASE OF CRITICAL SITUATION. …………….40

  - BREACHING COMMITTEE WITH THEIR ACTION PLAN. ..…..40

  - LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN

CASE OF BREACH. ……………………………………………………….……40

  - ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENTS……………………………………………………………..40

  - DETAILS OF CO-ORDINATION WITH CIVIL/ARMY AUTHORITIES. ………………………………………………………………….40

  - PARALLEL COMMUNICATION ARRANGEMENTS. …………….40

  - INDEX PLAN. ……………………………………………………………….......40

PART – B

CHAPTER-12

VULNERABLE SITES ON FLOOD BUND / STRUCTURES…….41

12.1	Apprehended breaches in Flood Bunds / Structures………..41

12.2	Operation of Breaching Section……………………………………….41

12.3	Breaches due to rising of Flood water, deterioration                                   of flood bunds etc……………………………………………………………41

CHAPTER-13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE

SITE (SITES) LISTED ABOVE. …………………………….……..……....42

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING

OUT OF THE BREACH SUPPORTED WITH LEVELS AT

RD. 117-120 OF AHMADPUR FLOOD BUND…………………..42

13.2	DETAIL OF VILLAGES ABADIES LIKELY TO

BE AFFECTED AND THIS SHOULD ALSO BE

SHOWN ON THE PLAN…………………………………………………..43

13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED

IN DETAIL. THIS MAY INCLUDE…………………………………….….44

13.3.1	ARRANGEMENTS………………………….……………………………………......44

13.3.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS………………………44

13.3.3	DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP SITES…….44

13.3.4	DEPARTMENTAL MACHINERY AVAILABLE………………………….......44

13.3.5	MACHINERY AVAILABLE FROM PRIVATE SOURCE…………………..44

13.3.6	FLOOD FIGHTING MATERIAL REQUIRED……………………………….…45

13.3.7	FLOOD FIGHTING MATERIAL AVAILABLE……………………………..….47

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE

ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS,

ROAD NETWORK, OTHER BUILDINGS, CANALS

AND DRAINAGE NETWORKS……………………………………………..…....49

CHAPTER-14

ACTION PLAN.…………………………….……..…………………………….…......50

14.1	RE-SHUFFLING / RECOUPING PLAN OF RESERVE STOCK OF STONE DEPARTMENTALLY……………………………………………………….………….50

14.2	LIST OF INLETS & OUTLETS CROSSING …………………………….……..50

14.3	DEPLOYMENT MACHINERY (MEDIUM TO HIGH FLOOD)…………...51

14.4	DEPLOYMENT MACHINERY (HIGH TO VERY HIGH FLOOD)………...51

14.5	DEPLOYMENT MACHINERY (VERY HIGH TO EXCEPTIONALLY HIGH

FLOOD)……………………………………………………………………………………….52

14.6	POLICE DEPLOYMENT PLAN ……………………………………………………….52

14.7	DETAILS OF SYNTHETIC BAGS WITH CAPACITY OF 500KG AND

1000KG …………………………..............................................................................52

14.8	DETAILS OF POLYTHENE SHEETS OF BLACK COLOR TO PROTECT

UPSTREAM SLOPE AGAINST WAVE ACTION AND TO CONTROL

SEEPAGE THROUGH EMBANKMENTS …………………..…………….……....52

CHAPTER-15

BACKUP DIVISION (IN CASE OF BREACH.…………………………..…..…....53

PART – A

CHAPTER 1

SALIENT FEATURE OF AHMADPUR CANAL DIVISION

1.1	LOCATION

Sutlej River enters in Pakistan near Ganda Singh Wala and after passing Sulemanki and Islam Head works, it finally approaches to Panjnad Head works. Ahmadpur Flood Bund starts from Lubana Chowk (Tail of Bahawalpur Distributry) near to Bahawalpur Railway Station and ends at RD. 67 of L.M.B of Panjnad Headworks. In the past, banks of Ahmadpur Branch and abandoned railway line together served as flood embankment. Later on the Bund from Railway Station Bahawalpur to RD. 167700 at L.M.B. of Panjnad Headworks (At crossing of Northern Sui Gas pipe line) was approved by worthy Chief Engineer Irrigation Bahawalpur vide his No.6612 dated 
08-03-1979. The specifications / sections were adopted strictly as per Sindh Bund Manual.

1.2	GENERAL DESCRIPTION

Objectives of the Flood Plan are to develop a framework for rescue, relief and rehabilitate activities with a view to:

- Save precious lives and properties.

- Enable those located in vulnerable areas in moving their live stock/ cattle.

- Minimize human misery and sufferings.

- Protect installations of sensitive nature.

- Provide protection against flood spills to Bahawalpur City from its western side.

- Save Sama Satta Railway Junction and valuable Agricultural land and the adjacent population.

- Protect the irrigation network of Ahmedpur Branch system.

It is important to mention that RD 0-150, Flood Bund protects against the spill of Sutluj River and from RD 150-167 with stand the back water of Chenab River and spill of Sutluj especially when Chenab River is in flood at Panjnad Head works.

CHANNELS OF AHMADPUR CANAL DIVISION

Ahmedpur Canal Division comprises of three Sub Divisions. One Abbasia Canal Sub Division located at Liaquatpur is perennial. The other Two Sub Divisions namely Ahmadpur Canal Sub Division & Kotla Musa Khan Canal Sub Division deriving supplies from Ahmedpur Branch are non perennial. The Abbasia Canal off-takes from Punjnad Head Works having a total authorized discharge of 1394 Cs at its head with a length of 44.91 Canal miles. It irrigates 257215 acres’ land of Tehsil Ahmedpur East (District Bahawalpur) and Tehsil Liaquatpur (District Rahim Yar Khan) Abbasia Canal System Downstream R.D 137+000 consists of perennial, non-perennial and flood supply channels which irrigates vast areas of Cholistan. Total G.C.A / C.C.A of Abbasia Canal is 307510/257328 Acres, which is respectively 88104/82686 Acres on Perennial Channels, 43322/40915 Acres on non perennial Channels and 176084/133727 Acres on Flood Supply Channels.

Ahmedpur Branch off-takes from tail Bahawal Canal (Head Lal Sohanra) having total authorized discharge of 2380 Cs at its head with length of 42.16 Miles.        AP Branch from RD: 0+000-210+800 falls in the jurisdiction of Ahmedpur Canal Division in length of 45.16 Miles. This channel irrigates the vast area of Tehsil Ahmedpur East. Total G.C.A/ C.C.A of A.P. Branch is 353588/325161 Acres for non perennial channels.

1.3	ADMINISTRATIVE SETUP

CHAPTER 2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1	DESIGN PARAMETER OF TRAINING WORKS

There are no flood protection and river training works allied to Ahmadpur Flood Bund.

FLOOD PROTECTION BUND

The detail of different segments of Ahmadpur Flood Bund RD. 0-167 is given below:-

| Sr. No. | Description | RD |
| --- | --- | --- |
|  |  | From | To |
| 1 | Ahmadpur Flood Bund starts from Labana Chowk (Bahawalpur) and connects at RD. 30 of 1R/AP Branch | 0 | 23 |
| 2 | Right Bank of 1R/AP Branch is considered as Flood Bund | 23 | 85 |
| 3 | Ahmadpur Flood Bund Meets with A.P Branch at RD of Ahmadpur Flood Bund. | 85 |
| 4 | RD of Ahmadpur Flood Bund at Tail Ahmadpur Branch. | 100 |
| 5 | RD of Ahmadpur Flood Bund along Ahmadpur Branch. | 85 | 100+210 |
| 6 | RD of Ahmadpur Flood Bund meets with Uch Disty. | 100 |
| 7 | RD of Ahmadpur Flood Bund along with Uch Disty. | 100 | 110 |
| 8 | RD of Ahmadpur Flood Bund where it separate from Uch Disty. | 110 |
| 9 | Low Line reaches of Ahmadpur Flood Bund (Existing Height = 9.62 Ft) | 112 | 120 |
| 10 | RD of Ahmadpur Flood Bund again meets with Uch Disty. | 145 |
| 11 | RD of Ahmadpur Flood Bund along Uch Disty. | 145 | 167 |

Design Data of Ahmadpur Flood Bund is as under:-

1.  Total length.	33.40 Mile

2.  Bank width.				20.0 feet

3.  Free Board.				5.0 ft above H.F.L 1973

4.  Side slope (River side/ Country side).	3:1/2:1

2.2	LOCATION MAP.

Index plan of Ahmadpur Canal Division Ahmadpur East.

CHAPTER 3

BRIEF HISTORY OF PAST FLOOD EVENTS

The highest ever discharges at Panjnad were experienced during 1973, 1988 and 1992 with 7.62, 5.07 and 8.12 Lac Cs respectively. The back water on all the three flood affected the Ahmadpur flood bund up to RD. 150, hence the bund in this reach is in satisfactory condition now and fortunately Uch Disty is also running parallel to this bund. This channel serves the purpose of wetting channels, which keeps the bund saturated and chances of leakage are minimized. But still close vigilance is required when both the rivers are in high flood. Prior to the Construction of Bhakara Dam in India, frequent floods were experienced on the Sutlej River. But after the completion of this Dam, frequency of high and exceptional high flood has been reduced. From the perusal of the histogram its indicated that only 4 times, every high flood had been experienced D/S Islam Headworks and once exceptionally high flood during 1988. During this Flood the spill water approached almost all along this flood bund starting from Bahawalpur bypass. The depths along the flood bund were observed 2.0 ft to 4.0 ft and the spill water could not over top in any reach. It has been experienced in past that up to a discharge of 1.5 Lac Cs. D/S Islam, no spill approached to the Ahmadpur Flood Bund except D/S Jhangra village. During the year 1998, 1999 and 2000 a flood of about 66328 Cs, 12244 Cs and 4866 Cs, respectively was experienced D/S Islam Headworks and no where the flood water touched the flood bund.

CHAPTER 4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEADWORKS / BARRAGES AND OTHER CONTROL POINTS

4.1	FLOOD LIMITS

Gauges and discharge from low, medium and high flood is measured at Head Ganda Singh Wala which is tabulated below:-

| Gauge (ft) | Discharge (Cs) | Gauge (ft) | Discharge (Cs) |
| --- | --- | --- | --- |
| 6.00 | 3000 |  |  |
| 7.00 | 5000 |  |  |
| 8.00 | 10000 |  |  |
| 9.00 | 15000 |  |  |
| 10.00 | 20000 |  |  |
| 11.00 | 26000 |  |  |
| 12.00 | 31000 |  |  |
| 13.00 | 28000 |  |  |
| 14.00 | 45000 |  |  |
| 15.00 | 50000 |  |  |
| 16.00 | 55000 |  |  |
| 17.00 | 60000 |  |  |
| 18.00 | 67000 | 19.50 (Low Flood) | 70000 |
| 19.00 | 72000 | 21.50 (Medium Flood) | 150000 |
| 20.00 |  | 23.50 (High Flood) | 300000 |
|  |  | 25.50 (Very High Flood) | 425000 |
|  |  | 26.00 (Very Very High Flood) | Not Measure |

In order to asses the intensity of floods, designed capacities and flood limits of River Sutlej at Islam and River Chenab at Panjnad Head works are given below:-

| Sr. No. | Name of River | Design Capacity (Lac Cs) | FLOOD LIMITS (Lac Cs ) |
| --- | --- | --- | --- |
|  |  |  | Low | Medium | High | Very High | Very exceptional High |
| 1 | Sutluj /Islam | 3.0 | 0.50 | 0.8 | 1.2 | 1.75 | 2.25 |
| 2 | Chennab/ Panjnad | 7.0 | 1.50 | 2 | 3 | 4.5 | 6 |

4.2	TIME LAGS OF FLOODS

| Sr. No. | Reach | Time lag days | Distance (Canal Miles) |
| --- | --- | --- | --- |
| 1 | Ferozepur – Sulemanki | 2 | 79 |
| 2 | Sulemanki – Islam | 3 | 121 |
| 3 | Islam – Panjnad | 4 | 149 |

  - HIGHEST FLOODS

| Sr. No. | Name of Head Works | Years | Highest Discharge (in Lac Cs) |
| --- | --- | --- | --- |
| 1 | Panjnad Head Work | 1973 | 7.62 |
| 2 | Panjnad Head Work | 1988 | 5.07 |
| 3 | Panjnad Head Work | 1992 | 8.12 |

4.4	PEAK DISCHARGES

Peak discharges measured at different Head works from 2019-2023 are tabulated below:-

| SR. NO. | YEAR | PEAK DISCHARGE OF HEAD WORKS (Cs) |
| --- | --- | --- |
|  |  | SULEMANKI HEAD WORKS | ISLAM HEAD WORKS | PANJNAD HEAD WORKS |
|  |  | Designed Capacity 3.25 Lac Cs | Designed Capacity 3.00 Lac Cs. | Designed Capacity 7.00 Lac Cs. |
| 1 | 2019 | 66459 | 54145 | 87336 |
| 2 | 2020 | 22628 | 8761 | 147296 |
| 3 | 2021 | 15162 | 2457 | 472 62 |
| 4 | 2022 | 21335 | 7580 | 101437 |
| 5 | 2023 | 176003 | 100028 | 109384 |

# CHAPTER 5

FLOOD FIGHTING STRATEGY

In order to ensure timely flood fighting and relief measures / activities Irrigation & Power Department and other agencies as Civil Administration, Police, Army, etc, strictly adhere to their functions delineated in the SOP, which explicitly indicates the roles and responsibilities of each functionary of the concerned Department. However, SOPs / Strategies to be adopted at different flood limits are given blow:-

FROM RD 0+000 TO 96+000 OF AHMADPUR FLOOD BUND.

The bund falls in the jurisdiction of Tehsil Bahawalpur, hence Tehsil Administration Bahawalpur and Military officers at Bahawalpur associate with this Department. The Sub Divisional Officer Ahmedpur will inspect the entire flood bund with T.M.O/Administrator Bahawalpur and Military Officers. Sub Engineers will inspect the flood bund and will ensure to close the ramps and will maintain the weak reaches. As soon as the flood downstream Islam is signaled as 1.0 Lac Cs, Sub Divisional Officer, Ahmedpur will shift his Head Quarter to Sama Satta and will ensure implementation of watching strength as per approved scale. The concerned Sub Engineer will shift his Head Quarters at dangerous reach i.e. Fattu Wali at RD 36+000 of flood bund.

When the discharge downstream Islam increases 1.50 Lac Cs.             Sub Division Officer, Ahmedpur will call Zilladars along with their Patwaries for flood duty. Simultaneously he will reduce the indent of Ahmedpur Branch to 75% and 50% and establishment of channels will be shifted to the flood bund.

Similarly, when the exceptionally high flood received downstream Islam, Executive Engineer Ahmedpur will also shift his Head Quarter on the flood bund. Watching establishment will further be increased by employing work charge establishment.

FROM RD 96+000 TO 167+700 OF AHMEDPUR FLOOD BUND.

This flood bund falls in the jurisdiction of Tehsil Ahmedpur East. Hence T.M.O/Administrator Ahmedpur and Military officers at Ahmedpur (Dera Nawab Cantt) will associate with the Department. The Sub Divisional Officer Kotla Musa Khan will inspect the entire flood bund with T.M.O/Administrator and Military officers. Sub Engineers will inspect the flood bund and will ensure to close the ramps and will maintain the week reaches. As soon as flood downstream Islam starts rising above 1.0 Lac Cs, Sub Divisional Officer Kotla Musa Khan will shift to Noushera Canal Rest House. He will depute his Sub Engineers to remain present opposite village Pippli Rajan and village Ali Wahan.

WHEN FLOOD DOWNSTREAM HEAD ISLAM EXCEEDS 1.5 LAC CS.

Sub Divisional Officer Kotla Musa Khan will himself shift to the above mentioned reaches. He will increase the watching strength as provided in the Duty Roster after getting permission from Executive Engineer Ahmedpur. At this stage, he will call all his Zilladars, Patwaries for flood duty. Sub Engineers will bring their 50% establishment on Flood Bund.

WHEN FLOOD DOWNSTREAM ISLAM INCREASES 2.25 LAC CS

Sub Divisional Officer Abbasia along with his Sub Engineers, Zilladars and Patwaries will also rush to Flood bund. Sub Divisional Officer Kotla Musa Khan at the same time will call his Rest of 50% Establishment. The duties of the Establishment and Officials will be readjusted as per Duty Roster. Sub Divisional Officer, Abbasia will be responsible for the reach124+000 to167+000 and Sub Divisional Officer Kotla Musa Khan will be over all     in charge in addition to his reach from R.D.96+000 to 124+000.

EFFECTIVELY HANDLING OF ANY FLOOD RELATED SITUATION.

On receipt of daily gauges from flood warning center and flood forecasting of metrological department, a comprehensive plan is    chalked-out for flood management in Ahmadpur Canal Division.

Keeping in view lengthy system of Bund along Sutlej River to effectively handle any flood related situation, such flood affected areas will be divided into various suitable sectors. Each sector headed by Sector         In charge along with requisite manpower and other resources to fight flood will be indicated.

The flood fighting area is divided into two Sub Sectors. The Executive Engineer, Ahmadpur will be overall Sector In charge.

SUB SECTOR NO. 1

Sub Divisional Officer, Ahmadpur Canal Sub Division alongwith his staff will look after Ahmadpur Flood Bund from RD. 0+000-96+000.

SUB SECTOR NO. 2

Sub Divisional Officer, Kotla Mousa Khan Sub Division alongwith his staff will look after Ahmadpur Flood Bund from RD. 96+000-106+000.

CHAPTER 6

FLOOD DAMAGES RESTORATION WORKS

The Ahmadpur Flood Bund is situated along the left side of Sutlej River. The said River is not received Flood water from the last 30 years and is just like dead. The river training works are not along the said flood bund, so no damages accorded during the year 2020-2023. There is no reserve stock for the River Training Works on Ahmadpur Flood Bund.

CHAPTER 7

FLOOD FIGHTING WATCHING ARRANGEMENT

7.1	PRE-FLOOD ARRANGEMENT

In emergency, plan has been prepared in which the camps will be shifted at different location as per Sub Sectors. Watching of Ahmadpur Flood Bund round the clock alongwith fighting material and machinery will be provided to avoid any mishap at vulnerable site.

7.2	WATCHING ESTABLISHMENT

Watching Establishment round the clock will be deployed for watching Ahmadpur Flood Bund. However, in the duty roster, detail for watching establishment is provided.

| Sr. No. | Site | Flood Limit |
| --- | --- | --- |
|  |  | Low | Medium | High | Very High | Exceptionally High |
|  |  | Man | Shift | Man | Shift | Man | Shift | Man | Shift | Man | Shift |
| 1 | RD: 0.00 -167000 | 3 | 1 | 16 | 2 | 24 | 3 | 73 | 3 | 153 | 3 |

7.3	ARRANGEMENT AT SENSITIVE SITES

All sensitive sites on Flood Embankments / Structures have been given special attention and all necessary arrangements regarding watching of the structures have been ensured for flood fighting.

7.4	FLOOD FIGHTING MATERIAL

DERA MASTI SECTION OF AHMADPUR CANAL SUB DIVISION

| SR. NO. | FLOOD FIGHTING MATERIAL | UNIT | MATERIAL REQUIRED | MATERIAL AVAILABLE | BALANCE REQUIRED | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No. | 46 | 20 | 26 | The balance material will be purchased before the start of flood 2024 |
| 2 | Wicks | Meter | 69 | 0 | 69 |  |
| 3 | Glass for Lamp | No. | 46 | 20 | 26 |  |
| 4 | K Oil in Tin | Ltr | 364 | 0 | 364 |  |
| 5 | Funnels Plastic | No. | 4 | 0 | 4 |  |
| 6 | Oil Extractor | No. | 4 | 0 | 4 |  |
| 7 | Khaji Mats | No. | 125 | 0 | 125 |  |
| 8 | Wooden Hammers | No. | 12 | 0 | 12 | The balance material will be purchased before the start of flood 2024 |
| 9 | Killas 6'-8' | No. | 232 | 0 | 232 |  |
| 10 | Needles | No. | 4 | 0 | 4 |  |
| 11 | Tents | No. | 1 | 0 | 1 |  |
| 12 | Flood Lights | No. | 1 | 0 | 1 |  |
| 13 | Gunny Bags | Each | 6000 | 47 | 5953 |  |
| 14 | Sutli | Lbs | 60 | 5 | 55 |  |
| 15 | Sewing Needles | Each | 48 | 17 | 32 |  |
| 16 | Baskets | Each | 1200 | 0 | 1200 |  |
| 17 | Khaji Mats 6' X 4' | Each | 120 | 0 | 120 |  |
| 18 | Munj Ban | Kg | 60 | 0 | 60 |  |
| 19 | Tranger | Each | 600 | 0 | 600 |  |
| 20 | Manila Rope | Kg | 300 | 0 | 300 |  |
| 21 | Axes | Each | 36 | 0 | 36 |  |
| 22 | Kasies with Handles | Each | 72 | 19 | 53 |  |
| 23 | Belchas | Each | 120 | 0 | 120 |  |
| 24 | Spare Handles for Kasies/Axes/Belchas etc | Each | 180 | 0 | 180 |  |
| 25 | Peg 4.5' | Each | 300 | 0 | 300 |  |
| 26 | Peg Small 3' | Each | 300 | 0 | 300 |  |
| 27 | Hand Saw | Each | 24 | 0 | 24 |  |
| 28 | Steel Wire Rope 1/8" dia | Each | 2400 | 0 | 2400 |  |
| 29 | Karries (2.5" X 3" X 6') | Each | 120 | 0 | 120 |  |
| 30 | Ballies (4" X 6" X 8') | Each | 120 | 0 | 120 |  |
| 31 | Bambose | Each | 180 | 0 | 180 |  |
| 32 | Wooden Mallets | Each | 24 | 0 | 24 |  |
| 33 | Iron Hammer | Each | 12 | 0 | 12 |  |
| 34 | Tents/Swiss Cottage | Each | 6 | 0 | 6 |  |
| 35 | Hand Pump | Each | 6 | 0 | 6 |  |
| 36 | Peter Pump with accessories | Each | 6 | 0 | 6 |  |
| 37 | Polythene Roll (50 feet length) | Each | 24 | 0 | 24 | The balance material will be purchased before the start of flood 2024 |
| 38 | Torches with cells | Each | 6 | 0 | 6 |  |
| 39 | Emergency lights/Flood light | Each | 24 | 0 | 24 |  |
| 40 | Portable Generator Set | Each | 6 | 0 | 6 |  |
| 41 | Generator 10-20 kv | Each | 6 | 0 | 6 |  |
| 42 | Electric Bulb Holder | Each | 72 | 0 | 72 |  |
| 43 | Electric Boards | Each | 72 | 0 | 72 |  |
| 44 | Electric Bulb 100 watt | Each | 72 | 0 | 72 |  |
| 45 | Electric Cable 7/29 | Rft | 3600 | 0 | 3600 |  |
| 46 | Life Jackets | Each | 36 | 0 | 36 |  |
| 47 | Motor Launch | Each | 6 | 0 | 6 |  |
| 48 | Synthetic Bags with a capacity of 50kg | Each | 500 | 0 | 500 |  |
| 49 | Synthetic Bags with a capacity of 100kg | Each | 0 | 0 | 0 |  |
| 50 | Polythene Roll Black Colour (50 ft Length) | Each | 1 | 0 | 1 |  |

SAMMA SATTA SECTION OF AHMADPUR CANAL SUB DIVISION

| SR. NO. | FLOOD FIGHTING MATERIAL | UNIT | MATERIAL REQUIRED | MATERIAL AVAILABLE | BALANCE REQUIRED | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No. | 137 | 20 | 117 | The balance material will be purchased before the start of flood 2024 |
| 2 | Wicks | Meter | 206 | 0 | 206 |  |
| 3 | Glass for Lamp | No. | 137 | 20 | 117 |  |
| 4 | K Oil in Tin | Ltr | 1092 | 0 | 1092 |  |
| 5 | Funnels Plastic | No. | 14 | 0 | 14 |  |
| 6 | Oil Extractor | No. | 11 | 0 | 11 |  |
| 7 | Khaji Mats | No. | 375 | 0 | 375 |  |
| 8 | Wooden Hammers | No. | 38 | 0 | 38 |  |
| 9 | Killas 6'-8' | No. | 695 | 0 | 695 |  |
| 10 | Needles | No. | 12 | 0 | 12 |  |
| 11 | Tents | No. | 3 | 0 | 3 |  |
| 12 | Flood Lights | No. | 1 | 0 | 1 | The balance material will be purchased before the start of flood 2024 |
| 13 | Gunny Bags | Each | 8000 | 47 | 7953 |  |
| 14 | Sutli | Lbs | 264 | 5 | 259 |  |
| 15 | Sewing Needles | Each | 64 | 17 | 48 |  |
| 16 | Baskets | Each | 1600 | 0 | 1600 |  |
| 17 | Khaji Mats 6' X 4' | Each | 160 | 0 | 160 |  |
| 18 | Munj Ban | Kg | 80 | 0 | 80 |  |
| 19 | Tranger | Each | 800 | 0 | 800 |  |
| 20 | Manila Rope | Kg | 400 | 0 | 400 |  |
| 21 | Axes | Each | 48 | 0 | 48 |  |
| 22 | Kasies with Handles | Each | 96 | 19 | 77 |  |
| 23 | Belchas | Each | 160 | 0 | 160 |  |
| 24 | Spare Handles for Kasies/Axes/Belchas etc | Each | 240 | 0 | 240 |  |
| 25 | Peg 4.5' | Each | 400 | 0 | 400 |  |
| 26 | Peg Small 3' | Each | 400 | 0 | 400 |  |
| 27 | Hand Saw | Each | 32 | 0 | 32 |  |
| 28 | Steel Wire Rope 1/8" dia | Rft | 3200 | 0 | 3200 |  |
| 29 | Karries (2.5" X 3" X 6') | Each | 160 | 0 | 160 |  |
| 30 | Ballies (4" X 6" X 8') | Each | 160 | 0 | 160 |  |
| 31 | Bambose | Each | 240 | 0 | 240 |  |
| 32 | Wooden Mallets | Each | 32 | 0 | 32 |  |
| 33 | Iron Hammer | Each | 16 | 0 | 16 |  |
| 34 | Tents/Swiss Cottage | Each | 8 | 0 | 8 |  |
| 35 | Hand Pump | Each | 8 | 0 | 8 |  |
| 36 | Peter Pump with accessories | Each | 8 | 0 | 8 |  |
| 37 | Polythene Roll (50 feet length) | Rft | 32 | 0 | 32 |  |
| 38 | Torches with cells | Each | 32 | 0 | 32 |  |
| 39 | Emergency lights/Flood light | Each | 32 | 0 | 32 |  |
| 40 | Portable Generator Set | Each | 8 | 0 | 8 |  |
| 41 | Generator 10-20 kv | Each | 8 | 0 | 8 | The balance material will be purchased before the start of flood 2024 |
| 42 | Electric Bulb Holder | Each | 96 | 0 | 96 |  |
| 43 | Electric Boards | Each | 96 | 0 | 96 |  |
| 44 | Electric Bulb 100 watt | Each | 96 | 0 | 96 |  |
| 45 | Electric Cable 7/29 | Rft | 4800 | 0 | 4800 |  |
| 46 | Life Jackets | Each | 48 | 0 | 48 |  |
| 47 | Motor Lanch | Each | 8 | 0 | 8 |  |
| 48 | Synthetic Bags with a capacity of 50kg | Each | 500 | 0 | 500 |  |
| 49 | Synthetic Bags with a capacity of 100kg | Each | 0 | 0 | 0 |  |
| 50 | Polythene Roll Black Colour (50 ft Length) | Each | 1 | 0 | 1 |  |

NOUSHEHRA SECTION OF KOTLA MOUSA KHAN CANAL SUB DIVISION

| SR. NO. | FLOOD FIGHTING MATERIAL | UNIT | MATERIAL REQUIRED | MATERIAL AVAILABLE | BALANCE REQUIRED | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No. | 90 | 20 | 70 | The balance material will be purchased before the start of flood 2024 |
| 2 | Wicks | Meter | 150 | 0 | 150 |  |
| 3 | Glass for Lamp | No. | 100 | 3 | 98 |  |
| 4 | K Oil in Tin | Ltr | 800 | 0 | 800 |  |
| 5 | Funnels Plastic | No. | 100 | 1 | 99 |  |
| 6 | Oil Extractor | No. | 22 | 1 | 21 |  |
| 7 | Khaji Mats | No. | 300 | 0 | 300 |  |
| 8 | Wooden Hammers | No. | 10 | 0 | 10 |  |
| 9 | Killas 6'-8' | No. | 600 | 0 | 600 |  |
| 10 | Needles | No. | 60 | 3 | 57 |  |
| 11 | Tents | No. | 3 | 0 | 3 |  |
| 12 | Flood Lights | No. | 2 | 0 | 2 |  |
| 13 | Gunny Bags | Each | 8000 | 94 | 7906 |  |
| 14 | Sutli | Lbs | 184 | 10 | 174 |  |
| 15 | Sewing Needles | Each | 64 | 33 | 31 |  |
| 16 | Baskets | Each | 1600 | 0 | 1600 | The balance material will be purchased before the start of flood 2024 |
| 17 | Khaji Mats 6' X 4' | Each | 160 | 0 | 160 |  |
| 18 | Munj Ban | Kg | 80 | 0 | 80 |  |
| 19 | Tranger | Each | 800 | 0 | 800 |  |
| 20 | Manila Rope | Kg | 400 | 0 | 400 |  |
| 21 | Axes | Each | 48 | 0 | 48 |  |
| 22 | Kasies with Handles | Each | 240 | 38 | 202 |  |
| 23 | Belchas | Each | 160 | 0 | 160 |  |
| 24 | Spare Handles for Kasies/Axes/Belchas etc | Each | 240 | 0 | 240 |  |
| 25 | Peg 4.5' | Each | 400 | 0 | 400 |  |
| 26 | Peg Small 3' | Each | 400 | 0 | 400 |  |
| 27 | Hand Saw | Each | 32 | 0 | 32 |  |
| 28 | Steel Wire Rope 1/8" dia | Rft | 3200 | 0 | 3200 |  |
| 29 | Karries (2.5" X 3" X 6') | Each | 160 | 0 | 160 |  |
| 30 | Ballies (4" X 6" X 8') | Each | 160 | 0 | 160 |  |
| 31 | Bambose | Each | 240 | 0 | 240 |  |
| 32 | Wooden Mallets | Each | 32 | 0 | 32 |  |
| 33 | Iron Hammer | Each | 16 | 0 | 16 |  |
| 34 | Tents/Swiss Cottage | Each | 8 | 0 | 8 |  |
| 35 | Hand Pump | Each | 8 | 0 | 8 |  |
| 36 | Peter Pump with accessories | Each | 8 | 0 | 8 |  |
| 37 | Polythene Roll (50 feet length) | Role | 32 | 0 | 32 |  |
| 38 | Torches with cells | Each | 32 | 0 | 32 |  |
| 39 | Emergency lights/Flood light | Each | 32 | 0 | 32 |  |
| 40 | Portable Generator Set | Each | 8 | 0 | 8 |  |
| 41 | Generator 10-20 kv | Each | 8 | 0 | 8 |  |
| 42 | Electric Bulb Holder | Each | 96 | 0 | 96 |  |
| 43 | Electric Boards | Each | 96 | 0 | 96 |  |
| 44 | Electric Bulb 100 watt | Each | 96 | 0 | 96 | The balance material will be purchased before the start of flood 2024 |
| 45 | Electric Cable 7/29 | Rft | 4800 | 0 | 4800 |  |
| 46 | Life Jackets | Each | 48 | 0 | 48 |  |
| 47 | Motor Lanch | Each | 8 | 0 | 8 |  |
| 48 | Synthetic Bags with a capacity of 50kg | Each | 500 | 0 | 500 |  |
| 49 | Synthetic Bags with a capacity of 100kg | Each | 0 | 0 | 0 |  |
| 50 | Polythene Roll Black Colour (50 ft Length) | Each | 1 | 0 | 1 |  |

KHAIRPUR DAHA SECTION OF KOTLA MOUSA KHAN CANAL SUB DIVISION

| SR. NO. | FLOOD FIGHTING MATERIAL | UNIT | MATERIAL REQUIRED | MATERIAL AVAILABLE | BALANCE REQUIRED | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No. | 63 | 20 | 43 | The balance material will be purchased before the start of flood 2024 |
| 2 | Wicks | Meter | 79 | 0 | 79 |  |
| 3 | Glass for Lamp | No. | 53 | 3 | 51 |  |
| 4 | K Oil in Tin | Ltr | 432 | 0 | 432 |  |
| 5 | Funnels Plastic | No. | 69 | 1 | 68 |  |
| 6 | Oil Extractor | No. | 20 | 1 | 19 |  |
| 7 | Khaji Mats | No. | 200 | 0 | 200 |  |
| 8 | Wooden Hammers | No. | 5 | 0 | 5 |  |
| 9 | Killas 6'-8' | No. | 173 | 0 | 173 |  |
| 10 | Needles | No. | 33 | 3 | 30 |  |
| 11 | Tents | No. | 2 | 0 | 2 |  |
| 12 | Flood Lights | No. | 0 | 0 | 0 |  |
| 13 | Gunny Bags | Each | 8000 | 94 | 7906 |  |
| 14 | Sutli | Lbs | 160 | 23 | 137 |  |
| 15 | Sewing Needles | Each | 64 | 6 | 58 |  |
| 16 | Baskets | Each | 1600 | 0 | 1600 |  |
| 17 | Khaji Mats 6' X 4' | Each | 160 | 0 | 160 |  |
| 18 | Munj Ban | Kg | 80 | 0 | 80 |  |
| 19 | Tranger | Each | 800 | 0 | 800 |  |
| 20 | Manila Rope | Kg | 400 | 0 | 400 | The balance material will be purchased before the start of flood 2024 |
| 21 | Axes | Each | 48 | 0 | 48 |  |
| 22 | Kasies with Handles | Each | 160 | 10 | 150 |  |
| 23 | Belchas | Each | 160 | 0 | 160 |  |
| 24 | Spare Handles for Kasies/Axes/Belchas | Each | 240 | 0 | 240 |  |
| 25 | Peg 4.5' | Each | 400 | 0 | 400 |  |
| 26 | Peg Small 3' | Each | 400 | 0 | 400 |  |
| 27 | Hand Saw | Each | 32 | 0 | 32 |  |
| 28 | Steel Wire Rope 1/8" dia | Rft | 3200 | 0 | 3200 |  |
| 29 | Karries (2.5" X 3" X 6') | Each | 160 | 0 | 160 |  |
| 30 | Ballies (4" X 6" X 8') | Each | 160 | 0 | 160 |  |
| 31 | Bambose | Each | 240 | 0 | 240 |  |
| 32 | Wooden Mallets | Each | 32 | 0 | 32 |  |
| 33 | Iron Hammer | Each | 16 | 0 | 16 |  |
| 34 | Tents/Swiss Cottage | Each | 8 | 0 | 8 |  |
| 35 | Hand Pump | Each | 8 | 0 | 8 |  |
| 36 | Peter Pump with accessories | Each | 8 | 0 | 8 |  |
| 37 | Polythene Roll (50 feet length) | Roll | 32 | 0 | 32 |  |
| 38 | Torches with cells | Each | 8 | 2 | 6 |  |
| 39 | Emergency lights/Flood light | Each | 32 | 0 | 32 |  |
| 40 | Portable Generator Set | Each | 8 | 0 | 8 |  |
| 41 | Generator 10-20 kv | Each | 8 | 0 | 8 |  |
| 42 | Electric Bulb Holder | Each | 96 | 0 | 96 |  |
| 43 | Electric Boards | Each | 96 | 0 | 96 |  |
| 44 | Electric Bulb 100 watt | Each | 96 | 0 | 96 |  |
| 45 | Electric Cable 7/29 | Rft | 4800 | 0 | 4800 |  |
| 46 | Life Jackets | Each | 48 | 0 | 48 |  |
| 47 | Motor Lanch | Each | 8 | 0 | 8 | The balance material will be purchased before the start of flood 2024 |
| 48 | Synthetic Bags with a capacity of 50kg | Each | 500 | 0 | 500 |  |
| 49 | Synthetic Bags with a capacity of 100kg | Each | 0 | 0 | 0 |  |
| 50 | Polythene Roll Black Colour (50 ft Length) | Each | 1 | 0 | 1 |  |

7.5	ARRANGEMENT FOR SOUNDING & PROBING

Equipments including Sounding Rods, Leveling Instruments, Arrows etc. are available to perform Sounding and Probing during the flood.

7.6	LIGHTING ARRANGEMENT

Necessary Lighting arrangements have also been made on Ahmadpur Flood Bund for flood fighting.

7.7	RATION ARRANGEMENT

Ration arrangement for the deployed labour is the responsibility of Civil Administration. However, this activity will also be taken into account at all levels during the floods.

7.8	POL ARRANGEMENT FOR VEHICLE

Necessary arrangements to facilitate earth moving machinery including P.O.L will also been ensured by IPD as well as by the Civil Department.

7.9	TRANSPORTATION

Only three Jeeps in Ahmadpur Canal Division are available. Three trucks will have to be requisitioned through District Co-ordination Officer, Bahawalpur for working during the High Floods. 2 Nos. Tractor Trollies and 2 Nos. Pick-ups will be required.

7.10	LAW AND ORDER

1.	District Coordination Officers, Bahawalpur District shall provide adequate police assistance in all sectors /relief centers/flood affected areas, during any flood related emergency, for security purpose and maintenance of law & order:

2.	Will render operational support to assist XEN, SDO and SBEs of 	Panjnad Headworks and shall also ensure maintenance of law and order 	in flood hit areas/relief centers.

3.	Will deploy adequate police force at Panjnad Headworks as well as 	River 	Chenab and Sutlej for evacuation of people / livestock from low lying areas

along the River bed in collaboration with Revenue department as well as

Military Authorities.

4.	Will put all District Police force in state of high alert and instruct them to collect and disseminate any flood related information to higher authorities as well as general public.

5.	Will make alternate arrangements for traffic, in case of suspension of 	normal routes, on account of floods.

6.	Will keep the District Coordination Officer abreast of any flood related 	situation.

7.	Will issue directions for use of public wireless system, for communication 	purposes, during the emergency.

7.11	MEDICAL ARRANGEMENT FOR LABOUR

E.D.O (H) will be expected to perform the following functions inter alia:

1.	Provision of First Aid /Medicare facilities during flood related emergency in District Bahawalpur.

2.	Extensive preventive vaccination/inoculation before, during and after the flood season.

3.	Provision of necessary medicines, antibiotic, drug, O.R.S and anti snake biting and other necessary vaccines, in adequate quantities in addition to necessary First Aid articles.

4.	Planning and organization of Emergency centers and establishment of emergency cells as well as special medical teams, for centralized planning and coordination, during actual emergency and carrying out mass inoculations/vaccination of the affected population, in targeted areas/relief centers.

5.	Provision of clean sanitary conditions in affected areas. Activation of mobile units with medical officer and staff, for provision of medical facilities in remotely located areas.

6.	Mobilization of disaster management unit and provision of essential articles e.g blankets, stoves, tents in the relief centers, upon advice of District Government.

7.12	LIAISON WITH OTHER DEPARTMENT

E.D.O (WORKS & SERVICES) BAHAWALUR.

E.D.O (W&S) will ensure all possible precautionary measures prior to onset of flooding season. He will make arrangements of protection and repair of bridges/roads and necessary infrastructure and will co-ordinate with Irrigation Department in every possible way, in the event of any contingency. He shall be responsible inter alia, for:

1.	Mobilization of all resources of District Works Department including machinery and manpower, in aid and assistance of District Government /Irrigation Department.

2.	Tabulating data of all excavator /trolleys in the District during the flood season required for repair of breach.

3.	Improving breaches/cuts on directions of competent authority, in order to facilitate discharge of water and to prevent larger catastrophes.

4.	Repair and rehabilitation of damaged roads, bridges or essential infrastructure, ensuring swift restoration of communication infrastructure, particularly to be used for relief operations.

XEN PROVINCIAL HIGH WAY DEPARTMENT.

Provincial Highway Department and District officer roads shall muster up all 	resources in aid of District Government in order to ensure that:

1.	Roads are in satisfactory state and normal flow of traffic is maintained before and after flood emergency situation.

2.	Comprehensive survey of damaged roads is conducted and repair works start immediately as soon as flood is over.

3.	Any other operation as the District Government authorities may direct, in aid and assistance of E.D.O (W&S) and XEN Irrigation.

E.D.O (HEALTH).

E.D.O (H) will be expected to perform the following functions inter alia:

1.	Provision of First Aid /Medicare facilities during flood related emergency in District Bahawalpur.

2.	Extensive preventive vaccination/inoculation before, during and after the flood season.

3.	Provision of necessary medicines, antibiotic, drug, O.R.S and anti snake biting and other necessary vaccines, in adequate quantities in addition to necessary first aid articles.

4.	Planning and organization of Emergency centers and establishment of emergency cells as well as special medical teams, for centralized planning and coordination, during actual emergency and carrying out mass inoculations/vaccination of the affected population, in targeted areas/relief centers.

5.	Provision of clean sanitary conditions in affected areas. Activation of mobile units with medical officer and staff, for provision of medical facilities in remotely located areas.

6.	Mobilization of disaster management unit and provision of essential articles e.g. blankets, stoves, tents in the relief centers, upon advice of District Government.

E.D.O (AGRICULTURE)

E.D.O Agriculture is expected to perform following functions inter alia:

1.		He will ensure that sufficient stock of Rabi crop seeds and fertilizers remain available in the District at all times,

2.	The supply of fodder for cattle during emergency is properly managed, by the Agriculture Department.

3.	He will launch a rigorous campaign in the District through loudspeaker announcements, regarding time and points of availability of fodder and wheat bhoosa/hay. Farmers shall be educated as to how they can secure their crops from flood/rain water.

4.	He will ensure that at least three mobiles teams headed by the D.D.O.A.Es Bahawalpur, Ahmadpur East remain available throughout the flood season, for monitoring of flood sectors and provision of assistance in targeted areas.

5.	He will manage the workforce in order to effectively combat any natural climate and render assistance in all Flood Sectors/Relief Camps on need basis.

E.D.O LIVESTOCK

It has been noticed that many people prefer to stay back and protect their livestock even in desperate times, at the peril of their lives. Such a dispensation not only endangers their own lives but also makes it extremely difficult for the rescue teams to be able to extract the marooned in case situation aggravates. In view therefore, D.O Livestock shall be expected to perform the following functions?

1.	A Relief Cell at the District level is established under supervision of District Livestock Officer in his office, which is remained open round the clock.

2.	D.O (Livestock) shall be responsible for vaccination of animals of flood affected areas. For this purpose, banners regarding flood relief activities will be displayed at conspicuous places in all flood relief centers, in order to apprise flood affecters about facilities available for vaccination and treatment of animals.

3.	In case of flood emergency, emergency field units will be activated for necessary measures pertaining to mass vaccination against spread of diseases. For this purpose, D.O (Livestock) shall organize sector wise mobile teams, for the purpose of providing treatment and vaccination. The teams will maintain active presence in flood-affected areas and render all possible assistance to the affected communities.

4.	D.O (Livestock) shall report to emergency centers about the extent of damages to live stock, after flood emergency is over.

E.D.O (EDUCATION)

The E.D.O will be expected to perform the following functions inter alia:

1.	He will make available all school premises along the vulnerable areas for establishment of relief camps, in order to be able to accommodate displaced people. He will detail requisite staff and will ensure that all school buildings remain readily available round the clock, for the purpose of accommodating the displaced people, throughout the entire flooding season.

2.	He will ensure presence of boy scouts and senior class students at relief camps and shall be overall incharge and focal person for this activity.

E.D.O (COMMUNITY DEVELOPMENT)

He will assist in collection of donations in cash/kind of arranging relief activities within and outside the District. He will also motivate local philanthropists/volunteers as well as N.G.Os in integrating their efforts with those of the status apparatus. He will maintain a complete record of volunteers/philanthropists, keen to extend assistance in relief activities and shall also maintain an inventory of all articles collected and distributed in this regard.

DISTRICT FLOOD CONTROLLER

District Food Controller will ensure that:

1.	In case of emergency, sufficient stocks of wheat /sugar remain available in flood affected areas.

2.	will prepare a scheme for opening of temporary ration depots in the areas likely to be affected by flood /rain

3.	Will depute requisite staff with District Flood Relief Officer, during and after flood emergency.

4.	Will arrange for emergency ration packets comprising of necessary available food items.

5.	Will arrange for immediate supply and distribution of food through D.D.O (R) concerned.

6.	Will immediately setup a centralized cell for affective coordination.

XEN WAPDA /MEPCO

WAPDA Officer at Ahmadpur / Bahawalpur will prepare necessary 	contingency plan to ensure that:-

1.		No breakdown in electricity is allowed to happen in flood affected areas.

2.		A Survey of electrical installation is conducted, particularly in flood /rain affected areas and appropriate arrangements are made for uninterrupted supply of electricity.

3.		Uninterrupted electricity is supplied to sector offices, relief camps, as well as important installations.

DIVISIONAL ENGINEER, PTCL

He will ensure uninterrupted communication in the District and shall provide 	telephone lines immediately, in any of the facility set up on urgent basis, 	especially when any requisition is made by Military authorities and assistance of

the civil administration. He will also be responsible for immediate restoration of 	telephonic linkages in case of damage to any PTCL installation, during and after 	flooding season.

INCHARGE RESCUE 1122

Incharge rescue 1122 will maintain close liaison with DFRO and shall promptly 	dispatch his rescue teams, at the call of DFRO, for rescue of marooned people. 	The 1122 service will remain in a state of high alert throughout the flooding 	season and shall be fully equipped with all gadgets as well as first aid 	equipments. Rescue 1122 will provide specialist swimmers, for extracting 	people from flood affected areas.

DISTRICT OFFICER (CIVIL DEFENCE)

1.		The Civil Defense Officer shall in consultation with D.F.R.O, formulate a plan for rescue and relief operation in case of any contingency.

2.		Arrange for training of Civil Defense contingent staff in handling any flood related situation.

3.		Provide adequate number of volunteers for coordination of rescue activities and management of relief centers.

4.		Will provide for motorboat and flood fighting equipment, on emergency basis.

5.		Will setup an emergency cell for coordination amongst all departments, in case there is a high flood warning.

6.		Will make available requisite number of Civil DE fence personnel/volunteers & material/equipment with District Flood relief officer Bahawalpur, for performance of duties during and after flood situation.

7.		Will monitor and train volunteers, for meaningful assistance in flood fighting operations.

8.		Will arrange training workshops for staff of different departments, for meaningful assistance in flood fighting operations.

DISTRICT POLICE OFFICER

1.		Will provide adequate police assistance in all sectors /relief centers/flood affected areas, during any flood related emergency, for security purpose and maintenance of law & order.

2.		Will render operational support to assist D.F.O /D.F.R.O/T.F.R.O/sector officers. In discharge of their duties and maintenance of law order in flood hit areas/relief centers.

3.		Will deploy adequate police force at Ahmadpur as well as River Sutlej for evacuation of people / livestock from low lying areas along the River bed in collaboration with revenue department as well as military authorities.

4.		Put all District Police force in state of high alert and instruct them to collect and disseminate any flood related information to higher authorities as well as general public.

5.		Make alternate arrangements for traffic, in case of suspension of normal routes, on account of floods.

6.		Will keep the District Coordination Officer abreast of any flood related situation.

7.		Will issue directions for use of public wireless system, for communication purposes, during the emergency.

7.13	ROLE OF THE ARMY

Constitution of Islamic Republic of Pakistan enjoins upon the armed forces, to aid and assist the civil administration in times of need. Accordingly, army may be requisitioned in aid of civil administration, as and when necessary, depending upon the nature and gravity of the situation. Headquarter 4-Corps Bahawalpur 35 Div. shall nominate liaison Officers, who shall coordinate with the District Coordination officer and the DFRO Bahawalpur, during times of emergency. The military officers shall be expected to maintain constant liaison with the District Govt. and to provide troops as well as flood fighting equipment/boats, to the District Government. Upon requisition, the District Government shall arrange for accommodation of Army Troops and shall provide all necessary facilities e.g. telephone lines etc. for communication/ operational purposes forward requests through proper channel and secure requisite number of TMO Bahawalpur and Ahmadpur East will be responsible for transportation of boats. In addition to troops from 4-Corps 35 Div, already deputed at Bahawalpur, may also be called to further assist the civil administration, during all rescue, relief and rehabilitation operations.

1.	Will provide adequate police assistance in all sectors /relief centers/flood affected areas, during any flood related emergency, for security purpose and maintenance of law & order.

2.	Will render operational support to assist D.F.O/ D.F.R.O/ T.F.R.O/ sector officers. In discharge of their duties and maintenance of law order in flood hit areas/relief centers.

7.14	DUTIES OF TELEPHONE ATTENDANT

Flood Control Rooms have been established at Tele Offices of Samma Satta, Musafir Khana, Noushehra Jadeed Sections which remain operational during the flood season and Signallers as well as Telephone Attendants remain present round the clock. All flood situation / reports is received hourly from field formation in the control rooms and conveyed to the Divisional Tele Office Ahmadpur East and Main Control Room at Zonal Office Bahawalpur.

| Sr No. | Name of Officer / Officials | Designation | Station | Period |
| --- | --- | --- | --- | --- |
|  |  |  |  | From | To |
| 1 | Muhammad Nawaz | Signallar | Sama Satta | 08:00AM | 08:00PM |
| 2 | Muhammad Arshad | Telephone Attendant | Musafir Khana | 08:00PM | 08:00AM |

7.15	WIRELESS ARRANGEMENTS

Wireless station at Ahmadpur Canal Division is available for communication   which is connected with Flood Warning Center at Lahore and barrages on the river upstream of Panjnad Headworks. Flood warnings are received through this communication. However, Executive Engineer, Ahmadpur Canal Division will be facilitated with wireless mounted on Jeep supplied by the Police Headquarters and District Civil Administration Bahawalpur.

CHAPTER 8

DETAIL OF ENCROACHMENT

Encroachment along Ahmadpur Flood Bund in Dera Masti Section of Ahmadpur Canal Division

| S.No. | NAME & FATHER'S NAME | AREA | R.D:/SIDE | KIND OF ENCROUCHMENT |
| --- | --- | --- | --- | --- |
| 1 | Shahbaz Patwari | 3.0 Marla | 0 - 1 / R | House |
| 2 | Ghulam Hussain S/O Pari | 2.0 Marla | 0 - 1 / R | House |
| 3 | Raiz | 3.0 Marla | 0 - 1 / R | House |
| 4 | Allah Ditta S/O Pari | 2.0 Marla | 0 - 1 / R | House |
| 5 | Khadim Hussain S/O Ghous Bukhsh | 3.0 Marla | 0 - 1 / R | House |
| 6 | Allah Ditta S/O Madari | 3.0 Marla | 0 - 1 / R | House |
| 7 | Ghulam Hussain S/O Hazara | 2.0 Marla | 0 - 1 / R | House |
| 8 | Muhammad Hussain S/O Muhammad Ramzan | 3.0 Marla | 0 - 1 / R | House |
| 9 | Peer Bukhsh S/O Noor Muhammad | 3.0 Marla | 0 - 1 / R | House |
| 10 | Yaqoob S/O Noor Muhammad | 2.0 Marla | 1 - 2 / R | House |
| 11 | Hussaina S/O Noor Muhammad | 3.0 Marla | 1 - 2 / R | House |
| 12 | Ghulam Fareed S/O Bugoo | 3.0 Marla | 1 - 2 / R | House |
| 13 | Pathana S/O Gul Muhammad | 2.0 Marla | 1 - 2 / R | House |
| 14 | Ghulam Fareed S/O Muhammad Ramzan | 3.0 Marla | 1 - 2 / R | House |
| 15 | Fida Hussain S/O Haq Nawaz | 3.0 Marla | 1 - 2 / R | House |
| 16 | Bashir S/O Gul Muhammad | 2.0 Marla | 1 - 2 / R | House |
| 17 | Ghulam Fareed S/O Muhammad Bukhsh | 3.0 Marla | 1 - 2 / R | House |
| 18 | Lal Bukhsh S/O Ahmad Nawaz | 3.0 Marla | 1 - 2 / R | House |
| 19 | Wazir Ahmad S/O Allah Bukhsh | 2.0 Marla | 1 - 2 / R | House |
| 20 | Allah Bukhsh S/O Wahid Bukhsh | 3.0 Marla | 1 - 2 / R | House |
| 21 | Tariq S/O Muhammad Sharif | 3.0 Marla | 1 - 2 / R | House |
| 22 | Manzoor S/O Ghulam Fareed | 2.0 Marla | 1 - 2 / R | Shop |
| 23 | Muhammad Ramzan S/O Wahid Bukhsh | 3.0 Marla | 1 - 2 / R | House |
| 24 | Muhammad Nawaz S/O Wahid Bukhsh | 3.0 Marla | 1 - 2 / R | House |
| 25 | Allah Bukhsh S/O Deewan | 2.0 Marla | 1 - 2 / R | House |
| 26 | Talib Hussain S/O Wahid Bukhsh | 3.0 Marla | 1 - 2 / R | House |
| 27 | Nazir Hassan S/O Wahid Bukhsh | 3.0 Marla | 1 - 2 / R | House |
| 28 | Muhammad Iqbal S/O Wahid Bukhsh | 2.0 Marla | 1 - 2 / R | House |
| 29 | Nazir Ahmad S/O Allah Bukhsh | 3.0 Marla | 2 - 3 / L | House |
| 30 | Muhammad Qasim S/O | 3.0 Marla | 2 - 3 / L | House |
| 31 | Taj Muhammad S/O | 2.0 Marla | 2 - 3 / L | House |
| 32 | Abdul Malik S/O Khan Muhammad | 3.0 Marla | 2 - 3 / L | House |
| 33 | Ghulam Hussain S/O Khan Muhammad | 3.0 Marla | 2 - 3 / L | House |
| 34 | Manzoor S/O Ghulam Fareed | 2.0 Marla | 2 - 3 / L | House |
| 35 | Muhammad Ramzan S/O Khan Muhammad | 3.0 Marla | 2 - 3 / L | House |
| 36 | Muhammad Hassan S/O Khan Muhammad | 3.0 Marla | 2 - 3 / L | House |
| 37 | Muhammad Sadiq S/O Khan Muhammad | 2.0 Marla | 2 - 3 / L | House |
| 38 | Allah Ditta S/O Ghulam Nabi | 3.0 Marla | 2 - 3 / L | House |
| 39 | Amir Bukhsh S/O Allah Ditta | 3.0 Marla | 2 - 3 / L | House |
| 40 | Ghulam Rasul S/O Peeran Ditta | 2.0 Marla | 2 - 3 / L | House |
| 41 | Muhammad Bukhsh S/O Peeran Ditta | 3.0 Marla | 2 - 3 / L | Shop |
| 42 | Ramzan S/O Qadir Bukhsh | 3.0 Marla | 2 - 3 / L | Shop |
| 43 | Ghulam Hussain S/O Peeran Ditta | 2.0 Marla | 2 - 3 / L | House |
| 44 | Khan Muhammad S/O Noor Khan | 3.0 Marla | 2 - 3 / L | House |
| 45 | Atta Muhammad S/O Noor Khan | 3.0 Marla | 3 - 4 / L | House |
| 46 | Karim Bukhsh S/O Pahilwan | 2.0 Marla | 3 - 4 / L | House |
| 47 | Allah Ditta S/O Jam Muhammad | 3.0 Marla | 3 - 4 / L | House |
| 48 | Mukhtiar Hussain S/O Karim Bukhsh | 3.0 Marla | 3 - 4 / L | House |
| 49 | Muhammad Ahmad S/O Bashir Ahmad | 2.0 Marla | 3 - 4 / L | Shop |
| 50 | Muhammad Azam S/O Sindhi | 3.0 Marla | 3 - 4 / L | House |
| 51 | Doctor Muhammad Amjad Quarashi | 3.0 Marla | 3 - 4 / L | Shop |
| 52 | Doctor Abdul Waheed & Doctor Muhammad Yasin | 2.0 Marla | 3 - 4 / L | Shop |
| 53 | Noor Din S/O | 3.0 Marla | 3 - 4 / L | Shop |
| 54 | Doctor Aamir Mahmood Bukhari | 3.0 Marla | 3 - 4 / L | Shop |
| 55 | Haji Asgher S/O | 2.0 Marla | 3 - 4 / L | House |
| 56 | Haji Ahmad | 3.0 Marla | 4 - 5 / R | House |
| 57 | Haji Asgher S/O | 3.0 Marla | 4 - 5 / R | Shop |
| 58 | D.C. Muhajir | 2.0 Marla | 4 - 5 / R | House |
| 59 | Bashir Patwari | 3.0 Marla | 4 - 5 / R | House |
| 60 | Muhammad Asif Adocate S/O | 3.0 Marla | 4 - 5 / R | House |
| 61 | Masjid | 2.0 Marla | 4 - 5 / R | Masjid |
| 62 | Haji Abdul Malik S/O | 3.0 Marla | 4 - 5 / R | Shop |
| 63 | Muhammad Iqbal S/O Sardar Khan. | 3.0 Marla | 5-6 / R | House |
| 64 | Suhail S/o Allah Bukhsh | 2.0 Marla | 5-6 / R | House |
| 65 | Muhammad Sadiq S/O Peer Bukhsh | 3.0 Marla | 5-6 / R | House |
| 66 | Raiz S/O Haji Muhammad Bukhsh | 3.0 Marla | 5-6 / R | House |
| 67 | Billal Ahmad S/O Faiz Bukhsh | 2.0 Marla | 5-6 / R | House |
| 68 | Ahmad Yar S/O Khuda Bukhsh | 3.0 Marla | 5-6 / R | House |
| 69 | Allah Wasaya S/O Ahmad | 3.0 Marla | 5-6 / R | House |
| 70 | Rafiq S/O Ashiq | 2.0 Marla | 5-6 / R | House |
| 71 | Haji Billal S/O Ghulam Sarwar | 3.0 Marla | 5-6 / R | House |
| 72 | Muhammad Yar S/O Ghulam Qadir | 3.0 Marla | 6 - 7 / R | House |
| 73 | Talib Hussain S/O Khalid Hussain | 2.0 Marla | 6 - 7 / R | Shop. |
| 74 | Mushtaq Ahmad S/O Allah Bukhsh | 3.0 Marla | 6 - 7 / R | House |
| 75 | Muhammad Bukhsh S/O Allah Ditta | 3.0 Marla | 6 - 7 / R | House |
| 76 | Ashiq S/O Khadim Hussain | 2.0 Marla | 6 - 7 / R | House |
| 77 | Muhammad Hussaoin S/O Khadim Hussain | 3.0 Marla | 6 - 7 / R | House |
| 78 | Muhammad Sadiq S/O Allah Ditta | 3.0 Marla | 6 - 7 / R | House |
| 79 | Manzoor Ahmad | 2.0 Marla | 6 - 7 / R | House |
| 80 | Zawar Hussain S/O Allah Diwaya | 3.0 Marla | 6 - 7 / R | House |
| 81 | Fayyaz Ahmad S/O Sarwar Khan | 3.0 Marla | 6 - 7 / R | Shop. |
| 82 | Muhammad Ahsan S/O Allah Yar | 2.0 Marla | 6 - 7 / R | Bhana (Cattle Shed) |
| 83 | Muhammad Tariq S/O Allah Wasaya | 3.0 Marla | 6 - 7 / R | House |
| 84 | Manzoor Ahmad S/O Ahmad Yar | 3.0 Marla | 6 - 7 / R | House |
| 85 | Muhammad Aslam S/O Ahmad | 2.0 Marla | 7 - 8 / R | House |
| 86 | Ahmad bukhsh S/O Sarwar | 3.0 Marla | 7 - 8 / R | House |
| 87 | Allah Wasaya S/O Khuda Bukhsh | 3.0 Marla | 7 - 8 / R | House |
| 88 | Soufi Rashid S/O Imam Bukhsh | 2.0 Marla | 7 - 8 / R | House |
| 89 | Malik Shah Muhammad | 3.0 Marla | 8 - 9 / R | House |
| 90 | Allah Rakyia S/O Peer Bukhsh | 3.0 Marla | 8 - 9 / R | House |
| 91 | Ahmad Mian S/O Mian Saeed | 2.0 Marla | 8 - 9 / R | House |
| 92 | Ghulam Nabi S/O Peer Bukhsh | 3.0 Marla | 9 - 10 / R | House |
| 93 | Muhammad Akram S/O Allah Ditta | 3.0 Marla | 9 - 10 / R | House |
| 94 | Muhammad Miraj S/O Shafi Muhammad | 2.0 Marla | 9 - 10 / R | House |
| 95 | Khadim Hussain S/O Peer Bukhsh | 3.0 Marla | 9 - 10 / R | House |
| 96 | Haq Nawaz S/O Peer Bukhsh | 3.0 Marla | 10 - 11 / R | House |
| 97 | Gopi Ram S/O Ashiq Ram | 2.0 Marla | 10 - 11 / R | House |
| 98 | Sono Ram S/O Haji Ram | 3.0 Marla | 10 - 11 / R | House |
| 99 | Malik Hafeez S/O Haji | 3.0 Marla | 10 - 11 / R | House |
| 100 | Haji Faiz Bukhsh S/O Qadir Bukhsh | 2.0 Marla | 10 - 11 / R | House |
| 101 | Muhammad Sultan S/O Muhammad Shafi | 3.0 Marla | 10 - 11 / R | House |
| 102 | Muhammad Rashid S/O Allah Bukhsh | 3.0 Marla | 13 - 14 / R | House |
| 103 | Muhammad Zubair S/O | 2.0 Marla | 13 - 14 / R | House |
| 104 | Ahmad Ali S/O Manzoor Ahmad | 3.0 Marla | 13 - 14 / R | House |
| 105 | Muhammad Yaqoob S/O Ghulam Fareed | 3.0 Marla | 13 - 14 / R | House |
| 106 | Muhammad Yousaf S/O Ghulam Fareed | 2.0 Marla | 13 - 14 / R | House |
| 107 | Muhammad Ibrahim S/O Ghulam Fareed | 3.0 Marla | 13 - 14 / R | House |
| 108 | Muhammad Rafiq S/O Yar Muhammad | 3.0 Marla | 14 - 15 / R | House |
| 109 | Ijaz Ahmad S/O Ghulam Sarwar | 2.0 Marla | 14 - 15 / R | House |
| 110 | Sajad Ahmad S/O Ghulam Sarwar | 3.0 Marla | 14 - 15 / R | House |
| 111 | Noor Muhammad S/O Yar Muhammad | 3.0 Marla | 14 - 15 / R | House |
| 112 | Muhammad Sidique S/O Fahad Ahmad | 2.0 Marla | 14 - 15 / R | House |
| 113 | Muhammad Zafar S/O Allah Rakyia | 3.0 Marla | 14 - 15 / R | House |
| 114 | Maher Mustafa s/O Ahmad Yar | 3.0 Marla | 14 - 15 / R | House |
| 115 | Abdul Hameed S/O Noor Muhammad | 2.0 Marla | 14 - 15 / R | House |
| 116 | Muhammad Billal S/O Muhammad Sidique | 3.0 Marla | 14 - 15 / R | House |
| 117 | Maher Azam S/O Abdul Hassan | 3.0 Marla | 15 - 16 / R | House |
| 118 | Imam Bukhsh S/O Mistri Allah Diwaya | 2.0 Marla | 15 - 16 / R | House |
| 119 | Muhammad S/O Muhammad Nawaz | 3.0 Marla | 15 - 16 / R | House |
| 120 | Allah Bachaya S/O Muhammad Ramzan | 3.0 Marla | 15 - 16 / R | House |
| 121 | Hazoor Bkhsh S/O Yar Muhammad | 2.0 Marla | 15 - 16 / R | House |
| 122 | Muhammad Sidique S/O Noor Muhammad | 3.0 Marla | 15 - 16 / R | House |
| 123 | Yasin S/O Abdulallah Rehman | 3.0 Marla | 15 - 16 / R | House |
| 124 | Atta Muhammad S/O Noor Muhammad | 2.0 Marla | 15 - 16 / R | House |
| 125 | Bashir Ahmad S/O Abdullah Rehman | 3.0 Marla | 15 - 16 / R | House |
| 126 | Ansoo Din Shah S/O Karim Haider Shah | 3.0 Marla | 15 - 16 / R | House |
| 127 | Ghulam Fareed Allah Wasaya | 2.0 Marla | 15 - 16 / R | House |
| 128 | Ghulam Fareed S/O Noor Muhammad | 3.0 Marla | 15 - 16 / R | House |
| 129 | Muhammad Yar S/O Ahmad Yar | 3.0 Marla | 15 - 16 / R | House |
| 130 | Abbas S/O Muhammad Akbar | 2.0 Marla | 15 - 16 / R | House |
| 131 | Muhammad Sadiq S/O Mulla | 3.0 Marla | 15 - 16 / R | House |
| 132 | Noor Muhammad S/O Qadir Bukhsh | 3.0 Marla | 15 - 16 / R | House |
| 133 | Muhammad Azam S/O Ghulam Fareed | 2.0 Marla | 15 - 16 / R | House |
| 134 | Dil shad S/O Abdul Razzaq | 3.0 Marla | 15 - 16 / R | House |
| 135 | Muhammad Arif S/O | 3.0 Marla | 17 - 18 | House |
| 136 | Dactor Liaqat S/O Najeeb | 2.0 Marla | 17 - 18 | House |
| 137 | Adnan Shah S/O Khalid bukhari | 3.0 Marla | 17 - 18 | House |
| 138 | Ghulam Qadir S/O Allah Bachaya | 3.0 Marla | 17 - 18 | House |
| 139 | Bashir Ahmad S/O Ghulam Nabi | 2.0 Marla | 17 - 18 | House |
| 140 | Abdul Hameed S/O Faiz Bukhsh | 3.0 Marla | 17 - 18 | House |
| 141 | Muhammad Ashiq S/O Faiz Bukhsh | 3.0 Marla | 17 - 18 | House |
| 142 | Muhammad Shafi S/O Faiz Bukhsh | 2.0 Marla | 17 - 18 | House |
| 143 | Muhammad Shafi S/O Faiz Bukhsh | 3.0 Marla | 17 - 18 | House |
| 144 | Muhammad Sarwar S/O Faiz Bukhsh | 3.0 Marla | 17 - 18 | House |
| 145 | Muhammad Shakir S/O Allah Wasaya | 2.0 Marla | 17 - 18 | House |
| 146 | Muhammad Rafiq S/O Allah Wasaya | 3.0 Marla | 17 - 18 | House |
| 147 | Nadir S/O Misti Allah Bukhsh | 3.0 Marla | 17 - 18 | House |
| 148 | Nadir S/O Amir Bukhsh | 2.0 Marla | 17 - 18 | House |
| 149 | Allah Yar S/O Qadir Bukhsh | 3.0 Marla | 17 - 18 | House |
| 150 | Faqir Bukhsh S/O Jind Wadda | 3.0 Marla | 17 - 18 | House |
| 151 | Misti Sharif S/O Jind Wadda | 2.0 Marla | 17 - 18 | House |
| 152 | Misti Muhammad Fareed S/O Jind Wadda | 3.0 Marla | 17 - 18 | House |
| 153 | Miraj Ahmad S/O Moulvi Manzoor | 3.0 Marla | 17 - 18 | House |
| 154 | Farooq S/O Khuda Bukhsh | 2.0 Marla | 17 - 18 | House |
| 155 | Shabir S/O Allah Bukhsh | 3.0 Marla | 17 - 18 | House |
| 156 | Haji Abdul Karim S/O Peeran Ditta | 3.0 Marla | 17 - 18 | House |
| 157 | Nazoo S/O Allah Bukhsh | 2.0 Marla | 17 - 18 | House |
| 158 | Amin S/O Muhammad Yar | 3.0 Marla | 17 - 18 | House |
| 159 | Abdul Aziz S/O Rahim Bukhsh | 3.0 Marla | 17 - 18 | House |
| 160 | Muhammad Sidique S/O Abdul Aziz | 2.0 Marla | 17 - 18 | House |
| 161 | Haq Nawaz S/O Qadi Bukhsh | 3.0 Marla | 18 - 19 | House |
| 162 | Abdul Rhman S/O Karim Bukhsh | 3.0 Marla | 18 - 19 | House |
| 163 | Allah Bukhsh S/O Allah Ditta | 2.0 Marla | 18 - 19 | House |
| 164 | Irshad S/O Ghulam Sarwar | 3.0 Marla | 18 - 19 | House |
| 165 | Shams U Din S/O Qadir Bukhsh | 3.0 Marla | 18 - 19 | House |
| 166 | Qadir Bukhsh S/O Rahim Bukhsh | 2.0 Marla | 18 - 19 | House |
| 167 | Muhammad Bukhsh S/O Karim Bukhsh | 3.0 Marla | 18 - 19 | House |
| 168 | Amir Bukhsh S/O jind Wadda | 3.0 Marla | 18 - 19 | House |
| 169 | Ghulam Muhammafd S/O Allah Wasayw | 2.0 Marla | 18 - 19 | House |
| 170 | Rafiq S/O Peeran Ditta | 3.0 Marla | 18 - 19 | House |
| 171 | Mistri Gulzar S/O Haji Ghulam | 3.0 Marla | 18 - 19 | House |
| 172 | Iqbal S/O Haji Ghulam | 2.0 Marla | 18 - 19 | House |
| 173 | Haji Ghulam S/O Ghuda Bukhsh | 3.0 Marla | 21 - 22 | House |
| 174 | Muhammad Hussain S/O Ch oudry Ramzan | 3.0 Marla | 21 - 22 | House |
| 175 | Ghulam Fareed S/O Jind Wadda | 2.0 Marla | 21 - 22 | House |
| 176 | Siraj S/O Manzoor | 3.0 Marla | 21 - 22 | House |
| 177 | Muhammad Yasin S/O Moulvi Riaz | 3.0 Marla | 21 - 22 | House |
| 178 | Mistri Zafar S/O Allah Ditta | 2.0 Marla | 21 - 22 | House |
| 179 | Billal S/O Haji Ghulam | 3.0 Marla | 21 - 22 | House |
| 180 | Allah Yar S/O Qadir Bukhsh | 3.0 Marla | 21 - 22 | House |
| 181 | Abdul Ghafoor S/O Muhammad Bukhsh | 2.0 Marla | 21 - 22 | House |
| 182 | Allah Nawaz S/O Qadir Bukhsh | 3.0 Marla | 21 - 22 | House |
| 183 | Shamas S/O | 3.0 Marla | 21 - 22 | House |

Ordinary encroachment

| Total encroachment | Removed encroachment | Balanced encroachment | Action to be taken |
| --- | --- | --- | --- |
| 183 No. | NIL | 183 No. | Lists have been provided to district administration vide this Office No. 4373-we dated 16-10-2018 for removal of encroachment |

Critical encroachment

| Total encroachment | Removed encroachment | Balanced encroachment | Action to be taken |
| --- | --- | --- | --- |
| NIL | NIL | NIL | NIL |

CHAPTER 9

DUTY ROSTER / FLOOD FIGHTING PROGRAM

In order to affectively handle any flood related situation, the flood fighting activities have been divided in to two operational domains i.e. Maintenance & Repair and Watching round the clock of Ahmadpur Flood Bund. During the emergency each sector is responsible for rehabilitation, appraisal of damages, restoration of services like repair and maintenance of flood bund, plugging of pipes fixed under the bund for cross irrigation purposes, maintaining of ramps, closing of cuts etc. Duty roster of each sector is illustrated below: -

SECTOR – 1 (AHMADPUR)

4.60 Mile		              14.60 Mile

| SUPERVISORY STAFF | -- 23 | 23 -- 48 | 48 -- 72 | 72 -- 96 |
| --- | --- | --- | --- | --- |
| SDO | During Medium Flood | SUB DIVISIONAL CANAL OFFICER AHMADPUR EAST |
|  | During High Flood | SDO AHMADPUR | DCL AHMADPUR |
| SBE | During Low Flood | DERA MASTI SECTION | SAMA SATTA SECTION |
|  | During Medium Flood | DERA MASTI SECTION | RELIVING | SMA SECTION | MFK SECTION |
| ZDRs & PTWs | During Medium & High Flood | ZDR SMA | ZDR MFK | ZDR AHMADPUR |
|  |  | PTW 10 NOS. | PTW 8 NOS. | PTW 10 NOS. | PTW 8 NOS. |
| OFFICIALS OF TEHSIL COUNCIL. | TMO BAHAWALPUR |
| POLICE DEPARTMENT | SHO / ASI / 3 NO. CONSTABLES CONCERNED |
| MATE | (a) During Low Flood 1 Beldar for two mile. | 2 | 7 |
| BELDAR | (b) During Medium Flood at a+ 1/2 stg of that section. | 2+1/2x27 = 15.5 | 7+1/2 x 17 = 15.5 |
| REGULAR | (c) During High Flood a+ full strength. | 2+27 (full strength) = 29 | 7+17 (full strength) = 24 |
| MATE | (a) July to September 5 No. Beldar per mile. | 23 | 73 |
| BELDAR | (b) When water depth varies from 0-3' ft = a+4beldar p/miles. | 2+18 = 20 | 7+58 = 65 |
| SEASONAL | (c) When water depth varies from 3-6' ft = a+8 beldar p/miles. | 2+37 = 39 | 7+117 = 124 |
|  | (d) When water depth exceeds from 6.0' ft = a+10 beldar p/miles. | 2+46 = 48 | 7+146 = 153 |
| Dozzer | 2 NOS. |

SECTOR – 2 (KOTLA MOUSA KHAN)

| SUPERVISORY STAFF | 96 | 110 | 124 | 138 | 152 167 |
| --- | --- | --- | --- | --- | --- |
| SDO | During Medium Flood | SUB DIVISIONAL CANAL OFFICER KOTLA MUSA KHAN |
|  | During High Flood | SDO KOTLA MUSA KHAN | SDO ABBASIA |
| SBE | During Low Flood | NOUSHERA SECTION. | KHAIR PUR DAHA SECTION |
|  | During Medium Flood | BWL SECTION | UCH SECTION | NSR SECTION | KMK SECTION | KPD SECTION |
| ZDRs & PTWs | During Medium & High Flood | ZDR KMK | ZDR BAHAWAL | ZDR HQI |
|  |  | PTW 10 NOS. | PTW 8 NOS. | PTW 10 NOS. | PTW 7 NOS. | PTW 11 NOS. |
| OFFICIALS OF TEHSIL COUNCIL. | TMO BAHAWALPUR |
| POLICE DEPARTMENT | SHO / ASI / 3 NO. CONSTABLES CONCERNED |
| MATE | (a) During Low Flood 1 Beldar for two mile. | 3 | 4 |
| BELDAR | (b) During Medium Flood at a+ 1/2 stg of that section. | 3+1/2x19 = 22.5 | 4+1/2 x 20 = 24 |
| REGULAR | (c) During High Flood a+ full strength. | 3+19 (full strength) = 22 | 4+20 (full strength) = 24 |
| MATE | (a) July to September 5 No. Beldar per mile. | 28 | 43 |
| BELDAR | (b) When water depth varies from 0-3' ft = a+4 beldar p/miles. | 3+22 = 25 | 4+34 = 38 |
| SEASONAL | (c) When water depth varies from 3-6' ft = a+8 beldar p/miles. | 3+45 = 48 | 4+69 = 73 |
|  | (d) When water depth exceeds from 6.0' ft = a+10 beldar p/miles. | 3+56 = 59 | 4+86 = 90 |
| Dozzer | 2 NOS. |

CHAPTER 10

EMERGENCY TELEPHONE NOS.

| Sr. No. | Description | Area Code | Telephone Numbers |
| --- | --- | --- | --- |
|  |  |  | Office | Residence |
| 1. | Secretary I&P Department Lahore. | 042 | 99212117 | 99212118 |
| 2. | Director Flood Lahore | 042 | 99231614 | 6653943 |
| 3. | Chief Engineer Drainage & Flood LHR. | 042 FAX# | 99230731 35862081 | 0345-4422649 |
| 4. | Chief Engineer Bahawalpur. | 062 | 9250333 | 9250334 |
| 5. | Superintending Engineer Bahawalpur | 062 | 9250300 | 9250270 |
| 6. | Executive Engineer Ahmedpur. | 062 | 2272367 | 2272367 |
| 7. | Sub Divisional Officer Ahmedpur | 062 | 2274167 | 2274167 |
| 8. | Sub Divisional Officer Kotla Musa Khan | 062 | 2275367 | 03006720073 |
| 9. | Executive Engineer Panjnad Head Works | 062 | 2552222 | 2552222 |
| 10. | Executive Engineer Bahawalpur. | 062 | 9250271 | 9250271 |
| 11. | Flood Emergency office Bahawalpur. | 062 | 9250265 | 9250268 |
| 12. | Flood Warning cord Lahore. | 042 | 7572091 |  |
| 13. | SP Bahawalpur | 062 | 9250364 |  |
| 14. | A.S.P Ahmedpur. | 062 | 2272704 | 2273704 |
| 15. | D.S.P Bahawalpur (City). | 062 | 9250370 |  |
| 16. | D.S.P Bahawalpur (Sadar) | 062 | 9250366 |  |
| 17. | Military Office 31-Core Bahawalpur. | 062 | 8915632 |  |
| 18. | District Nazim Bahawalpur. | 062 | 9250042 | 9250044 |
| 19. | Tehsil Nazim Bahawalpur. | 062 | 9250196 | 9250198 |
| 20. | Tehsil Nazim Ahmedpur. | 062 | 2271101 |  |
| 21. | Deputy Director Agriculture Bahawalpur. | 062 | 887496 |  |
| 22. | Director Flood Lahore. | 042 | 99231614 | 0300-4080364 |

CHAPTER 11

STANDARD OPERATING PROCEDURE (SOP) FOR BREACHING SECTIONS

  - HISTORY OF THE BREACHING SECTION.

(Not Applicable)

  - LOCATION, DESIGN, QUANTITY AND VARIETY OF THE

EXPLOSIVE REQUIRED FOR DETONATION

ARRANGEMENT OF EXPLOSIVES AND SECURITY OF

EXPLOSIVE STORES. (Not Applicable)

  - LIST OF THE SECURITY STAFF ALONG WITH DETAIL OF

THEIR TRAINING ETC.

(Not Applicable)

  - DETAIL OF MECHANICAL MEANS AS A STANDBY

(Not Applicable)

ARRANGEMENTS IN CASE OF DETONATION FAILURE.

  - DUTY ROSTER IN CASE OF CRITICAL SITUATION.

(Not Applicable)

11.7	BREACHING COMMITTEE WITH THEIR ACTION PLAN. 						(Not Applicable)

  - LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN

CASE OF BREACH.

(Not Applicable)

  - ANNOUNCEMENT AND DETAIL OF EVACUATION

ARRANGEMENTS

(Not Applicable)

  - DETAILS OF CO-ORDINATION WITH CIVIL/ARMY

AUTHORITIES.

(Not Applicable)

  - PARALLEL COMMUNICATION ARRANGEMENTS.

(Not Applicable)

  - INDEX PLAN. NOT RELATED

CHAPTER 12

VULNERABLE SITES ON FLOOD BUND / STRUCTURES

The Ahmadpur Flood Bund is situated along the left side of River Sutlej and the Flood water at low and medium flows in the bed of River Sutlej and it never touched the embankment in the past. The bund in the reach 117-120 becomes under maximum pressure when Sutluj and Chenab Rivers both are simultaneously in very high flood.

12.1	Apprehended breaches in Flood Bunds / Structures

The Ahmadpur Flood Bund is situated along the left flank of River Sutlej. The said river is dead last 20 years. The reach from RD: 117-120 is vulnerable in Ahmadpur Flood Bund as per prevailing situation.

12.2	Operation of Breaching Section

There is no breaching section on Ahmadpur Flood Bund.

12.3	Breaches due to rising of Flood water, deterioration of flood bunds etc

In the high flood during 1988 and 1992, back water of River Chenab upstream Panjnad Headworks slightly touched the toe of the flood embankment at different places.

CHAPTER 13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE (SITES) LISTED ABOVE.

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH 	SUPPORTED WITH LEVELS AT RD. 117-120 OF AHMADPUR FLOOD BUND

13.2	DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD 	ALSO BE SHOWN ON THE PLAN.

LIST OF VILLAGES LIKELY TO BE INUNDATED IN CASE OF BREACHES

The following villages / public property could be affected if breach occurs 			between RD. 117-120 of Ahmadpur Flood Bund.

| Sr. No. | Villages | Houses (Nos.) | Population (Nos.) |
| --- | --- | --- | --- |
|  | Pipli Rajan | 400 | 6000 |
|  | Pul Farooqabad | 300 | 4000 |
|  | Januwala | 800 | 8000 |
|  | Mubarikpur | 950 | 10000 |
| Total:- | 2450 | 28000 |

13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL. THIS MAY INCLUDE

13.3.1		ARRANGEMENTS

Guny bags, Plastic sheets, baskets, Belchas & machinery are available to control the breach / vulnerable site.

13.3.2 	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

Flood Fighting Camps at vulnerable site i.e. RD. 117-120 of Ahmadpur Flood Bund (Pipli Rajan) will be established for watching round the clock.

13.3.3 	DUTIES OF OFFICERS / OFFICIALS AND THEIR CAMP 	SITES

| Sr. No. | Name of camp | Camp Supervisor | Camp Incharge | Overall Incharge |
| --- | --- | --- | --- | --- |
| 1 | RD. 115 | Irfan Babar Sub Engineer Noushehra Section 0300-6855781 | Muhammad Zamran Sub Divisional Officer Ahmadpur Canal Sub Division 0305-8281995 | Farrukh Touseef XEN, Ahmadpur Canal Division 0333-6498054 |
| 2 | RD. 120 | Hafiz M Tariq Sub Engineer Khairpur Daha Section 0300-8321093 |  |  |

13.3.4 	DEPARTMENTAL MACHINERY AVAILABLE

Pick up		=	1 No.

13.3.5 	MACHINERY AVAILABLE FROM PRIVATE SOURCE

Excavator 		=	1 No.

Dumper 		=	1 No.

Tractor Trolly 	=	2 Nos.

Truck 			=	1 No.

Pick Up 		=	2 No.

13.3.6 	FLOOD FIGHTING MATERIAL REQUIRED

Available material is located at khairpur Daha Canal Rest House

| SR. NO. | FLOOD FIGHTING MATERIAL | UNIT | MATERIAL REQUIRED | MATERIAL AVAILABLE | BALANCE REQUIRED | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No. | 63 | 20 | 43 | The balance material will be purchased before the start of flood 2024 |
| 2 | Wicks | Meter | 79 | 0 | 79 |  |
| 3 | Glass for Lamp | No. | 53 | 3 | 51 |  |
| 4 | K Oil in Tin | Ltr | 432 | 0 | 432 |  |
| 5 | Funnels Plastic | No. | 69 | 1 | 68 |  |
| 6 | Oil Extractor | No. | 20 | 1 | 19 |  |
| 7 | Khaji Mats | No. | 200 | 0 | 200 |  |
| 8 | Wooden Hammers | No. | 5 | 0 | 5 |  |
| 9 | Killas 6'-8' | No. | 173 | 0 | 173 |  |
| 10 | Needles | No. | 33 | 3 | 30 |  |
| 11 | Tents | No. | 2 | 0 | 2 |  |
| 12 | Flood Lights | No. | 0 | 0 | 0 |  |
| 13 | Gunny Bags | Each | 8000 | 94 | 7906 |  |
| 14 | Sutli | Lbs | 160 | 23 | 137 |  |
| 15 | Sewing Needles | Each | 64 | 6 | 58 |  |
| 16 | Baskets | Each | 1600 | 0 | 1600 |  |
| 17 | Khaji Mats 6' X 4' | Each | 160 | 0 | 160 |  |
| 18 | Munj Ban | Kg | 80 | 0 | 80 |  |
| 19 | Tranger | Each | 800 | 0 | 800 |  |
| 20 | Manila Rope | Kg | 400 | 0 | 400 |  |
| 21 | Axes | Each | 48 | 0 | 48 |  |
| 22 | Kasies with Handles | Each | 160 | 10 | 150 |  |
| 23 | Belchas | Each | 160 | 0 | 160 |  |
| 24 | Spare Handles for Kasies/Axes/Belchas etc | Each | 240 | 0 | 240 |  |
| 25 | Peg 4.5' | Each | 400 | 0 | 400 | The balance material will be purchased before the start of flood 2024 |
| 26 | Peg Small 3' | Each | 400 | 0 | 400 |  |
| 27 | Hand Saw | Each | 32 | 0 | 32 |  |
| 28 | Steel Wire Rope 1/8" dia | Rft | 3200 | 0 | 3200 |  |
| 29 | Karries (2.5" X 3" X 6') | Each | 160 | 0 | 160 |  |
| 30 | Ballies (4" X 6" X 8') | Each | 160 | 0 | 160 |  |
| 31 | Bambose | Each | 240 | 0 | 240 |  |
| 32 | Wooden Mallets | Each | 32 | 0 | 32 |  |
| 33 | Iron Hammer | Each | 16 | 0 | 16 |  |
| 34 | Tents/Swiss Cottage | Each | 8 | 0 | 8 |  |
| 35 | Hand Pump | Each | 8 | 0 | 8 |  |
| 36 | Peter Pump with accessories | Each | 8 | 0 | 8 |  |
| 37 | Polythene Roll (50 feet length) | Roll | 32 | 0 | 32 |  |
| 38 | Torches with cells | Each | 8 | 2 | 6 |  |
| 39 | Emergency lights/Flood light | Each | 32 | 0 | 32 |  |
| 40 | Portable Generator Set | Each | 8 | 0 | 8 |  |
| 41 | Generator 10-20 kv | Each | 8 | 0 | 8 |  |
| 42 | Electric Bulb Holder | Each | 96 | 0 | 96 |  |
| 43 | Electric Boards | Each | 96 | 0 | 96 |  |
| 44 | Electric Bulb 100 watt | Each | 96 | 0 | 96 |  |
| 45 | Electric Cable 7/29 | Rft | 4800 | 0 | 4800 |  |
| 46 | Life Jackets | Each | 48 | 0 | 48 |  |
| 47 | Motor Lanch | Each | 8 | 0 | 8 |  |

13.3.7       FLOOD FIGHTING MATERIAL AVAILABLE

Available material is located at Naushehra Canal Rest House

| SR. NO. | FLOOD FIGHTING MATERIAL | UNIT | MATERIAL REQUIRED | MATERIAL AVAILABLE | BALANCE REQUIRED | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No. | 63 | 20 | 43 | The balance material will be purchased before the start of flood 2024 |
| 2 | Wicks | Meter | 79 | 0 | 79 |  |
| 3 | Glass for Lamp | No. | 53 | 3 | 51 |  |
| 4 | K Oil in Tin | Ltr | 432 | 0 | 432 |  |
| 5 | Funnels Plastic | No. | 69 | 1 | 68 |  |
| 6 | Oil Extractor | No. | 20 | 1 | 19 |  |
| 7 | Khaji Mats | No. | 200 | 0 | 200 |  |
| 8 | Wooden Hammers | No. | 5 | 0 | 5 |  |
| 9 | Killas 6'-8' | No. | 173 | 0 | 173 |  |
| 10 | Needles | No. | 33 | 3 | 30 |  |
| 11 | Tents | No. | 2 | 0 | 2 |  |
| 12 | Flood Lights | No. | 0 | 0 | 0 |  |
| 13 | Gunny Bags | Each | 8000 | 94 | 7906 |  |
| 14 | Sutli | Lbs | 160 | 23 | 137 |  |
| 15 | Sewing Needles | Each | 64 | 6 | 58 |  |
| 16 | Baskets | Each | 1600 | 0 | 1600 |  |
| 17 | Khaji Mats 6' X 4' | Each | 160 | 0 | 160 |  |
| 18 | Munj Ban | Kg | 80 | 0 | 80 |  |
| 19 | Tranger | Each | 800 | 0 | 800 |  |
| 20 | Manila Rope | Kg | 400 | 0 | 400 |  |
| 21 | Axes | Each | 48 | 0 | 48 |  |
| 22 | Kasies with Handles | Each | 160 | 10 | 150 |  |
| 23 | Belchas | Each | 160 | 0 | 160 |  |
| 24 | Spare Handles for Kasies/Axes/Belchas etc | Each | 240 | 0 | 240 | The balance material will be purchased before the start of flood 2024 |
| 25 | Peg 4.5' | Each | 400 | 0 | 400 |  |
| 26 | Peg Small 3' | Each | 400 | 0 | 400 |  |
| 27 | Hand Saw | Each | 32 | 0 | 32 |  |
| 28 | Steel Wire Rope 1/8" dia | Rft | 3200 | 0 | 3200 |  |
| 29 | Karries (2.5" X 3" X 6') | Each | 160 | 0 | 160 |  |
| 30 | Ballies (4" X 6" X 8') | Each | 160 | 0 | 160 |  |
| 31 | Bambose | Each | 240 | 0 | 240 |  |
| 32 | Wooden Mallets | Each | 32 | 0 | 32 |  |
| 33 | Iron Hammer | Each | 16 | 0 | 16 |  |
| 34 | Tents/Swiss Cottage | Each | 8 | 0 | 8 |  |
| 35 | Hand Pump | Each | 8 | 0 | 8 |  |
| 36 | Peter Pump with accessories | Each | 8 | 0 | 8 |  |
| 37 | Polythene Roll (50 feet length) | Roll | 32 | 0 | 32 |  |
| 38 | Torches with cells | Each | 8 | 2 | 6 |  |
| 39 | Emergency lights/Flood light | Each | 32 | 0 | 32 |  |
| 40 | Portable Generator Set | Each | 8 | 0 | 8 |  |
| 41 | Generator 10-20 kv | Each | 8 | 0 | 8 |  |
| 42 | Electric Bulb Holder | Each | 96 | 0 | 96 |  |
| 43 | Electric Boards | Each | 96 | 0 | 96 |  |
| 44 | Electric Bulb 100 watt | Each | 96 | 0 | 96 |  |
| 45 | Electric Cable 7/29 | Rft | 4800 | 0 | 4800 |  |
| 46 | Life Jackets | Each | 48 | 0 | 48 |  |
| 47 | Motor Lanch | Each | 8 | 0 | 8 |  |

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE 	INSTALLATIONS, 	ROAD NETWORK, OTHER BUILDINGS, CANALS AND 	DRAINAGE NETWORKS.

- ROADS / INFRASTRUCTURES LIKELY TO BE AFFECTED IN CASE OF BREACHES

1.	Uch Disty

2.	Sultan Disty

3.	Bahawal Disty

4.	Pacca Road from Noushehra to Hateji

5.	Pacca Road from Januwala to Mubarikpur

6.	Pacca Road from Noorpur to Uch Sharif

7.	Pacca Road from Ahmadpur to Khairpur Dhaha

8.	Pacca Road from Ahmadpur to Rahimyarkhan (KLP)

- SCHOOLS / COLLEGES / OTHER EDUCATIONAL INSTITUTIONS

1.	Government High School Mubarikpur

2.	Government High School Januwala

3.	Government High School Pipli Rajan

4.	Government Middle School Chowk Bhatta

5.	Government High School Hathaji

- OTHER BUILDING ETC.

- Rural Health Center Pipli Rajan

- Rural Health Center Januwala

- Basic Health Unit Mubarakpur

- Veterinary Hospital Mubarakpur

- Electric Pools 11KVA

- Communication Towers

- Main Sui Gas Pipeline Guddu to Multan

Action Plan

CHAPTER 14

ACTION PLAN

14.1	RE-SHUFFLING / RECOUPING PLAN OF RESERVE STOCK OF STONE DEPARTMENTALLY.

There is no stock of Stone available in this Division.

14.2	LIST OF INLETS & OUTLETS CROSSING

List of Inlets & Outlets Crossing Ahmadpur Flood Bund

14.3	DEPLOYMENT MACHINERY (MEDIUM TO HIGH FLOOD)

| Sr. No. | Name of structures | Length in Mile | Vulnerable reach | Camp location | Site in charge | Excavator | Dozer | Tractor | Availability of stone in lac Cft. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Ahmadpur Flood Bund | 33.40 | 23-43 | Fatuwali at RD:16+000 of Ahmadpur Flood Bund | Sub Engineer Dera Masti Section | 1 | - | - |  |
| 2 |  |  | 84-96 | Kot Dadu Ghaloo | Sub Engineer Sama Satta Section | - | 1 | 1 |  |
| 3 |  |  | 106-125 | Pipli Rajan | Sub Engineer Naushehra Section | 1 | - | 1 |  |
| 4 |  |  | 142-167 | At RD:167+000 of Ahmadpur Flood Bund | Sub Engineer Khair Pur Daha Section | - | 1 | - |  |
| Total | 2 | 2 | 2 |  |

Note:

Payment of Machinery & work charge employees subject to verification by TPM / Consultant

14.4	DEPLOYMENT MACHINERY (HIGH TO VERY HIGH FLOOD)

| Sr. No. | Name of structures | Length in Mile | Vulnerable reach | Camp Location | Site in charge | Excavator | Dozer | Tractor | Availability of stone in lac Cft. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Ahmadpur Flood Bund | 33.40 | 23-43 | Fatuwali at RD:16+000 of Ahmadpur Flood Bund | Sub Engineer Dera Masti Section | 1 | 1 | 1 |  |
| 2 |  |  | 84-96 | Kot Dadu Ghaloo | Sub Engineer Sama Satta Section | 1 | 1 | 1 |  |
| 3 |  |  | 106-125 | Pipli Rajan | Sub Engineer Naushehra Section | 1 | 1 | 1 |  |
| 4 |  |  | 142-167 | At RD:167+000 of Ahmadpur Flood Bund | Sub Engineer Khair Pur Daha Section | 1 | 1 | 1 |  |
| Total | 4 | 4 | 4 |  |

Note:

Payment of Machinery & work charge employees subject to verification by TPM / Consultant.

14.5	DEPLOYMENT MACHINERY (VERY HIGH TO EXCEPTIONALLY HIGH FLOOD)

| Sr. No. | Name of structures | Length in Mile | Vulnerable reach | Camp Location | Site in charge | Excavator | Dozer | Tractor | Availability of stone in lac Cft. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Ahmadpur Flood Bund | 33.40 | 23-43 | Fatuwali at RD:16+000 of Ahmadpur Flood Bund | Sub Engineer Dera Masti Section | 1 | 2 | 2 |  |
| 2 |  |  | 84-96 | Kot Dadu Ghaloo | Sub Engineer Sama Satta Section | - | 1 | 2 |  |
| 3 |  |  | 106-125 | Pipli Rajan | Sub Engineer Naushehra Section | 1 | 1 | 2 |  |
| 4 |  |  | 142-167 | At RD:167+000 of Ahmadpur Flood Bund | Sub Engineer Khair Pur Daha Section | - | 2 | 2 |  |
| Total | 2 | 6 | 8 |  |

Note:

Payment of Machinery & work charge employees subject to verification by TPM / Consultant.

14.6	POLICE DEPLOYMENT PLAN

During high to exceptionally high flood, the police of Sama Satta, Musafir Khana, Naushehra and Dhorkot police stations will be called on.

14.7	DETAILS OF SYNTHETIC BAGS WITH CAPACITY OF 500KG AND 1000KG

| Sr No. | Name of Section | Nos. of Bags 500Kg | Nos. of Bags 1000Kg | Remarks |
| --- | --- | --- | --- | --- |
|  |  | Required | Available | Required | Available |  |
| 1 | Dera Masti | 400 | 400 | 150 | 50 | The balance material will be purchased before the start of flood 2024 |
| 2 | Sama Satta | 400 | 400 | 150 | 65 |  |
| 3 | Naushehra | 400 | 400 | 150 | 60 |  |
| 4 | Khairpur Daha | 400 | 400 | 150 | 45 |  |

14.8	DETAILS OF POLYTHENE SHEETS OF BLACK COLOR TO PROTECT UPSTREAM SLOP AGAINST WAVE ACTION AND TO CONTROL SEEPAGE THROUGH EMBANKMENTS

| Sr No. | Name of Section | 12ft wide | Remarks |
| --- | --- | --- | --- |
|  |  | Required | Available |  |
| 1 | Dera Masti | 1000 ft | - | The balance material will be purchased before the start of flood 2024 |
| 2 | Sama Satta | 1000 ft | - |  |
| 3 | Naushehra | 1000 ft | - |  |
| 4 | Khairpur Daha | 1000 ft | - |  |

CHAPTER 15

BACK UP DIVISION (IN CASE OF ANY BREACH)

In case of any eventuality / breach, Bahawalpur Canal Division will serve as Backup Division of Ahmadpur Canal Division. All establishment of this Division will immediately be deputed on the breach site and Executive Engineer, Bahawalpur Canal Division will be responsible for: -

- Shall share his experience with Executive Engineer, Ahmadpur Canal Division for taking all necessary measures to cope with any emergency.

- Shall arrange location for positioning of requisite machinery / material near the breach site to handle the situation.

- Shall be responsible for stock piling of essential articles to combat any flood related contingency.

- Shall arrange labour for proper maintenance of breach site.

- Shall keep liaison with the High-ups to transmit all instructions to the lower formation.

M. Arhraf Sub Engineer, Baghdad Section of Bahawalpur Canal Division shall be responsible for arranging Ration / meal to all labour / establishment deployed on the breach site on Government expense.

| Executive Engineer, Ahmadpur Canal Division, Ahmadpur East. |
| --- |
| Superintending Engineer, Bahawalpur Canal Circle, Bahawalpur. | Chief Engineer, Irrigation Bahawalpur. |

# Text boxes

JHANGRA