PART-A

CHAPTER-1

SALIENT FEATURE OF THE BHAKKAR CANAL DIVISION BHAKKAR

1.1	LOCATION.

Bhakkar Canal Division is located at District Headquarter of Bhakkar.  Divisional Headquarter is at 80 miles Down Stream of Chashma Barrage along left bank of River Indus. The jurisdiction of Bhakkar Canal Division starts from Tehsil Darya Khan of District Bhakkar 45 miles Down Stream Chashma Barrage along left bank of River Indus and upto Tehsil Karor of District Layyah.

1.2	GENERAL DESCRIPTION.

Bhakkar Canal Division comprises of Three Sub Divisions namely Bhakkar, Notak & River Sub Division. All Sub Divisions are located in Canal Colony at Bhakkar City. Executive Engineer Canal Division Bhakkar is overall incharge of the Division. His primary duty is equitable distribution of canal water and safe running of irrigation channels in addition to proper watch and ward of flood structures built for safety of Bhakkar City. The jurisdiction of Bhakkar Canal Division starts from RD 291+000 Thal Canal Main Line Lower and extends up to RD 448+000 with its off taking distributaries and minors. The length of channels is 330.18 Miles. The gross commanded area of Bhakkar Canal Division is 326955 acres. The area of Thal Canal Main Line lower falling in the jurisdiction of Bhakkar Canal Division is spread over in two Districts as under.

| Name of District | G.C.A (Acres) | C.C.A (Acres) |
| --- | --- | --- |
| Bhakkar | 243530 | 198129 |
| Layyah | 83425 | 68510 |
| Total | 326955 | 266639 |

XEN BKR

1.3	ADMINISTRATIVE SETUP

XEN BKR

CHAPTER-2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1   DESIGN PARAMETERS OF TRAINING WORKS:

| S.No | Name of Flood Structures | Length | Mile | Top width | Side Slope | Free board | Condition |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Feet | River side | Country side | Feet |  |
| 1 | Bhakkar Flood Bund RD 0+000 – 105+000 | 105000 | 21 | 25 | 3:1 | 2:1 | 6 | Satisfactory |
| 2 | J-Head Spur at RD 5+000 . | 3510 | 0.70 | 30 | 3:1 | 2:1 | 6 | Restoration near to completion. |
| 3 | Solid Stone Stud at RD 7+500 | 210 | 0.042 | 15 | 1:1 | 1:1 | 6 | Satisfactory |
| 4 | Solid Stone Stud at RD 8+600 | 75 | 0.015 | 15 | 1:1 | 1:1 | 6 | Satisfactory |
| 5 | Solid Stone Stud at RD 9+140 | 35 | 0.007 | 15 | 1:1 | 1:1 | 6 | Satisfactory |
| 6 | Solid Stone Stud at RD 10+000 | 60 | 0.012 | 20 | 1:1 | 1:1 | 6 | Satisfactory |
| 7 | J-Head spur No.1 RD 14+700 | 4263 | 0.85 | 25 | 3:1 | 2:1 | 6 | Satisfactory |
| 8 | J-Head spur No.2 RD 27+175 | 2843 | 0.57 | 25 | 3:1 | 2:1 | 6 | Satisfactory |
| 9 | J-Head spur No.3 RD 38+550 | 5000 | 1.00 | 25 | 1:1 | 1:1 | 6 | Satisfactory |
| 10 | Hockey stud at RD 43+500 | 1312 | 0.26 | 15 | 3:1 | 2:1 | 6 | Satisfactory |
| 11 | J-Head spur at RD 47+000 | 4000 | 0.80 | 30 | 3:1 | 2:1 | 6 | Satisfactory |
| 12 | J-Head spur at RD 52+800 | 4100 | 0.82 | 30 | 3:1 | 2:1 | 6 | Satisfactory |
| 13 | Inverted hockey stud at RD 56+800 | 206 | 0.041 | 12 | 1:1 | 1:1 | 0 | Satisfactory |
| 14 | Solid stone stud at RD 57+500 | 100 | 0.020 | 15 | 1:1 | 1:1 | 0 | Satisfactory |
| 15 | Solid stone stud at RD 58+050 | 94 | 0.01 | 30 | 3:1 | 2:1 | 0 | Satisfactory |
| 16 | J-Head Spur at RD 58-800 . | 2660 | 0.53 | 30 | 3:1 | 2:1 | 6 | Satisfactory |
| 17 | Concavo Convex Guide wall b/w RD 58-59 | 1450 | 0.29 | 15 | 1:1 | 1:1 | 6 | Satisfactory |
| 18 | Solid stone stud at RD 59+500 | 200 | 0.04 | 12 | 3:1 | 2:1 | 0 | Satisfactory |
| 19 | Solid Stone inverted Hockey Stud at RD 60+250 | 418 | 0.084 | 12 | 3:1 | 2:1 | 0 | Satisfactory |
| 20 | Mole Head spur RD 60+700 | 1060 | 0.21 | 30 | 1:1 | 1:1 | 6 | Satisfactory. |
| 21 | Solid stone stud at RD 62+500 | 75 | 0.039 | 15 | 1:1 | 1:1 | 0 | Satisfactory |
| 22 | Solid stone stud at RD 63+000 | 75 | 0.031 | 15 | 1:1 | 1:1 | 0 | Satisfactory |
| 23 | Inverted Hockey stud at RD 63+700 | 762 | 0.152 | 20 | 3:1 | 1:1 | 0 | Restoration of apron required. |
| 24 | J-Head Spur at RD 70+000 . | 5462 | 1.09 | 30 | 3:1 | 2:1 | 6 | Restoration of apron and river side stone pitching required. |
| 25 | Mole head spur at RD 71+750 | 1525 | 0.30 | 30 | 3:1 | 2:1 | 6 | Satisfactory |
| 26 | Inverted Hockey Stud at RD 73+000 | 826 | 0.165 | 20 | 1:1 | 1:1 | 0 | Under construction |
| 27 | Solid Stone Stud at RD 74+250. | 60 | 0.011 | 20 | 1;1 | 1;1 | 0 | Satisfactory |
| 28 | Solid Stone Stud at RD 74+500. | 60 | 0.011 | 20 | 1;1 | 1;1 | 0 | Satisfactory |
| 29 | Solid Stone Stud at RD 74+800. | 60 | 0.011 | 20 | 1;1 | 1;1 | 0 | Satisfactory |
| 30 | Solid Stone Stud at RD 75+000. | 60 | 0.011 | 20 | 1;1 | 1’1 | 0 | Satisfactory |
| 31 | Hockey Stud at RD 75+800 | 350 | 0.070 | 25 | 3:1 | 2:1 | 6 | Satisfactory |
| 32 | Inverted Hockey Stud at RD 77+100 | 550 | 0.100 | 20 | 1;1 | 1;1 | 0 | Satisfactory |
| 33 | Concavo Convex Guide Wall at RD 105+000 of Bhakkar Flood Bund. | 1000 | 0.20 | 30 | 1:2 | 1:3 | 6 | Satisfactory |
| 34 | Concavo Convex Guide Wall in front of Basti Maharan. | 1000 | 0.20 | 30 | 1:2 | 1:3 | 6 | Satisfactory |
| 35 | Concavo Convex Guide Wall in front of Basti Cheema. | 1000 | 0.20 | 30 | 1:2 | 1:3 | 6 | Satisfactory |
| 36 | Concavo Convex Guide Wall in front of Basti Warah Seeran. | 1000 | 0.20 | 30 | 1:2 | 1:3 | 6 | Satisfactory |

XEN BKR

2.2	LOCATION MAP

(Attached)

CHAPTER-3

BRIEF HISTORY OF PAST FLOOD EVENTS

Bhakkar Flood Bund was constructed from RD 0+000 – 42+000 during the year 1996-97 to protect low lying Katcha agricultural area, abadies, schools, basic health units and other infrastructures. Bhakkar flood bund was further extended from RD 42+000 – 105+000 with allied structures during the year 2006-07 by development Division Mianwali. After completion of the project Bhakkar Flood Bund from 0+000 – 105+000 along with allied structure was handed over to the Bhakkar Canal Division in June 2012. River Indus D/S Chashma Barrage passed exceptionally high flood in 2010 which passed safely from the jurisdiction of Bhakkar Canal Division Bhakkar.

Bhakkar Flood Bund remained under direct hit of aggressive action of River Indus from 2012 -14 due to which a number of flood protection works were executed during last three years. In order to have a permanent remedy to check the continuous river action and a permanent threat to Bhakkar Flood Bund, model study was conducted to determine the suitable interventions and to eradicate the erosive action of river Indus between RD 0+000 – 76+000, following river training works were proposed by model study.

1.	Construction of J-Head Spur at RD 5+000 of Bhakkar flood bund.

2. 	Construction of J-Head Spur at RD 58+800 of Bhakkar flood bund.

3.  	Restoration of Existing J-Head Spur, Shank at RD 70+000 of Bhakkar flood bund.

The aforementioned works were executed under ADP. During Flood 2018, it was experienced that maximum discharge of 286554 cusecs passed through Bhakkar Flood Bund and no damage occurred in said reach due to blessing of these under construction structures.

The reach of River Indus beyond RD 105+000 of Bhakkar Flood Bund remained under severe threat and river was penetrating further towards left due to continuous tendency of erosion. Some thickly populated villages namely “Basti Metala, Basti Manchra & Basti  Tarkhani of Tehsil Bhakkar” had since been gulped by the river and following were under threat “Bast Moharan, Basti Cheema, Basti Mongar, Basti Warah Seeran,  Basti Sohla, Basti Bahar Shah and Basti Rakhwan of Tehsil Bhakkar and Tehsil Karor Lal Essan”. There was every likely hood of their burial if not protected on the dot.

In order to comply with the directions imported by the high-ups detailed precise survey was carried out at site, the depicted on the plan afresh presented to Irrigation Research Institute Lahore for conducting model study on the basis of fresh survey.

The outcomes of model study issued vide Irrigation Research Institute Lahore No. 1213/PRO (H)/836-C/II dated 23.11.2017, reveals that construction of 5 No. Concavo Convex shaped Guide Walls at different locations as depicted in the plan by the Irrigation Research Institute Lahore will certainly fructify in checking, drifting and training the river in the affected vicinity of District Bhakkar and Layyah. Afterwards due to site conditions,

1 No. concavo convex guide wall was deleted.

The following interventions were constructed and their locations are here under:-

1)    Concavo convex Guide Wall at RD 105+000 of Bhakkar Flood Bund.

2)    Concavo Convex Guide Wall in front of Basti Maharan.

3)   Concavo Convex Guide Wall in front of Basti Cheema.

4)   Concavo Convex Guide Wall in front of Basti Warah Seeran.

In spite of giving alignment of proposed flood bund from RD 105+000 – RD 200+000 along with interventions “it was advised in the said technical report that the River morphology may be monitored after construction of above recommended Guide Walls. It was observed on the model that the River morphology will be improved after construction of Guide Walls. The assessment of change of the river morphology for a period of 4 years may be recorded to ascertain the need of extension of existing Bhakkar Flood Bund. If the river regime of this reach after above assessment attracts the requirement of the extension of the existing Bhakkar Flood Bund, then a fresh model study may be got conducted with the site prevailing conditions for alignment of the proposed extension of Bhakkar Flood Bund along with other training works as Phase-II. It is also suggested that partial implementation of scheme may be avoided.”

Furthermore, in order to comply with the directions imported by the high-ups detailed survey was carried out at site, the depicted on the plan afresh presented to Irrigation Research Institute Lahore for conducting model study on the basis of fresh survey. Model study conducted at Research station Nandipur but final outcome of Model study is awaited.

The works proposed by Model Study may be taken up as a permanent engineering solution for safety of abadies in vicinity of District Bhakkar and Layyah.

XEN BKR

CHAPTER-4.

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF

HEAD WORKS / BARRAGES AND OTHER CONTROL POINTS

4.1	FLOOD LIMITS

Since there is no Head` works / Barrage in the jurisdiction of Bhakkar Canal Division. Therefore this Division has to come active with respect to discharge of River Indus downstream Chashma Barrage. The terminology of different kind of flood as low, Medium, High, Very high and exceptionally high will be taken as such in the light of discharge received from downstream Chashma Barrage.

| S.No | Site | Low Flood | Medium Flood | High Flood | Very High Flood | Exceptionally High Flood |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | River Indus downstream Chashma Barrage | 250000 Cs | 375000 Cs | 500000 Cs | 650000 Cs | 800000 Cs |

4.2	TIME LAG OF FLOODS

| S.No | Site | Mile | Hours |
| --- | --- | --- | --- |
| 1 | Distance from Attock to Jinnah Barrage Kalabagh | 106 | 48 |
| 2 | Distance from Jinnah Barrage Kalabagh to Chashma Barrage | 41 | 18 |
| 3 | Distance from Chashma Barrage to Kallurkot | 25 | 7.30 |

4.3.HIGHEST FLOODS

| YEAR | DATE | DISCHARGE |
| --- | --- | --- |
| 1976 | 1976 | 7,87,000 Cs |
| 1998 | 17-07-1998 | 5,02,948 Cs |
| 2005 | 18-07-2005 | 5,15,581 Cs |
| 2010 | 01-08-2010 | 10,38,873Cs |
| 2013 | 15-08-2013 | 5,59,935 Cs |
| 2015 | 03-08-2015 | 6,18,626 Cs |
| 2016 | 06-07-2016 | 3,74,610 Cs |
| 2017 | 05-08-2017 | 4,46,361 Cs |
| 2019 | 11-08-2019 | 3,63,783 Cs |
| 2020 | 03-09-2020 | 4,91,184 Cs |
| 2021 | 02.08.2021 | 3,30,102 Cs |
| 2022 | 28.08.2022 | 5,23,937 Cs |
| 2023 | 25.07.2023 | 415651 Cs |

XEN BKR

4.4	PEAK DISCHARGES (Last 10 Years)

| YEAR | DATE | DISCHARGE |
| --- | --- | --- |
| 2014 | 18.08.2014 | 2,57,632Cs |
| 2015 | 03-08-2015 | 6,18,626 Cs |
| 2016 | 06-07-2016 | 3,74,610 Cs |
| 2017 | 05-08-2017 | 4,46,361 Cs |
| 2018 | 16-08-2018 | 2,86,554 Cs |
| 2019 | 11-08-2019 | 3,63,783 Cs |
| 2020 | 03.09.2020 | 4,91,184 Cs |
| 2021 | 02.08.2021 | 3,30,102 Cs |
| 2022 | 28.08.2022 | 5,23,937 Cs |
| 2023 | 25.07.2023 | 415651 Cs |

XEN BKR

CHAPTER-5

FLOOD FIGHTING STRATEGY

All precautionary measures will be adopted to cope with any eventuality during flood 2024, Flood fighting strategy would be adopted for the safe passage of flow.

In low flood, the temporary watching huts will be established and flood fighting material will be shifted. Watching establishment employed for this purpose will remain busy under the supervision of concerned Sub Engineer.

When river water enters in to medium stage, it will start spreading on adjoining area touching toe of Bunds. Then it becomes necessary to be vigilant, watching of Bunds and deploying of machinery will be started to avoid any leakage from bunds. Sub Engineers will shift their camps to site as per duty rosters. The Telegraph office of Bhakkar Canal Division will act as flood information center and flood situation will be conveyed to Civil Administration and flood warning centers. SDO, River Sub Division, Bhakkar will keep the Executive Engineer apprised about latest development regarding flood situation.

When river water enters in high flood range and above, the Sub Divisional Officers, River, Bhakkar and Notak shall also shift their camps at vulnerable sites as planned in the duty roaster. Executive Engineer will keep liaison with Civil Administration, Army & Public representatives.

XEN BKR

CHAPTER-6

FLOOD DAMAGES / RESTORATION WORKS

INESCAPABLE WORKS TO BE CARRIED BEFORE FLOOD 2024

| S.No | Name of Work | Amount (In Millions) |
| --- | --- | --- |
| 1 | Maintaining Design Parameters of Bhakkar Flood Protection Bund in Reach RD 10+200-10+500. | 1.023 |
| 2 | Conversion of Existing solid stone stud RD 62+500 into Inverted Hockey Spur. | 180.235 |
| 3 | Restoration of Inverted Hockey Stud at RD 63+700 of Bhakkar Flood Protection Bund. | 129.319 |
| 4 | Restoration of J-Head Spur at RD 70+000 of Bhakkar Flood Protection Bund. | 187.767 |
| 5 | Protection of Bhakkar Flood Protection Bund in Reach RD 73+250-74+250. | 41.024 |
|  | TOTAL:- | 539.368 |

Note.

Estimates of above said works were submitted to competent authority. Base line data has been checked by NESPAK Consultants & under the process of sanction in Chief Engineer Sargodha office.

XEN BKR

CHAPTER-7

FLOOD FIGHTING / WATCHING ARRANGEMENTS

7.1	PRE FLOOD ARRANGEMENTS

Flood season starts from 15th June every year and watching establishment as per detail will be engaged during flood season for watching operation and flood fighting activities on monthly basis from 15-06-2024 to 15-10-2024. However, in case of very high flood or in emergency, strength of watching establishment will be increased as per site condition and requirements as provided in duty roaster.

| Sr. No. | Item | Scale |
| --- | --- | --- |
| 1 | Lamps Hurricane | 1 per beldar, 1 per mate and 20% extra of total only for the night shift |
| 2 | Wicks | 9 inch per lamp |
| 3 | Chimneys | 1 spare for each lamp |
| 4 | Burners & caps | 1 spare for each lamp |
| 5 | Torches – 3 cell | 1 for Executive Engineer, 1 for Sub Divisional Officer, 1 for Sub Engineer 1 one spare |
| 6 | Cells for Torches | 1 full and six spare sets |
| 7 | Patromix lamp | At depressions, old breach sites and dangerous sites each lamp with 2 spare chimneys, 2 nozzles, 2 funnels fitted with wire gauze |
| 8 | Fuel for lighting fire | To be collected by beldar establishment |
| 9 | Kerosine Oil | As per practice 1/3 bottle per lantern per night and one bottle per patromax per night (22 nights per month) |
| 10 | Match Boxes | 1 match box per month |
| 11 | Spirit | 1 bottle per patromax per month |
| 12 | Funnels | 2 No. per watching hut |
| 13 | Oil Extractor (Ordy) | 2 No. per watching hut |
| 14 | Spirit cans | 1 per patromax |
| 15 | Larmal 50 feet long | 50 per watching hut |
| 16 | Mallets wooden | 5 mallets per watching hut |
| 17 | Tranger wire | 1 roll of 14 BSW gauge at each bund |
| 18 | Gunny bags | 100 bags per mile |
| 19 | Axes | 2 No per mile |
| 20 | Kassies with handles | 1 for each beldar + 10% (for one shift only) |
| 21 | Hammer 2.5 lbs | 1 per mile |
| 22 | Hammer 10 lb | 2 per mile |
| 23 | Buckets (12 inch size) | 5 No. per mile |
| 24 | Sledge hammer 14 lbs | 1 per mile |
| 25 | Bhan (Cow Dung) in ECbags | 20 bags per mile for dangerous portions |
| 26 | Sand | Collection of 200 cft. Every mile for dangerous portions |
| 27 | Stacks (6-8 feet) long | 100 stacks per mile |
| 28 | Khajji mats 3’*4’ | 50 Nos per mile |
| 29 | Baskets | 1 toot /2 Pilchi baskets per beldar of shift twice a month |
| 30 | Sutli | 1 lb per 100 bags |
| 31 | Needles | 4 Nos per beldar huts |
| 32 | Kassi Handles | 50% of the no. of kassies as spare |
| 33 | Munj/Patha/Pees/ Taranger 3 cft capacity of stone. | 500 No.s for each structure. |
| 34 | Tooth basket | 100 Nos each Sub Engineer |
| 35 | G I Wire Crates | 500 No |

Additional Information

| Sr.No | Site | Sanction Limit Lac Cft | Available Lac Cft | Balance Required |
| --- | --- | --- | --- | --- |
| 1 | J-Head Spur No.1 at RD 14+700 of Bhakkar Flood Protection Bund | 1.50 | 1.50 | - |
| 2 | Head Spur No.2 at RD 27+175 of Bhakkar Flood Protection Bund | 1.50 | 1.360 | 0.140 |
| 3 | J-Head Spur No.3 at RD 38+550 of Bhakkar Flood Protection Bund | 1.50 | 1.013 | 0.397 |
| 4 | J-Head Spur No.4 at RD 47+000 of Bhakkar Flood Protection Bund | 1.50 | 1.03 | 0.47 |
| 5 | J-Head Spur No.5 at RD 52+000 of Bhakkar Flood Protection Bund | 1.50 | 1.00 | 0.50 |
| 6 | Solid stone Hockey stud at RD 60+250 of Bhakkar Flood Protection Bund | 1.00 | - | 1.00 |
| 7 | Mole Head Spur No.6 at RD 60+700 of Bhakkar Flood Protection Bund | 1.50 | 0.909 | 0.591 |
| 8 | J-Head Spur No.7 at RD 71+750 of Bhakkar Flood Protection Bund | 1.50 | 1.015 | 0.485 |
| 9 | Hockey spur at RD 75+800 of Bhakkar Flood Protection Bund | 1.50 | 0.295 | 1.205 |
|  | TOTAL | 13.00 | 8.10 | 4.90 |

Note:-

Minimum required quantity of reserve stock will be procured after allocation of necessary funds.

XEN BKR

7.2	WATCHING  ESTABLISHMENT

7:3 	ARRANGEMENTS AT SENSITIVE SITES.

In case of emergency at Sensitive sites, the arrangements for the duty roaster are already attached on page No.20.-27

XEN BKR

7.4		WATCHING MATERIAL

Watching material will be provided in ample quantity as the experience shows that flood material’s deployment is very necessary. The particular care would be taken to ensure that there is adequate quantity of the required material shown as to be readily available everywhere particularly at dangerous site.

| Sr# | Description | Quantity Required | Quantity Available | Quantity Net (Balance) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | Kassies with handle | 528 | 36 | 528 | Flood fighting material will be purchase as per necessity |
| 2 | Torches | 35 | 12 | 23 |  |
| 3 | Cell for Torches | 500 | 0 | 500 |  |
| 4 | Shouldari double fly | 4 | 4 | 0 |  |
| 5 | Generator 2.5 KV (Mitsubishi) China | 3 | 1 | 2 |  |
| 6 | Axes | 70 | 36 | 34 |  |
| 7 | Umbrella. | 18 | 18 | 0 |  |
| 8 | Hammer Wooden | 50 | 14 | 36 |  |
| 9 | Patha Ban | 504 | 35 | 469 |  |
| 10 | Life Jacket | 14 | 6 | 8 |  |
| 11 | PVC insulated twin core Copper conductor cable 7/0.036 | 300 | 100 | 200 |  |
| 12 | Electric bulb 200 watt. | 70 | 25 | 45 |  |
| 13 | Toot baskets. | 1400 | 00 | 1400 |  |
| 14 | Diesel. | 2100 Ltr. | 0 | 2100 |  |
| 15 | Gunny bags. | 2100 | 000 | 2100 |  |
| 16 | Chairs. | 42 | 18 | 24 |  |
| 17 | Table. | 11 | 3 | 8 |  |
| 18 | Munj / patha tranger | 12500 | 0 | 12500 |  |
| 19 | Steel Charpoy | 9 | 3 | 6 |  |
| 20 | Teak Wood Board | 7 | 3 | 4 |  |
| 21 | Brass Holder | 32 | 12 | 20 |  |
| 22 | Switch Open Type | 14 | 10 | 4 |  |

Note: 	 Full quantum of material will be purchased before flood season on receipt of funds.

7.5	ARRANGEMENT FOR SOUNDING AND PROBING

The arrangement for sounding and probing will be taken up with the boat.

7.6	LIGHTING ARRANGEMENT

Generator along with all accessories i.e. electric insulated conductor cable and bulb etc will be kept available at site.

7.7	RATION ARRANGEMENT

Ration will be arranged by the local agencies and through NGO’s etc.

7.8	P.O.L ARRANGEMENT FOR VEHICLE.

## The arrangements of P.O.L will be made as per site requirement.

XEN BKR

## 7.9	TRANSPORTATION

# Transportation arrangements will be made with the help of Civil Administration.

7.10	LAW AND ORDER

Situation of Law & Order will be controlled with the help of law enforcing agencies, i.e.  Police

7.11	MEDICAL ARRANGEMENT FOR LABOUR

Medical facilities will be provided with the help of Health Department.

7.12	LIAISON WITH OTHER DEPARTMENT

The Executive Engineer Bhakkar will keep liaison with Civil Administration, Police, Health and Civil Defense Department and fully apprise the other Departments about flood situation.

7.13	ROLE OF THE ARMY

Pak Army will play his role in evacuating the Flood affected community, Livestock, Armed Forces will also help in controlling the law and order situation in case of emergency.

7.14	DUTIES OF TELEPHONE ATTENDANT

The telephone attendant will remain present 24 hours turn wise. They will receive gauges from all related stations and pass on to concerned quarter for necessary action.

| Sr. No | Name of officials | Time of Duties |
| --- | --- | --- |
|  |  | From | To |
| 1 | Muhammad Javed Signaler Cell No. 0344-7988130 Muhammad Awais Naib Qasid Cell No 0333-8040556 | 6:00 AM | 02:00 PM |
| 2 | Jamshed Iqbal Signaler Cell No 0345-7642139 Mohsin Shah T.A Cell No 0344-7642465 | 02:00 PM | 10: 00 PM |
| 3 | Asim Niwaz Signaler Cell No. 0307-4303639 Muhammad Iqbal Naib Qasid Cell No. 0343-1747420 | 10:00 PM | 06:00 AM |

7.15	WIRELESS ARRANGEMENTS

Wireless set will be installed in the vehicles of the Executive Engineer Bhakkar, Sub Divisional officer River, Bhakkar flood emergency center of Canal division Bhakkar with the help of police Department.

XEN BKR

CHAPTER-8

DETAIL OF ENCROACHMENT

The flood bunds and spurs are constructed to train the river and to ensure safe passage of the flood water. During flood season, inhabitants of river area evacuate their houses and take shelter on the flood bunds along with their animals. However no encroachments exist on the river training works / Flood bunds in Bhakkar Division.

Ordinary Encroachment

| Total Encroachments | Removed | Action To Be Taken |
| --- | --- | --- |
| Nil | Nil | Nil |

XEN BKR

CHAPTER -9

DUTY ROASTER / FLOOD FIGHTING PROGRAM.

Phase-I (Pre Flood Period)

This phase covers the pre flood period starting from start of the flood season upto the time the flood water raises up to 1.0 foot above general Natural Surface Level (NSL) along the flood bunds.

WATCHING:

Flood watching establishment will be arranged through Government contractor on hire & fire basis according to flood scales / stages and other essential needs at site.

| Stage | Strength |
| --- | --- |
| Water level is 1 feet above NSL or below along the flood bund | 1 watchman per mile per shift in two shifts during 24 hours on Bhakkar flood bund. |
| Water level is more than 1 foot above NSL along the flood bund | 1 watchman per mile per shift in three shifts during 24 hours on Bhakkar flood bunds |

During this phase concerned Sub Divisional officer of the bunds and respective Sub Engineers of the sections of the bunds will be the controlling officers under the overall supervision of the Executive Engineer, Bhakkar Canal Division Bhakkar.

Phase-II (Low Flood from 250000-375000 Cs.

This phase starts when the discharge downstream Chashma barrage is between 250000 Cs to 375000 Cs. The detail of actions to be taken during this phase is as follows.

| Activity | Action |
| --- | --- |
| Shifting of watching and necessary flood material to watching huts | Respective Sub Engineers. |

| Stage | Strength |
| --- | --- |
| The discharge ranges between 2.5 to 3.75 lac cusecs | 1 person per mile per shift in three shifts during 24 hours on Bhakkar flood bund. 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 foot above NSL. |

XEN BKR

Supervisory Staff

| 1 | Bhakkar Flood Bund RD 0+000 – 58+000 | Incharge SDO River, SEN Bhakkar. |
| --- | --- | --- |
| 2 | Solid Stone Stud at RD 7+500 | // |
| 3 | Solid Stone Stud at RD 8+600 | // |
| 4 | Solid Stone Stud at RD 9+140 | // |
| 5 | Solid Stone Stud at RD 10+000 | // |
| 6 | J-Head spur No.1 RD 14+700 | // |
| 7 | J-Head spur No.2 RD 27+175 | // |
| 8 | J-Head spur No.3 RD 38+550 | // |
| 9 | Hockey stud at RD 43+500 | // |
| 10 | J-Head spur RD 47+000 | // |
| 11 | J-Head spur No.5 at RD 52+800 | // |
| 12 | Solid stone inverted hockey stud at RD 57+500 | // |
| 13 | Hockey stud at RD 56+800 | // |
|  | Bhakkar Flood Bund RD 58+000-105+000 | // |
| 14 | Solid stone stud at RD 58+050 | // |
| 15 | Concavo Convex Guide wall b/w RD 58-59 | // |
| 16 | Solid stone stud at RD 59+500 | // |
| 17 | Solid Stone inverted Hockey Stud at RD 60+250 | // |
| 18 | Mole Head spur RD 60+700 | // |
| 19 | Inverted Hockey stud at RD 63+700 | // |
| 20 | Mole head spur at RD 71+750 | // |
| 21 | Hockey Stud at RD 75+800 | // |
| 22 | Hockey Stud at RD 77+100 | // |
| 23 | J-Head spur at RD 05+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Bhakkar |
| 24 | J-Head spur at RD 58+800 of Bhakkar Flood Bund | // |
| 25 | J-Head spur at RD 70+000 of Bhakkar Flood Bund | Incharge SDO River, SEN ISP. |
| 26 | Hockey Stud at RD 73+000 of Bhakkar Flood Bund | // |
|  | GUIDE WALLS |  |
| 1 | Concavo Convex Guide Wall at RD 105+000 of Bhakkar Flood Bund | Incharge SDO River, SEN River. |
| 2 | Concavo Convex Guide Wall in front of Basti Maharan | Incharge SDO River, SEN River. |
| 3 | Concavo Convex Guide Wall in front of Basti Cheema | Incharge SDO River SEN River. |
| 4 | Concavo Convex Guide Wall in front of Basti Warah Seeran | Incharge SDO River SEN River. |

Phase-III (Medium Flood From 375000 - 500000 Cs.

This phase starts when the discharge downstream Chashma crosses to flood limits 375000 - 500000 Cs.The detail of the action to be taken during this phase are as follows :-

| Stage | Strength |
| --- | --- |
| The discharge ranges between 3.75 to 5.0 Cs. | 2 persons per mile per shift in three shifts during 24 hours on Bhakkar flood bund. 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 foot above NSL. |

Supervisory Staff

| S.No | Name of Flood Structures | Duty of Officers / Officials |
| --- | --- | --- |
| 1 | Bhakkar Flood Bund RD 0+000 – 58+000 | Incharge SDO River, SEN Bhakkar. |
| 2 | Solid Stone Stud at RD 7+500 | // |
| 3 | Solid Stone Stud at RD 8+600 | // |
| 4 | Solid Stone Stud at RD 9+140 | // |
| 5 | Solid Stone Stud at RD 10+000 | // |
| 6 | J-Head spur No.1 RD 14+700 | // |
| 7 | J-Head spur No.2 RD 27+175 | // |
| 8 | J-Head spur No.3 RD 38+550 | // |
| 9 | Hockey stud at RD 43+500 | // |
| 10 | J-Head spur RD 47+000 | // |
| 11 | J-Head spur No.5 at RD 52+800 | // |
| 12 | Solid stone inverted hockey stud at RD 57+500 | // |
| 13 | Hockey stud at RD 56+800 | // |
|  | Bhakkar Flood Bund RD 58+000-105+000 | // |
| 14 | Solid stone stud at RD 58+050 | // |
| 15 | Concavo Convex Guide wall b/w RD 58-59 | // |
| 16 | Solid stone stud at RD 59+500 | // |
| 17 | Solid Stone inverted Hockey Stud at RD 60+250 | // |
| 18 | Mole Head spur RD 60+700 of Bhakkar Flood Bund | // |
| 19 | Inverted Hockey stud at RD 63+700 | // |
| 20 | Mole head spur at RD 71+750 | // |
| 21 | Hockey Stud at RD 75+800 | // |
| 22 | Hockey Stud at RD 77+100 | // |
|  | Under Construction Structures (SPURS) |  |
| 23 | J-Head spur at RD 05+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Bhakkar |
| 24 | J J-Head spur at RD 58+800 of Bhakkar Flood Bund | // |
| 25 | J-Head spur at RD 70+000 of Bhakkar Flood Bund | // |
| 26 | Hockey Stud at RD 73+000 of Bhakkar Flood Bund | // |
|  | GUIDE WALLS |  |
| 1 | Concavo Convex Guide Wall at RD 105+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Khokhar. |
| 2 | Concavo Convex Guide Wall in front of Basti Maharan | Incharge SDO River, SEN Bkr&ISP |
| 3 | Concavo Convex Guide Wall in front of Basti Cheema | Incharge SDO River, SEN Bkr&ISP, |
| 4 | Concavo Convex Guide Wall in front of Basti Warah Seeran | Incharge SDO River, SEN Asif |

This duty roster during this phase of the officers/officials is tabulated below. The officials under the overall control of the Sub Divisional Officers concerned will perform the duties.

Phase-IV (High Flood From 500000-650000 Cs.

This phase starts when the discharge downstream Chashma crosses to flood limits 500000 Cs to 650000 Cs. The detail of the action to be taken during this phase is as follows:-

| Stage | Strength |
| --- | --- |
| The discharge ranges between 5.0 to 6.5 Cs. | 4 persons per mile per shift in three shifts during 24 hours on Bhakkar flood bund. 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 foot above NSL. |

## Breach Closing Squad

When the discharge will exceed 4.50 Lac cusecs, the mobile units consisting of following items are to be raised. It will be ensured that pick up and tractor trolly are in proper working condition.

Stack bullies 16 foot long			= 140 No.

Killas						= 200 No.

Munj Ban Course				= 140 Kg

Showels					= 50 No.

Gunny bags					= 700 No.

Sutli						= 3 Kg

Needles					= 28   No.

Baskets						= 350 No.

Bhakkar Sub Division, a unit will be deployed at Bhakkar Flood Bund.

A gang of 10 persons and a mate will move along with the unit at a moment notice. At the same time the Army Authorities will also be requested to provide manpower for closing leakage/breach.

Supervisory Staff

This duty roster during this phase of the officers/officials is tabulated below. The officials under the overall control of the Sub Divisional Officers concerned will perform the duties.

| S.No | Name of Flood Structures | Duty of Officers / Officials |
| --- | --- | --- |
| 1 | Bhakkar Flood Bund RD 0+000 – 42+000 | Incharge SDO River, SEN Bhakkar. |
| 2 | Solid Stone Stud at RD 7+500 | // |
| 3 | Solid Stone Stud at RD 8+600 | // |
| 4 | Solid Stone Stud at RD 9+140 | // |
| 5 | Solid Stone Stud at RD 10+000 | // |
| 6 | J-Head spur No.1 RD 14+700 | // |
| 7 | J-Head spur No.2 RD 27+175 | // |
| 8 | J-Head spur No.3 RD 38+550 | // |
|  | Bhakkar Flood Bund RD 43+000 – 76+000 | Incharge SDO River, SEN Jharkil. |
| 9 | Hockey stud at RD 43+500 | // |
| 10 | J-Head spur RD 47+000 | // |
| 11 | J-Head spur No.5 at RD 52+800 | // |
| 12 | Solid stone inverted hockey stud at RD 57+500 | // |
| 13 | Hockey stud at RD 56+800 | // |
| 14 | Solid stone stud at RD 58+050 | // |
| 15 | Concavo Convex Guide wall b/w RD 58-59 | // |
| 16 | Solid stone stud at RD 59+500 | // |
| 17 | Solid Stone inverted Hockey Stud at RD 60+250 | // |
| 18 | Mole Head spur RD 60+700 | // |
| 19 | Inverted Hockey stud at RD 63+700 | // |
| 20 | Mole head spur at RD 71+750 | // |
| 21 | Hockey Stud at RD 75+800 | // |
| 22 | Hockey Stud at RD 77+100 |  |
|  | Under Construction Structures (SPURS) |  |
| 23 | J-Head spur at RD 05+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Bhakkar |
| 24 | J J-Head spur at RD 58+800 of Bhakkar Flood Bund | // |
| 25 | J-Head spur at RD 70+000 of Bhakkar Flood Bund | // |
| 26 | Hockey Stud at RD 73+000 of Bhakkar Flood Bund |  |
|  | GUIDE WALLS |  |
| 1 | Concavo Convex Guide Wall at RD 105+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Khokhar. |
| 2 | Concavo Convex Guide Wall in front of Basti Maharan | Incharge SDO River, SEN Bkr & ISP |
| 3 | Concavo Convex Guide Wall in front of Basti Cheema | Incharge SDO River, SEN Bkr & ISP |
| 4 | Concavo Convex Guide Wall in front of Basti Warah Seeran | Incharge SDO River, SEN Asif |

Phase-V (Very High Flood From. 650000 - 800000 Cs.

This phase starts when the discharge at the River Indus is in very high flood stage i.e. between 6.5 to 8.0 Lac cusecs. During this phase, special attention will be given to watch most vulnerable reaches of the bunds. Concerned officer In charge is responsible for proper up keeping of their reaches that these points. The details of the actions to be taken during this phase are as follows:-

| Stage | Strength |
| --- | --- |
| The discharge ranges between 5.0 to 6.50 Cs. | 8 persons per mile per shift in three shifts during 24 hours on Bhakkar flood bund. 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 foot above NSL. |

Supervisory Staff

This duty roster during this phase of the officers/officials is tabulated blew. The officials Under the

Overall control of the Sub Divisional Officers concerned will perform the duties.

| S.No | Name of Flood Structures | Duty of Officers / Officials |
| --- | --- | --- |
| 1 | Bhakkar Flood Bund RD 0+000 – 42+000 | Incharge SDO River, SEN Bhakkar, |
| 2 | Solid Stone Stud at RD 7+500 | // |
| 3 | Solid Stone Stud at RD 8+600 | // |
| 4 | Solid Stone Stud at RD 9+140 | // |
| 5 | Solid Stone Stud at RD 10+000 | // |
| 6 | J-Head spur No.1 RD 14+700 | // |
| 7 | J-Head spur No.2 RD 27+175 | // |
| 8 | J-Head spur No.3 RD 38+550 | // |
|  | Bhakkar Flood Bund RD 43+000 – 76+000 | Incharge SDO River, SEN ISP. |
| 9 | Hockey stud at RD 43+500 | // |
| 10 | J-Head spur RD 47+000 | // |
| 11 | J-Head spur No.5 at RD 52+800 | // |
| 12 | Solid stone inverted hockey stud at RD 57+500 | // |
| 13 | Hockey stud at RD 56+800 | // |
| 14 | Solid stone stud at RD 58+050 | // |
| 15 | Concavo Convex Guide wall b/w RD 58-59 | // |
| 16 | Solid stone stud at RD 59+500 | // |
| 17 | Solid Stone inverted Hockey Stud at RD 60+250 | // |
| 18 | Mole Head spur RD 60+700 | // |
| 19 | Inverted Hockey stud at RD 63+700 | // |
| 20 | Mole head spur at RD 71+750 | // |
| 21 | Hockey Stud at RD 75+800 | // |
| 22 | Hockey Stud at RD 77+100 | // |
|  | Under Construction Structures (SPURS) |  |
| 23 | J-Head spur at RD 05+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Bhakkar |
| 24 | J J-Head spur at RD 58+800 of Bhakkar Flood Bund | // |
| 25 | J-Head spur at RD 70+000 of Bhakkar Flood Bund | // |
| 26 | Hockey Stud at RD 73+000 of Bhakkar Flood Bund | // |
|  | GUIDE WALLS |  |
| 1 | Concavo Convex Guide Wall at RD 105+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Khokhar. |
| 2 | Concavo Convex Guide Wall in front of Basti Maharan | Incharge SDO River, SEN ISP |
| 3 | Concavo Convex Guide Wall in front of Basti Cheema | Incharge SDO River, SEN Bkr &ISP |
| 4 | Concavo Convex Guide Wall in front of Basti Warah Seeran | Incharge SDO River ,SEN Asif |

Phase-VI (Exceptionally High Flood i.e. more than 800000 Cs.

This phase commence when the discharge downstream Chashma Barrage crosses the very High Flood limit of 8.0 Lac Cs. The detail of actions to be taken during the phase is as follows:-

| Activity | Action By |
| --- | --- |
| Deputy Commissioner is to be informed to make arrangement for the evacuation of the marooned public within Bhakkar Flood Bund | Executive Engineer |
| Stage | Strength |
| The discharge ranges between 8.0 Lac Cs and above. | Six Watchmen per miles per shift in three shifts during 24 Hrs on Main embankments and other structures. 1 Chowkidar per watching hut for round the clock duty till the time watching material is taken back from the watching huts after recession of the flood to a level 1 Foot above NSL. |

Supervisory Staff

This duty roster during this phase of the officers/officials is tabulated blew. The officials under the overall control of the Sub Divisional Officers concerned will perform the duties.

| S.No | Name of Flood Structures | Duty of Officers / Officials |
| --- | --- | --- |
| 1 | Bhakkar Flood Bund RD 0+000 – 42+000 | Incharge SDO River, SEN Bhakkar, |
| 2 | Solid Stone Stud at RD 7+500 | // |
| 3 | Solid Stone Stud at RD 8+600 | // |
| 4 | Solid Stone Stud at RD 9+140 | // |
| 5 | Solid Stone Stud at RD 10+000 | // |
| 6 | J-Head spur No.1 RD 14+700 | // |
| 7 | J-Head spur No.2 RD 27+175 | // |
| 8 | J-Head spur No.3 RD 38+550 | // |
|  | Bhakkar Flood Bund RD 43+000 – 76+000 | Incharge SDO River, SEN ISP |
| 9 | Hockey stud at RD 43+500 | // |
| 10 | J-Head spur RD 47+000 | // |
| 11 | J-Head spur No.5 at RD 52+800 | // |
| 12 | Solid stone inverted hockey stud at RD 57+500 | // |
| 13 | Hockey stud at RD 56+800 | // |
| 14 | Solid stone stud at RD 58+050 | // |
| 15 | Concavo Convex Guide wall b/w RD 58-59 | // |
| 16 | Solid stone stud at RD 59+500 | // |
| 17 | Solid Stone inverted Hockey Stud at RD 60+250 | // |
| 18 | Mole Head spur RD 60+700 | // |
| 19 | Inverted Hockey stud at RD 63+700 | // |
| 20 | Mole head spur at RD 71+750 | // |
| 21 | Hockey Stud at RD 75+800 | // |
| 22 | Hockey Stud at RD 77+100 | // |
|  | Under Construction Structures (SPURS) |  |
| 23 | J-Head spur at RD 05+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Bhakkar |
| 24 | J J-Head spur at RD 58+800 of Bhakkar Flood Bund | // |
| 25 | J-Head spur at RD 70+000 of Bhakkar Flood Bund | // |
| 26 | Hockey Stud at RD 73+000 of Bhakkar Flood Bund | // |
|  | GUIDE WALLS |  |
| 1 | Concavo Convex Guide Wall at RD 105+000 of Bhakkar Flood Bund | Incharge SDO River, SEN Khokhar. |
| 2 | Concavo Convex Guide Wall in front of Basti Maharan | Incharge SDO River, SEN ISP |
| 3 | Concavo Convex Guide Wall in front of Basti Cheema | Incharge SDO River, SEN Bkr &ISP |
| 4 | Concavo Convex Guide Wall in front of Basti Warah Seeran | Incharge SDO River ,SEN Asif |

NOTE:-

- All the Sub Engineers would perform their duties assigned above along with their establishment with 	necessary T & P.

- Executive Engineers Bhakkar would be the overall In charge of the whole operation during very high and 	exceptionally high flood.

- However the Sub Engineers with their establishment would be called any time anywhere and at any 	point as desired and required by the SDO’ Incharge under intimation to Executive Engineer Bhakkar 	the In charge of whole operation.

XEN BKR

CHAPTER-10

EMERGENCY TELEPHONE NUMBERS

| S. No | Designation | Office | Resd / Mobile |
| --- | --- | --- | --- |
| 1 | Secretary Irrigation Department Lahore. | 042-99212117 042-99212118 | 042-99200954 |
| 2 | Chief Engineer Drainage & Flood Lahore | 042-9923551 | 042-35294102 0321-8969386 |
| 3 | Director Flood Lahore | 042-9923552 | 0323-4864378 |
| 4 | Deputy Director Flood Lahore | 042-35880700 | 042-99230282 0321-9485218 |
| 5 | Flood Warning Center Lahore. | 042-99205371 | - |
| 6 | Chief Engineer Irrigation Sargodha Zone | 048-9230445 | 048-9230451 0336-7501575 |
| 7 | Executive Engineer Operation Sargodha Zone | 048-9230446 | 048-3740050 0300-6363739 |
| 8 | Superintending Engineer Bhakkar Canal Circle,Bhakkar. | 0453921316 | 03006763112 |
| 9 | Executive Engineer Canal Division Bhakkar | 0453-921016 | 0300-4436614 |
| 10 | Sub Divisional Officer, River. | 0453-921016 | 0321-7743954 |
| 11 | Sub Engineer, Bhakkar. | 0333-8301002 | 0333-8301002 |
| 12 | Sub Engineer, Firdous. | 03036506750 | 03487200763 |
| 13 | Sub Engineer, Jharkil. | 0301-2860289 | 03419734210 |
| 14 | Chashma Barrage Exchange at Chashma Colony Kundian | 0459-241289 0459-242858 |  |

DISTRICT ADMINISTRATION BHAKKAR.

| 1 | Deputy Commissioner Bhakkar | 0453-921188 0453-921288 | 0453-9200388 0304-0920077 |
| --- | --- | --- | --- |
| 2 | Additional Commissioner Revenue Bhakkar | 0453-921396 | 0344-4000063 |
| 3 | Additional Deputy Commissioner General Bhakkar | 0453-921307 0453-921312 | 0333-0721412 |
| 4 | District Police Officer Bhakkar | 0453-921350 0453-921351 | 0312-5599299 |
| 5 | Assistant Commissioner Bhakkar | 0453-921299 | 0300-0857127 |
| 6 | Bhakkar Flood Control Room | 0453-921082 | 0453-921082 |

XEN BKR

CHAPTER-11

STANDARD OPERATION PROCEDURE (SOP) FOR BREACHING SECTIONS

  - HISTORY OF THE BREACHING SECTION.

There is no breaching section in the jurisdiction of Canal Division Bhakkar.

  - LOCATION, DESIGN, QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATION.

Not Applicable.

  - ARRANGEMENT OF EXPLOSIVES AND SECURITY OF EXPLOSIVE STORES.

Not Applicable.

  - LIST OF THE SECURITY STAFF ALONGWITH DETAIL OF THEIR TRAINING ETC.

Not Applicable.

  - DETAIL OF MECHANICAL MEANS AS A STANDBY ARRANGEMENTS IN CASE OF DETONATION FAILURE

Not Applicable.

  - DUTY ROSTER IN CASE OF CRITICAL SITUATION.

Attached in Page.20 -.27

  - BREACHING COMMITTEE WITH THEIR ACTION PLAN.

Not Applicable.

  - LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN CASE OF BREACH

Not Applicable.

  - ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENTS.

Not Applicable.

  - DETAILS OF COORDINATION WITH CIVIL / ARMY AUTHORITIES.

Not Applicable.

  - PARALLEL COMMUNICATION ARRANGEMENT.

Not Applicable.

  - INDEX PLAN.

Attached

Executive Engineer				           		Superintending Engineer

Bhakkar Canal Division, 						      Bhakkar Canal Circle

Bhakkar         			  				  Bhakkar

Chief Engineer,

Sargodha Irrigation Zone,

Sargodha.

CHAPTER-12

VULNERABLE SITES ON FLOOD BUND / STRUCTURES

12.1	APPREHENDED BREACHES IN FLOOD BUNDS / STRUCTURES

Vulnerable sites are given as below.

| S. No | Name of Flood Bund | Reach | Camp Location |
| --- | --- | --- | --- |
|  |  | From RD | To RD | RD |
| 1 | Bhakkar Flood Protection Bund | 62+000 | 73+000 | 58+050 |
| 2 | Bhakkar Flood Protection Bund | 73+000 | 74+000 | 70+500 |
| 3 | Bhakkar Flood Protection Bund | 80+000 | 92+000 | 92+000 |

12.2  	Operation of breaching sections.

There is no such case in Bhakkar Canal Division Bhakkar.

12.3  	Breaches due to rising of flood water, deterioration of flood bund.

There is no such case in Bhakkar Canal Division Bhakkar.

XEN BKR

CHAPTER-13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES LISTED ABOVE

PLAN NO. 1

Bhakkar Flood Protection Bund RD 62+000 – 63+000

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED

WITH LEVELS.

Plan Attached

XEN BKR

13.2                     DETAIL OF VILLAGES ABADIES LIKELY TO BE EFFECTED.

| S. No | Name of Villages Abadies |
| --- | --- |
| 1 | Bait Bogha |
| 2 | Basti Bachri |
| 3 | Basti Bokhara |
| 4 | Basti Jando |
| 5 | Basti Lahori |
| 6 | Basti Main Khan |
| 7 | Bawan pur Shumali |
| 8 | Bharmi Charagh |
| 9 | Bharmi Nawab |
| 10 | Binda Baho Shah |
| 11 | Chanda |
| 12 | Charar |
| 13 | Chuni Janubi |
| 14 | Ganji |
| 15 | Honday wali |
| 16 | Humayaoun wala |
| 17 | Hussain Abad |
| 18 | Hussain Bakhsh |
| 19 | Inayat Abad |
| 20 | Jhammat |
| 21 | Jhok Hafiz |
| 22 | Jhoke Tibba |
| 23 | Katchi Shahani |
| 24 | Khushka |
| 25 | Langer Kot |
| 26 | Machar wali |
| 27 | Mian |
| 28 | Mithu Bindo |
| 29 | Mulan wali |
| 30 | Notak Nasheb |
| 31 | Peer Ashab Nasheb |
| 32 | Rakh Dhandla |
| 33 | Rawana |
| 34 | Razai Shah Janobi |
| 35 | Sawar Nawan |
| 36 | Sultan Ahmad Shah |
| 37 | Yousaf Shah |

XEN BKR

13.3	STRATEGY AND ACTION TO BE TAKEN.

The arrangements will be made to watch Flood Bund on round the clock basis. The Incharge Sub Engineer and Sub Divisional Officer will look after all the watching activities. They will keep liaison with the Civil Administration Public Representative, Police Department, Army authorities and Executive Engineer Bhakkar.

In case of any emergency, the proclamation on loudspeakers will be arranged with the coordination of Civil Administration for evacuation of abadies inside the flood plain. Flood fighting activities will be carried out with the permission and guidance of Executive Engineer Bhakkar. The establishment will be deployed as per site requirements. The Executive Engineer Bhakkar will make the arrangement of hiring the machinery on emergent basis and also request will be made to the Agricultural Engineering Department for the provision of the Departmental machinery i.e. dozers etc. The flood water coming out of breach site will affect the Abadies of Mouze Dajal, Katchi Shahani, Jhok Tibba and other infrastructures like schools, basic health units and road network etc. The flood water will spread out in the adjoining area as mentioned above as well as shown in the index plan in a height of ranging from 05 ft to 06 ft height. The tentative area inundated by flood water will be 33200 Acres of Tehsil Bhakkar as shown on plan at Page No.35

The spilled out water from breach site after flowing parallel to Bhakkar Flood Protection Bund will again fall in the river Indus downstream flood bund. The Sub Divisional Officer, River Sub Division, Bhakkar will monitor the entire situation. He will arrange timely coordination with Civil Administration and Police Department.

The flood fighting activities will be performed in true letter and spirit to control the situation and to save the human beings and public property.

XEN BKR

13.3.1	ARRANGEMENTS

The effective arrangements will be made to mitigate the devastating effects of flood.

13.3.2 ESTABLISHMENT AND LOCATION OF FLOOD FIGHTING CAMPS

The Flood Fighting Camps will be established as given under.

RD 58+050 of Bhakkar Flood Protection Bund.

13.3.3 DUTIES OF OFFICERS / OFFICIALS ON THEIR CAMP SITES.

Sub Engineer Bhakkar Section will be In charge of the camp site. The following staff will be at the camp site.

| Camp NO. | Officer (Name Designation & Cell No). | Official |
| --- | --- | --- |
| 01 | Nadim Iqbal Sub Engineer 03338301002 | 5 No Establishment |

13.3.4 DEPARTMENTAL MACHINERY AVAILABLE

02 No tractor along with front end loader + trolley + water tank.

13.3.5 MACHINERY AVAILABLE FROM PRIVATE SOURCE

The following machinery can be made available through private source i.e Government contractors.

| S. No | Name of Items Required | Medium | High | Very High | Exceptionally |
| --- | --- | --- | --- | --- | --- |
| 1 | Excavator | 2 | 3 | 4 | 6 No |
| 2 | Tractor Trolly / Dumper | 2 | 4 | 6 | 8 No |
| 3 | Tractor with front blade / Water Tank | 1 | 2 | 2 | 2 No |
| 4 | Tractor with water tank | 1 | 1 | 1 | 1 No |
| 5 | Dozer / Showal | NIL | NIL | 1 | 1 No |

13.3.6  	FLOOD FIGHTING MATERIAL REQUIRED SITE NO.1 RD.56+000-57+000

| S.No | Items | Unit | Total Required Quantity | Available Quantity | Balance | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No | 10 | - | 10 | Flood fighting material will be purchased as per necessity |
| 2 | Cell for Torches | No | 540 | - | 540 |  |
| 3 | Gunny Bags | No | 800 | - | 800 |  |
| 4 | Hammer 2.5 lb | No | 5 | - | 5 |  |
| 5 | Hammer 10 lb | No | 10 | - | 10 |  |
| 6 | Kassi with handles | No | 100 | - | 100 |  |
| 7 | Mallet wooden | No | 5 | - | 5 |  |
| 8 | Needles for sewing bags | No | 5 | - | 5 |  |
| 9 | Spare handle for kassies | No | 40 | - | 40 |  |
| 10 | Torch 3 Cell | No | 20 | - | 20 |  |
| 11 | Tranger Wire | No | 1 | - | 1 |  |
| 12 | Shouldari double fly | No | 1 | - | 1 |  |
| 13 | Generator 2.5 Km (Mistubishi) China | No | 1 | - | 1 |  |
| 14 | Life Jacket | No | 6 | - | 6 |  |
| 15 | PVC Insulated twin core copper conductor cable 7/0.0 | No | 100 | - | 100 |  |
| 16 | Electric Bulb 200 Watt | No | 50 | - | 50 |  |
| 17 | Toot baskets | No | 200 | - | 200 |  |
| 18 | Diesel | Liter | 300 | - | 300 |  |
| 19 | Chairs | No | 6 | - | 6 |  |
| 20 | Table | No | 1 | - | 1 |  |
| 21 | Munj Patta Tranger | No | 5000 | - | 5000 |  |
| 22 | Steel Charpoy | No | 2 | - | 2 |  |
| 23 | Brass Bracket with Holder | No | 12 | - | 12 |  |
| 24 | Switch Open type | No | 10 | - | 10 |  |
| 25 | Teak wood board | No | 3 | - | 3 |  |
| 26 | Umbrella Large | No | 3 | - | 3 |  |

13.3.7	FLOOD FIGHTING MATERIAL AVAILABLE AT SITE NO.1 RD 58+000

| S.No | Description | Location | Quantity Available |
| --- | --- | --- | --- |
| 1 | Kassies | AT RD 58+000 OF BHAKKAR FLOOD BUND. | 20 No |
| 2 | Shouldari |  | 1 No |
| 3 | Steel Charpoy |  | 02 No |
| 4 | Umbrella |  | 03 No |
| 5 | Teak Wood Board |  | 03 No |
| 6 | Brass bracket with holder |  | 12 No |
| 7 | Switch Open Type |  | 10 No |
| 8 | Twin cure copper cable 0.036 |  | 300 Meter |
| 9 | Electric bulb 200.w |  | 24 No |
| 10 | Toot baskets |  | 200 No |
| 11 | Chairs. |  | 6 No |
| 12 | Table. |  | 1 No |

13.4		DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRICITY.

Road network, Schools, Health centers and Electric transmission lines exist all along in the Katcha area. There is no any other important installation.

XEN BKR

PLAN NO. 2

Bhakkar Flood Protection Bund of RD 73+000 – 74+000

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED

WITH LEVELS.

Plan Attached

XEN BKR

13:2           DETAILS OF VILLAGES ABADIES LIKELY TO BE AFFECTED

| S. No | Name of Villages Abadies |
| --- | --- |
| 1 | Bait Bogha |
| 2 | Basti Bachri |
| 3 | Basti Jando |
| 4 | Bhawan pur Shumali |
| 5 | Bharmi Charagh |
| 6 | Bharmi Nawab |
| 7 | Chanda |
| 8 | Charar |
| 9 | Chuni Janubi |
| 10 | Ganji |
| 11 | Honday wali |
| 12 | Humayaoun wala |
| 13 | Hussain Abad |
| 14 | Hussain Bakhsh |
| 15 | Inayat Abad |
| 16 | Jhammat |
| 17 | Jhok Hafiz |
| 18 | Jhoke Tibba |
| 19 | Katchi Shahani |
| 20 | Khushka |
| 21 | Langer Kot |
| 22 | Mian |
| 23 | Mithu Bindo |
| 24 | Mulan wali |
| 25 | Notak Nasheb |
| 26 | Peer Ashab Nasheb |
| 27 | Rakh Dhandla |
| 28 | Rawana |
| 29 | Razai Shah Janobi |
| 30 | Sawar Nawan |
| 31 | Sultan Ahmad Shah |
| 32 | Yousaf Shah |

XEN BKR

13.3	 STRATEGY AND ACTION TO BE TAKEN.

The arrangements will be made to watch Flood Bund on round the clock basis. The Incharge Sub Engineer and Sub Divisional Officer will look after all the watching activities. They will keep liaison with the Civil Administration Public Representative, Police Department, Army authorities and Executive Engineer Bhakkar.

In case of any emergency, the proclamation on loudspeakers will be arranged with the coordination of Civil Administration for evacuation of abadies inside the flood plain. Flood fighting activities will be carried out with the permission and guidance of Executive Engineer Bhakkar. The establishment will be deployed as per site requirements. The Executive Engineer Bhakkar will make the arrangement of hiring the machinery on emergent basis and also request will be made to the Agricultural Engineering Department for the provision of the Department machinery i.e. dozers etc. The flood water coming out of breach site will affect the Abadies of Mouza Dajal, Katchi Shahani, Jhok Tibba and other infrastructures like schools, basic health units and road network etc. The flood water will spread out in the adjoining area as mentioned above as well as shown in the index plan in a height of ranging from 05 ft to 06 ft height. The tentative area inundated by flood water will be 27970 Acres of Tehsil Bhakkar as shown on plan at Page No. 42

The spilled out water from breach site after flowing parallel to Bhakkar Flood Protection Bund will again fall in the river Indus downstream flood bund. The Sub Divisional Officer, River Sub Division, Bhakkar will monitor the entire situation. He will arrange timely coordination with Civil Administration and Police Department.

The flood fighting activities will be performed in true letter and spirit to control the situation and to save the human beings and public property.

XEN BKR

13.3.1	ARRANGEMENTS

The effective arrangements will be made to mitigate the devastating effects of flood.

13.3.2 ESTABLISHMENT AND LOCATION OF FLOOD FIGHTING CAMPS

The Flood Fighting Camps will be established as given under.

RD 70+500 of Bhakkar Flood Protection Bund

13.3.3 DUTIES OF OFFICERS / OFFICIALS ON THEIR CAMP SITES

Sub Engineer Islampur Section will be in charge of the camp site. The following staff will be at the camp site.

| Camp NO. | Officer (Name Designation & Cell No. | Official |
| --- | --- | --- |
| 02 | Muhammad Majid Sub Engineer 03419734210 | 15 No Establishment |

13.3.4 DEPARTMENTAL MACHINERY AVAILABLE

01 No tractor along with front end loader + trolly.

13.3.5 MACHINERY AVAILABLE FROM PRIVATE SOURCE

The following machinery can be made available through private source i.e. Government contractors.

| S. No | Name of Items Required | Medium | High | Very High | Exceptionally |
| --- | --- | --- | --- | --- | --- |
| 1 | Excavator | 2 | 3 | 4 | 6 No |
| 2 | Tractor Trolly / Dumper | 2 | 4 | 6 | 8 No |
| 3 | Tractor with front blade / Water Tank | 1 | 2 | 2 | 2 No |
| 4 | Tractor with water tank | 1 | 1 | 1 | 1 No |
| 5 | Dozer / Showal | NIL | NIL | 1 | 1 No |

XEN BKR

13.3.6  	FLOOD FIGHTING MATERIAL REQUIRED SITE NO.2 RD.73+000-74+000

| S.No | Items | Unit | Total Required Quantity | Available Quantity | Balance | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No | 10 | - | 10 | Flood fighting material will be purchased as per necessity |
| 2 | Cell for Torches | No | 540 | - | 540 |  |
| 3 | Gunny Bags | No | 800 | - | 800 |  |
| 4 | Hammer 2.5 lb | No | 5 | - | 5 |  |
| 5 | Hammer 10 lb | No | 10 | - | 10 |  |
| 6 | Kassi with handles | No | 100 | - | 100 |  |
| 7 | Mallet wooden | No | 5 | - | 5 |  |
| 8 | Needles for sewing bags | No | 5 | - | 5 |  |
| 9 | Spare handle for kassies | No | 40 | - | 40 |  |
| 10 | Torch 3 Cell | No | 20 | - | 20 |  |
| 11 | Tranger Wire | No | 1 | - | 1 |  |
| 12 | Shouldari double fly | No | 1 | - | 1 |  |
| 13 | Generator 2.5 Km (Mistubishi) China | No | 1 | - | 1 |  |
| 14 | Life Jacket | No | 6 | - | 6 |  |
| 15 | PVC Insulated twin core copper conductor cable 7/0.0 | No | 100 | - | 100 |  |
| 16 | Electric Bulb 200 Watt | No | 50 | - | 50 |  |
| 17 | Toot baskets | No | 200 | - | 200 |  |
| 18 | Diesel | Liter | 300 | - | 300 |  |
| 19 | Chairs | No | 6 | - | 6 |  |
| 20 | Table | No | 1 | - | 1 |  |
| 21 | Munj Patta Tranger | No | 5000 | - | 5000 |  |
| 22 | Steel Charpoy | No | 2 | - | 2 |  |
| 23 | Brass Bracket with Holder | No | 12 | - | 12 |  |
| 24 | Switch Open type | No | 10 | - | 10 |  |
| 25 | Teak wood board | No | 3 | - | 3 |  |
| 26 | Umbrella Large | No | 3 | - | 3 |  |

13.3.7    FLOOD FIGHTING MATERIAL AVAILABLE AT SITE NO.2 RD 73+000 – 74+000

| S.No | Description | Location | Quantity Available |
| --- | --- | --- | --- |
| 1 | Kassies | At RD 80+000 of Bhakkar Flood Bund. | Nill |
| 2 | Shouldari |  | // |
| 3 | Steel Charpoy |  | // |
| 4 | Umbrella |  | // |
| 5 | Teak Wood Board |  | // |
| 6 | Brass bracket with holder |  | // |
| 7 | Switch Open Type |  | // |
| 8 | Twin cure copper cable 0.036 |  | // |
| 9 | Electric bulb 200.w |  | // |
| 10 | Toot baskets |  | // |
| 11 | Chairs. |  | // |
| 12 | Table. |  | // |

13.4		DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRICITY.

Road network, Schools, Health centers and Electric transmission lines exist all along in the Katcha area. There is no any other important installation.

PLAN NO. 3

Bhakkar Flood Protection Bund of RD 80+000 – 92+000

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED

WITH LEVELS.

Plan Attached

XEN BKR

13:2           DETAILS OF VILLAGES ABADIES LIKELY TO BE AFFECTED

| S. No | Name of Villages Abadies |
| --- | --- |
| 1 | Bait Bogha |
| 2 | Basti Bachri |
| 3 | Basti Jando |
| 4 | Bhawan pur Shumali |
| 5 | Bharmi Charagh |
| 6 | Bharmi Nawab |
| 7 | Chanda |
| 8 | Charar |
| 9 | Chuni Janubi |
| 10 | Ganji |
| 11 | Honday wali |
| 12 | Humayaoun wala |
| 13 | Hussain Abad |
| 14 | Hussain Bakhsh |
| 15 | Inayat Abad |
| 16 | Jhammat |
| 17 | Jhok Hafiz |
| 18 | Jhoke Tibba |
| 19 | Katchi Shahani |
| 20 | Khushka |
| 21 | Langer Kot |
| 22 | Mian |
| 23 | Mithu Bindo |
| 24 | Mulan wali |
| 25 | Notak Nasheb |
| 26 | Peer Ashab Nasheb |
| 27 | Rakh Dhandla |
| 28 | Rawana |
| 29 | Razai Shah Janobi |
| 30 | Sawar Nawan |
| 31 | Sultan Ahmad Shah |
| 32 | Yousaf Shah |

13:3	STRATEGY AND ACTION TO BE TAKEN.

The arrangements will be made to watch Flood Bund on round the clock basis. The In charge Sub Engineer and Sub Divisional Officer will look after all the watching activities. They will keep liaison with the Civil Administration Public Representative, Police Department Army authorities and Executive Engineer Bhakkar.

In case of any emergency, the proclamation on loudspeakers will be arranged with the coordination of Civil Administration for evacuation of abadies inside the flood plain. Flood fighting activities will be carried out with the permission and guidance of Executive Engineer Bhakkar. The establishment will be deployed as per site requirements. The Executive Engineer Bhakkar will make the arrangement of hiring the machinery on emergent basis and also request will be made to the Agricultural Engineering Department for the provision of the Department machinery i.e. dozers etc. The flood water coming out of breach site will affect the Abadies of Mouza Dajal, Katchi Shahani, Jhok Tibba and other infrastructures like schools, basic health units and road network etc. The flood water will spread out in the adjoining area as mentioned above as well as shown in the index plan in a height of ranging from 05 ft to 06 ft height. The tentative area inundated by flood water will be 27970 Acres of Tehsil Bhakkar as shown on plan at Page No.

The spilled out water from breach site after flowing parallel to Bhakkar Flood Protection Bund will again fall in the river Indus downstream flood bund. The Sub Divisional Officer, River Sub Division, Bhakkar will monitor the entire situation. He will arrange timely coordination with Civil Administration and Police Department.

The flood fighting activities will be performed in true letter and spirit to control the situation and to save the human beings and public property.

13.3.1	ARRANGEMENTS

The effective arrangements will be made to mitigate the devastating effects of flood.

13.3.2 ESTABLISHMENT AND LOCATION OF FLOOD FIGHTING CAMPS

The Flood Fighting Camps will be established as given under.

RD 92+000 of Bhakkar Flood Protection Bund

13.3.3 DUTIES OF OFFICERS / OFFICIALS ON THEIR CAMP SITES

Sub Engineer Jharkil Section will be in charge of the camp site. The following staff will be at the camp site.

| Camp NO. | Officer (Name Designation & Cell No. | Official |
| --- | --- | --- |
| 02 | Muhammad Imran Sub Engineer 0303-5593451 | 15 No Establishment |

13.3.4 DEPARTMENTAL MACHINERY AVAILABLE

01 No tractor along with front end loader + trolly.

13.3.5 MACHINERY AVAILABLE FROM PRIVATE SOURCE

The following machinery can be made available through private source i.e. Government contractors.

| S. No | Name of Items Required | Medium | High | Very High | Exceptionally |
| --- | --- | --- | --- | --- | --- |
| 1 | Excavator | 2 | 3 | 4 | 6 No |
| 2 | Tractor Trolly / Dumper | 2 | 4 | 6 | 8 No |
| 3 | Tractor with front blade / Water Tank | 1 | 2 | 2 | 2 No |
| 4 | Tractor with water tank | 1 | 1 | 1 | 1 No |
| 5 | Dozer / Showal | NIL | NIL | 1 | 1 No |

XEN BKR

13.3.6  	FLOOD FIGHTING MATERIAL REQUIRED SITE NO.3 RD.80+000- 92+000

| S.No | Items | Unit | Total Required Quantity | Available Quantity | Balance | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No | 10 | - | 10 | Flood fighting material will be purchased as per necessity |
| 2 | Cell for Torches | No | 540 | - | 540 |  |
| 3 | Gunny Bags | No | 800 | - | 800 |  |
| 4 | Hammer 2.5 lb | No | 5 | - | 5 |  |
| 5 | Hammer 10 lb | No | 10 | - | 10 |  |
| 6 | Kassi with handles | No | 100 | - | 100 |  |
| 7 | Mallet wooden | No | 5 | - | 5 |  |
| 8 | Needles for sewing bags | No | 5 | - | 5 |  |
| 9 | Spare handle for kassies | No | 40 | - | 40 |  |
| 10 | Torch 3 Cell | No | 20 | - | 20 |  |
| 11 | Tranger Wire | No | 1 | - | 1 |  |
| 12 | Shouldari double fly | No | 1 | - | 1 |  |
| 13 | Generator 2.5 Km (Mistubishi) China | No | 1 | - | 1 |  |
| 14 | Life Jacket | No | 6 | - | 6 |  |
| 15 | PVC Insulated twin core copper conductor cable 7/0.0 | No | 100 | - | 100 |  |
| 16 | Electric Bulb 200 Watt | No | 50 | - | 50 |  |
| 17 | Toot baskets | No | 200 | - | 200 |  |
| 18 | Diesel | Liter | 300 | - | 300 |  |
| 19 | Chairs | No | 6 | - | 6 |  |
| 20 | Table | No | 1 | - | 1 |  |
| 21 | Munj Patta Tranger | No | 5000 | - | 5000 |  |
| 22 | Steel Charpoy | No | 2 | - | 2 |  |
| 23 | Brass Bracket with Holder | No | 12 | - | 12 |  |
| 24 | Switch Open type | No | 10 | - | 10 |  |
| 25 | Teak wood board | No | 3 | - | 3 |  |
| 26 | Umbrella Large | No | 3 | - | 3 |  |

13.3.7    FLOOD FIGHTING MATERIAL AVAILABLE AT SITE NO.3 RD 80+000 – 92+000

| S.No | Description | Location | Quantity Available |
| --- | --- | --- | --- |
| 1 | Kassies | At RD 92+000 of Bhakkar Flood Bund. | Nill |
| 2 | Shouldari |  | // |
| 3 | Steel Charpoy |  | // |
| 4 | Umbrella |  | // |
| 5 | Teak Wood Board |  | // |
| 6 | Brass bracket with holder |  | // |
| 7 | Switch Open Type |  | // |
| 8 | Twin cure copper cable 0.036 |  | // |
| 9 | Electric bulb 200.w |  | // |
| 10 | Toot baskets |  | // |
| 11 | Chairs. |  | // |
| 12 | Table. |  | // |

13.4		DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRICITY.

Road network, Schools, Health centers and Electric transmission lines exist all along in the Katcha area. There is no any other important installation.

XEN BKR

CHAPTER-14

Action Plan

14.1	RESHUFFLING/RECOUPING PLAN OF RESERVE STOCK OF STONE DEPARTMENTALLY.

Reserve stock of stone in case of emergency will be shifted to critical site through contractor as per requirement

14.2	DETAIL OF INLET/OUTLET CROSSING ALONG WITH CLOSING METHODOLOGY

Nil

14.3	DEPLOYMENT OF MACHINERY (MEDIUM TO HIGH FLOOD)

Attached at Page No.53

14.4	DEPLOYMENT OF MACHINERY (HIGH TO VERY HIGH FLOOD)

Attached at Page No.54

14.5	DEPLOYMENT OF MACHINERY (HIGH TO EXCEPTIONALLY HIGH FLOOD)

Attached at Page No.55

14.6	POLICE DEPLOYMENT PLAN

Attached at Page No.56

14.7	DETAILS OF SYNTHETIC BAGS WITH CAPACITY OF 500 KG AND 1000 KG

Details is attached on Chapter 13.3.6

14.8	DETAILS OF POLYTHENE SHEETS OF BLACK COLOR TO PROTECT UPSTREAM SLOPE WAVE ACTION AND TO CONTROL SEEPAGE THROUGH EMBANKMENTS

Details is attached on Chapter 13.3.6

XEN BKR

CHAPTER-15

BACKUP DIVISIONS (IN CASE OF BREACH)

In case of Emergency Khansar Canal Division Kallurkot will be requested for help.

Executive Engineer			 			 Superintending Engineer

Bhakkar Canal Division,			        		        Bhakkar Canal Circle

Bhakkar				        				 Bhakkar

Chief Engineer,

Sargodha Irrigation Zone,

Sargodha.