I N D E X

| Sr. No | Description | Page No |
| --- | --- | --- |
|  |  | (Part “A”) |  |
| Chapter 1 |  | Salient Feature | 3-4. |
|  | 1.1 | Location | 5-7. |
|  | 1.2 | General Description | 8 |
|  | 1.3 | Administration Setup | 9 |
| Chapter 2 |  | Flood protection and River Training works | 10 |
|  | 2.1 | Designed Parameter of Training works | 11 |
|  | 2.2 | Location Map | 12 |
| Chapter 3 |  | Brief History of past flood events | 13 |
| Chapter 4 |  | Design Data, Historic Peak flood data and previous five years flood data of Head Works / Barrages and or other control points | 14 |
|  | 4.1 | Flood Limits | 14 |
|  | 4.2 | Time Lags of Floods | 14 |
|  | 4.3 | Highest Floods | 14 |
|  | 4.4 | Peak discharge | 15 |
| Chapter 5 |  | Flood Fighting Strategy | 16 |
| Chapter 6 |  | Flood damages restoration works | 17 |
| Chapter 7 |  | Flood fighting watching arrangements | 18 |
|  | 7.1 | Pre-Flood Arrangements | 18 |
|  | 7.2 | Watching establishment | 19 |
|  | 7.3 | Arrangement at sensitive sites | 19 |
|  | 7.4 | Watching material | 19 |
|  | 7.5 | Arrangement for sounding & probing | 20 |
|  | 7.6 | Lighting arrangement | 20 |
|  | 7.7 | Ration arrangement | 20 |
|  | 7.8 | P.O.L arrangement for vehicles | 20 |
|  | 7.9 | Transportation | 20 |
|  | 7.10. | Law and Order | 20 |
|  | 7.11 | Medical arrangement for labour | 21 |
|  | 7.12 | Liaison with other Department | 21 |
|  | 7.13 | Role of the Army | 21 |
|  | 7.14 | Duties of Telephone Attendant | 21 |
|  | 7.15 | Wireless arrangements | 21 |
| Chapter 8 |  | Detail of encroachment | 22 |
| Chapter 9 |  | Duty roaster/ flood fighting program | 23 |
| Chapter 10 |  | Emergency Telephone Nos. | 24 |
| Chapter 11 |  | Standard operating procedure (SOP) for breaching sections | 25 |
|  | 11.1 | History of the breaching section | 25 |
|  | 11.2 | Location, design, quantity and variety of the explosive required for detonation | 25 |
|  | 11.3 | Arrangement of explosives and security of explosive stores | 25 |
|  | 11.4 | List of the security staff along with detail of their training etc | 25 |
|  | 11.5 | Detail of mechanical means as a standby arrangements in case of detonation failure. | 25 |
|  | 11.6 | Duty roaster in case of critical situation | 25 |
|  | 11.7 | Breaching committee with their action plan | 25 |
|  | 11.8 | List of the villages likely to be inundated in case of breach | 26 |
|  | 11.9 | Announcement and detail of evacuation arrangements | 26 |
|  | 11.10. | Details of coordination with Civil /Army authorities | 26 |
|  | 11.11 | Parallel communication arrangements | 26 |
|  | 11.12 | Index Plan | 27 |
|  |  | (Part “B”) |  |
| Chapter 12 |  | Vulnerable sites on Flood Bunds/ Structures | 28 |
|  | 12.1 | Apprehended breaches in flood Bunds / Structures | 28 |
|  | 12.2 | Operation of breaching sections | 28 |
|  | 12.3 | Breaches due to rising of flood water, deterioration of flood bund etc. | 28-29 |
| Chapter 13 |  | Emergency Contingency Plan for vulnerable sites listed above. | 30 |
|  |  | Emergency contingency plan must include |  |
|  | 13.1 | Plan showing route of flood water coming out of the breach supported with levels | 30-34 |
|  | 13.2 | Detail of villages abadies likely to be affected and this should also be shown on the plan | 30-34 |
|  | 13.3 | Strategy and action taken be explained in detail. This may include | 35 |
|  | 13.3.1 | Arrangements | 35 |
|  | 13.3.2 | Establishment of Flood Fighting Camp sites | 35 |
|  | 13.3.3 | Duties of Officers/ Officials and their camps | 35 |
|  | 13.3.4 | Departmental Machinery available | 35 |
|  | 13.3.5 | Machinery available from private source | 35 |
|  | 13.3.6 | Flood fighting material required | 36 |
|  | 13.3.7 | Flood fighting material available | 36 |
|  | 13.4 | Detail of other infrastructure like electric, Sui gas , Telephones installations, Road network, Other buildings, Canals and drainage network | 37 |
| Chapter 14 |  | Action Plan | 38 |
|  | 14.1 | Re-Scuffling/ recouping plan of reserve stone departmentally | 38 |
|  | 14.2 | Detail of inlet/ outlet crossing along with closing mythology | 38 |
|  | 14.3 | Deployment of Machinery (Medium to High Flood) | 38 |
|  | 14.4 | Deployment of Machinery (high to very high flood) | 38 |
|  | 14.5 | Deployment of Machinery (high to exceptionally high flood) | 39 |
|  | 14.6 | Police Deployment Plan | 39 |
|  | 14.7 | Details of Synthetic bags with capacity of 500 kg and 1000 kg | 40 |
|  | 14.8 | Details of polythene sheets of black color to protect upstream slope against wave action and to control seepage through embankments | 40 |
| Chapter 15 |  | Back up Divisions (in case of breach) | 41 |

PART A

Chapter No.1

SALIENT FEATURES

D.G.Khan canals Division-I, D.G.Khan is responsible for the operation and maintenance of canal Irrigation network detailed below:-

a)	D.G.Khan Canal from RD: 40-220 with off taking distributaries

b)	Link No. I from RD: 0-203 (tail) with off taking channels.

All these channels are irrigating an area of 299 Sq miles consisting of Tehsil D.G.Khan, District Dera Ghazi Khan and Tehsil Jampur of District Rajanpur.

D.G.Khan Canal is running parallel on the edge of Koh Suleman range from north to south. The distance of Hill Torrents to D.G.Khan Canal ranges from 8 to 15 miles on the west. During monsoon period, the following Channels of D.G.Khan Canal system are affected with high flood:-

D.G.Khan Canal RD: 0-220

Which comes from the following Hill Torrents:

- Sori Lund

- Sori Khosa

- Vidore

The hydrology and alluvial morphology of the Hill Torrents are of a such complex nature that no systematic hydrograph is predictable. The creeks developed due to Hill Torrents water destroy farmers managed basin, bunds across their lands who utilize this water in accordance with their ancient traditions and orthodox culture of this water distribution.

The floodwater then reaches furiously down to the foothills and is encountered by the right bank of D.G.Khan Canal-I. There are aqueduct crossings of insufficient capacity for each of the Hill Torrent to transfer flood water across left bank of D.G.Khan Canal at RD: 220 for its eventual outflow into river Indus after damaging the fertile irrigated land, mostly cotton crop and other public properties.

This flood water extends and spreads out to the village of Shadan Lund, Kala, Shah Saddar Din, Yaru, and D.G.Khan. Vigilant watching and maintaining of the above reaches of right bank of D.G.Khan Canal at RD:220 is most essential specially during the flood season from 15th April to 15th September.

DETAIL OF BANKS OF D.G.KHAN CANAL-I PROPOSED TO BE CONVERTED INTO FLOOD EMBANKMENT ALONG WITH  ITS PARAMETERS ARE TABULATED AS UNDER:-

| Sr.No | Name of Embankment | Length (Miles) | Top Width (ft) | Free Board (ft) | Side Slope | Stone Pitching |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Flood Bund along right bank of D.G.Khan Canal RD: 88000-144000 | 11.20 | 25 | 5 | 3:1/2:1 | 500 ft on the outer slope of banks along with the structures/ Hill torrent Crossings |
| 2 | Flood Bund along right bank of D.G.Khan Canal RD: 164+000-168+000 RD: 180+000-220+000 | 0.80 8.00 | 25 25 | 5 5 | 3:1/2:1 do |  |

It is pertinent to mention here, that Kachhi Canal has been constructed by WAPDA on the right side of D.G.Khan Canal at RD;220. Now, the Kachhi Canal acts as 1st defense line against the Hill Torrents flood water. Unfortunately, the incomplete banks and structures of Kachhi Canal acted adversely during the recent flood of 2012 & 2013. The accumulated flood water on the right bank of Kachhi Canal outburst through the gaps & incomplete structures which damaged the banks and Hill Torrent X-ings of D.G.Khan Canal-I at RD 220. The restoration and strengthening of mishaps of the banks and structures were taken in hand on emergent basis which are held up due to paucity of funds.

.

LOCATION

1.1		Location

DERA GHAZI KHAN IRRIGATION SYSTEM

Dera Ghazi Khan, is a District in the Punjab province of Pakistan. The District covers an area of 5,306 km² and it is a long narrow strip of country, 198 km. in length, sloping gradually from the hills which form its western boundary to the river Indus on the east. Below the hills the country is high and arid, generally level, but sometimes rolling in sandy undulations, and intersected by 201 hill torrents. With the exceptions of two, these streams dry up after the rains, and their influence is only felt for a few miles below the Hills.The eastern portion of the district is at a level sufficiently low to benefit by the floods of the Indus. A barren tract intervenes between these zones and is beyond the reach of the hill streams on the one hand and of the Indus on the other. Although liable to great extremes of temperature and to a very scanty rainfall, the district is not unhealthy. The Suleman Mountains rise to a height of 10,000 feet (3,000 m) in the north of the District.

### CLIMATE AND GEOGRAPHY

Dera Ghazi Khan is located at 30’03″ N and 70’38″ E. The overall climate of the city is dry with little rainfall. The winter is relatively cold and the climate is hot during the remaining part of the year, but it is very hot in summer. The temperature during summer is usually about 115 °F (46 °C), while during winter season the temperature is as low as 40 °F (4 °C). The prevailing wind direction is North-South. Due to the barren mountains of Koh-Suleman (Sulaiman Mountains) and the sandy soil of the area, windstorms are very common in the summer. During summer, the temperatures are generally amongst the highest in Pakistan

CLIMATE CHANGE IMPACTS ON ROD KOHI

•This unique system is extremely prone to devastating effects of climate change because it entirely depends on the rainfall.

•Climate change induces extreme events of floods / drought conditions.

•An integrated management of Rod Kohi irrigation system is imperative to mitigate the climate change effects by identifying climate adaptation measures to minimize adverse effects on land use and water management practices

FLOODS

The area is also vulnerable to floods from the Indus River in the East and from the Rod Koh coming from Suleman Mountains in the West. In 1957 flood water entered in the city and almost after 60 years second time in history water entered in the city on 9 September 2012 due to heavy rains in Koh-e-Suleman.The following main Hill Torrents remains active during heavy Rainfall

| Sr.# | Name of Hill Torrent | Maximum Discharge (Cusecs) |
| --- | --- | --- |
| 1 | SORI LUND | 98000 |
| 2 | Vidoor | 150000 |

Safety measures for protection of abadies, human lives and infrastructure of Public as well as Government are adopted before the coming flood season. Flood water extends and spreads out to villages of Shadan Lund, Kala,Shah Sadar Din, Yaru, and D.G.Khan, Keeping in view the flood velocity the flood water spreads and make different routs which can damaged other unknown abadies which has been Scattered faraway and they may can be considered as unknown villages.

1.2	 GENERAL DESCRIPTION

D.G.Khan Canal -I is off taking from the right side of Taunsa Barrage with a designed capacity of 8953 Cs which is irrigating an area of about 0.90 Million Acres. It falls within the Canal command of D.G.Khan canal from RD: 40+000 to 220.

Total length of Channels of D.G.Khan Canal Division-I is as under:-

- Main Canal (D.G.Khan Canal)				=	36.00 C. Miles

- Link No. I 							=	40.68 C. Miles

- Distributaries & Minors					=	222.00 C. Miles

Total 					=	299.00 C. Miles

- Gross Command Area 					=	238125 Acres

- Culture able Command Area 				=	227575 Acres

- No of Outlets 							=	1024

- Water Allowance 						=	6.36

1.3 ADMINISTRATIVE SETUP

Chapter No.2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1 DESIGNED PARAMETER

OF TRAINING WORKS

NO TRAINING WORK

2.2 	Location Map

Chapter No.3

BRIEF HISTORY OF PAST FLOOD EVENTS

D.G.Khan Canal-I and its whole system is situated on the east side of                         Koh-e-Suleman. The distance of D.G.Khan Canal and Dajal Branch Canal from                         Koh-e-Suleman varies from 8 C. Miles to 15 C. Miles respectively. The length of D.G.Khan Canal is 69 C. Miles where as the length of Dajal Branch Canal is 20 C. Miles. 5 C. Miles of Dajal Branch falls in D.G.Khan whereas the remaining 15 C. Miles falls in District Rajanpur. When there is slow or heavy rains, all type of run off passes through the Darrahas striking  to  right bank of the D.G.Khan Canal and Dajal Branch.  The water then spreads in the vast  area of various villages. The hill torrent water damages the crops, public properties, roads, telephone lines and high transmission electric lines and also damages the D.G.Khan Canal System of D.G.Khan as well as Jampur Tehsil of Rajanpur. The Hill Torrent water breaches the D.G.Khan Canal & Dajal Branch Canal system as a whole and enters into the canal commanded area, and then enters into Manka Drain whereas the capacity of Manka Drain is not sufficient to accommodate the appreciable quantum of Hill torrent flood water. The bulk of flood water normally exceeds the capacity of this drain, then left bank breaches opposite RD: 185, RD: 242 and 316 of D.G.Khan Canal. The water then enters in the natural depressions called Shoria Disty near D.G.Khan and Kapper Drain near Choti. This flood water stands in these depressions till it is infiltrated and evaporated since it has no out fall to the river.

During August 2012, there has been a wide spread heavy rain in the catchment area of Hill torrents, which generated into high flood in the entire surface area of D.G.Khan. This Hill torrent water reached the canal command area of D.G.Khan within hours, as the slope is quite steep due to hilly area. It entered in to the City & various villages of D.G.Khan by damaging and overtopping the right as well as left bank of D.G.Khan Canal. Hill Torrents named vidore,  Sori Loond and vidore which are the active Hill Torrents, who hit the D.G.Khan Canal at RD.185-186. The Hill Torrent flood water damaged the banks of said sites and work was taken in hand previously after restoration of banks channel was put in to operation to feed the tails of the Irrigation system of DGKhan Canal Division as well as Rajanpur Canal Division.

Chapter No.4

DESIGN DATA, HISTORIC PEAK FLOOD DATA & PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS/ BARRAGE & OTHER CONTROL POINT.

4.1	Flood Limits

Not Related

  - Time Lags of Floods

| Sr. No | Name of Hill torrent | Distance in Km | Time in hours |
| --- | --- | --- | --- |
| 1 | Sori Lund | 23K.M | 8 Hours |
| 2 | Vidore | 17 K.M | 6 Hours |

4.3 	(a)	Highest Floods.

Vidore 39254 Cs	dated 30.07.2023

(b)	DISCHARGE OF HILL TORRENT

| Sr No | Name | Discharge 25 Years return period (Cs) | Peak Discharge flood 2022 (Cs) | Catchment area (Sq Miles) | Cultivated area (Acres) | Annual average rain fall (Inches) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Sori Lund | 50700 | 64304 | 193 | 38696 | 1.06 |
| 2 | Vidore | 83000 | 39254 | 298 | 32983 | 0.99 |

4.4	 Peak discharge

| Sr. No | Year | Name of Hill Torrent | Peak Discharge in Cusecs | Date | No. of Days |
| --- | --- | --- | --- | --- | --- |
| 1 | 2012 | Sori Lund | 39758 | 09.09.2012 | 01 |
|  |  | Vidore | 75589 | 15-09.2012 | 01 |
| 2 | 2013 | Sori Lund | 97710 | 16.08.2013 | 01 |
|  |  | Vidore | 24767 | 14.08.2013 | 01 |
| 3 | 2014 | Sori Lund | 51460 | 02.08.2014 | 01 |
|  |  | Vidore | 56258 | 02.08.2014 | 01 |
| 4 | 2015 | Sori Lund | 64304 | 13.06.2015 | 01 |
|  |  | Vidore | 24764 | 29.06.2015 | 01 |
| 5 | 2016 | Sori Lund | 51460 | 03.08.2016 | 01 |
|  |  | Vidore | 24767 | 12.03.2016 | 01 |
| 6 | 2017 | Sori Lund | 54609 | 18.07.2017 | 01 |
|  |  | Vidore | 19355 | 24.07.2017 | 01 |
| 7 | 2018 | Sori Lund | 39758 | 16.07.2018 | 01 |
|  |  | Vidore | 19355 | 23.07.2018 | 01 |
| 8 | 2019 | Sori Lund | 98525 | 11.08.2019 | 01 |
|  |  | Vidore | 121000 | 11.08.2019 | 01 |
| 9 | 2020 | Sori Lund | 24679 | 30.06.2020 | 01 |
|  |  | Vidore | 39254 | 30.06.2020 | 01 |
| 10 | 2021 | Sori Lund | 6145 | 17.08.2021 | 01 |
|  |  | Vidore | 10151 | 21.08.2021 | 01 |
| 11 | 2022 | Sori Lund | 152487 | 21.08.2022 | 01 |
|  |  | Vidore | 174360 | 21.08.2022 | 01 |
| 12 | 2023 | Sori Lund | 64304 | 29.07.2023 | 01 |
|  |  | Vidore | 39254 | 30.07.2023 | 01 |

Chapter No.5

FLOOD FIGHTING STRATEGY

STAGE-1

When the discharge ranges of Hill torrents between 10000 to 50000 Cs Sub Divisional Officer, Gajjani, Dera and Darkhast Sub Division will be In-charge of overall watching operation and the Sub Engineer In-charge of their Sections will perform watching duties in their respective jurisdictions. No special watching is required.

STAGE  - II

When discharge ranges between 50000 to 100000 Cs. The Executive Engineer, DGKhan Construction Division and DGKhan Canal Division will be overall In-charge of watching operation. In addition the Sub Divisional Officers, will be In-charge of watching operation of DGKhan Canal & Dajal Branch along with supervisory staff and  Sub Engineer concerned , along with their watching gangs as listed in duty roster .

STAGE  - III

When discharge ranges between 100000 to 200000 Cs. The Executive Engineer, DGKhan Construction division and DGKhan Canal Division will be overall In-charge of watching operation. The Sub Divisional officer Gajjani, Dera , Darkhast Sub Division, along with supervisory staff of all the concerned Sub Engineers will be responsible for the watching operation.

All the flood gauges from upper region are received through the wireless system already installed at various Police Stations in the District. This is primarily an inadequate arrangement that may be improved. The Executive Engineer Construction Division D.G.Khan will be responsible for transmission of the debit of flood at RIM station and at canal crossings of each Hill Torrent. An information reached even few hour before can save colossal losses by timely adjustment of discharge in the canal. This purpose can be achieved by setting up special long range wireless communication system by installing at selected base and sub-base station. This facility will be extended to the vehicles of the officers and to the handsets for Sub – Engineers. The whole network will be alive to any untoward situation.

Responsibility of Staff

(1) 	Executive Engineer, of D.G.Khan Canals Division-I will be responsible for watch and ward of D.G.Khan Canal Division. The Executive Engineer, D.G.Khan will have an overall control over the flood preparedness and should have clarity in mind how to control and avert any grievous situation developing at any point around D.G.Khan Canal system. He should also apprise himself and alert other concerned about weather report and flood forecast.

(2)	The Executive Engineer, D.G.Khan construction Division will be responsible for transmission of report of flood at RIM station and at Canal crossings of each hill torrent.

(3)	The Sub Divisional Officer, Gajjani Sub Division will take over of D.G.Khan Canal RD: 40+000 to  88+500 , RD: 144+000 to 198+000, Gajjani Escape & Link No. 1 from RD 0+000 to 59+000. He will maintain his head quarter at Gajjani.

(4) 	The Sub Divisional Officer Dhingana Sub Division will be responsible of 
Link No.1 Form RD: 59+000 to 220+400 (Tail). The S.D.O along with entire staff will be shifted from their head quarter to Mahatam Rest House for Day and Night watching when the discharge in River Indus D/s Taunsa bridge will be increased from 3.00 Lac Cs.

Chapter No.6

FLOOD DAMAGES RESTORATION WORKS

NIL

Chapter No.7

FLOOD FIGHTING / WATCHING ARRANGEMENTS

7.1 	PRE FLOOD ARRANGEMENTS

Strict watching arrangements will be started by 15th of May every year. The watching establishment will be employed according to the scale fixed by the department. The pre-flood arrangements explained below are necessarily required.

- Flood fighting material should be arranged in requisite quantity. Particular care should be taken to ensure that adequate quantity of the required material is distributed and placed at all the watching huts at the start of flood season.

- The Sub Engineers will inspect all the D.G.Khan Canal-I under Sub Divisional Jurisdiction. They should walk along the toe of right side of Canal and locate rats or porcupine holes, get them opened, refilled and compacted. Similarly Sub Divisional Officer should inspect all the vulnerable reaches of the bunds on foot and act in similar way.

  - All lamps, patromax torches will be in good working condition. The lighting arrangements at important points and at vulnerable reaches of Canals will be available and ready for use.

  - In case of any emergency, Sub Engineers and Sub Divisional Officers will make adequate arrangements for communications of urgent massages from any part of the Canal to the Executive Engineer and the Superintending Engineer. If there is no telephone, telegraph or wire less link special massager should kept ready with proper conveyance at all times for this purpose.

  - All the watching establishment should be properly trained and alerted. Each member should know the duty to be performed by him.

  - Dry Run Rehearsal of flood fighting plan will be done by the end of May and any shortcoming noticed should immediately be rectified. The watching staff will be engaged on the following works.

- Clearing of jungle growth from the outer toe of embankment of 	Canals up to 5 feet height.

- Killing rats and other borrowing animals and closing their holes.

- Repairing / establishment temporary watching huts located along 	the Canals at vulnerable sites.

Detail of stone available and sanctioned

| Description | Total Quantity Required During YEAR 2023-24 | Available Quantity of Reserve Stock | Balance Quantity Required |
| --- | --- | --- | --- |
| Stone | Nil | Nil | Nil |

Any other work which is deemed necessary. Temporary watching huts to 	be constructed / repaired for storing flood fighting material by the watching establishment and are normally to be located at suitable points where a breach could occur or a relief cut is to be introduced.

7.2 	WATCHING ESTABLISHMENTS

During different stages of flood limits, sufficient strength of labour shall remain throughout the period of flood on the following basis.

| Site | Flood Limits |
| --- | --- |
|  | Low | Medium | High | Very High | Excep: High |
|  | Men | Shift | Men | Shift | Men | Shift | Men | Shift | Men | Shift |
| Hill torrent Xing 69+500 | 5 | 2 | 6 | 2 | 8 | 3 | 10 | 3 | 10 | 3 |
| Hill torrent Xing 144+000 | 5 | 2 | 6 | 2 | 8 | 3 | 10 | 3 | 10 | 3 |
| Hill torrent Xing 185+000 | 5 | 2 | 6 | 2 | 8 | 3 | 10 | 3 | 10 | 3 |

Note:

Payment of machinery and work charged establishment subject to verification by the TPM / Consultants

After every three miles there will be a Mate and for every five miles there will be a Mistry in addition to Mate to supervise the work of Beldars.

7.3	SPECIAL WATCHING OF VULNERABLE SITES

The normal watching of D.G.Khan Canal RD: 40 – 345230/R and Dajal Branch RD: 0 – 100 is very necessary. The following sites of D.G.Khan Canal and Dajal Branch need special watching during the high flood period.

- D.G.Khan Canal at RD: 40 – 88500.

- D.G.Khan Canal at RD: 120 – 197

- Bank of D.G.KHAN Canal at RD: 197-220

7.4	WATCHING  MATERIAL

The following scale of materials as prescribed below is provided

| Sr No. | Name of Material | Total required (Qty) | Available (Qty) | Balance (Qty) | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | Lamps hurricane. | 50 | -- | 50 | Material required & estimates are under process |
| 2 | Wicks | 50 | -- | 50 |  |
| 3 | Globes. | 50 | -- | 50 |  |
| 4 | Burners & caps spare for 1/3 No. of lamps. | 150 | -- | 150 |  |
| 5 | Torches | 20 | -- | 20 |  |
| 6 | Cells | 80 | -- | 80 |  |
| 7 | Fuel for lighting | 1000 Ltr | -- | 1000 Ltr |  |
| 8 | Kerosene oil | 500 Ltr | -- | 500 Ltr |  |
| 9 | Generator | 4 | -- | 4 |  |
| 10 | Match boxes | 50 | -- | 50 |  |
| 11 | Spirit | 100 Ltr | -- | 100 Ltr |  |
| 12 | Funnels | 50 dozen | -- | 50 dozen |  |
| 13 | Spirit canes | 10 | -- | 10 |  |
| 14 | Oil canes | 250 | -- | 250 |  |
| 15 | Gunny bags | 25000 | -- | 25000 |  |
| 16 | Khaji Mats | 12000 | -- | 12000 |  |
| 17 | Baskets | 2500 | -- | 2500 |  |
| 18 | Kassies | 1200 | -- | 1200 |  |

  - ARRANGEMENT FOR SOUNDING & PROBING

Every vulnerable sites/ structure following arrangements (detail below) should made for probing.

Lighting arrangements

Ration arrangements

P.O.L arrangements

Transportation arrangements

Law & order arrangements

Medical arrangements

Availability of Boat/ sounding rods etc.

There is no boat / sounding rods in D.G.Khan Canal Division D.G.Khan

  - LIGHTING ARRANGEMENTS.

Generators/ Gas lamps and lanterns for each camp site will be purchased and will be shifted as per requirements before flood season.

  - RATION ARRANGEMENTS

The Ration arrangements are the responsibility of civil authorities.

  - P.O.L ARRANGEMENTS

Grant under Head P.O.L has already been received from higher office for running Govt. Jeeps but it is insufficient for expensive touring/ watching in flood days.

  - TRANSPORTATION.

Civil Authorities will be responsible for any emergency to provide the transpiration for inhabitants of flood affected areas.

  - LAW & ORDER

Law & order is the core responsibility of District Govt: and Police for which both the agencies have been requested to provide Police Guard to Control the law & order situation if arises for any mishap by the people of the area.

  - MEDICAL ARRANGEMENTS FOR LABOUR

Department cannot arrange the medical facilities for labour due to non availability of any such kind of funds. It will be the responsibility of District Govt: to provide medical facilities in flood areas where is required.

  - LIAISON WITH OTHER DEPARTMENTS

Necessary liaison with all other District Heads has been made to handle the flood situation. Executive Engineer, D.G.Khan Canals Division, D.G.Khan will keep liaison with civil /Army authorities to combat any mishap occurring due to floods and also will have liaison with flood forecasting centers Lahore for collection of flood related information.

  - ROLE OF THE ARMY.

Role of the Army is very impotent in case if any emergent situation arises due to high flood. Continuous liaison with the army authorities will be maintained during the flood if required.

  - DUTIES OF TELEPHONE ATTENDANT

To collect the hill-torrent/ river gauge or any kind of messages from any other sources and its proper delivery, the officials are deputed to perform their duties on telephone as telephone attendant during the flood season w.e.f 15-06-2024 to 15-10-2024 respectively.

| Name of Official | Period | Time |
| --- | --- | --- |
|  |  | From | To |
| Muhammad Abid (Signaler) | 15.06.2024 to 15.10.2024 | 8:00 AM | 8:00 PM |
| Muhammad Qasim (Signaler) | 15.06.2024 to 15.10.2024 | 8:00 PM | 8:00 AM |

  - WIRELESS ARRANGEMENTS

| 1 | Superintending Engineer, Derajat Circle, Dera Ghazi Khan. | During flood Police Department provide / fix the wireless system on the officers vehicles. Department has no wireless system. During flood wireless system is also installed on the critical / important sites i.e. Canal Telegraph Office DGKhan, Canal Rest House Mahtam & Canal Rest House at Head Gajjani RD: 88500 |
| --- | --- | --- |
| 2 | Executive Engineer, D.G.Khan Canal Division-I |  |
| 3 | Sub Divisional Officer, Gajjani. |  |

Chapter No.8

DETAIL OF ENCROACHMENT

| Total No of Encroachment | Removed | Balance | Action to be taken |
| --- | --- | --- | --- |
| Nil | Nil | Nil | Nil |

Chapter No.9

DUTY ROSTER/ FLOOD FIGHTING PROGRAM

| Gajjani Sub Division |
| --- |
| Gajjani Section | Ghazi Section |
| D.G.Khan Canal RD: 40-150 | D.G.Khan Canal RD:197-220 |
| Sub Divisional Officer |
| Sub Engineer Concerned |

Executive Engineer,

D.G.Khan Canals Division-I

D.G.Khan

Chapter No.10

EMERGENCY TELEPHONE NUMBERS

| Sr# | Name of Officers | Office | Residence / Cell No |
| --- | --- | --- | --- |
| Irrigation Department |
| 1 | Secretary, Irrigation & Power Department, Lahore. | 042 – 99212117 - 18 | 0304-0920033 |
| 2 | Chief Engineer, Irrigation Zone, D.G.Khan | 064 / 9260245 | 064 / 9260246 |
|  |  |  | 0322-2228637 |
| 3 | Chief Engineer, Drainage & Flood Zone, Lahore | 042-99233551 | 0303-7713303 |
| 4 | Superintending Engineer, Project Circle, (Irrg:) D.G.Khan. | 064 / 9260248 | 0300-9603980 |
| 5 | Superintending Engineer, Derajat Circle, D.G.Khan. | 064 / 9260247 | 0333-8581585 |
| 6 | Executive Engineer, D.G.Khan Construction Division, D.G.Khan. | 064 / 9260257 | 0300-0425111 |
| 7 | Executive Engineer, Jampur Construction Division (Irrg:) D.G.Khan. | 064 – 9260250 | 0333-0508781 |
| 8 | Executive Engineer, Rajanpur Canal Division, Rajanpur. | 0604 / 689064 | 0333-1871816 |
| 9 | Executive Engineer, D.G.Khan Canal Division,-I D.G.Khan. | 064 - 9260249 | 0300-6306140 |
| 10 | Executive Engineer, D.G.Khan Canal Division-II D.G.Khan. | 064 - 9260509 | 0300-2920290 |
| 11 | Executive Engineer, Taunsa Barrage Division, Kot Adu. | 066 / 2242796 | 0300-4436614 |
| 12 | Director Floods, Lahore. | 042 / 99212166 | 0331-6062020 |
| 13 | Flood Emergency Cell, Lahore | 042 / 7572091 - 93 | -- |
| 14 | Executive Engineer (Operation) DGKhan Irrigation Zone, (Flood Emergency Cell, DGKhan. | 064 / 9260251 | 0300-6306140 |
| 15 | Canal Telegraph Office, D.G.Khan. | 064 / 9260253 | 0336-6615223 |
| 16 | Canal Telegraph Office, Head Taunsa Barrage Kot Addu | 066/2243398 | 066 / 2243398 |
| Civil Administration |
| 1 | Police Wireless Station, DGKhan. | 064 / 9260113 | --- |
| 2 | District Coordination Officer, DGKhan. | 064 / 9060340 - 41 | 064 / 9260342 |
| 3 | Tehsil Municipal Officer. | 064 / 2463271 | -- |
| 4 | D.I.G, D.G.Khan. | 064 / 9060471 - 72 | -- |
| 5 | District Police Officer, DGKhan. | 064 / 9260100 - 102 | -- |
| 6 | District Revenue Officer, D.G.Khan. | 064 / 9260334 | -- |
| 7 | District Coordination Officer, Rajanpur. | 0604 / 689131 | 0604 / 689002 |
| 8 | District Police Officer, Rajan pur. | 0604 / 689055 | 0604 / 689042 |
| 9 | Deputy District Revenue Officer, Rajanpur. | 0604 / 689071 | 0604 / 689131 |
| Army Authority |
| 1 | Military Officer Head Quarter Engineers 2 Corps Multan Cantt. | 061/5313388 | --- |
|  |  | 5313389 | --- |
| 2 | Military Officer, Head Quarter Engineers 31-Corps Bahawalpur Cantt. | 0621/891/2353/2360 | --- |
| TEHSIL MUNICIPAL ADMINISTRATION |
| 1 | Tehsil Municipal Officer | 064-9260357/ 064-9260553 | --- |
| LIVE STOCK |
| 1 | Live Stock Office | 064-9260277 | -- |
| Water and Power Development Authority (WAPDA |
| 1 | Chief Engineer, MEPCO | --- | -- |
| 2 | Superintending Engineer MEPCO | 064-9260229 | -- |
| 3 | Executive Engineer MEPCO | 064-9260231 | -- |
| Roads Department |
| 1 | Executive District Officer Roads | 064-9260115 | --- |

Chapter No.11

STANDARD OPERATING PROCEDURES (SOP) FOR BREACHING SECTION

  - HISTORY OF THE BREACHING SECTION

There is no breaching section on any site of the flood infrastructure in DGKhan Canal Division DGKhan. Hence no need any arrangements.

  - LOCATION DESIGN QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATION

There is no breaching section on any site of the flood infrastructure in DGKhan Canal Division DGKhan. Hence no need any arrangements.

  - ARRANGEMENT OF EXPLOSIVES AND SECURITY OF EXPLOSIVE STORES.

There is no breaching section on any site of the flood infrastructure in DGKhan Canal Division DGKhan. Hence no need any arrangements.

  - LIST OF SECURITY STAFF ALONG WITH DETAIL OF THEIR TRAINING ETC.

There is no breaching section on any site of the flood infrastructure in DGKhan Canal Division DGKhan. Hence no need any arrangements.

  - DETAIL OF MECHANICAL MEANS AS A STAND BY ARRANGEMENTS IN CASE OF DETONATION FAILURE

There is no breaching section on any site of the flood infrastructure in DGKhan Canal Division DGKhan. Hence no need any arrangements.

  - DUTY ROASTER IN CASE OF CRITICAL SITUATION

According to the flood situation, duty roaster programme has been already mentioned in flood fighting plan in Chapter No.9.

  - BREACHING COMMITTEE WITH THEIR ACTION PLAN

For this purpose, following relief cuts committees is proposed who will approve the action of operating the relief cuts at site as and when necessity arises with their specific orders and supervision. The committee will start functioning from 15th of May each year.

| 1 | District Coordination Officer, D.G.Khan or his representative. | Convener |
| --- | --- | --- |
| 2 | Executive Engineer, D.G.Khan Canal Division-I, D.G.Khan. | Member |
| 3 | Superintendent of Police, D.G.Khan. | Member |
| 4 | The Sub Divisional Officers Gajjani. | Member |

  - LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN CASE OF BREACH.

| Sr No | Name of Tahsil | Name of District | Name of Village | Area in (Acrs) |
| --- | --- | --- | --- | --- |
| 1 | Relief cuts RD 181 left side of D.G.Khan Canal |
| i) | D.G.Khan | D.G.Khan | Yaru | 1704 |
| ii) |  |  | Chabri | 137 |
| iii) |  |  | Chabri Bala | 17040 |

  - ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENTS.

Commissioner D.G.Khan

District Coordination Officer D.G.Khan.

  - DETAIL OF COORDINATION WITH CIVIL /ARMY AUTHORITIES

Nil

  - PARALLEL COMMUNICATION ARRANGEMENTS

Canal Telegraph Office D.G.Khan and wireless in all vehicles of officer

  - INDEX PLAN

As there is no breaching section, So index plan is not required.

LOCATION PLAN OF BREACHING SECTION

PART B

Chapter No.12

VULNERABLE SITES ON FLOOD BUNDS /STRUCTURES

12.1 	Apprehended breaches in D.G.Khan Canals Division

a) 	Right bank of D.G.Khan canal RD:88+500   to RD:198+000

Right bank of D.G.Khan canal RD:198+000 to 220+000

b) 	Left bank of Link No. 1 RD:138+000 to RD:205+000 (Tail)

12.2	Operation of Breaching Sections

Breaches are made with the consultation of District Administration, Police Department, as well as with the consultation of Pak Army,  keeping in view the site condition and to save the public as well as Govt: infrastructures breaches are made. After subsiding of flood water breaches are closed by deploying Govt: machinery, Irrigation field staff to fill the breaches through gunny bags and sand etc.

12.3 	Breaches due to rising of Flood Water River/ Hill-Torrent water, deterioration of D.G.Khan canal, Dajal Branch & Link No.1

10 Nos. Hill-torrent crossings on D.G.Khan canal & 4 Nos. on Dajal Branch exists. During the Monsoon Season even on normal flood water of these hill-torrents, caused breaches on the right bank of D.G.Khan Canal-I due to the insufficient capacity of Hill torrents.  (Detail are given below as Appendix “A”)

The left bank of Link No 1 has been inundated during the flood 2010. However the condition of the left bank of Link No.1 is very poor and due to rising of flood water, there are chances of breach at any location.

Appendix “A”

Chapter No.12

| Sr.No. | Name of Hill Torrent. | Reach of Canal attacked. | H.T.X-ing At RD | Capacity of H.T X-ing (Cs) |
| --- | --- | --- | --- | --- |
| 1 | Sori Lund | RD. 40 – 140 D.G.Khan Canal | 69100 | 10000 |
| 2 | Chumbi sori Khosa (Sughri) Balab. | RD. 140 – 180 D.G.Khan Canal | 144+000 156+750 | 1000 1000 |
| 3 | Vidore | RD. 180 – 245 D.G.Khan Canal | 185+500 242+300 | 2000 10000 |

Chapter No.13

Emergency contingency plan for vulnerable site (Sites) listed above Emergency contingency plan must include

13.1	Plan showing of rout of flood water coming out of the breach supported with levels.

Plan showing the routs of coming H/t water and damaged Right Bank of 	D.G.Khan Canal ( Sori Lund , Sori Khosa and Vidore Hill Torrent)

13.2	 Detail of villages & Abadies likely to be affected

a) 	Detail of H/T Damaged the villages & Abadies given below:

Location Map A

| Sr No | Name of District | Tehsil | Vulnerable Sites | Sr. No | Villages | Area (Acres) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | D.G.KHAN | D.G.KHAN | Hill torrent xing RD: 69+500 Sori Lund & RD: 144+000 & 185+000 D.G.Khan Canal | 1 | Shero Dasti | 908 |
|  |  |  |  | 2 | Maqsoda Jhojhar | 105 |
|  |  |  |  | 3 | Rakh Dahi Chalikhan | 1102 |
|  |  |  |  | 4 | Bahadurgarh | 191 |
|  |  |  |  | 5 | Sheikhani | 90 |
|  |  |  |  | 6 | Chabri Bala Sharqi | 632 |
|  |  |  |  | 7 | Chabri Bala Gharbi | 1240 |
|  |  |  |  | 8 | Yaroo | 1704 |
|  |  |  |  | 9 | Chabri | 157 |

b)	 Detail of Abadies & villages

Yaroo, Chabri, Chabri Bala Sharqi, Chabri Bala Gharbi,  Shero Dasti, Maqsoda Jhojhar, Rakh Dahi Chalikhan, Bahadurgarh, Sheikhani, Kot Haibat ,

13.1	Plan showing of rout of flood water coming out of the breach 	supported with levels.

Plan showing the routs of coming H/t water and damaged Right Bank of 	D.G.Khan Canal & Dajal Branch (Sakhi Sarwar, Mithawan Hill torrent and 	Kaha Hill torrent)

13.2	 Detail of villages & Abadies likely to be affected

- Nil –

13.1	Plan showing of rout of flood water coming out of the breach 	supported with levels.

The route maps for left bank of Link No. 1 from RD:138+000 to 205+000 (Tail)

13.2	 Detail of villages & Abadies likely to be affected

Detail of H/T Damaged the villages & Abadies given below:

Location Map b

| Sr No | Name of District | Tehsil | Vulnerable Sites | Sr. No | Villages | Area (Acres) |
| --- | --- | --- | --- | --- | --- | --- |
| Left bank of Link No.I RD: 138+000 to 205+000 River Side |
| 1 | DGKhan | DGKhan | Link No.I RD: 138+000 to 205+000 | 1 | Qasba Samin | 5034 |
|  |  |  |  | 2 | Basti Mahatam | 6275 |
|  |  |  |  | 3 | Basti Jhoke | 1658 |
|  |  |  |  | 4 | Moza Hazara | 2600 |
|  |  |  |  | 5 | Basti Rindan | 287 |

b)	 Detail of Abadies & villages of Left bank of Link No. 1

Samin, Darh wala , farooq Abad, Aali wala, Haider wahn, Ghous Abad,    Nai wala, Rupey wala, Dait wala, Nawan Shehr, Sikhani Wala, Jhoke Utra, Puner Wala, Haider wahan, Ghous Abad, Jhoke Utra Puner wala, Sikhni wala, Nawan Shehr, Jalbani, Daha, Dhole, Jakhar Imam Shah,Haji Kamand

13.3 		Strategy and action taken be explained in detail this may 			include

To meet with any emergent/ critical situation at site safety measures i.e. to save the Government/ Public infrastructure & Human Lives etc. First of all efforts will be made to control the flood water by deploying heavy machinery / man power.

13.3.1		Arrangements

Arrangements for the flood fighting have been completed

13.3.2 	Establishment of flood fighting camps

D.G.Khan Canal RD: 150, 170, 220

13.3.3		Duties of Officers/ Officials given below:

| Gajjani Sub Division |
| --- |
| Gajjani Section | Ghazi Section |
| D.G.Khan Canal RD: 40-150 | D.G.Khan Canal RD:197-220 |
| Mr. Shahzad Umar Sub Divisional Officer 0333-3164644 |
| Sub Engineer Concerned |

13.3.4		Department Machinery Available

No Machinery is available in D.G.Khan Canals Division.

13.3.5		Machinery Available from private source.

Machinery can be made available from private source during the flood emergency situations detail of machinery is as under.

1.	Excavator

2No. (1 No for Link 1 , 1No for D.G.Khan Canal )

2. 	Tractor with trolley

6 No. (2 No. for Link No 1, 4 No for D.G.Khan Canal)

3.	Tractor with front blade

2 No. (1 No for Link 1 , 1No for D.G.Khan Canal)

13.3.6		Flood fighting Material required

13.3.7		Flood fighting Material available

D.G.Khan Canal (4 No. camps)

| Sr No | Description | Unit | Total Qty Required | Available Qty | Balance Qty | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Lantern | No | 258 No | -- | 258 No | Material required & estimates are under process |
| 2 | K.Oil | Ltr | 3212 Ltr | -- | 3212 Ltr |  |
| 3 | Wicks | Rft | 300 Rft | -- | 300 Rft |  |
| 4 | Chimneys | No | 200 No | -- | 200 No |  |
| 5 | Torches | No. | 50 No. | -- | 50 No. |  |
| 6 | Cells | Dozen | 100 Dozen | -- | 100 Dozen |  |
| 7 | I.C Bags / Gunny Bags | No | 1000 No | -- | 1000 No |  |
| 8 | Sutli | Kg | 30 Kg | -- | 30 Kg |  |
| 9 | Sewing needles | No | 36 No | -- | 36 No |  |
| 10 | Axes | No | 100 No | -- | 100 No |  |
| 11 | Kassies | No | 100 No | -- | 100 No |  |
| 12 | Baskets | No | 100 No | -- | 100 No |  |
| 13 | Match Boxes | No | 100 No | -- | 100 No |  |
| 14 | Chuldari | No | 3 No | -- | 3 No |  |
| 15 | Steel Charpai | No | 12 No | -- | 12 No |  |
| 16 | Bamboos | No | 300 No | -- | 300 No |  |

13.4	Detail of other infrastructure like electric, Sui gas, telephone installation, road network, other building, canal and drainages network.

Approach to Link No. I through metalled roads

Ghazi Ghat to Kot chutta at RD: 132+000 Link No. I, Samina east RD: 138 Link No.I Jhokeutra RD: 195-196 Link No.I, D.G.Khan to Taunsa road RD: 49+000 Link No.I, Yaru Road RD: 110000 Link No.I

Approach to D.G.Khan Canal  through metalled roads

D.G.Khan to Sakhi Sarwar Road at RD: 227+000 D.G.Khan Canal, D.G.Khan Choti Road RD: 316+000 D.G.Khan Canal, Vodore road RD: 212+000 D.G.Khan Canal, D.G.Khan to Taunsa road RD: 40+000 D.G.Khan Canal.

Buildings

| Name of Infrastructures (Building) | No of infrastructures(Building) |
| --- | --- |
| Schools | 8 |
| Dispensaries | 5 |

Chapter No.14

Action Plan

14.1	Re-Shuffling / recouping plan of reserve stone departmentally

N.A

14.2	Detail of inlet/ outlet crossing along with closing mythology

N.A

14.3	Deployment of Machinery (Medium To High Flood)

| Sr# | Name of structure | Length (in Mile) | Vulnerable Reach | Camp Location | Site in charge by Name and Cell | Machinery /Labour Deployed |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozers | Trolleys/ Dumpers | Tractor with Front Blade | Labour Beldar +Mate | Availability of stone (Lac Cft) |
| 1 | DGKhan Canal | 22 | 88+500 to 198+000 | DGKhan Canal RD: 150 to 170 | Mr. Shahzad Umar Sub Divisional Officer 0333-3164644 | 3 | 6 | 13 | 15 | 30+2 | nil |

14.4	Deployment of Machinery (high to very high flood)

| Sr# | Name of structure | Length (in Mile) | Vulnerable Reach | Camp Location | Site in charge by Name and Cell | Machinery /Labour Deployed |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozers | Trolleys/ Dumpers | Tractor with Front Blade | Labour Beldar +Mate | Availability of stone Cft |
| 1 | DGKhan Canal | 22 | 88+500 to 198+000 | DGKhan Canal RD: 150 to 170 | Mr. Shahzad Umar Sub Divisional Officer 0333-3164644 | 5 | 8 | 17 | 17 | 48+2 | nil |

Note: Payment of machinery and work charge establishment to verification by the TPM /Consultants

14.5	Deployment of Machinery (high to exceptionally high flood)

| Sr# | Name of structure | Length (in Mile) | Vulnerable Reach | Camp Location | Site in charge by Name and Cell | Machinery /Labour Deployed |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozers | Trolleys/ Dumpers | Tractor with Front Blade | Labour Beldar +Mate | Availability of stone Cft |
| 1 | DGKhan Canal | 22 | 88+500 to 198+000 | DGKhan Canal RD: 150 to 170 | Mr. Shahzad Umar Sub Divisional Officer 0333-6430523 | 6 | 8 | 20 | 22 | 52+2 | Nil |

Note: Payment of machinery and work charge establishment to verification by the TPM /Consultants

In case of any emergency machinery will be available at vulnerable sites to meet the unwanted situation

  - Police Deployment Plan

| Flood duty Roster police and Ranger |
| --- |
| 1- |  |  |  |  |  |
| Sr. | Site of Breaching section | Concerned Canal Division | Concerned Police station & District | Police personal to be deployed | Remarks (if any) |
|  |  |  |  | Inspector / S.I / A.S.I | Constables |  |
| 1 | -- | -- | -- | -- | -- | -- |
| 2- |  |  |  |  |  |  |
| Sr. | Vulnerable sites used for illegal cuts during floods | Concerned Canal Division | Concerned Police station & District | Police personal to be deployed | Remarks (if any) |
|  |  |  |  | Inspector / S.I / A.S.I | Constables |  |
| 1 | RD 181 left side of D.G.Khan Canal (Yaru, Chabri, Chabri Bala) | DGKhan Canal Division | Police station Sadar DGKhan District DGKhan | Sub Inspector = 01 Nos. | 4 Nos. |  |
| 3- |  |  |  |  |  |  |
| Sr. | Name of Barrage | Concerned Canal Division | Concerned Police station & District | Police personal to be deployed | Remarks (if any) |
|  |  |  |  | Inspector / S.I / A.S.I | Constables |  |
| 1 | -- | -- | -- | -- | -- | -- |
| 4- |  |  |  |  |  |  |
| Traffic police if required for smooth traffic flow at Barrage during flood. (add required detail) |
| 04 Nos. Traffic Police constables will be required during flood. |
| 5- |  |  |  |  |  |  |
| Any other suggestions. |
| NIL |

  - Details of synthetic bags with capacity of 500 kg and 1000 kg

Not Required

  - Details of polythene sheets of black color to protect upstream slope    against wave action and to control seepage through embankments.

Not Required

Chapter No.15

Back up Divisions (in case of breach)

DGKhan Construction Division is Backup Division of DGKhan Canal Division DGKhan and will cooperate in case of any emergency during flood season

# Text boxes

Executive Engineer,

D.G.Khan Canals Division-I,

EXECUTIVE ENGINEER

DGKhan Canal Division-I

STAFF OF  TELEGRAPH OFFICE

S.D.O  GAJJANI

SUB ENGINEER

KHARIK WALA  SECTION

SUB ENGINEER

GAJJANI SECTION

SUB ENGINEER

GHAZI SECTION

S.D.O

DHINGANA

SUB ENGINEER

MIRO SECTION

SUB ENGINEER

MAHTAM SECTION

SUB ENGINEER

JHOKE SECTION

SUB ENGINEER

MANA SECTION

Executive Engineer,

D.G.Khan Canals Division-I

Executive Engineer,

D.G.Khan Canals Division-I

Superintending Engineer, Derajat Circle D.G.Khan

Executive Engineer,

D.G.Khan Canals Division-I,

D.G.Khan

Executive Engineer,

D.G.Khan Canals Division-I

Executive Engineer,

D.G.Khan Canals Division-I

Executive Engineer,

D.G.Khan Canals Division-I,

D.G.Khan

Executive Engineer,

D.G.Khan Canals Division-I,

D.G.Khan

Executive Engineer,

D.G.Khan Canals Division-I,

D.G.Khan

Superintending Engineer, Derajat Canal Circle D.G.Khan

Chief Engineer D.G.Khan,

Irrigation Zone D.G.Khan.