GOVERNMENT OF THE PUNJAB

IRRIGATION  DEPARTMENT

FLOOD FIGHTING PLAN

FOR THE YEAR 2024

KASUR DIVISION DCC, KASUR

DEPALPUR CANAL CIRCLE, LAHORE

LAHORE IRRIGATION ZONE, LAHORE

APRIL-2024

INDEX

FLOOD FIGHTING PLANS-2024

| Chapter | PART-A | Page No |
| --- | --- | --- |
| 1 | Salient Feature of Division | 1 |
| 1.1 | Location | 1-5 |
| 1.2 | General Description | 6-8 |
| 1.3 | Administrative Setup | 9 |
| 2 | Flood Protection and River Training Works | 10 |
| 2.1 | Design parameter of Training works | 10-14 |
| 2.2 | Location Map | 15 |
| 3 | Brief History of Past Flood Events | 16 |
| 4 | Design Data, Historic Peak flood data and previous Five Years Flood Data of Headworks/ Barrages and or other control points | 17 |
| 4.1 | Flood Limits | 17 |
| 4.2 | Time Lags of Flood | 18 |
| 4.3 | Highest Floods | 18 |
| 4.4 | Peak Discharges | 19 |
| 5 | Flood Fighting Strategy | 20 |
| 6 | Flood Damages Restoration Works | 21 |
| 7 | Flood Fighting Watching Arrangements | 22 |
| 7.1 | Pre Flood Arrangements | 22 |
| 7.2 | Watching Establishment | 22 |
| 7.3 | Arrangements at sensitive sites | 23 |
| 7.4 | Watching Material | 24 |
| 7.5 | Arrangement of sounding and probing | 25 |
| 7.6 | Lighting Arrangement | 25 |
| 7.7 | Ration Arrangements | 25 |
| 7.8 | POL Arrangement for Vehicle | 25 |
| 7.9 | Transportation | 25 |
| 7.10 | Law and Order | 25 |
| 7.11 | Medical Arrangement for Labour | 26 |
| 7.12 | Liaison with other Departments | 26 |
| 7.13 | Role of Army | 26 |
| 7.14 | Duties of Telephone Attendant | 26 |
| 7.15 | Wireless Arrangements | 26 |
| 8 | Detail of Encroachment | 27 |
| 9 | Duty Roster / Flood Fighting Program | 28-30 |
| 10 | Emergency Telephone Nos. | 31-32 |
| 11 | Standard Operating Procedure (SOP) for Breaching Section | 33 |
| 11.1 | History of the Breaching Section | 33 |
| 11.2 | Location, Design, Quantity and Verity of the Explosive required for detonation | 33 |
| 11.3 | Arrangement of Explosive and security of Explosive Store | 33 |
| 11.4 | List of the Security Staff along with detail of their Training etc. | 33 |
| 11.5 | Detail of Mechanical Means as a Standby Arrangement in case of Detonation Failure. | 33 |
| 11.6 | Duty roster in case of critical situation | 33 |
| 11.7 | Breaching committee with their action plan | 34 |
| 11.8 | List of the villages likely to be inundated in case of breach | 34 |
| 11.9 | Announcement and detail of evacuation arrangements | 34 |
| 11.10 | Detail of coordination with civil / army authorities | 34 |
| 11.11 | Parallel communication arrangement | 34 |
| 11.12 | Index Plan | 35 |
| Chapter | PART-B | Page No |
| 12 | Vulnerable Sites of Flood Bund / Structures | 36 |
| 12.1 | Apprehended breaches Flood Bunds / Structures | 36 |
| 12.2 | Operation of Breaching Sections | 36 |
| 12.3 | Breaches due to rise of flood water, deterioration of flood bunds. | 36 |
| 13 | Emergency Contingency Plan For Vulnerable sites | 37 |
| 13.1 | Plan Showing Route of Flood Water coming out the expected breaching point supported with levels | 38 |
| 13.2 | Detail of Villages, Abadies likely to be affected and this should also be shown on plan. | 38 |
| 13.3 | Strategy and action taken, explained in detail this may include | 38 |
|  | 13.3.1 | Arrangements | 38 |
|  | 13.3.2 | Establishment of Flood Fighting Camps | 38 |
|  | 13.3.3 | Duties of Officers/ Officials at their camp sites | 38 |
|  | 13.3.4 | Departmental Machinery available | 39 |
|  | 13.3.5 | Machinery available from private sources | 39 |
|  | 13.3.6 | Flood Fighting Material | 40 |
| 13.4 | Detail of other infrastructure like electricity, Sui Gas, Telephone Installation, Road network, Other Building, Canal and Drainage Network. | 41 |
| 14 | Action Plan | 42 |
| 14.1 | Re-shuffling / recouping plan of reserve stock of stone departmently | 42 |
| 14.2 | Detail of inlet and outlet crossing along with closing methodology. | 43 |
| 14.3 | Deployment of machinery (Medium to high flood) | 43 |
| 14.4 | Deployment of machinery (High to very high) | 43 |
| 14.5 | Deployment of machinery (High to exceptionally high flood) | 43 |
| 14.6 | Police deployment plan. | 44 |
| 14.7 | Detail of synthetic bags with capacity of 500 Kg and 1000 Kg. | 45 |
| 14.8 | Detail of Polythene sheets of black colour to protect upstream slope against wave action and to control seepage through embankment. | 45 |
| 15 | Back up Divisions (In case of breach) | 46 |

PART-A

CHAPTER – 1

SALIENT FEATURE OF KASUR DIVISION DCC, KASUR.

  - LOCATION

Location of Kasur Division falls along the South – West Indo – Pak border between right bank of  Sutlej River and left bank of Sukh Bias Naullah up to B.S Link Canal.

Area of Kasur Division is affected by floods in  Sutlej River. Flood Bunds and Spurs have been constructed to protect area of District Kasur and Okara.

FLOOD protection bunds on river sutlej

The jurisdiction of Kasur Division starts from Sehjra enclave and Dhaya bund (Right Bank of River bias) opposite Rohiwal village and this Division is responsible for the maintenance of flood bunds along with the right bank of River Sutlej upto outfall of B.S. Link upstream Sulemanki Head Works.

The location of these bunds is falling in Kasur Division with salient features as shown on the plan of River Sutlej which are as under:-

- DHAYA BUND RD.0+000 to 11+090 (2.22 MILES)

This bund joins Right Marginal Bund at RD.35600 which was constructed to protect area form the spill of Rohi Naulla diversion. The bund has been raised by Defence Authorities by taking of earth from River side as per their proposals and putting the bund unsafe against Hydraulic pressure of flood water. The design data of this bund is given as under:-

Top width (RD.0-10100)		=	20.0 ft

(RD.10100-11090)			=	15.0 ft

Side slopes

River Side				=	3:1

Country Side				=	2:1

Free Board from H.F.L.			=	5.0 ft

H.F.L. 1988.				=	664.00

At present, the shape of bund is not safe. It is perforated by army authorities by constructing bunkers.

XEN KASUR

01

- RIGHT MARGINAL BUND RD.22+500 TO 35+600 (2.62 MILES)

This portion of Right Marginal Bund of Ferozepur Head Works falls in Pakistan territory. The bund at present is being maintained on the following design data:-

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L. 1988. 				=	660.35 ft

- LINK bund rd.0+000 TO 17+800 (3.56 miles)

This Bund along with Right Marginal Bund and Railway Guide Bund are very important for the protection of large area. Great difficulties were faced during exceptionally high flood   as a nominal free board of 1.0’ was remained. The work of rasing of this bund was got executed in different financial years. The designed parameters of this bund are tabulated as under:-

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L. 1988. 				=	660.35 ft

4.  railway guide bund rd.0+000 TO 7+500 (1.50 miles)

Railway shading was provided from Ganda Singh Wala to Ferozepur Head Works for carriage of stone. After partition, the track was removed and the formation was converted into a regular flood bund. As a result of breach at nose during super flood 1988, a Mole Head Spur was constructed to avoid further damage to nose and to protect Sanda Ranger Post and adjoining area. The design parameters of bund are as under:-

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L. 1988. 				=	660.35 ft

XEN KASUR

02

5. right retired embankment rd.0+000 TO 7+500 (1.5 miles)

Since Right Marginal Bund falls in India, Right Retired Embankment was constructed in a set back position. Subsequently, the maintenance of this bund was done with the following design parameters:-

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L. 1988. 				=	660.35 ft

6.  LOOP BUND RD.0+000 TO 1+750 (0.35 MILES)

Due to Indian action of demolishing same portion of Right Marginal Bund and other allied spur on right side of River Sutlej falling in Indian Territory, a loop bund was constructed to join Sufaida Bund with right retired embankment according to the following data.

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L. 1988. 				=	660.35 ft

7.  SUFAIDA BUND RD.0-2+342 (0.47 MILES)

The design parameters of bund are as under:-

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L. 1988. 				=	660.35 ft

XEN KASUR

03

8.  FLOOD EMBANKMENT ALONG WITH LOWER GANJA MINOR RD.0-TAIL (42+850) (8.57 MILES)

Left Bank of Lower Ganja Minor from Head to tail has been converted into flood embankment to Protect Large area from spills of River Sutlej which falling on Right Side of Minor. The embankment is being maintained according to following data:-

Top width.			=	8.0 ft

Side Slope River Side		=	3:1

Free Board from H.F.L. 1988	=	2.0 ft

9.  FLOOD EMBANKMENT ALONG WITH LOWER GANJA SUB MINOR RD.0+000 TO   10+ 200 (2.04 miles).

The flood embankment along with left bank of lower Ganja Sub Minor from RD.0-10200 was constructed during 1989 to check the spill of River Sutlej and to save Sub Minor from damage. The embankment is being maintained as follows:-

Top width.			=	15.0 ft

Side slopes

River Side.			=	3:1

Country Side			=	2:1

Free Board			=	2.5 ft

H.F.L. 1988  			=	624.44

10.  FLOOD EMBANKMENT ALONG WITH LEFT BANK OF upper DEPALPUR CANAL RD.136-156+860 (4.17 MILES).

Upper Depalpur Canal runs parallel to Sutlej River at a short distance to save the Channel and area during floods on the right bank. The left bank of Upper Depalpur Canal from RD.136000 to 156860 was converted into flood embankment with the following data:-

Top width.				=	25.0 ft with dowel

Slope on either side.			=	2:1

Free Board				=	5.0 ft

H.F.L. 1988  				=	625.00

XEN KASUR

04

11.  FLOOD EMBANKMENT ALONG WITH FATEH MUHAMMAD DISTY RD.0+000 TO 88+600 (17.72 MILES).

River Sutlej has been meandering towards Pakistan since 1952 consequently, some portions of Fateh Muhammad Disty were washed away during different times and diversions had to be made in set back position. Subsequently, left bank of the channel was converted into flood embankment and further extended to join with Lalluguddar Disty at RD.32+200 with the following design data:-

Top width				=	25.0 ft

Side slopes

River Side.				=	3:1

Country Side				=	2:1

H.F.L. 1988 				=	617.88

Free Board from H.F.L. 1988		=	6 ft

XEN KASUR

05

1.2 GENERAL DESCRIPTIONS

Sutlej River starts from Hamaliya range of mountains (Tibbat China) and flow towards Punjab (India) and enters into Pakistan territory 10 miles upstream Ferozepur Headworks.

It is perennial and Major River in subcontinent. The River Bias meets with Sutlej upstream of Herike Headworks in India. River Sutlej runs parallel to the   Indo – Pak International Boarder from Ferozepur Head Works upto Sulemanki Headworks. This reach of River is about 50 Miles. As there is no structure / Bridge on the River up to Sulemanki so behavior of this River is very un-predictable. Normally River becomes in flood during moon soon season from July to October. As per record, almost major floods have been observed during 15 September to 15 October. Due to construction of different Spurs and Embankments from defence point of view, this reach of Sutlej needs immediate attention in even low supplies.

DAMES ON SUTLEJ RIVER:-

Following 02 No Dams exists at sutluj river which are in torritorial jurisdicran of indian.

1.	The Bhakra Dam   was constructed on  Sutlej River in 1935 to 1954 for flood control, irrigation, electricity and fish development purpose. The measurement and technical data of said dam is as under:-

Height of this dam 750 ft. and it was highest dam in the world at the time of construction. The length on top of weir is 1700 ft. and 325 ft. at bottom in “V” shape gorge in Shivalik Hills. Thickness of foundation at bottom is 1320 ft. and tapered to 30 ft at top with road facilities. Maximum depth of dam is 740 ft and minimum is 300 ft. The name of reservoir is Gobind Sagar with its 90 miles length.

2.	Nungle Dam was constructed at 8 miles downstream of Bhakra Dam for Hydel power generation, its height is 95 ft and length is 1000 ft. It is a gate operated weir (29 No. gates with 30 ft each span). The Nungle Hydel Canal off takes from left side of  Sutlej River, it is concrete lined channel in the length of 40 miles.

HEADWORKS OF RIVER SUTLEJ:-

- Roper Headworks

Roper Headworks was constructed in 1867-1872 and only Sirhund Canal off takes from left side of  Sutlej River.

- Herike Headworks

Herike Headworks was constructed by Indian Government after independence near about 1965 to regulate the River Sutlej and canals off taking from Ferozepur Headworks without any fear by Pakistan in case of war. It is also a meeting point of River Bias with Sutlej.

XEN KASUR

06

- Ferozepur Headworks

Ferozepur Headworks was construced in 1916-27 ans is in jurisdiction of Indian  teritory. Depalpur Canal as off takes from right side of Bikaner, Eastern Canals off takes from left side of Ferozepur Head Works. The water supply in Depalpur Canal was disconnected by India after partition. Pakistan restored the supply in Depalpur Canal through BRBD Link Canal. The reach RD. 0-18500 Depalpur Canal has abandoned forever.

- SULEMANKI HEAD WORKS

Sulemanki Headworks was constructed in 1916-27 and is in jurisdiction of Pakistan teritory is about 126 Km. down stream from Frozepur Headworks. Pakpattan Canal off take from Sulemanki Headworks right & Eastern Sadqia and Fordwah Canal off take from left of this Headworks.

- ISLAM HEAD WORKS

Islam Headworks was constructed in 1916-27 and is in jurisdiction of Pakistan teritory is about 99 Km. down stream from Sulemanki Headworks. Malsi Canal off takes from right, Bahawalpur Canal and Qaimpur Canal off takes from left of this Head works.

- PUNJNAD HEAD WORKS

Punjnad Headworks was constructed in 1916-27 and is in jurisdiction of Pakistan teritory is about 215 Km. down stream from Islam Headworks. This Head work was constructed under the same project Punjnad and Abasia Canals   off takes from this Head works.

1. FLOOD BUND AROUND GANDA SINGH WALA

The protection measures of flood bunds in Kasur Division are concerned with the discharge in  Sutlej River and diversion portion of Rohi Naullah was constructed in 1960 which outfalls in River Sutlej upstream of Ferozepur Headwork’s during flood period. Gauge Reader is appointed / deputed at Talwar Post for observation of gauges during Flood Season. As soon as the gauge rises to 6.0 (W.L. 652.000), Sub Engineer Ganda Singh wala section will shift his head quarter to Talwar post, for which properly equipped watching staff comprising of 30 No. Beldars and 3 No. Mates in three shift of 8.0 hours each will be engaged. This establishment will watch Dhaya Flood Bund and R.M.B. 30-35600.

When the gauge at Kikar Ranger post raises above 8.0 (RL 654.00), the Sub Divisional Officer Chunian will shift his camp at Ganda Singh Wala and supervise the watching of bunds around Ganda Singh Wala with the assistance of Sub Engineer Chorkot Section and Zilladar Khudian Section alongwith the watching staff.

XEN KASUR

07

- UPPER DEPALPUR CANAL R.D. 136+000 to 156+860. (4.17 MILES)

The Sutlej River runs almost parallel to Upper Depalpur Canal System up to Sulemanki Hedwork’s. During flood period, the water spills and starts attacking the left bank of Upper Depalpur Canal.

As soon as the River gauge at Bakerke Gauge station raises above 17.70 feet, the Sub Divisional Officer Khudian will shift his camp at Bakerke Rest House along with Sub Engineer, Jajjal and Zilladar Jajjal for his assistance in order to watch the channel day / night. Sub Engineer Bakerke Section will also be present in section.

- FATEH MUHAMMAD DISTY. R.D. 0-86+600 (17.72 MILS)

As already stated that River Sutlej runs parallel to the Irrigation Channels and has changed its course towards Pakistan territory. The old creek has become active with the result that the channel remains under direct hit during the flood period. The channel has been shifted back many times in the past. In order to guard against damage to the channel, as and when River gauge at Bakerke rises up to 15.00 feet, the Sub Divisional Officer Kanganpur will shift his camp at Fateh Muhammad Canal Rest House. The Sub Engineer Kanganpur, Hira Singh, and Zilladar Fateh Muhammad will assist him day and night.

- lALLUGUDDAR DISTY R.D. 22-94+500 (TAIL) (14.50 MILES)

This channel, like Fateh Muhammad disty comes under direct hit during flood period and the safety of the canal is endangered. In order to check and guard against damage to the channel during flood period, the Sub Engineer Fateh Muhammad Section and Zilladar Kanganpur will supervise, watching of the canal day and night with a gang of 18 No. mates and 152 No. Beldars in shifts of 8 hours each.

XEN KASUR

08

1.3 ADMINISTRATIVE SETUP

The Administrative setup of Kasur Division DCC Kasur is as under:-

XEN KASUR

09

CHAPTER – 2

FLOOD PROTECTION AND RIVER TRAINING WORKS

  - NAME AND DESIGN PARAMETER OF TRAINING WORKS

- DHAYA BUND RD.0-11+090 (2.22 MILES)

Top width (RD.0-10100)		=	20.0 ft

(RD.10100-11090)			=	15.0 ft

Side slopes

River Side.				=	3:1

Country Side				=	2:1

Free Board from H.F.L			=	5.0 ft

H.F.L  					=	664.00

- RIGHT MARGINAL BUND RD.22+500-35+600 (2.62 MILES)

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L  					=	660.35 ft

- LINK bund rd.0-17+800 (3.56 miles)

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L  					=	660.35 ft

railway guide bund rd.0-7+500 (1.50 miles)

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L  					=	660.35 ft			XEN KAUSR

10

- right retired embankment rd.0-7+500 (1.5 miles)

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L  					=	660.35 ft

- LOOP BUND RD.0-1+750 (0.35 MILES)

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L  					=	660.35 ft

- SUFAIDA BUND RD.0-2+342 (0.47 MILES)

Top width				=	25.0 ft

Side slopes

River Side.				=	1:3

Country Side				=	1:2

Free Board				=	6.0 ft

H.F.L  					=	660.35 ft

- J-HEAD SPUR AT PANDOKI OUT FALL RD 0+000 TO 4+530 (0.91 MILES)

Top width				=	25.0 ft

Side Slope U/S				=	2:1

Side Slope D/S				=	3:1

Free Board above H.F.L  		=	5.0 ft

- J-HEAD SPUR OPPOSITE VILLAGE ATTAR SINGH WALA RD 0+000 TO 4+700 (0.94 MILES)

Top width				=	25.0 ft

Side Slope U/S				=	2:1

Side Slope D/S				=	3:1

Free Board above H.F.L  		=	5.0 ft

XEN KASUR

11

- FLOOD EMBANKMENT along with lower ganja minor rd 0-42+850          (8.57 MILES)

Top width.				=	8.0 ft

Side Slope River Side			=	2:1

Free Board from H.F.L			=	2.0 ft

- FLOOD EMBANKMENT ALONG With LOWER GANJA SUB MINOR RD 0-10+200 (2.04 Mils)

Top width.				=	15.0 ft

Side slopes

River Side.				=	3:1

Country Side				=	1½:1

Free Board				=	2.5 ft

H.F.L  					=	624.44

- FLOOD EMBANKMENT ALONG WITH LEFT BANK OF DEPALPUR CANAL RD.136-156+860 (4.17 MILES).

Top width.				=	25.0 ft with dowel

Slope on either side.			=	2:1

Free Board from H.F.L 1988		=	5.0 ft

H.F.L  					=	625.00

- FLOOD EMBANKMENT ALONG WITH FATEH MUHAMMAD DISTY RD.0-88+600 (17.72 MILES).

Top width				=	25.0 ft

Side slopes

River Side.				=	3:1

Country Side				=	2:1

H.F.L 					=	617.88

Free Board from H.F.L			=	6 ft

XEN KASUR

12

- J- HEAD SPUR AT RD. 30+300 OF FATEH MUHAMMAD DISTY RD. 0+000 TO 4+700 (0.94 MILES)

Top width				=	25.0 ft

Side Slope U/S				=	2:1

Side Slope D/S				=	3:1

Free Board above H.F.L	  	=	5.0 ft

H.F.L  					=	611.00

Top R.L					=	616.00

- J-HEAD SPUR AT RD. 50+400 OF FATEH MUHAMMAD DISTY RD. 0+000 TO 3+850 (0.77 MILES)

Top width				=	30.0 ft

Side Slope U/S				=	2:1

Side Slope D/S				=	3:1

Free Board above H.F.L  		=	5.0 ft

H.F.L  					=	607.65

Top R.L					=	612.65

- SLOPING SPUR AT RD. 54+460 OF FATEH MUHAMMAD DISTY RD. 0+000 TO 0+950 (0.19 MILES)

Top width				=	30.0 ft

Side Slope U/S				=	3:1

Side Slope D/S				=	3:1

Free Board above H.F.L  		=	5.0 ft

H.F.L  					=	606.85

Top R.L					=	611.85

- FLOOD EMBANKMENT ALONG WITH LALUGUDDAR DISTY RD.22+000 TO 94+500(14.50 MILES)  AND KANDA MINOR RD.0+000 TO 14+300 (2.86 MILES) Total =17.36 MILES

Top width				=	20.0 ft

Side Slope (Inner)			=	2:1

Side Slope (Outer)			=	1.50:1

Free Board				=	6 ft

- ATTARI MOLE-HEAD SPUR AT RD. 3+380 KANDA MINOR RD 0+000 TO 4+560 (0.91 MILES)

Top width				=	25.0 ft

Side Slope U/S				=	2:1

Side Slope D/S				=	3:1

Free Board above H.F.L  		=	5.0 ft

H.F.L  					=	600.50

Top R.L					=	605.50

XEN KASUR

13

- J-HEAD SPUR OF KANDA MINOR TAIL AT RD. 0+000 TO 5+400 (1.08 MILES)

Top width				=	30.0 ft

Side Slope U/S				=	2:1

Side Slope D/S				=	3:1

Free Board above H.F.L  		=	5.0

H.F.L  					=	600.00

Top R.L					=	605.00

Length					=	5400 ft

XEN KASUR

14

2.2 LOCATION MAP

XEN KASUR

15

CHAPTER-3

BRIEF HISTORY OF PAST FLOOD EVENTS

The Sutlej River was in spate in the year 1947 with 313700 Cusecs Discharge. Severe floods synchronized in Sutlej River in 1950 with Peak Discharge as 353937 Cusecs. The said River was in-spite in 1951 with Peak Discharge as 360000 Cusecs. In 1955 the River Sutlej was in high flood and registered highest discharge on record as 836764 Cusecs at Ferozepur Headworks through weir & breaches. The said River was in-spite in 1961 again with Peak discharge as 309925 Cusecs. The River Sutlej was again in high flood during September 1988 with Peak Discharge as 525450 Cusecs. The River Sutlej was once again in exceptionally high flood during August 2023 with Peak Discharge as 278297 Cusecs.

MAINTENANCE/ UPKEEPING OF RIVER TRAINING WORKS

The Kasur Division DCC, Kasur is responsible for the maintenance /up keeping and safety of following Flood Embankments and River Training Works on Right side of River Sutlej.

- Dhaya bund RD.0-11090 (2.22 miles)

- Right Marginal Bund RD.22500-35600 (2.62 miles)

- Link Bund RD.0-17800 (3.56 miles)

- Railway Guide Bund RD.0-7500 (1.50 miles)

- Right Retired Embankment RD.0-7500 (1.5 miles)

- Loop Bund RD.0-1750 (0.35 miles)

- Sufaida Bund RD.0-2342 (0.47 miles)

- J-Head Spur at Pandoki out fall RD 0-4+530 (0.91 miles)

- J-Head Spur opposite village Attar Singh Wala RD 0-4+700 (0.94 Miles)

- Flood Embankment along with Lower Ganja Minor RD.0-tail (42850) (8.57 miles)

- Flood Embankment along with Lower Ganja Sub Minor 0-10200 (2.04 mils)

- Flood Embankment along with left bank of Depalpur Canal RD.136-156860 (4.17 miles).

- Flood Embankment along with Fateh Muhammad Disty RD.0-88600 (17.72 miles).

- J- Head Spur RD. 30+300 of Fateh Muhammad Disty RD. 0-4700 (0.94 miles)

- J-Head Spur at RD. 50+400 of Fateh Muhammad. Disty RD. 0-3850 (0.77 miles)

- Sloping Spur at RD. 54+460 of Fateh Muhammad Disty RD. 0-950 (0.19 miles)

- Flood Embankment along with Lalluguddar Disty RD.22-94+500(14.50 miles) and Kanda minor RD.0-14300 (2.86 miles) (Total 17.36 miles)

- Attari mole-Head Spur at RD. 3+380 Kanda minor RD 0-4+560 (0.91 miles)

19 J-Head Spur at Tail of Kanda Minor RD 0-5400 (1.08 miles)

XEN KASUR

16

CHAPTER – 4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS 5 YEARS FLOOD DATA OF HEADWORKS / BARRAGES AND OR OTHER CONTROL POINTS

4.1 FLOODS LIMITS

Flood limits down stream Ferozepur Head Works and at Bakarke Gauge sites on River Sutlej as observed in the past are as under;-

| Location | Flood Limits | Zero Level | Low Ft. | Medium Ft | High Ft. | Very High Ft. | Exceptionally High Ft. |
| --- | --- | --- | --- | --- | --- | --- | --- |
| D/S Ferozepur Head Works / Ganda Singh Wala | Gauge | 623.45 | 18.00 | 19.75 | 20.75 | 21.80 | 22.55 |
| Bakerke | Gauge | 609.80 | 15.00 | 17.70 | 19.50 | 22.50 | 24.50 |

From Ferozpur Head Works Ganda Singh Wala

1.	Low Flood				18.00 ft.		50000 Cs.

2.	Medium Flood				19.75 ft.		80000 Cs.

3.	High Flood				20.75 ft.		120000 Cs.

4.	Very High Flood			21.80 ft.		175000 Cs.

5.	Exceptionally very High Flood	22.55 ft & above	above

XEN KASUR

17

4.2 TIME LAG OF FLOODS

| Sr. No. | Reach | Distance | Lag Time |
| --- | --- | --- | --- |
| i. | Lag time of flood water in River Bias is as under:- |
| 1. | Dera Gopi to Herike Headworks | 220 KM | One Day |
| ii. | Lag time of flood water in River Sutlej is as under:- |
| 1. | Bhakra Dam to Roper Headworks | 81 KM | One Day |
| 2. | Roper Headworks to Herike Headworks | 190 KM | Two Days |
| 3. | Herike Headworks to Ferozepur Headworks | 51 KM | One Day |
| 4. | Ferozepur Headworks to Sulemanki Headworks | 126 KM | Two Days |
| 5. | Sulemanki Headworks to Islam Headworks | 99 KM | Three Days |
| 6. | Islam Headworks to Punjnad Headworks | 215 KM | Four Days |

4.3  PREVIOUS HIGHEST FLOOD

In the River Sutlej, the highest floods in various period is tabulated as under:-

| Sr.No. | Highest Flood Year | Discharge D/S Ferozepur Head Works |
| --- | --- | --- |
| 1 | 1947 | 313700 Cusecs |
| 2 | 1950 | 353937 Cusecs |
| 3 | 1951 | 360000 Cusecs |
| 4 | 1955 | 836764 Cusecs |
| 5 | 1961 | 309925 Cusecs |
| 6 | 1988 | 525450 Cusecs |
| 7 | 2023 | 278297 Cusecs |

XEN KASUR

18

4.4  PEAK DISCHARGES D/S FEROZEPUR HEAD WORKS(in Cusecs)

| Year | August | September | October |
| --- | --- | --- | --- |
| 1988 | 95050 | 525450 | 320000 |
| 1989 | 27025 | NIL | NIL |
| 1990 | 1814.80 | 4455.74 | 195.75 |
| 1991 | 743.03 | 797.40 | NIL |
| 1992 | 2725.35 | 4252.85 | NIL |
| 1993 | 161.58 | 142.38 | NIL |
| 1994 | 4843.11 | 3263.09 | 34.97 |
| 1995 | 2327.93 | 180097.49 | 165.23 |
| 1996 | 1779.71 | 1533.24 | 267.11 |
| 1997 | 1647.81 | 1276.62 | 106.78 |
| 1998 | 711.89 | 2440.77 | 1085.79 |
| 1999 | 747.48 | 124.57 | 106.78 |
| 2000 | 355.94 | NIL | NIL |
| 2001 | 658.48 | NIL | NIL |
| 2002 | NIL | NIL | NIL |
| 2003 | 284.76 | 320.35 | NIL |
| 2004 | NIL | NIL | NIL |
| 2005 | 35000 | 9000 | 2000 |
| 2006 | 15000 | 25000 | 600 |
| 2007 | 13000 | 11000 | 2000 |
| 2008 | 53000 | 45000 | 11000 |
| 2009 | 16000 | 8000 | 2000 |
| 2010 | 50000 | 50000 | 50000 |
| 2011 | 74600 | 43020 | 3620 |
| 2012 | 3620 | 7741 | 687 |
| 2013 | 83700 | 11971 | 2000 |
| 2014 | 01507 | 10543 | 00033 |
| 2015 | 61820 | 5890 | 360 |
| 2016 | 9591 | 1507 | 219 |
| 2017 | 19166 | 2000 | 77 |
| 2018 | 2810 | 36560 | 3620 |
| 2019 | 60340 | 11019 | 1211 |
| 2020 | 2000 | NIL | NIL |
| 2021 | 1014 | NIL | NIL |
| 2022 | 4755 | 2810 | 77 |
| 2023 | 278297 | 59287 | 6048 |

XEN KASUR

19

CHAPTER – 5

FLOOD FIGHTING STRATEGY

Flood start from 1st July. One shift of watching staff will be employed @ one beldar for 2 miles for normal maintenance purpose of flood embankment. As soon as the gauge rises up to 6.0 ft. at Talwar Post the strength of watching staff will be increased up to one beldar for one mile during medium flood stage, two beldars for one mile in 3 shifts will be employed during high / very high floods, one mate for 30 No. Beldars will be employed for management purpose. Sub Engineer Ganda Singh Wala will shift his headquarter at Talwar Post.

As soon as the information is received from flood forecasting centre regarding Flood, Sub Divisional Officer Chunian will shift his camp at Ganda Singh Wala Rest House, similarly Sub Divisional Officer Khudian & Kanganpur will shift their camps at Bakerke & Fateh Mohammad Rest House. They will make arrangement for engaging watching staff locally or through contractor.  Executive Engineer Kasur Division DCC, Kasur will be overall incharge of the flood Fighting strategy and will keep liaison with District Administrator. Telegraph Office Kasur will remain open during flood season round the clock.

1. 	During Low Flood

When the gauge rises from 13 ft. to 18.00 ft. the river will be flowing in Low Flood. The Flood Emergency Center will established No.01on the R.M.B at Talwar Post, No.02. D/S Ferozpur Head Works at Kikar Post No.03. at Bakarke Canal Rest House and No.04 at Fateh Muhammad Canal Rest House. Every things relating to flood emergency will be available and ready round the clock at the mentioned sites.

2.	During Medium Flood

When the gauge rises from 18.00 to 19.75 ft. the river will be flowing in Medium Flood. All the necessary machinery will be stand by round the clock at the critical sites.

3.	During High Flood

when the gauge rises 19.75 to 20.75 ft. the river will be flowing in High Flood all the machinery will be  ready and in quick response position for facing any situation which and when created by the floods round the clock.

XEN KASUR

20

CHAPTER – 6

FLOOD DAMAGES / RESTORATION WORKS

During the exceptionally high flood 2023, leakage and seepage occurred at the right side of the Right Marginal Bund, Dhaya Bund, and Right Retired Embankment, extending 200 ft into the fields. These issues were mitigated through flood fighting efforts.

1. Existing Army bunkers along all flood bunds were closed to manage seepage/leakage during the exceptionally high flood of 2023 and also strengthened in restoration of bunds. However, these bunkers, constructed by the Pak Army without consideration of flood levels in collaboration with the Irrigation Department, have been reopened. Their reopening poses a risk of seepage/leakage and may lead to untoward situations during future floods.

2. The Sub Lower Ganja Minor experienced a breach from RD.4+000 to 5+000 due to the overtopping of floodwater. Estimates for the restoration of the Lower Ganja Sub Minor have been prepared and submitted to higher authorities for approval. The work is scheduled to be completed during the closure season of 2024 under the Head of M&R Main Canal.

3. Minor cracks developed on top of J-Head Spur Attar Singh Wala and Sloping Spur No.05, Kaluwala, which were promptly addressed at the site.

4.  The apron of J-Head Spur RD 30+300 at the Fateh Muhammad Bund was severely damaged/eroded due to the force of the River Sutlej. The existing apron is less than 20 ft in width at the site.

5. A prong along J-Head Spur RD 30+300 at the Fateh Muhammad Bund was washed away during the flood of 2023 over a length of 120 ft. Additional stone was dumped from the reserve stock to control further erosion.

6. The Kanda Flood Bund also sustained partial damage.

7. The earthen bank eroded along Canal Rest House Fateh Muhammad, necessitating restoration with a stone apron and stone pitching on the slope.

XEN KASUR

21

CHAPTER – 7

FLOOD FIGHTING / WATCHING ARRANGEMENTS

7.1 PRE- FLOOD ARRANGEMENTS

SCHEDULE OF FLOOD PREPAREDNESS ACTIVITIES FOR FLOOD SEASON 2024

| Sr: # | Activities | Target Dates |
| --- | --- | --- |
| I. | Preparation of Flood Fighting Plans |
|  | Submission of Draft Divisional Plans by Zonal Chiefs to Chief Engineer, D&F (after scrutiny by SEs/CEs) | Done |
|  | Review by Chief Engineer D&F | --- |
|  | Final submission of Flood Fighting Plans | will be circulated as per schedule |
| II. | Inspection of Flood Infrastructure |
|  | By XENs. | Done |
|  | By SEs/CEs | Done |
|  | By Departmental & Army Teams | Done |
| III. | Indication of Encroachments on bunds and spurs to the Civil Administration | nil |
| IV. | Painting Gauges, RD Marks, Data Boards and Repairs to Flood Bunds etc. | in progress |
| V. | Replenishment of Reserve Stock of Stone and Flood Fighting Material |
|  | Identification of needs | Completed |
|  | Funding / Procurement Arrangements | underway |
|  | Procurement, stacking prescribed field checks | underway |
| VI. | Installation of Wireless Sets | will be done |
| VII. | Opening of Zonal Flood Cells |
|  | Duty Roster | --- |
|  | Operative | --- |

XEN KASUR

22

| Sr. No. | Description | Reserve Stock Limit(lac/cft) | Quantity of stone available at site(lac/cft) | Balance Qty of stone to be procured | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | chunian sub division Defence Flood Bund Opposite village Ullake | 0.52610 | 0.52610 | Nil | - |
| 2 | Village Rajiwala | 0.22365 | 0.22365 | Nil | - |
| 3 | RRE Flood Bund | 0.25513 | 0.25513 | Nil | - |
|  | Total:- | 1.00488 | 1.00488 |  |  |
| 4 | kanganpur sub division J-Head Spur RD.30+300 FMD Disty & Flood Embankment along with FMD Disty RD.27-31 | 0.99011 | 0.20211 | 0.788 | - |
|  | Total:- | 0.99011 | 0.20211 | 0.788 |  |
|  | G. Total:- | 1.99499 | 1.207 | 0.788 |  |
|  | Say:- | 1.994 | 1.207 | 0.788 |  |

- STATUS OF STONE STRUCTURE WISE

XEN KASUR

23

(B) CONSOLIDATED STATUS OF STONE

| Reserve Stock Limit of total consolidated stones(Lac/cft) | Quantity of stone available at site(Lac/cft) |
| --- | --- |
| 1.994 | 1.207 |

7.2 WATCHING ESTABLISHMENT

Camps are established on all vulnerable sites to monitor the situation during flood season. Cell Phones are provided and generator sets are installed at important / vulnerable reaches. The flood watching material is procured and shifted to the camps sites.

To provide swift acquisition and disposal of any information related to flood situation in order to intiate prompt action, Gauge Readers will be appointed at Talwar Post, Kikar Post U/S &D/S Ferozepur Head Works. Keeping in view the possibility of receiving floods, precautionary measures will be taken from 1st july to 15th October. Watching Establishment will be employed for the flood season as per limits of flood already fixed for various magnitude of Discharge in River Sutlej.

XEN KASUR

24

FLOOD FIGHTING MATERIAL SANCTIONED QUANTITY

| Sr. No. | Site | Dhaya Bund | Canal Rest House Ganda Singh Wala | Canal Rest House Bakerke | Canal Rest House Fateh Muhammad | RD.36 of Lallugudar Disty | J-Spur RD.30300 Fateh Muhammad Dsity | J-Spur RD.3380 Kanda Minor | J-Spur RD.10600 Kanda Minor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
|  | Suti(Seba) Kg | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 5 | 5 | 5 |
|  | Needles(Soa) Dozon | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
|  | Torches 3 Cells | 5 | 20 | 10 | 20 | 10 | 10 | 10 | 10 |
|  | Cell in Dozen | 4 | 10 | 8 | 9 | 9 | 9 | 9 | 9 |
|  | Buckets No. | 20 | 40 | 30 | 40 | 20 | 20 | 20 | 20 |
|  | Baskets No. | 200 | 400 | 200 | 400 | 200 | 200 | 200 | 200 |
|  | Plastic Bags No. | 1000 | 2500 | 1000 | 2000 | 1000 | 1000 | 1000 | 500 |
|  | Shouldry No. | 1 | 2 | 1 | 2 | 2 | 2 | 2 | 2 |
|  | Swiss Cottage | 1 | 1 | 1 | 2 | - | 1 | 1 | 1 |
|  | Kassi No. | 50 | 100 | 50 | 100 | 50 | 50 | 50 | 50 |
|  | Manila Rope Kg. | 10 | 30 | 10 | 20 | 10 | 10 | 10 | 10 |
|  | G.I Wire Kg. | 50 | 100 | 50 | 100 | 50 | 50 | 50 | 50 |
|  | PVC Cable | 50 | 100 | 50 | 100 | 50 | 50 | 50 | 50 |
|  | Switch Board | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
|  | Bamboo | 100 | 200 | 100 | 200 | 100 | 100 | 100 | 100 |

7. 3ARRANGEMENTS FOR SOUNDING & PROBING

Sounding / probing arrangements are available at site.

7.4  LIGHTING ARRANGEMENTS

Adequate lighting arraignments are available at site with a stand by Generator and Torches.

7.5  RATION ARRANGEMENTS

The ration arrangements will be made by civil administration.

7.6  P.O.L ARRANGEMENTS FOR VEHICLE

The P.O.L arrangements for departmental vehicle will be arranged by Irrigation Department and other Departments will arrange P.O.L for their vehicles by Civil Administration.

7.7  TRANSPORTATION

The transportation for flood emergency / relief works will be provided by Civil Administration.

XEN KASUR

25

7.8  LAW AND ORDER

Law and order situation will be tackled by the by Civil Administration, Pak Ranger and Pak Army.

7.9  MEDICAL ARRANGEMENTS FOR LABOUR

Health Department will have its own arrangements to provide all such of the medical facilities at the spot.

7.10  LIAISON WITH OTHER DEPARTMENT

The Sub Divisional Officer Chunian will act as Liaison Officer for District Kasur and Sub Division Officer Kanganpur for District Okara. The Executive Engineer will act as Coordinator for all other Departments. The Liaison Officer will keep informed about the River gauges with passing discharge at various points in their jurisdiction to Civil as well as the Departmental Offices.

7.11  ROLE OF ARMY

Besides arrangements of watching staff by Irrigation Department, additional volunteers will be requisitioned from the Pak Army on special request. They will also take position for the rescue of the peoples and live stock of flood effected areas on request of Civil Administration.

7.12  DUTIES OF TELEPHONE ATTENDANT

During the flood days as communication is important one, so the communication is recommended at the Divisional Office Kasur as base station with police communication at the following stations.

Talwar Post, Kikar Post, Bakerke Rest House, Fateh Muhammad Canal Rest House and Attari Ranger Post. The telephone attendant will communicate the massages of flood emergency to Pak Army and other departments at 24 Hours.

7.13  WIRELESS ARRANGEMENTS

Base Stations at Kasur, Khudian, Kanganpur and Hira Singh Wala will be established and Mobile Wireless will be installed on Govt. Vehicles during Flood Season. Also Wireless Stations will be established by Police at Talwar Post, Kikkar Post , Bakerke Rest House and Fateh Muhammad Rest House.

XEN KASUR

26

CHAPTER – 8

DETAIL OF ENCROACHMENTS

There is no encroachment on embankments bunds in Kasur Division DCC, Kasur.

| TOTAL ENCROCHMENT | REMOVED | REMARKS |
| --- | --- | --- |
| Nil | Nil | Nil |

XEN KASUR

27

CHAPTER – 9

DUTY ROSTER / FLOOD FIGHTING PROGRAME	At Low flood

| 0600 Hrs to 1400 Hrs | 1400 Hrs to 2200 Hrs | 2200 Hrs to 0600 Hrs |
| --- | --- | --- |

| Sr. No. | Sub Division Section | Reach of Flood Bunds | Incharge of Watching Staff | W.C. Staff | Incharge of Watching Staff | W.C Staff | Incharge of Watching Staff | W.C Staff |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| I. U/S FEROZEPUR HEAD WORKS |
| 1. | Chunian GSW | Dhaya Bund with a Gauge of above 6.0 ft at Talwar Post | Sub Engineer Ganda singh wala | Mate 01 Nos Beldars 05 Nos. | Zilladar Khudian | Mate 01 Nos Beldars 05 Nos. | Sub Engineer Bedian | Mate 01 Nos Beldars 05 Nos. |
| 2. | Chunian GSW | Flood Bunds arround Ganda Singh Wala | Sub Engineer Ganda singh wala | Mate 01 Nos Beldars 05 Nos. | Zilladar Chunian | Mate 01 Nos Beldars 05 Nos. | Sub Engineer Bedian | Mate 01 Nos Beldars 05 Nos. |
| 3. | Chunian GSW | J –Head spur at pandoki out fall | Sub Engineer Ganda singh wala | Mate 0 No Beldars 05 No | Zilladar Chunian | Mate 0 No Beldars 05 No | Sub Engineer Kasur | Mate 0 No Beldars 05 No |
| Total Field Establishment Required at Low Flood (For 03 Shifts) | 01 No. Sub Engineers | Mate 02 No Beldars 15 No | 02 No. Zilladars | Mate 02No Beldars 15 No | 02 No. Sub Engineers | Mate 02No Beldars 15 No |
| G. Total | Total Sub Engineers. 03 + Zilladar. 02 + Mate. 06 + Beldar. 45= 56 |
| II. D/S FEROZEPUR HEAD WORKS |
| 4. | Khudian Bakerke | RD.136-156 +860 Depalpur Canal & Lower Ganja Minor RD.0+000to42+850&Lower Ganga sub minor RD. 0+000to10+200 | Sub Engineer Bakerke | Mate 0 No Beldars 05 No. | Sub Engineer Jajjal Section | Mate 01 No Beldars 05 No. | Sub Engineer Chunian | Mate 0 No Beldars 05 No. |
| 5. | Khudian Bakerke | J-Head spur opposite villege Atter singh wala | Sub Engineer Bakerke | Mate 01 No Beldars 05 No. | Sub Engineer Jajja Section | Mate 01 No Beldars 05 No. | Sub Engineer Chunian | Mate 01 No Beldars 05 No. |
| 6. | Kanganpur FMD | Fateh Muhammad Disty RD.0-88+600 | Sub Engineer Fateh Mohd | Mate 01No Beldars 08 No. | Sub Engineer Ladian Section | Mate 01No Beldars 08 No. | Sub Engineer Hira Singh Section | Mate 01No Beldars 08 No. |
| 7. | Kanganpur FMD | Lallugudar Disty RD.32+000-94+500 & Kanda Minor RD.0+000-14+300 | Sub Engineer Fateh Mohd | Mate 01No Beldars 08 No.. | Sub Engineer Ladian Section | Mate 01No Beldars 08 No.. | Sub Engineer Hira Singh Section | Mate 01No Beldars 08 No.. |
| 8. | Kanganpur FMD | J-Spur at RD.30+300 FMD (RD 0-4700 ft ) | Sub Engineer Fateh Mohd | Mate 0 No Beldars 05 No. | Sub Engineer Ladian Section | Mate 0 No Beldars 05 No. | Sub Engineer Hira Singh Section | Mate 0 No Beldars 05 No. |
| 9. | Kanganpur FMD | J-Spur at RD.50+400 FMD (RD 0-3850 ft ) | Sub Engineer Fateh Mohd | Mate 0 No Beldars 03 No. | Sub Engineer Chorkot section | Mate 0 No Beldars 03 No. | Sub Engineer Hira Singh Section | Mate 0 No Beldars 03 No. |
| 10. | Kanganpur FMD | Sloping Spur at RD.54+460 FMD (RD 0-950 ft ) | Sub Engineer Fateh Mohd | Mate 0 No Beldars 04 No. | Sub Engineer Chorkot section | Mate 0 No Beldars 04 No. | Sub Engineer kanganpur Section | Mate 0 No Beldars 04 No. |
| 11. | Kanganpur FMD | J-Spur at RD.30+300 FMD (RD 0-4700 ft ) | Sub Engineer Fateh Mohd | Mate 01 No Beldars 05 No. | Sub Engineer Chorkot section | Mate 01 No Beldars 05 No. | Sub Engineer kanganpur Section | Mate 01 No Beldars 05 No. |
| 12. | Kanganpur FMD | Attari Mole-Head spur at RD.3+380 Kanda Minor (RD0-5090 ft) | Sub Engineer Fateh Mohd | Mate 01 No Beldars 05 No. | Sub Engineer Chorkot section | Mate 01 No Beldars 05 No. | Sub Engineer kanganpur Section | Mate 01 No Beldars 05 No. |
| 13. | Kanganpur FMD | J-Head Spur of Kanda Minor at tail (0-5400 ft) | Sub Engineer Fateh Mohd | Mate 01 No Beldars 05 No. | Sub Engineer Chorkot section | Mate 01 No Beldars 05 No. | Sub Engineer kanganpur Section | Mate 01 No Beldars 05 No. |
| Total Field Establishment Required at Low Flood (For 03 Shifts) | 02 No. Sub Engineers | Mate 06 No Beldars 53 No | 03 No. Sub Engineers | Mate 07 No Beldars 53 No | 03 No. Sub Engineers | Mate 06 No Beldars 53 No |
| G. Total | Total Sub Engineers. 08 + Mate. 19 + Beldar. 159= 186. |
| Note:- In case of very high exceptionally flood extra-ordinary establishment and material for flood fighting will be arranged through contractor. |

XEN KASUR

28

DUTY ROSTER / FLOOD FIGHTING PROGRAME	At Medium flood

| 0600 Hrs to 1400 Hrs | 1400 Hrs to 2200 Hrs | 2200 Hrs to 0600 Hrs |
| --- | --- | --- |

| Sr. No. | Sub Division Section | Reach of Flood Bunds | Incharge of Watching Staff | W.C. Staff | Incharge of Watching Staff | W.C Staff | Incharge of Watching Staff | W.C Staff |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| I. U/S FEROZEPUR HEAD WORKS |
| 1. | Chunian GSW | Dhaya Bund with a Gauge of above 6.0 ft at Talwar Post | Sub Engineer Ganda singh wala | Mate 02Nos Beldars 20 Nos. | Zilladar Khudian | Mate 02Nos Beldars 20 Nos. | Sub Engineer Bedian | Mate 02Nos Beldars 20 Nos. |
| 2. | Chunian GSW | Flood Bunds arround Ganda Singh Wala | Sub Engineer Ganda singh wala | Mate 04 Nos Beldars 40Nos. | Zilladar Chunian | Mate 04 Nos Beldars 40Nos. | Sub Engineer Bedian | Mate 04 Nos Beldars 40Nos. |
| 3. | Chunian GSW | J –Head spur at pandoki out fall | Sub Engineer Ganda singh wala | Mate 02Nos Beldars 20 Nos. | Zilladar Chunian | Mate 02Nos Beldars 20 Nos. | Sub Engineer Kasur | Mate 02Nos Beldars 20 Nos. |
| Total Field Establishment Required at Medium Flood (For 03 Shifts) | 01 No. Sub Engineers | Mate 8 No Beldars 80 No | 02 No. Zilladars | Mate 08 No Beldars 80 No | 02 No. Sub Engineers | Mate 08 No Beldars 80 No |
| G. Total | Total Sub Engineers. 03 + Zilladars. 02 + Mate. 24 + Beldar. 240= 269 |
| II. D/S FEROZEPUR HEAD WORKS |
| 4. | Khudian Bakerke | RD.136-156 +860 Depalpur Canal & Lower Ganja Minor RD.0+000to42+850&Lower Ganga sub minor RD. 0+000to10+200 | Sub Engineer Bakerke | Mate 02 Nos Beldars 20 No. | Sub Engineer Jajjal Section | Mate 02 Nos Beldars 20 No. | Sub Engineer Chunian | Mate 02 Nos Beldars 20 No. |
| 5. | Khudian Bakerke | J-Head spur opposite villege Atter singh wala | Sub Engineer Bakerke | Mate 02 No Beldars 20 No. | Sub Engineer Jajja Section | Mate 02 No Beldars 20 No. | Sub Engineer Chunian | Mate 02 No Beldars 20 No. |
| 6. | Kanganpur FMD | Fateh Muhammad Disty RD.0-88+600 | Sub Engineer Fateh Mohd | Mate 02Nos Beldars 36 No. | Sub Engineer Ladian Section | Mate 02Nos Beldars 36 No. | Sub Engineer Hira Singh Section | Mate 02Nos Beldars 36 No. |
| 7. | Kanganpur FMD | Lallugudar Disty RD.32+000-94+500 & Kanda Minor RD.0+000-14+300 | Sub Engineer Fateh Mohd | Mate 03 No Beldars 32 No. | Sub Engineer Ladian Section | Mate 03 No Beldars 32 No. | Sub Engineer Hira Singh Section | Mate 03 No Beldars 32 No. |
| 8. | Kanganpur FMD | J-Spur at RD.30+300 FMD (RD 0-4700 ft ) | Sub Engineer Fateh Mohd | Mate 02 No Beldars 20 No. | Sub Engineer Ladian Section | Mate 02 No Beldars 20 No. | Sub Engineer Hira Singh Section | Mate 02 No Beldars 20 No. |
| 9. | Kanganpur FMD | J-Spur at RD.50+400 FMD (RD 0-3850 ft ) | Sub Engineer Fateh Mohd | Mate 01 No Beldars 14 No. | Sub Engineer Chorkot section | Mate 01 No Beldars 14 No. | Sub Engineer Hira Singh Section | Mate 01 No Beldars 14 No. |
| 10. | Kanganpur FMD | Sloping Spur at RD.54+460 FMD (RD 0-950 ft ) | Sub Engineer Fateh Mohd | Mate 0 No Beldars 8No. | Sub Engineer Chorkot section | Mate 0 No Beldars 8No. | Sub Engineer kanganpur Section | Mate 0 No Beldars 8No. |
| 11. | Kanganpur FMD | J-Spur at RD.30+300 FMD (RD 0-4700 ft ) | Sub Engineer Fateh Mohd | Mate 02 No Beldars 20 No. | Sub Engineer Chorkot section | Mate 02 No Beldars 20 No. | Sub Engineer kanganpur Section | Mate 02 No Beldars 20 No. |
| 12. | Kanganpur FMD | Attari Mole-Head spur at RD.3+380 Kanda Minor (RD0-5090 ft) | Sub Engineer Fateh Mohd | Mate 02 No Beldars 20 No. | Sub Engineer Chorkot section | Mate 02 No Beldars 20 No. | Sub Engineer kanganpur Section | Mate 02 No Beldars 20 No. |
| 13. | Kanganpur FMD | J-Head Spur of Kanda Minor at tail (0-5400 ft) | Sub Engineer Fateh Mohd | Mate 02 No Beldars 20 No. | Sub Engineer Chorkot section | Mate 02 No Beldars 20 No. | Sub Engineer kanganpur Section | Mate 02 No Beldars 20 No. |
| Total Field Establishment Required at Medium Flood (For 03 Shifts) | 02 No. Sub Engineers | Mate 18 No Beldars 200 No | 03 No. Sub Engineers | Mate 18 No Beldars 200 No | 03 No. Sub Engineers | Mate 18 No Beldars 200 No |
| G. Total | Total Sub Engineers. 08 + Mate. 54 + Beldar. 600= 662 |
| Note:- In case of very high exceptionally flood extra-ordinary establishment and material for flood fighting will be arranged through contractor. |

XEN KASUR

29

DUTY ROSTER / FLOOD FIGHTING PROGRAME	At High Flood

| 0600 Hrs to 1400 Hrs | 1400 Hrs to 2200 Hrs | 2200 Hrs to 0600 Hrs |
| --- | --- | --- |

| Sr. No. | Sub Division Section | Reach of Flood Bunds | In charge of Watching Staff | W.C. Staff | In charge of Watching Staff | W.C Staff | In charge of Watching Staff | W.C Staff |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| I.U/S FEROZEPUR HEAD WORKS |
| 1. | Chunian GSW | Dhaya Bund with a Gauge of above 6.0 ft at Talwar Post | Sub Engineer Ganda singh wala | Mate 03 No Beldars 30 No | Zilladar Khudian | Mate 03 No Beldars 30 No | Sub Engineer Bedian | Mate 03 No Beldars 30 No |
| 2. | Chunian GSW | Flood Bunds arround Ganda Singh Wala | Sub Engineer Ganda singh wala | Mate 06No Beldars 60 No | Zilladar Chunian | Mate 06No Beldars 60 No | Sub Engineer Bedian | Mate 06No Beldars 60 No |
| 3. | Chunian GSW | J –Head spur at pandoki out fall | Sub Engineer Ganda singh wala | Mate 03 No Beldars 30 No | Zilladar Chunian | Mate 03 No Beldars 30 No | Sub Engineer Kasur | Mate 03 No Beldars 30 No |
| Total Field Establishment Required at High Flood (For 03 Shifts) | 01 No. Sub Engineers | Mate 12 No Beldars 120 No | 02 No. Zilladars | Mate 12 No Beldars 120 No | 02 No. Sub Engineers | Mate 12 No Beldars 120 No |
| G. Total | Total Sub Engineers. 03 + Zilladars. 02 + Mate. 36 + Beldar. 360= 401 |
| II. D/S FEROZEPUR HEAD WORKS |
| 4. | Khudian Bakerke | RD.136-156 +860 Depalpur Canal & Lower Ganja Minor RD.0+000to42+850&Lower Ganga sub minor RD. 0+000to10+200 | Sub Engineer Bakerke | Mate 06No Beldars 60 No | Sub Engineer Jajjal Section | Mate 06No Beldars 60 No | Sub Engineer Chunian | Mate 06No Beldars 60 No |
| 5. | Khudian Bakerke | J-Head spur opposite villege Atter singh wala | Sub Engineer Bakerke | Mate 03 No Beldars 30 No | Sub Engineer Jajja Section | Mate 03 No Beldars 30 No | Sub Engineer Chunian | Mate 03 No Beldars 30 No |
| 6. | Kanganpur FMD | Fateh Muhammad Disty RD.0-88+600 | Sub Engineer Fateh Mohd | Mate 05No Beldars 54 No | Sub Engineer Ladian Section | Mate 05No Beldars 54 No | Sub Engineer Hira Singh Section | Mate 05No Beldars 54 No |
| 7. | Kanganpur FMD | Lallugudar Disty RD.32+000-94+500 & Kanda Minor RD.0+000-14+300 | Sub Engineer Fateh Mohd | Mate 04 No Beldars 48 No. | Sub Engineer Ladian Section | Mate 04 No Beldars 48 No. | Sub Engineer Hira Singh Section | Mate 04 No Beldars 48 No. |
| 8. | Kanganpur FMD | J-Spur at RD.30+300 FMD (RD 0-4700 ft ) | Sub Engineer Fateh Mohd | Mate 03 No Beldars 30 No | Sub Engineer Ladian Section | Mate 03 No Beldars 30 No | Sub Engineer Hira Singh Section | Mate 03 No Beldars 30 No |
| 9. | Kanganpur FMD | J-Spur at RD.50+400 FMD (RD 0-3850 ft ) | Sub Engineer Fateh Mohd | Mate 02No Beldars 21 No. | Sub Engineer Chorkot section | Mate 02No Beldars 21 No. | Sub Engineer Hira Singh Section | Mate 02No Beldars 21 No. |
| 10. | Kanganpur FMD | Sloping Spur at RD.54+460 FMD (RD 0-950 ft ) | Sub Engineer Fateh Mohd | Mate 01 No Beldars 12 No. | Sub Engineer Chorkot section | Mate 01 No Beldars 12 No. | Sub Engineer kanganpur Section | Mate 01 No Beldars 12 No. |
| 11. | Kanganpur FMD | J-Spur at RD.30+300 FMD (RD 0-4700 ft ) | Sub Engineer Fateh Mohd | Mate 03 No Beldars 30 No | Sub Engineer Chorkot section | Mate 03 No Beldars 30 No | Sub Engineer kanganpur Section | Mate 03 No Beldars 30 No |
| 12. | Kanganpur FMD | Attari Mole-Head spur at RD.3+380 Kanda Minor (RD0-5090 ft) | Sub Engineer Fateh Mohd | Mate 03 No Beldars 30 No | Sub Engineer Chorkot section | Mate 03 No Beldars 30 No | Sub Engineer kanganpur Section | Mate 03 No Beldars 30 No |
| 13. | Kanganpur FMD | J-Head Spur of Kanda Minor at tail (0-5400 ft) | Sub Engineer Fateh Mohd | Mate 03 No Beldars36 No. | Sub Engineer Chorkot section | Mate 03 No Beldars36 No. | Sub Engineer kanganpur Section | Mate 03 No Beldars36 No. |
| Total Field Establishment Required at High Flood (For 03 Shifts) | 02 No. Sub Engineers | Mate 33 No Beldars 351 No | 03 No. Sub Engineers | Mate 33 No Beldars 351 No | 03 No. Sub Engineers | Mate 33 No Beldars 351 No |
| G. Total | Total Sub Engineers. 08 + Mate. 99 + Beldar. 1053=1160 |
| Note:- In case of very high exceptionally flood extra-ordinary establishment and material for flood fighting will be arranged through contractor. |

XEN KASUR

30

CHAPTER – 10

EMERGENCY TELEPHONE NUMBERS

| Sr. No. | Name of Officer | Telephone Numbers |
| --- | --- | --- |
|  |  | Office | Residence |
| 1. | Chief Engineer, Irrigaiton Lahore Zone Lahore | 042-99212086 042-99212085 | Fax:042-212084 |
| 2. | Chief Engineer, Drainage & Flood Lahore. | 042-99230602 | 042-5760127 |
| 3. | Malik Sarfraz , Superintending Engineer, Depalpur Canal Circle, Lahore. | 042-99250307 | 0300-5459697 |
| 4. | Executive Engineer, (OP) Lahore Irrigation Zone Lahore. | 042-99212089 |  |
| 5. | Muhammad Shaban Ghulam Nabi Executive Engineer, Kasur Division DCC, Kasur. | 049-9250141 049-9250201 | 0333-4787659 |
| 6. | Director Floods Lahore / Secretary Flood Commission Punjab, Lahore. | 042-99231614 | - |
| 7. | Executive Engineer (OP) Scarp | 042-99212089 | - |
| 8. | Flood Warning Centre Lahore | 042-7572091-93 | - |
| 9. | Mr. Saleem Akhter Sub Divisional Officer Chunian Head Quarter at Kasur | 049-9250201 | 0306-8898365 |
| 10. | Mr. Asher Latif Mehar, Sub Divisional Officer Khudian Sub Division | - | 0334-4353036 |
| 11. | Abdul Hakeem Sub Divisional Officer, Kangnapur Sub Division. | - | 0300-7745337 |
| 12. | Duty Clerk Flood Emergency Kasur Division. | 049-9250141 | - |
| 13. | Muhammad Rauf, Ganda Singh Wala Section | 049-9250141 | 0302-9280655 |
| 14. | Umair Aslam Sub Engineer Bakerke Section | 049-9250141 | 0305-7669904 |
| 15. | Hafiz Mubasher Sub Engineer, Fateh Muhammad Section | - | 0322-8079598 |

XEN KASUR

31

CIVIL AUTHORITES

| 16. | Deputy Commissioner, Kasur. | 049-9250140 | 049-9250143 |
| --- | --- | --- | --- |
| 17. | Deputy Commissioner, Okara | 044-9200026 | 044-9200027-28 |
| 18. | D.O.(R) Okara | 044-9200251 | 044-9200460 |
| 19. | Superintending Police, Okara | 044-9200351 | 044-9200353 |
| 20 | Deputy Superintending of Police Depalpur | 044-540406 |  |
| 21 | Deputy District Officer (Revenue), Kasur. | 049-9250156 | - |
| 22 | Superintending Police, Kasur. | 049-9250137 | 049-2764492 |
| 23 | Police Station Ganda Singh Wala, Kasur. | 049-2711420 | - |
| 24 | Police Wireless Control, Kasur. | 049-9250071 | - |

XEN KASUR

32

CHAPTER – 11

STANDARD OPERATING PROCEDURE(SOP) FOR BREACHING SECTIONS

11.1	HISTORY OF THE BREACHING SECTION

It is certified that there is no breaching section in Kasur Division DCC, Kasur.

11.2	LOCATION, DESIGN, QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATION.

Not Applicable.

11.3	ARRANGEMENT OF EXPLOSIVES AND SECURITY OF EXPLOSIVE SOURS

Not Applicable

11.4	LIST OF THE SECURITY STAFF ALONGWITH DETAIL OF THEIR TRAINING ETC

Not Applicable

11.5	DETAIL OF MACHINERY MEANS AS A STANDBY ARRANAGMENTS IN CASE OF DETONATION FAILURE

Not Applicable

11.6	DUTY ROSTER IN CASE OF CRITICAL SITUATION

Not Applicable

XEN KASUR

33

11.7 BREACHING COMMITTEE WITH THEIR ACTION PLAN

Not Applicable.

11.8 LIST OF VILLAGES LIKELY TO BE INUNDATE IN CASE OF BREACH

Saifalian, Fatti Wala, Kamalpura, Bangladesh, Bhekiwind, Sheikhupura Kohna, Sheikhpura Nau, Raji Wala, Mahalam Kalan, Bhedian Kalan, Bhedian Khurad, Ganda Singh Wala, Sanda Nizam, Churi Wala, Burjh, Doni Ullake, Kujian Wala, Jume Wala, Walay Wala, Kharapar, Noori Wala, Bhedian Usman, Attar Singh Wala, Rajowal, Nijabat, Fateh Muhammad.

11.9	ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENT

All announcements regarding evacuation will be made through District Administration by electronic media radio, local Mosque and Loud speakers etc.

11.10 DETAIL OF COORDINATION WITH CIVIL / ARMY AUTHORITIES

Not Applicable.

11.11 PARALLEL COMMUNICATION ARRANGEMENTS

All communication will be made on wireless, special messengers and telephones mobile phones etc.

XEN KASUR

34

11.12 INDEX PLAN

XEN KASUR

35

EMERGENCY CONTINGENCY PLAN

PART – B

FLOOD FIGHTING PLAN

FOR THE YEAR 2024

Executive Engineer		 Supeintending Engineer	   Chief Engineer

Kasur Division DCC		 Depalpur Canal Circle		   Irrigation Lahore Zone

Kasur				 Lahore				   Lahore

CHAPTER.12

VULNERABLE SITES ON FLOOD BUND/STRUCTURES

12.1 -   APPREHENDED BREACHES IN FLOOD BUNDS /    STRUCTURES

Following is vulnerable site on Flood Bund in Kasur Division DCC Kasur.

(i)- Right Retired Embankment RD. 0+000 To 7+500 (1.5 miles.)

12.2 - Operation of Breaching Section

NOT APPLICABLE

12.3 - Breaches due to rise of floodwater, deterioration of flood bunds.

No bund except the one mentioned above may breach ever in exceptionally high floods.

XEN KASUR

36

XEN KASUR

37

CHAPTER # 13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITE (SITES)

13.1- PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVEL

Plan Attached.

13.2 - DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED

Sanda Nizam, Fatohi Wala, Kujjian Wala, Ullake, Churiwala, Walle wala.

13.3 - STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL.

13.3.1-  Arrangements.

13.3.2- Establishment of Flood fighting Camps.

F.E.C – I	As soon as the gauge rises to 6.0 (W.L 652.00), Sub Engineer Ganda Singh Wala Section will shift his head quarter from Ganda Singh Wala Canal Rest House to Talwar Post at Right Marginal Bund.

F.E.C – II 	When the gauge at Kikar Ranger Post shell rises above 8.0 (R.L 654.00), the Sub Divisional Officer Chunian will shift his camp at Ganda Singh Wala and supervises the watching of Bunds around Ganda Singh Wala with assistance of Sub Engineer Chorkot Section and Zialladar Khudian along with the watching staff.

F.E.C – III	As soon as the river gauge at Bakarke Gauge Station rises above 17.70 ft., the Sub Divisional Officer Khudian will shift his camp at Bakarke Rest House along with Sub Engineer Bakarke Section incharge of Campus will also present in section, Sub Engineer Jajjal & Zilladar Jajjal for his assistance in order to watch the channels day / night.

F.E.C – IV	when the river gauge at Bakarke rises upto 15.0 ft., the Sub Divisional Officer Kanganpur Sub Division will shift his camp at Fateh Muhammad Canal Rest House. The Sub Engineer FMD will incharge of camp Sub Engineer Kanganpur, Hira Singh and Zilladar Fateh Muhammad will assist him day / night.

13.3.3- Duties of officers/Officials and their camp sites.

The sub Engineer Ganda Singh Wala section under the control of Sub Divisional Officer Chunian Sub Division shall be the incharge of camp site.

His contact No. is given below:-

Name: -			Muhammad Rauf

Cell No. : -		  	0302-9280655

Work Charged Beldars:   	30 No. in three shifts.

Mates:				03 No. in three shifts.			XEN KASUR

38

13.34 - Departmental Machinery available.

No Government Machinery is available and it may be arranged through private resources as per requirement.

13.3.5 - Machinery available from Private source.

Name of contractor:  		Jutt Brothers Govt Contractor.

Contact No. 		 	0301-6839700

Location.			59-Munir Shaheed Colony, Kasur.

Excavator Machine		= 04 No.

Tractor with Front Blade	= 06 No.

Tractor with Trollies		= 8 No

XEN KASUR

39

13.3.6    STATUS OF FLOOD FIGHTING MATERIAL

| Sr. No | Name of article | Total Required quantity | Availabe quantity | deficent quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | Manila Rope ( Kg) | 100 | Nil | 100 | The balance material will be procured before the start of flood season 2024 subjected to the availabiliy of funds |
| 2 | G.I. Wire (Kg) | 500 | Nil | 500 |  |
| 3 | PVC Cable Single core 7.029” ( Mtr ) | 500 | Nil | 500 |  |
| 4 | Switch Board (No) | 8 | Nil | 8 |  |
| 5 | Bamboos 12-14 ft (No) | 1000 | Nil | 1000 |  |
| 6 | Sutli Seba (Kg) | 27.5 | Nil | 27.5 |  |
| 7 | Torches ( 3 Cell) | 95 | 10 | 85 |  |
| 8 | Cell (Dozen) | 67 | Nil | 67 |  |
| 9 | Kassi (No) | 500 | 100 | 400 |  |
| 10 | Bucket (No) | 170 | 40 | 130 |  |
| 11 | Basket (No) | 1000 | 100 | 900 |  |
| 12 | Plastic Bag (No) | 10000 | 2000 | 8000 |  |
| 13 | Shouldary (No) | 14 | 3 | 11 |  |
| 14 | Swiss Cotage | 7 | 1 | 6 |  |

XEN KASUR

40

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUIGAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDING, CANALS AND DRAINAGE NETWORK

INFRASTRUCTURES

Canals

Depalpur Canal & its System

Ferozepur Road.

Schools / Colleges

Government  Boys and girls High School Ganda Singh Wala

Government  Girls Middle School Fatohi Wala.

Government  Boys  Primary School Fatohi Wala.

Govt. Girls and Boys Primary School Kujian Wala.

Health Centre

Rural Health Centre Ganda Singh Wala

Police Station

Police Station Ganda Singh Wala

Telephone Exchanges.

Nil

Army Infrastructures

Ranger Head Quarter Kasur,

Company Headquarter Kasur

Ranger Post Sanda Nizam, Hanif Shaheed Check Post.

Grid Station.

Nil

Note:  Pandoki Canal Division at Bhambha, Lahore will act as back up Division in case of emergency.

XEN KASUR

41

CHAPTER - 14

ACTION PLAN

14.1	RE-SHUFFLING / RECOUPING PLAN OF RESERVE STOCK OF STONE DEPARTMENTALLY.

There is a necessity of RE-SHUFFLING / RE-STACKING OF RESERVE STOCK OF STONE on FMD J-Head spur RD 30+300 most of which has been settled under the spur.

XEN KASUR

42

14.2	DETAIL OF INLET AND OUTLET CROSSING ALONGWITH

CLOSING METHODOLOGY.

No any inlet and outlet crossing

14.3 DEPLOYMENT OF MACHINERY (Medium to High Flood).

| Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site In-charge by name & Cell No. | Machinery Deployed |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Excavator | Dozer | Trolleys / Dumpers | Tractor with front blade | Labour (Beldar + Mate) | Availability of Stone lacCft |
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Railwey Gude Bund spur) | 1.50 | RD.0-7500 | Talwar post | Sub Engineer Ganda sinh wala Section | 1 | 1 | 4 | 2 | 100+10 | (0.60000) |
| Total | 1.50 |  |  |  | 1 | 1 | 4 | 2 | 100+10 |  |

14.4 	DEPLOYMENT OF MACHINERY (High to Very High Flood).

| Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site In-charge by name & Cell No. | Machinery Deployed |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Excavator | Dozer | Trolleys / Dumpers | Tractor with front blade | Labour (Beldar + Mate) | Availability of Stone lacCft |
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Railwey Gude Bund spur) | 1.50 | RD.0-7500 | Talwar post | Sub Engineer Ganda sinh wala Section | 2 | 2 | 5 | 3 | 150+10 | (0.60000) |
| Total | 1.50 |  |  |  | 2 | 2 | 5 | 3 | 150+10 |  |

14.5 DEPLOYMENT OF MACHINERY (High to Exceptionally High Flood).

| Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site In-charge by name & Cell No. | Machinery Deployed |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Excavator | Dozer | Trolleys / Dumpers | Tractor with front blade | Labour (Beldar + Mate) | Availability of Stone lacCft |
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Railwey Gude Bund spur) | 1.50 | RD.0-7500 | Talwar post | Sub Engineer Ganda sinh wala Section | 3 | 3 | 6 | 4 | 200+10 | (0.60000 |
| Total | 1.50 |  |  |  | 3 | 3 | 6 | 4 | 200+10 |  |

Note: Payment for Machinary and work charge Employees subject to verificaton by Third Party Monitoring (TPM)/Departmental Committee.

XEN KASUR

43

LIST OF LOCAL CONTRACTORS

| Name of Govt. Contractor | Contact Number | Remarks |
| --- | --- | --- |
| Sardar Ali & Co. | 0344-4725851 | Excavators and other machinery may be made available through these contractors. |
| Jutt Brothers | 0302-6808250 |  |
| Jawad Enterprises | 0301-6808012 |  |

14.6 	POLICE DEPLOYMENT PLAN

Proforma – 1

| Sr. | Site of Breaching Section | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / Sub Inspector / A.S.I | Constable |  |
| Not Applicable |

Proforma – 2

| Sr. | Vulnerable sites used for illegal cuts during floods | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / Sub Inspector / A.S.I | Constable |  |
| 1 | Right Retired Embankment Rd. 0+000 To 7+500 | Kasur Division DCC kasur. | Ganda Singh Wala Police Station Distt: Kasur | ASI=2 | 5 | -- |

XEN KASUR

44

Proforma – 3

| Sr. | Name of Barrage | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector / Sub Inspector / A.S.I | Constable |  |
| Not Applicable |

14.7. DETAIL OF SYNTHETIC BAGS WITH CAPACITY OF 500 KG AND 1000 KG.

1.	Synthetic Bags with capacity 500 KG				=3000 No

2.	Synthetic Bags with capacity 1000 KG				=1500 No.

| 1000 kg | 500 kg |
| --- | --- |
| Required (No.) | Availabe | Balance | Required (No.) | Availabe | Balance |
| 1500 | Nil | 1500 | 3000 | Nil | 3000 |

Note. The balance quantity will be procurred on subject to avalability of funds before on set of floood season.

14.8. DETAIL OF POLYTHENE SHEETS OF BLACK COLOUR TO PROTECT UPSTREEM SLOPE AGAINST WAVE ACTION AND TO CONTROL SEEPAGE THROUGH EMBANKMENT.

Polythene sheets of black color for protecting upstream slopes

Waves and control to seepage   (Average 20 FT Width) 	21000 Rft

| Polythene sheets of black color for protecting upstream slopes Waves and control to seepage (Average 20 FT Width) |
| --- |
| Required Rft | Availabe Rft | Balance Rft |  |
| 21000 | Nil | 21000 |  |

Note. The balance quantity will be procurred on subject to avalability of funds before on set of floood season

XEN KASUR

45

CHAPTER - 15

BACK UP DIVISIONS (IN CASE OF BREACH)

In case of emergency Depalpur  Canal Circle and Pandoki Canal Division will be back-up divisions for Right Flank of River Sutlej at upstream Ganda sing wala Headworks while Lahore Canal Division Depalpur  Canal Circle will be backup divisions for Left Flank of River Sutlej at Ganda singh wala Headworks.

Executive Engineer		Supeintending Engineer		Chief Engineer

Kasur Division DCC		Depalpur Canal Circle			Irrigation Lahore Zone

Kasur				Lahore					Lahore

XEN KASUR

46

# Text boxes

Executive Engineer

Kasur Division DCC KASUR,

Kasur.

Sub Divisional Officer,

Khudian Sub Division

Sub Divisional Officer

Chunian Sub Division

Sub Divisional Officer,

Kanganpur Sub Division

Ganda Singh Wala Section

Hira Singh Section

Kanganpur Section

Fateh Muhammad ection

Bakerke Section

Jajjal Section

Ladian Section

Bedian Section

Kasur Section

Chunian  Section

Chorkot Section