PART – A

CHAPTER-1

SALIENT FEATURE OF DIVISION

Jhang Canal Division is one of the Divisions of Lower Chenab Canal West Circle, Faisalabad Zone and started its function from 17-08-1911. It irrigates the area under the command of Bhowana Branch and Jhang Branch Lower Canal System. Out of an area of 678,489 acres GCA, 533,366 acres CCA of District Faisalabad, Jhang, Chiniot and Toba Tek Singh falls in the jurisdiction of Jhang Canal Division. Irrigation system of division comprises of two Branch Canals off taking from Tail of Jhang Branch Upper named as Jhang Branch Lower and Bhowana Branch Canal and its Sub System of Channels consist of 31 number distributaries and 42 number minors. It comprises of four Sub Divisions headed by the Sub Divisional Officers, namely; Wer, Dhaular, Veryam & Flood Bund.

In addition to above mentioned canal system there are three Flood Bunds as following:-

- Jhang Flood Protection Bund

- Thatta Mahla flood bund

- Loop Bund

These Bunds were constructed by the Irrigation Department during the years 1950 & 1959, to check the spill of River Chenab entering in Jhang Sadar and the other abadies of Jhang City with the total length of 26.70 miles.

Thatta Mahla flood Bund was constructed to save the Jhang City, valuable crops and vital installations. The said Flood Bund breached during the Flood of 1973 and major damages occurred in the Jhang City. To improve the condition of the Flood Bund, it was remodeled and its top level was raised up to a free board of 5` above High flood level of 1973.  Loop Bund is a second defence line for the Thatta Mahla Flood Bund. It starts from RD. 1500 Thatta Mahla Flood Bund and terminates at RD. 11500 adopting a shape of Loop.

AREA UNDER COMMAND OF JHANG DIVISION

|  | G.C.A (In acres) | C.C.A (In acres) | G.A (In acres) | Fish Forms (In acres) |
| --- | --- | --- | --- | --- |
| Total Area under the Division | 678489 | 533366 | - | - |
| EXISTING AREA |  |  |  |  |
| Wer Sub Division | 191752 | 154303 | 491.49 | - |
| Dhaular Sub Division | 262189 | 204676 | 2427.52 | 2.16 |
| Veryam Sub Division | 224548 | 174387 | 4301.08 | 8.50 |
| Flood Bund Sub Division | - | - | - | - |
| Total Area of Division | 678489 | 533366 | 7220.09 | 10.66 |

DISTRICT WISE AREA IN JHANG DIVISION

  - LOCATION:

THATTA MAHLA BUND

This Bund was constructed during the year 1950 to check the spill of River Chenab upstream Revaz Bridge entering Jhang City and adjoining abadies. This Bund starts from Kilometer  16  of Jhang Chund Railway line and terminates at RD: 126000 of Sultan Pakhra Disty: Total length of the Bund is 10.20 Miles with its Zero at Railway Line.

JHANG FLOOD PROTECTION BUND

This Bund is in continuation of left marginal Bund of Trimmu Head Works and was constructed during the year 1950 to check the spill of River Chenab downstream Revaz Bridge entering Jhang Town and adjoining Abadies.    This   also   saves Jhang Multan Road from inundation.  The total length of the Bund is 14.20 miles. Wetting Channel is also exist from RD 0+000 – 15+000.

LOOP BUND

This Bund was constructed by the Irrigation Department in the year 1959 to function as a Second Defense Line to Thatta Mahla Bund in the dangerous reach RD: 1500 to 11500.  This Bund has also been renovated during the year 1981-82 with 20’ top width and 6.0’ free board above H.F.L of 1973.  A wetting channel also exists along this Bund.

  - GENERAL DESCRIPTION:

THATTA MAHLA BUND

The Bund was constructed by the Irrigation Department during 1950.  The Bund was breached during flood 1973 and caused heavy damages to Jhang Town and other important installations.  To improve the parameters of the Bund, it was strengthened and raised so as to provide a free board of 5.00ft above H.F.L of flood 1973.  After the experience of floods of 1976, the Government decided to further strengthen the Bund with a free Board of 6.0ft instead of 5.0ft.

WETTING CHANNEL:

Wetting Channel along this Bund exists from RD: 12+000 to 20+000 so as to detect any defects in the Bund before the actual Floods. 2 No. T/Wells at RD: 16+000 and 19+000 each of 0.5 Cs capacities have been installed for filling the wetting channel.

LOOP BUND

This Bund was constructed by the Irrigation Department in the year 1959 to function as a Second Defense Line to Thatta Mahla Bund in the dangerous reach RD: 1500 to 11500.  This Bund has also been renovated during the year 1981-82 with 20’ top width and 6.0’ free board above H.F.L of flood 1973.  A wetting channel also exists along this Bund.

JHANG FLOOD PROTECTION BUND

This Bund is a continuation of left marginal Bund of Trimmu Head Works and was constructed during the year 1950 to check the spill of River Chenab downstream Revaz Bridge entering Jhang Town and adjoining Abadies.    This   also   saves Jhang Multan Road from inundation. The total length of the Bund is 14.20 miles.

During the unpredicted Flood of 1973, the water entered from the breaches of Thatta Mahla Bund and Loop Bund after inundating Jhang Town accumulated on country side along this Bund. When the River subsided, the water level in the city side was 4.0; higher than river side. This Bund was cut between RD: 22-33 to release the pressure on the city side.  The following improvements in the Bund have been made after the Flood of 1973, 1975, 1976 & 1977.

(i)	Drainage culverts with sluice valves have been constructed between RD: 22-33 to drain out rain water and affluent of Jhang Town.

(ii)			Old T/Wells crossings have been replaced with 		R.C.C. pipe crossings fitted with sluice valves.

(iii)			During the Floods of 1975 and 1976, seepage 						occurred between RD: 25-27, 39-41 and   45-						48 and sloughing of slopes were noticed.  A 						pushta to cover the Hydraulic Gradient has 						since been provided in these reaches.

(iv)	During flood 2014, breach occurred between RD 1+000 to 2+000 of Jhang Flood Protection Bund, which was restored to its original design.

More over the Khairwala Main Drain takes right hand turn opposite RD: 29000 of Jhang Flood Protection Bund and outfalls into River Chenab.  During the Flood of even medium intensity, the water flows back into the drain and flows down in depression along Flood Protection Bund.

During the flood 1997 a heavy flow had been flowing in the toe of the Bund.  Village Road bridge opposite RD: 27-28 of Jhang Flood Bund has been constructed by union council No. 13 under Matching Grant Scheme.

The bridge was constructed with a very tight waterway of only 24ft in the Channel of 250ft wide.  Inclination of bridge at 42 degree with Flood Bund alignment results in jet like passage of water through Bridge and directly hits to Flood Bund.

During flood season 2014 an unprecedented / exceptionally high flood generated at Maralla Headworks with peak discharge of 861464 Cusecs at 20:00 hours on 06.09.2014 against 838990 cusecs during 1992. At Khanki Head works, a discharge of 947099 Cusecs passed on 07.09.2014 at 08:00 hour against 864000 Cusecs during 1973 and 910512 cusecs during 1992. At Qadriabad 903540 Cusecs discharge passed on 07.09.2011at 11:00 hours against 854000 Cusecs during 1973 and 948446 cusecs during 1992.

A parallel flow was observed from RD: 47+500 to RD: 0+000 and the water level rose abnormally high due to unprecedented flood in River Chenab. Jhang city was under serious threat during flood 2014 due to insufficient design criteria. The Jhang by-pass road has been constructed at the top of Jhang Flood Bund from RD 18+000 to 52+500 and the river side slope is badly short in this reach i-e 1:1 against 3:1 which is alarming situation for such an exceptionally high flood.

In view of the sensitivity of site and protection of Jhang city, raising of Jhang Flood Protection Bund by 2 ft alongwith stone pitching from RD 18+000 to 56+500 is necessary to avoid any untoward situation in future. The strengthening of flood bunds has been executed by PIU. The following work executed by the PIU.

|  | Jhang Flood Protection Bund |  |
| --- | --- | --- |
| 1. | Strengthening of Jhang Flood Protection Bund | RD 0+000 to RD 71+000 |
| 2. | Pitching & stone Apron | RD 23+000 to 26+900,RD 44+000 to 48+500 |
| 3. | Pumping Station | 3 No. (4+000,8+000,13+000) |
|  | Thatta Mahla Flood Bund |  |
| 1. | Strengthening of Thatta Mahla Flood Bund | RD 0+000 – RD 51+000 |
| 2. | Sheet Pilling | RD 0+000 - RD 12+000 |
| 3. | Pumping Station ` | 2No. (RD 16+000,RD 19+000) |

  - ADMINISTRATIVE SETUP OF JHANG DIVISION.

Chapter-2

Flood Protection and River Training Works

  - DESIGN PARAMETERS OF TRAINING WORKS

DETAIL OF FLOOD PROTECTION BUNDS

1.	Thatta Mahla Bund.				RD: 0-51000 (About 10.2 miles)

2.	Loop Bund					RD: 0-11500 (About 2.3 miles)

3.	Jhang Flood Protection Bund 		RD: 0-71000 (About 14.2 miles)

Total Length 		 			26.70	Miles

DESIGN PARAMETER  OF FLOOD BUNDS

| Sr. No. | Name | Length | Top Width | Side Slopes | Free Board |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | River Side | Country Side |  |
| 1 | Thatta Mahla Bund | RD:0-51000 (10.20 Miles ) | i.0-31 = 25ft ii.31-51 = 25ft | 3:1 | 2:1 | 6ft |
| 2 | Jhang Flood Bund | RD:0-71000 (14.20 Miles) | i. 0-15 =25ft ii. 15-64=25ft iii.64-71=25ft | 2:1 3:1 3:1 | 2:1 2:1 2:1 | 6ft |
| 3 | Loop Bund | RD:0-11500 (2.30 Miles) | 20ft | 3:1 | 2:1 | 6ft |
|  | Mileage | 26.70 Miles |  |  |  |  |

  - LOCATION MAP

Part Index Plan attached showing Flood Bunds at page 56.

Chapter-3

BRIEF HISTORY OF PAST FLOOD EVENTS

As a consequence to exceptionally high Floods in river Chenab, Thatta Mahla Bund, main protection Line for Jhang city breached during the night between 11-12 August,1973.  The gauge at RD: 1+500, of Thatta Mahla Flood Bund recorded at the time of breach was 526.90 ft against the previous highest level ever recorded as 525.90 ft during Floods of 1957.  The total length of breach occurred in the bund was 2155 ft during 1973 with an approximate discharge of 80,000 Cs: passed through the breach when the gauge recorded at Revaz Bridge was 522.70 ft against the highest ever recorded 522.20 ft during 1957.

The peak discharges passed through the river Chenab at critical gauge site at RD.1500 of Thatta Mahla flood Bund are as under.

| Sr.No. | Year | Date of Peak Flood at Trimmu H/W | Discharge at Trimmu Head Works | Date | Gauge RD 1+500 of Thatta Mahala Bund | Duration |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 1973 | 15.08.73 | 666910 | 15.08.73 | 526.9 |  |
| 2 | 1974 | 17.07.74 | 150170 | - | - | - |
| 3 | 1975 | 20.07.75 | 458247 | - | - | - |
| 4 | 1976 | 10.08.76 | 704633 | 10.08.76 | 525.2 | - |
| 5 | 1977 | 19.07.77 | 293628 | - | - | - |
| 6 | 1978 | 20.07.78 | 286806 | - | - | - |
| 7 | 1979 | 17.07.79 | 168680 | - | - | - |
| 8 | 1980 | 17.07.80 | 182081 | - | - | - |
| 9 | 1981 | 31.07.81 | 306171 | 29.07.81 | 521.8 | 8-12 Hrs |
| 10 | 1982 | 04.08.82 | 135522 | - | - | - |
| 11 | 1983 | 05.09.83 | 272781 | - | - | - |
| 12 | 1984 | 31.08.84 | 150608 | - | - | - |
| 13 | 1985 | 11.08.85 | 277512 | 21.07.85 | 520.9 | 6-12 Hrs |
| 14 | 1986 | 08.08.86 | 403187 | 31.07.86 | 520.5 | 1-10 Hrs |
| 15 | 1987 | 14.06.87 | 157613 | - | - - | - |
| 16 | 1988 | 29.09.88 | 493123 | 29.09.88 | 524.5 | 4-5 Hrs |
| 17 | 1989 | 03.08.89 | 481517 | 2-3.08.89 | 521.1 | 21-03 Hrs |
| 18 | 1990 | 24.03.90 | 207396 | - - | - | - |
| 19 | 1991 | 16.04.91 | 207026 | - | - | - |

| Sr. No. | Year | Date of Peak Flood at Trimmu H/W | Discharge at Trimmu Head Works | Date | Gauge RD 1+500 of Thatta Mahala Bund | Duration |
| --- | --- | --- | --- | --- | --- | --- |
| 20 | 1992 | 13.09.92 | 683117 | 13.09.92 | 524.35 | 16-19 Hrs |
| 21 | 1993 | 14.07.93 | 326744 | - |  |  |
| 22 | 1994 | 23.07.94 | 323099 | - |  |  |
| 23 | 1995 | 01.08.95 | 129561 | 31.07.95 | 525.95 | 15-21 Hrs |
| 24 | 1996 | 27.08.96 | 543708 | 27.08.96 | 527 | 4-6 Hrs |
| 25 | 1997 | 01.09.97 | 677417 | 30.08.97 | 525.4 | 5-10 Hrs |
| 26 | 1998 | 13.07.98 | 148668 | - | - | - |
| 27 | 1999 | 22.07.99 | 61476 | - | - | - |
| 28 | 2000 | 26.07.2000 | 116179 | - | - | - |
| 29 | 2001 | 18.08.2001 | 72431 | - | - | - |
| 30 | 2002 | 17.08.2002 | 108627 | - | - | - |
| 31 | 2003 | 07.08.2003 | 122805 | - | - | - |
| 32 | 2004 | 21.08.2004 | 42756 | - | - | - |
| 33 | 2005 | 17.07.2005 | 162097 | 11.07.05 | 522.4 | 9-13 Hrs |
| 34 | 2006 | 07.09.2006 | 266270 | 06.09.06 | 523.6 | 18-21 Hrs |
| 35 | 2007 | 16.03.2007 | 173529 | - | - | - |
| 36 | 2008 | 04.08.2008 | 132220 | - | - | - |
| 37 | 2009 | 21.08.2009 | 62265 | - | - | - |
| 38 | 2010 | 10.08.2010 | 323026 | 10.08.2010 | 522.5 | 15- 19-Hrs |
| 39 | 2011 | 20.09.2011 | 132890 | - | - | - |
| 40 | 2012 | 07.08.2012 | 82794 | `- | - | - |
| 41 | 2013 | 20.08.2013 | 272609 | 19.08.2013 | 525.4 | 07-13 Hrs |
| 42 | 2014 | 11.09.2014 | 626006+ 77000 | 09.09.2014 | 528.1 | 06-07 Hrs |
| 43 | 2015 | 29.07.2015 | 150570 | - | - | - |
| 44 | 2016 | 10.08.2016 | 166139 | 10.08.2016 | 520.8 | 1.00 Hrs |
| 45 | 2017 | 21.07.2017 | 92595 | - | - | - |
| 46 | 2018 | 16.08.2018 | 94680 | - | - | - |
| 47 | 2019 | 22.08.2019 | 105821 | - | - | - |
| 48 | 2020 | 01.09.2020 | 196077 | - | - | - |
| 49 | 2021 | 31.07.2021 | 123167 | - | - | - |
| 50 | 2022 | 18.08.2022 | 129815 | - | - | - |
| 51 | 2023 | 25.07.2023 | 125186 | - | - | - |

During 1976, a maximum discharge of 706442 cusec passed through Trimmu Barrage.  A maximum gauge of 525.20 was recorded at RD: 1500 Thatta Mahla Bund on 09.08.1976 at 05:00 Hours with corresponding gauge 521.50 of Revaz Bridge and 506.80 at RD: 23000 of Flood protection Bund.  There was damage to top and slope of bund due to heavy rains and wave action during Floods of 1976.  All necessary repairs were carried out at site after Floods of 1976.  There was no appreciable Flood in the River during the year 1977, 1978, 1979 and 1980.  During 1981, the maximum discharge passing downstream Khanki was 5.47 Lac cusec on 26.08.1981, Qadirabad 5.79 Lac cusec on 26.07.1981 and at Trimmu 3.06 Lac cusec on 31.07.1981.  The maximum gauge along Jhang Flood Protection Bund at RD: 23000 was 502.00 on 30.07.1981.  There was no Flood during 1982 and 1983.

During 1985, the maximum discharge passed D/S Khanki was 309068 Cs. on 07.08.1985, Qadirabad 318117 Cs. on 08.08.1985 and Trimmu 277512 Cs. on 11.08.1985. The corresponding gauge at Revaz Bridge was 519.10 on 11.08.1985. The gauge at RD: 23000 Jhang Flood Protection Bund was 503.60 on 22.07.1985. During 1986, the maximum discharge passed D/S Khanki was 3,26,000 Cs. on 28.07.1986 at 09:00 hours, Qadirabad 312862 Cs. on 28.07.1986 at 12.00 hours.  The maximum discharge D/S Rasul Barrage was recorded as 141404 cs: on 05.08.1986 at 06.00 hours.  The accumulated effect of Rasul and Qadirabad was received at Trimmu on 08.08.1986 at 04.00 hours and was recorded as 403187 Cs. The maximum gauge recorded at Revaz Bridge was 518.40 and corresponding gauge at RD; 1500 T.M Bund was 521.10 and that of RD: 23000 of J. F.P Bund was 502.90.

During 1987, Maximum Discharge D/S Khanki was 98745 Cs. on 27.07.1987.  The peak gauge at Revaz Bridge was 516.70 Cs. on 29.07.1987.  However the Flood water did not touch the Bunds during 1987.  During 1988 maximum discharge D/S  Khanki was 864220 Cs. on 26.09.1988 at  12.00  hours  and  D/S Qadirabad  892299  Cs. on  26.09.1988  at 16.00 hours and D/S Trimmu 993123 Cs. on 29.09.1988 at 17.00 hours. The maximum  gauge  recorded  at  Revaz  Bridge was 521.20 on 29.09.1988 at 5.00 hours and gauge at RD: 1500 T.M Bund was 524.50 on 29.09.1988 at 4.00 hours and that of RD: 23000 F.P Bund was 505.10 on 29.09.1988.  The Flood water touched the bunds and parallel flow caused damages to the slopes of Jhang F.P Bund.  A jet like water flow passing through bridge opposite RD: 27-28 J.F.P Bund  also caused serious damage to the Bund.

During 1989, there was very high flood in River Chenab. Peak discharge of 512205 Cs. on 31.07.1989 at 2.00 hours to 5.00 hours was recorded at Khanki and same reached Qadirabad on the same day at 16.00 hours with maximum discharge of 547400 Cs. This very high flood showed Peak discharge of 431517 Cs. at Trimmu Barrage with duration of 6.00 hours to 13.00 hours on 03.08.1989 and maximum gauge at Revaz Bridge was recorded 519.40 on 02.08.1989 at 23.00 hours for 2.00 hours duration.  Flood water touched the T.M Bund & J.F.P Bund on 31.07.1989 at 9.00 hours/5.00 hours respectively.  The Flood water resulted maximum gauge along T.M flood Bund RD: 1500 as 521.00 on 03.08.1989 & J.F.P Bund RD: 23000 gauge 505.75

on 02.08.1989. During 1990 there was very high flood in the River Chenab Peak and a discharge of 160760 Cs was observed on 10.09.1990 at 12.00 hours at Khanki and Qadirabad respectively and peak discharge of 151584 Cs at Trimmu Head Works on 12.09.1990 at 12.00 hours. During 1991 there was high flood in River Chenab with peak discharge of 103878 and 120469 Cs. on 14.07.1991 at 6.00 A.M at Khanki Head & Qadirabad Barrage respectively and peak discharge of 161471 Cs. on 24.07.1991 at 6.00 A.M at Trimmu Barrage.  The flood water showed the maximum gauge at Revaz Bridge as 518.00.

During 1992, maximum discharge of 910512 Cs passed D/S  Khanki  on 11.09.1992 at  21.00  hours  and  D/S Qadirabad  948446  Cs. on  11.09.1992  at 04.00 hours.  The maximum gauge recorded at  Revaz  Bridge was 520.30 on 13.09.1992 at 19.00 hours and gauges observed  at RD: 1500 T.M Bund were 524.35 on 13.09.1992 at 16.00 hours and that of RD: 23+000 J. F.P Bund 506.75 on 13.09.1992 at 01:00 hours .  The Flood water touched the bunds and parallel flow caused damages to the slopes of Jhang F.P Bund.

During 1996, on 23.08.1996 maximum flood of 851223 Cs. was observed down stream QBD Barrage at 5.00 A.M and raised up to 853231 at 10.00 A.M with Revaz Bridge gauge 518.00 & 518.20 respectively. The maximum effect was received on 27.08.1996 at Revaz Bridge.  The4 maximum gauge observed 522.60 and gauge at RD: 1500 of Thatta Mahla Flood Bund was received 527.00 at 2.00 am.  This position remained constant up to 7.00 A.M and breaching section was not operated.  After 7.00 am, gauge at RD: 1500 T.M.F.B went down slowly.

During  flood  1997 on 28.08.1997 high flood of 873442 Cs. passed down stream Qadirabad Barrage at 17.00 hours and remained constant up to 22.00 hours.  The maximum accumulated effect was received 30.08.1997, at Revaz Bridge at 24.00 hours. The maximum gauge at Revaz Bridge was observed 521.21 and maximum gauge at RD: 1500 of Thatta Mahla Bund was noted on 31.08.1997 at 5.00 AM.  This maximum gauge level 525.40  remained constant up to 10.00 AM.  After 10.00 A.M, the gauge at RD: 1500 of Thatta Mahla Bund went down slowly.  No flood was received during 2003-2004.

During 2005, River Chenab received flood at Maralla on 07.07.2005 at 15:00 hours  with its peak at 24:00 Hours with a discharge of  333744 Cs. Khanki Head Works started  raising on  07.07.2005 at 22:00 Hours  and flood water reached  to  high  flood  with  its   peak discharge of 368078 Cs at 10.00 Hrs on 08.07.2005.  River Chenab came into low flood at Qadirabad Head Works on 07.07.2005 at 22:00Hrs and turned to medium flood with peak discharge of 369847 Cs at 17:00Hrs on 08.07.2005.  Similarly rising of flood water at Chiniot Bridge started on 09.07.2005 at 14:00 Hours

and level fell down with 263200 Cs from 15:00Hrs on 09.07.2005 to 23:00Hrs and it again raised with discharge 282000 at 24:00Hrs on 09.07.2005 to peak of 295800 Cs. up to 7:00Hrs on 10.07.2005.  The gauge at Revaz Bridge raised from 516.80 at

5:00Hrs on 09.07.2005 to 520.30 at 4:00Hrs on 11.07.2005.  With the rising of gauge at Revaz Bridge, water spilled out from river and travelled on left side towards T.M.B parallel to Railway Line and hit T.M.B at R.D 1500 at 4:00Hrs on 10.07.2005. The flood water effect reached at Trimmu Head Works with peak discharge of 171137 Cs.

During year 2006, River Chenab received high Flood on 03.09.2006, at Marala with discharge of 332950 Cs. Khanki Head Works raised and reached to high flood on .4.9.06 at 9.00 Hrs with its peak discharge of 418740 Cs. River Chenab came into high flood at Qadirabad Barrage on 4.9.06 on 14.00 Hrs with peak discharge of 432206 Cs. Flood water at Chiniot Bridge started raising on 5.9.06 and falling with 309600 Cs discharge on 5.9.06 at 23.00 Hrs. With the raising of gauges at Revaz bridge, the water spilled out from the river on left side towards T.M.B parallel to Railway Line and hit T.M.B at RD: 1500. The flood water reached at Trimmu Head Works with peak discharge of 266270 Cs on 7.9.2006 at 16.00 Hrs.

There was heavy rain fall in the catchment area of River Chenab during the month March, 2007 resulting high Flood at Marala Head works with peak discharge 252409 Cs on 13.03.2007 at 15 Hours, simultaneously at Khanki on 13.03.2007 at 17:00 Hours with Peak discharge of 3,00 197 Cs. River Chenab raised at Qadirabad Barrage with peak discharge of 3,12,836 Cs on 13.03.2007 at 21:00 Hrs. This Flood water reached at Trimmu Headworks on 15.03.2007 at 6.00 Hrs with discharge of 156882 Cs.

During the year 2007, River Chenab received a maximum discharge of 83867 Cs at Qadirabad Barrage on 1.07.2007 at 6.00 Hrs which passed through Trimmu Barrage with max discharge of 62421 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2008, River Chenab received a maximum discharge of 125317 Cs at Qadirabad Barrage on 04.08.2008 at 6.00 Hrs which passed through Trimmu Barrage with max discharge of 67836 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2009, River Chenab received a maximum discharge of 77535 Cs at Qadirabad Barrage on 19.06.2009 at 6.00 Hrs which passed through Trimmu Barrage with max discharge of 72625 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2010, River Chenab received a maximum discharge of 319733 Cs at Qadirabad Barrage on 07.08.2010 at 3.00 Hrs which passed through Trimmu Barrage with max discharge of 222204 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2011, River Chenab received a maximum discharge of 170547Cs at Qadirabad Barrage on 17.09.2011 at 12.00 Hrs which passed through Trimmu Barrage with max discharge of 132890 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2012, River Chenab received a maximum discharge of 180789Cs at Qadirabad Barrage on 05.08.2012 at 11.00 Hrs which passed through Trimmu Barrage with max discharge of 82794 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2013, River Chenab received a maximum discharge of 403403 Cs at Qadirabad Barrage on 15.08.2013 at 18.00 Hrs which passed through Trimmu Barrage with max discharge of 272609 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2014, River Chenab received exceptionally High flood with maximum discharge of 904285 Cs at Qadirabad Barrage on 07.09.2014 at 11.00 Hrs which passed through Trimmu Barrage with max discharge of 626006 Cs the through Barrage and 77000 Cs through Breaching section. Jhang Flood Protection Bund of Jhang Canal Division L.C.C (W) Jhang breached / damaged in between RD 1+000 to 2+000 on 10.09.2014 at 01:40 hours.

The water level at Rivaz Railway Bridge during 1973 Flood was recorded 522.60 that raised upto 524.90 on 09.09.2014 at 06:000 hours (Difference 2.30 ft). Water level at RD 1+500 Thatta Mahalla Flood Bund raised upto 528.10 on 09.09.2014 at 06:00 hours against HFL of 1973 i.e., 526.90 ft. (Difference 1.20 ft). Danger Flood mark at RD: 23+000 of Jhang Flood Protection Bund is 508.00 and water level raised upto 510.30 on 09.09.2014 at 23:00 hours. (Difference 2.30 ft).At RD 6+000 Jhang Flood Protection Bund, designed Highest Flood Level (HFL) is 506.79 where as water level raised to 508.80 on 09.09.2014 at 24:00 hours (Difference 2.01 ft).

During the year 2015, River Chenab received a maximum discharge of 161054 Cs at Qadirabad Barrage on 13.07.2015 at 10.00 Hrs which passed through Trimmu Barrage with max discharge of 150570 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2016, River Chenab received a maximum discharge of 405542 Cs at Qadirabad Barrage on 08.08.2016 at 3:00 Hrs which passed through Trimmu Barrage with max discharge of  166139 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2017, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 164660 Cs at 13:00 and remain same upto 14:00 on 19.07.2017 at 2:00 Hrs which passed through Trimmu Barrage with max discharge of  92595 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2018, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 172031 Cs at 6:00 and remain same upto 13:00 on 14.08.2018 at 24:00 Hrs which passed through Trimmu Barrage with maximum discharge of 94680 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2019, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 131899 Cs at 9:00 and remain same upto12 :00 on 15.08.2019 at 3:00 Hrs which passed through Trimmu Barrage with max discharge of 105821 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2020, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 267540 Cs at 15:00 and remain same upto 20 :00 on 28.08.2020 at 5:00 Hrs which passed through Trimmu Barrage with max discharge of 206077 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2021, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 187812 Cs at 6:00 and remain same upto 18 :00 on 29.07.2021 at 5:00 Hrs which passed through Trimmu Barrage with max discharge of 123167 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2022, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 193577 Cs at 15:00 and remain same upto 17:00 on 12.08.2022 at 15:00 Hrs which passed through Trimmu Barrage with max discharge of 129815 Cs without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

During the year 2023, River Chenab received a maximum discharge of  D/S Qadirabad Barrage was 185749 Cs at 09:00 and remain same upto 12:00 on 20.07.2023 at 9:00 Hrs which passed through Trimmu Barrage with max discharge of 125186 Cs on 25.07.2023 at 21:00 without damaging to the Flood Protection Bunds of Jhang Canal Division L.C.C (W) Jhang.

CHAPTER-4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS / BARRAGES AND OTHER CONTROL POINTS

  - FLOOD LIMITS

The terminology of different kinds of flood is low, Medium, High, very high and exceptionally high and they will be taken as such in the light of any wireless message received from respective warning centers.

| FLOOD LIMIT | TRIMMU | QADIRABAD | RASUL |
| --- | --- | --- | --- |
| 1. Low | 1.50 to 2.00 Lac | 1.00 Lac | 0.75 Lac |
| 2. Medium | 2.00 to 3.00 Lac | 1.50 Lac | 1.10 Lac |
| 3. High | 3.00 to 4.50 Lac | 2.00 Lac | 1.25 Lac |
| 4. Very High | 4.50 to 6.00 Lac | 4.00 Lac | 2.23 Lac |
| 5. Exceptionally High | Above 6.00 Lac | 6.00 Lac & Above | Above 3.00 Lac |

  - TIME LAGS OF FLOODS

As per statement, the following are the time lags for average flood flows in the Rivers

| RIVER | SITE | DESIGNED CAPACITY | DISTANCE IN K.M. | TIME LAG IN HOURS |
| --- | --- | --- | --- | --- |
| Chenab | Marala | 11.00 Lac | - | - |
|  | Khanki | 11.00 Lac | 56 | 9 |
|  | Qadirabad | 9.00 Lac | 30 | 6 |
|  | Chiniot Bridge |  | 101 | 38 |
|  | Revaz Bridge |  | 80 | 16 |
|  | Trimmu | 8.75 Lac | 34 | 10 |
|  | Panjnad | 7.00 Lac | 257 | 81 |

4.3	HIGHEST FLOODS

The highest flood discharges in cuses recorded upstream Trimmu Head Works and gauge at Thatta Mahalla Flood Bund  RD: 1+500 during last Ten  years are as under:-

| Sr. No. | Year | Date of Peak Flood at Trimmu H/W | Discharge at Trimmu Head Works | Date | Gauge RD.1+500 of Thatta Mahala Bund | Duration |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 2012 | 07.08.2012 | 82794 | - | - | - |
| 2 | 2013 | 20.08.2013 | 272609 | 19.08.2013 | 525.40 | 07-13 Hrs |
| 3 | 2014 | 10.09.2014 | 626006 +73000 | 09.09.2014 | 528.10 | 06-07 Hrs |
| 4 | 2015 | 29.07.2015 | 150570 | - | - | - |
| 5 | 2016 | 10.08.2016 | 166139 | 10.08.2016 | 528.10 | 1.00 Hrs |
| 6 | 2017 | 21.07.2017 | 92595 | - | - | - |
| 7. | 2018 | 16.08.2018 | 94680 | - | - | - |
| 8. | 2019 | 22.08.2019 | 105821 | - | - | - |
| 9. | 2020 | 01.09.2020 | 206077 | - | - | - |
| 10. | 2021 | 31.07.2021 | 123167 | - | - | - |
| 11 | 2022 | 18.08.2022 | 128915 | - | - | - |

  - PEAK DISCHARGE

| Year | Khanki Barrage | Qadirabad Barrage | Trimmu Barrage |
| --- | --- | --- | --- |
|  | Date | Time | Discharge | Date | Time | Discharge | Date | Time | Discharge |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 1973 | 8-Oct | 6.12 | 864000 | 8-Oct | 6.12 | 854000 | 8-Dec | 16.12 | 611972 |
| 1974 | 24/7 | 24.00 | 196076 | 25/7 | 6.00 | 19828 | 27/7 | 02.00 | 150172 |
| 1975 | 17/7 | 12.00 | 660680 | 17/7 | 18.00 | 669819 | 21/7 | 05.00 | 458247 |
| 1976 | 17/07 | 12 | 666241 | 17/07 | 17.18 | 669819 | 20/07 | 17 | 458247 |
| 1977 | 8-Jul | 2 | 586453 | 8-Jul | 8 | 608057 | 8-Oct | 2 | 706433 |
| 1978 | 8-Sep | 14 | 433095 | 8-Sep | 22.24 | 428009 | 8-Dec | 17.52 | 238042 |
| 1979 | 8-Mar | - | 246868 | 8-Mar | - | 245566 | 8-May | - | 269584 |
| 1980 | 15/07 | 6 | 128209 | 15/07 | 6 | 122166 | 17/07 | 12 | 183681 |
| 1981 | 26/07 | 21 | 546505 | 26/07 | 19 | 578968 | 31/07 | 2.04 | 306171 |
| 1982 | 8-Feb | 3 | 256010 | 25/07 | 12 | 221777 | 27/07 | 12 | 138532 |
| 1983 | 8-Sep | 20 | 303913 | 8-Sep | 6 | 283227 | 8-Sep | 6 | 276988 |

| Year | Khanki Barrage | Qadirabad Barrage | Trimmu Barrage |
| --- | --- | --- | --- |
|  | Date | Time | Discharge | Date | Time | Discharge | Date | Time | Discharge |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 1984 | 8-Dec | 6 | 135855 | 8-Sep | 18 | 108476 | 30/08 | 11 | 155000 |
| 1985 | 8-Jul | 18 | 309069 | 8-Aug | 6 | 318118 | 8-Nov | 6 | 277512 |
| 1986 | 8-May | 12 | 341000 | 8-May | 12 | 345258 | 8-Aug | 12 | 403187 |
| 1987 | 27/07 | 6 | 98745 | 27/07 | 18 | 77279 | 30/07 | 6 | 98083 |
| 1988 | 26/09 | 12 | 88422 | 26/09 | 16 | 892299 | 29/09 | 17 | 93123 |
| 1989 | 31/07 | 2 | 612205 | 29/07 | 16 | 547400 | 8-Mar | 6 | 431517 |
| 1990 | 9-Oct | 12 | 234460 | 9-Oct | 12 | 243272 | 9-Dec | 12 | 151584 |
| 1991 | 14/07 | 6 | 103870 | 14/07 | 6 | 120429 | 24/07 | 6 | 161471 |
| 1992 | 9-Oct | 21 | 910512 | 9-Nov | 4.08 | 948446 | 13/09 | 21 | 683117 |
| 1993 | 7-Nov | 9 | 430410 | 7-Nov | 17 | 443054 | 13/09 | 17 | 335889 |
| 1994 | 20/07 | 24 | 425160 | 21/07 | 4 | 425567 | 23/07 | 3 | 303521 |
| 1995 | 27/07 | 17 | 604336 | 29/07 | 13 | 644397 | 8-Dec | - | 609561 |
| 1996 | 23/08 | 5 | 851269 | 23/08 | 10 | 853231 | 27/08 | 16 | 543708 |
| 1997 | 28/08 | 12 | 847650 | 28/08 | to 17.00 | 873442 | 9-Jan | to 9.00 | 677417 |
| 1998 | 10.09.98 | 6 | 26832 | 25/9 | 6 | 39780 | 29/9 | 6 | 16876 |
| 1999 | 11.8 | 6 | 112147 | 20/7 | 6 | 108190 | 8-May | 6 | 54856 |
| 2000 | 237 | 6 | 268358 | 24/7 | 6 | 190640 | 26/7 | 6 | 116179 |
| 2001 | 24.7 | 6 | 131888 | 8-Aug | 6 | 125483 | 27/7 | 6 | 57211 |
| 2002 | 15.8 | 6 | 137210 | 15/8 | 6 | 182170 | 17/8 | 6 | 101855 |
| 2003 | 19/02 | 18 | 371788 | 19/02 | 22 | 367408 | 22/02 | 5 | 165169 |
| 2004 | 18/08 | 6 | 85101 | 18/08 | 6 | 90043 | 21/08 | 6 | 48173 |
| 2005 | 7-Aug | 10 | 368078 | 7-Aug | 17 | 369847 | 17.07/2005 | 15 | 162097 |
| 2006 | 4/9/2006 | 9 | 418740 | 4/9/2006 | 14 | 432206 | 7/9/2006 | 16 | 266270 |
| 2007 | 1/7/2007 | 6 | 72923 | 1/7/2007 | 6 | 83867 | 2/7/2007 | 6 | 173529 |
| 2008 | 4/8/2008 | 6 | 123320 | 4/4/2008 | 6 | 103317 | 4/8/2008 | 6 | 132220 |
| 2009 | - | - | - | 16/06/2009 | 6 | 77535 | 21/8/2009 | 6 | 62265 |
| 2010 | 07.08.2010 | 13 | 327637 | 7/8/2010 | 10 | 319733 | 10/8/2010 | 22 | 323026 |
| 2011 | 19.09.2011 | 19 | 171383 | 17.09.2011 | 12 | 170547 | 20.09.2011 | 6 | 132890 |
| 2012 | 05.08.2012 | 6 | 176197 | 05.08.2012 | 11 | 180789 | 07.08.2012 | 6 | 82794 |
| 2013 | 15.08.2013 | 10 | 410332 | 15.08.2013 | 18 | 403403 | 20.08.2013 | 13 | 272609 |
| 2014 | 07.09.2014 | 7:00 | 947099 | 07.09.2014 | 11:00 | 904285 | 10.09.2014 | 19:00 | 626006 +77000 |
| 2015 | 13.07.2015 | 3:00 | 155567 | 13.07.2015 | 10:00 | 161054 | 29.07.2015 | 15:00 | 150570 |
| 2016 | 07.08.2016 | 24:00:00 | 418736 | 08.08.2016 | 3:00 | 405542 | 10.08.2016 | 14:00 | 166139 |
| 2017 | 19.07.2017 | 8:00 | 184346 | 19.07.2017 | 13:00 | 164660 | 21.07.2017 | 18:00 | 92595 |
| Year | Khanki Barrage | Qadirabad Barrage | Trimmu Barrage |
|  | Date | Time | Discharge | Date | Time | Discharge | Date | Time | Discharge |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 2018 | 13.08.2018 | 12:00 | 182025 | 14.08.2018 | 6:00 | 172031 | 16.08.2018 | 24:00:00 | 94680 |
| 2019 | 15.08.2019 | 24:00:00 | 133613 | 15.08.2019 | 9:00 | 131899 | 22.08.2019 | 18:00 | 105821 |
| 2020 | 28.08.2020 | 7:00 | 286230 | 28.08.2020 | 15:00 | 267540 | 01.09.2020 | 3:00 | 206077 |
| 2021 | 29.07.2021 | 6:00 | 189683 | 29.072021 | 6:00 | 187812 | 31.07.2021 | 5:00 | 123167 |
| 2022 | 12.08.2022 | 6:00 | 210945 | 12.08.2022 | 15:00 | 193577 | 18.08.2022 | 15:00 | 129815 |
| 2023 | 20.07.2023 | 2:00 | 204041 | 20.07.2023 | 09:00 | 185749 | 25.07.2023 | 21:00 | 125186 |

Chapter-5

FLOOD FIGHTING STRATEGY

DANGEROUS FLOOD MARKS FOR THE BUNDS ARE AS UNDER: -

| Name of Bund | Danger Flood Mark | Site or RD of Bund |
| --- | --- | --- |
| 1. Thatta Mahla Flood Bund | 525.00 | 1500 |
| 2. Jhang Flood Protection Bund | 508.00 | 23000 |

When these gauges are attained at respective sites, the Sub Divisional Officer Wer Sub Division (at Jhang) will issue a warning to the District Administration who will arrange to inform the public to evacuate immediately from the areas identified in this Plan.

The following Flood Bunds, are directly affected by the Floods and Flood spill:-

| S.No: | FLOOD BUND/CHANNELS | REACH. | LENGTH. |
| --- | --- | --- | --- |
| 1. | Jhang Flood Protection Bund | RD:0+000-71+000 | 14.20 miles |
| 2. | Thatta Mahalla Bund | RD: 0+000-51+000 | 10.20 miles |
| 3. | Loop Bund | RD: 0+000-11+500 | 2.30 miles |
|  |  | Total: | 26.70 miles. |

For watching of Flood Bunds, one man per mile will be employed for one month i.e. 1st June to 30th September, in addition to existing strength of one man per six mile length. Since there is no regular establishment on Jhang Flood  Protection Bund.

Thatta Mahalla Bund , so a gang of one man per mile will be employed on Jhang  Flood  Protection Bund and one man for Thatta Mahalla Bund will be employed w,e,f, 1st June to 30th September and one mate at every                           Nine  persons.

The establishment will take care of all preparations like filling depressions, rain cuts/gharas, clearance of slopes upto 10 feet beyond toe of Flood Bund, Opening / puddling holes etc.

i.	LOW FLOOD DISCHARGE 100000-150000 Cs.

No extra labour will be employed. The labour arranged for preparedness will continue as such. The Sub Engineer Jhang Flood Bund Section will shift his camp at  RD: 23+000 Jhang Flood  Protection Bund and Sub Engineer Thatta Mahla Flood Bund will also watch Thatta Mahalla Bund at RD: 19+000.

ii. 	MEDIUM FLOOD DISCHARGE 150,000-200,000 Cs.

The flood water flows within River banks. No extra labour will be employed on
Jhang  Flood  Protection Bund. In case of any emergency, SDO Flood bund Jhang  will promptly contact Executive Engineer Jhang  and suggest/take fighting measures with prior concurrence of Superintending Engineer LCC(west), Circle Faisalabad. He will keep a close liaison with Flood Center of District Coordination Officer Jhang and Flood Emergency Officer of Faisalabad Irrigation Zone Faisalabad.

iii. 	HIGH FLOOD DISCHARGE 200000-400000 Cs.

The flood water spills out during this stage of flow and a gang of two men per mile per shift for three shifts will be employed on Flood Bunds whereas the labour strength of 2 men per mile per shift will be employed on Jhang Flood Protection Bund, Thatta Mahla bund and Loop bund. The Sub Engineer Jhang Flood Bund will shift his camp at Jhang Flood Protection Bund at RD: 6+000 and of Thatta Mahalla Flood Bund at RD: 11+500, The Sub Divisional Officer Flood Bund Jhang will be overall in-charge of flood watching and related activities. In Medium to high flood stage 07No. excavator, 2 No. Dozer, 14 No. Trolleys / Dumpers, 14 No. Tractor with front blade  & 70 No. Labour (Beldar & Mate) required.

iv.	VERY HIGH FLOOD DISCHARGE 400000-600000 Cs.

All activities will remain as such. The watching establishment will be raised to three men per mile per shift for three shifts on Jhang  Flood  Protection Bund & Thatta Mahalla Flood Bund. In high to very flood stage 07No. excavator, 2 No. Dozer , 14 No. Trolleys / Dumpers , 16 No. Tractor with front blade  & 80 No. Labour (Beldar & Mate) required.

v.   	EXCEPTIONALLY HIGH FLOOD ABOVE 600000 Cs.

This stage warrants alarming situation. The watching labour will be raised to 5 men per mile per shift for three shifts on Flood Bund. Similarly the strength will be raised to six men per shift on Jhang Flood Protection Bund and three men per shift for three shifts on Thatta Mahalla Bund On receipt of exceptionally high flood, the Deputy Collector Jhang along with concerned Zilladars will shift their camp at Jhang Canal  Rest House. He will arrange,

- Proclamation on loudspeakers etc for evacuation of abadies inside the flood bunds.

- Prepare maps for the areas inundated and carry out immediate  survey for damages to crops and other properties.

- Keep a close liaison with Sub Divisional Officer and assist him in 		 procurement of labour and other camping arrangements.

Executive Engineer, Jhang Division will camp at Jhang Canal Rest House and will be overall in charge of all watching and Flood  fighting activities. He will remain in touch with District Administration Jhang and Flood Emergency Officer, Jhang. He will launch Flood fighting activities with Consultation/Concurrence of Superintending Engineer, LCC(West), Circle Faisalabad. In very high to Exceptionally high flood stage  07No. excavator, 2 No. Dozer , 14 No. Trolleys / Dumpers , 21 No. Tractor with front blade  & 94 No. Labour (Beldar & Mate) required.

CHAPTER-6

FLOOD DAMAGES RESTORATION WORKS

There are no flood damage restoration works under execution in Jhang Canal Division LCC(W), Jhang for the year 2023.

CHAPTER-7

FLOOD FIGHTING WATCHING ARRANGEMENT

The flood season which is generally from June to September every year, demands strict watching of flood bunds.  Thus to meet with emergency and necessity of watching, work charge establishment will be employed from 01.07.2023 to 30.09.2023, Furthermore, during receipt of flood and keeping in view the situation of flood, civil administration also provides labour of District Council, Town Committee and also from the other Departments for the purpose of close watching on the Flood Bunds.

  - PRE –FLOOD ARRANGEMENTS

SCHEDULE OF FLOOD PREPAREDNESS ACTIVITIES FOR FLOOD SEASON 2024.

| Sr.# | Activity | Target Dates | Achievements |
| --- | --- | --- | --- |
| I. | Preparation of Flood Fighting Plans. |  |  |
|  | a) Submission of Draft Divisional Plans By Zonal Chief to Chief Engineer Drainage and Flood (after Scrutiny by S.E / C.E). | 01.03.2024 |  |
|  | b) Review by Chief Engineer D&F | 31.03.2024 |  |
|  | c) Final submission of Divisional Plans. | 15.04.2024 |  |
| II | Inspection of Flood Works |  |  |
|  | a. By Executive Engineer | 15.03.2024 |  |
|  | b. Checking Inspection by S.E / C.E | 31.03.2024 |  |
|  | c. Inspection by the Departmental Army Team | 31.03.2024 | Departmental Team = Awaited Army Team = Awaited |
| III | Identification of Encroachments on Bunds and spurs to the Civil Administration | 31.03.2024 |  |
| IV | Painting Gauges, RD Marks , Data Boards and Repairs to Flood Bund etc. | 31.05.2024 | Work will be completed before 31.05.2024. |
| V | Replenishment of Reserve Stock of Stone and Flood Fighting Materials |  |  |
|  | a) Identification of needs | 28.02.2024 | There is no sanction reserve stock of stone, however 423.411 %Cft Reserve stock of Stone received from PIU during Remodeling of Jhang Flood Protection Bund & Thatta Mahla Flood which is sufficient. |
|  | b) Funding procurement Arrangements | 15.03.2024 | N.A |
|  | c) Procurement, stacking, Prescribed Field checks | 31.05.2024 | N.A |
| VI | Installation of Wireless Sets | 15.06.2024 | Will be installed on 15.06.2024 |
| VII | Opening of Zonal Flood Cells |  |  |
|  | a) Duty Roster | 01.06.2024 | Will be notified before 01.06.2024 |
|  | b) Operative | 15.06.2024 | Will be made operational from 15.06.2024. |

- UPTO DATE STATUS OF RESERVE STOCK OF STONE

| Sanctioned Stock of Stone | Available Quantity | Defected Quantity | Remarks |
| --- | --- | --- | --- |
| Nil | 423.411 % Cft | - | Reserve stock of Stone received from PIU Jhang Canal Division after completion work Remodeling of selected reaches Jhang Flood Protection Bund & Thatta Mahla Flood Bund. . |

- UPTO DATE STATUS OF RESERVE STOCK OF STONE  DETAIL STRUCTURE WISE.

| Sr. No. | Name of structure | Sanctioned Quantity | Available Quantity (% Cft) | Balance Quantity | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Jhang Flood Protection Bund RD 5+000 | - | 231.69 % Cft | - | Reserve stock of Stone received from PIU Jhang Canal Division after completion work Remodeling of selected reaches Jhang Flood Protection Bund & Thatta Mahla Flood Bund. |
| 2. | Thatta Mahla Flood Bund RD 12+000 | - | 191.72 % Cft | - |  |

7.2	WATCHING ESTABLISHMENT

Following are the main spots where watching Huts will be established on Flood Bunds, the tents/chouldaries will be erected on Flood Bunds. Watching material will be shifted in such huts. One Chowkidar for each Hut will be employed from the report of receipt of medium Flood and will remain employed till end of flood season.

| Sr.# | Name of Bunds | Site | Flood Limits |
| --- | --- | --- | --- |
|  |  |  | Low | Medium | High | Very High | Exceptionally High |
|  |  |  | Man | Shift | Man | Shift | Man | Shift | Man | Shift | Man | Shift |
| 1 | Jhang flood protection bund | RD6+000 | - | - | 9 | 3 | 18 | 3 | 22 | 3 | 26 | 3 |
|  |  | RD 23+000 | - | - | 9 | 3 | 18 | 3 | 22 | 3 | 26 | 3 |
| 2 | Thatta Mahla flood bund | RD 1+500 | - | - | 9 | 3 | 18 | 3 | 22 | 3 | 26 | 3 |
|  |  | RD 11+500 | - | - | 9 | 3 | 18 | 3 | 22 | 3 | 26 | 3 |

7.3 	ARRANGEMENT AT SENSITIVE SITES

After completed work by PIU  Remodeling  Selected Reaches of Jhang Flood Protection Bund & Thatta Mahla Flood Bund there is no sensitive site location on flood bunds.

7.4 	WATCHING MATERIAL

There will be total 06 No. watching Camps along Flood Bunds: 03 No. on Jhang Flood Protection Bund and 3 No. Thatta Mahla Flood Bund. The following Flood material will be arranged and stored at Canal Colony Jhang and Thatta Mahla Flood       Bund. The material will be shifted to watching huts as soon as the intimation of Medium / High Flood limit is received. The medium flood limit applies to Thatta Mahalla Flood Bund and High Flood limit for Jhang Flood Protection  Bund. . Following will be the scale of watching material for temporary watching camps / huts.

LIST OF WATCHING MATERIAL REQUIRED FOR WATCHING CAMPS

| Sr. No. | Name of Item | Unit | Total Required Quantity | Available Quantity | Required Quantity | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No. | 80 | 20 | 60 | Required flood fighting material will be purchased before 30.06.2024 |
| 2 | Bamboos 8' to 10' (for Lighting arrangements) | No. | 904 | 154 | 750 |  |
| 3 | Chouldaries | No. | 5 | 0 | 5 |  |
| 4 | E.G. Bags | No. | 4500 | 1500 | 3000 |  |
| 5 | Folding Chair | No. | 24 | 0 | 24 |  |
| 6 | Folding Table | No. | 4 | 0 | 4 |  |
| 7 | G.I. Buckets | No. | 100 | 0 | 100 |  |
| 8 | Generator (8.00 K.Watts) | No. | 2 | 0 | 2 |  |
| 9 | Hand Saws | No. | 4 | 0 | 4 |  |
| 10 | Handle for Kassi / Axes | No. | 200 | 0 | 200 |  |
| 11 | Kassi with Handles | No. | 625 | 50 | 575 |  |
| 12 | M. Oil | Litter | 20 | 0 | 20 |  |
| 13 | Manila Rope | Kg | 50 | 0 | 50 |  |
| 14 | Petrol for Generator | Litter | 200 | 0 | 200 |  |
| 15 | Steel Charpoy | No. | 20 | 0 | 20 |  |
| 16 | Torches Chargeable | No. | 52 | 2 | 50 |  |
| 17 | Umbrella | No. | 20 | 0 | 20 |  |
| 18 | Cotton bags | No. | 47 | 4 | 43 |  |
| 19 | Jackets | No. | 25 | 2 | 23 |  |
| 20 | Polyethene Sheet | Kg | 5000 | 500 | 4500 |  |

7.5 	ARRANGEMENT FOR SOUNDING & PROBING

This item relates to barrage / Head works Canal Divisions.

7.6 	LIGHTING ARRANGEMENT

Sufficient numbers of emergency lights, lanterns and patromax lamps have already been provided. Petrol generators will be arranged and available for lighting arrangements.

7.7 	RATION ARRANGEMENT

The establishment and supervisory staff will be provided food and water by the Irrigation Departmental arrangement.

7.8 	P.O.L. ARRANGEMENT FOR VEHICLES

Civil Administration & Irrigation Department will arrange to supply POL for vehicles.

7.9 	TRANSPORTATION

Vehicles are available for transportation during Flood Season.

7.10 	LAW AND ORDER

There is no likelihood of any interruption by anyone except cutting of banks of Flood Bund to reduce heading up. In case of necessity, District Coordination Officer Jhang  will be contacted by the Executive Engineer, Canal Jhang Division to take decision at site.

7.11 	MEDICAL ARRANGEMENT FOR LABOUR

It will be responsibility of Health Department to provide Medical Facilities in flood areas where is required under supervision of Civil Administration.

7.12 	LIAISON WITH OTHER DEPARTMENT

Executive Engineer, Jhang Canal Division will keep liaison with the Civil and Army Authorities and will keep the Superintending Engineer LCC Faisalabad, fully apprised of the flood situation in Jhang Canal Division.

7.13 	ROLE OF THE ARMY

Role of the Army is very important in case of any emergent position arising due to high flood. A continuous liaison with the Army Authorities will be maintained during flood and if required necessary help will be sought.

7.14 	DUTIES OF TELEPHONE ATTENDANT

The Phone and Cell No of all officers and official to make immediate contact at any emergency during flood as below.

| Sr. No | Name of Officer / Official | Telephone No. | Period | Time |
| --- | --- | --- | --- | --- |
|  |  |  |  | From | To |
| 1. | (Mr. Faisal Sultan) Telephone attendant Jhang Canal Division Jhang | 047-9200300 | 15.06.2024 to 15.10.2024 | 9:00 AM | 4:00 PM |
| 2. | Telegraph Office Jhang | 047-9200300 |  | 9:00 AM | 4:00 PM |
|  |  |  |  | 4:00 PM | 12:00PM |
|  |  |  |  | 12:00 PM | 9:00AM |
| 3. | (Mr. Ali Hussnain) Sub Divisional Officer Flood Sub Division | 0316-7839321 |  | 24 Hours |
| 4. | (Mr. Danish Majeed) Sub Engineer Sheikh Chur Section | 0341-0518828 |  | 24 Hours |

  - WIRELESS ARRANGEMENTS

Wireless system will be installed w.e.f  01.06.2024 in the vehicle of  XEN Jhang No. GAA-888 and Vehicle of SDO Flood Bund No. FSO-8795.

CHAPTER-8

DETAIL OF ENCROACHMENT

- DETAIL OF ENCROACHMENT

| Sr. No | Total Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| 1. | 5 No. Houses Jhang Flood Protection Bund at RD 17+000 – 18+000 | - | 5 No. Houses Jhang Flood Protection Bund at RD 17+000 – 18+000 | A letter was issued to deputy Commissioner, Jhang vide this office letter No. 356/25-M dated 06.03.2024 for removal of encroachment |
| 2. | 2 No. Shops Thatta Mahla Flood Bund at 27+000 . | - | 2 No. Shops Thatta Mahla Flood Bund at 27+000 . |  |

- DETAIL OF CRITICAL ENCROACHMENT

| Sr. No | Total Critical Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| 1. | 5 No. Houses Jhang Flood Protection Bund at RD 17+000 – 18+000 | - | 5 No. Houses Jhang Flood Protection Bund at RD 17+000 – 18+000 | A letter was issued to deputy Commissioner, Jhang vide this office letter No. 356/25-M dated 06.03.2024 for removal of encroachment |
| 2. | 2 No. Shops Thatta Mahla Flood Bund at 27+000 . | - | 2 No. Shops Thatta Mahla Flood Bund at 27+000 . |  |

CHAPTER-9

DUTY ROSTER/FLOOD FIGHTING PROGRAM

DUTIES OF IRRIGATION STAFF

I)	Signallers.

The Canal Telegraph Station at Jhang shall remain open for 24 hours.  This station has the following installations for receiving and transmitting the massages.

- Canal Telegraph System connected Faisalabad.

- Trunk Telephone No.047-9200300

- Local Telephone connected with the following points.

  - Revaz Bridge

  - Thatta Mahla Bund RD 1500 and 11500

  - Flood Protection Bund RD 23000

  - Trimmu Head Works

This station shall remain open for 24 hours during flood emergency days and the following signallers will assist the Signaller at Jhang.

- Signaller Sheikh Chuhar.

- Signaller Veryam.

- Signaller Lakhlana.

The work of Sheikh Chuhar and Lakhlana Telegraph Offices will be looked after by the Signaller Wer, Bhangu and Ashaba respectively.

The Signaler Sheikh Chuhar, Veryam and Lakhlana will be called for duty by Signaller Jhang when the discharge at Qadirabad goes beyond medium flood.

FIELD STAFF

a)	SUB DIVISIONAL OFFICERS

The Flood Bunds fall in the jurisdiction of Sub Divisional Officer Flood Bund Sub Division with Headquarter at Jhang who under the advice and directions of the Executive Engineer, Jhang will be overall In-charge of all the operations connected with the Flood Bunds.  Sub Divisional Officer Veryam and Dhaular Sub Divisions assist him during flood days, SDO Veryam will be in-charge of all the operations/arrangements on Jhang Flood Protection Bund and Sub Divisional Officer, Dhaular on Thatta Mahalla Bund.  Sub Divisional Officer Veryam shall keep his temporary Headquarter at RD 6+000 of Jhang Flood Protection Bund. SDO Dhaular will keep his Headquarter at RD 11+500 of Thatta Mahla flood bund. The Sub Divisional Officers shall move for flood duty when Qadirabad records medium flood and is still rising.

.

b)	SUB ENGINEERS AND ZILLADARS

The Canal is completely closed during flood days.  The Sub Engineers from other sections along their Class-IV establishment with their kassies shall move to their duties shown at page 28.  They shall also bring their own Gauge Readers, Dak Runners, Artificers and Electricians to assist them in recording and transmitting gauges, removing defects of electric installations and T&P in their respective jurisdiction.

THEIR DUTIES SHALL CONSIST OF

- To deploy the labour for detecting and repairing rat holes/cracks rain cuts and other defects.

- To remove the Jungle from the inner toe of bank.

- Puddle the river side of the banks as the flood raises.

4.  To ensure that the gauges are being recorded directly and promptly by the 	Gauge Readers on duty.

5.	To maintain the road for movement of the Vehicles.

- To inform promptly to the Officer incharge regarding any apprehended danger and other important incidents.

- Each Sub Engineer, will be responsible for receiving the emergency store required by him for the use of the labour and return the same to the Sub Engineer, Sheikh Chuhar section, the emergency is over.

- They will ensure complete closure of culverts for water courses crossing flood bunds by Sluice valves or gunny bags.

OFFICIAL STAFF

The Sub Divisional Office will remain open for 24 Hrs: during flood days.  The Head Clerk will depute the clerical staff to attend office Telephone No.047-9200300 promptly and for this purpose, the Executive Engineer will   approve a duty roaster, before first July.

One cyclist will be deputed by Sub Divisional Officer Flood Bund to remain on duty in the Divisional Office for prompt delivery of the messages.

DUTY  ROSTER:  BATTLE  STATIONS  OF KEY PERSONAL

DURING HIGH & EXCEPTIONALLY  HIGH FLOOD  FLOW

| Name of Bund | Office Incharge | Field Staff on Flood Duty | Reach of Duty | Departmental Labour |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Regular | Temporary Estt: | Sectional Estt: |  |
| Thatta Mahla Flood Bund | Sub Divisional Officer flood Bund Sub Division & Sub Divisional Officers, Wer , Dhaular Sub Division with two Magistrates. | Sub Engineer, SCR ----------------- Wer ------------------ MRW | RD. 0-6 RD: 6+000 -11+500 | 2 2 | 8 6 | 10+10 Wer & JRA 10+10 LKN & MRW | Sub Engineer, Thatta Mahla Flood Bund to Keep Vigilance in reach RD: 0+000 -51+000 and arrange Labour & Material at Thatta Mahla Flood Bund. |
|  |  | Zilladar BLN Sub Engineer Tawan --------------- Jaura Zilladar SCR: | RD:11+500 -15+000 RD: 15-31 RD: 31-51 | 1 1 - | 6 5 5 6 | 10 ASB: 10 TWN 10 KRW 30 70 |  |
| Jhang Flood Protection Bund | Sub Divisional Officer Flood bund Sub Division & Sub Divisional Officers, Wer, Veryam Sub Division & Deputy Collector with two Magistrates | Sub Engineer JWA Sub Engineer As-haba Sub Engineer VRM Zilladar--------- Sub Engineer BLN: ------------------ Gojra Zilladar---------------- Sub Engineer AKW Zilladar Ashaba | RD: 0-18 RD: 18-31 RD: 31-42 RD: 42-71 (Tai) | 1 2 3 1 7 | 4 10 6 10 31 | 10 Veryam 10 + 5 JWA BLN 10 GRA 10 AKW 45 | Sub Engineer, Jhang Flood Protection Bund shall be In charge of store At RD: 23,000 |

Note:-

1. Sub Divisional Officer, Flood Bund Sub Division will be over all in-charge of all embankments.

2. During high Flood in case of emergency, Faisalabad Canal Division being the sister Division will be connected for performing Flood Duty alongwith its complete Establishment and Officers.

CHAPTER-10

EMERGENCY TELEPHONE NOS.

| Sr.No. | Departments | Office | Residence |
| --- | --- | --- | --- |
| 1 | Secretary I& Department Lahore | 042-99212117-18 | 042-35731116 |
| 2 | Deputy Commissioner Jhang | 047-9200081 | 047-9200181 |
| 3 | District Officer (Revenue) | 047-9200107 | 047-9200299 |
| 4 | Deputy District Officer (Revenue) | 047-9200433 | 047-9200422 |
| 5 | D.D.O.(R) Jhang. | 047-9200433 | 047-9200422 |
| 7 | D.P.O Jhang | 047-9200444 | 047-9200445 |
| 8 | Add: D.P.O Jhang | 047-9200094 | 047-9200040 |
| 9 | S. D.P.O Sadar | 047-9200312 |  |
| 10 | Wireless Control | 047-9200066 |  |
| 11 | Army Flood Officer 72 Medium GRW | 2695064/5 |  |
| 12 | District & Session Judge | 047-9200092 | 047-9200096 |
| 13 | Executive Engineer Jhang Division L.C.C (W) Jhang | 047-9200300 | 0304-0826776 |
| 14 | Chief Engineer D & F Zone Lahore | 042-99230731 Fax:5862081 | 0300-7315880 |
| 15 | Telegraph Office Faisalabad | 041-9200774 |  |
| 16 | Flood Warning Centre Lahore | 042-7572091-93 | Fax: 042-7572092 |
| 17 | Flood Emergency Office Faisalabad | 041-9200270 |  |

| Sr.No. | Departments | Office | Residence |
| --- | --- | --- | --- |
| 18 | Chief Engineer Irrigation Faisalabad | 041-9200268 | 041-9200269 |
| 19 | Executive Engineer Khanki Division | 055-6266239 055-6605255 | 055-766239 |
| 20 | Executive Engineer Trimmu | 047-7647200 | 0301-3277500 |
| 21 | Executive Engineer Q.B Link Division Farooqabad | 0563-874046 | 0563-876430 |
| 22 | Superintending Engineer Q.B Link Circle Farooqabad | 04945-874046 | 04945-874046 |
| 23 | Superintending Engineer, Lower Chenab Canal West Circle Faisalabad | 041-9200272 | 041-9200272 |
| 24 | Director Flood / Secretary, Flood Commission Punjab, Lahore | 042-99231614 | 0300-4777120 |
| 25 | Executive Engineer Qadirabad Barrage Division | 0547-550190 | 0547-550190 |
| 26 | Tele Office Qadirabad Barrage Division | 0547-550490 | 0547-550490 |
| 27 | Sub Divisional Officer, Flood Sub Division LCC(W) Jhang | 047-9200305 | 0316-7839321 |

CHAPTER-11

Standard operating procedure (SOP) for Breaching Sections

There is no breaching section under control of Jhang Canal Division Jhang. Hence action mentioned from serial No. 11.1 to 11.12 is not applicable.

| 11.1 | History of the breaching section | There is no breaching section under control of this office. |
| --- | --- | --- |
| 11.2 | Location, Design, Quantity and Variety of the explosive required for detonation. | There is no breaching section under control of this Division so there is no Location, Design, Quantity and Variety of the explosive required for detonation. |
| 11.3 | Arrangement of explosives and security of explosive stores | There is no breaching section under control of this office so there is no Arrangement of explosives and security of explosive stores. |
| 11.4 | List of the security staff alongwith detail of their training etc | There is no Security staff sanctioned for this office. |
| 11.5 | Detail of mechanical means as a standby arrangements in case of detonation failure | There is no breaching section under control of this office. |
| 11.6 | Duty Roster in case of critical situation | Duty Roster in case of critical situation mentioned at Page #41-43) |
| 11.7 | Breaching Committee with their action plan | There is no breaching section at any site of this office so no Breaching Committee with their action plan |
| 11.8 | List of the villages likely to be inundated in case of breach | List the villages likely to be inundated in case of breach at Page No.37. |
| 11.9 | Announcement and detail of evacuation arrangements | The matter related to Administration Department |
| 11.10 | Details of coordination with Civil/Army Authorities | According to the critical situation the coordination with the Civil / Army Authorities well in time. Flow |

| 11.11 | Parallel communication arrangements | According to the critical situation the coordination with the Civil / Army Authorities well in time. |
| --- | --- | --- |
| 11.12 | Index Plan | There is no breaching section under control of this office so there is no need of index plan |

Sub Divisional Officer,				Executive Engineer,

Flood Sub Division LCC(W),	 			Jhang Division LCC(W)

Jhang		.					Jhang.

Superintending Engineer,				Chief Engineer,

Lower Chenab Canal(W)Circle,			Faisalabad Irrigation Zone,

Faisalabad.						Faisalabad.

FLOOD FIGHTING PLAN- 2022.

PART – B

Chapter-12

VULNERABLE SITES ON FLOOD BUND/STRUCTURES:

THATTA MAHALLA FLOOD BUND &

JHANG FLOOD PROTECTION BUND

12.1	 APPREHENDED BREACH SITES IN FLOOD BUNDS/STRUCTURES

There is no apprehension site of flood bunds in Jhang Division

12.2	 OPERATION OF BREACHING SECTION

There is no breaching section in jurisdiction of Jhang Canal Division Jhang. The breaching section exists at Revaz Bridge and relates to Railway Department.

12.3	 BREACHES DUE TO RISING OF FLOOD WATER , DETERIORATION OF FLOOD BUNDS ETC

- Nil-

| Sr.No. | Name of Structure | Location of Vulnerable Site | Reference of contingency Plan |
| --- | --- | --- | --- |
| No vulnerable reach |

CHAPTER-13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES  LISTED ABOVE. EMERGENCY CONTINGENCY PLAN MUST INCLUDE:-

THATTA MAHALLA FLOOD BUND

13.1 	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

After Completion of work by PIU, Remodeling Selected reaches of Thatta Mahla Flood Bund there is no vulnerable sites on Thatta Mahla Flood Bund.

  - Detail of villages abadies likely to be affected and this should also be shown on the plan.

LIST OF THE VILLAGES LIKELY TO BE INUNDATED DURING VARIOUS FLOOD LIMITS

LOW FLOOD

Ballo Shahabal, Sultanpur, Koriana, Ramana.

MEDIUM FLOOD

Mauza Shamal,  Mauza Maghiana, Mauza Lindi  Bag, Chak  Shakhiana, Thatta Mahla.

HIGH FLOOD

Mauza Khewa, Mauza Khanuana, Mauza Pacca Wala, Mouza Kharora Baqar, Mauza Viglana , Thatti Rehmana, Mauza Ballian, Mauza Kurhian Wala,  Mauza Patuana, Mauza Hasnana,

LIST OF VILLAGES LIKELY TO BE MAROONED IN CASE OF BREACHING SECTION

Under mentioned Villages are likely to be marooned when the breaching section is operated.

Kot Khira , Vijhlana, Mouza Paccay wala

JHANG FLOOD PROTECTION BUND

13.1 	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS.

After Completion of work by PIU, Remodeling Selected reaches of Jhang Flood Protection Bund there is no vulnerable sites on Jhang Flood Protection Bund.

  - Detail of villages abadies likely to be affected and this should also be shown on the plan.

LIST OF THE VILLAGES LIKELY TO BE INUNDATED DURING VARIOUS FLOOD LIMITS

LOW FLOOD

Mouza Choori Noona, Mouza Maghiana , Mouza Baila Bungash

MEDIUM FLOOD

Mouza Diraj , Mouza Hasnana

HIGH FLOOD

Mouza Hasnana, Mouza Vijhlana, Mouza Kot Khaira, Mouza Malluana,

LIST OF VILLAGES LIKELY TO BE MAROONED IN CASE OF  BREACHING

Under mentioned Villages are likely to be marooned when the breaching section is operated.

Billi Kaleke,Asamo,Jandran ,Habib ,Pacca Wala

13.3 	Strategy and action taken be explained in detail.  This may include.

13.3.1	 Arrangements

13.3.2  Establishment of Flood Fighting Camps.

| Sr. No. | Description of Flood Fighting Camps | Location of Camps | Remarks |
| --- | --- | --- | --- |
| 1 | Jhang Flood Protection Bund | At RD:6+000. | There is sufficient Flood material are available alongwith duty staff officers/ officials |
| 2 | Jhang Flood Protection Bund | At RD:23+000. | There is sufficient Flood material are available alongwith duty staff officers/ officials . |
| 4 | Thatta Mahalla Flood Bund | At RD:1+500 | There is sufficient Flood material are available alongwith duty staff officers/ officials |
| 5 | Thatta Mahalla Flood Bund | At RD:11+500 | There is sufficient Flood material are available alongwith duty staff officers/ officials |

13.3.3  Duties of Officers/Officials and their camp sites

During High Flood Flow   	(as per page #43-44.)

| Name of Bund | Office Incharge | Field Staff on Flood Duty | Reach of Duty | Departmental Labour |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Regular | Temporary Estt: | Sectional Estt: |  |
| Thatta Mahla Flood Bund | Sub Divisional Officer flood Bund Sub Division & Sub Divisional Officers, Wer , Dhaular Sub Division with two Magistrates. | Sub Engineer, SCR ----------------- Wer ------------------ MRW | RD. 0-6 RD: 6+000 -11+500 | 2 2 | 8 6 | 10+10 Wer & JRA 10+10 LKN & MRW | Sub Engineer, Thatta Mahla to Keep Vigilance in reach RD: 0+000 -11+500 and arrange Labour & Material at Thatta Mahla Flood Bund. |
|  |  | Zilladar BLN Sub Engineer Tawan --------------- Jaura Zilladar SCR: | RD:11+500 -15+000 RD: 15-31 RD: 31-51 | 1 1 - | 6 5 5 6 | 10 ASB: 10 TWN 10 KRW 30 70 |  |
| Jhang Flood Protection Bund | Sub Divisional Officer Flood bund Sub Division & Sub Divisional Officers, Wer, Veryam Sub Division & Deputy Collector with two Magistrates | Sub Engineer JWA Sub Engineer As-haba Sub Engineer VRM Zilladar--------- Sub Engineer BLN: ------------------ Gojra Zilladar---------------- Sub Engineer AKW Zilladar Ashaba | RD: 0-18 RD: 18-31 RD: 31-42 RD: 42-71 (Tai) | 1 2 3 1 7 | 4 10 6 10 31 | 10 Veryam 10 + 5 JWA BLN 10 GRA 10 AKW 45 | Sub Engineer Jhang Flood Bund shall be In-charge of store At RD: 23,000 |

Sub Divisional Officer, Flood Bund Sub Division will be in charge of overall embankments

13.3.4  Departmental Machinery available

There is no departmental machinery in control of Jhang Canal Division Jhang. However in case of any emergency during flood season 2022, the Government Machinery / Bulldozers of Agricultural Engineering Department Punjab will be arranged.

13.3.5  Machinery available from Private Source

If the exceptionally high flood is forecasted by the Meteorological Department, the following machinery will be arranged / hired from private source.

1 No. Bulldozer, 2 No. Excavator Machines, 6 No. Tractors with trollies and 1 No. tractor with blade will be arranged for Thatta Mahla Flood Bund and same equipment / machinery for Jhang Flood Protection Bund.

13.3.6 FLOOD FIGHTING MATERIAL REQUIRED

| Sr. No. | Name of Item | Unit | Total Required Quantity | Available Quantity | Required Quantity | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Axes | No. | 80 | 20 | 60 | Required flood fighting material will be purchased before 30.06.2024 |
| 2 | Bamboos 8' to 10' (for Lighting arrangements) | No. | 904 | 154 | 750 |  |
| 3 | Chouldaries | No. | 5 | 0 | 5 |  |
| 4 | E.G. Bags | No. | 4500 | 1500 | 3000 |  |
| 5 | Folding Chair | No. | 24 | 0 | 24 |  |
| 6 | Folding Table | No. | 4 | 0 | 4 |  |
| 7 | G.I. Buckets | No. | 100 | 0 | 100 |  |
| 8 | Generator (8.00 K.Watts) | No. | 2 | 0 | 2 |  |
| 9 | Hand Saws | No. | 4 | 0 | 4 |  |
| 10 | Handle for Kassi / Axes | No. | 200 | 0 | 200 |  |
| 11 | Kassi with Handles | No. | 625 | 50 | 575 |  |
| 12 | M. Oil | Litter | 20 | 0 | 20 |  |
| 13 | Manila Rope | Kg | 50 | 0 | 50 |  |
| 14 | Petrol for Generator | Litter | 200 | 0 | 200 |  |
| 15 | Steel Charpoy | No. | 20 | 0 | 20 |  |
| 16 | Torches Chargeable | No. | 52 | 2 | 50 |  |
| 17 | Umbrella | No. | 20 | 0 | 20 |  |
| 18 | Cotton bags | No. | 47 | 4 | 43 |  |
| 19 | Jackets | No. | 25 | 2 | 23 |  |
| 20 | Polyethene Sheet | Kg | 5000 | 500 | 4500 |  |

13.3.7  FLOOD FIGHTING MATERIAL AVAILABLE

| Sr. No. | Name of Item | Unit | Total Required Quantity | Available Quantity | Required Quantity |
| --- | --- | --- | --- | --- | --- |
| 1 | Axes | No. | 80 | 20 | 60 |
| 2 | Bamboos 8' to 10' (for Lighting arrangements) | No. | 904 | 154 | 750 |
| 3 | Chouldaries | No. | 5 | 0 | 5 |
| 4 | E.G. Bags | No. | 4500 | 1500 | 3000 |
| 5 | Folding Chair | No. | 24 | 0 | 24 |
| 6 | Folding Table | No. | 4 | 0 | 4 |
| 7 | G.I. Buckets | No. | 100 | 0 | 100 |
| 8 | Generator (8.00 K.Watts) | No. | 2 | 0 | 2 |
| 9 | Hand Saws | No. | 4 | 0 | 4 |
| 10 | Handle for Kassi / Axes | No. | 200 | 0 | 200 |
| 11 | Kassi with Handles | No. | 625 | 50 | 575 |
| 12 | M. Oil | Litter | 20 | 0 | 20 |
| 13 | Manila Rope | Kg | 50 | 0 | 50 |
| 14 | Petrol for Generator | Litter | 200 | 0 | 200 |
| 15 | Steel Charpoy | No. | 20 | 0 | 20 |
| 16 | Torches Chargeable | No. | 52 | 2 | 50 |
| 17 | Umbrella | No. | 20 | 0 | 20 |
| 18 | Cotton bags | No. | 47 | 4 | 43 |
| 19 | Jackets | No. | 25 | 2 | 23 |
| 20 | Polyethene Sheet | Kg | 5000 | 500 | 4500 |

  - Detail of other infrastructure like electric, Sui Gas, Telephone installations, road network, other buildings, canals and drainage network.

List of Infrastructure coming under water is as under:-

1.	Government Hospital	=	2 Nos.

2.	Private Hospital 		=	16 Nos.

3.	Schools 			=	16 No.

4.	D.C Office 			=	1 NO.

5.	High Ways Offices 	=	1 No.

6.	Irrigation Offices 		=	1 No.

7.	Rail Way Lines 		=	1 No,

8.	Main Pacca Roads 	=	3 Nos.

9.	Courts 			=	1 No.

10.	P.T.C.L Offices 		=	1 No.

11.	W.A.P.D.A Offices 		=	1 No.

12.	SUI GASS Offices	 	=	1 No.

13.	Private Property Like Kacha Houses

Sub Divisional Officer,					Executive Engineer,

Wer Sub Division L.C.C (W) 					Jhang Division L.C.C(W)

Jhang		.						Jhang.

Superintending Engineer,				Chief Engineer

Lower Chenab Canal West Circle				Faisalabad Irrigation Zone,

Faisalabad.							Faisalabad.

CHAPTER-14

ACTION PLAN

14.1 RE-SHUFFLING/ RECOUPING PLAN OF RESERVE STONE

DEPARTMENTALLY.

Through Tractor Trolly.

14.2 	DETAIL OF INLET/ OUTLET CROSSING ALONG WITH CLOSING METHODOLOGY

-N.A-

| 14.6 | POLICE DEPLOYMENT PLAN |
| --- | --- |

Performa-1

| Sr. No. | Site of Breaching Section | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector /Sub Inspector / A.S.I | Constable |  |
| Relates to Civil Administration Department |

Performa-2

| Sr. No. | Vulnerable Sites used for illegal cuts during floods | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector /Sub Inspector / A.S.I | Constable |  |
| Relates to Civil Administration Department |

Performa-3

| Sr. No. | Name of Barrage | Concerned Canal Division | Concerned Police Station and District | Police Persons Deployed | Remarks (if any) |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Inspector /Sub Inspector / A.S.I | Constable |  |
| Relates to Civil Administration Department |

| 14.7 | DETAILS OF SYNTHETIC BAGS WITH CAPACITY OF 500 KG AND 1000KG |
| --- | --- |

There is no requirement of synthetic bags for vulnerable reaches after strengthening of flood bunds under work Remodeling of Selected reached by PIU.

| 14.8 | DETAILS OF POLYTHENE SHEET OF BLACK COLOUR TO PROTECT UPSTREAM SLOPE AGAINST WAVE ACTION AND TO CONTROL SEEPAGE THROUGH EMBANKMENTS |
| --- | --- |

| Sr. No. | Name of Flood Bund | Unit | Total Required Quantity | Available Quantity | Required Quantity |
| --- | --- | --- | --- | --- | --- |
| 1 | Thatta Mahla Flood bund | Kg.. | 2000 | 150 | 1850 |
| 2. | Jhang Flood Protection Bund | Kg. | 3000 | 350 | 2650 |
|  | Total | Kg | 5000 | 500 | 4500 |

CHAPTER-15

| BACK UP DIVISIONS (IN CASE OF BREACH) | N.A |
| --- | --- |

Faisalabad  Drainage Division , Faisalabad.