IRRIGATION DEPARTMENT

FLOOD FIGHTING PLAN

FOR THE YEAR 2024

SHAHDARA CANAL DIVISION,

SHAHDARA

UPPER CHENAB CANAL CIRCLE 	          IRRIGATION LAHORE ZONE

LAHORE					       LAHORE

I  N  D  E  X

Flood Fighting Plan 2024

| Chapter | PART (A) | Page No |
| --- | --- | --- |
| 1 | Salient feature of Shahdara Canal Division | 1 |
| 1.1 | Location | 2 |
| 1.2 | General Description | 2-3 |
| 1.3 | Administrative setup | 4 |
| 2 | Flood Protection and River Training Works | 5 |
| 2.1 | Design parameter of Training Works | 6-7 |
| 2.2 | Location Map | 8 |
| 3 | Brief history of past flood events | 9-10 |
| 4 | Design Data, History peak flood data and previous five years flood data of Head Works/Barrage and or other control points | 11-12 |
| 4.1 | Flood Limits | 13 |
| 4.2 | Time Lags of Floods | 13 |
| 4.3 | Highest Floods | 14 |
| 4.4 | Peak Discharges | 14 |
| 5 | Flood Fighting Strategy | 15-17 |
| 6 | Flood Damages Restoration Works | 18-19 |
| 7 | Flood Fighting Watching Arrangements | 20 |
| 7.1 | Pre-flood Arrangements | 21 |
| 7.2 | Watching Establishment | 21 |
| 7.3 | Arrangement at Sensitive sites | 22 |
| 7.4 | Watching Material | 22 |
| 7.5 | Arrangement for Sounding & Probing | 22 |
| 7.6 | Lightening Arrangement | 22 |
| 7.7 | Ration Arrangement | 23 |
| 7.8 | P.O.L Arrangements | 23 |
| 7.9 | Transportation | 23 |
| 7.10 | Law & Order | 23 |
| 7.11 | Medical Arrangement for Labour | 23 |
| 7.12 | Liaison with other Department | 23 |
| 7.13 | Role of Army | 23 |
| 7.14 | Duties of Telephone Attendant | 23 |
| 7.15 | Wireless Arrangements | 23 |
| 8 | Detail of Encroachment | 24-25 |
| 9 | Duty roaster / Flood Fighting Programme | 26-27 |
| 10 | Emergency Telephone Numbers | 28-29 |
| 11 | Standard operating procedure(SOP) for Breaching Sections | 30 |
| 11.1 | History of the breaching Section | 31 |
| 11.2 | Location, Design, Quantity and variety of the explosive required for detonation. | 32 |
| 11.3 | Arrangement of explosive and security of explosive stores | 32 |
| 11.4 | List of the security staff along with detail of their training etc. | 33 |
| 11.5 | Detail of mechanical means as a standby arrangements in case of detonation failure | 33 |
| 11.6 | Duty Roster in case of critical situation | 33 |
| 11.7 | Breaching Committee with their action plan | 33-34 |
| 11.8 | List of the villages likely to be inundated in case of breach | 35 |
| 11.9 | Announcement and detail of evacuation arrangements | 36 |
| 11.10 | Details of coordination with Civil/Army Authorities | 36 |
| 11.11 | Parallel communication arrangements | 36 |
| 11.12 | Index plan | 37 |
| Chapter | PART (B) |  |
| 12 | Vulnerable sites on flood Bund Structures | 38 |
| 12.1 | Apprehended breaches in Flood Bund/Structures | 39 |
| 12.2 | Operation of Breaching sections | 39 |
| 12.3 | Breaches due to rise of flood water, deterioration of flood bunds | 39 |
| 13 | Emergency Contingency Plan for vulnerable site No. 1. | 40 |
| 13.1 | Plan showing route of Flood Water coming out of the breach supported with levels. | 41-42 |
| 13.2 | Detail of villages abadies likely to be affected and this should also be shown on the plan. | 43 |
| 13.3 | Strategy and action taken be explained in detail. This may include: | 44 |
|  | 13.3.1 Arrangements | 44 |
|  | 13.3.2 Establishment of Flood Fighting Camps | 44 |
|  | 13.3.3 Duties of Officers/Officials and their camp sites | 45 |
|  | 13.3.4 Departmental Machinery Available | 45 |
|  | 13.3.5 Machinery Available from Private source | 45 |
|  | 13.3.6 Flood Fighting Material Available (SITE-I) | 46 |
|  | 13.3.7 Flood Fighting Material Required (SITE-I) | 47 |
| 13.4 | Detail Of Other Infrastructure Like Electric, Sui Gas, Telephone Installations, Road Network, Other Buildings, Canals And Drainage Network. | 48 |
|  | Emergency Contingency Plan for vulnerable site No. 2. |  |
| 13.5 | Plan showing route of Flood Water coming out of the breach supported with levels. | 49-50 |
| 13.6 | Detail of villages abadies likely to be affected and this should also be shown on the plan. | 51 |
| 13.7 | Strategy and action taken be explained in detail. This may include: | 52 |
|  | 13.7.1 Arrangements | 52 |
|  | 13.7.2 Establishment of Flood Fighting Camps | 52 |
|  | 13.7.3 Duties of Officers/Officials and their camp sites | 53 |
|  | 13.7.4 Departmental Machinery Available | 53 |
|  | 13.7.5 Machinery Available from Private source | 53 |
|  | 13.7.6 Flood Fighting Material Available (SITE-II) | 54 |
|  | 13.7.7 Flood Fighting Material Required (SITE-II) | 55 |
| 13.8 | Detail Of Other Infrastructure Like Electric, Sui Gas, Telephone Installations, Road Network, Other Buildings, Canals And Drainage Network. | 56 |
| 14 | Action Plan | 57 |
| 14.1 | Re-shuffling / Recouping plan of reserve stone Departmentally | 58 |
| 14.2 | Detail of inlet / outlet crossing along with closing methodology | 58 |
| 14.3 | Development Machinery (Medium to high flood) | 59 |
| 14.4 | Development Machinery (High to very high flood) | 60 |
| 14.5 | Development Machinery (Very high to exceptionally high flood) | 61 |
| 14.6 | Police development plan | 62 |
| 14.7 | Detail of synthetic bags with capacity of 500 kg and 1000 kg | 62 |
| 14.8 | Details of polythene sheet of black colour to protect upstream slope against wave action and to control seepage through embankments to p | 63 |
| 15 | Back up division (In case of breach) | 64 |

PART – A

CHAPTER-1

SALIENT FEATURE OF SHAHDARA CANAL DIVISION

CHAPTER-1

SALIENT FEATURE OF SHAHDARA CANAL DIVISION

1.1	LOCATION

Shahdara Canal Division falls in Civil Districts of Gujranwala, Sialkot, Sheikhupura and partially in Lahore. Canal water is supplied to cultureable commanded area of 6.18 Lac Acres.

1.2	GENERAL DESCRIPTION

409.33 miles long network of canals irrigates the aforementioned vast commanded area. Main features i.e. length of canals, discharges, detail of area and water allowances / intensity are given below:-

TOTAL LENGTH OF CHANNELS

a)	Main canal and Branches			=	11.9	Miles.

b)	Major Distys and Minors			=	397.43 Miles.

Total:			=	409.33 Miles.

BRIEF 0F DISCHARGE SUPPLY COMPONENTS

SHAHDARA CANAL DIVISION offtakes from BRBD & M.R Link Canal system.

There are following major canal, systems off taking from BRBD Link & M.R. Link.

1.	Sadhoke Disty.			= 	Non Perennial

2.       Muridke Branch.			=	Non Perennial

3.       Muridke Disty                                  Non Perennial

4.	Sohal Disty.				= 	Non Perennial

5.	Shahdara Disty			= 	Non Perennial

6.	Begumpur Disty 			=      	Non Perennial

7.	Badomalhi Disty			=	Non Perennial

INTENSITY AND WATER ALLOWANCES

Upper Chenab Canal System

Non Perennial

Intensity 			=  25%

Water Allowance 		=  3.79 Cs %o Acres.

.

CIVIL JURISDICTION

The civil jurisdiction of the Sub Divisions is as under: -

S.# 		Name of Sub Division 				District

1.	Sadhoke Sub Division UCC		=	Gujranwala, Sialkot,

Sheikhupura

2.	Muridke Sub Division UCC		=	Sheikhupura.

3.	Shahdara Sub Division UCC.		=	Sheikhupura , Lahore&

Narowal.

1.3	ADMINISTRATIVE SETUP:

The Executive Engineer, Shahdara Canal Division is administrative head of the Shahdara Canal Division. The organization chart is as under:-

CHAPTER-2

FLOOD PROTECTION AND RIVER TRAINING WORKS

CHAPTER-2

FLOOD PROTECTION AND RIVER TRAINING WORKS

2.1	DESIGN PARAMETER OF TRAINING WORKS

Shahdara Canal Division Shahdara is the 2nd Division of the Upper Chenab Canal Circle.

There are numerous drains and nullah’s around the canal system of Shahdara Canal Division. Rain and flood water flows to these nulláh’ s and drains. Major nullah is known as Deg Nullah and it falls into River Ravi. These Nullahs are under administrative control of Rechna Drainage Division, Sheikhupura and Gujranwala Drainage division. The Bunds fall under the jurisdiction of Shahdara Canal Division as under:-

i).DETAIL OF BUNDS ALONG DEG NULLAH WITH DESIGNED DATA

| a). | Sadhoke Sub Division | Length | Top Width | Side slope |
| --- | --- | --- | --- | --- |
|  |  |  |  | River Side | Country Side |
| i) | Ananta Minor Bund RD. 0+000 to 19+500. | 19500 ft | 15 ft | 3:1 | 1.5:1 |
| ii) | Ghulab Singh Minor Bund RD. 9+750 to 33+500. | 23750 ft | 15 ft | 3:1 | 1.5:1 |
| iii) | Dandian Disty Bund RD. 45+500 to 64+000. | 18500 ft | 15 ft | 3:1 | 1.5:1 |
| iv) | Begumpur Disty Bund 0+000 to 13+000 | 13000 ft | 25 ft | 3:1 | 2:1 |
| v) | Talwandi Disty Bund 0+000 to 30+000 | 30000 ft | 25 ft | 3:1 | 2:1 |
| vi) | Ratta Minor RD. 0+000 to 20+500 | 20500 ft | 25 ft | 3:1 | 2:1 |
| b). | Muridke Sub Division |  |  |  |  |
| 1. | Chakian Bund RD. 0+000 to 9+000 | 9000 Ft | 15 ft | 3:1 | 1.5:1 |

ii_. DETAIL OF BUNDS ALONG RIVER RAVI WITH DESIGNED DATA

a)	The hydraulic data of the Shahdara Disty Flood Bund from RD. 0+000 – 72+000 is as under:-

| Reach RD | Top Width | Free Board | Side Slope |
| --- | --- | --- | --- |
|  |  |  | River Side | Country Side |
| 0+000 to 65+000 | 25 ft. | 6.00’ above H.F.L of 1988 | 3:1 | 2:1 |
| 65+500 to 72+000 | 20 ft. | 3.00’ above H.F.L of 1973 | 3:1 | 2:1 |

b)	The hydraulic data of J-Head Spur Babakwal off-taking from RD. 39+000/L of Shahdara Disty Flood Bund is as under :-

| Reach RD | Top Width | Free Board | Side Slope |
| --- | --- | --- | --- |
|  |  |  | U/S Side | D/S Side |
| RD 0+000 to 5+400 | 25 ft. | 6.00’ above H.F.L of 1988 | 3:1 | 2:1 |

No doubt that all the flood bunds are very important but specially Shahdara Disty Flood Bund is the most important as it envisages the safety of the Shahdara / Lahore City and the allied structure of’ River Ravi.

Executive Engineer,

Shahdara Canal Division,

Shahdara.

2.

CHAPTER-3

BRIEF HISTORY OF PAST FLOOD EVENTS

CHAPTER-3

BRIEF HISTORY OF PAST FLOOD EVENTS

Shahdara Disty Flood protection bund consists of embankment from               RD. 0+000 to 72+000 along the Shahdara Disty and a J-Head Spur            off-taking at RD. 39+000/L of Shahdara Disty Flood Protection Bund, which has been constructed to protect Shahdara Disty and the adjoining area on right side of the Disty.

FLOOD 2008 & 2009

During flood season 2008-09 & 2009-10, the River changed its meandering and directly attacked D/S shank of the Spur and badly damaged the shank of spur and tried to bisect spur into two parts but timely measures were taken and the spur was saved.

FLOOD 2018

River Ravi is a meandering River of incised character. Due to these meandering phenomena, the river creates serious problem in its entire length. During the flood season 2023, the maximum discharge passed at Shahdara on 21.07.2023 was 36477 Cusecs which falls in the category of medium flood.

In order to protect the graveyard and flood bund, four number of stone studs have been constructed during current financial year.

Executive Engineer,

Shahdara Canal Division,

Shahdara.

CHAPTER-4

DESIGN DATA, HISTORY PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS/BARRAGE AND OR OTHER CONTROL POINTS

CHAPTER-4

DESIGN DATA, HISTORIC PEAK FLOOD DATA AND PREVIOUS FIVE YEARS FLOOD DATA OF HEAD WORKS / BARRAGES AND OTHER CONTROL POINTS.

DESIGN DATA OF SHAHDARA DISTY FLOOD PROTECTION BUND

The hydraulic data of the Shahdara Disty Flood Bund from RD. 0+000 to 72+000 is as under:-

| Reach RD | Top Width | Free Board | Side Slope |
| --- | --- | --- | --- |
|  |  |  | River Side | Country Side |
| 0+000 to 65+000 | 25 ft. | 6.00’ above H.F.L of 1988 | 3:1 | 2:1 |
| 65+500 to 72+000 | 20 ft. | 3.00’ above H.F.L of 1973 | 3:1 | 2:1 |

DESIGN DATA OF BUND ALONG DEG NULLAH

a)	Sadhoke Sub Division

| S.# | Name of Bund | Length | Top width | Side slope |
| --- | --- | --- | --- | --- |
|  |  |  |  | River Side | Country Side |
| i) | Ananta Minor Bund RD. 0+000 to 19+500. | 19500 ft | 15 ft | 3:1 | 1.5:1 |
| ii) | Ghulab Singh Minor RD. 9+750 to 33+500. | 23750 ft | 15 ft | 3:1 | 1.5:1 |
| iii) | Dandian Disty Bund RD. 45+500 to 64+000. | 18500 ft | 15 ft | 3:1 | 1.5:1 |
| iv) | Begumpur Disty RD. 0+000 to 13+000 | 13000 ft | 25 ft | 3:1 | 2:1 |
| iv) | Talwandi Disty RD. 0+000 to 30+000 | 30000 ft | 25 ft | 3:1 | 2:1 |
| v) | Ratta Minor RD. 0+000 to 20+500 | 20500 ft | 25 ft | 3:1 | 2:1 |

b)	Muridke Sub Division

| S.# | Name of Bund | Length | Top width | Side slope |
| --- | --- | --- | --- | --- |
|  |  |  |  | River Side | Country Side |
| i) | Chakian Bund RD. 0+000 to 9+000 | 9000 ft | 15 ft | 3:1 | 1.5:1 |

PREVIOUS FIVE YEAR FLOOD DATA

| S.# | Date | HFL at Zero gauge critical level 693.50 | HFL at RD. 65000 junction point of SDR Disty Flood Bund (Critical level 699.00’) | Discharge of River Ravi at Shahdara (Cs) |
| --- | --- | --- | --- | --- |
| 1. | 09.08.2018 | - | 677.70 | 35894 |
| 2. | 19.08.2019 | - | 677.00 | 37200 |
| 3. | 28.08.2020 | - | 676.50 | 34531 |
| 4. | 21-07-2021 | - | 776.90 | 36477 |
| 5. | 02.08.2022 | - | 676.20 | 31415 |
| 6. | 29-07-2023 | - | 677.10 | 38060 |

4.1	FLOOD LIMITS

| S.# | Category of Flood | Ravi at | Shahdara Railway Bridge | Deg at Qila Soba Singh |
| --- | --- | --- | --- | --- |
|  |  | Jassar | Ravi Syphon |  |  |
|  |  | Cs. In Lacs | Cs. In Lacs | Cs. In Lacs | Cs. In Lacs |
| 1. | Low Flood | 0.50 | 0.40 | 0.40 | 0.036 |
| 2. | Medium Flood | 0.75 | 0.65 | 0.65 | 0.075 |
| 3. | High Flood | 1.00 | 0.90 | 0.90 | 0.150 |
| 4. | Very High Flood | 1.50 | 1.35 | 1.35 | 0.300 |
| 5. | Super High Flood | 2.00 | 1.80 | 1.80 | 0.350 |

4.2	TIME LAGS OF FLOODS

| River | Site | Design Capacity (Cs) | Low Flood (Cs) | Med: flood (Cs) | High Flood (Cs) | Very High Flood (Cs) | Ex: high Flood (Cs) | Time lag (Hrs) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | From | To |  |  |  |  |  |  |  |
| Ravi | Kot Naina | Jassar | 2.75 | 0.50 | 0.75 | 1.00 | 1.50 | 2.00 | 12 |
|  | Jassar | Ravi Siphon | 4.5 | 0.40 | 0.65 | 0.90 | 1.35 | 1.80 | 18 |
|  | Ravi Siphon | SDR | 2.5 | 0.40 | 0.65 | 0.90 | 1.35 | 1.80 | 8 |

4.3	HIGHEST FLOODS

| S.# | Date | HFL at RD. 65000 junction point of SDR Disty Flood Bund (Critical level 699.00’) | Discharge of River Ravi at Shahdara (Cs) |
| --- | --- | --- | --- |
| 1. | 21.09.1950 | 691.80 | 193000 |
| 2. | 06.10.1955 | 695.00 | 527315 |
| 3. | 11.08.1973 | 693.02 | 237380 |
| 4. | 27.09.1988 | 694.70 | 326100 |

4.4	PEAK DISCHARGES

| S.# | Date | HFL at RD. 65000 junction point of SDR Disty Flood Bund (Critical level 699.00’) | Discharge of River Ravi at Shahdara (Cs) |
| --- | --- | --- | --- |
| 1. | 09.08.2018 | 677.70 | 35894 |
| 2. | 19.08.2019 | 677.00 | 37200 |
| 3. | 28.08.2020 | 676.50 | 34531 |
| 4. | 21-07-2021 | 776.90 | 36477 |
| 5. | 02.08.2022 | 676.20 | 31415 |
| 6. | 29-07-2023 | 677.10 | 38060 |

Executive Engineer,

Shahdara Canal Division,

Shahdara.

CHAPTER-5

FLOOD FIGHTING STRATEGY

CHAPTER-5

FLOOD FIGHTING STRATEGY

The total length of River Training Works of River Ravi has been divided into 2 sectors

i)	Reach RD. 0+000 to 40+000 Babakwal

ii)	Reach RD. 40+000 to 72+000 Haji Kot Hut

Under the normal conditions, the bund will be supervised by the Sub Divisional Officer, Shahdara Sub Division UCC and his Sub Engineers, when the discharge in the River Ravi at Jassar reaches 1.0 lac Cs: or rising.

Sector-I   	REACH RD. 0+000 TO 40+000 BABAKWAL

The reach from R.D 0+000 to 40+000 will be supervised by the Sub Divisional Officer, Muridke Sub Division UCC along with his Sub Engineer, Muridke, Ahdian and Mehta Suja with the camp at Babakwkal Hut. Sub Divisional Officer Muridke Sub Division UCC will also bring all his establishment of the canal system along with him for watching of the bund day and night.

Sector-2	REACH RD. 40+000 TO 72+000 HAJI KOT HUT

Sub Divisional Officer, Shahdara Sub Division UCC along with the Sub Engineer, Shahdara, Rayya with all the establishment of channels will watch the bund day and night.

The camp of Sub Divisional Officer, Shahdara Sub Division UCC and his establishment will be at junction point. Sub Divisional officer, Shahdara Sub Division UCC will be responsible for making all arrangements of watching and providing T&P stock at both camp sites. Sub Divisional Officer, Shahdara Sub Division UCC will further check and shift all the flood fighting materials at both the camp sites before 01/07/2022 or earlier on the occurrence of flood.

i)	Sub Divisional Officer, Shabdara Sub Division UCC is directed to get the emergency telephone installed at Babakwal Rest House before 1st July of every year. Divisional Engineer (PTCL) is requested to co-operate in this connection on emergent basis.

ii)	Electrification and Light arrangements are to be made from the 1st July. Sub Divisional Officer, Shahdara Sub Division UCC will arrange temporary power connection well before the above dates. A standby generator is also kept ready for generation of electricity during load shedding hours or power failure.

iii)	The emergency flood fighting material as appended here with at page 40 is put at junction point and Haji Kot by the Sub Divisional Officer Shahdara and Sub Engineer Shahdara to cater for the requirement with the consultation of the Executive Engineer, Shahdara Canal Division, Shahdara. The flood fighting material will be used in the following reaches in cases of emergency:-

a) 	From junction point to Haji Kot.

b)	From Haji Kot to Head.

ACTION PLAN FOR DEPLOYMENT OF LABOUR

| S.# | Condition | Labour |
| --- | --- | --- |
| 1. | Medium Flood | 49 Regular & Work charge establishment will be deployed during Medium Flood |
| 4. | High Flood | 56 Regular & Work charge establishment will be deployed during High Flood |
| 5. | Very High Flood | 112 Regular & Work charge establishment will be deployed during Very High Flood |
| 6. | Exceptionally High Flood | 140 Regular & Work charge establishment will be deployed during Exceptionally High Flood |

ACTION PLAN FOR DEPLOYMENT OF MACHINERY

| S.# | Condition | Machinery |
| --- | --- | --- |
| 1. | Medium to High Flood | 01 No. Tractor with blade and water tank for Each Site. |
| 2. | Very Exceptionally High Flood | 01 No. Excavator and 5 No. Tractor Trollies For Each Site. |

Executive Engineer,

Shahdara Canal Division,

Shahdara.

CHAPTER-6

FLOOD DAMAGES RESTORATION WORKS

CHAPTER-6

FLOOD DAMAGES RESTORATION WORKS

No Such Work

Executive Engineer,

Shahdara Canal Division,

Shahdara.

CHAPTER-7

FLOOD FIGHTING WATCHING ARRANGEMENTS

CHAPTER-7

FLOOD FIGHTING WATCHING ARRANGEMENTS

7.1	PRE-FLOOD ARRANGEMENT

- Pre-Flood inspections of Flood Bunds have been carried out by the Departmental inspection team and concerned Executive Engineer, and Sub Divisional Officer.

- Purchase of Flood Fighting Material is under process.

- Repair to defective Liners of Breaching Section is under way.

- Repairing & painting of gauges and critical gauge will be done before flood season.

| Site | Sanctioned Limit (Lac Cft) | Available (Lac Cft) | Balance (Lc Cft) |
| --- | --- | --- | --- |
| J-Head Spur RD.39000 | 1 .0 | 0.78 | 0.22 |
| Shahdara Disty Bund | 2.50 | 2.00 | 0.50 |
| Total | 3.50 | 2.78 | 0.72 |

7.2	WATCHING ESTABLISHMENT

From the first of June watching of the bund is started with following scale:

| S.# | Condition | Scale Reach RD 0 to 72 | Remarks |
| --- | --- | --- | --- |
| 1 | 1st June | 1 beldar per 2.5 miles (1x14/2.5x1) | 6 Beldar from Regular Establishment |
| 2 | From 1st July, when there is no spill in River Ravi | 1 beldar in 2 miles 3 shifts (1x14/2x3) | 21 Beldar from Regular Establishment |
| 3 | River spills but does not touch bund | 1 man per mile 3 shifts (1x14x3) = 1 man per 2 mile night time (1x14/2X1) = | 42 07 |
| Total :- | 49 Seasonal Work Charge |
| 4 | Depth of water 0—2 Ft. along the bund | 1 man per mile 3 shifts (1x14x3) = 1 man per mile night time (1x14x1) = | 42 14 |
| Total :- | 56 |
| 5 | Water depth 2 – 4 Ft along the Bund | 1 man per ½ mile 3 shifts (1x14/0.5x3) = 1 man per ½ mile for night (1x14/0.5x1) = | 84 28 |
| Total :- | 112 |
| 6 | 4’.O and above upto critical level 699’.OO till breaching action, | 1 man per ½ mile 3 shifts (1x14/0.5x3) 1 man 1/4 mile for night (1x14/0.25x1) | 84 56 |
| Total :- | 140 |
|  |  | 30 Men per shift in three shifts of 08 hours & 70 men per shift Civil labour including volunteers if necessary accordingly |  |

7.3	ARRANGEMENT AT SENSITIVE SITES

Necessary Flood Fighting Camps would be shifted at Sensitive sites on 16th June (Start of Flood Season)

i)	First camp will be established at Babakwal Rest House at RD. 39+000 of Shahdara Disty Flood Protection Bund.

| Site | Sanctioned Limit | Available | Balance |
| --- | --- | --- | --- |
| J-Head Spur RD.39000 | 1 Lac Cft | 0.78 Lac Cft | 0.22 Lac Cft |

ii)	2nd camp will be established at Haji Kot hut at RD. 61+200 of Shahdara Disty Flood Protection Bund.

| Site | Sanctioned Limit | Available | Balance |
| --- | --- | --- | --- |
| Shahdara Disty Bund | 2.50 Lac Cft | 2.00 Lac Cft | 0.50 Lac Cft |

NOTE	Balance stone will be procured after receipt of necessary funds.

7.4	WATCHING MATERIAL

| Name of Article | Required Qty | Available Qty | Balance Qty to be purchased | Remarks |
| --- | --- | --- | --- | --- |
| Generator | 3 | - | 3 | Balance qty will be purchase after receipt of funds. |
| Gas Lamp | 12 | - | 12 |  |
| Laltains | 150 | 48 | 102 |  |
| Torches | 9 | 3 | 6 |  |

7.5	ARRANGEMENT FOR SOUNDING AND PROBING

i).	Arrangement of boats for observation of Sounding & Probing in case of critical situation against rising of rivers.

ii).	Provision of sounding rods

7.6	LIGHTING ARRANGEMENT

Executive Engineer LESCO Shahdara Division and S.D.O Electricity G.T Road Sub Division Shahdara shall ensure smooth and sustained flow of electricity during flood emergency. Standby Generator will also made available at bund.

7.7	RATION ARRANGEMENT

District Administration is responsible for providing ration arrangements for evacuated / displaced peoples.

7.8	P.O.L ARRANGEMENT FOR VEHICLE

The requirements of H.S Diesel oil at Shahdara Disty Flood Protection Bund shall be 300 liters during flood season.

7.9	TRANSPORTATION

One No. Govt. Tractor Trolley will be required for the transportation of Flood Fighting Material and labour in case of emergency.

7.10	LAW AND ORDER

Maintenance of Law and order is the responsibility of District Administration and law enforcing agencies of District Sheikhupura.

7.11	MEDICAL ARRANGEMENT FOR LABOUR

Necessary medicines will be arranged from the Health Department to combat with the out breaks of expected epidemics.

7.12	LIAISON WITH OTHER DEPARTMENT

Executive Engineer, Shahdara Canal Division Shahdara and Sub Division Officer, Shahdara Sub Division will keep liaison with their counterparts of other Department as well as the Higher Authorities of the parent Department.

  - ROLE OF THE ARMY

Pakistan Army (16 Engineering Corps Lahore) is responsible for blow up of Breaching Section as and when the operating Committee takes decision for its operation.

7.14	DUTY OF TELEPHONE ATTENDANT

Telephone attendants will perform their duty for 24 hours during flood season at Divisional Telegraph Office                             No. 04299333439

7.15	WIRELESS ARRANGEMENTS

Wireless Station established at Police Head Quarter at Sheikhupura during flood season and will communicate the flood situation to all concerned.

Executive Engineer,

Shahdara Canal Division,

Shahdara.

CHAPTER-8

DETAIL OF ENCROACHMENT

CHAPTER-8

DETAIL OF ENCROACHMENT

| Sr. No. | Total Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| 1 | NIL | NIL | NIL | NIL |

DETAIL OF CRITICAL ENCROACHMENT

| Sr. No. | Total Critical Encroachments | Removed | Remaining | Remarks |
| --- | --- | --- | --- | --- |
| 1 | NIL | NIL | NIL | NIL |

Executive Engineer,

Shahdara Canal Division,

Shahdara.

CHAPTER-9

DUTY ROASTER / FLOOD FIGHTING PROGRAMME

CHAPTER-9

DUTY ROSTER/FLOOD FIGHTING PROGRAM

Executive Engineer, Shahdara Canal Division is over all in charge of flood management and to control all the flood fighting operation on flood embankments.

Under the normal condition, Sub Divisional Officer, Shahdara Sub Division alongwith Sub Engineers will supervise the flood bunds and channels.

As & when the discharge in River Ravi at Jassar Reach 1.0 Lac cusec and in rising, mode the supervisory staff will shift their camps at following locations:-

| S.# | Officer / Official | Camp Site | Duties |
| --- | --- | --- | --- |
| 1 | Sub Divisional Officer, Muridke Sub Division | Babakwal Rest House RD. 39+000 | To watch & check flood fighting arrangements along Shahdara Disty Flood Bund and its spur from RD. 0+000 to 40+000 and to receive flood gauges along bund and spur. |
| 2 | Sub Divisional Officer, Shahdara Sub Division | Haji Kot Hut RD. 61+200 | To watch & check flood fighting arrangements along Shahdara Disty Flood Bund and its spur from RD. 40+000 to 72+000 and to receive flood gauges along bund and spur. |

Executive Engineer,

Shahdara Canal Division,

Shahdara

CHAPTER-10

EMERGENCY TELEPHONE NUMBERS

CHAPTER-10

EMERGENCY TELEPHONE NUMBERS

| Designation of Officers | Office | Fax | Mobile | Residence |
| --- | --- | --- | --- | --- |
| Secretary Irrigation Department | 042-991212117-18 | 042-99212116 |  |  |
| Chief Engineer Drainage & Flood Zone | 042-99233551 |  | 0321-8409386 | 0321-8409386 |
| Chief Engineer, Irrigation Lahore Zone | 042-99212085-86 | 042-99212084 | 0300-4017310 | 0300-4017310 |
| S.E Upper Chenab Canal Circle | 042-99250333 | 042-99250332 | 0333-6289951 | 0333-6289951 |
| Director Flood | 042-99233552 | - | 0300-4399884 | 0300-4399884 |
| Flood Warning Center Lahore | 042-99205372 | 042-99205371 | - | - |
| Police Wireless Center Lahore | 042-99205373 | - | - | - |
| Canal Telegraph Office Secretariat Lahore | 042-99212166 | - | - | - |
| Head Quarter Engineer 4-Corps 108 Battalian Lahore Cantt | 042-366992360 042-36373315 | - | - | - |
| 16 Engineer 4-Corps Lahore | 042-669995186 | - | - | - |
| 23 Engineer Battalian 4-Corps Lahore | 042-66995184 | - | - | - |
| DC Sheikhupura | 056-9200150-51 | 056-9200152 | 0304-0920061 | 056-9200153-54 |
| DC Gujranwala | 055-9200051-52 | 055-9200043 | 0304-0920064 | 0304-0920064 |
| XEN Irrigation Shahdara | 042-99333439 | 042-99333439 | 0344-0754050 | 0344-0754050 |
| XEN Marala | 052-3502102 | 052-3502120 | 0346-4132454 | 0346-4132454 |
| XEN Pasrur Link Sialkot | 052-9250088 | 052-9250089 | 0321-4116234 | 0321-4116234 |
| T.M.A Ferozewala | 042-37944124 | - | 0308-8081965 | 0308-8081965 |
| SDO Shahdara | - | - | 0321-6662221 | 0321-6662221 |
| SDO Muridke | - | - | 0333-7375014 | 0333-7375014 |

CHAPTER-11

STANDARD OPERATING PROCEDURE (SOP) FOR BREACHING SECTIONS

CHAPTER-11

Standard Operation Procedure (SOP) for Breaching Sections

11.1	HISTORY OF BREACHING SECTION

The Critical gauge level is 699.00 which is fixed at RD 65+000 of Shahdara Disty Flood Bund.

The breaching section is operated by the committee authorized by the Government when the water level reaches the critical gauge R.L 699.00 with reference to mean sea level and is in rising position at the Flood Bund.

LOCATION

There are five number approved breaching sections.

1.  At RD. 64-65

- At  RD. 63-64

- At  RD. 59-60

- At  RD. 58-59

- At  RD. 55-56

There are 5 No Sections having a length of 1000 Ft at 4000 Ft interval is to be ballasted at each Breaching Section.

These Breaching sections were operated during the years 1950, 1955, 1973, 1975, 1978 and 1988.

11.2	LOCATION, DESIGN, QUANTITY AND VARIETY OF THE EXPLOSIVE REQUIRED FOR DETONATIONS

The site of breaching section is located at RD. 55+000 to 65+000 Shahdara Disty Flood Protection Bund in 5 segments having length 800 ft and quantity as under :-

| S.# | Description | Location RD. | PVC Linner 5 inches Dia 6 ft long | PVC Linner 5 inches Dia 4 ft long | Linner Cover | Total Liner |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Breaching Section-I | 64 – 65 | 60 | 40 | 100 | 100 |
| 2 | Breaching Section-II | 63 – 64 | 60 | 40 | 100 | 100 |
| 3 | Breaching Section-III | 59 – 60 | 60 | 40 | 100 | 100 |
| 4 | Breaching Section-IV | 58 – 59 | 50 | 20 | 50 | 50 |
| 5 | Breaching Section-V | 55 - 56 | 50 | 20 | 50 | 50 |
| Total |  | 280 | 160 | 400 | 400 |

  - ARRANGEMENT OF EXPLOSIVES AND SECURITY OF EXPLOSIVE STORE

Considering law & order situation, the whole material as mentioned above is lying in the supervision of Army personals at Lahore Cantt: as they being the experts, know much better than Irrigation establishment about the condition of explosive material and its safety.

In case of emergency of breaching, the following materials are required:-

| Name of Explosive | Qty required | Qty available | Deficient Qty | When deficient Qty will be procured |
| --- | --- | --- | --- | --- |
| Detonators No. 8 Plain | 10 | 10 | - | Nothing is deficient for operation of breaching section. |
| Safety Fuses | 225 Meters | 225 Meters | - |  |
| Liquid Explosive | 14 Drums | 14 Drums | - |  |
| P.E Pipe 5 Ft Long | 78 | 78 | - |  |
| P.E Pipe 7 Ft Long | 117 | 117 | - |  |
| Wabox (25 Kg) | 70 | 70 | - |  |
| Wabo Cards in Meter | 3200 Meter | 3200 Meter | - |  |
| Det Instant | 40 | 40 | - |  |
| Det Delay | 1 | 1 | - |  |
| Det Instant Electric | 37 | 37 | - |  |
| PE-3A | 653.9 Kg | 653.9 Kg | - |  |
| Wabox | 1750 Kg | 1750 Kg | - |  |

  - LIST OF THE SECURITY STAFF WITH DETAIL OF THEIR

TRAINING

As the explosive material, has since been shifted from Babakwal explosive Store to Lahore Cantonment in the Army custody. 2 No. sappers / retired Army persons have been appointed for security of explosive of Shahdara Breaching Section lying in the custody of Army Authority.

11.5	DETAIL OF MECHANICAL MEANS AS A STANDBY ARRANGEMENTS IN CASE OF DETONATION FAILURE

One number dozer from Agriculture Department Sheikhupura will be engaged at the breaching section as a stand by arrangements in case of detonation failure.

11.6	DUTY ROSTER IN CASE OF CRITICAL SITUATION

Independent Sub Divisional Officer (S.D.O Shahdara Sub Division) and Sub Engineer (Shahdara Section) have been deputed at the breaching section.

11.7	BREACHING COMMITTEE WITH THEIR ACTION PLAN

Operating Committee

A committee was constituted vide Notification                            No. SO(Floods) VI-33/97 dated 15.07.2015 and the following are the members of committee for operating the breaching section:-

- District Coordination Officer, of the district in which the breaching section is located who shall also be the convener of the committee (District Coordination Officer, Sheikhupura).

- District Coordination Officer of the district likely to be effected by the operation of breaching section or his representative

- Representative of the department owning the structure at which the breaching section is located (not less than the rank of an Executive Engineer or equivalent)

- Representative of C&W Department not below the rank of an Executive Engineer.

- Executive Engineer, Shahdara Canal Division Shahdara. (Member)

- Representative of Pakistan Army not below the rank of Lt. Colonel.

Operating Criteria

4 Engineer Corps Lahore will be responsible for the blasting operation on receiving signal from Executive Engineer, Shahdara Canal Division Shahdara, and District Co-ordination Officer, Sheikhupura, both will be present at the site. The Army Authorities are required to monitor the flood gauges at their own. As and when the discharge in River Ravi at Jassar reaches 1 Lac cusec, and if it is rising they will rush to the site and shift the explosive material from Lahore Cantt: to the breaching / blasting point, and will make all other necessary arrangements well before the critical situation arises, without any further intimation from concerned Department.

The critical reduce levels for the operation of the Breaching Section is fixed as 699 ft at RD 65+000, junction point of the Shahdara Disty Flood Bund and Shahdara Flood Protection Bund, 698 ft at the gauge site on Mehmood Booti Bund and protection bund. The Breaching Section should be operated when either of the 2 levels is attained earlier and the River Ravi is in risen trend

11.8	LIST OF THE VILLAGES LIKELY TO BE INUNDATED IN CASE OF BREACH

| S.# | Name of Village | Teh | Distt | S.# | Name of Village | Teh | Distt | S.# | Name of Village | Teh | Distt |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Fateh Rehan | FZW | SKP | 17 | Babakwal | FZW | SKP | 33 | Khaki | FZW | SKP |
| 2 | Garang Wala | FZW | SKP | 18 | Nathukot | FZW | SKP | 34 | Sharaqpur Khurd | FZW | SKP |
| 3 | Muhammad Pura | FZW | SKP | 19 | Haji Kot | FZW | SKP | 35 | Kot Abdul Malik | FZW | SKP |
| 4 | Goil | FZW | SKP | 20 | Bhart | FZW | SKP | 36 | Abul Khair | FZW | SKP |
| 5 | Meekhowali | FZW | SKP | 21 | Karol | FZW | SKP | 37 | Sattar Wala | FZW | SKP |
| 6 | Kot Hadayat All | FZW | SKP | 22 | Qazi Mirali | FZW | SKP | 38 | Nooraywala | FZW | SKP |
| 7 | Kot Mole Chand | FZW | SKP | 23 | Rangian Jhangian | FZW | SKP | 39 | Rana Bhatti | FZW | SKP |
| 8 | Dandian | FZW | SKP | 24 | Taj Colony | FZW | SKP | 40 | Meerpur | FZW | SKP |
| 9 | Bulkhe | FZW | SKP | 25 | Ferozewala | FZW | SKP | 41 | Satto Jhangian | FZW | SKP |
| 10 | Ferozewala | FZW | SKP | 26 | Kutchehry & Premises | FZW | SKP | 42 | Chah Hakim Singh Wala | FZW | SKP |
| 11 | Thatha Khuda Yaar | FZW | SKP | 27 | Imamia Colony | FZW | SKP | 43 | Chah Sharam Singh Wala | FZW | SKP |
| 12 | Faizpur | FZW | SKP | 28 | Rechna Town | FZW | SKP | 44 | Malik Pur | FZW | SKP |
| 13 | Nain Sukh | FZW | SKP | 29 | Rana Town | FZW | SKP | 45 | Taradday Wali | FZW | SKP |
| 14 | Kot Begum | FZW | SKP | 30 | Vandala Diyal Shah | FZW | SKP | 46 | Lurkey | FZW | SKP |
| 15 | Dhaddian | FZW | SKP | 31 | Dhaka Nizam Pura | FZW | SKP |  |  |  |  |
| 16 | Latheypur |  |  | 32 | Badd |  |  |  |  |  |  |

11.9	ANNOUNCEMENT AND DETAIL OF EVACUATION ARRANGEMENTS

The District Administration, Sheikhupura will be responsible for flood warning / vacation of public and adopting all other relief measures well in time so as to minimize the flood destruction. Area likely to be inundated by the flood water in case of operation of breaching sections is appended herewith for taking timely action.

11.10	DETAIL OF COORDINATION WITH CIVIL/ARMY AUTHORITIES

In case of high flood, hourly flood gauges will be supplied to civil as well as Army. These three departments remain in touch through telephone and wireless system.

11.11		PARALLEL COMMUNICATION ARRANGEMENTS

Telephone and wireless system shall be the parallel arrangements for communication.

Executive Engineer, 				Superintending Engineer,

Shahdara Canal Division,			Upper Chenab Canal Circle,

Shahdara. 						Lahore.

Chief Engineer,

Irrigation Lahore Zone,

Lahore.

PART - B

CHAPTER-12

VULNERABLE SITES ON FLOOD BUND/STRUCTURES:

CHAPTER-12

Vulnerable Sites on Flood Bund / Structure

12.1	APPREHENDED BREACHES IN FLOOD BUNDS / STRUCTURES

Nill

12.2	OPERATION OF BREACHING SECTIONS

4 Engineer Corps Lahore will be responsible for the blasting operation on receiving signal from Executive Engineer, Shahdara Canal Division Shahdara, and District Co-ordination Officer, Sheikhupura, both will be present at the site. The Army Authorities are required to monitor the flood gauges at their own. As and when the discharge in River Ravi at Jassar reaches 1 Lac cusec, and if it is rising they will rush to the site and shift the explosive material from Lahore Cantt. To the breaching / blasting point, and will make all other necessary arrangements well before the critical situation arises, without any further intimation from concerned Department.

12.3	BREACHES DUE TO RISE OF FLOOD WATER, DETERIORATION OF FLOOD BUNDS

The critical reduce levels for the operation of the Breaching Section is fixed as 699 ft at RD 65+000, junction point of the Shahdara Disty Flood Bund and Shahdara Flood Protection Bund, 698 ft at the gauge site on Mehmood Booti Bund and protection bund. The Breaching Section should be operated when either of the 2 levels is attained earlier and the River Ravi is in risen trend

CHAPTER-13

EMERGENCY CONTINGENCY PLAN FOR VULNERABLE SITES LISTED ABOVE. EMERGENCY CONTINGENCY PLAN MUST INCLUDE:-

CHAPTER-13

Emergency Contingency Plan for vulnerable site (sites)

EMERGENCY CONTINGENCY PLANS FOR SITE NO. 1 (RD. 47-48)

13.1PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS (RD. 47 – 48).

- Plan showing route is attached on page No. 29.

13.2 DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED

AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.

| S.# | Name of Villages | Teh | Distt | S.# | Name of Village | Teh | Distt |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Dandian | FZW | SKP | 10. | Imamia Colony | FZW | SKP |
| 2. | Kot Hadayat | FZW | SKP | 11. | Faisal Town | FZW | SKP |
| 3. | Karol | FZW | SKP | 12. | Wandala Dial Singh | FZW | SKP |
| 4. | Bhart | FZW | SKP | 13. | Taj Colony | FZW | SKP |
| 5. | Haji Kot | FZW | SKP | 14. | Nizam Pura | FZW | SKP |
| 6. | Barkat Town | FZW | SKP | 15. | Khaki | FZW | SKP |
| 7. | Ferozewala | FZW | SKP | 16. | Sharaqpur Khurd | FZW | SKP |
| 8. | Abu Alkhair | FZW | SKP | 17. | Kot Abdul Malik | FZW | SKP |
| 9. | Thatha Khudayar | FZW | SKP |  |  |  |  |

13.3	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL. THIS MAY INCLUDE

Executive Engineer, Shahdara Canal Division Shahdara will be overall in charge of the entire flood fighting works. He will send requisitions for help to Dist Management, Military and other Departments. Sub Divisional Officer, Shahdara Sub Division along with Sub Engineers will shift his camp at effective site  and will be the in charge of restoration of bund.

    - ARRANGEMENTS

Sub Divisional officer, Shahdara Sub Division will arrange the machinery required for restoration of any effective reach from the private source and as well as authorities

13.3.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

First camp will be established at Babakwal Rest House at RD. 39+000 of Shahdara Disty Flood Protection Bund and Sub Divisional Officer, Muridke Sub Division UCC alongwith his sub divisional staff will look after the reach of flood bund from RD. 0+000 – 40+000.

ii).	2nd camp will be established at Haji Kot hut at RD. 61+200 of Shahdara Disty Flood Protection Bund and Sub Divisional Officer, Shahdara Sub Division UCC alongwith his sub divisional staff will look after the reach of flood bund from RD.  40+000 – 72+000.

13.3.3	DUTIES OF OFFICERS/OFFICIALS AND THEIR CAMP SITES

| Sr. No | Camp Location | Duties of Officers (Name, Designation & Mobile No) | Duties of Officers (Name, Designation & Mobile No) |
| --- | --- | --- | --- |
| 1 | Babakwal Rest House Rd 39+000 | Ahsan Jamil SDO Muridke 03337375014 | 1. Rana Waheed Ahmad Sub Engineer Adian Section 03056042197 2. Jamshaid Ahmad Sub Engineer Mehta Suja Section 03074535210 |
| 2 | Haji Kot Hut Rd 61+200 | Iftikhar Majeed Mirza SDO Shahdara 03216662221 | 1. Sajid Mehboob Wattoo Sub Engineer Shahdara Section 03065299422 2. Ameer Ali Sub Engineer Rayya Section 03026752649 |

13.3.4	DEPARTMENTAL MACHINERY AVAILABLE

Tractor with Trolley, blade and water tanker

13.3.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE

Excavator	 	=	1 No. (For Each Site)

Tractor Torlley	=	5 No   (For Each Site)

13.3.6		FLOOD FIGHTING MATERIAL AVAILABLE AT SITE NO-I.

| SR # | Flood Fighting Materail | Available | Unit |
| --- | --- | --- | --- |
| 1. | Killas 6.0’ long | 250 | Nos. |
| 2. | Ballies 10’—12’ long | 250 | Nos. |
| 3 | Lanterns | 24 | Nos. |
| 4 | Bulbs | - | Nos. |
| 5 | PVC cable off sizes | - | Yards |
| 6 | Buckets | 12 | Nos. |
| 7 | Baskets | 25 | Nos. |
| 8 | Manila rope off sorts | 01 | Munds |
| 9 | Kassies with handle | 125 | Nos. |
| 10 | Shouldaries | - | Nos. |
| 11 | Empty Gunny Bags | 1000 | Nos. |
| 12 | Empty Nylon Bags | 1000 | Nos. |
| 13 | Torches (3 Cells) | 03 | Nos. |
| 14 | Dry battery cell for Torches | 03 | Dozen |
| 15 | Torch Tube Light | 03 | Nos. |
| 16 | Pick Axes with Handle | 25 | Nos. |
| 17 | Gas Lamp (Petromax) | 06 | Nos. |
| 18 | K. Oil | 15 | Ltrs |
| 19 | Generator 220 Vol 1.5 K. Watts. | 01 | No |
| 20 | Swiss Cottage Tents. | 02 | Nos. |
| 21 | Life Savings Belts | 06 | Nos. |
| 22 | Charpays | 03 | Nos. |
| 23 | Degcha Large | 01 | Nos. |
| 24 | Pedestal Fan 24” | 01 | Nos. |
| 25 | Cherry Chairs | 06 | Nos. |
| 26 | Teapay | - | Nos. |
| 27 | Water Set | 01 | Nos. |
| 28 | Tea Set | 01 | Nos. |
| 29 | Water Cooler | - | Nos. |
| 30 | Hot Case | - | Nos. |
| 31 | Tea Spoons |  | Dozen |
| 32 | Petrol | 20 | Gallons |
| 33 | Mental | - | Dozen |
| 34 | Vick | - | Yards |
| 35 | Chimneys Glass | - | Dozen |
| 36 | Electric Connection for Flood period | - | Job |
| 37 | Reserve Stock of Stone on Shahdara Disty Flood Bund (a) RD 35 - 42 & 15 - 19 (b) RD 0 – 4884 J-Head Spur | A - 200121 Cft B – 77653 Cft |  |

13.3.7		FLOOD FIGHTING MATERIAL REQUIRED AT SITE NO-I.

| SR # | Flood Fighting Materail | Required | Unit |
| --- | --- | --- | --- |
| 1. | Killas 6.0’ long | 500 | Nos. |
| 2. | Ballies 10’—12’ long | 100 | Nos. |
| 3 | Lanterns | 100 | Nos. |
| 4 | Bulbs | 200 | Nos. |
| 5 | PVC cable off sizes | 500 | Yards |
| 6 | Buckets | 50 | Nos. |
| 7 | Baskets | 500 | Nos. |
| 8 | Manila rope off sorts | 02 | Munds |
| 9 | Kassies with handle | 100 | Nos. |
| 10 | Shouldaries | 04 | Nos. |
| 11 | Empty Gunny Bags | 1000 | Nos. |
| 12 | Empty Nylon Bags | 1000 | Nos. |
| 13 | Torches (3 Cells) | 12 | Nos. |
| 14 | Dry battery cell for Torches | 04 | Dozen |
| 15 | Torch Tube Light | 06 | Nos. |
| 16 | Pick Axes with Handle | 12 | Nos. |
| 17 | Gas Lamp (Petromax) | 04 | Nos. |
| 18 | K. Oil | 24 | Ltrs |
| 19 | Generator 220 Vol 1.5 K. Watts. | 01 | No |
| 20 | Swiss Cottage Tents. | 02 | Nos. |
| 21 | Life Savings Belts | 12 | Nos. |
| 22 | Charpays | 06 | Nos. |
| 23 | Degcha Large | 02 | Nos. |
| 24 | Pedestal Fan 24” | 01 | Nos. |
| 25 | Cherry Chairs | 12 | Nos. |
| 26 | Teapay | 02 | Nos. |
| 27 | Water Set | 02 | Nos. |
| 28 | Tea Set | 02 | Nos. |
| 29 | Water Cooler | 02 | Nos. |
| 30 | Hot Case | 02 | Nos. |
| 31 | Tea Spoons | 01 | Dozen |
| 32 | Petrol | 40 | Gallons |
| 33 | Mental | 02 | Dozen |
| 34 | Vick | 20 | Yards |
| 35 | Chimneys Glass | 04 | Dozen |
| 36 | Electric Connection for Flood period | 01 | Job |

13.4	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDINGS, CANALS AND DRAINAGE NETWORK.

On breaching of River Training / Flood Protection Works of Shahdara Canal Division Shahdara, the following Irrigation and roads networks shall be affected.

- Main Irrigation Net work.

- Shahdara Disty System

- Main Road Network

- Lahore – Gujranwala Road (G.T Road)

- Main Sheikhupura Road

- Motorway M-2 & M-3

- Eastern Bypass Lahore Sialkot Motorway

- Railway Structures

- Lahore – Sheikhupura Line

- Lahore – Rawalpindi Line

- Lahore – Narowal Line

- Canal & Drainage Network

- Leila Nullah

- Bhed Nullah

- Building and Allied Abadies

- Villages Abadies of Shahdara town and other allied abadies can be affected due to flood water.

- Back Up Division:

- In case of emergency, Gujranwala Division UCC will back up Shahdara Canal Division Shahdara.

Executive Engineer, 				Superintending Engineer,

Shahdara Canal Division, 			Upper Chenab Canal Circle,

Shahdara.  						Lahore.

Chief Engineer,

Irrigation Lahore Zone,

Lahore.

Emergency Contingency Plan for vulnerable site

EMERGENCY CONTINGENCY PLANS FOR SITE NO. 2 (RD. 55-56)

13.5 PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS (RD. 55 – 56).

- Plan showing route is attached on next page.

13.6 DETAIL OF VILLAGES ABADIES LIKELY TO BE AFFECTED AND THIS SHOULD ALSO BE SHOWN ON THE PLAN.

RD. 55 – 56

| S.# | Name of Villages | Teh | Distt | S.# | Name of Village | Teh | Distt |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Haji Kot | FZW | SKP | 8. | Wandala Dial Singh | FZW | SKP |
| 2. | Barkat Town | FZW | SKP | 9. | Taj Colony | FZW | SKP |
| 3. | Ferozewala | FZW | SKP | 10. | Nizam Pura | FZW | SKP |
| 4. | Abu Alkhair | FZW | SKP | 11. | Khaki | FZW | SKP |
| 5. | Thatha Khudayar | FZW | SKP | 12. | Sharaqpur Khurd | FZW | SKP |
| 6. | Imamia Colony | FZW | SKP | 13. | Kot Abdul Malik | FZW | SKP |
| 7. | Faisal Town | FZW | SKP |  |  |  |  |

13.7	STRATEGY AND ACTION TAKEN BE EXPLAINED IN DETAIL. THIS MAY INCLUDE

Executive Engineer, SHAHDARA CANAL DIVISION, UCC will be overall in charge of the entire flood fighting works. He will send requisitions for help to Dist Management, Military and other Departments. Sub Divisional Officer, Shahdara Sub Division along with Sub Engineers will shift his camp at effective site  and will be the in charge of restoration of bund.

    - ARRANGEMENTS

Sub Divisional Shahdara Sub Division will arrange the machinery required for restoration of any effective reach from the private source and as well as authorities

13.7.2	ESTABLISHMENT OF FLOOD FIGHTING CAMPS

First camp will be established at Babakwal Rest House at RD. 39+000 of Shahdara Disty Flood Protection Bund and Sub Divisional Officer, Muridke Sub Division UCC alongwith his sub divisional staff will look after the reach of flood bund from RD. 0+000 – 40+000.

ii).	2nd camp will be established at Haji Kot hut at RD. 61+200 of Shahdara Disty Flood Protection Bund and Sub Divisional Officer, Shahdara Sub Division UCC alongwith his sub divisional staff will look after the reach of flood bund from RD.  40+000 – 72+000.

13.7.3	DUTIES OF OFFICERS/OFFICIALS AND THEIR CAMP SITES

| Sr. No | Camp Location | Duties of Officers (Name, Designation & Mobile No) | Duties of Officers (Name, Designation & Mobile No) |
| --- | --- | --- | --- |
| 1 | Babakwal Rest House Rd 39+000 | Ahsan Jamil SDO Muridke 03337375014 | 1. Rana Waheed Ahmad Sub Engineer Adian Section 03056042197 2. Jamshaid Ahmad Sub Engineer Mehta Suja Section 03074535210 |
| 2 | Haji Kot Hut Rd 61+200 | Iftikhar Majeed Mirza SDO Shahdara 03216662221 | 1. Sajid Mehboob Wattoo Sub Engineer Shahdara Section 03065299422 2. Ameer Ali Sub Engineer Rayya Section 03026752649 |

13.7.4	DEPARTMENTAL MACHINERY AVAILABLE

Tractor with Trolley, blade and water tanker

13.7.5		MACHINERY AVAILABLE FROM PRIVATE SOURCE

Excavator	 	=	1 No. (For Each Site)

Tractor Torlley	=	5 No   (For Each Site)

13.7.6	 FLOOD FIGHTING MATERIAL AVAILABLE AT SITE NO-II

| SR # | Flood Fighting Material | Available | Unit |
| --- | --- | --- | --- |
| 1. | Killas 6.0’ long | 250 | Nos. |
| 2. | Ballies 10’—12’ long | 250 | Nos. |
| 3 | Lanterns | 24 | Nos. |
| 4 | Bulbs | - | Nos. |
| 5 | PVC cable off sizes | - | Yards |
| 6 | Buckets | 12 | Nos. |
| 7 | Baskets | 25 | Nos. |
| 8 | Manila rope off sorts | - | Munds |
| 9 | Kassies with handle | 125 | Nos. |
| 10 | Shouldaries | 02 | Nos. |
| 11 | Empty Gunny Bags | 1000 | Nos. |
| 12 | Empty Nylon Bags | 1000 | Nos. |
| 13 | Torches (3 Cells) | 03 | Nos. |
| 14 | Dry battery cell for Torches | 03 | Dozen |
| 15 | Torch Tube Light | 03 | Nos. |
| 16 | Pick Axes with Handle | 25 | Nos. |
| 17 | Gas Lamp (Petromax) | 06 | Nos. |
| 18 | K. Oil | 15 | liters |
| 19 | Generator 220 Vol 1.5 K. Watts. | 01 | No |
| 20 | Swiss Cottage Tents. | 02 | Nos. |
| 21 | Life Savings Belts | 06 | Nos. |
| 22 | Charpays | 03 | Nos. |
| 23 | Degcha Large | 01 | Nos. |
| 24 | Pedestal Fan 24” | 01 | Nos. |
| 25 | Cherry Chairs | 06 | Nos. |
| 26 | Teapay | - | Nos. |
| 27 | Water Set | 01 | Nos. |
| 28 | Tea Set | 01 | Nos. |
| 29 | Water Cooler | - | Nos. |
| 30 | Hot Case | - | Nos. |
| 31 | Tea Spoons | - | Dozen |
| 32 | Petrol | 20 | Gallons |
| 33 | Mental | - | Dozen |
| 34 | Vick | - | Yards |
| 35 | Chimneys Glass | - | Dozen |
| 36 | Electric Connection for Flood period | - | Job |

13.7.7	 FLOOD FIGHTING MATERIAL REQUIRED SITE NO-II

| SR # | Flood Fighting Material | Required | Unit |
| --- | --- | --- | --- |
| 1. | Killas 6.0’ long | 250 | Nos. |
| 2. | Ballies 10’—12’ long | 50 | Nos. |
| 3 | Lanterns | 50 | Nos. |
| 4 | Bulbs | 100 | Nos. |
| 5 | PVC cable off sizes | 250 | Yards |
| 6 | Buckets | 25 | Nos. |
| 7 | Baskets | 250 | Nos. |
| 8 | Manila rope off sorts | 01 | Munds |
| 9 | Kassies with handle | 50 | Nos. |
| 10 | Shouldaries | 02 | Nos. |
| 11 | Empty Gunny Bags | 500 | Nos. |
| 12 | Empty Nylon Bags | 500 | Nos. |
| 13 | Torches (3 Cells) | 06 | Nos. |
| 14 | Dry battery cell for Torches | 02 | Dozen |
| 15 | Torch Tube Light | 03 | Nos. |
| 16 | Pick Axes with Handle | 06 | Nos. |
| 17 | Gas Lamp (Petromax) | 02 | Nos. |
| 18 | K. Oil | 12 | liters |
| 19 | Generator 220 Vol 1.5 K. Watts. | 01 | No |
| 20 | Swiss Cottage Tents. | 01 | Nos. |
| 21 | Life Savings Belts | 06 | Nos. |
| 22 | Charpays | 03 | Nos. |
| 23 | Degcha Large | 01 | Nos. |
| 24 | Pedestal Fan 24” | 01 | Nos. |
| 25 | Cherry Chairs | 06 | Nos. |
| 26 | Teapay | 01 | Nos. |
| 27 | Water Set | 01 | Nos. |
| 28 | Tea Set | 01 | Nos. |
| 29 | Water Cooler | 01 | Nos. |
| 30 | Hot Case | 01 | Nos. |
| 31 | Tea Spoons | 01 | Dozen |
| 32 | Petrol | 20 | Gallons |
| 33 | Mental | 01 | Dozen |
| 34 | Vick | 10 | Yards |
| 35 | Chimneys Glass | 02 | Dozen |

13.8	DETAIL OF OTHER INFRASTRUCTURE LIKE ELECTRIC, SUI GAS, TELEPHONE INSTALLATIONS, ROAD NETWORK, OTHER BUILDINGS, CANALS AND DRAINAGE NETWORK.

On breaching of River Training / Flood Protection Works of Shahdara Canal Division, Shahdara the following Irrigation and roads networks shall be affected.

- Main Irrigation Net work.

- Shahdara Disty System

- Main Road Network

- Lahore – Gujranwala Road (G.T Road)

- Main Sheikhupura Road

- Motorway M-2 & M-3

- Eastern Bypass Lahore Sialkot Motorway

- Railway Structures

- Lahore – Sheikhupura Line

- Lahore – Rawalpindi Line

- Lahore – Narowal Line

- Canal & Drainage Network

- Leila Nullah

- Bhed Nullah

- Building and Allied Abadies

- Villages Abadies of Shahdara town and other allied abadies can be affected due to flood water.

- Back Up Division:

- In case of emergency, Marala Division UCC will back up Shahdara Canal Division, Shahdara.

Executive Engineer, 				Superintending Engineer,

Shahdara Canal Division, 			Upper Chenab Canal Circle,

Shahdara.  						Lahore.

Chief Engineer,

Irrigation Lahore Zone,

Lahore.

CHAPTER-14

ACTION PLAN

14.1	RE-SHUFLING / RECOUPING PLAN OF RESERVE STOCK STONE DEPARTMENTALLY.

Re-shuffling 		=	NIL

Reserve stock stone has been approved by Chief Engineer, Irrigation Lahore Zone Lahore vide his office letter No. ___________________________________ dated _________ however recouping plan / procurement of reserve stock of stone is as under :-

| S.# | Name of Structure | Qty in hand (Lac Cft) | Qty to be procured (Lac Cft) |
| --- | --- | --- | --- |
| 1 | Shahdara Disty Flood Bund | 2.00 Cft | 0.50 Cft |
| 2 | J-Head Spur | 0.78 Cft | 0.22 Cft |
| Total | 2.78 Cft | 0.72 Cft |

14.2	DETAIL OF INLET / OUTLET CROSSES ALONG WITH CLOSING METHODOLOGY.

No inlet in flood reach from RD. 0+000 – 72+000 of Shahdara Disty Flood Bund

Following are the outlet which is operate-able when required.

| S.# | Location | Size | Type |
| --- | --- | --- | --- |
| 1 | RD. 1135/L Shahdara Disty |  | APM |
| 2 | RD. 3859/L Shahdara Disty |  | APM |
| 3 | RD. 11440/L Shahdara Disty | 5” dia | Steel Pipe |
| 4 | RD. 17575/L Shahdara Disty | 7” dia | Steel Pipe |
| 5 | RD. 21210/L Shahdara Disty | 3” dia | Steel Pipe |
| 6 | RD. 27900/L Shahdara Disty |  | OF |
| 7 | RD. 30870/L Shahdara Disty | 6” dia | Steel Pipe |
| 8 | RD. 31650/L Shahdara Disty | 9.5” dia | Steel Pipe |
| 9 | RD. 32810/L Shahdara Disty | 6” dia | Steel Pipe |
| 10 | RD. 37616/L Shahdara Disty | 6” dia | Steel Pipe |
| 11 | RD. 39200/L Shahdara Disty | 8” dia | Steel Pipe |
| 12 | RD. 43000/L Shahdara Disty | 9” dia | Steel Pipe |
| 13 | RD. 48000/L Shahdara Disty | 5” dia | Steel Pipe |
| 14 | RD. 53200/L Shahdara Disty | 6” dia | Steel Pipe |
| 15 | RD. 60000/L Shahdara Disty | 8” dia | Steel Pipe |
| 16 | RD. 63025/L Shahdara Disty | 9” dia | Steel Pipe |
| 17 | RD. 67760/L Shahdara Disty | 7” dia | Steel Pipe |
| 18 | RD. 67800/L Shahdara Disty |  | OSM |

14.3	DEPLOYMENT OF MACHINERY (MEDIUM TO HIGH FLOOD)

| S.# | Name of structure / bund | Length in mile | Vulnerable reach (RD.) | Camp Location | Site incharge by name cell No. | Machinery Deployment | Availability of stone (Lac cft) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Dumper | Tractor | Labour Beldar |  |
| 1 | Shahdara Disty Flood Bund RD. 0+000 – 72+000 | 14.4 | - | 61200 | Iftikhar Majeed Mirza SDO Shahdara 03216662221 | 1 | - | - | 5 | 50 | 2.00 |
| 2 | J-Head Spur RD. 39000/L | 1 | - | 39000 | Ahsan Jamil SDO Muridke 03337375014 |  |  |  |  | 06 | 0.78 |
| Total | 1 |  |  | 5 | 43 | 2.78 |

14.4	DEPLOYMENT OF MACHINERY (HIGH TO VERY HIGH FLOOD)

| S.# | Name of structure / bund | Length in mile | Vulnerable reach (RD.) | Camp Location | Site incharge by name cell No. | Machinery Deployment | Availability of stone (Lac cft) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Dumper | Tractor | Labour Beldar |  |
| 1 | Shahdara Disty Flood Bund RD. 0+000 – 72+000 | 14.4 | - | 61200 | Iftikhar Majeed Mirza SDO Shahdara 03216662221 | 1 | - | 1 | 5 | 14.4 | 1.45 |
| 2 | J-Head Spur RD. 39000/L | 1 | - | 39000 | Ahsan Jamil SDO Muridke 03337375014 |  |  | 2 | 1 | 1 | 0.15 |
| Total | 1 |  |  | 6 | 56 | 1.60 |

14.5	DEPLOYMENT OF MACHINERY (HIGH TO EXCEPTIONALLY HIGH FLOOD)

| S.# | Name of structure / bund | Length in mile | Vulnerable reach (RD.) | Camp Location | Site incharge by name cell No. | Machinery Deployment | Availability of stone (Lac cft) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Excavator | Dozer | Dumper | Tractor | Labour Beldar |  |
| 1 | Shahdara Disty Flood Bund RD. 0+000 – 72+000 | 14.4 | - | 61200 | Iftikhar Majeed Mirza SDO Shahdara Cell No. 03216662221 | 1 | - | - | 5 | 125 | 1.45 |
| 2 | J-Head Spur RD. 39000/L | 1 | - | 39000 | Ahsan Jamil SDO Muridke Cell No. 03337375014 |  |  |  |  | 15 | 0.15 |
| Total:- | 1 | - | - | 5 | 127 | 1.60 |

14.6 POLICE DEPLOYMENT PLAN

| S.# | Site of Breaching Section | Concerned Canal Division | Concerned Police Station | Police Person Deployed | Remarks |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | SHO/SI/ASI | Constable |  |
| 1 | RD 55- 65 , Shahdara Distty Flood Bund | Shahdara Canal Division | Iftikhar Majeed Mirza SDO Shahdara Cell No. 03216662221 | 1 No. | 3 No. | - |

| S.# | Venerable Sites used for illegal cuts during floods | Concerned Canal Division | Concerned Police Station | Police Person Deployed | Remarks |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | SHO/SI/ASI | Constable |  |
| 1 | RD 47- 48 and 55- 56, Shahdara Distty Flood Bund | Shahdara Canal Division | Iftikhar Majeed Mirza SDO Shahdara Cell No. 03216662221 | 1 No. | 3 No. | - |

14.7 DETAIL OF SYNTHETIC BAGS WITH CAPACITY OF 40 KG.

| S.# | Name of Structure | Length in Feet | Vulnerable Reach | Camp Location | Site Incharge by name / Cell No. | Detail of Synthetic Bags with capacity of 40 kg (Required) | Detail of Synthetic Bags with capacity of 40 kg (Availabale) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Shahdara Disty Flood Bund RD. 0+000 – 72+000 | 72000 ft | 47-48 55-56 | RD. 61200 Shahdara Disty Flood Bund | Iftikhar Majeed Mirza SDO Shahdara Cell No. 03216662221 | 1500 Nos | 750 No. |
| 2 | J-Head Spur RD. 39000/L | 5000 ft | - | RD. 39000 Shahdara Disty Flood Bund | Ahsan Jamil SDO Muridke Cell No. 03337375014 | 500 Nos | 250 No. |

14.8 DETAIL OF POLYTHENE SHEETS OF BLACK COLOR TO

PROTECT U/S SLOPES AGAINST WAVE ACTION AND TO

CONTROL SEEPAGE THROUGH EMBANKMENTS.

| S.# | Name of Structure | Length in Mile | Vulnerable Reach | Camp Location | Site Incharge by name / Cell No. | Required Polythene sheet (300 Guage), | Available Polythene sheet (300 Guage) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Shahdara Disty Flood Bund RD. 0+000 – 72+000 | 14.4 | 47-48 55-56 | RD. 61200 Shahdara Disty Flood Bund | Iftikhar Majeed Mirza SDO Shahdara Cell No. 03216662221 | 2500 Kg | - |
| 2 | J-Head Spur RD. 39000/L | 1 | - | RD. 39000 Shahdara Disty Flood Bund | Ahsan Jamil SDO Muridke Cell No. 03337375014 | 1000 Kg | - |

15	BACK UP DIVISION (IN CASE OF BREACH)

5 No. breaching sections exist in this Division.  In case of breaching sister Division Gujranwala Canal Division, Gujranwala and all the relevant Administrative Department will informed that will be helpful to this Division.

Executive Engineer,

Shahdara Canal Division,

Shahdara.

STATEMENT SHOWING POSITION OF WATER WAYS UNDER DUAL CARRIAGE WAY (G.T ROAD)

| S.# | Distance from Shahdara Disty crossing (K.M) | (i) Water way under Shahdara – Gujranwala Road | (ii) water way under Gujranwala – Shahdara Road | Av: existing Disc: Capc: | Remarks |
| --- | --- | --- | --- | --- | --- |
|  |  | Size (Ft) | Open bays | Closed Bays | Total Bays | Discharge Capacity | Size (Ft) | Open bays | Closed Bays | Total Bays | Discharge Capacity |  |  |
|  |  |  | No | Water Way (Ft) | No | Water Way (Ft) | No | Water Way (Ft) | Exs: | Des: |  | No | Water Way (Ft) | No | Water Way (Ft) | No | Water Way (Ft) | Exs: | Des: |  |  |
| 1 | 0 | 10 | 1 | 10 | 0 | 0 | 1 | 10 | 160 | 160 | 10 | 1 | 10 | 0 | 0 | 1 | 10 | 160 | 160 | 160 | Shahdara Disty Crossing |
| 2 | 0.41 | 12 | 5 | 60 | 1 | 12 | 6 | 72 | 960 | 1152 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 960 | Both sides blocked by abadies |
| 3 | 1.16 | 10 | 15 | 150 | 8 | 80 | 23 | 230 | 2400 | 3680 | 20 | 12 | 240 | 0 | 0 | 12 | 240 | 3840 | 3840 | 3120 | Water way blocked on D/S side flow not possible Gap between railway line and road is cleared no bridge under railway line in front of road bridge |
| 4 | 2.21 | 10 | 58 | 580 | 85 | 850 | 143 | 1430 | 9280 | 22880 | 10 | 90 | 900 | 20 | 200 | 110 | 1100 | 14400 | 17600 | 11840 | U/S & D/S 50% blocked it is infornt of 100 bays railway bridge closed bays under both the roads need to be got opened |
| 5 | 3.61 | 6 | 71 | 426 | 0 | 0 | 71 | 426 | 6816 | 6816 | 5.5 | 86 | 473 | 0 | 0 | 86 | 473 | 7568 | 7568 | 7192 | Both sides of road bridge open railway bridge also existing |
| 6 | 3.91 | 40 | 6 | 240 | 0 | 0 | 6 | 240 | 3840 | 3840 | 60 | 4 | 240 | 0 | 0 | 4 | 240 | 3840 | 3840 | 3840 | Bhed Nullah x-ing bondary wall constructed on U.S side 2 No. bays on D/S side blocked by the boundary wall of Azhar Cooking oil Factory which needs to be got removed |
| 7 | 4.56 | 10 | 1 | 10 | 0 | 0 | 1 | 10 | 160 | 160 | 10 | 1 | 10 | 0 | 0 | 1 | 10 | 160 | 160 | 160 | Dargai Minor crossing |
| 8 | 5.81 | 30 | 2 | 60 | 0 | 0 | 2 | 60 | 960 | 960 | 10 | 2 | 20 | 0 | 0 | 2 | 20 | 320 | 320 | 640 | Leila Nullah Crossing |
| 9 | 6.1 | 10.5 | 30 | 315 | 0 | 0 | 30 | 315 | 5040 | 5040 | 5 | 61 | 305 | 0 | 0 | 61 | 305 | 4880 | 4880 | 4960 | Open on both sides road cut is recommend 300’ before eastern end of this bridge |
| Total :- | 189 | 1851 | 94 | 942 | 283 | 2793 | 29616 | 44688 |  | 257 | 2198 | 20 | 200 | 277 | 2398 | 35168 | 38368 | 32872 | Only 73.56% water way available |

FROM SHAHDARA TO KALA SHAH KAKU BYE PASS LINK ROAD.

Note :-		1.	Distance given in the column 2 of the statement are measured from Shahdara Railway Station

2.	Average velocity of flood water for calculation of estimated discharge through bridge is adopted as 4.0 ft /Sec

POSITION OF WATER WAY UNDER SHAHDARA – SHEIKHUPURA RAILWAY LINE

| S.# | Railway line Lahore to Sheikhupura (KM) | Water way under railway line | Estimated Discharge | Remarks |
| --- | --- | --- | --- | --- |
|  |  | No. of bays | Width of bays | Water ways (Ft) |  |  |
| 1 | 3.25 | 1 | 6 | 6 | 96 | Proposed to be plugged |
| 2 | 3.40 | 1 | 6 | 6 | 96 | -do- |
| 3 | 3.80 | 80 | 8.5 | 680 | 21500 | - |
| 4 | 7.40 | 5 | 20 | 100 | 3000 | Bhed Nullah |
| 5 | 8.40 | 5 | 20 | 100 | 2500 | Leila Nullah |
| 6 | 8.70 | 10 | 20 | 200 | 2500 | - |
| 7 | 9.00 | 6 | 12 | 72 | 1152 | - |
| Total :- | 108 | - | 1164 | 30844 |  |

POSITION OF WATER WAY UNDER SHAHDARA – SHEIKHUPURA RAILWAY LINE

| S.# | Distance from Shahdara Disty Crossing (K.M) | Water way under road | Estimated Discharge (Cs) | Remarks |
| --- | --- | --- | --- | --- |
|  |  | No. | Size | Water way (LFt) |  |  |
| 1 | 0 | 1 | 10 | 10 | 160 | Shahdara Disty Crossing |
| 2 | 0.5 | 3.3 | 10 | 30 | - | U/S permanently blocked by industrial construction and D/S open plot residential construction after plot |
| 3 | 1 | 25.24 | 12 | 294 | - | D/S permanently blocked by Shirine U/S blocked by industrial construction |
| 4 | 2.5 | 34.25 | 12 | 354 | 5664 | Water way clear on both sides residential area after 700’ on D/S |
| 5 | 3.4 | 34.34 | 12 | 408 | 6528 | Water way blocked |
| 6 | 3.7 | 3.3 | 8 | 24 | - | Permanently blocked by industrial growth |
| 7 | 3.8 | 1.1 | 8 | 8 | - | Permanently choked and blocked |
| 8 | 4.1 | 3.4 | 42.31 | 126 | 2016 | Bhed Nullah Crossing |
| 9 | 4.4 | 1 | 8 | 8 | - | Choked and plugged No culvert or cause way on SKP – SDR Road |
| 10 | 4.5 | 42.28 | 12 | 420 | 6720 | Scattered abadies U/S side 1 No house and 1 No. factory existing in water way |
| Total :- |  |  | 1682 | 21088 |  |

POSITION OF WATER WAY UNDER MOTORWAY

(From Shahdara – Jaranwala Road Crossing to

Shahdara – Sheikhupura Road Crossing)

| S.# | Distance from Jaranwala Road Crossing (K.M) | Water way under road | Estimated Discharge (Cs) | Remarks |
| --- | --- | --- | --- | --- |
|  |  | No. of bays | Width of bays (ft) | Water way (Ft) |  |  |
| 1 | 0.67 | 1 | 80 | 80 | 1280 | Shahdara Disty |
| 2 | 1.1 | 1 | 8 | 8 | 128 |  |
| 3 | 1.28 | 1 | 8 | 8 | 128 |  |
| 4 | 1.7 | 6 | 80 | 480 | 7680 |  |
| 5 | 2.38 | 6 | 80 | 480 | 7680 |  |
| 6 | 2.93 | 1 | 8 | 8 | 128 |  |
| 7 | 4.15 | 10 | 80 | 800 | 12800 | Bhed Nullah |
| 8 | 5.43 | 2 | 80 | 160 | 2560 | Sheikupura Road |
| 9 | 4.4 | 1 | 8 | 8 | - | Choked and plugged No culvert or cause way on SKP – SDR Road |
| Total :- | 28 |  | 2024 | 32384 |  |

ACTION PLAN FOR DEPLOYMENT OF LABOUR

| S.# | Condition | Labour |
| --- | --- | --- |
| 1. | Medium Flood | 49 Regular & Work charge establishment will be deployed during Medium Flood |
| 4. | High Flood | 56 Regular & Work charge establishment will be deployed during High Flood |
| 5. | Very High Flood | 112 Regular & Work charge establishment will be deployed during Very High Flood |
| 6. | Exceptionally High Flood | 140 Regular & Work charge establishment will be deployed during Exceptionally High Flood |

ACTION PLAN FOR DEPLOYMENT OF MACHINERY

| S.# | Condition | Machinery |
| --- | --- | --- |
| 1. | Medium to High Flood | 01 No. Tractor with blade and water tank |
| 2. | Very Exceptionally High Flood | 01 No. Excavator and 5 No. Tractor Trollies |

END

# Text boxes

1

2

3

4

Executive Engineer,

Shahdara Canal Division

Sub Divisional Officer,

Shahdara Sub Division

Sub Divisional Officer,

Muridke Sub Division

Sub Divisional Officer,

Sadhoki Sub Division

Sub Engineer Lalupur Section

Sub Engineer

Maluki Section

Sub Engineer

Mian wali Section

Maluki Section

Sub Engineer Mehta Suja Section

Sub Engineer Muridke Section

Sub Engineer Ahdian Section

Sub Engineer

Badhomalhi Section

Sub Engineer

Shahdara Section

Sub Engineer        Rayya Section

Sub Engineer         Begumpur Section

Executive Engineer,

SHAHDARA CANAL DIVISION UCC,

Gujranwala.

5

6

3

3

7

8

9

10

11

12

13

8

14

9

15

16

17

18

19

20

21

22

22

15

23

24

25

26

27

28

29

30

31

32

33

34

35

36

37

11.12 	INDEX PLAN

38

39

40

41

42

13.1	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS (RD. 47-48)

43

44

45

46

47

48

49

50

13.5 	PLAN SHOWING ROUTE OF FLOOD WATER COMING OUT OF THE BREACH SUPPORTED WITH LEVELS (RD. 55-56)

51

52

53

54

55

56

57

58

59

60

61

62

63

64

65

66

67

68

69

70